3GPP TSG-RAN5 Meeting #86-e	R5-200897

Electronic Meeting, 17th – 28th February 2020

3GPP TSG RAN Meeting #87-e	RP-20xxxx

Electronic Meeting, 16th – 19th Mar 2020	(revision of xx-yyxxxx)

# Source:	CMCC

# Title:	New WID on UE Conformance Test Aspects – EN-DC PC2 TDD-TDD UE

# Document for:	Approval

Agenda Item:	7.4.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	UE Conformance Test Aspects EN-DC PC2 TDD-TDD UE

## Acronym: ENDC_PC2_TDD_TDD-UEConTest

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network |  |
|  | Services |  |

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  |  |  |  |  |
| No | X | X | X | X |  |
| Don't know |  |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

|  | Feature |
| --- | --- |
| X | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work Items |
| --- |
| Unique ID | Title |
| 820179 | Core part: High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) |
| 820279 | Perf. part: High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

The 3GPP Rel-16 work item on High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) was completed at RP#86 (Dec-2019). The work item added PC2 to TDD-TDD EN-DC UE.

In order to reduce the big imbalance between 5G NR uplink and downlink coverage, RAN4 has completed PC2 HPUE feature to improve the uplink coverage for 5G SA deployments on NR bands n41, n77, n78 and n79 in Rel-15 NR WI, including PC2 UL MIMO (2Tx 23+23dBm) and PC2 1Tx (26dBm) UE. The following NR bands were approved to support PC2 HPUE for 5G NR SA in Rel-15：

- Band n41 (2496 – 2690 MHz)：

UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n41

- Band n77 (3.3 - 4.2 GHz)：

UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n77

- Band n78 (3.3 - 3.8 GHz)：

UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n78

- Band n79 (4.4 - 5 GHz)：

UL-MIMO (2Tx 23+23dBm) and 1Tx (26dBm) are supported for NR Band n79

For 5G NR NSA deployment, the imbalance between UL and DL coverage still exists, and the uplink coverage for EN-DC is also need to be improved. Considering the technical status of the industry chain, the Power Class 2 (+26dBm) EN-DC UE should be the most practical and suitable choice to improve the UL coverage for 5G NR NSA deployment.

It is proposed to specify Power Class 2 UE for EN-DC (1LTE band +1 NR band) supporting +26 dBm. PC2 EN-DC for TDD-TDD band combinations are proposed in this Work Item. The Work Item is to develop a new feature to enable Power Class 2 EN-DC UE with 26 dBm maximum output power.

There is a need to introduce an associated RAN5 work item to enable UE conformance testing for High power (power class 2) EN-DC (1 LTE TDD band + 1 NR TDD band) UEs.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance test cases for High power (power class 2) EN-DC (1 LTE TDD band + 1 NR TDD band) UEs covering RF aspects.

This WI is aimed to specify the category of PC2 EN-DC band combinations consisting of 2 different bands DL with 2 different bands UL (1 LTE band and 1 NR band). An overview table of these PC2 EN-DC configurations is provided here:

| EN-DC configuration | Uplink EN-DC configuration |
| --- | --- |
| DC_39A-n41A | DC_39A-n41A |
| DC_(n)41AA | DC_(n)41AA |
| DC_41A-n41A | DC_41A-n41A |
| DC_39A-n79A | DC_39A-n79A |
| DC_41A-n79A | DC_41A-n79A |

NOTE: The core requirements of DC_(n)41AA and DC_41A-n41A have been completed in RAN4 Rel-15 TS 38.101-3. And the UE conformance test cases, including power class 2 test cases, for both DC_(n)41AA and DC_41A-n41A are in the scope of RAN5 Rel-15 WI “5GS_NR_LTE-UEConTest”.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 38.508-1 | Definition of common test environment for the NR Rel-16 CA configurations. | TSG RAN#91 (Mar-21) |  |
| TS 38.508-2 | Introduction of common implementation conformance statement (ICS) for new NR Rel-16 CA configurations | TSG RAN#91 (Mar-21) |  |
| TS 38.521-3 | Introduction of new NR Rel-16 CA configurations specific RF requirements for Range 1 and Range 2 Interworking operation with other radios. | TSG RAN#91 (Mar-21) |  |
| TS 38.522 | Applicability statements of the new NR Rel-16 CA configurations for the RF & RRM test cases. | TSG RAN#91 (Mar-21) |  |
| TR 38.905 | Documentation of test points for NR Rel-16 CA RF test cases | TSG RAN#91 (Mar-21) |  |

## 6	Work item Rapporteur(s)

SONG, Dan (China Mobile)

songdan@chinamobile.com

## 7	Work item leadership

RAN5

## 8	Aspects that involve other WGs

None

## 9	Supporting Individual Members

Supporting IM name

CMCC

Huawei

Hisilicon

ZTE

OPPO

Sporton

Sprint