3GPP TSG-RAN5 Meeting #87-e	R5-202514

Electronic Meeting, 18 May – 29 May 2020

3GPP TSG RAN Meeting #88-e	RP-20xxxx

Electronic Meeting, 29 June – 3 July 2020	Revision of RP-20xxxx

# Source:	Huawei, HiSilicon

# Title:	New WID on: NR R16 UE Conformance Test Aspects for V2X

# Document for:	Approval

Agenda Item:	TBD

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	UE Conformance Test Aspects for 5G V2X with NR sidelink

## Acronym: 5G_V2X_NRSL-UEConTest

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network |  |
|  | Services |  |

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  |  |  |
| No | X |  | X | X |  |
| Don't know |  |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

|  | Feature |
| --- | --- |
| X | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work Items |
| --- |
| Unique ID | Title |
| 830078 | 5G V2X with NR sidelink |
| 830178 | Core part: 5G V2X with NR sidelink |
| 830278 | Perf. part: 5G V2X with NR sidelink |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

5G V2X service with NR sidelink is urgently desired from market requirement as widely deployed LTE/NR-based network provides the opportunity for the vehicle industry to realize the concept of ‘connected cars’. 3GPP is actively conducting study and specification work on NR-based V2X in order to meet this requirement.

The Rel-16 WI 5G_V2X_NRSL aims to specify enhancements to both Uu transport and PC5 transport in E-UTRAN/NR to support NR-based V2X (V2V, V2I/N, and V2P). 3GPP RAN WG1/2/3/4 have completed the most of core part work in core specifications in April 2020. The corresponding UE conformance specifications are now required to be implemented in 3GPP RAN WG5. For now, at least test cases on following aspects need to be specified:

-	Signaling tests:

-	Mode 1 sidelink communication

-	Dynamic grant

-	Configuration grant type 1

-	Configuration grant type 2

-	Mode 2 sidelink communication

-	Sidelink communication during HO/Re-establishment

-	Event-triggered and Periodical measurement reporting on PC5

-	RF tests:

-	Tx & Rx characteristics of NR sidelink

-	RRM tests:

-	UE Transmit Timing error;

-	Initiation/Cease of SLSS transmissions and drop rate;

-	SL-RSRP measurement report delay and accuracy;

-	Interruptions to Uu caused by PC5;

-	Demod tests:

-	Demodulation of PSCCH

-	Demodulation of PSSCH

-	Demodulation of PSBCH

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The objective of this work item is to provide conformance test specifications for the core requirements Rel-16 WI 5G_V2X_NRSL in RAN1, RAN2 and RAN4. This work item will cover RF, RRM, Demodulation and Protocol conformance test specifications with NR-based V2X operation.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 38.508-1 | Definition of common environment for NR V2X requirements tests | TSG RAN#94 (Dec-21) |  |
| TS 38.508-2 | Introduction of common implementation conformance statements for NR V2X test cases. | TSG RAN#94 (Dec-21) |  |
| TS 38.509 | Introduction of special conformance testing functions for NR V2X test cases. | TSG RAN#94 (Dec-21) |  |
| TS 36.509 | Introduction of special conformance testing functions for NR V2X test cases. | TSG RAN#94 (Dec-21) |  |
| TS 38.521-1 | Introduction of tests for NR V2X FR1 RF requirements under SA | TSG RAN#94 (Dec-21) |  |
| TS 38.521-3 | Introduction of tests for NR V2X RF requirements under NSA | TSG RAN#94 (Dec-21) |  |
| TS 38.521-4 | Introduction of tests for NR V2X demod requirements | TSG RAN#94 (Dec-21) |  |
| TS 38.522 | Introduction of test applicability for NR V2X RF requirements. | TSG RAN#94 (Dec-21) |  |
| TS 38.533 | Introduction of tests for NR V2X RRM requirements | TSG RAN#94 (Dec-21) |  |
| TS 38.523-1 | Introduction of the SIG tests for NR V2X requirements | TSG RAN#94 (Dec-21) |  |
| TS 38.523-2 | Introduction of test applicability for SIG tests for NR V2X requirements | TSG RAN#94 (Dec-21) |  |
| TS 38.523-3 | Introduction of test model for NR V2X requirements | TSG RAN#94 (Dec-21) | Note: Progress of TTCN development is tracked in MCC TF160 reports to RAN5/RAN. |
| TR 38.903 | Derivation of test tolerances and measurement uncertainty for User Equipment (UE) conformance test cases for NR V2X requirements | TSG RAN#94 (Dec-21) |  |
| TR 38.905 | Derivation of test points for NR V2X RF requirements | TSG RAN#94 (Dec-21) |  |

## 6	Work item Rapporteur(s)

Wu, Yuchun (Huawei)

wuyuchun@huawei.com

## 7	Work item leadership

RAN5

## 8	Aspects that involve other WGs

None

## 9	Supporting Individual Members

Supporting IM name

Huawei

HiSilicon

CMCC

China Telecom

China Unicom

CATT

CAICT

Orange

SamSung

Keysight

ZTE