## Slide 1: 3GPP RAN5 #88-e 17 to 28 Aug 2020 R5-204848 Test Tolerance review process for FR2 RRM Test cases

## Slide 2: Current status
RAN5 focus is now on FR2, with many new challenges for MU/TT
  Significant TT effort required to complete FR2 RRM Test cases
  FR2 RRM has new features to be handled and needs new templates
  FR2 RRM Test cases developed in parallel by multiple companies
First FR2 RRM TT analyses have started to appear
  FR2 SS-RSRP TT templates R5-201713, 14: proposals endorsed at RAN5#87-e
  Complete FR2 Tx timing TT analysis provided at RAN5#87-e in R5-202867, not agreed because some MU values are in [ ]
New FR2 RRM TT analysis features discussed
  R5-198363 technical discussion of features provided at RAN5#85
  R5-200163 added handling of common FR2 TT Topics in 38.903 A.2

## Slide 3: Proposed Way Forward (1 of 4)
“Startup” stage leading up to RAN5#88-e
  Anritsu will prepare some basic FR2 TT templates as “toolkit” for selected test cases to start the process, at RAN5#88-e and RAN5#89-e
  We propose putting the available draft templates into TR38.903, with editor’s notes per TT analysis stating the incomplete items. Drafts will be removed as soon as complete TT analyses are provided.
FR2 RRM Test Tolerance review process for RAN5#89-e onwards
  Following similar process currently used for FR1
  Providing companies to develop FR2 TT analyses based on toolkit
  Share review workload between FR2 TT reviewing companies
..more details on following slides

## Slide 4: Proposed Way Forward (2 of 4)
Leading up to RAN5#88-e, RAN5#89-e
  Anritsu will prepare FR2 TT analysis templates for selected test cases
Analysis for Test cases: | Test case type | EN-DC 5.x Providing Company | SA 7.x Providing Company | Comments
7.1.1.2 | Inter-f Reselection | - | Huawei | Unresolved method for absolute thresholds
5.3.2.2.1+7.3.2.2.1 | Random Access | Anritsu | Anritsu | Held up in RAN4 on method for thresholds
5.4.1.1+7.4.1.1 | Tx Timing | Qualcomm | Qualcomm | Awaiting MU, rest OK
5.5.1.3+7.5.1.3 | RLM Out-of-Sync | Qualcomm | Qualcomm | Awaiting MU, rest OK
5.6.1.2+7.6.1.2 | Intra-f Event Trig | Huawei | Huawei | Awaiting MU and 240kHz SCSSSB method
5.6.2.2+7.6.2.2 | Inter-f Event Trig | Ericsson | Ericsson | Awaiting MU, rest OK
5.7.1.1+7.7.1.1 | Intra-f SS-RSRP | Rohde+Schwarz | Rohde+Schwarz | Awaiting MU, rest OK
5.7.1.2+7.7.1.2 | Inter-f SS-RSRP | Rohde+Schwarz | Rohde+Schwarz | Awaiting MU and 240kHz SCSSSB method

## Slide 5: Proposed Way Forward (3 of 4)
Leading up to RAN5#88-e, RAN5#89-e
  Baseline for list of test cases was the Representative test cases to start FR2 RRM MU analysis in R5-201155, also considering
  Random Access test cases have issues with signalled absolute thresholds and the range of allowed UE gain. Anritsu has proposed a method of handling this in RAN4, awaiting agreement
  The same issue with signalled absolute thresholds also affects the Inter-frequency reselection test case
  Aim for most FR2 RRM test case providing companies to contribute
  FR2 RRM test case providing companies can become familiar with the analysis method and toolkit
  All analyses will need to be updated, according to outcome of FR2 MU agreements

## Slide 6: Proposed Way Forward (4 of 4)
FR2 RRM Test Tolerance review process for RAN5#89-e onwards
  “Declaration” date: normally (meeting upload deadline – 4 weeks)
  “Drafts available” date: normally (meeting upload deadline – 2 weeks)
  Providing companies to develop FR2 TT analyses based on toolkit
  Share review workload between FR2 RRM reviewing companies
  NR TT review process runs at main meetings only (4 times per year)
  Test case sign-up companies resolve any associated RAN4 issues
RRM TT reviewing companies so far for FR2 (thanks):
  Qualcomm, Rohde & Schwarz, Ericsson, Anritsu, Keysight
  Other companies welcome to join

## Slide 7: Scope and Technical basis
Scope of FR2 RRM Test Tolerance review process:
  RRM Test cases containing at least one cell in FR2
Technical basis:
  Principle of Superposition, as defined in TR 38.903
  Uncertainties are orthogonal (required for superposition to be valid)
  Base on common uncertainties, such as TS 38.533 Table F.1.1.2-2
  Measurement uncertainty tolerance interval 95%, as in TR 38.903
  All core requirement side conditions met, based on tolerance interval
  The technical basis above aligns with TT = MU

## Slide 8: Deliverables (1 of 2)
At the “Declaration” date:
  Which test cases the contributing company intends to work on
  Identify any not-yet-finalised MU values for these test cases
At the “Drafts available” date:
  Draft TT analysis, .xls and .doc as required
  TR 38.903 CR to include the TT analysis as .zip files and update of the grouping table in clause 8
  Conformance test spec CRs to include TT in the test cases, together with Annex F updates (Uncertainties and Test requirement derivation)
  Draft MU discussion paper provided to the FR2 MU reflector
  Identify issues and proposals to solve, for example RAN4 updates

## Slide 9: Deliverables (2 of 2)
At the Tdoc upload date and at the meeting:
  TR 38.903 and Conformance test spec CRs
  Known status of any associated issues such as RAN4 dependency

## Slide 10: Open issues
FR2 Uncertainties/MUs
  RAN5 has not yet agreed some of the key FR2 MU values
RAN4 Core requirements in TS 38.133 and 38.101-2
  Many FR2 requirements / conditions only defined for Power Class 3
AoA of RRM test cases in TS 38.133 Annex A
  Likely that some RRM Test cases with 2 AoA will need to be changed from setup 3 (both AoA Spherical coverage) to setup 4 (one AoA Spherical coverage, one AoA Rx beam peak) to avoid huge variations
RRM test cases in TS 38.133 Annex A using absolute thresholds
  Signalled value may need to be derived from a calibration process
Unknown unknowns in TS 38.133 Annex A
  Test cases may reveal problems and immaturities when analysed

## Slide 11: Summary: Way Forward for FR2
RAN5 is asked to endorse key points for FR2 TT review process:
  “Declaration” date: normally (meeting upload deadline – 4 weeks)
  “Drafts available” date: normally (meeting upload deadline – 2 weeks)
  Providing companies to develop FR2 TT analyses based on toolkit
  Share review workload between NR-reviewing companies
  NR TT review process runs at main meetings only (4 times per year)
  Test case sign-up companies resolve any associated RAN4 issues
RAN5 is also asked to endorse:
  Scope is RRM, and currently Power Class 3
  Technical basis as given on slide 7
  Identify any test cases where special handling of TT is required