3GPP TSG-RAN5 Meeting #88-e	R5-204354

Electronic Meeting, 17th – 28th Aug 2020

3GPP TSG RAN Meeting #89-e	RP-20xxxx

Electronic Meeting, 14th – 18th Sep 2020	(revision of RP-2xxxx)

# Source:	China Unicom，CMCC

# Title:	New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band)

# Document for:	Approval

Agenda Item:	7.4.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	UE Conformance Test Aspects - High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band)

## Acronym: ENDC_UE_PC2_FDD_TDD-UEConTest

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network |  |
|  | Services |  |

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  |  |  |  |  |
| No | X | X | X | X |  |
| Don't know |  |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

|  | Feature |
| --- | --- |
| X | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

The following lists of RAN4 work items that will be tested in this RAN5 work item will be maintained in future revisions of this WI description:

| Parent Work Items |
| --- |
| Unique ID | Title |
| 860055 | Core part: High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 820061 | Study on high power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) | Study item on support of high power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) |

## 3	Justification

The HPUE (PC2) for EN-DC (1 LTE FDD band and 1 NR TDD band) have significant benefits for increasing UE transmission power and improving EN-DC network UL coverage. The 3GPP R16 Study item on High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) is already completed at Dec 2019, and the corresponding RAN4 WI ENDC_UE_PC2_FDD_TDD is 60% completion and targeted at August 2020.

It is proposed to introduce an associated RAN5 work item to enable UE conformance testing for High power (power class 2) EN-DC (1 LTE FDD band + 1 NR TDD band) UEs.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance test cases and associated test environment, test applicability, test point analysis on High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band).

The scope of this WI is all the Ran4 completed PC2 1 LTE FDD +1 NRTDD EN-DC configurations as following：DC_3A_n78A, DC_3A_n41A. More PC2 EN-DC configurations may be introduced in this Work Item after other basket WIs of ENDC_UE_PC2_FDD_TDD in RAN4 is completed.

NOTE: The DC_3A_n78A configuration is in the scope of RAN5 Rel-15 WI “5GS_NR_LTE-UEConTest”, and the DC_3A_n41A configuration is in the scope of RAN5 Rel-16 WI “NR_CADC_NR_LTE_DC_R16-UEConTest”.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 38.508-1 | Definition of common test environment for the NR Rel-16 PC2 FDD-TDD EN-DC configurations. | TSG RAN#94 (Dec-21) |  |
| TS 38.508-2 | Introduction of common implementation conformance statement (ICS) for R16 PC2 FDD-TDD EN-DC configurations | TSG RAN#94 (Dec-21) |  |
| TS 38.521-3 | Introduction of R16 PC2 FDD-TDD EN-DC configurations RF requirements | TSG RAN#94 (Dec-21) |  |
| TS 38.522 | Applicability statements of the R16 PC2 FDD-TDD EN-DC configurations for the RF & RRM test cases. | TSG RAN#94 (Dec-21) |  |
| TR 38.905 | Derivation of test points for R16 HPUE PC2 FDD-TDD requirements in radio transmission and reception User Equipment (UE) conformance test cases. | TSG RAN#94 (Dec-21) |  |

## 6	Work item Rapporteur(s)

SHI, Yu (China Unicom)

shiyu19@chinaunicom.cn

Song，Dan (CMCC)

songdan@chinamobile.com

## 7	Work item leadership

RAN5

## 8	Aspects that involve other WGs

None

## 9	Supporting Individual Members

Supporting IM name

China Unicom

Huawei

Hisilicon

Qualcomm

ZTE Corporation

CMCC

Ericsson

Samsung

OPPO