3GPP TSG WG RAN5 Meeting #89-e														R5-205023

Electronic Meeting

9th – 20th November 2020

3GPP TSG WG RAN5 Meeting #88-e																R5-203214

Electronic Meeting

17th – 28th August 2020

# Report from the RAN WG5#88-e Meeting

# Electronic Meeting

17th – 28th August 2020

# v 1.0

# Chairman:					Jacob John, Motorola Mobility

Meeting Secretary:		Ingbert Sigovich, ETSI/MCC Project manager

Vice Chairman (SIG sub WG):	Xiaozhong Chen, CATT

RF session Chair (RF sub WG):	Pradeep Gowda, Qualcomm Inc

RF session Secretary:		Amy Tao, Bureau Veritas

## Contents:

1	Opening of the meeting	15

2	Reports	16

2.1	Live Reports	16

2.2	General Reports for information	18

3	 Incoming Liaison Statements	19

4	RAN5 General Issues	22

4.1	New Work Item proposals - for intro only	22

4.2	General Discussion Papers	27

4.2.1	5GS	27

4.2.2	All other topics	28

4.3	RAN5 PRDs/Templates	28

4.4	Meeting schedule for 2020-21	28

4.5	Tdocs for mid-week joint session	28

4.5.1	RF group docs for WG review/verdict - original A.I. retained	28

4.5.2	Sig group docs for WG review/verdict - original A.I. retained	28

4.5.3	Other open issues from joint sessions - original A.I. retained	28

4.5.4	UE Application Layer Data Throughput Performance  TEI11_Test / TEI15_Test (TR 37.901)	30

4.5.5	GCF Test Optimisation	30

4.5.6	5GS	30

4.5.7	Other	30

5	RF Functional Area	30

5.1	Review action points (fm A.I. 2.1)	30

5.2	Review incoming LS (fm A.I. 3) & new subject discussion papers	30

5.3	Open Work Items	31

5.3.1	Rel-14 LTE CA configurations (UID - 720098) LTE_CA_R14-UEConTest	31

5.3.1.1	TS 36.508	31

5.3.1.2	TS 36.521-1	32

5.3.1.3	TS 36.521-2	32

5.3.1.4	TS 36.521-3	32

5.3.1.5	TS 37.571-1	32

5.3.1.6	TS 37.571-3	32

5.3.1.7	TS 37.571-5	32

5.3.1.8	TR 36.903 (E-UTRAN RRM TT analyses)	32

5.3.1.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)	32

5.3.1.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	32

5.3.1.11	Discussion Papers, Work Plan, TC lists	33

5.3.2	5G system with NR and LTE (UID - 760087) 5GS_NR_LTE-UEConTest	33

5.3.2.1	TS 38.508-1	33

5.3.2.2	TS 38.508-2	42

5.3.2.3	TS 38.509	45

5.3.2.4	TS 38.521-1	45

5.3.2.4.1	Tx Requirements (Clause 6)	45

5.3.2.4.2	Rx Requirements (Clause 7)	51

5.3.2.4.3	Clauses 1-5, Annexes	53

5.3.2.5	TS 38.521-2	55

5.3.2.5.1	Tx Requirements (Clause 6)	55

5.3.2.5.2	Rx Requirements (Clause 7)	65

5.3.2.5.3	Clauses 1-5, Annexes	66

5.3.2.6	TS 38.521-3	69

5.3.2.6.1	Tx Requirements (Clause 6)	70

5.3.2.6.2	Rx Requirements (Clause 7)	77

5.3.2.6.3	Clauses 1-5, Annexes	86

5.3.2.7	TS 38.521-4	87

5.3.2.7.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	88

5.3.2.7.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	92

5.3.2.7.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	93

5.3.2.7.4	Clauses 1-4, Annexes	93

5.3.2.8	TS 38.522	94

5.3.2.9	TS 38.533	96

5.3.2.9.1	EN-DC with all NR cells in FR1 (Clause 4)	102

5.3.2.9.2	EN-DC with at least 1 NR Cell in FR2 (Clause5)	109

5.3.2.9.3	NR Standalone in FR1 (Clause 6)	111

5.3.2.9.4	NR standalone with at least one NR cell in FR2 (Clause7)	122

5.3.2.9.5	E-UTRA – NR Inter-RAT with E-UTRA serving cell (Clause 8)	124

5.3.2.9.6	Clauses 1-3, Annexes	125

5.3.2.10	TS 36.508	131

5.3.2.11	TS 36.521-3	131

5.3.2.12	TS 37.571-1	131

5.3.2.13	TS 37.571-3	131

5.3.2.14	TS 37.571-5	131

5.3.2.15	TR 38.903 ((NR MU &  TT analyses)	131

5.3.2.16	TR 38.905 (NR Test Points Radio Transmission and Reception )	140

5.3.2.17	Discussion Papers, Work Plan, TC lists	146

5.3.3	Rel-15 LTE CA configurations (UID - 770064) LTE_CA_R15-UEConTest	179

5.3.3.1	TS 36.508	179

5.3.3.2	TS 36.521-1	179

5.3.3.3	TS 36.521-2	181

5.3.3.4	TS 36.521-3	182

5.3.3.5	TS 37.571-1	182

5.3.3.6	TS 37.571-3	182

5.3.3.7	TS 37.571-5	182

5.3.3.8	TR 36.903 (E-UTRAN RRM TT analyses)	182

5.3.3.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)	182

5.3.3.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	182

5.3.3.11	Discussion Papers, Work Plan, TC lists	182

5.3.4	Rel-16 CA configurations (UID - 810061) LTE_CA_R16-UEConTest	182

5.3.4.1	TS 36.508	182

5.3.4.2	TS 36.521-1	182

5.3.4.3	TS 36.521-2	182

5.3.4.4	TS 36.521-3	182

5.3.4.5	TS 37.571-1	182

5.3.4.6	TS 37.571-3	182

5.3.4.7	TS 37.571-5	182

5.3.4.8	TR 36.903 (E-UTRAN RRM TT analyses)	182

5.3.4.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)	182

5.3.4.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	182

5.3.4.11	Discussion Papers, Work Plan, TC lists	182

5.3.5	Shortened TTI and processing time for LTE (UID - 820064) LTE_sTTIandPT-UEConTest	182

5.3.5.1	TS 36.508	182

5.3.5.2	TS 36.521-1	182

5.3.5.3	TS 36.521-2	184

5.3.5.4	TS 36.521-3	184

5.3.5.5	TR 36.903 (E-UTRAN RRM TT analyses)	185

5.3.5.6	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	185

5.3.5.7	Discussion Papers, Work Plan, TC lists	185

5.3.6	Enhancing LTE CA Utilization (UID - 820066) LTE_euCA-UEConTest	186

5.3.6.1	TS 36.508	186

5.3.6.2	TS 36.521-2	186

5.3.6.3	TS 36.521-3	186

5.3.6.4	TR 36.903 (E-UTRAN RRM TT analyses)	186

5.3.6.5	Discussion Papers, Work Plan, TC lists	186

5.3.7	REL-16 NR CA and DC; and NR and LTE DC Configurations (UID-830083)  NR_CADC_NR_LTE_DC_R16-UEConTest	186

5.3.7.1	TS 38.508-1	186

5.3.7.2	TS 38.508-2	187

5.3.7.3	TS 38.521-1	191

5.3.7.3.1	Tx Requirements (Clause 6)	191

5.3.7.3.2	Rx Requirements (Clause 7)	191

5.3.7.3.3	Clauses 1-5, Annexes	192

5.3.7.4	TS 38.521-2	193

5.3.7.4.1	Tx Requirements (Clause 6)	193

5.3.7.4.2	Rx Requirements (Clause 7)	193

5.3.7.4.3	Clauses 1-5, Annexes	193

5.3.7.5	TS 38.521-3	193

5.3.7.5.1	Tx Requirements (Clause 6)	193

5.3.7.5.2	Rx Requirements (Clause 7)	198

5.3.7.5.3	Clauses 1-5, Annexes	200

5.3.7.6	TS 38.521-4	201

5.3.7.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	201

5.3.7.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	201

5.3.7.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	201

5.3.7.6.4	Clauses 1-4, Annexes	201

5.3.7.7	TS 38.522	201

5.3.7.8	TS 38.533	201

5.3.7.9	TR 38.903 (NR MU &  TT analyses)	201

5.3.7.10	TR 38.905 (NR Test Points Radio Transmission and Reception)	201

5.3.7.11	Discussion Papers, Work Plan, TC lists	206

5.3.8	Enhancements on Full-Dimension (FD) MIMO for LTE (UID - 830085) LTE_eFDMIMO-UEConTest	206

5.3.8.1	TS 36.508	206

5.3.8.2	TS 36.521-1	206

5.3.8.3	TS 36.521-2	206

5.3.8.4	TR 36.904 (E-UTRAN Radio Reception TT analyses)	206

5.3.8.5	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	206

5.3.8.6	Discussion Papers, Work Plan, TC lists	206

5.3.9	Study on 5G NR User Equipment (UE) Application Layer Data Throughput Performance (UID - 840090) FS_UE_5GNR_App_Data_Perf	206

5.3.9.1	TR 37.901-5	206

5.3.9.2	Discussion Papers, Work Plan, TC lists	208

5.3.10	LTE Advanced high power TDD UE (power class 2) for Rel-15 (UID - 850061) LTE_TDD_HPUE_R15-UEConTest	208

5.3.10.1	TS 36.521-1	208

5.3.10.2	TS 36.521-2	208

5.3.10.3	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	208

5.3.10.4	Discussion Papers, Work Plan, TC lists	208

5.3.11	New Rel-16 NR bands and extension of existing NR bands (UID - 850062) NR_bands_BW_R16-UEConTest	208

5.3.11.1	TS 38.508-1	208

5.3.11.2	TS 38.508-2	210

5.3.11.3	TS 38.521-1	210

5.3.11.3.1	Tx Requirements (Clause 6)	211

5.3.11.3.2	Rx Requirements (Clause 7)	213

5.3.11.3.3	Clauses 1-5, Annexes	215

5.3.11.4	TS 38.521-2	216

5.3.11.4.1	Tx Requirements (Clause 6)	216

5.3.11.4.2	Rx Requirements (Clause 7)	216

5.3.11.4.3	Clauses 1-5, Annexes	216

5.3.11.5	TS 38.521-4	216

5.3.11.5.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	216

5.3.11.5.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	216

5.3.11.5.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	216

5.3.11.5.4	Clauses 1-4, Annexes	216

5.3.11.6	TS 38.533	216

5.3.11.7	TS 37.571-1	216

5.3.11.8	TR 38.903 ((NR MU &  TT analyses)	216

5.3.11.9	TR 38.905 (NR Test Points Radio Transmission and Reception)	216

5.3.11.10	Discussion Papers, Work Plan, TC lists	218

5.3.12	Addition of Power Class 2 UE for LTE bands 31 and 72 (UID – 860030) LTE_PC2_B31_B72-UEConTest	219

5.3.12.1	TS 36.521-1	219

5.3.12.2	TS 36.521-2	219

5.3.12.3	Discussion Papers, Work Plan, TC lists	219

5.3.13	Further NB-IoT enhancements (UID – 860031) NB_IOTenh2-UEConTest	219

5.3.13.1	TS 36.508	219

5.3.13.2	TS 36.521-1	219

5.3.13.3	TS 36.521-2	220

5.3.13.4	TS 36.521-3	221

5.3.13.5	TS 37.571-1	222

5.3.13.6	TS 37.571-3	222

5.3.13.7	TS 37.571-5	222

5.3.13.8	TR 36.903 (E-UTRAN RRM TT analyses)	222

5.3.13.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)	222

5.3.13.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	222

5.3.13.11	Discussion Papers, Work Plan, TC lists	222

5.3.14	Even further enhanced MTC for LTE (UID – 860032) LTE_eMTC4-UEConTest	222

5.3.14.1	TS 36.508	222

5.3.14.2	TS 36.521-1	222

5.3.14.3	TS 36.521-2	227

5.3.14.4	TS 36.521-3	227

5.3.14.5	TS 37.571-1	227

5.3.14.6	TS 37.571-3	227

5.3.14.7	TS 37.571-5	227

5.3.14.8	TR 36.903 (E-UTRAN RRM TT analyses)	227

5.3.14.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)	227

5.3.14.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	227

5.3.14.11	Discussion Papers, Work Plan, TC lists	227

5.3.15	RF requirements for NR frequency range 1 (FR1) (UID-870061)  NR_RF_FR1-UEConTest	227

5.3.15.1	TS 38.508-1	227

5.3.15.2	TS 38.508-2	227

5.3.15.3	TS 38.521-1	227

5.3.15.3.1	Tx Requirements (Clause 6)	227

5.3.15.3.2	Rx Requirements (Clause 7)	231

5.3.15.3.3	Clauses 1-5, Annexes	233

5.3.15.4	TS 38.521-3	234

5.3.15.4.1	Tx Requirements (Clause 6)	234

5.3.15.4.2	Rx Requirements (Clause 7)	234

5.3.15.4.3	Clauses 1-5, Annexes	234

5.3.15.5	TS 38.522	234

5.3.15.6	TS 38.533	234

5.3.15.7	TR 38.903 (NR MU &  TT analyses)	234

5.3.15.8	TR 38.905 (NR Test Points Radio Transmission and Reception)	234

5.3.15.9	TS 36.521-3	236

5.3.15.10	TR 36.903 (E-UTRAN RRM TT analyses)	236

5.3.15.11	Discussion Papers, Work Plan, TC lists	236

5.3.16	High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) (UID-870062)  ENDC_UE_PC2_TDD_TDD-UEConTest	236

5.3.16.1	TS 38.508-1	236

5.3.16.2	TS 38.508-2	236

5.3.16.3	TS 38.521-3	236

5.3.16.3.1	Tx Requirements (Clause 6)	236

5.3.16.3.2	Rx Requirements (Clause 7)	236

5.3.16.3.3	Clauses 1-5, Annexes	236

5.3.16.4	TS 38.522	236

5.3.16.5	TR 38.905 (NR Test Points Radio Transmission and Reception)	236

5.3.16.6	Discussion Papers, Work Plan, TC lists	236

5.3.17	Even Further Mobility Enhancement for E-UTRAN (UID – 880066) LTE_feMob-UEConTest	236

5.3.17.1	TS 36.508	236

5.3.17.2	TS 36.521-2	236

5.3.17.3	TS 36.521-3	236

5.3.17.4	TR 36.903 (E-UTRAN RRM TT analyses)	236

5.3.17.5	Discussion Papers, Work Plan, TC lists	236

5.3.18	NR Mobility Enhancements (UID-880068)  NR_Mob_enh-UEConTest	236

5.3.18.1	TS 38.508-1	236

5.3.18.2	TS 38.508-2	236

5.3.18.3	TS 38.522	236

5.3.18.4	TS 38.533	236

5.3.18.5	TR 38.903 (NR MU &  TT analyses)	236

5.3.18.6	Discussion Papers, Work Plan, TC lists	237

5.3.19	5G V2X with NR sidelink (UID-880069)  5G_V2X_NRSL_eV2XARC-UEConTest	237

5.3.19.1	TS 38.508-1	237

5.3.19.2	TS 38.508-2	237

5.3.19.3	TS 38.509	237

5.3.19.4	TS 38.521-1	237

5.3.19.4.1	Tx Requirements (Clause 6)	237

5.3.19.4.2	Rx Requirements (Clause 7)	237

5.3.19.4.3	Clauses 1-5, Annexes	237

5.3.19.5	TS 38.521-3	237

5.3.19.5.1	Tx Requirements (Clause 6)	237

5.3.19.5.2	Rx Requirements (Clause 7)	237

5.3.19.5.3	Clauses 1-5, Annexes	237

5.3.19.6	TS 38.521-4	238

5.3.19.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	238

5.3.19.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	238

5.3.19.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	238

5.3.19.6.4	Clauses 1-4, Annexes	238

5.3.19.7	TS 38.522	238

5.3.19.8	TS 38.533	238

5.3.19.9	TS 36.509	238

5.3.19.10	TR 38.903 (NR MU &  TT analyses)	238

5.3.19.11	TR 38.905 (NR Test Points Radio Transmission and Reception)	238

5.3.19.12	Discussion Papers, Work Plan, TC lists	238

5.3.20	Enhancements on MIMO for NR (UID-880070)  NR_eMIMO-UEConTest	240

5.3.20.1	TS 38.508-1	240

5.3.20.2	TS 38.508-2	240

5.3.20.3	TS 38.521-1	240

5.3.20.3.1	Tx Requirements (Clause 6)	240

5.3.20.3.2	Rx Requirements (Clause 7)	240

5.3.20.3.3	Clauses 1-5, Annexes	240

5.3.20.4	TS 38.521-2	240

5.3.20.4.1	Tx Requirements (Clause 6)	240

5.3.20.4.2	Rx Requirements (Clause 7)	240

5.3.20.4.3	Clauses 1-5, Annexes	240

5.3.20.5	TS 38.521-3	240

5.3.20.5.1	Tx Requirements (Clause 6)	240

5.3.20.5.2	Rx Requirements (Clause 7)	240

5.3.20.5.3	Clauses 1-5, Annexes	240

5.3.20.6	TS 38.521-4	240

5.3.20.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	240

5.3.20.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	240

5.3.20.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	240

5.3.20.6.4	Clauses 1-4, Annexes	240

5.3.20.7	TS 38.522	240

5.3.20.8	TS 38.533	240

5.3.20.9	TR 38.903 (NR MU &  TT analyses)	240

5.3.20.10	TR 38.905 (NR Test Points Radio Transmission and Reception)	240

5.3.20.11	Discussion Papers, Work Plan, TC lists	240

5.3.21	UE Power Saving in NR (UID-880071)  NR_UE_pow_sav-UEConTest	241

5.3.21.1	TS 38.508-1	241

5.3.21.2	TS 38.508-2	241

5.3.21.3	TS 38.521-4	241

5.3.21.3.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)	241

5.3.21.3.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)	241

5.3.21.3.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)	241

5.3.21.3.4	Clauses 1-4, Annexes	241

5.3.21.4	TS 38.522	241

5.3.21.5	TS 38.533	241

5.3.21.6	Discussion Papers, Work Plan, TC lists	241

5.4	Routine Maintenance for LTE only TEIx_Test	241

5.4.1	LTE RF	241

5.4.1.1	TS 36.508	241

5.4.1.2	TS 36.521-1	241

5.4.1.2.1	Tx Requirements (Clause 6)	241

5.4.1.2.2	Rx Requirements (Clause 7)	243

5.4.1.2.3	Clauses 1-5, 8-10, Annexes	244

5.4.1.3	TS 36.521-2	244

5.4.1.4	TS 36.521-3	245

5.4.1.5	RRM Test & Radio Reception Test Tolerances	248

5.4.1.5.1	TR 36.903 (E-UTRAN RRM TT analyses)	248

5.4.1.5.2	TR 36.904 (E-UTRAN Radio Reception TT analyses)	249

5.4.1.5.3	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )	249

5.4.1.6	TS 34.121-1	249

5.4.1.7	TS 34.121-2	249

5.4.1.8	TS 34.122	249

5.4.1.9	TS 34.108	249

5.4.1.10	TR 34.902 (UTRAN RRM Test Tolerance analyses)	249

5.4.1.11	Discussion Papers, Work Plan, TC lists	249

5.5	Other Routine Maintenance TEIx_Test	249

5.5.1	TS 34.108	249

5.5.2	TS 34.121-1 All sections other than annexes	249

5.5.3	TS 34.121-1 Annexes only	249

5.5.4	TS 34.121-2	249

5.5.5	TS 34.122	250

5.5.6	TS 34.171	250

5.5.7	TS 34.172	250

5.5.8	TS 34.114	250

5.5.9	TS 37.571-1	250

5.5.10	TS 37.571-3	251

5.5.11	TS 37.571-5	251

5.5.12	TS 51.010-1 (RF/Performance)	251

5.5.13	TS 51.010-2 (RF/Performance)	251

5.5.14	TS 51.010-7 (RF/Performance)	251

5.5.15	TS 37.544	251

5.5.16	Discussion Papers, Work Plan, TC lists	251

5.6	Outgoing liaison statements for provisional approval	251

5.7	AOB	251

6	Signalling Protocol Functional Area	251

6.1	Review action points (fm A.I. 2.1)	251

6.2	Review incoming LS (fm A.I. 3) & new subject discussion papers	251

6.3	Open Work Items	252

6.3.1	Rel-14 LTE CA configurations (UID - 720098) LTE_CA_R14-UEConTest	252

6.3.1.1	TS 36.508	252

6.3.1.2	TS 36.523-1	252

6.3.1.3	TS 36.523-2	252

6.3.1.4	TS 36.523-3	252

6.3.1.5	Discussion Papers, Work Plan, TC lists	252

6.3.2	5G system with NR and LTE (UID - 760087) 5GS_NR_LTE-UEConTest	252

6.3.2.1	TS 38.508-1	252

6.3.2.2	TS 38.508-2	265

6.3.2.3	TS 38.509	266

6.3.2.4	TS 38.523-1	267

6.3.2.4.1	Clauses 1 - 5	267

6.3.2.4.2	Idle Mode (Clause 6)	267

6.3.2.4.3	Layer 2	278

6.3.2.4.3.1	NR Layer 2	278

6.3.2.4.3.1.1	Common Test Case Specific Values for Layer 2 (Clause 7.1.0)	278

6.3.2.4.3.1.2	MAC	278

6.3.2.4.3.1.3	RLC	282

6.3.2.4.3.1.4	PDCP	283

6.3.2.4.3.1.5	SDAP	285

6.3.2.4.4	RRC	286

6.3.2.4.4.1	NR RRC	286

6.3.2.4.4.2	MR-DC RRC	286

6.3.2.4.4.1.1	RRC Connection Management Procedures (clause 8.1.1)	286

6.3.2.4.4.2.1	RRC UE Capability / Others (clause 8.2.1)	289

6.3.2.4.4.1.2	RRC Reconfiguration (clause 8.1.2)	289

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)	289

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)	290

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)	291

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)	293

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)	294

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)	295

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)	295

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)	296

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)	296

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)	297

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)	298

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)	298

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)	300

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)	301

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)	301

6.3.2.4.4.1.5	RRC Others (clause 8.1.5)	301

6.3.2.4.4.2.4	RRC Carrier Aggregation (clause 8.2.4)	302

6.3.2.4.4.1.5	RRC Others (clause 8.1.5)	302

6.3.2.4.4.2.5	RRC Reconfiguration / Radio Link Failure (clause 8.2.5)	302

6.3.2.4.4.2.6	RRC Others (clause 8.2.6)	302

6.3.2.4.5	5GS Mobility Management	303

6.3.2.4.5.1	MM Primary authentication and key agreement (clause 9.1.1)	303

6.3.2.4.5.2	MM Security mode control, Identification & Generic UE configuration update (clauses 9.1.2, 9.1.3 & 9.1.4)	304

6.3.2.4.5.3	MM Registration & De-registration (clauses 9.1.5 & 9.1.6)	304

6.3.2.4.5.4	MM Service Request (clause 9.1.7)	307

6.3.2.4.5.5	MM SMS Over NAS (clause 9.1.8)	307

6.3.2.4.5.6	Inter-system Mobility (clause 9.3)	307

6.3.2.4.6	5GS Session Management	307

6.3.2.4.6.1	SM PDU session authentication and authorization (clause 10.1.1)	307

6.3.2.4.6.2	SM Network-requested PDU session modification & release (clauses 10.1.2 & 10.1.3)	307

6.3.2.4.6.3	SM UE-requested PDU session establishment, modification & release (clauses 10.1.4, 10.1.5 & 10.1.6)	307

6.3.2.4.7	EN-DC Session Management	307

6.3.2.4.8	5GS Multilayer and Services	307

6.3.2.4.8.1	EPS Fallback	307

6.3.2.4.8.2	RAT Fallback	309

6.3.2.4.8.3	Unified Access Control (UAC)	309

6.3.2.4.8.4	Emergency Services	310

6.3.2.5	TS 38.523-2	310

6.3.2.6	TS 38.523-3	312

6.3.2.7	TS 34.229-1	313

6.3.2.8	TS 34.229-2	313

6.3.2.9	TS 34.229-3	314

6.3.2.10	TS 34.229-5	314

6.3.2.11	TS 36.508	320

6.3.2.12	TS 36.509	321

6.3.2.13	TS 36.523-1	321

6.3.2.14	TS 36.523-2	321

6.3.2.15	TS 36.523-3	321

6.3.2.16	TS 37.571-2	321

6.3.2.17	TS 37.571-3	322

6.3.2.18	TS 37.571-4	322

6.3.2.19	TS 37.571-5	322

6.3.2.20	Discussion Papers, Work Plan, TC lists	322

6.3.3	Rel-15 CA configurations (UID - 770064) LTE_CA_R15-UEConTest	323

6.3.3.1	TS 36.508	323

6.3.3.2	TS 36.523-1	323

6.3.3.3	TS 36.523-2	323

6.3.3.4	TS 36.523-3	323

6.3.3.5	Discussion Papers, Work Plan, TC lists	323

6.3.4	Mission Critical Improvements (UID - 790052) MCImp-UEConTest	323

6.3.4.1	TS 36.579-1	323

6.3.4.2	TS 36.579-2	324

6.3.4.3	TS 36.579-3	324

6.3.4.4	TS 36.579-4	324

6.3.4.5	TS 36.579-5	325

6.3.4.6	TS 36.579-6 (pCRs only)	325

6.3.4.7	TS 36.579-7 (pCRs only)	326

6.3.4.8	TS 36.508	326

6.3.4.9	TS 36.509	326

6.3.4.10	TS 36.523-1	326

6.3.4.11	TS 36.523-2	326

6.3.4.12	TS 36.523-3	326

6.3.4.13	Discussion Papers, Work Plan, TC lists	326

6.3.5	Rel-16 LTE CA configurations (UID - 810061) LTE_CA_R16-UEConTest	326

6.3.5.1	TS 36.508	326

6.3.5.2	TS 36.523-1	326

6.3.5.3	TS 36.523-2	326

6.3.5.4	TS 36.523-3	326

6.3.5.5	Discussion Papers, Work Plan, TC lists	326

6.3.6	Shortened TTI and processing time for LTE (UID - 820064) LTE_sTTIandPT-UEConTest	326

6.3.6.1	TS 36.508	326

6.3.6.2	TS 36.509	327

6.3.6.3	TS 36.523-1	327

6.3.6.4	TS 36.523-2	327

6.3.6.5	TS 36.523-3	328

6.3.6.6	Discussion Papers, Work Plan, TC lists	328

6.3.7	Enhancing LTE CA Utilization (UID - 820066) LTE_euCA-UEConTest	328

6.3.7.1	TS 36.508	328

6.3.7.2	TS 36.523-1	328

6.3.7.3	TS 36.523-2	328

6.3.7.4	Discussion Papers, Work Plan, TC lists	328

6.3.8	REL-16 NR CA and DC; and NR and LTE DC Configurations (UID-830083)  NR_CADC_NR_LTE_DC_R16-UEConTest	328

6.3.8.1	TS 38.508-1	328

6.3.8.2	TS 38.508-2	328

6.3.8.3	TS 38.523-1	328

6.3.8.4	TS 38.523-2	328

6.3.8.5	TS 38.523-3	328

6.3.8.6	Discussion Papers, Work Plan, TC lists	328

6.3.9	LTE Advanced high power TDD UE (power class 2) for Rel-15 (UID - 850061) LTE_TDD_HPUE_R15-UEConTest	328

6.3.9.1	TS 36.523-1	328

6.3.9.2	TS 36.523-2	328

6.3.9.3	TS 36.523-3	329

6.3.9.4	Discussion Papers, Work Plan, TC lists	329

6.3.10	New Rel-16 NR bands and extension of existing NR bands (UID - 850062) NR_bands_BW_R16-UEConTest	329

6.3.10.1	TS 38.508-1	329

6.3.10.2	TS 38.508-2	329

6.3.10.3	TS 38.523-3	329

6.3.10.4	Discussion Papers, Work Plan, TC lists	329

6.3.11	Further NB-IoT enhancements (UID – 860031) NB_IOTenh2-UEConTest	329

6.3.11.1	TS 36.508	329

6.3.11.2	TS 36.509	330

6.3.11.3	TS 36.523-1	330

6.3.11.4	TS 36.523-2	331

6.3.11.5	TS 36.523-3	331

6.3.11.6	Discussion Papers, Work Plan, TC lists	331

6.3.12	Even further enhanced MTC for LTE (UID – 860032) LTE_eMTC4-UEConTest	331

6.3.12.1	TS 36.508	331

6.3.12.2	TS 36.509	332

6.3.12.3	TS 36.523-1	332

6.3.12.4	TS 36.523-2	333

6.3.12.5	TS 36.523-3	336

6.3.12.6	Discussion Papers, Work Plan, TC lists	336

6.3.13	RF requirements for NR frequency range 1 (FR1) (UID-870061)  NR_RF_FR1-UEConTest	336

6.3.13.1	TS 38.508-1	336

6.3.13.2	TS 38.508-2	336

6.3.13.3	TS 38.523-1	336

6.3.13.4	TS 38.523-2	336

6.3.13.5	TS 38.523-3	336

6.3.13.6	Discussion Papers, Work Plan, TC lists	336

6.3.14	Even Further Mobility Enhancement for E-UTRAN (UID – 880066) LTE_feMob-UEConTest	336

6.3.14.1	TS 36.508	336

6.3.14.2	TS 36.523-1	336

6.3.14.3	TS 36.523-2	336

6.3.14.4	TS 36.523-3	336

6.3.14.5	Discussion Papers, Work Plan, TC lists	336

6.3.15	Support of NR Industrial Internet of Things (IoT) (UID-880067)  NR_IIOT-UEConTest	336

6.3.15.1	TS 38.508-1	336

6.3.15.2	TS 38.508-2	336

6.3.15.3	TS 38.523-1	336

6.3.15.4	TS 38.523-2	336

6.3.15.5	TS 38.523-3	336

6.3.15.6	TS 36.508	336

6.3.15.7	TS 36.523-1	336

6.3.15.8	TS 36.523-2	336

6.3.15.9	TS 36.523-3	337

6.3.15.10	Discussion Papers, Work Plan, TC lists	337

6.3.16	NR Mobility Enhancements (UID-880068)  NR_Mob_enh-UEConTest	337

6.3.16.1	TS 38.508-1	337

6.3.16.2	TS 38.508-2	337

6.3.16.3	TS 38.523-1	337

6.3.16.4	TS 38.523-2	337

6.3.16.5	TS 38.523-3	337

6.3.16.6	Discussion Papers, Work Plan, TC lists	337

6.3.17	5G V2X with NR sidelink (UID-880069)  5G_V2X_NRSL_eV2XARC-UEConTest	337

6.3.17.1	TS 38.508-1	337

6.3.17.2	TS 38.508-2	337

6.3.17.3	TS 38.509	337

6.3.17.4	TS 38.523-1	337

6.3.17.5	TS 38.523-2	337

6.3.17.6	TS 38.523-3	337

6.3.17.7	TS 36.509	337

6.3.17.8	Discussion Papers, Work Plan, TC lists	337

6.3.18	Enhancements on MIMO for NR (UID-880070)  NR_eMIMO-UEConTest	339

6.3.18.1	TS 38.508-1	339

6.3.18.2	TS 38.508-2	339

6.3.18.3	TS 38.523-1	339

6.3.18.4	TS 38.523-2	339

6.3.18.5	TS 38.523-3	339

6.3.18.6	Discussion Papers, Work Plan, TC lists	339

6.3.19	UE Power Saving in NR (UID-880071)  NR_UE_pow_sav-UEConTest	339

6.3.19.1	TS 38.508-1	339

6.3.19.2	TS 38.508-2	339

6.3.19.3	TS 38.523-1	339

6.3.19.4	TS 38.523-2	339

6.3.19.5	TS 38.523-3	339

6.3.19.6	Discussion Papers, Work Plan, TC lists	339

6.3.20	Private Network Support for NG-RAN (UID-880072)  NG_RAN_PRN_Vertical_LAN-UEConTest	339

6.3.20.1	TS 38.508-1	339

6.3.20.2	TS 38.508-2	339

6.3.20.3	TS 38.523-1	339

6.3.20.4	TS 38.523-2	339

6.3.20.5	TS 38.523-3	339

6.3.20.6	Discussion Papers, Work Plan, TC lists	339

6.3.21	Optimisations on UE radio capability signalling – NR/E-UTRA Aspects (UID-880073)  RACS-UEConTest	339

6.3.21.1	TS 38.508-1	339

6.3.21.2	TS 38.508-2	339

6.3.21.3	TS 38.523-1	339

6.3.21.4	TS 38.523-2	340

6.3.21.5	TS 38.523-3	340

6.3.21.6	TS 36.508	340

6.3.21.7	TS 36.523-1	340

6.3.21.8	TS 36.523-2	340

6.3.21.9	TS 36.523-3	340

6.3.21.10	Discussion Papers, Work Plan, TC lists	340

6.4	Routine Maintenance for TS 38 Series TEIx_Test	340

6.4.1	TS 38.508-1	340

6.4.2	TS 38.508-2	348

6.4.3	TS 38.509	348

6.4.4	TS 38.523-1	348

6.4.4.1	Clauses 1 - 5	348

6.4.4.2	Idle Mode (Clause 6)	348

6.4.4.3	Layer 2	348

6.4.4.3.1	NR Layer 2	348

6.4.4.3.1.1	Common Test Case Specific Values for Layer 2 (Clause 7.1.0)	348

6.4.4.3.1.2	MAC	348

6.4.4.3.1.3	RLC	348

6.4.4.3.1.4	PDCP	349

6.4.4.3.1.5	SDAP	349

6.4.4.4	RRC	349

6.4.4.4.1	NR RRC	349

6.4.4.4.1.1	RRC Connection Management Procedures (clause 8.1.1)	349

6.4.4.4.1.2	RRC Reconfiguration (clause 8.1.2)	349

6.4.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)	349

6.4.4.4.1.4	RRC Handover (clause 8.1.4)	349

6.4.4.4.1.5	RRC Others (clause 8.1.5)	350

6.4.4.4.2	MR-DC RRC	351

6.4.4.4.2.1	RRC UE Capability / Others (clause 8.2.1)	351

6.4.4.4.2.2	RRC Radio Bearer (clause 8.2.2)	352

6.4.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)	352

6.4.4.4.2.4	RRC Carrier Aggregation (clause 8.2.4)	352

6.4.4.4.2.5	RRC Reconfiguration / Radio Link Failure (clause 8.2.5)	352

6.4.4.4.2.6	RRC Others (clause 8.2.6)	352

6.4.4.5	5GS Mobility Management	352

6.4.4.5.1	MM Primary authentication and key agreement (clause 9.1.1)	352

6.4.4.5.2	MM Security mode control, Identification & Generic UE configuration update (clauses 9.1.2, 9.1.3 & 9.1.4)	352

6.4.4.5.3	MM Registration & De-registration (clauses 9.1.5 & 9.1.6)	352

6.4.4.5.4	MM Service Request (clause 9.1.7)	352

6.4.4.5.5	MM SMS Over NAS (clause 9.1.8)	352

6.4.4.6	5GS Non-3GPP Access Mobility Management (clause 9.2)	352

6.4.4.7	5GS Inter-system Mobility (clause 9.3)	353

6.4.4.8	5GS Session Management	353

6.4.4.8.1	SM PDU session authentication and authorization (clause 10.1.1)	353

6.4.4.8.2	SM Network-requested PDU session modification & release (clauses 10.1.2 & 10.1.3)	353

6.4.4.8.3	SM UE-requested PDU session establishment, modification & release (clauses 10.1.4, 10.1.5 & 10.1.6)	353

6.4.4.9	EN-DC Session Management (clause 10.2)	353

6.4.4.10	5GS Non-3GPP Access Session Management (clause 10.3)	353

6.4.4.11	5GS Multilayer and Services	353

6.4.4.11.1	EPS Fallback	353

6.4.4.11.2	RAT Fallback	354

6.4.4.11.3	Unified Access Control (UAC)	354

6.4.4.11.4	Emergency Services	354

6.4.5	TS 38.523-2	354

6.4.6	TS 38.523-3	355

6.4.7	Discussion Papers, Work Plan, TC lists	355

6.5	Routine Maintenance for TS 36 Series TEIx_Test	355

6.5.1	Routine Maintenance for TS 36.508	355

6.5.2	Routine Maintenance for TS 36.509	356

6.5.3	Routine Maintenance for TS 36.523-1	356

6.5.3.1	Idle Mode	356

6.5.3.2	Layer 2	357

6.5.3.2.1	MAC	357

6.5.3.2.2	RLC	357

6.5.3.2.3	PDCP	357

6.5.3.3	RRC	357

6.5.3.3.1	RRC Part 1 (clauses 8.1 and 8.5)	357

6.5.3.3.2	RRC Part 2 (clause 8.2),	357

6.5.3.3.3	RRC Part 3 (clause 8.3)	357

6.5.3.3.4	Inter-RAT (clauses 8.4 & 8.4A)	357

6.5.3.3.5	RRC LTE MDT (clause 8.6)	357

6.5.3.3.6	RRC ANR for UTRAN (clause 8.7)	358

6.5.3.4	EPS Mobility Management	358

6.5.3.5	EPS Session Management	360

6.5.3.6	General Tests	360

6.5.3.7	Interoperability Radio Bearers	360

6.5.3.8	Multilayer Procedures	360

6.5.3.9	PWS - ETWS, CMAS	360

6.5.3.10	Non-3GPP	360

6.5.3.11	Others (TS 36.523-1 clauses not covered by other AIs under AI 6.5.3, e.g. eMBMS, Home (e)NB, MBMS in LTE, D2D, SC-PTM, NB-IoT, CIoT...)	360

6.5.4	Routine Maintenance for TS 36.523-2	362

6.5.5	Routine Maintenance for TS 36.523-3	362

6.5.6	Discussion Papers, Work Plan, TC lists	363

6.6	Other Maintenance TEIx_Test	364

6.6.1	Routine Maintenance for TDD (HCR & LCR)	364

6.6.1.1	TS 34.108	364

6.6.1.2	TS 34.123-1	364

6.6.1.3	TS 34.123-2	364

6.6.1.4	TS 34.123-3	364

6.6.1.5	Discussion Papers, Work Plan, TC list & CR summary	364

6.6.2	Routine Maintenance for TS 34.108	364

6.6.3	Routine Maintenance for TS 34.109	364

6.6.4	Routine Maintenance for TS 34.123	364

6.6.4.1	TS 34.123-1	364

6.6.4.2	TS 34.123-2	364

6.6.4.3	TS 34.123-3	364

6.6.5	Discussion Papers, Work Plan, TC lists	364

6.6.6	Routine Maintenance for TS 34.229	364

6.6.6.1	TS 34.229-1	364

6.6.6.2	TS 34.229-2	366

6.6.6.3	TS 34.229-3	366

6.6.6.4	TS 34.229-4	366

6.6.6.5	Discussion Papers, Work Plan, TC lists	366

6.6.7	Routine Maintenance for TS 37.571	366

6.6.7.1	TS 37.571-2	366

6.6.7.2	TS 37.571-3	367

6.6.7.3	TS 37.571-4	367

6.6.7.4	TS 37.571-5	367

6.6.7.5	Discussion Papers, Work Plan, TC lists	367

6.6.8	Routine Maintenance for TS 51.010	367

6.6.8.1	TS 51.010-1 (Signalling)	367

6.6.8.2	TS 51.010-2 (Signalling)	367

6.6.8.3	TS 51.010-5 (Signalling)	367

6.6.8.4	TS 51.010-7 (Signalling)	367

6.6.8.5	Discussion Papers, Work Plan, TC list & CR summary	367

6.6.9	Routine Maintenance for MCPTT	367

6.6.9.1	TS 36.579-1	367

6.6.9.2	TS 36.579-2	369

6.6.9.3	TS 36.579-3	372

6.6.9.4	TS 36.579-4	372

6.6.9.5	TS 36.579-5	372

6.6.9.6	Other Specs	372

6.6.9.7	Discussion Papers, Work Plan, TC lists	372

6.7	Outgoing liaison statements for provisional approval	373

6.8	AOB	375

7	Closing Joint Session	375

7.1	Pointer CRs	375

7.2	Open Issues	375

7.2.1	RF group docs still requiring WG verdict/confirmation - original A.I. retained	375

7.2.2	Sig group docs still requiring WG verdict/confirmation - original A.I. retained	375

7.2.3	Other open issues from joint sessions - original A.I. retained	375

7.2.4	UE Application Layer Data Throughput Performance - original A.I. retained	375

7.2.5	Other	375

7.3	iWD/PRD Updates	375

7.4	Work Items/ Study Items	376

7.4.1	Final version of Work Item Proposals	376

7.4.2	Active Work Items/ Study Item: work plans (wp), status reports (sr), Work Item Descriptions (wid)	378

7.4.3	Work Plan updates of recently closed work items	385

7.5	Docs still needing agreement/endorsement/approval (e.g. Outgoing LS, Reports, New Specs, Info for certification bodies etc.)	385

7.6	Confirmation of Future RAN5 Matters	387

7.7	AOB	387

Annex A: Contribution documents and status	388

A1: List of TDocs	388

A2: Tdoc decision timing	431

Annex B: List of change requests	432

Annex C: Lists of liaisons	482

C1: Incoming liaison statements	482

C2: Outgoing liaison statements	482

Annex D: List of agreed/approved new and revised Work Items	483

Annex E: List of draft Technical Specifications and Reports	484

Annex F: List of action items	485

SIG:		485

Action Points at RAN5#88-e	485

Action Points at RAN5#87-e	485

Action Points at RAN5#86-e	485

Action Points at RAN5#85 - Reno	486

RF:		486

Action Points at RAN5#88-e	486

Action Points at RAN5#87-e	486

Action Points at RAN5#85 Reno	487

Action Points at RAN5#84 Ljubljana	487

Action Points at RAN5#83 Reno	487

Annex G: List of decisions	488

Annex H: List of participants	489

Annex I: List of future meetings	493

## 1	Opening of the meeting

R5-203200	Agenda - opening session

Type: agenda		For: Information
					Source: WG Chairman

Discussion:

EAR statement changed following the recent decision of the US Department of Commerce clarifying the participation of US companies in standard organizations.204233

Decision: 		The document was revised to R5-204338.

R5-204338	Agenda - opening session

Type: agenda		For: Information
					Source: WG Chairman

(Replaces R5-203200)

Discussion:

Reminder for IPR declaration

The RAN5 Chair drew the attention to the delegates' obligations under the 3GPP Partner Organizations’ IPR policies. Every Individual Member organization is obliged to declare to the Partner Organization or Organizations of which it is a member any IPR owned by the Individual Member or any other organization which is or is likely to become essential to the work of 3GPP.

Delegates are asked to take note that they are thereby invited:

•	to investigate whether their organization or any other organization owns IPRs which were, or were likely to become Essential in respect of the work of 3GPP.

•	to notify their respective Organizational Partners of all potential IPRs, e.g., for ETSI, by means of the IPR Information Statement and the Licensing declaration forms (e.g. see the ETSI IPR forms http://webapp.etsi.org/Ipr/).

Antitrust Guidance

The RAN5 Chair drew the delegates' attention to the fact that 3GPP activities are subject to all applicable antitrust and competition laws and that compliance with said laws is therefore required of any participant of this TSG/WG meeting including the Chairman and Vice Chairman. In case of question it is recommended that you contact your legal counsel.

The leadership shall conduct the present meeting with impartiality and in the interests of 3GPP.

Furthermore, the timely submission of work items in advance of TSG/WG meetings is important to allow for full and fair consideration of such matters.”

http://www.3gpp.org/about-3gpp/legal-matters/21-3gpp-calendar/1616-statement-of-antitrust-compliance

Decision: 		The document was approved.

R5-203201	RAN5#88-e E-Meeting Timelines, Scope, Process

Type: agenda		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

## 2	Reports

### 2.1	Live Reports

R5-203202	RAN5 Leadership Team

Type: other		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203203	RAN5#87-e WG Minutes

Type: report		For: Approval
					Source: ETSI Secretariat

Decision: 		The document was approved.

R5-203204	RAN5#87-e WG Action Points

Type: report		For: Information
					Source: ETSI Secretariat

Decision: 		The document was noted.

R5-203205	Latest RAN Plenary notes

Type: report		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203206	Latest RAN Plenary draft Report

Type: report		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203207	Post Plenary Active Work Item update

Type: other		For: Information
					Source: ETSI Secretariat

Decision: 		The document was noted.

R5-203531	MCC TF160 Status Report

Type: report		For: Approval
					Source: MCC TF160

Abstract:

Completed:

LTE: Aerial UEs

IMS: VoLTE: call cancel, codec change, concatenated SMS.

Started:

LTE: Extended/spare fields

IMS: IMS over NR/5GC

Progressed:

5GS: EN-DC single carrier

EN-DC NR CA

NR/5GC single carrier

NR/5GC Inter-RAT

NR/5GC NR CA

LTE: Rel-14/15/16 CA new BCs

MCPTT; On-network group call

Summary & open issues from 
TTCN Workshop #50 (6th Jul’0):

New Test Models – 5G:

Common aspects:

Handling of the number of PDSCH HARQ processes at RRC connection establishment or resume: a prose CR to TS 38.508-1 proposed at RAN5#88-e.

RLC test case 7.1.2.3.5 performance aspects: a prose CR to TS 38.523-1 proposed at RAN5#88-e to optimise the prose to reduce execution time.

Intra-NR mobility in RRC_CONNECTED with NR CA: sequence of events endorsed, a prose CR to TS 38.523-3 proposed at RAN5#88-e.

NR/5GC (SA option 2):

Flexible handling multi PDUs and PDNs in the 5G test specifications: continued discussions from RAN5#87-e with proponent Samsung, to further prepare draft TTCN-3 trial delivery for SS Vendors. CRs (re-)submitted by Samsung at RAN5#88-e.

Updates to NAS type definitions to support newly implemented test cases.

Endorsed test model addition for NR-DC Layer3 and NR-DC PDCP. A prose CR to TS 38.523-3 proposed at RAN5#88-e.

2020 TTCN Work – Funding:

2020 workload is estimated at 110.5 man.months (mm), see previous slides.

PCG#43/OP#42 approved the 3GPP funding of 68 mm for 2020 TTCN tasks.

PTCRB(CTIA) and GCF have agreed to continue TF160 financial support in 2020.3GPP companies / 3GPP MRPs committed to provide 18.5 mm as voluntary contributions for 2020 TTCN development.

Total resources of 110.5 mm -> no funding gap.

2021 TTCN Work:

Course of action to secure funding for TF160 work in 2021:

Prior to RAN5#88-e meeting (August), a request to identify the potential TTCN development tasks in 2021 has been made to 3GPP members.

At RAN5#88-e, a provisional ‘TTCN Tasks List’ shall be endorsed by RAN5.

The TTCN Tasks List will be presented at RAN#89-e (Sept) for TSG RAN initial endorsement.

The RAN Chair will then present the List to 3GPP PCG/OP (Oct) in order to support TF160 request for the TTCN funding in 2021.

The finalized TTCN Tasks List will be reviewed and endorsed at RAN5#89-e (Nov) for TSG RAN approval at RAN#90-e (Dec).

2021 Funding: 2021 workload is estimated at 104 mm (previous slide).

Funding will be requested to 3GPP PCG/OP.

Typically only part of necessary funding provided by PCG/OP

example: 68 mm in 2020

Funding shall also be obtained through voluntary contributions from 3GPP companies and/or MRPs.

RAN / RAN5 member companies and 3GPP MRPs are respectfully asked to consider providing funding support for the TTCN tasks in 2021.

Q. to RAN5: RAN5 is requested to endorse

The 2021 TTCN Tasks List presented in the previous slides,

The request from RAN5 to TSG RAN and 3GPP PCG/OP for funding of 68 man.months in 2021.

the usual funding of 58 man.months,

plus a special additional funding of 10 man.months:

to complete in 2021 TTCN development & verification of the Rel-15 5G test cases, and

to accelerate TTCN development & verification in 2021 of the Rel-16 5G test cases.

Note: Voluntary contributions of 36 man.months are expected for 2021.

Decision: 		The document was revised to R5-204350.

### 2.2	General Reports for information

R5-203208	RAN5 SR to RP#88-e

Type: report		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203209	TF160 SR to RP#88-e

Type: report		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203614	GCF 3GPP TCL after GCF CAG#63

Type: report		For: Information
					Source: Ericsson

Abstract:

At the GCF CAG#63 meeting, 7-10 July 2020, the GCF 3GPP Test Case List (TCL) was produced in [1]. The document includes the list of GCF selected 3GPP test cases and priorities as the outcome of GCF CAG#63.

The purpose of this document is to inform RAN5 about the changes introduced in GCF work items related to 3GPP test cases.

Summary of changes to GCF selected 3GPP test cases:

•	67 new Test Cases have been selected by GCF.

•	145 Test Cases have been removed by GCF.

•	13 Test Cases have changed GCF priority.

•	No change of GCF Work Item assignments for current selected Test Cases.

•	84 Test Cases have changed description in the GCF Test Case database.

Decision: 		The document was noted.

R5-203616	3GPP RAN5 CA status list  (pre-RAN5#88-e meeting)

Type: other		For: Information
					Source: Ericsson

Abstract:

"The purpose of this document is to provide an overview of all RAN4 CA configurations from Rel-10 and forward (including their fallbacks) and the associated status in RAN5 test specifications. This list does not replace the RAN5 work plan for the individual RAN5 CA work items.

The scope of this version is:

- RAN4 CA configurations from Rel-10 to Rel-16 including new and revised Rel-16 CA WIDs approved at RAN#85 plenary (Sep-19). The list is

pending additional Rel-16 CA configurations added up to RAN#88 (Jun-20).

- RAN5 completion status at the end of RAN#87-e (May-20).

CA configurations marked as ""Open for company assignment"" needs companies to contribute to enable progress in RAN5. Please contact leif.mattisson@ericsson.com if You want Your company to be assigned to one or more CA configurations.

Note!

- For RAN4 CA configurations introduced before Rel-13 it has been assumed that those have been completed by RAN5 Pre-Rel-13 work items. If it is identified that a pre Rel-13 CA configuration was not included as part of the earlier release CA work item then the CA configuration is added to one of the open RAN5 basket CA work items.

- For CA configurations introduced by any RAN4 ""non-basket"" work items, e.g. in work items introducing new bands that also includes associated CA

configurations, the list may not include those yet. The aim is to make the list complete including all RAN4 introduced CA configurations independent

on the type pf work item introducing it. If any missing RAN4 CA configurations or errors in the listed CA configurations are found then please report

this to leif.mattisson@ericsson.com.  "

Decision: 		The document was noted.

## 3		Incoming Liaison Statements

R5-203215	NGMN Liaison Statement to 3GPP RAN4 on 5G NR Over The Air test methodologies and performance requirements

Type: LS in		For: Information
					Original outgoing LS: 200603 Liaison Statement from NGMN to 3GPP RAN4 on 5G NR OTA_V1.1, to -, cc -
					Source: NGNM

Abstract:

NGMN Alliance Project “Devices and Chipsets for 5G”

1. About the NGMN Alliance

The NGMN Alliance is an industry organization of leading world-wide Telecom Operators, Vendors and Research Institutes (see www.ngmn.org) and was founded by international network operators in 2006. Its objective is to ensure that the functionality and performance of next generation mobile network infrastructure, service platforms and devices will meet the requirements of operators and, ultimately, will satisfy end user demand and expectations. The NGMN Alliance will drive and guide the development of all future mobile broadband technology enhancements with a focus on 5G. The targets of these activities are supported by the strong and well-established partnership of worldwide leading operators, vendors, universities, and successful co-operations with other industry organisations.

2. Intention of the LS and required actions

In 2019, NGMN started a brand new project devoted to 5G Devices.

Overall objective of NGMN 5G Devices project is to foster commercial 5G Devices ecosystem, by:

1.	providing a categorization (on a use case basis) and prioritization of standard defined technical requirements for 5G Devices

2.	assessing and pushing for maturity of 5G Devices ecosystem, evaluating current amount and variety of available 5G Devices, and their capabilities and characteristics

In relation to 1., please consider NGMN white paper on “5G Devices Categorization”, published in March 2020 and available at https://www.ngmn.org/highlight/5g-devices-categorization-2.html

Instead, in relation to 2., one of expected deliverable from NGMN is a survey white paper analyzing 5G NR Devices Over The Air test methodologies and performance requirements that are or will be defined and available from different Standard Organizations.

NGMN does believe that 3GPP RAN4 WG (together with RAN5 WG and RAN Plenary) is one of main players active in this field.

Consequently, NGMN is kindly requesting 3GPP RAN4 WG to provide information on:

-	status of study items and work items related to the definition of UE antenna performance test methodologies and related minimum performance requirements for 5G NR User Equipment for both Frequency Range 1 and 2 – and in both cases of 5G SA Option 2 and 5G NSA Option 3x

-	any potential distinction between different frequency bands belonging to same Frequency Range that 3GPP RAN4 WG is considering in addressing such UE 5G NR antenna performance test methodologies and minimum requirements

-	3GPP Technical Reports and Technical Specifications currently impacted by such study items and work items

-	potential roadmap and further future work plan on such topics

NGMN would like to thank you in advance 3GPP RAN4 WG for cooperation.

Decision: 		The document was noted.

R5-203216	Reply LS on support of eCall over NR

Type: LS in		For: Information
					Original outgoing LS: C1-203221, to -, cc -
					Source: TSG WG CT1

Abstract:

Response to:	LS SP-200287 on support of eCall over NR from SA

Release:	Rel-16

Work Item:	TEI16

CT1 thanks SA for their LS on support of eCall over NR.

CT1 would like to inform SA that CT1 has completed the work required to support eCall in IMS over NR (with 5G Core) as requested by SA, via the agreement of the attached CR.

2	Actions

To SA:	3GPP TSG CT WG1 asks SA to take the above information into account.

Decision: 		The document was noted.

R5-203217	Reply LS to GSMA TS.48 publication

Type: LS in		For: Information
					Original outgoing LS: C6-200331, to -, cc -
					Source: TSG WG CT6

Abstract:

Response to:	LS C6-200276 on announcing the publication of GSMA TS.48 Generic eUICC Test Profile for Device Testing version 2.0

Release:	Release 15, Release 16

Work Item:	(TEI15, TEI16)

CT6 thanks GSMA for their Liason Statement announcing the publication of GSMA TS.48 version 2.0.

CT6 noted that the attached document GSMA_TS48_eSIM_GTP_Profile_Structure v2.0.xlsx describes a file system containing both files, EF IMSI, (under ADFUSIM), and EF NSI, (under ADFUSIM/5FC0).

This configuration is not compliant with 3GPP TS 31.102 Release 15 v15.9.0, stating that EF NSI can’t be present in a 3GPP Release 15 file system, (see clause 4.4.11.11). And it is not compliant with a 3GPP Release 16 v16.0.0 onward as the presence of files EF IMSI and EF NSI is conditional, depending on the services enabled in the UST table (see service n°130 and its implications). Only one of them can be present in the USIM.

2. Actions: CT6 recommends TSG eSIMTP to take in account what explained above.

Decision: 		The document was noted.

R5-203221	Reply LS to Reply LS on support for eCall over NR

Type: LS in		For: Information
					Original outgoing LS: S5-203369, to -, cc -
					Source: TSG WG SA5

Abstract:

Response to:	LS (SP-200287/S5-203035) Reply LS on support for eCall over NR

Release:	Release 16

Work Item:	EIEI, 5GS_Ph1

SA5 thanks SA for the LS on support for eCall over NR.

SA5 can confirm that the IMS charging enhancements, introduced from Rel-15 to cover IMS on top of 5GCore, include IMS emergency sessions, with no restriction on the 3GPP radio access type (E-UTRA or NR).

Therefore, the support eCall in IMS over NR with 5G Core is already covered from charging's perspective from Rel-15.

2. Actions: To SA group: 	SA5 kindly asks SA to take into account the answer above.

Decision: 		The document was noted.

R5-203222	dummy LS1

Type: LS in		For: Information
					Original outgoing LS: -, to -, cc -
					Source: ETSI Secretariat

Decision: 		The document was withdrawn.

R5-203223	dummy LS2

Type: LS in		For: Information
					Original outgoing LS: -, to -, cc -
					Source: ETSI Secretariat

Decision: 		The document was withdrawn.

## 4	RAN5 General Issues

### 4.1	New Work Item proposals - for intro only

R5-203230	New WID on: UE Conformance Test Aspects - 410 – 430 MHz E-UTRA FDD Band(s) for LTE PPDR and PMR/PAMR in Europe (Bands 87 and 88)

Type: WID new		For: Endorsement
					Source: Nokia, Nokia Shanghai Bell

Abstract:

Justification

The core and performance work items for LTE bands 87 and 88 were completed at RAN#86 Dec-2019, as inclusion of LTE systems in the band 410 - 430 MHz in the 3GPP specifications.

The core and performance work items introduced Bands 87 and 88 to be supported NB1 and NB2 UE; and category M1 and M2 UE.

There is a need to introduce an associated RAN5 work item to enable UE conformance testing for UEs supporting for LTE Bands 87 and 88.

Objective

The objective of this work item is to provide UE conformance test cases for the RF, RRM and protocol aspects of the Rel-16 core and performance parts for LTE Bands 87 and 88 as well as its support for NB1 and NB2 UE; and category M1 and M2 UE.

Decision: 		The document was revised to R5-204351.

R5-203465	New WID on UE Conformance Test Aspects – B1C Signal in A-BDS Positioning System Support for LTE and NR

Type: WID new		For: Endorsement
					Source: CATT

Abstract:

Justification

In release 16, enhancements to support B1C signal in the network-assisted BDS System, as part of A-GNSS positioning methods in LTE and NR, have been introduced. CRs have been agreed in RAN#87-e (RP-200357 CR0083, CR0248, CR0013) and RAN#88-e (RP-201055 CR0020, CR0011) meeting. And it needs to be tested to verify that the functionality complies with specifications.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to provide conformance test specifications for B1C signal in BeiDou Navigation Satellite System in LTE and NR. This work item will cover signalling and performance in NR and E-UTRAN which are used by BeiDou Navigation Satellite System positioning, e.g. LPP signalling, RRC signalling, sensitivity, nominal accuracy, dynamic range, etc.

Decision: 		The document was revised to R5-204352.

R5-203703	New WID on UE Conformance Test Aspects for SON and MDT support for NR

Type: WID new		For: Endorsement
					Source: China Mobile Com. Corporation

Abstract:

Justification

Self-Organising Networks (SON) and Minimization of Drive Tests (MDT) were introduced in LTE to support deployment of the system and performance optimization. Many of the standardized SON/MDT features are implemented in LTE commercial networks and have provided means for a cost-efficient handing of the networks.

The core part of WI SON/MDT support for NR was introduced in Rel-16. It uses LTE solutions as baseline and takes the NR new architectures and features into account, e.g., EN-DC, beam, etc. In this WI, SON features Mobility Robustness Optimisation (MRO), RACH optimisation, L2 measurements and Minimization of Drive Tests (MDT) support for NR were introduced.

The Rel-16 WI NR_SON_MDT-Core has been completed at RAN#88 e-meeting. According to the requirements of NR network deployment and performance optimization, it is justified to now start the work on the corresponding UE conformance test specifications for NR MDT feature in 3GPP RAN WG5 to meet the market requirements in time.

(Note: SON aspects of NR_SON_MDT-Core are not subject of this Testing part WI and may be tested in a future WI.)

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance requirements corresponding to WID on MDT support for NR with Unique identifier 840191. This work item will cover Protocol conformance test specifications with NR MDT.

Discussion:

r1

Decision: 		The document was revised to R5-204353.

R5-203900	New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band)

Type: WID new		For: Endorsement
					Source: China Unicom

Abstract:

Justification

The HPUE (PC2) for EN-DC (1 LTE FDD band and 1 NR TDD band) have significant benefits for increasing UE transmission power and improving EN-DC network UL coverage. The 3GPP R16 Study item on High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) is already completed at Dec 2019, and the corresponding RAN4 WI ENDC_UE_PC2_FDD_TDD is 60% completion and targeted at August 2020.

It is proposed to introduce an associated RAN5 work item to enable UE conformance testing for High power (power class 2) EN-DC (1 LTE FDD band + 1 NR TDD band) UEs.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance test cases and associated test environment, test applicability, test point analysis on High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band).

The scope of this WI is all the Ran4 completed PC2 1 LTE FDD +1 NRTDD EN-DC configurations as following：DC_3A_n78A, DC_3A_n41A. More PC2 EN-DC configurations may be introduced in this Work Item after other basket WIs of ENDC_UE_PC2_FDD_TDD in RAN4 is completed.

NOTE: The DC_3A_n78A and DC_3A_n41A configurations are in the scope of RAN5 Rel-15 WI “5GS_NR_LTE-UEConTest”.

Discussion:

China Mobile asked to join.

Decision: 		The document was revised to R5-204354.

R5-203901	New WID on UE Conformance Test Aspects – Single Radio Voice Call Continuity from 5G to 3G

Type: WID new		For: Endorsement
					Source: China Unicom

Abstract:

Justification

The voice service continuity from 5G to UTRAN is currently missing in 3GPP R15 specifications， which will have impact on MNOs for providing voice service in 5G initial network deployment with limited NR coverage. Therefore, 3GPP SA initiated and completed study item and work item on single radio voice continuity from 5GS to 3G in R16, and the 3GPP R16 work item RAN aspects of 5G SRVCC is already 100% completion at July 2020.

It is proposed to introduce an associated RAN5 work item to enable UE conformance test for SRVCC from 5G to 3G.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to provide conformance tests for the protocol aspects of the SRVCC from 5G to 3G core requirement:

1.	Inter-RAT measurement test cases to support voice service continuity from 5GS to UTRAN

2.	Indirect Inter-RAT handover test cases to support voice service continuity from 5GS to UTRAN

3.	UE capability reporting for supporting SRVCC

The objective of this work item is to provide conformance tests for the performance aspects of the SRVCC from 5G to 3G core requirement:

1.	RRM test cases to support the SRVCC from 5G to 3G core requirement:

Discussion:

Qualcomm: have to consider also 3G framework.

FDD, or also TDD is considered? Only CDMA

Decision: 		The document was revised to R5-204355.

R5-203906	New WID on UE Conformance Test Aspects for NR performance enhancement

Type: WID new		For: Endorsement
					Source: Qualcomm Korea

Abstract:

NR_perf_enh-Perf-UEConTest

Justification

As part of the NR Rel-15 performance requirements, RAN4 only covered the single carrier Demodulation and CSI requirements. This Rel-16 WI was created to add the requirements for features that were originally specified in Rel-15 core part, but not covered in the Rel-15 performance part of the Rel-15 core part. Key features included in this WI are the CA and DC Demodulation and CSI requirements, LTE NR co-existence for TDD mode, CSI requirements for Tx port larger than 8 Tx.

The performance part of Rel-16 NR Perf enhancement is already 75% completed and targeted for Dec 2020 completion. RAN5 can start on the work item to deliver relevant conformance test cases for Rel-16 NR performance enhancement requirements.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance requirements corresponding to WID on NR performance enhancement, analyse the test case impact, applicability, test environment, and update the relevant conformance specifications for Rel-16.

Discussion:

r1

Decision: 		The document was revised to R5-204356.

R5-204231	New WID on UE Conformance Test Aspects - Mission Critical Enhancements

Type: WID new		For: Endorsement
					Source: NIST, Samsung

Abstract:

Justification

With the planned building out of LTE networks designed for first responders in various countries around the world, the demand and need for Mission Critical services on 5G networks is growing. 3GPP has answered this demand with enhancements to core specifications for Mission Critical Services (MCS). MCS includes Mission Critical Push To Talk (MCPTT), Mission Critical Video (MCVideo), and Mission Critical Data (MCData). RAN5 has completed, or will complete shortly, the UE conformance tests for MCS for Release 14. RAN5 needs to address developing test specifications that relate to Release 15 MCPTT, MCVideo and MCData requirements.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to provide conformance test specifications for the Rel-15 core requirements for MCPTT, MCVideo and MCData by updating the TS 36.579 family of specifications to Rel-15.

In general, in SA1, SA2, SA3, SA4 and SA6, functional architecture and information flows to support mission critical communication services are defined which will be reflected in this RAN5 work item.  In CT1, CT3, CT4 and CT6, MCPTT, MCVideo, and MCData protocol aspects are defined which, whenever relevant, will be reflected in this RAN5 work item. In CT1, IMS profiles to support MCPTT, MCVideo, and MCData are defined which will be reflected in this RAN5 work item.

The relevant core specifications for this work item are the same as in Release 14:

TS 24.379 – MCPTT Call Control

TS 24.380 – MCPTT Media Plane

TS 24.481 – MCS Group Management

TS 24.482 – MCS Identity Management

TS 24.483 – MCS Management Object (MO)

TS 24.484 – MCS Configuration Management

TS 24.281 – MCVideo signalling protocol

TS 24.581 – MCVideo media plane control

TS 24.282 – MCData signalling protocol

TS 24.582 – MCData media plane control

TR 24.980 - Minimum requirements for support of MCPTT over the Gm

TS 33.180 - Security of the mission critical service

This Work Item should keep the same numbering scheme for the MCS conformance specifications. The MCS conformance specifications are found in the TS 36.579 family of specifications. Although "36" refers to LTE, changing the numbers should not be an option because the industry is already is familiar with the 36.579 family of specifications and changing will bring too many complications. This Work Item should also provide a solution for 5G as a bearer/QoS flow technology similar to how this was done for LTE in Release 14 MCS conformance tests.

Discussion:

presented by Samsung.

More updates.

Decision: 		The document was revised to R5-204357.

R5-204292	New WID - UE Conformance Test Aspects for CLI handling for NR

Type: WID new		For: Endorsement
					Source: Qualcomm Incorporated

Abstract:

Justification

As captured in TR38.802 (as shown in below) in Section 5.1, NR aims to support duplexing flexibility in both paired and unpaired spectrum.

“NR supports paired and unpaired spectrum and strives to maximize commonality between the technical solutions, allowing FDD operation on a paired spectrum, different transmission directions in either part of a paired spectrum, TDD operation on an unpaired spectrum where the transmission direction of time resources is not dynamically changed, and TDD operation on an unpaired spectrum where the transmission direction of most time resources can be dynamically changing. DL and UL transmission directions at least for data can be dynamically assigned on a per-slot basis at least in a TDM manner. It is noted that transmission directions include all of downlink, uplink, sidelink, and backhaul link. NR supports at least semi-statically assigned DL/UL transmission direction as gNB operation, i.e., the assigned DL/UL transmission direction can be signaled to UE by higher layer signaling.”

CLI is Cross Link Interference where one Aggressor UE’s UL interferes with DL of second Victim UE, based on dynamic UL-DL allocation.

Rel-14 NR study showed that duplexing flexibility with cross-link interference mitigation shows better user throughput compared to static UL/DL operation or dynamic UL/DL operation without interference mitigation in indoor hotspot (4GHz and 30GHz) and urban macro scenarios (4GHz and 2GHz). The mitigation techniques include coordinated scheduling scheduling/beamforming, power control, link adaptation, hybrid dynamic/static UL/DL resource assignment.

During Rel-15 NR WI, enablers for basic support of cross-link interference mitigation schemes to support duplexing flexibility for paired and unpaired spectrum were discussed but could not specified as the work has been deprioritized. Mainly, it was agreed to introduce UE-to-UE measurement for CLI, and TRP-to-TRP measurement/coordination techniques were discussed. Rel-15 NR specification supports mechanisms to allow dynamic DL/UL assignments. Yet, any cross-link interference mitigation techniques and coexistence requirements have not been specified and thus the use of dynamic DL/UL assignment operation is considerably restricted.

As observed during study, dynamic DL/UL resource assignments would be more beneficial in indoor hotspot and urban macro scenarios where gNB TX power is rather limited, and ISD is small. During the study, dynamic DL/UL assignment operations offers performance gain in high frequencies such as 4 GHz and 30 GHz. In such frequencies, advanced MIMO techniques can be utilized to mitigate cross-link interference which has not been fully evaluated.

Furthermore, semi-static and/or dynamic DL/UL resource assignments should also consider coexistence issues particularly among different operators where tight coordination are challenged. Coexistence mechanisms among different operators in co-channel and adjacent channels are essential regardless whether each cell operates in semi-static or dynamic DL/UL assignment mechanism. For efficient coexistence, not only coexistence requirements need to be understood but also advanced mechanisms to mitigate interference such as TRP-to-TRP measurement and adaptation based on measurements should be considered.

In commercial TD-LTE network with macro deployment scenario, it is observed in relatively large scale of eNBs that IoT (amounts to above -105dBm, even to -90dBm in some extreme cases) in these eNBs intermittently deteriorated to severely impact the network coverage and connection successful rate. Jointed with several approaches, e.g., IoT statistics from the eNBs in some regions over the forecast of troposphere bending (http://www.dxinfocentre.com/tropo.html) , as well as the symptoms varying with the artificially constructed transmission patterns, it is identified that this kind of IoT degradation is caused by the downlink signal of remote eNB (furthest as 300km away with observed record) as long as the atmospheric conditions favourable for producing troposphere bending of radio waves are available. To mitigate the impact of this kind of remote base station interference as it intermittently happens, but not to scarify the network resources all the time, in the field TD-LTE network, some adaptive mechanisms are introduced, where abnormal IoT enhancement will trigger the victim eNB to transmit a specific signal in a window, each eNB that detected the specific signal in a window will identify itself as the contributor of the deteriorated IoT in some eNB(s), and then it will reconfigure the GP or some other parameters to reduce its weight to the interference. In this framework, the impact of troposphere bending is mitigated to some extension, however, some disadvantages are also apparent in the proprietary implementation, e.g., rely on some static mechanism for detection signal transmission and detection  due to lack inter-vendor inter-eNB coordination, decision making is per individual eNB based implementation, etc.

In NR deployment on lower TDD frequency, the impact of the troposphere bending will continue existing if no special mechanisms are introduced. Though the design of the frame structure in NR has already considered much more flexible GP to leave larger room for avoiding the remote interference, it is necessary to study mechanisms for identifying when or how long will the long enough GP be configured, as well as corresponding gNB’s behaviour and inter-gNB’s coordination procedure.

This WI shall not consider the RIM (Remote Interference Management) as RIM applies to BS and impacts RAN1 and RAN3. Hence this WI shall be restricted only to CLI (Cross Link Interference) which impacts RAN1, RAN2 and RAN4.

Objective of SI or Core part WI or Testing part WI

The objective of this work item is to define the UE conformance requirements corresponding to WID on CLI handling support for NR. This work item will cover RRM conformance test specifications aspects for CLI including the Applicability, Test Environment, Intial Conditions, Test Procedure, Messaeg Exceptions, Test Setup, Connection Diagram, etc..

Discussion:

r3

Decision: 		The document was revised to R5-204358.

### 4.2	General Discussion Papers

#### 4.2.1	5GS

R5-203795	Updated Check List for adding new NR bands and for new channel bandwidth to existing NR bands

Type: other		For: Endorsement
					Source: Ericsson

Decision: 		The document was noted.

R5-203798	Checklist - NR_Rel-16_CA_DC for RAN5#88-e

Type: other		For: Endorsement
					Source: CMCC, Bureau Veritas

Decision: 		The document was noted.

#### 4.2.2	All other topics

### 4.3	RAN5 PRDs/Templates

R5-203210	RAN5#88-e LS Template

Type: other		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-203532	RAN5 PRD12 version 6.4

Type: other		For: Approval
					Source: MCC TF160

Decision: 		The document was withdrawn.

### 4.4	Meeting schedule for 2020-21

R5-203211	Meeting schedule for 2020-21

Type: other		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

### 4.5	Tdocs for mid-week joint session

#### 4.5.1	RF group docs for WG review/verdict - original A.I. retained

#### 4.5.2	Sig group docs for WG review/verdict - original A.I. retained

#### 4.5.3	Other open issues from joint sessions - original A.I. retained

R5-203613	Discussion paper on tracking of 5GS protocol test cases Rel-16 and beyond

Type: discussion		For: Endorsement
					Source: Ericsson

Abstract:

For LTE the TS rapporteur of TS 36.523-1 have provided a test case tracking document pre and post every RAN5 meeting. The purpose of the tracking is to provide an overview of test case status and avoid duplication of test cases numbers when new LTE work items and TEI test cases are introduced.

The purpose of this paper is to propose to introduce a TS 38.523-1 tracker document and the process and responsibilities for maintaining it.

Discussion:

post-meeting activities

The RAN5 Chair thanked Clause Arzelier (ex Blackberry) for his contributions throughout the years and his long term commitment to maintaining the RAN5 lists.

The successor is Mr. Stoyan Baev (Samsung).

r3

Decision: 		The document was revised to R5-204366.

R5-204366	Discussion paper on tracking of 5GS protocol test cases Rel-16 and beyond

Type: discussion		For: Endorsement
					Source: Ericsson

(Replaces R5-203613)

Discussion:

Noted and proposals accepted.

Decision: 		The document was noted.

R5-204219	Proposals for new GNSS scenarios for TS 37.571-X

Type: discussion		For: Information
					Source: Spirent Communications

Abstract:

5.5.16, Also AI 6.6.7.5

Following the discussion of issues with the current GNSS scenarios used for testing BeiDou (BDS), described in R5-202023, and following RAN 5 endorsement of a basic way-forward, some companies have held off-line discussions to agree a more detailed way-forward. The proposals are detailed below for information. Any other company wishing to comment or take part in further off-line discussions is invited to contact the author.

Detail:

1. It is clear that if the BDS scenarios are to be updated, then all the other GNSS scenarios also should be updated at the same time to bring them up to a similar level of realism. Note that this will also automatically add the new BDS B1C signal.

2. In order to provide the most realistic simulations possible, we will use “live orbital data” from a web site or websites that lists the actual orbital data used at some (recent) point in time. The websites to be used is currently under discussion off-line.

3. In order to simplify our work we will only use one scenario/set of orbital data per GNSS.

4. In TS 37.571-5 we will record the orbital data in a format(s) to be agreed (TLE or Yuma or Rinex). This may require more than one format as Yuma is only almanac, Rinex is ephemeris and it is agreed that both will be specified (see below).

5. We will ensure the RAN 4 / RAN 5 requirements for the number of satellites per GNSS is achieved. Currently this does not seem possible for BDS but this is still under investigation.

6. To avoid too many changes, we will use/specify the same locations as used currently (note therefore we will not take into account the requirements of NavIC).

7. In order to avoid any issues with UEs when using the current, very old, dates and times, we will specify much more recent (fixed) date(s) and time(s). The date(s) will be at least this year (2020), after the latest GPS roll-over.

8. In order to reduce the amount of unnecessary work in making the changes above, we will no longer specify in TS 37.571-5 all the assistance data as is done today. Much of this is highly repetitive and prone to errors etc. As well as time(s) and locations we will just specify the almanac (as Yuma?) and the ephemeris (as Rinex?). The atmospheric conditions will be specified in the Rinex files. The specification of the Acquisition assistance is under discussion and it is possible we will just specify search windows etc. It will be for Test Vendors to create and correctly format the appropriate Assistance Data.

9. We will propose a “grace period” until the end of 2021 for the final cut-over to the new data discussed above to avoid too much re-validation etc.

10 It is currently proposed to start introducing the new data etc. into the specifications at the November RAN 5 meeting.

Decision: 		The document was noted.

#### 4.5.4	UE Application Layer Data Throughput Performance  TEI11_Test / TEI15_Test (TR 37.901)

#### 4.5.5	GCF Test Optimisation

#### 4.5.6	5GS

#### 4.5.7	Other

## 5	RF Functional Area

### 5.1	Review action points (fm A.I. 2.1)

### 5.2	Review incoming LS (fm A.I. 3) & new subject discussion papers

R5-203218	CAG-20-331_LS on replacement of 3CC to 5CC RRM TCs in GCF scheme

Type: LS in		For: Information
					Original outgoing LS: CAG-20-331_LS on replacement of 3CC to 5CC RRM TCs in GCF scheme, to -, cc -
					Source: GCF CAG

Abstract:

GCF thanks RAN5 for their liaison statement in R5-184116 (submitted to CAG as CAG-18-335). The LS indicated that a number of new TCs had been introduced in TS 36.521-3 to replace some existing TCs. It was understood that some of the TCs were already validated so there would be a period of time where both old and new TCs would exist in the GCF DCC database, to avoid disruption to the certification scheme.

The change-over has been completed and the tables below shows the details for each TC: [..]

Discussion:

moved to RF.

presented by R&S.

Bureau Veritas will check with PTCRB.

Decision: 		The document was noted.

R5-203220	LS response on Multiband relaxation for FR2

Type: LS in		For: Information
					Original outgoing LS: R4-2006351, to -, cc -
					Source: TSG WG RAN4

Abstract:

Response to:	LS on Multiband relaxation for FR2 from WG5

Release:	Rel-15

Work Item:	NR_newRAT-Core

RAN4 thanks RAN5 for the LS on multiband relaxation (MBR) for FR2 [R5-199424].  Based on the testability analysis of MBR, as provided by RAN5, RAN4 has agreed the following:

-	In the scope of Rel-15:

o	RAN4 shall introduce a maximum cap to the per-band relaxation factors, such that ∆MBP,n ≤ 0.75 dB and ∆MBS,n ≤ 0.75 dB

o	This MBR framework is applicable to the bands defined in Rel-15 (i.e. n257, n258, n260, n261) and is defined only in the Rel-15 version of TS38.101-2

o	The corresponding CR to the Rel-15 TS38.101-1 is attached in [1]

-	In the scope of Rel-16 and beyond:

o	RAN4 shall define fixed per-band relaxation factors, ∆MBP,n and ∆MBS,n, directly in the specification

o	This MBR framework applies to a Rel-16+ UE supporting any FR2 band(s)

o	This MBR framework also applies to a Rel-15 UE if it supports any FR2 band which is introduced in Rel-16+ (e.g. band n259)

o	The corresponding CR to the Rel-16 TS38.101-2 is attached in [2]

o	The corresponding CR to the Rel-16 TS38.307 is attached in [3]

RAN4 kindly asks RAN5 to take the above information into account.

Discussion:

moved to RF.

Presented by Apple.

Decision: 		The document was noted.

### 5.3	Open Work Items

#### 5.3.1	Rel-14 LTE CA configurations (UID - 720098) LTE_CA_R14-UEConTest

##### 5.3.1.1	TS 36.508

R5-203989	Adding signalling test frequency for 3A-41A

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1327  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

reissued as R5-204348 because of title change

Decision: 		The document was withdrawn.

R5-204348	Adding signalling test frequency for 1A-38A

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1332  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

reissued from R5-203989 because of title change

Decision: 		The document was agreed.

##### 5.3.1.2	TS 36.521-1

R5-203986	Updating test casees for several CA configurations

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5176  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

TP in R5-20xxxx and R5-20xxxx

Discussion:

r1

Decision: 		The document was revised to R5-204750.

R5-204750	Updating test casees for several CA configurations

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5176  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203986)

Decision: 		The document was agreed.

##### 5.3.1.3	TS 36.521-2

##### 5.3.1.4	TS 36.521-3

##### 5.3.1.5	TS 37.571-1

##### 5.3.1.6	TS 37.571-3

##### 5.3.1.7	TS 37.571-5

##### 5.3.1.8	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.1.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.1.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

R5-203987	Updating test point analysis for AMPR of NS_01 and NS_04

Type: CR		For: Agreement
					36.905 v16.4.0	  CR-0237  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

TC in R5-203986

Decision: 		The document was agreed.

R5-203988	Updating test point analysis for 3A-41A to add SE-coex

Type: CR		For: Agreement
					36.905 v16.4.0	  CR-0238  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

TC in R5-203986

Decision: 		The document was agreed.

##### 5.3.1.11	Discussion Papers, Work Plan, TC lists

#### 5.3.2	5G system with NR and LTE (UID - 760087) 5GS_NR_LTE-UEConTest

##### 5.3.2.1	TS 38.508-1

R5-203287	Correction PRB-Id for PUCCH secondHopPRB

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1368  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203631	Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1428  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

r1

Decision: 		The document was revised to R5-204751.

R5-204751	Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1428  rev 1 Cat: F (Rel-16)

					Source: Ericsson, Telefonica

(Replaces R5-203631)

Decision: 		The document was agreed.

R5-203671	Update of PDSCH-to-HARQ_feedback timing indicator (k1) value

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1433  Cat: F (Rel-16)

					Source: Qualcomm Korea

Decision: 		The document was agreed.

R5-203672	Jumbo CR for update to Demod message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1434  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r1

Decision: 		The document was revised to R5-204852.

R5-204852	Jumbo CR for update to Demod message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1434  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea, Anritsu

(Replaces R5-203672)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205007.

R5-205007	Jumbo CR for update to Demod message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1434  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea, Anritsu

(Replaces R5-204852)

Decision: 		The document was agreed.

R5-203680	Updating indicator for SUL FR1 test cases

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1435  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

associated CR in R5-203679

Discussion:

r1

Decision: 		The document was revised to R5-204708.

R5-204708	Updating indicator for SUL FR1 test cases

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1435  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203680)

Decision: 		The document was agreed.

R5-203681	Editorial correction typos in annex C.2.3.2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1436  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

Editorial

Decision: 		The document was agreed.

R5-203683	Update frequencyDomainResources and nrofcandidates

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1437  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

discussion paper in R5-203686

Discussion:

r1

Decision: 		The document was revised to R5-204709.

R5-204709	Update frequencyDomainResources and nrofcandidates

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1437  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203683)

Decision: 		The document was agreed.

R5-203730	Scheduling Request Resource config for RRM test cases

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1444  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

"R&S: Table numbers of new tables, either R5-203864 or R5-203730 will be updated to use a new number. Still discussing with HW

Huawei revised 3864 to remove overlap"

Decision: 		The document was agreed.

R5-203731	OSI scheduling config for RRM test cases

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1445  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

"R&S: Table numbers of new tables, either R5-203864 or R5-203731 will be updated to use a new number. Still discussing with HW

Huawei revised 3864 to remove overlap"

Decision: 		The document was agreed.

R5-203764	Adding default value for IE rbg-Size for demodulation and CSI reporting tests

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1448  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204899.

R5-204899	Adding default value for IE rbg-Size for demodulation and CSI reporting tests

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1448  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203764)

Decision: 		The document was agreed.

R5-203815	FR2 PUSCH K2 values alignment to TS 38.214

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1458  Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

Abstract:

Changed K2 value entries for FR2 to align with TS38.214

Decision: 		The document was agreed.

R5-203863	Correction to Table 7.3.1-3 SSB-MTC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1459  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

overlap with R5-204223 (R&S)

Decision: 		The document was withdrawn.

R5-203864	Correction to TCI-state related configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1460  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204752.

R5-204752	Correction to TCI-state related configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1460  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203864)

Decision: 		The document was agreed.

R5-203865	Correction to CSI-RS related configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1461  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204753.

R5-204753	Correction to CSI-RS related configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1461  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203865)

Decision: 		The document was agreed.

R5-203888	Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1462  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r3

Decision: 		The document was revised to R5-204900.

R5-204900	Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1462  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203888)

Decision: 		The document was agreed.

R5-203908	Corrections on test frequencies for NR FR2 CA band n261

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1463  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Corrections on test frequencies for NR FR2 CA band n261

Decision: 		The document was agreed.

R5-203920	Update on test frequencies for EN-DC configurations including FR2

Type: CR		For: Agreement
					38.508-1 v15.4.0	  CR-1464  Cat: F (Rel-15)

					Source: ZTE Corporation

Abstract:

Update on test frequencies for EN-DC configurations including FR2

Discussion:

-

Decision: 		The document was withdrawn.

R5-203937	Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1465  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Title change!! Adding the test frequency for DC_3A-7A_n78A

Decision: 		The document was revised to R5-204700.

R5-204700	Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1465  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203937)

Discussion:

reissued as R5-204704 because of title change.

Decision: 		The document was withdrawn.

R5-204704	Adding the test frequency for DC_3A-7A_n78A

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1503  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

reissued from R5-204700 because of title change.

Decision: 		The document was agreed.

R5-203999	Update on test frequencies for EN-DC configurations including FR2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1468  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update on test frequencies for EN-DC configurations including FR2

Discussion:

r1

Decision: 		The document was revised to R5-204754.

R5-204754	Update on test frequencies for EN-DC configurations including FR2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1468  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203999)

Decision: 		The document was agreed.

R5-204049	Correction to the procedure for determination of SSB and CORESET0

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1475  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204050	Correction to message configuration for performance tests

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1476  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r2

Decision: 		The document was revised to R5-204901.

R5-204901	Correction to message configuration for performance tests

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1476  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204050)

Decision: 		The document was agreed.

R5-204051	Correction to PRB-Id

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1477  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

solved with R5-203287 (KS).

Decision: 		The document was withdrawn.

R5-204052	PUCCH Resource ID for CSI TCs

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1478  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204053	Correction to PDCCH-ConfigCommon for performance tests

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1479  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204164	Corrections of test frequency tables for CA_n258x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1485  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204755.

R5-204755	Corrections of test frequency tables for CA_n258x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1485  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204164)

Decision: 		The document was agreed.

R5-204165	Corrections of test frequency tables for CA_n260x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1486  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204756.

R5-204756	Corrections of test frequency tables for CA_n260x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1486  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204165)

Decision: 		The document was agreed.

R5-204166	Corrections of test frequency tables for CA_n261x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1487  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204757.

R5-204757	Corrections of test frequency tables for CA_n261x

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1487  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204166)

Decision: 		The document was agreed.

R5-204167	Corrections of test frequency tables for CA_n260(A-I)

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1488  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204168	Update Table 7.3.1-4: ServingCellConfigCommon

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1489  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204223	Update missing SMTC configurations in RRM message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1491  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204235	Add SSB subcarrier spacing configurations in RRM message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1492  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

offline feedback from Anritsu to correct the derivation path of the new RRM table to the corresponding section 4 table instead of to 38.331 spec.

Decision: 		The document was revised to R5-204758.

R5-204758	Add SSB subcarrier spacing configurations in RRM message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1492  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204235)

Decision: 		The document was agreed.

##### 5.3.2.2	TS 38.508-2

R5-203288	Added UE Phy layer capabilitity into 38.508-2 from 38.306

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0086  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r2

TF160 comments - As per TS 38.306 UE capability field can have a different value between FR1 and FR2 so 2 PICS with suffixes FR1 and FR2 needed.

Action point raised on TS 38.508-2 rapporteur to review all existing PICS definition to be compliant with TS 38.306 definition - UE capability field can have a different value for FDD and TDD if 'FDD-TDD DIFF' is set as 'Yes' and for FR1 and FR2 if  'FR1-FR2 DIFF' is set as 'Yes'.

r3

Decision: 		The document was revised to R5-204853.

R5-204853	Added UE Phy layer capabilitity into 38.508-2 from 38.306

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0086  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203288)

Decision: 		The document was agreed.

R5-203289	Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0087  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r3

Decision: 		The document was revised to R5-204902.

R5-204902	Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0087  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203289)

Decision: 		The document was agreed.

R5-203632	Introduction of UE capabilities for additional Rel-15 band EN-DC inter-band configurations

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0090  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203887	Introduction and correction of general capabilities and some band-combo information for EN-DC

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0092  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r2

Decision: 		The document was revised to R5-204903.

R5-204903	Introduction and correction of general capabilities and some band-combo information for EN-DC

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0092  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203887)

Decision: 		The document was agreed.

R5-203974	Addition of PICS for intra-band EN-DC PC2

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0102  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204759.

R5-204759	Addition of PICS for intra-band EN-DC PC2

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0102  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203974)

Decision: 		The document was agreed.

R5-204187	CR to 38.508-2 to allow vendor declarations related to beam peak searches

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0105  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Abstract:

Allow vendors to declare when beam peak search results can be re-used.

Discussion:

r1

implements Proposals 2 and 3 from R5-204186 (no comments received)

Decision: 		The document was revised to R5-204710.

R5-204710	CR to 38.508-2 to allow vendor declarations related to beam peak searches

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0105  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204187)

Decision: 		The document was agreed.

R5-204301	Add new PICS

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0107  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Discussion:

had wrong CADC AI.

r1

Decision: 		The document was revised to R5-204904.

R5-204904	Add new PICS

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0107  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204301)

Decision: 		The document was agreed.

##### 5.3.2.3	TS 38.509

##### 5.3.2.4	TS 38.521-1

###### 5.3.2.4.1	Tx Requirements (Clause 6)

R5-203256	Template

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0915  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

late doc

not available. Title not descriptive

Decision: 		The document was withdrawn.

R5-203291	Correction of K1 to achieve PUCCH Format 3 in FDD in EVM and in-band emission

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0927  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203572	Corrected test config for NS_24 in additional spurious emission test 6.5.3.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0932  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203674	Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0933  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TP in R5-203675,R5-203676

Discussion:

r1

Decision: 		The document was revised to R5-204711.

R5-204711	Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0933  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203674)

Decision: 		The document was agreed.

R5-203677	Cleaning up of Tx inter-band CA test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0934  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

MU and TT are introduced in R5-203678

Discussion:

r1

Decision: 		The document was revised to R5-204760.

R5-204760	Cleaning up of Tx inter-band CA test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0934  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203677)

Decision: 		The document was agreed.

R5-203679	Updating message content in SUL test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0936  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

associated CR in R5-203680

Decision: 		The document was agreed.

R5-203682	Updating test case 6.5A.2.4.1-NR ACLR for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0937  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203748	Change of RB allocation start for test case 6.3.4.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0958  Cat: F (Rel-16)

					Source: Ericsson, Keysight

Decision: 		The document was agreed.

R5-203754	Correct UE output power configuration to some UL MIMO cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0959  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom, Orange

Discussion:

r3

Decision: 		The document was revised to R5-204854.

R5-204854	Correct UE output power configuration to some UL MIMO cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0959  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom, Orange

(Replaces R5-203754)

Decision: 		The document was agreed.

R5-203880	Correction of UE mean power requirements Table numbers in SEM and ACLR test cases for SA FR1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0973  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203881	Adding NOTEs to the test requirement tables in 6.2D.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0974  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203882	Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0975  Cat: F (Rel-16)

					Source: CAICT

Abstract:

No.1 and No.2 of summary of change is baed on Proposal 8 in discussion paper R5-203868.

Discussion:

r2

Decision: 		The document was revised to R5-204905.

R5-204905	Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0975  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203882)

Decision: 		The document was agreed.

R5-203883	Correction of test requirement for 6.2.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0976  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r2

Decision: 		The document was revised to R5-204906.

R5-204906	Correction of test requirement for 6.2.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0976  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203883)

Decision: 		The document was agreed.

R5-203884	Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0977  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r2

Decision: 		The document was revised to R5-204907.

R5-204907	Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0977  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203884)

Decision: 		The document was agreed.

R5-203885	Correction of test requirement for 6.2.1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0978  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203886	Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0979  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r3

Decision: 		The document was revised to R5-204908.

R5-204908	Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0979  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203886)

Decision: 		The document was agreed.

R5-203909	Update of 6.2.3 for minimum conformance requirements for A-MPR

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0980  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of 6.2.3 for minimum conformance requirements for A-MPR

Discussion:

r1

Decision: 		The document was revised to R5-204909.

R5-204909	Update of 6.2.3 for minimum conformance requirements for A-MPR

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0980  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203909)

Decision: 		The document was agreed.

R5-203964	Update of test cases for UEs supporting Tx Diversity

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0982  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Depending on R4-2010808

Decision: 		The document was withdrawn.

R5-203967	Editorial correction of 6.2.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0983  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-204010	Correction to target power level Pmin for SA UL MIMO TCs

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0986  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-204054	Correction to test Configuration of flatness for Pi/2 BPSK

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0990  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204195	Update 6.5.3.2 Spurious emission for UE co-existence

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0996  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Decision: 		The document was agreed.

R5-204258	Editorial correction to FR1 co-existence requirements

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-1000  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204761.

R5-204761	Editorial correction to FR1 co-existence requirements

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-1000  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204258)

Decision: 		The document was agreed.

###### 5.3.2.4.2	Rx Requirements (Clause 7)

R5-203290	Clarification of Interferer frequency selection in FR1 IBB test case 7.6.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0926  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203876	Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0969  Cat: F (Rel-16)

					Source: CAICT

Abstract:

RAN4 dependency: R4-2009617 and R4-2009616.

Discussion:

r1

Decision: 		The document was revised to R5-204855.

R5-204855	Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0969  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203876)

Decision: 		The document was agreed.

R5-203877	Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0970  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r1

Decision: 		The document was revised to R5-204910.

R5-204910	Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0970  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203877)

Decision: 		The document was agreed.

R5-203878	Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0971  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r1

Decision: 		The document was revised to R5-204911.

R5-204911	Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0971  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203878)

Decision: 		The document was agreed.

R5-203879	Correction of diversity characteristics requirement in section 7.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0972  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203962	Update of SA Rx test cases for 4Rx UEs

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0981  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r2

Decision: 		The document was revised to R5-204912.

R5-204912	Update of SA Rx test cases for 4Rx UEs

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0981  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203962)

Decision: 		The document was agreed.

R5-204202	Update for 7.3A.0 Minimum conformance requirements for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0997  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Decision: 		The document was agreed.

R5-204204	Update Uplink power control window size for SA RX TCs

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0998  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204913.

R5-204913	Update Uplink power control window size for SA RX TCs

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0998  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204204)

Decision: 		The document was agreed.

###### 5.3.2.4.3	Clauses 1-5, Annexes

R5-203283	Update of clause5 into TS 38.521-1 R15

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0923  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

r1

Decision: 		The document was revised to R5-204762.

R5-204762	Update of clause5 into TS 38.521-1 R15

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0923  rev 1 Cat: F (Rel-16)

					Source: China Unicom

(Replaces R5-203283)

Decision: 		The document was agreed.

R5-203678	Adding MU and TTs for Inter-band UL CA test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0935  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

associated CR in R5-203677

Decision: 		The document was agreed.

R5-203684	Adding FR1 PDCCH Aggregation Level in Annex C.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0938  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

discussion paper in R5-203686

Discussion:

r1

Decision: 		The document was revised to R5-204712.

R5-204712	Adding FR1 PDCCH Aggregation Level in Annex C.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0938  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203684)

Discussion:

after the meeting agreed  with Keysight Spain that set AL=4 will impact some TCs since there maybe collision for the PDCCH of SIB1 and PDCCH of UL_grant, for example, in TPC Test, the PDCCH of DCI_0-1 with TPC command may can’t be scheduled in some slots due to collision with PDCCH of SIB1.

Probably withdrawn.

Decision: 		The document was withdrawn.

R5-204103	Correction of QPSK UL RMC

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0991  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Decision: 		The document was agreed.

R5-204263	Update of CSI-RS definition for DL RMCs in TS 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-1001  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

##### 5.3.2.5	TS 38.521-2

R5-204056	CR to update MU and TT in 38.521-2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0403  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r3

Decision: 		The document was revised to R5-204856.

R5-204856	CR to update MU and TT in 38.521-2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0403  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204056)

Decision: 		The document was agreed.

###### 5.3.2.5.1	Tx Requirements (Clause 6)

R5-203293	FR2 ACLR MBW correction according to RAN4

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0374  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

overlaps with Ericsson & Wuawei.

Decision: 		The document was withdrawn.

R5-203516	Update of test procedure for Minimum output power for CA in FR2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0377  Cat: F (Rel-16)

					Source: TTA

Decision: 		The document was withdrawn.

R5-203517	Update of test procedure for Error vector magnitude for CA in FR2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0378  Cat: F (Rel-16)

					Source: TTA

Decision: 		The document was withdrawn.

R5-203581	Beam correspondence - SRS configuration corrections in section 6.6.1

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0380  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

R4-2011414 has been formally agreed in RAN4.

r1

Decision: 		The document was revised to R5-204857.

R5-204857	Beam correspondence - SRS configuration corrections in section 6.6.1

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0380  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203581)

Decision: 		The document was agreed.

R5-203718	Correction to test configuration for Carrier leakage for CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0382  Cat: F (Rel-16)

					Source: LG Electronics

Discussion:

r2

Decision: 		The document was revised to R5-204713.

R5-204713	Correction to test configuration for Carrier leakage for CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0382  rev 1 Cat: F (Rel-16)

					Source: LG Electronics

(Replaces R5-203718)

Decision: 		The document was agreed.

R5-203720	Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0383  Cat: F (Rel-16)

					Source: LG Electronics

Discussion:

r2

Decision: 		The document was revised to R5-204714.

R5-204714	Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0383  rev 1 Cat: F (Rel-16)

					Source: LG Electronics

(Replaces R5-203720)

Decision: 		The document was agreed.

R5-203722	Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0384  Cat: F (Rel-16)

					Source: LG Electronics

Discussion:

r2

Decision: 		The document was revised to R5-204715.

R5-204715	Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0384  rev 1 Cat: F (Rel-16)

					Source: LG Electronics

(Replaces R5-203722)

Decision: 		The document was agreed.

R5-203724	Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0385  Cat: F (Rel-16)

					Source: LG Electronics

Discussion:

r2

Decision: 		The document was revised to R5-204716.

R5-204716	Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0385  rev 1 Cat: F (Rel-16)

					Source: LG Electronics

(Replaces R5-203724)

Decision: 		The document was agreed.

R5-203727	Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0386  Cat: F (Rel-16)

					Source: LG Electronics

Discussion:

r2

Decision: 		The document was revised to R5-204717.

R5-204717	Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0386  rev 1 Cat: F (Rel-16)

					Source: LG Electronics

(Replaces R5-203727)

Decision: 		The document was agreed.

R5-203765	Core spec alignment for measurement BW in 6.5.2.3, ACLR

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0387  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

overlap with R5-203293.

Decision: 		The document was withdrawn.

R5-203766	Updates to test case 6.3.4.3, relative power tolerance

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0388  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

offline comment from R&S.

Decision: 		The document was revised to R5-204914.

R5-204914	Updates to test case 6.3.4.3, relative power tolerance

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0388  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203766)

Decision: 		The document was agreed.

R5-203874	Correction of test procedure of ACLR and SEM for SA FR2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0391  Cat: F (Rel-16)

					Source: CAICT

Discussion:

-

Decision: 		The document was withdrawn.

R5-203968	Miscellaneous corrections due to core spec alignment

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0393  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204763.

R5-204763	Miscellaneous corrections due to core spec alignment

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0393  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson

(Replaces R5-203968)

Decision: 		The document was agreed.

R5-203969	Updating beam correspondance capability

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0394  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-204025	CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0397  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

r1

Update based on comments from Huawei, Ericsson, and R&S about the MU values and removed procedure step information as it is covered in R5-204185r1.

Decision: 		The document was revised to R5-204858.

R5-204858	CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0397  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204025)

Decision: 		The document was agreed.

R5-204030	CR to 38.521-2 to update Transmit OFF Power

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0398  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

r1

Received comments from Keysight  and we decided to add NOTE 2 in Table in test requirements to clarify the testable Band and power class.

Decision: 		The document was revised to R5-204915.

R5-204915	CR to 38.521-2 to update Transmit OFF Power

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0398  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204030)

Decision: 		The document was agreed.

R5-204031	CR to TS 38.521-2: Correction to time mask requirements

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0399  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

r1

updated to align with relaxation agreements in R5-204277r1.

r2

Decision: 		The document was revised to R5-204916.

R5-204916	CR to TS 38.521-2: Correction to time mask requirements

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0399  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204031)

Decision: 		The document was agreed.

R5-204044	CR to TS 38.521-2: Correction to MB relaxation minimum requirements

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0401  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

R&S: you are introducing Band n259 to the MOP test case. However, no MTSU has been specified for this band yet. Only MU estimates for deriving TT have been provided by TEVs. Therefore, this test case cannot be validated for band n259.

The aspect of missing MU for band n259 has to be reflected in the editor’s note.

In addition, maybe I have missed it, but there seems not to be any CR updating the general sections of the spec (Clause 5 etc.) with band n259 which also makes it hard to call this test case complete for n259.

r2

Decision: 		The document was revised to R5-204859.

R5-204859	CR to TS 38.521-2: Correction to MB relaxation minimum requirements

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0401  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204044)

Decision: 		The document was agreed.

R5-204055	Clean up complete status for FR2 SA test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0402  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r3

Decision: 		The document was revised to R5-204917.

R5-204917	Clean up complete status for FR2 SA test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0402  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204055)

Decision: 		The document was agreed.

R5-204057	Update to UE maximum output power for CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0404  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204918.

R5-204918	Update to UE maximum output power for CA

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0404  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204057)

Decision: 		The document was agreed.

R5-204185	CR to 38.521-2 to adjust the test step sequences

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0406  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Abstract:

To harmonize on the sequence of test steps, the order of test steps was adjusted for TX power test cases

from: Scheduling -> TPC commands -> Beam Forming to TX Beam Peak Direction & dwell time -> UBF

to Scheduling -> Beam Forming to TX Beam Peak Directi

Discussion:

r2

Decision: 		The document was revised to R5-204860.

R5-204860	CR to 38.521-2 to adjust the test step sequences

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0406  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204185)

Decision: 		The document was agreed.

R5-204188	CR to 38.521-2 to allow vendor declarations related to beam peak searches

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0407  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Abstract:

Allow vendors to declare when beam peak search results can be re-used.

Discussion:

r1

implements Proposals 2 and 3 from R5-204186 (no comments received)

Decision: 		The document was revised to R5-204861.

R5-204861	CR to 38.521-2 to allow vendor declarations related to beam peak searches

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0407  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204188)

Decision: 		The document was agreed.

R5-204193	CR to 38.521-2 on QoQZ Verification Clarification

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0408  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Abstract:

Clarify in the QoQZ validation procedures that the positioner coordinates/ orientations with respect to the reference probe/reflector shall remain the same for each reference antenna orientation.

Discussion:

Additional clarifications added based on feedback received by R&S.

r1

Decision: 		The document was revised to R5-204862.

R5-204862	CR to 38.521-2 on QoQZ Verification Clarification

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0408  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204193)

Decision: 		The document was agreed.

R5-204247	FR2 Minimum output power measurement period definition

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0410  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

R4-2011693 (revision of R4-2011387) and mirror R4-2011402 are now officially agreed.

Decision: 		The document was revised to R5-204919.

R5-204919	FR2 Minimum output power measurement period definition

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0410  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204247)

Decision: 		The document was agreed.

R5-204255	FR2 Minimum output power MU updates

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0411  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204863.

R5-204863	FR2 Minimum output power MU updates

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0411  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204255)

Decision: 		The document was agreed.

R5-204264	Editorial correction of ACLR CA test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0412  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204266	Update of FR2 OBW test case

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0414  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204267	Update of Tx signal quality test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0415  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204764.

R5-204764	Update of Tx signal quality test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0415  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204267)

Decision: 		The document was agreed.

R5-204278	FR2 EIRP OFF power MU updates

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0417  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

r3

Decision: 		The document was revised to R5-204864.

R5-204864	FR2 EIRP OFF power MU updates

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0417  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204278)

Decision: 		The document was agreed.

###### 5.3.2.5.2	Rx Requirements (Clause 7)

R5-203292	Clarification of Interferer frequency selection in FR2 IBB test case 7.6.2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0373  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203487	Adjacent Channel Selectivity FR2 MU updates in 38.521-2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0375  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

Decision: 		The document was withdrawn.

R5-203491	In-band Blocking FR2 MU updates in 38.521-2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0376  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

Decision: 		The document was withdrawn.

R5-203816	FR2 RefSens and EIS spherical PC3 MBR table update

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0389  Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

Abstract:

Align FR2 RefSens and EIS spherical MBR table to recent R4 updates

Discussion:

r3

Decision: 		The document was revised to R5-204920.

R5-204920	FR2 RefSens and EIS spherical PC3 MBR table update

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0389  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

(Replaces R5-203816)

Decision: 		The document was agreed.

R5-203873	Correction of UL power level requirement in 7.4

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0390  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was withdrawn.

R5-203970	Addition of UL power setting for Rx test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0395  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Discussion:

r1

Decision: 		The document was revised to R5-204765.

R5-204765	Addition of UL power setting for Rx test cases

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0395  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

(Replaces R5-203970)

Decision: 		The document was agreed.

###### 5.3.2.5.3	Clauses 1-5, Annexes

R5-203580	Beam correspondence - SRS configuration corrections in annex K.1.1

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0379  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

R4-2011414 has been formally agreed in RAN4.

Decision: 		The document was revised to R5-204865.

R5-204865	Beam correspondence - SRS configuration corrections in annex K.1.1

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0379  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203580)

Decision: 		The document was agreed.

R5-203685	Adding FR2 PDCCH Aggregation Level in Annex C.3

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0381  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

discussion paper in R5-203686

Discussion:

r2

Decision: 		The document was revised to R5-204718.

R5-204718	Adding FR2 PDCCH Aggregation Level in Annex C.3

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0381  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203685)

Discussion:

Keysight noticed after the meeting that forcing Aggregation Level 4 makes impossible to avoid collisions with DCIs sent in CORESET#0 (where interleaving is used) so in test cases requiring a continuous scheduling in all slots during the measurement, that will not be possible assuming DCIs over CORESET#0 are of higher priority.

Probably withdrawn.

Decision: 		The document was withdrawn.

R5-203875	Alignment of general sections with core spec of SA FR2 R15

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0392  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203971	Addition of modified MPR behavior

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0396  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Core spec alignment. Depending on R4-20xxxx

Discussion:

r3

Decision: 		The document was revised to R5-204921.

R5-204921	Addition of modified MPR behavior

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0396  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203971)

Decision: 		The document was agreed.

R5-204033	CR to TS 38.521-2: Annex F EIRP OFF Power

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0400  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

r1

updated to align with relaxation agreements in R5-204277r1.

r3

Decision: 		The document was revised to R5-204922.

R5-204922	CR to TS 38.521-2: Annex F EIRP OFF Power

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0400  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204033)

Decision: 		The document was agreed.

R5-204104	Correction of QPSK UL RMC

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0405  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Discussion:

fully covered by Huawei’s CR R5-203968.

Decision: 		The document was withdrawn.

R5-204203	CR to TS 38.521-2 on DUT alignment options

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0409  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

offline discussion with Keysight.

r3

Decision: 		The document was revised to R5-204923.

R5-204923	CR to TS 38.521-2 on DUT alignment options

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0409  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204203)

Decision: 		The document was agreed.

R5-204265	Editorial correction of Annex C.3 Connection

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0413  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204268	Update of CSI-RS definition for DL RMCs in TS 38.521-2

Type: CR		For: Agreement
					38.521-2 v16.4.0	  CR-0416  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

fully covered by Huawei’s R5-203968.

Decision: 		The document was withdrawn.

##### 5.3.2.6	TS 38.521-3

R5-203870	Update of Test applicability for some Inter-Band EN-DC including FR2 TCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0666  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r1

Decision: 		The document was revised to R5-204924.

R5-204924	Update of Test applicability for some Inter-Band EN-DC including FR2 TCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0666  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203870)

Decision: 		The document was agreed.

R5-204060	CR to update MU and TT in 38.521-3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0689  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204866.

R5-204866	CR to update MU and TT in 38.521-3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0689  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204060)

Decision: 		The document was agreed.

###### 5.3.2.6.1	Tx Requirements (Clause 6)

R5-203515	Editorial correction of test case 6.5B.3.3.1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0651  Cat: F (Rel-16)

					Source: TTA

Decision: 		The document was agreed.

R5-203753	Update test procedure to 6.5B.3.3.1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0660  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Decision: 		The document was agreed.

R5-203763	Editorial correction of referenced clause (6.2.3) in test case 6.2B.2.1.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0661  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Editorial

Decision: 		The document was agreed.

R5-203818	Spurious inter-band EN-DC FR2 UL MIMO test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0665  Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

Abstract:

FR2 EN-DC Spur UL MIMO TC added

Discussion:

r2

Decision: 		The document was revised to R5-204766.

R5-204766	Spurious inter-band EN-DC FR2 UL MIMO test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0665  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

(Replaces R5-203818)

Decision: 		The document was agreed.

R5-203872	Adding RRCConnectionReconfiguration Table for E-UTRA on FDD band and UE does not support dynamic power sharing in 6.5B.3.3.1 and 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0668  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203938	Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0672  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204701.

R5-204701	Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0672  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203938)

Discussion:

reissued as R5-204705 because of title change.

Decision: 		The document was withdrawn.

R5-204705	Addition of test configuration for 71AA in 6.2B.1.1 MOP

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0739  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

reissued from R5-204701 because of title change.

Decision: 		The document was agreed.

R5-203940	Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0673  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204767.

R5-204767	Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0673  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203940)

Decision: 		The document was agreed.

R5-203946	Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0678  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204768.

R5-204768	Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0678  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203946)

Decision: 		The document was agreed.

R5-203960	Correction to additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0680  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203965	Update of MOP test cases for EN-DC PC2 Rel-15 requirements

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0682  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Relevant Rel-16 changes in R5-203966

Decision: 		The document was withdrawn.

R5-203973	Cleaning up of delta_TIB

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0684  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-204008	Correction to UE co-existence Test Case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0685  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

overlapping with R5-204207.

Decision: 		The document was withdrawn.

R5-204058	Clean up complete status for EN-DC test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0687  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204925.

R5-204925	Clean up complete status for EN-DC test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0687  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204058)

Decision: 		The document was agreed.

R5-204199	Update for Spurious Emissions for intra-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0714  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Abstract:

TP analysis R5-204196

Decision: 		The document was agreed.

R5-204207	Update for 6.5B.3.3.2 Spurious emission band UE co-existence

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0716  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

RAN4 dependent CR R4-2009619 was agreed.

Decision: 		The document was revised to R5-204867.

R5-204867	Update for 6.5B.3.3.2 Spurious emission band UE co-existence

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0716  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204207)

Decision: 		The document was agreed.

R5-204249	Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0999  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

-

Decision: 		The document was withdrawn.

R5-204250	FR2 Minimum output power measurement period definition

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0721  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

R4-2011693 (revision of R4-2011387) and mirror R4-2011402 are now officially agreed.

Decision: 		The document was agreed.

R5-204256	FR2 Minimum output power measurement uncertainties updates

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0722  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204868.

R5-204868	FR2 Minimum output power measurement uncertainties updates

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0722  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204256)

Discussion:

only change it does is removing the editor’s note relative to the MU and it is no longer applicable.

Decision: 		The document was withdrawn.

R5-204259	Editorial correction to EN-DC co-existence requirements

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0723  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204769.

R5-204769	Editorial correction to EN-DC co-existence requirements

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0723  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204259)

Decision: 		The document was agreed.

R5-204280	FR2 Minimum output power measurement uncertainties updates

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0725  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

Decision: 		The document was withdrawn.

R5-204296	Addition of test case 6.4B.2.4.1D

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0726  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204297	Addition of test case 6.4B.2.4.2D

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0727  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204298	Addition of test case 6.4B.2.4.3D

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0728  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204299	Addition of test case 6.4B.2.4.4D

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0729  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204310	Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0730  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204311	Addition of pending UL-MIMO tests (FR2) in Clause 6

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0731  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

cl. aff.

r2

Decision: 		The document was revised to R5-204926.

R5-204926	Addition of pending UL-MIMO tests (FR2) in Clause 6

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0731  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204311)

Decision: 		The document was agreed.

R5-204314	Common updates across tests in Clause 6

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0734  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TS 38.521-3: Core Spec alignment

Discussion:

revisit these sections in the next meeting as some additional analysis is needed for the contained tests.

Decision: 		The document was withdrawn.

###### 5.3.2.6.2	Rx Requirements (Clause 7)

R5-203488	Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0649  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204869.

R5-204869	Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0649  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203488)

Decision: 		The document was agreed.

R5-203492	In-band Blocking FR2 MU updates in 38.521-3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0650  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203633	Introduction of additonal Rel-15 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0653  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

-

Decision: 		The document was withdrawn.

R5-203817	FR2 RefSens inter-band EN-DC UL MIMO test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0664  Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

Abstract:

FR2 EN-DC RefSens UL MIMO TC added

Discussion:

r2

Decision: 		The document was revised to R5-204770.

R5-204770	FR2 RefSens inter-band EN-DC UL MIMO test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0664  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Wireless GmbH

(Replaces R5-203817)

Decision: 		The document was agreed.

R5-203871	Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0667  Cat: F (Rel-16)

					Source: CAICT

Discussion:

r3

RAN4 CR R4-2011936 going to be agreed updating the content that the editor’s note.

r4

Decision: 		The document was revised to R5-204927.

R5-204927	Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0667  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203871)

Discussion:

reissued as R5-205005 because of title change.

Decision: 		The document was withdrawn.

R5-205005	Update of OOBB and Spurious Response of Inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0741  Cat: F (Rel-16)

					Source: CAICT

Abstract:

reissued from R5-204927 because of title change.

Decision: 		The document was agreed.

R5-203910	Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0670  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1

Discussion:

r2

comments from Ericsson.

Decision: 		The document was revised to R5-204771.

R5-204771	Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0670  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203910)

Decision: 		The document was agreed.

R5-203941	Addition of the test description to apply LTE agnostic approach in 7.4B.2 MIL

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0674  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203942	Addition of intra-band contiguous EN-DC with more than 2CCs within FR1 in 7.4B.3_1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0675  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

too early to update MIL for > 2CCs before the EN-DC REFSENS structure is determined.

Decision: 		The document was withdrawn.

R5-203943	Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0676  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204772.

R5-204772	Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0676  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203943)

Decision: 		The document was agreed.

R5-203963	Update of NSA Rx test cases for 4Rx UEs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0681  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r2

Decision: 		The document was revised to R5-204928.

R5-204928	Update of NSA Rx test cases for 4Rx UEs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0681  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203963)

Decision: 		The document was agreed.

R5-204059	Correction to default test setting of 7.3B.2.3_1.1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0688  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was withdrawn.

R5-204102	Update Refsense exceptions for EN-DC including n78

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0690  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Discussion:

Original RAN4 reference document R4-2010794 contents have been merged to R4-2011760. “Not concluded” officially.

r1

The RAN4 dependent CR R4-2011938 has been agreed.

Decision: 		The document was revised to R5-205006.

R5-205006	Update Refsense exceptions for EN-DC including n78

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0690  rev 1 Cat: F (Rel-16)

					Source: Rohde & Schwarz

(Replaces R5-204102)

Decision: 		The document was agreed.

R5-204170	Update for TC 7.5B.0 Minimum Conformance Requirements of ACS for DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0697  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204171	Update for TC 7.5B.1 ACS for intra-band contiguous EN-DC 2CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0698  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-204172	Update for TC 7.5B.2 ACS for intra-band non-contiguous EN-DC 2CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0699  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-204173	Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0700  Cat: F (Rel-16)

					Source: CMCC

Discussion:

r1

Decision: 		The document was revised to R5-204929.

R5-204929	Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0700  rev 1 Cat: F (Rel-16)

					Source: CMCC

(Replaces R5-204173)

Decision: 		The document was agreed.

R5-204174	Addition of TC 7.5B.3_1.3 ACS for EN-DC within FR1 5CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0701  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was withdrawn.

R5-204175	Addition of TC 7.5B.3_1.4 ACS for EN-DC within FR1 6CC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0702  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was withdrawn.

R5-204176	Update for TC 7.5B.4 ACS for inter-band EN-DC including FR2 2CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0703  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204177	Update for TC 7.5B.4_1.1 ACS for inter-band EN-DC including FR2 3CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0704  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204178	Update for TC 7.5B.4_1.2 ACS for inter-band EN-DC including FR2 4CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0705  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204179	Update for TC 7.5B.4_1.3 ACS for inter-band EN-DC including FR2 5CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0706  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204180	Update for TC 7.5B.4_1.4 ACS for inter-band EN-DC including FR2 6CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0707  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

R5-204181	Addition of TC 7.5B.4D ACS for inter-band EN-DC including FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0708  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-204182	Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0709  Cat: F (Rel-16)

					Source: CMCC

Discussion:

r1

Decision: 		The document was revised to R5-204773.

R5-204773	Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0709  rev 1 Cat: F (Rel-16)

					Source: CMCC

(Replaces R5-204182)

Decision: 		The document was agreed.

R5-204183	Addition of TC 7.6B.2.4D Inband blocking for inter-band EN-DC including FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0710  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-204184	Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0711  Cat: F (Rel-16)

					Source: CMCC

Discussion:

r1

comments from R&S.

ETSI MCC: wrong title.

r2

Decision: 		The document was revised to R5-204930.

R5-204930	Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0711  rev 1 Cat: F (Rel-16)

					Source: CMCC

(Replaces R5-204184)

Decision: 		The document was agreed.

R5-204197	Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0712  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204931.

R5-204931	Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0712  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204197)

Decision: 		The document was agreed.

R5-204198	Update for 7.3B.2.0

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0713  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Decision: 		The document was agreed.

R5-204201	Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0715  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204719.

R5-204719	Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0715  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204201)

Decision: 		The document was agreed.

R5-204209	Update Uplink power control window size for NSA RX TCs

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0717  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Decision: 		The document was agreed.

R5-204215	Re-organization of EN-DC refsens test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0719  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r3

Decision: 		The document was revised to R5-204932.

R5-204932	Re-organization of EN-DC refsens test cases

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0719  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204215)

Decision: 		The document was agreed.

R5-204262	Update to reference sensitivity test case 7.3B.2.3_1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0724  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

merged into E\\\ R5-204215.

Decision: 		The document was withdrawn.

R5-204312	Addition of pending UL-MIMO tests (FR2) in Clause 7

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0732  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

-

Decision: 		The document was withdrawn.

R5-204315	Common updates across tests in Clause 7

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0735  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TS 38.521-3: Core Spec alignment

Discussion:

revisit these sections in the next meeting as some additional analysis is needed for the contained tests.

Decision: 		The document was withdrawn.

R5-204322	Update for TC 7.5B.5 ACS for inter-band EN-DC including both FR1 and FR2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0736  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

###### 5.3.2.6.3	Clauses 1-5, Annexes

R5-203294	Correction of MU definition for test case 6.5B.2.1.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0645  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203295	definition of MU and TT for test case 6.3B.4.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0646  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203296	definition of MU and TT for test case 6.5B.4.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0647  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203297	Definition of MU and TT for test case 7.3B.2.4

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0648  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-204151	Updated to EN-DC Rel-15 Configuration information in clause 5

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0691  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

Added Rel-15 CA/DC configurations which has been assigned to company and at least 1 TC requirement included in the spec

Discussion:

no further requirement received.

Decision: 		The document was withdrawn.

R5-204313	TS 38.521-3 Section 1-5 and Annex updates to align with core specification

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0733  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TS 38.521-3: Core Spec alignment

Decision: 		The document was agreed.

##### 5.3.2.7	TS 38.521-4

R5-204065	CR to update MU and TT in 38.521-4

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0229  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

coversheet fix.

r2

Decision: 		The document was revised to R5-204933.

R5-204933	CR to update MU and TT in 38.521-4

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0229  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204065)

Decision: 		The document was agreed.

R5-204100	Update to common test parameters and channel mappings

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0232  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Discussion:

R&S: Anritsu CR R5-204067 has been withdrawn. QC will remove the conflicting parts from R5-203673 so that R&S CR R5-204100 can be kept as is.

Decision: 		The document was agreed.

###### 5.3.2.7.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

R5-203298	Activate Test Mode in NSA Demod Test Cases

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0215  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203670	message contents correction for TC 5.2.3.1.2_1

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0217  Cat: F (Rel-16)

					Source: Qualcomm Korea

Decision: 		The document was agreed.

R5-203717	Correction to TC 5.2.3.1.1_1 4Rx FDD FR1 PDSCH mapping Type A performance

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0219  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203756	Removing unnecessary IE rbg-Size from message exceptions

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0220  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203903	Addition of FR1 2Rx TDD PDSCH mapping type B test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0222  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r1

Decision: 		The document was revised to R5-204870.

R5-204870	Addition of FR1 2Rx TDD PDSCH mapping type B test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0222  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-203903)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205008.

R5-205008	Addition of FR1 2Rx TDD PDSCH mapping type B test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0222  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-204870)

Decision: 		The document was agreed.

R5-203904	Test applicability update for all PDSCH mapping type B test cases

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0223  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r1

Decision: 		The document was revised to R5-204774.

R5-204774	Test applicability update for all PDSCH mapping type B test cases

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0223  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-203904)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205009.

R5-205009	Test applicability update for all PDSCH mapping type B test cases

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0223  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-204774)

Decision: 		The document was agreed.

R5-203905	Addition of 4Rx FDD FR1 RI reporting test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0224  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r1

Decision: 		The document was revised to R5-204871.

R5-204871	Addition of 4Rx FDD FR1 RI reporting test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0224  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-203905)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205010.

R5-205010	Addition of 4Rx FDD FR1 RI reporting test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0224  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-204871)

Decision: 		The document was agreed.

R5-204061	Correction to frequencyDomainAllocation

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0225  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204934.

R5-204934	Correction to frequencyDomainAllocation

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0225  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204061)

Decision: 		The document was agreed.

R5-204062	Correction to PDSCH reference channel

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0226  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009540 was agreed.

Decision: 		The document was agreed.

R5-204063	Correction to 2Rx FDD FR1 periodic wideband CQI reporting under fading conditions

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0227  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204064	Correction to LTE-NR coexistence performance

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0228  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204066	Correction to MU and TT for FR1 PMI and RI tests

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0230  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

removed overlapping part from R5-203905 (QC).

Decision: 		The document was revised to R5-204935.

R5-204935	Correction to MU and TT for FR1 PMI and RI tests

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0230  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204066)

Decision: 		The document was agreed.

R5-204261	Editorial correction of message exceptions

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0235  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

###### 5.3.2.7.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

R5-203673	Update to FR2 PDSCH test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0218  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r2

Decision: 		The document was revised to R5-204936.

R5-204936	Update to FR2 PDSCH test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0218  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-203673)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205011.

R5-205011	Update to FR2 PDSCH test case

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0218  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-204936)

Decision: 		The document was agreed.

R5-204067	Correction to common test parameters for FR2 demod and CSI tests

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0231  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

Already covered in R&S R5-204100.

Decision: 		The document was withdrawn.

###### 5.3.2.7.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.2.7.4	Clauses 1-4, Annexes

R5-203668	Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0216  Cat: F (Rel-16)

					Source: Qualcomm Korea

Discussion:

r1

Decision: 		The document was revised to R5-204937.

R5-204937	Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0216  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-203668)

Discussion:

rev: - !

Decision: 		The document was revised to R5-205012.

R5-205012	Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0216  rev 2 Cat: F (Rel-16)

					Source: Qualcomm Korea

(Replaces R5-204937)

Decision: 		The document was agreed.

R5-203902	Correction to Annex G minimum test time table

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0221  Cat: F (Rel-16)

					Source: Qualcomm Korea

Decision: 		The document was agreed.

R5-204101	Update E-UTRA cell configuration for NSA

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0233  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Decision: 		The document was agreed.

R5-204105	Addition of missing FR1 RMC

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0234  Cat: F (Rel-16)

					Source: Rohde & Schwarz

Discussion:

RAN4 dependent CR R4-2010798 has been noted.

Decision: 		The document was withdrawn.

R5-204273	Update of AWGN flatness in TS 38.521-4

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0236  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Associated discussion paper in R5-204271

Discussion:

r1

Decision: 		The document was revised to R5-204938.

R5-204938	Update of AWGN flatness in TS 38.521-4

Type: CR		For: Agreement
					38.521-4 v16.4.0	  CR-0236  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204273)

Decision: 		The document was agreed.

##### 5.3.2.8	TS 38.522

R5-203330	TP for TS 38.522

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0043  Cat: F (Rel-16)

					Source: CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm

Discussion:

r2

Decision: 		The document was revised to R5-204939.

R5-204939	TP for TS 38.522

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0043  rev 1 Cat: F (Rel-16)

					Source: CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm

(Replaces R5-203330)

Decision: 		The document was agreed.

R5-203869	Correction of 38.522

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0044  Cat: F (Rel-16)

					Source: CAICT

Abstract:

Based on proposals in discussion paper R5-203868.

Discussion:

r2

Decision: 		The document was revised to R5-204940.

R5-204940	Correction of 38.522

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0044  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203869)

Decision: 		The document was agreed.

R5-203975	Addition of PICS for intra-band EN-DC PC2

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0045  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was withdrawn.

R5-204098	Correct applicability EN-DC event-triggered inter-frequency tests

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0046  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204099	Correct applicability NR SA event-triggered inter-frequency tests

Type: CR		For: Agreement
					38.522 v16.4.0	  CR-0047  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

##### 5.3.2.9	TS 38.533

R5-204283	Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0857  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

R&S: -	The test procedure is modified to say: “For Test 2, the DL timing change shall be applied immediately upon expiration of the preceding DRX ON duration.”

o	We would like to understand the reason why the DL timing change needs to be applied after the DRX ON duration.

o	Furthermore, if this is really needed, would it be possible to make it more concrete? “Immediately upon expiration” is a bit open for interpretation, would it be possible to specify the slot?

-	An editorial comment, in Table 4.4.1.1.4.3-2, the name of the parameter drxSlotOffset is being removed. I guess the intention was to specify “Not Present”, therefore the name of the parameter should stay.

r1

Decision: 		The document was revised to R5-204872.

R5-204872	Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0857  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204283)

Decision: 		The document was agreed.

R5-204284	Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0858  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

r1

Decision: 		The document was revised to R5-204873.

R5-204873	Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0858  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204284)

Decision: 		The document was agreed.

R5-204285	Correction to Message Exceptions for 4.6.2.5 EN-DC FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0859  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

No Comments received.

Decision: 		The document was agreed.

R5-204286	Correction to General Test Parameters for 6.6.2.5 NR SA FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0860  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

merged into R5-204286.

Decision: 		The document was withdrawn.

R5-204287	Correction to General Test Parameters for 6.6.2.2 NR SA FR1-FR1 event-triggered reporting in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0861  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

merged into R5-204286.

Decision: 		The document was withdrawn.

R5-204288	Correction to General Test Parameters for 6.6.2.6 NR SA FR1-FR1 event-triggered reporting in DRX with SSB time index detection

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0862  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

merged into R5-204286.

Decision: 		The document was withdrawn.

R5-204289	Correction to 6.3.1.1 NR SA FR1 handover with known target cell sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0863  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204290	Correction to 6.3.1.2 NR SA FR1 handover with unknown target cell sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0864  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204291	Correction to 6.3.1.3 NR SA FR1-FR1 handover with unknown target cell sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0865  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204302	Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0866  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

Worked offline with Anritsu, to remove the overlap.

r1

Decision: 		The document was revised to R5-204874.

R5-204874	Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0866  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204302)

Decision: 		The document was agreed.

R5-204303	Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0867  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

r1

Decision: 		The document was revised to R5-204875.

R5-204875	Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0867  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204303)

Decision: 		The document was agreed.

R5-204304	Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0868  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

Worked offline with Anritsu, to remove the overlap.

r1

Decision: 		The document was revised to R5-204876.

R5-204876	Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0868  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204304)

Decision: 		The document was agreed.

R5-204305	Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0869  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

r1

Decision: 		The document was revised to R5-204877.

R5-204877	Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0869  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204305)

Decision: 		The document was agreed.

R5-204306	Correction to 4.5.1.1 EN-DC FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0870  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204307	Correction to 6.5.1.2 EN-DC RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0871  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204308	Correction to 6.5.1.3 EN-DC FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0872  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

R5-204309	Correction to 6.5.1.4 EN-DC FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0873  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Corrections to already completed / validated RRM test cases

Discussion:

-

Decision: 		The document was withdrawn.

###### 5.3.2.9.1	EN-DC with all NR cells in FR1 (Clause 4)

R5-203241	Update TC 4.7.4.1.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0750  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204878.

R5-204878	Update TC 4.7.4.1.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0750  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203241)

Decision: 		The document was agreed.

R5-203242	Update TC 4.7.4.1.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0751  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204775.

R5-204775	Update TC 4.7.4.1.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0751  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203242)

Decision: 		The document was agreed.

R5-203243	Update TC 4.7.4.2.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0752  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204879.

R5-204879	Update TC 4.7.4.2.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0752  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203243)

Decision: 		The document was agreed.

R5-203244	Update TC 4.7.4.2.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0753  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204776.

R5-204776	Update TC 4.7.4.2.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0753  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203244)

Decision: 		The document was agreed.

R5-203268	Correction of test applicability for EN-DC event-triggered tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0766  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203274	Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0771  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204777.

R5-204777	Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0771  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203274)

Decision: 		The document was agreed.

R5-203301	Correction of delta offset application for Cell 2 in test case 4.7.1.2.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0775  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203304	Correction to the RRC Reconfiguration message for measurements

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0778  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203306	Update extreme conditions limits in TC 4.7.1.2.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0779  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203732	Set ss-sinr request to false for EN-DC RRM measurement accuracy tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0790  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203827	Addition of 4.5.5.0 minimum requirement for BFR

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0151  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

cover: 38.533!

withdrawn and reissued as R5-204337 because of wrong spec!

Decision: 		The document was withdrawn.

R5-204337	Addition of 4.5.5.0 minimum requirement for BFR

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0874  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

reissued from R5-203827 because of wrong spec!

Decision: 		The document was agreed.

R5-203828	Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0794  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204985.

R5-204985	Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0794  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203828)

Decision: 		The document was agreed.

R5-203829	Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0795  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204986.

R5-204986	Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0795  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203829)

Decision: 		The document was agreed.

R5-203830	Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0796  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204987.

R5-204987	Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0796  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

(Replaces R5-203830)

Decision: 		The document was agreed.

R5-203831	Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0797  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204988.

R5-204988	Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0797  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

(Replaces R5-203831)

Decision: 		The document was agreed.

R5-203832	Update of 4.5.6.1.0 minimum requirement for DCI-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0798  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203833	Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0799  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204989.

R5-204989	Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0799  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203833)

Decision: 		The document was agreed.

R5-203834	Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0800  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204990.

R5-204990	Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0800  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203834)

Decision: 		The document was agreed.

R5-203835	Update of 4.5.6.2.0 minimum requirement for RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0801  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203836	Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0802  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204991.

R5-204991	Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0802  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203836)

Decision: 		The document was agreed.

R5-204072	Correction to EN-DC and SA FR1-FR1 SS-RSRP and SS-RSRQ periodical measurement accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0833  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204073	Correction to SS-RSRQ periodical measurement accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0834  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009550 was agreed.

Decision: 		The document was agreed.

R5-204074	Correction to connection diagram for radio link monitoring tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0835  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204941.

R5-204941	Correction to connection diagram for radio link monitoring tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0835  rev 1 Cat: F (Rel-16)

					Source: Anritsu

(Replaces R5-204074)

Decision: 		The document was agreed.

R5-204075	Correction to message configuration for radio link monitoring tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0836  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204077	Correction to SRS PeriodicityAndOffset for Timing Advance tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0838  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009544 was agreed.

Decision: 		The document was agreed.

R5-204126	Correction of minimum conformance requirements 4.6.4.0 for EN-DC FR1 L1-RSRP measurement test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0851  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Minimum conformance requirements correction to align with RAN4 changes

Decision: 		The document was agreed.

###### 5.3.2.9.2	EN-DC with at least 1 NR Cell in FR2 (Clause5)

R5-204068	Correction to FR2 timing advance adjustment accuracy

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0829  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009567 was agreed.

Decision: 		The document was agreed.

R5-204069	Correction to EN-DC FR2 interruptions at transitions between active and non-active during DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0830  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204116	Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0841  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204117	Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0842  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Discussion:

r1

Decision: 		The document was revised to R5-204942.

R5-204942	Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0842  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204117)

Decision: 		The document was agreed.

R5-204118	Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0843  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204119	Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.4

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0844  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204127	Correction of minimum conformance requirements 5.6.3.0 for EN-DC FR2 L1-RSRP measurement test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0852  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Minimum conformance requirements correction to align with RAN4 changes

Decision: 		The document was agreed.

###### 5.3.2.9.3	NR Standalone in FR1 (Clause 6)

R5-203245	Update TC 6.7.4.1.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0754  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204880.

R5-204880	Update TC 6.7.4.1.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0754  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203245)

Decision: 		The document was agreed.

R5-203246	Update TC 6.7.4.1.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0755  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204778.

R5-204778	Update TC 6.7.4.1.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0755  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203246)

Decision: 		The document was agreed.

R5-203247	Update TC 6.7.4.2.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0756  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r2

Decision: 		The document was revised to R5-204881.

R5-204881	Update TC 6.7.4.2.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0756  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203247)

Decision: 		The document was agreed.

R5-203248	Update TC 6.7.4.2.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0757  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204779.

R5-204779	Update TC 6.7.4.2.2 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0757  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203248)

Decision: 		The document was agreed.

R5-203264	Correction to the test procedure of NR SA event triggered tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0762  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204780.

R5-204780	Correction to the test procedure of NR SA event triggered tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0762  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203264)

Decision: 		The document was agreed.

R5-203265	Correction to the test procedure of NR SA event triggered tests inter-freq

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0763  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204781.

R5-204781	Correction to the test procedure of NR SA event triggered tests inter-freq

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0763  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203265)

Decision: 		The document was agreed.

R5-203266	Correction to the test procedure of NR SA event triggered tests inter-RAT

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0764  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204782.

R5-204782	Correction to the test procedure of NR SA event triggered tests inter-RAT

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0764  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203266)

Decision: 		The document was agreed.

R5-203267	[EDITORIAL] Fix formatting issues throwing DOCX conversion errors in TS 38.533

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0765  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

EDITORIAL

Decision: 		The document was agreed.

R5-203269	Correction of test applicability for NR SA event-triggered tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0767  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203272	Remove IE includeBeamMeasurements from 6.6.1.5 and 6.6.1.6

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0770  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203299	Corrected test description in non-DRX test case 6.5.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0773  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203300	Correction of comment for monitoringSymbolsWithinSlot

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0774  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203302	Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0776  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd, Qualcomm Incorporated

Discussion:

Offline Comments from TF160.

r1

Decision: 		The document was revised to R5-204882.

R5-204882	Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0776  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd, Qualcomm Incorporated

(Replaces R5-203302)

Decision: 		The document was agreed.

R5-203303	PUSCH allocation correction in test case 6.4.3.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0777  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203307	Update extreme conditions limits in TC 6.7.1.2.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0780  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203317	Removing SearchSpaceId and ControlResourceSetId modification

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0786  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203318	Test Procedure correction in test case 6.5.1.3 for definition of Point C

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0787  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

cover 38.523-1

r1 was produced.

Decision: 		The document was revised to R5-204883.

R5-204883	Test Procedure correction in test case 6.5.1.3 for definition of Point C

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0787  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203318)

Decision: 		The document was agreed.

R5-203733	Set ss-sinr request to false for NR SA RRM measurement accuracy tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0791  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203820	Correction of RRM Test Case 6.1.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0793  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204733.

R5-204733	Correction of RRM Test Case 6.1.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0793  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203820)

Decision: 		The document was agreed.

R5-203837	Update of FR1 Test Tolerance in 6.3.2.1.3 RRC re-establishment without serving cell timing

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0803  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203838	Addition of 6.5.2.0 minimum requirement for interruptions during measurements on NR SCC

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0804  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203839	Update of 6.5.2.1 interruptions during measurements on deactivated NR SCC

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0805  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Decision: 		The document was agreed.

R5-203840	Addition of new Test Case 6.5.3.1 SCell activation and deactivation for 160ms cycle

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0806  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Decision: 		The document was agreed.

R5-203841	Addition of new Test Case 6.5.3.2 SCell activation and deactivation for 320ms cycle

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0807  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Decision: 		The document was agreed.

R5-203842	Addition of new Test Case 6.5.3.3 SCell activation and deactivation of unknown SCell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0808  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, CAICT

Decision: 		The document was agreed.

R5-203843	Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0809  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204992.

R5-204992	Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0809  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203843)

Decision: 		The document was agreed.

R5-203844	Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0810  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204993.

R5-204993	Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0810  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203844)

Decision: 		The document was agreed.

R5-203845	Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0811  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204994.

R5-204994	Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0811  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203845)

Decision: 		The document was agreed.

R5-203846	Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0812  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204995.

R5-204995	Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0812  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203846)

Decision: 		The document was agreed.

R5-203847	Update of 6.5.6.1.0 minimum requirement for DCI-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0813  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203848	Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0814  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

RAN4 dependent CR R4-2011103 revised to R4-2012078.

Decision: 		The document was revised to R5-204996.

R5-204996	Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0814  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203848)

Decision: 		The document was agreed.

R5-203849	Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0815  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

RAN4 dependent CR R4-2011103 revised to R4-2012078.

Decision: 		The document was revised to R5-204997.

R5-204997	Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0815  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203849)

Decision: 		The document was agreed.

R5-203850	Update of 6.5.6.2.0 minimum requirement for RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0816  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203851	Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0817  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

was changed according to the related CRs R4-2012071 (from CATT) and R4-2012078 (from Huawei).

Decision: 		The document was revised to R5-204998.

R5-204998	Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0817  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203851)

Decision: 		The document was agreed.

R5-203852	Update of test parameters in 6.3.1.4 inter-RAT handover

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0818  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204999.

R5-204999	Update of test parameters in 6.3.1.4 inter-RAT handover

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0818  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203852)

Decision: 		The document was agreed.

R5-203853	Correction to FR1 intra-frequency measurement with gap test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0819  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

the original CR R4-2011105 was agreed during the second round of RAN4 discussion, so R4-2012079 was withdrawn.

Decision: 		The document was agreed.

R5-203895	Correction of RRM Test Case 6.1.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0824  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204734.

R5-204734	Correction of RRM Test Case 6.1.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0824  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203895)

Decision: 		The document was agreed.

R5-204071	Correction on event-triggered reporting with gap in DRX and DRX configuration settings for NR serving cell

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0832  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204076	Correction to NR SA FR1 E-UTRA RRC connection release with redirection

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0837  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009542 was agreed.

Decision: 		The document was agreed.

###### 5.3.2.9.4	NR standalone with at least one NR cell in FR2 (Clause7)

R5-203431	Addition of new RRM Test Cases in clause 7.5.5

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0789  Cat: F (Rel-16)

					Source: ZTE Corporation

Discussion:

r1

Decision: 		The document was revised to R5-204884.

R5-204884	Addition of new RRM Test Cases in clause 7.5.5

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0789  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203431)

Decision: 		The document was agreed.

R5-203896	Correction of RRM Test Case 7.1.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0825  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204735.

R5-204735	Correction of RRM Test Case 7.1.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0825  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203896)

Decision: 		The document was agreed.

R5-203897	Correction of RRM Test Case 7.1.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0826  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204736.

R5-204736	Correction of RRM Test Case 7.1.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0826  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203897)

Decision: 		The document was agreed.

R5-204034	CR to 38.533 on RRM Test Cases in clause 7.5.3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0827  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Decision: 		The document was agreed.

R5-204036	CR to 38.533 on RRM Test Cases in clause 7.5.7

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0828  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Decision: 		The document was agreed.

R5-204122	Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0847  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204123	Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0848  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204124	Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0849  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204125	Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.4

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0850  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

RRM test case correction

Decision: 		The document was agreed.

R5-204128	Correction of minimum conformance requirements 7.6.3.0 for SA FR2 L1-RSRP measurement test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0853  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Minimum conformance requirements correction to align with RAN4 changes

Decision: 		The document was agreed.

###### 5.3.2.9.5	E-UTRA – NR Inter-RAT with E-UTRA serving cell (Clause 8)

R5-203234	Update TC 8.5.2.1.1.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0747  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203235	Update TC 8.5.2.2.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0748  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203236	Update TC 8.5.2.3.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0749  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204783.

R5-204783	Update TC 8.5.2.3.1 with TT results and message contents

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0749  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203236)

Decision: 		The document was agreed.

R5-203252	Void unnecessary TC 8.5.2.1.1.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0761  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

###### 5.3.2.9.6	Clauses 1-3, Annexes

R5-203249	Annex E and F update with TT results for 8.5.2.x.x iRAT periodic reporting test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0758  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203250	Annex E and F update with TT results for 4.7.4.x.x EN-DC L1-RSRP periodic reporting test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0759  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203251	Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0760  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204784.

R5-204784	Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0760  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203251)

Decision: 		The document was agreed.

R5-203270	Adding annex table for iRAT measurement configuration

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0768  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203271	Clarification on the usage of auxiliary bands

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0769  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm Finland RFFE Oy

Decision: 		The document was agreed.

R5-203308	Update extreme conditions limits in TC 4.7.1.2.1 and TC 6.7.1.2.1 - Annex F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0781  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203309	Correction power offset for Band Group F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0782  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203314	CR to update the RRM FR2 MUs in Annex F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0783  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

To be provided based on the agreements of the RRM FR2 MU discussion

Discussion:

r1

Decision: 		The document was revised to R5-204885.

R5-204885	CR to update the RRM FR2 MUs in Annex F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0783  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203314)

Decision: 		The document was agreed.

R5-203315	Add information on the AoA change during test for RRM FR2 tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0784  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r3

Decision: 		The document was revised to R5-204886.

R5-204886	Add information on the AoA change during test for RRM FR2 tests

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0784  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203315)

Decision: 		The document was agreed.

R5-203316	Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0785  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-204785.

R5-204785	Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0785  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203316)

Decision: 		The document was agreed.

R5-203319	Unification of cell frequency for FR1-FR1 test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0788  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Decision: 		The document was agreed.

R5-203757	Update of PDSCH RMC in Annex A.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0792  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204730.

R5-204730	Update of PDSCH RMC in Annex A.1.1

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0792  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203757)

Decision: 		The document was agreed.

R5-203854	Update of FR1 Test Tolerance in Annex F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0820  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204786.

R5-204786	Update of FR1 Test Tolerance in Annex F

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0820  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203854)

Decision: 		The document was agreed.

R5-203855	Update of Cell mapping in Annex E

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0821  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203856	Update of default configurations for RMC scheduling in Annex A

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0822  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent

Discussion:

r1

Decision: 		The document was revised to R5-205000.

R5-205000	Update of default configurations for RMC scheduling in Annex A

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0822  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203856)

Decision: 		The document was agreed.

R5-203862	Correction to default configurations in Annex H

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0823  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204787.

R5-204787	Correction to default configurations in Annex H

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0823  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203862)

Decision: 		The document was agreed.

R5-204070	Addition of E-UTRA Test frequency selection rule for IRAT test cases

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0831  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204078	Correction to PDSCH reference measurement channel

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0839  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

changes are included in R5-203757(Mediatek).

Decision: 		The document was withdrawn.

R5-204079	Correction to CSI-RS for tracking for TDD FR2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0840  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009569 was agreed.

Decision: 		The document was agreed.

R5-204120	Correction of FR2 condition tables in Annex B

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0845  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Correcting  outdated FR2 band grouping and adding missing conditions in annex B.

Discussion:

is also NR_bands_BW_R16-UEConTest.

r1

Decision: 		The document was revised to R5-204943.

R5-204943	Correction of FR2 condition tables in Annex B

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0845  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204120)

Decision: 		The document was agreed.

R5-204121	Introduction of band n259 in clause 3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0846  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Addition of new band n259 (introduced by RAN4 duirng RAN4 #95-e) and other  corrections.

Discussion:

is also NR_bands_BW_R16-UEConTest.

r1

Decision: 		The document was revised to R5-204944.

R5-204944	Introduction of band n259 in clause 3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0846  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204121)

Decision: 		The document was agreed.

R5-204220	Update missing SMTC and SSB configurations in H.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0854  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204221	Update missing SMTC and SSB configurations in H.3

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0855  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-204222	Editorial: correct table placement in H.2

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0856  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

This is an Editorial CR

Decision: 		The document was agreed.

##### 5.3.2.10	TS 36.508

##### 5.3.2.11	TS 36.521-3

##### 5.3.2.12	TS 37.571-1

##### 5.3.2.13	TS 37.571-3

##### 5.3.2.14	TS 37.571-5

##### 5.3.2.15	TR 38.903 ((NR MU &  TT analyses)

R5-203231	TT analysis for RRM TC 8.5.2.1.1.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0131  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203234

Decision: 		The document was agreed.

R5-203232	TT analysis for RRM TC 8.5.2.2.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0132  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203235

Decision: 		The document was agreed.

R5-203233	TT analysis for RRM TC 8.5.2.3.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0133  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203236

Decision: 		The document was agreed.

R5-203237	TT analysis for RRM TC 4.7.4.1.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0134  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203241

Decision: 		The document was agreed.

R5-203238	TT analysis for RRM TC 4.7.4.1.2

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0135  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203242

Decision: 		The document was agreed.

R5-203239	TT analysis for RRM TC 4.7.4.2.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0136  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Corresponding TC TDoc is R5-203243

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-203240	TT analysis for RRM TC 4.7.4.2.2

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0137  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

The corresponding TC TDoc is R5-203244

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-203305	Correction to the extreme conditions in TT analysis of 4.7.1.2.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0138  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204788.

R5-204788	Correction to the extreme conditions in TT analysis of 4.7.1.2.1

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0138  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203305)

Decision: 		The document was agreed.

R5-203313	CR to update the DL AWGN absolute power for RRM test cases

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0139  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

To be provided based on the agreements of the RRM FR2 MU discussion

Discussion:

r1

Decision: 		The document was revised to R5-204887.

R5-204887	CR to update the DL AWGN absolute power for RRM test cases

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0139  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203313)

Discussion:

late upload

Decision: 		The document was agreed.

R5-203323	Add Draft Test Tolerance analysis for FR2 Tx Timing Test cases

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0140  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

R4-2009552 was agreed.

Decision: 		The document was agreed.

R5-203324	Add Draft Test Tolerance analysis for FR2 Inter-freq Event-trig Test cases

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0141  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

R4-2009573 was agreed.

Decision: 		The document was agreed.

R5-203325	Add Draft Test Tolerance analysis for FR2 Intra-freq SS-RSRP Test case

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0142  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

R4-2009565 and R4-2009573 were agreed.

Decision: 		The document was agreed.

R5-203486	Adjacent Channel Selectivity FR2 MU definition in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0143  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204888.

R5-204888	Adjacent Channel Selectivity FR2 MU definition in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0143  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203486)

Decision: 		The document was agreed.

R5-203490	In-band Blocking FR2 MU definition in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0144  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204889.

R5-204889	In-band Blocking FR2 MU definition in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0144  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203490)

Decision: 		The document was agreed.

R5-203821	Addition of FR1 Test tolerance analysis for DCI based BWP switch

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0145  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent, corresponding TCs TDoc: R5-203833/3834/3848/3849

Discussion:

r1

Decision: 		The document was revised to R5-205001.

R5-205001	Addition of FR1 Test tolerance analysis for DCI based BWP switch

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0145  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203821)

Decision: 		The document was agreed.

R5-203822	Addition of FR1 Test tolerance analysis for RRC based BWP switch

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0146  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent, corresponding TCs TDoc: R5-203836/3851

Discussion:

r1

Decision: 		The document was revised to R5-205002.

R5-205002	Addition of FR1 Test tolerance analysis for RRC based BWP switch

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0146  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203822)

Decision: 		The document was agreed.

R5-203823	Addition of FR1 Test tolerance analysis for SSB based BFR

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0147  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent, corresponding TCs TDoc :R5-203828/3829/3843/3844

Discussion:

r1

Decision: 		The document was revised to R5-205003.

R5-205003	Addition of FR1 Test tolerance analysis for SSB based BFR

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0147  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203823)

Decision: 		The document was agreed.

R5-203824	Addition of FR1 Test tolerance analysis for CSI-RS based BFR

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0148  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

RAN4 dependent, corresponding TCs TDoc :R5-203830/3831/3845/3846

Discussion:

r1

Decision: 		The document was revised to R5-205004.

R5-205004	Addition of FR1 Test tolerance analysis for CSI-RS based BFR

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0148  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203824)

Decision: 		The document was agreed.

R5-203825	Addition of FR1 Test tolerance analysis for 6.3.2.1.3 RRC Re-establishment

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0149  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Corresponding TC TDoc:R5-203837

Decision: 		The document was agreed.

R5-203826	Update of grouping of test cases in clause 8

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0150  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-204028	CR to 38.903 on some of the Transmit OFF power MU parameters

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0152  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

r1

updated to align with relaxation agreements in R5-204277r1.

r3

Decision: 		The document was revised to R5-204945.

R5-204945	CR to 38.903 on some of the Transmit OFF power MU parameters

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0152  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204028)

Decision: 		The document was agreed.

R5-204080	CR to update MU in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0153  Cat: F (Rel-16)

					Source: Anritsu, Keysight Technologies

Discussion:

r1

cl. aff.

r3

Decision: 		The document was revised to R5-204890.

R5-204890	CR to update MU in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0153  rev 1 Cat: F (Rel-16)

					Source: Anritsu, Keysight Technologies

(Replaces R5-204080)

Decision: 		The document was agreed.

R5-204190	On Standard Deviation Definition in 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0154  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Abstract:

Introduce the definition of the standard deviation that is commonly used for OTA measurements.

Decision: 		The document was agreed.

R5-204257	FR2 Minimum output power measurement uncertainty

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0155  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204891.

R5-204891	FR2 Minimum output power measurement uncertainty

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0155  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204257)

Decision: 		The document was agreed.

R5-204272	Update of AWGN flatness in TR 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0156  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Associated discussion paper in R5-204271

Discussion:

r3

Decision: 		The document was revised to R5-204946.

R5-204946	Update of AWGN flatness in TR 38.903

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0156  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-204272)

Decision: 		The document was agreed.

R5-204281	FR2 EIRP OFF power measurement uncertainty

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0157  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

r2

Decision: 		The document was revised to R5-204947.

R5-204947	FR2 EIRP OFF power measurement uncertainty

Type: CR		For: Agreement
					38.903 v16.4.0	  CR-0157  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

(Replaces R5-204281)

Decision: 		The document was agreed.

##### 5.3.2.16	TR 38.905 (NR Test Points Radio Transmission and Reception )

R5-203675	Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0271  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TC in R5-203674

Discussion:

r1

Decision: 		The document was revised to R5-204789.

R5-204789	Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0271  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203675)

Decision: 		The document was agreed.

R5-203676	Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0272  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TC in R5-203674

Discussion:

r1

Decision: 		The document was revised to R5-204790.

R5-204790	Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0272  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203676)

Decision: 		The document was agreed.

R5-203805	Addition of test point analysis of DC_66A_n2A in Tx spurious emissions

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0277  Cat: F (Rel-16)

					Source: Sporton

Discussion:

-

Decision: 		The document was withdrawn.

R5-203939	Update of test point analysis of MOP for intra-band contiguous EN-DC

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0279  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

is affected by R5-204704.

Decision: 		The document was revised to R5-204728.

R5-204728	Update of test point analysis of MOP for intra-band contiguous EN-DC

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0279  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203939)

Decision: 		The document was agreed.

R5-203947	Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0280  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204791.

R5-204791	Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0280  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203947)

Decision: 		The document was agreed.

R5-203948	Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0281  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r3

Decision: 		The document was revised to R5-204792.

R5-204792	Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0281  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203948)

Decision: 		The document was agreed.

R5-203949	Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0282  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r3

Decision: 		The document was revised to R5-204793.

R5-204793	Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0282  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203949)

Decision: 		The document was agreed.

R5-203950	Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0283  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r3

Decision: 		The document was revised to R5-204794.

R5-204794	Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0283  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203950)

Decision: 		The document was agreed.

R5-203951	Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0284  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r3

Decision: 		The document was revised to R5-204795.

R5-204795	Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0284  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203951)

Decision: 		The document was agreed.

R5-203952	Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0285  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204796.

R5-204796	Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0285  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203952)

Decision: 		The document was agreed.

R5-203961	Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0292  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204797.

R5-204797	Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0292  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203961)

Decision: 		The document was agreed.

R5-204147	Addition of Test Point analysis for FR2 Transmit OFF Power for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0295  Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

Discussion:

.docx

r1

Decision: 		The document was revised to R5-204948.

R5-204948	Addition of Test Point analysis for FR2 Transmit OFF Power for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0295  rev 1 Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

(Replaces R5-204147)

Decision: 		The document was agreed.

R5-204148	Addition of Test Point analysis for FR2 Occupied bandwidth for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0296  Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

Discussion:

-

Decision: 		The document was withdrawn.

R5-204149	Addition of Test Point analysis for FR2 Transmitter Spurious emissions for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0297  Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

Discussion:

-

Decision: 		The document was withdrawn.

R5-204196	TP analysis 6.5B.3 TX SpurEmission EN-DC V2

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0298  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204949.

R5-204949	TP analysis 6.5B.3 TX SpurEmission EN-DC V2

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0298  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204196)

Decision: 		The document was agreed.

R5-204208	Add_TP_analysis_table for TX_spurious_emission

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0299  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204720.

R5-204720	Add_TP_analysis_table for TX_spurious_emission

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0299  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204208)

Decision: 		The document was agreed.

R5-204216	Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0300  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204950.

R5-204950	Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0300  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204216)

Decision: 		The document was agreed.

##### 5.3.2.17	Discussion Papers, Work Plan, TC lists

R5-203310	Quality of the Quiet Zone measurement results for enhanced IFF

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

The QoQZ for enhanced IFF setup is still FFS. This contribution provides the measurements of the QoQZ in an Enhanced IFF test system and proposed the value of the QoQZ based on the results.

Proposal 1: Use 0.6 dB as QoQZ Measurement Uncertainty for enhanced IFF.

Proposal 2: Use 0.4 dB as QoQZ Measurement Uncertainty for calibration for enhanced IFF.

Discussion:

r1

Decision: 		The document was revised to R5-204737.

R5-204737	Quality of the Quiet Zone measurement results for enhanced IFF

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

(Replaces R5-203310)

Decision: 		The document was noted.

R5-203311	Uncertainty assessment DL AWGN absolute power for enhanced IFF

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

The uncertainty assessment for DL AWGN absolute power for enhanced IFF method is captured in TR 38.903 [1]. However, the uncertainty values for several uncertainty sources are missing:

•	QoQZ

•	Mismatch

•	Influence of the XPD

•	Multiple measurement antenna uncertainty

•	DUT repositioning

•	QoQZ for the calibration process

The uncertainty values for the 2 QoQZ measurements are proposed in [2] based on measurement results. This paper will focus on the other 4 sources.

Proposal 1: re-use the mismatch from IFF also for enhanced IFF.

Proposal 2: re-use the influence of the XPD from IFF also for enhanced IFF.

Proposal 3: re-use the multiple measurement antenna uncertainty from IFF also for enhanced IFF

Proposal 4: re-use the DUT repositioning from IFF also for enhanced IFF

Discussion:

Keysight Spain: similar impact of mismatch in Anritsu paper.

R&S: propose mismatch to be the same.

r1: offline discussion with Anritsu and Keysight.

Proposal 2 withdrawn.

r2

Decision: 		The document was revised to R5-204742.

R5-204742	Uncertainty assessment DL AWGN absolute power for enhanced IFF

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

(Replaces R5-203311)

Discussion:

"Revised from: R5-203311r2.

Noted, proposals endorsed"

Decision: 		The document was noted.

R5-203312	MTSU DL AWGN absolute power for RRM

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

The uncertainty assessment for DL AWGN absolute power for enhanced IFF method has been finalized in [1] and [2]. The uncertainty assessment DL AWGN absolute power for IFF was already concluded in RAN5 #87-e.

This contribution proposed a value for the MTSU DL AWGN absolute power for RRM in order to progress with the RRM FR2 test case definition.

Proposal 1: Use 5.19 dB as the MTSU for RRM DL AWGN absolute power

Discussion:

R&S: Can note this paper.

AT&T: based on proponent feedback, this paper can be noted.

Decision: 		The document was noted.

R5-203321	FR2 RRM test cases: dB range in Spherical coverage

Type: discussion		For: Discussion
					Source: ANRITSU LTD

Abstract:

Where a test case has an angle of arrival from Spherical Coverage directions, there is only a small dB range of applied signal level which meets both the minimum side condition at the lower end, and the maximum side condition at the higher end.

This Tdoc

Discussion:

Where a test case has an angle of arrival from Spherical Coverage directions, there is only a small dB range of applied signal level which meets both the minimum side condition at the lower end, and the maximum side condition at the higher end.

This Tdoc explains the key restrictions and where they apply, and looks at options for test case parameter values.

Decision: 		The document was noted.

R5-203322	Test Tolerance review process for FR2 RRM Test cases

Type: discussion		For: Discussion
					Source: ANRITSU LTD

Abstract:

Current status

RAN5 focus is now on FR2, with many new challenges for MU/TT

Significant TT effort required to complete FR2 RRM Test cases

FR2 RRM has new features to be handled and needs new templates

FR2 RRM Test cases developed in parallel by multiple companies

First FR2 RRM TT analyses have started to appear

FR2 SS-RSRP TT templates R5-201713, 14: proposals endorsed at RAN5#87-e

Complete FR2 Tx timing TT analysis provided at RAN5#87-e in R5-202867, not agreed because some MU values are in [ ]

New FR2 RRM TT analysis features discussed

R5-198363 technical discussion of features provided at RAN5#85

R5-200163 added handling of common FR2 TT Topics in 38.903 A.2

Proposed Way Forward

“Startup” stage leading up to RAN5#88-e

Anritsu will prepare some basic FR2 TT templates as “toolkit” for selected test cases to start the process, at RAN5#88-e and RAN5#89-e

We propose putting the available draft templates into TR38.903, with editor’s notes per TT analysis stating the incomplete items

FR2 RRM Test Tolerance review process for RAN5#89-e onwards

Following similar process currently used for FR1

Providing companies to develop FR2 TT analyses based on toolkit

Share review workload between FR2 TT reviewing companies

Leading up to RAN5#88-e, RAN5#89-e

Anritsu will prepare FR2 TT analysis templates for selected test casesLeading up to RAN5#88-e, RAN5#89-e

Baseline for list of test cases was the Representative test cases to start FR2 RRM MU analysis in R5-201155, also considering

Random Access test cases have issues with signalled absolute thresholds and the range of allowed UE gain. Anritsu has proposed a method of handling this in RAN4, awaiting agreement

The same issue with signalled absolute thresholds also affects the Inter-frequency reselection test case

Aim for most FR2 RRM test case providing companies to contribute

FR2 RRM test case providing companies can become familiar with the analysis method and toolkit

All analyses will need to be updated, according to outcome of FR2 MU agreements

FR2 RRM Test Tolerance review process for RAN5#89-e onwards

“Declaration” date: normally (meeting upload deadline – 4 weeks)

“Drafts available” date: normally (meeting upload deadline – 2 weeks)

Providing companies to develop FR2 TT analyses based on toolkit

Share review workload between FR2 RRM reviewing companies

NR TT review process runs at main meetings only (4 times per year)

Test case sign-up companies resolve any associated RAN4 issues

RRM TT reviewing companies so far for FR2 (thanks):

Qualcomm, Rohde & Schwarz, Ericsson, Anritsu, Keysight

Other companies welcome to join

Scope and Technical basis

Scope of FR2 RRM Test Tolerance review process:

RRM Test cases containing at least one cell in FR2

Technical basis:

Principle of Superposition, as defined in TR 38.903

Uncertainties are orthogonal (required for superposition to be valid)

Base on common uncertainties, such as TS 38.533 Table F.1.1.2-2

Measurement uncertainty tolerance interval 95%, as in TR 38.903

All core requirement side conditions met, based on tolerance interval

The technical basis above aligns with TT = MU

Deliverables

At the “Declaration” date:

Which test cases the contributing company intends to work on

At the “Drafts available” date:

Draft TT analysis, .xls and .doc as required

TR 38.903 CR to include the TT analysis as .zip files

Conformance test spec CRs to include TT in the test cases, together with Annex F updates (Uncertainties and Test requirement derivation)

Identify issues and proposals to solve, for example RAN4 updates

At the Tdoc upload date and at the meeting:

TR 38.903 and Conformance test spec CRs

Known status of any associated issues such as RAN4 dependency

Open issues

FR2 Uncertainties/MUs

RAN5 has not yet agreed some of the key FR2 MU values

RAN4 Core requirements in TS 38.133 and 38.101-2

Many FR2 requirements / conditions only defined for Power Class 3

AoA of RRM test cases in TS 38.133 Annex A

Likely that some RRM Test cases with 2 AoA will need to be changed from setup 3 (both AoA Spherical coverage) to setup 4 (one AoA Spherical coverage, one AoA Rx beam peak) to avoid huge variations

RRM test cases in TS 38.133 Annex A using absolute thresholds

Signalled value may need to be derived from a calibration process

Unknown unknowns in TS 38.133 Annex A

Test cases may reveal problems and immaturities when analysed

Summary: Way Forward for FR2

RAN5 is asked to endorse key points for FR2 TT review process:

“Declaration” date: normally (meeting upload deadline – 4 weeks)

“Drafts available” date: normally (meeting upload deadline – 2 weeks)

Providing companies to develop FR2 TT analyses based on toolkit

Share review workload between NR-reviewing companies

NR TT review process runs at main meetings only (4 times per year)

Test case sign-up companies resolve any associated RAN4 issues

RAN5 is also asked to endorse:

Scope is RRM, and currently Power Class 3

Technical basis as given on slide 7

Identify any test cases where special handling of TT is required

Discussion:

related CRs R5-203323-4-5.

AT&T wondered whether some adjusments for FR2 MU for RRM are needed.

r1

offline comments from AT&T and Ericsson.

Decision: 		The document was revised to R5-204848.

R5-204848	Test Tolerance review process for FR2 RRM Test cases

Type: discussion		For: Discussion
					Source: ANRITSU LTD

(Replaces R5-203322)

Discussion:

noted, wayfwd in Slide#11 for handling FR2 MU /TT documents for FR2 RRM tests is endorsed"

Decision: 		The document was noted.

R5-203485	On ACS FR2 Measurement Uncertainty definition

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

The acceptable uncertainty of Test System is not defined yet for Adjacent Channel Selectivity (ACS) test in FR2. In this document it will be discussed and proposed both the main contributions to consider and how to consider them in the overall calculation of the measurement uncertainty (MU).

In order to define the acceptable uncertainty of Test System for Adjacent Channel Selectivity (ACS) test in FR2, the following observations and proposals were made in this contribution:

Proposal 1: reuse approach followed for ACS in FR1 and calculate overall ACS MU as [SQRT (wanted_level_error2 + interferer_level_error2)] + ACLR effect.

Proposal 2: For the wanted signal level error, reuse the calculations for the reference sensitivity test uncertainty in [2], section B.19.

Proposal 3: For the interferer signal level error, consider only those MU factors uncorrelated with the wanted signal, reducing the list of contributions essentially to mismatch, interferer generator uncertainty, amplifier and insertion lost uncertainties and assume for them the same value as for the wanted signal.

Discussion:

Proposals 1 and 2 were endorsed.

r1

Decision: 		The document was revised to R5-204743.

R5-204743	On ACS FR2 Measurement Uncertainty definition

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-203485)

Discussion:

Noted, proposal 1&2 endorsed

Decision: 		The document was noted.

R5-203489	On IBB FR2 Measurement Uncertainty definition

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Discussion:

r1

Decision: 		The document was revised to R5-204744.

R5-204744	On IBB FR2 Measurement Uncertainty definition

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-203489)

Discussion:

Noted, proposal 1&2 endorsed

Decision: 		The document was noted.

R5-203669	FR2 Demod MU due to finite test time

Type: discussion		For: Endorsement
					Source: Qualcomm Korea

Abstract:

One of the MU contributors for FR2 DEMOD scenarios is result variation due to finite test time. In this paper we present our view on this MU contributor.

Endorse the below proposals and accordingly update Annex F of 38.521-4 for overall uncertainty for test tolerance calculations.

Proposal 1: For all FR2 PDSCH Demodulation scenarios add a SNR uncertainty of +/- 0.3 dB due to finite test time in the overall test system uncertainty.

Proposal 2: For all FR2 PDCCH Demodulation scenarios add a SNR uncertainty of +/- 0.4 dB due to finite test time in the overall test system uncertainty.

Discussion:

Ericsson: the simulations were 10 and 100Hz.

Conclusion: both proposals are endorsed, incl. the change in r1.

revised to r1 to limit the SNR uncertainty due to finite test time for < 100Hz doppler PDSCH Demodulation scenarios.

Decision: 		The document was revised to R5-204738.

R5-204738	FR2 Demod MU due to finite test time

Type: discussion		For: Endorsement
					Source: Qualcomm Korea

(Replaces R5-203669)

Discussion:

noted and proposals are endorsed.

Decision: 		The document was noted.

R5-203686	Discussion about proposals in LS R4-2005205

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

Abstract:

associated CR in R5-203683, R5-203684, R5-203685

Introduction

Since RAN4 has identified that the NR UE receiver ACS test requirements for PDCCH/DCI could be tighter than PDSCH due to that the PDCCH/DCI may not occupy the entire channel bandwidth where the signal power is lower than that of PDSCH as defined in ACS core specifications, two solutions were proposed to mitigate this potential issue in LS R4-2005205 [1].

This paper is to discuss the possibility of implementation of these solutions in RAN5.

________________________________________

2.	Discussion

There were two solutions suggested by RAN4 to avoid potential risks. We show our views on these solutions in the sub-clauses below [..]

In this contribution we introduced our views to the proposed solutions in LS R4-2005205. The conclusions are listed below.

Proposal 1: For FR1, the PDCCH Aggregation Level in TS 38.521-1[2] C.3-Connection is configured as table 2.1-1.

Proposal 2: For FR2, the PDCCH Aggregation Level in TS 38.521-2[3] C.3-Connection is configured as table 2.1-2.

Proposal 3: Modify the nrofcandidates of SearchSpace in TS 38.508-1 [4] for AL=1, AL=8 and AL=16 to n2.

Proposal 4: Modify frequencyDomainResources in TS 38.508-1 [4] to align with candidates for AL=8 and AL=16.

Proposal 5: Removing both edge PDCCH allocations from full bandwidth isn’t implemented.

Discussion:

Comments from Keysight Spain on Proposals 3 and 4.

Qualcomm commented that if really necessary a phased case for ACS only could be considered.

RAN5 Vice Chair: are the 3 tests only RF tests?

No changes to DMOD or RRM. Only -1 and -2 specs, plus 38.508-1 for RRM.

Conclusion: changes only for the ACS test!

Keysight Spain: then the change in 38.508-1 is not required.

r1

Decision: 		The document was revised to R5-204721.

R5-204721	Discussion about proposals in LS R4-2005205

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

(Replaces R5-203686)

Discussion:

noted and proposals endorsed and implemented in CRs.

Decision: 		The document was noted.

R5-203819	Discussion on PCC prioritization for FR1 and FR2 UL CA testing

Type: discussion		For: Discussion
					Source: Qualcomm Inc, Verizon Inc.

Abstract:

The purpose of this discussion paper is to discuss 5G NR PCC prioritization configuration for FR1 and FR2 UL CA testing.

This paper provides background for a potential discrepancy across 3GPP RAN 1, RAN 4 and RAN 5 TS regarding 5G NR PCC and SCC power allocation during FR1 and FR2 UL CA testing.

Observation 1: RAN 5 test points are intended to be tested in their worst cases configuration. Currently for all UL CA test cases a UE under test gets configured to prioritize PCC (per RAN 1 spec). This results in no power being allocated to SCC. Thus all FR1 and FR2 UL CA test cases that require configuring maximum power (worst case) for all CCs are not being tested as intended.

Proposal 1: For all UL CA test cases add following editor’s note: “Incomplete as tests prioritize power allocation to PCC resulting in no power in SCC. PCC prioritization needs to be disabled for UL CA testing”.

Proposal 2: RAN 5 to discuss and design a new dedicated test mode signaling to be used in the test procedure of UL CA tests to allow disabling of PCC prioritization in a test mode as opposed to mission mode of operation where PCC has prioritization.

Discussion:

Orange: we have to not only test the requirements from RAN4 but also the network behaviour.

Rohde&Schwarz: check which requirements need the UL PCC.

Huawei: allow UE transmit only on PCCCH.

Ericsson: do like for power control tests.

CMCC: consider a case by case basis.

Deferred.

Discuss 5G NR PCC prioritization issue (SCC starves) for FR1 and FR2 UL CA testing

RF session1 comments:

Anritsu has a parallel paper in RAN4 impacting prop1 , in terms of which requirements needs uniform power and which do not, which will change the number of RAN5 tests having this impact.

KEYS: Is Operator view of testing without prioriization OK from conformance POV

Orange: More discussion needed on how to have UE's tested in conformance the way they are deployed.

R&S: Check which RAN4 requirements need the UL PCC prio disabled to get to the goal of the test

Huawei: Aligns with orange view

E///: if RAN4 requirements are designed with equal power , then we shlud align the PSD before starting the test but complication of test procedure is to be evaluated.

CMCC: aligns with R&S view

Qualcomm to initiate a discussion on Prop2 via email , wait for prop1 before concluding on the tests.

Noted no proposals endorsed

Decision: 		The document was noted.

R5-203868	Discussion on Scope, Purpose and drafting guideline for 38.522

Type: discussion		For: Endorsement
					38.522 v..
					Source: CAICT

Abstract:

Corresponding CR: R5-203869.

During RAN5#87-e there was an email discussion about scope, purpose and drafting guideline for TS 38.522, but no formal agreement was achieved. Moreover no agreement could be reached on how to handle“Tested Bands” column and “Branch” column at RAN5#87-e, the disagreement is essentially about Scope, Purpose and drafting guideline for 38.522, such as what information shall be put in TS 38.522 and how to put the information in TS 38.522.

This paper highlights the scope and purpose of 38.522 according to the current definition in 38.522 (Scope in section 1 & definition of each column in the beginning of section 4), proposes to correct some corresponding incorrect or ambiguous content in 38.522, and also provides some drafting guidelines for TS 38.522.

Observation 1: The first paragraph in section 1 Scope of 38.522 is incorrect as Implementation Conformance Statement (ICS) proforma for 5G New Radio (NR) User Equipment (UE) is provided in 38.508-2, not in 38.522.

Proposal 1: Delete the first paragraph in section 1 Scope of 38.522.

Observation 2: Scope of 38.522 is applicability statement for test cases based on the features implemented in the UE.

Observation 3: Current 38.522 includes some information (underlined part) that has nothing to do with applicability statement for test cases based on the features implemented in the UE.

Observation 3a: NOTE 1 is too general to identify the principle of a test case to be considered as complete or incomplete, this ambiguity will lead to misunderstanding among both the test case owners and the spec readers.

Proposal 2: Revise Scope of 38.522 and definition of “Additional Information” column to include completion status of test cases. Revise NOTE1 to include the clear principle for a test case to be considered as complete or incomplete.

Observation 3b: NOTE 2 basically shall also be considered as incomplete and has been included in NOTE1. Moreover 38.522 shall not include TCs which RAN5 has decided not to be included in 38.522 because of testability issue.

Observation 3c: Based on 38.522, all the supported bands belong to the “Tested Bands / CA/DC Configurations Selection” column will be selected for each test case, so NOTE 4 is just for emphasizing for test case selecting considering test verdict given. RAN5 has sent LS to RAN4 for MBR issue and RAN4 has different solutions in the Rel-15 and Rel-16 CRs which make NOTE 4 not accurate and not easy to be summarized in one NOTE. Basically this emphasizing is only better to have as 38.522 can select test cases correctly without this emphasizing. Moreover 38.521-x or 38.533 is enough for test requirement and test verdict given.

Observation 3d: All E-UTRA standalone TCs in TS 36.521-1 shall be tested, not only the TCs with NOTE 5.

Proposal 2a: Remove NOTE 2 and NOTE 4. Remove “E-UTRA is tested standalone using TS 36.521-1.” from NOTE 5.

Observation 4: Notations “R”, “O”,  and “N/A” are not defined in Table 4.0-1, only “Ci” is defined in Table 4.0-1, “Ci” is not defined immediately following the table.

Proposal 3: Delete the first underlined part and update the second underlined part to “in Table 4.0-1”.

Observation 5: The syntax "IF (... OR ...) …AND  ... THEN … ELSE ..." is used for the nested conditional expressions of Ci. The nested conditional expressions of Ci shall avoid ambiguities. The definition of “Condition” column shows no purpose to separate multiple conditions just to emphasize that the same test case supports multiple features.

Observation 6: Introducing multiple conditions to one same test case (without branch) has no benefit for test case selecting but will lead to ambiguities; people will be confused about the syntax for applicability of that test case, “C39a AND C39b”, or “C39a OR C39b”? Similar story is about introducing multiple band sets to one same test case.

Observation 7: “Tested Bands / CA/DC Configurations Selection” column defines a set of bands / CA/DC Configurations the test is to be run for, if the test is applicable. The syntax "(... OR ...) …AND..." is used for the nested conditional expressions of notations of Tested Bands / CA/DC Configurations. The definition of “Tested Bands / CA/DC Configurations Selection” column shows no purpose to separate multiple band sets just to emphasize that the same test case supports multiple features.

Observation 8: The “Condition” and “Tested Bands / CA/DC Configurations Selection” column are in the format of Cxx, Dxx or Exx, using the syntax "(... OR ...) …AND..." for the nested expressions of notations. The purpose of duplicating the applicability statement for the test cases to 38.522 is mainly for the convenience of software reading to improve the efficiency of test cases selecting for a curtain UE.

Observation 9: The “Branch” column is introduced to meet the validation requirements from certification bodies as there is a need to uniquely reference branch for certain test case because of TE implementation. The branch concept is used on an absolutely need basis, if TE implementation and validation does not require branch, the branch column shall not be introduced. CAG63 decided to introduce the branch concept for 4Rx/2Rx, and still has no conclusion for PC2/PC3.

Proposal 4: Remove the branches of PC2&PC3 from 38.522 as there is no explicit demand from certification bodies for TE implementation and validation so far. Introduce new conditions for 2Rx/4Rx to make the condition accurate for applicability statement of branch.

Observation 10: Introducing multiple band sets to one same test case will lead to ambiguities; people will be confused about the syntax for the set of bands the test is to be run for, “D001 AND D002”, or “D001 OR D002”? It seems that the syntax shall be “D001 OR D002”. As band set D001 already includes D002, the syntax “D001 OR D002” is not necessary.

Proposal 5: Remove the unnecessary D002 from test band column to avoid introducing multiple unnecessary ambiguous band sets to one same test case.

Observation 10a: “Tested Bands/CA/DC-Configurations Selection” definitions for CA TCs in 38.521-1 and EN-DC TCs in 38.521-3 are not accurate. Notations “Ei” shall be used for CA/DC Configurations Selection Criteria instead of “Di”. EN-DC TCs in 38.521-3 are separated into intra-band contiguous EN-DC in FR1 (2 CCs), intra-band non-contiguous EN-DC in FR1 (2 CCs), inter-band EN-DC within FR1 (2 CCs), and so on. 38.508-2 has Baseline Implementation Capabilities for Intra-band contiguous EN-DC in FR1, Intra-band non-contiguous EN-DC in FR1, Inter-band EN-DC within FR1 (two bands) and so on.

Observation 10b: Definitions of Condition C009,C010,C011,C012,C009m, C010m,C011m,C012m include EN-DC and NE-DC, while the Comments for C009,C010,C011,C012,C009m, C010m,C011m,C012m only include EN-NC. Definitions of Condition C009,C010,C011,C012,C009m, C010m,C011m,C012m are not separated based on scope of test cases for different number of UL or DL CCs.

Proposal 5a: Use notations “Ei” for CA/DC Configurations Selection Criteria instead of “Di”. “Tested Bands/CA/DC-Configurations Selection” definitions shall be separated based on the scope of the test case and the definition of Baseline Implementation Capabilities in 38.508-2 correspondingly for accuracy.

Proposal 5b: Revise the definitions of Condition C009,C010,C011,C012,C009m, C010m,C011m,C012m to only include EN-DC and separate the Conditions based on scope of test cases for different number of UL or DL CCs.

Observation 11: "Comments" column contains a verbal description of the "Condition" column, which means condition "C001" shall have only one same comment. The current spec has two different comments for the same condition "C001": UEs supporting 5GS FR1 and UEs supporting 5GS FR1 PC3.

Observation 11a: “Comment” column of 6.2.3 and “Additional Information” column of 6.2.4 are not aligned with 38.521-1.

Proposal 6: Revise “Comment” column of 6.2.3 to “UEs supporting 5GS FR1” and remove “PC3 requirements applied” from “Additional Information” column of 6.2.4 to align with 38.521-1. Introduce new conditions for PC2/PC3 to make the condition accurate for applicability statement of test case.

Observation 12: "Additional Information" defines the exceptions because of UE capabilities and the measurement execution. "Additional Information" column is not the comment for "Condition" column.

Proposal 7: Remove “PC3 requirements applied” from "Additional Information" column of 6.5.2.4.2.

Proposal 8: Revise 6.2D.1 in 38.521-1 to make MPR=1.5dB as MOP test points and test requirements as suggested by RAN4. Revise the NOTE in the Test applicability section of 6.2D.1 in 38.521-1 to “Test execution is not necessary if 1.5dB MPR test points in TS 38.521-1 6.2D.2 are executed.” Replace “Maximum Output Power for UL-MIMO is tested as part of the MPR test case with using MPR=1.5dB suggested by RAN4.” to “Test execution is not necessary if 1.5dB MPR test points in TS 38.521-1 6.2D.2 are executed.” in the "Additional Information" column of 6.2D.1 of Table 4.1.1-1  in 38.822.

Proposal 9: Drafting guideline for 38.522:

1.	Information that has nothing to do with test cases applicability statement based on the features implemented in the UE and completion status for test cases shall not be duplicated to 38.522.

2.	Multiple conditions or multiple band sets shall not be introduced to one same test case (without branch) just to emphasize that the same test supports multiple features. In this case the multiple conditions or multiple band sets shall be combined to one condition notation or one band set notation using the syntax “... OR ...” in Table 4.0 to avoid ambiguities.

3.	Applicability statement for test cases based on the features implemented in the UE shall be in the “Condition” and “Tested Bands / CA/DC Configurations Selection” columns in the format of Cxx, Dxx or Exx, which are mainly for the convenience of software reading to improve the efficiency of test cases selecting for a curtain UE. Applicability statement for test cases based on the features implemented in the UE shall not be in the “Additional Information" column in the format of a Note which is not for the convenience of software reading and will not improve the efficiency of test cases selecting for a curtain UE.

4.	Each “Condition” notation shall have only one same “Comment” throughout 38.522, multiple different comments for one same “Condition” notation shall not be permitted.

5.	The branch concept shall be used on an absolutely need basis (mandatory for TE implementation and validation), if TE implementation and validation does not require branch from certification bodies, the branch concept shall not be introduced.

6.	In order to facilitate branch selecting, different conditions or band sets shall be introduced for applicability statement for Branches based on the features implemented in the UE.

Discussion:

already long discussions had taken place.

Bureau Veritas wondered regarding proposal 2 how the features are configured in the test cases. Note 1 can be removed.

Anritsu: proposal 9 has some conflicting information.

Rohde&Schwarz: TE POV are not needed here.

Qualcomm: better keep the 2 branches 2Rx 4Rx as they are and add a note.

Dish: branching is not needed in RAN5 spec.

Ericsson: all the test cases woud need to be re-validated. Not call it branch but feature list.

CMCC: branches are needed, it is the only way for certification bodies to validate.

Deferred.

Proposal 8 was not endorsed.

r2

Decision: 		The document was revised to R5-204951.

R5-204951	Discussion on Scope, Purpose and drafting guideline for 38.522

Type: discussion		For: Endorsement
					38.522 v..
					Source: CAICT

(Replaces R5-203868)

Decision: 		The document was noted.

R5-203972	Discussion on QZ size

Type: discussion		For: Information
					Source: Huawei, HiSilicon

Decision: 		The document was withdrawn.

R5-204022	Discussion on FR2 absolute power control MU

Type: discussion		For: Discussion
					Source: Samsung R&D Institute UK

Discussion:

AP assigned: For FR2 absolute power control test cases analyze to determine if we can test both upper and lower limits with a very large span when the aggregated BW is smaller than or equal to 400 MHz. Supporting: Samsung, E///, Anritsu, Keysight, R&S, Huawei

Decision: 		The document was noted.

R5-204027	Discussion on remaining parameters for FR2 EIRP Tx OFF power MU

Type: discussion		For: Discussion
					Source: Samsung R&D Institute UK

Abstract:

It was decided at previous meetings to include an editor’s note for “testability of OFF power needs further study” [1] in all test cases that are dependent on EIRP OFF power that consist of the following test cases:

•	6.3.3.2: General ON/OFF time mask

•	6.3A.3.1: Transmit ON/OFF time mask for CA (2UL CA)

•	6.3D.3.1: General ON/OFF time mask for UL MIMO

•	6.3D.3.4: SRS time mask for UL MIMO

The test cases listed above minimum conformance requirements are as such: [..]

At RAN5#87-e meeting EIRP measurements for Transmit OFF power was included to Annex B.8 [2]. However, there are still some remaining parameters for FR2 EIRP Tx OFF power MU that are still open. In this contribution, we briefly discuss and provide our views and recommendations for some of the remaining parameters concerning FR2 EIRP Tx OFF power.

In this contribution, we further discussed our views on some of the remaining parameters for FR2 EIRP Tx OFF power MU that are still open. Based on the discussion, our observation and proposals are summarized as follows:

Proposal 1: Agree to the MU threshold for EIRP measurement for Transmit OFF power values with brackets.

Proposal 2: Set Uncertainty of the Network Analyzer as 1.5dB for FR2 EIRP OFF Power MU and Standard uncertainty as 0.75 dB and remove the brackets.

Proposal 3: Set Influence of noise to reference ACLR Table B.17.2-3 for FR2 EIRP OFF Power MU.

Proposal 4: Set EIRP Expanded uncertainty to [5.09] with brackets + influence of noise to be in alignment with ACLR.

Proposal 5: Set FR2 EIRP OFF Power TT = 0.65xMU.

Proposal 6: Test proposals 1-5 are agreed to be included in TR38.903.

Discussion:

Qualcomm: Can European operators comment on the removal of brackets for the relaxation amounts due to regulatory body concerns? Should we consider some test procedure/conditions to reduce the relaxation.

Keysight: we kept brackets on relaxation amounts in our proposal as this is the first meeting. We could consider skipping Tx Off power.

Samsung: this is also being used to address the off power in the transient tests.

Noted, proposal 1&2 endorsed.

Decision: 		The document was noted.

R5-204042	Discussion on multi-band relaxation framework requirement enhancement

Type: discussion		For: Discussion
					Source: Samsung R&D Institute UK

Abstract:

At RAN5#85, a LS on multiband relaxation for FR2 in [1] asking RAN4 to consider defining an upper limit of MBR (either ΔMBP or ∑MBP) which will be of high value for RAN5 when defining measurement uncertainty or to consider MBR per band instead of summation across all bands. At RAN4#95e meeting, a LS response on multiband relaxation for FR2 in [2] was approved by RAN4 based on further testability analysis of MBR.

RAN4 asked RAN5 to take the information below into consideration concerning the Release 15 and Release 16 MBR requirements: [..]

In this contribution, we briefly discuss and provide our view on Release 15 and Release 16 MBR requirements.

In this contribution, we further discussed our views on Release 15 and Release 16 MBR requirements and related test cases. Based on the discussion, our observation and proposal are summarized as follows:

Observation 1: The MBR definition factors currently defined in TR 38.903 [7] are no longer valid for Release 16 since MB is an obsolete definition as it has been removed.

Proposal 1: Update the MBR definition in the calculation method to account for the changes to the MBR framework requirements in RAN4.

Discussion:

is endorsed.

Decision: 		The document was noted.

R5-204081	On AWGN and signal flatness uncertainty for FR2 Performance tests

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In [2], frequency flatness uncertainty is proposed in RAN5#87e however that was not endorsed due to some TEV’s requested for double-checking the value. This paper (re)propose the DL signal flatness uncertainty and also mention the sensitivity factor for the flatness uncertainty used for FR2 perf test.

RAN5 is asked to endorse following proposals.

Proposal 1: Apply +/-3.0 dB(1.96sigma) for MU term of AWGN and signal flatness for both FR2a and FR2b for up to 400MHz.

Proposal 2: Apply x0.25 sensitivity factor for frequency faltness of signal and AWGN for FR2 performance test cases.

Discussion:

"8/21: will make final conclusion after decision on R5-204271.

8/25: Proposal 2 can be endorsed.

Noted, proposla 2 endorsed"

Decision: 		The document was noted.

R5-204082	On FR2 DL absolute level uncertainty for DFF.

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In FR2 RRM, DFF(or Hybrid) is listed as available test method for RRM, however no estimation of total MU for DFF has been provided in RAN5 which prevents the TT analysis where the common MU among all test methodology regardless of test method or their test case types(1AoA, 2AoA) is desired. With this background, in this paper, we provide our view on the FR2 DL absolute level uncertainty for DFF.

In this contribution, we present our view on the FR2 DL absolute level uncertainty

Observation 1 : Impact from finite far field measurement distance(Measurement distance uncertainty and phase curvature) is estimated with in the order of +/- 0.15  ~ +/- 0.5 dB

Observation 2 : Need to clarify which MU element (Measurement distance uncertainty/phase curvature) applies and which is set to 0.

Observation 3: The total FR2 DFF MU is close to 6.0dB rather than 5.0dB, and it could be bigger than 6.0dB depending on the final QoQZ value.

Proposal 1 : For FR2 DFF MU, reuse green highlighted values in Table 1 from FR2 IFF MU budget table

Proposal 2 : For FR2 DFF MU, reuse blue highlighted values in Table 1 from FR2 IFF MU budget table

Proposal 3 : Adopt +/- 0.30dB for “Phase centre offset of calibration” for DFF budget table.

Recommendation 1 : Concerning parties are encouraged to provide analysis for remaining FR2 DFF MU elements, especially quality of quiet zone value.

Discussion:

r1

Keysight Spain: mismatch value can be reused for DFF.

r2

Decision: 		The document was revised to R5-204745.

R5-204745	On FR2 DL absolute level uncertainty for DFF.

Type: discussion		For: Endorsement
					Source: Anritsu

(Replaces R5-204082)

Discussion:

"Revised from: R5-204082r2.

Noted, proposals endorsed

"

Decision: 		The document was noted.

R5-204083	On gNB emulator fading model impairments for FR2 Performance tests

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In this paper we propose gNB emulator fading model impairments uncertainty for FR2 demodulation test case.

RAN5 is asked to endorse following proposals.

Proposal 1: Apply +/- 0.5dB for 1Tx and +/- 0.7dB for 2Tx for gNB emulator fading impairments.

Discussion:

Qualcomm: do you consider a separate term for the fading uncertainty?

Anritsu: suggesting same approach as LTE. Just different naming.

AT&T: Proposal can be endorsed.

Noted proposal endorsed

Decision: 		The document was noted.

R5-204084	On FR2 ACS and IBB Test Implementation and MU

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In this paper, we discuss the FR2 ACS and IBB implementation variations and how to define MUs in RAN5.

We present our view for the implementation variation of blocker test and MU definitions.

Following observations are made in this paper.

Observation 1 : Wanted signal and interfering(blocker) signal is not necessarily emitted from the same physical antenna. Implementation using slightly offset antenna can be discussed as part of MU discussion in RAN5 from practical implementation PoV.

Regarding the need of offset antenna use for blocker signal, following observations (reasons) are made.

Observation 2 : Offset antenna approach does not give impact to the signal path of the wanted signal which is the primary path for all the test cases other than blocking test. This is very important aspect when test system used in e.g. regulatory test(as early stage demand) is rectified to support blocker test with minimum impact.

Observation 3 : Additional combiner in the RF path would reduce the dynamic range of the test system where the dynamic range is very precious in FR2 OTA test system as discussed ever for low PSD/high Power test case testability topics in RAN5. In this situation, sacrificing the dynamic range due to the very small number of test case would not a reasonable choice from our PoV.

Observation 4 : Independence of signal path is more promising for less complexity and more scalability than having tightly combined paths from long term perspective. It should be noted RAN5 anyway already permitted offset antenna for spurious emission test, then having offset antenna itself is not a serious issue from complexity perspective.

Observation 5 : As blocker test is to test the DUT’s capability of filtering or intermodulation inside a UE RF frontend, then the blocker’s power level that UE RF frontend receives is the primary matter rather than the angle of arrival.

Observation 6 : The UE reception power reduction from offset angle can be compensated at some extent. Details need to be studied further.

RAN5 is asked to endorse followings.

Proposal 1 : RAN5 to study the MU of blocker test case considering the implementation of Type 1, 2 and 3.

Proposal 2 : As long as the MTSU is met, all the implementation Type 1, 2 or 3 are allowed. Which case the MTSU value is finalized is determined on the way to finalize the MU.

Discussion:

R&S: we have different understanding from Anritsu of RAN4 requirement. Not sure that the UE antenna delta for the offset can be compensated. MU for RSRP is quite large due to the linearity. RAN4 is the right place to decide if this is an appropriate test method. Relative approach cannot be done here as in KS paper and will lead to increased MU.

KS: RAN5 could evaluate the offset antenna approach to determine the tradeoff in MU and testability. Need to understand how much this would deviate from the requirements.

Anritsu: could ask RAN4 after RAN5 understands the impact. Cannot assume any correlation with wanted/interferer signal for IBB test case so MU would similar between Type 2 and Type 3 implementation. Don't use RSRP but use EIS. Relative differences could be measured accurately. Don't see that a 10 degree offset is required for the IBB test and offset angle could be much smaller. Existing RF test cases will be affected by adding blocker to wanted signal path.

AT&T: Proposal 1 can be endorsed.

Noted , Prop1 endorsed

Decision: 		The document was noted.

R5-204085	On FR2 OBW MU

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

OBW MUs have been discussed in [1-16] but no conclusion was reached as of now. In [9], action item for UE/Chip vendors for the spectrum assumption for deriving the OBW MUs are made, and the reference spectrum is provided in [10]. In RAN5#86e, OBW MU analyses based on the reference spectrum [10] are provided [11]-[16]. This paper provide the simulation result and proposes MU for FR2 OBW considering the discussions in RAN5#87-e.

In this paper FR2 OBW MU and testability limit is studied based on the previous discussions.

Following observations are made.

Observation 1 : For 100MHz and below, 2.0[%CBW] error is reasonable choice.

Observation 2 : For 400MHz BW, by setting OBW measurement span to 28GHz, the OBWsignal (w/o noise/ripple) is now 397.8MHz(1.5x BW) or 398.6MHz(2.0x BW), then there is only 2.2MHz or 1.4MHz margin from core requirement.

Observation 3 : For 400MHz BW, even  though SNR is enough good(40dB), 97.5% tile value excess the upper limit of measurement error.

Observation 4 : The current MU evaluation assumption may have a gap from typical situation(UE performance, TE performance)

RAN5 is asked to endorse following proposals.

Proposal 1 : Define OBW Measurement Error based with (OBWmeas - OBWsignal) / CBW *100 [%CBW]

Proposal 2 : Agree on the Table 2 for FR2 OBW MTSU/measurement span

Discussion:

r3

Decision: 		The document was revised to R5-204849.

R5-204849	On FR2 OBW MU

Type: discussion		For: Endorsement
					Source: Anritsu

(Replaces R5-204085)

Discussion:

"Revised from: R5-204085r3.

noted and proposal 1 is endorsed

"

Decision: 		The document was noted.

R5-204086	Noise impact for FR2 test case where MPR applies

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

This paper provides the SNR estimations for FR2 test cases for MPR and ACLR, and proposes the testability limit and MU value for “influence of noise”.

RAN5 is asked to endorse following proposals.

Proposal 1 : For FR2 MPR test case, apply SNR=0.2dB for FR2a and SNR=0.4dB for FR2b for MPR test case up to 400MHz aggregated BW for PC3

Proposal 2 : For FR2 ACLR test case, test FR2 ACLR without relaxation for the configuration with MPR not greater than the values in Table 2.

Proposal 3 : For FR2 ACLR test case for FR2a, apply the relaxation of (MPR for test points – value in Table 2) > 0 for dBc value.

Proposal 4 : For FR2 ACLR test case for FR2b, do not test the test points with MPR values bigger than Table 2

Proposal 5 : Apply SNR in Table 3 for FR2 ACLR for up to 400MHz aggregated BW for PC3.

Discussion:

Proposals are endorsed.

r2

Decision: 		The document was revised to R5-204746.

R5-204746	Noise impact for FR2 test case where MPR applies

Type: discussion		For: Endorsement
					Source: Anritsu

(Replaces R5-204086)

Discussion:

"Revised from: R5-204086r2.

Noted, proposals endorsed"

Decision: 		The document was noted.

R5-204087	On MU for FR2 MPR Test

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

This paper proposes the measurement uncertainty for FR2 MPR test case. Though the MPR test is categorized in P3 test, as it is tightly relating to P2 test ACLR and SEM, it should be prioritized as well.

Proposal 1 : For FR2 MPR test, apply the same MU budget as for EIRP MOP except for the “influence of noise”.

Discussion:

Proposal 1 is endorsed.

Decision: 		The document was noted.

R5-204088	On frequency flatness uncertainty for FR2 RRM and Performance tests

Type: discussion		For: Endorsement
					Source: Anritsu

Decision: 		The document was withdrawn.

R5-204089	On gNB emulator SNR uncertainty for FR2

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In RAN5#87e, FR2 gNB emulator SNR Uncertainty was proposed in [1] and proposals endorsed. The gNB emulator SNR uncertainty value itself was agreed with [0.3dB] for double checking from other TEVs. This paper is resubmission of [1] to fix the “gNB emulator SNR uncertainty”. Some detailed background information described already in [1] is omitted in this paper.

RAN5 is asked to endorse following proposal.

Proposal 1 : For baseband-combining approach and for up to DL 64QAM, apply +/-0.3dB(1.96sigma)  for FR2a and FR2b for up to 400MHz BW for” gNB emulator SNR uncertainty”.

Discussion:

AT&T: Proposal can be endorsed.

Noted and proposal endorsed.

Decision: 		The document was noted.

R5-204090	Proposal of MUs for FR2 spurious emission UE co-existence

Type: discussion		For: Endorsement
					Source: Anritsu

Abstract:

In this contribution, we present our view on the MU value for FR2 spurious UE-coexisting test.

Followings are observed:

Observation 1 : The same MU values as General spurious emission can be applied for spurious UE co-existence for corresponding frequency range except for influence of noise.

RAN5 is asked to endorse following proposals.

Proposal 1: For PC3 spurious emission UE-coexistence (protected=n260, aggressor=n257 and n261), apply the same MU values as general spurious for f=23.45 GHz to 40.8 GHz except for DSNR which was agreed in [1]

Proposal 2: For PC3 spurious emission UE-coexistence (protected=n257/n261, aggressor=n250), apply the same MU values as general spurious for f=23.45 GHz to 40.8 GHz except for DSNR which was agreed in [1]

Proposal 3: For PC3 spurious emission UE-coexistence (protected=57 GHz ≤ f  ≤  66GHz), apply the same MU values as general spurious for f= 40.8 GHz to 66 GHz

Proposal 4 : For PC3 spurious emission UE-coexistence (protected=57 GHz ≤ f  ≤  66GHz), apply DSNR=1.0dB with no relaxation for core requirement. (Just removing [ ])

Discussion:

"8/21: Need to confirm status with ourcome of R5-204293.

8/25: Proponent confirmed that the content is covered by the KS paper in R5-204293 and this paper can be noted."

Decision: 		The document was noted.

R5-204136	Review on FR1 TRx test point analysis for Extreme Condition

Type: discussion		For: Endorsement
					38.521-1 v..
					Source: DOCOMO Communications Lab.

Abstract:

The purpose of this contribution is to review existing test point analysis for Extreme condition and to discuss the necessity of optimization.

2	Discussion

3GPP compliant UEs shall fulfil all RF core requirements not only in NC (Normal Condition) but also in EC (Extreme Temperature, Voltage) according to the Annex E of core specification [2].

Regarding temperature/voltage depended test cases, in RAN5, (1) are tested for each test ID. This makes some test cases much larger in terms of number of the test points.

Total test point (including testing time) can be reduced if we can optimize these EC test points. Following figures describe some options for optimization. RAN5 can adopt these options if we prove applicability or reasonability to skip specific EC test points (purple highlighted) with technical justification.

	(b) Option 1	: Test EC with some test ID (e.g. #01, 05), and test only NC with the other test IDs

	(c) Option 2	: Test only corner cases (TL/VL, TH/VH) and skip TL/VH and TH/VL

Observation 1	: EC is fully tested in the current approach and there is a chance to optimize EC test points.

Therefore, it is proposed that UE vendors provide technical justification in order to make the analysis of EC test points more meaningful.

Proposal 1	:  UE vendors to provide technical justification for whether Option 1 or Option 2 is applicable in FR1 RF tests.

Discussion:

Qualcomm: it is good to reduce those conditions which is time consuming. Prefer option 2.

Huawei: high temp plus low voltage would be a more critical scenario. Agree with Ericsson and Qualcomm. Test 1-8 is belonging to one test or several?

NTT DOCOMO: need to check.

Keysight Spain wanted to remind that also RRM measurement performance, using EC testing would be a similar case t be considered.

Deferred.

r1

Decision: 		The document was revised to R5-204952.

R5-204952	Review on FR1 TRx test point analysis for Extreme Condition

Type: discussion		For: Endorsement
					38.521-1 v..
					Source: DOCOMO Communications Lab.

(Replaces R5-204136)

Discussion:

"Revised from: R5-204136r1.

noted , prop1  further analysis is needed

"

Decision: 		The document was noted.

R5-204186	On Beam Peak Searches for different test configurations

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

This contribution addresses the need to perform TX and RX beam peak searches for different test configurations.

The following observations and proposals were made in this contribution

Observation 1: Whether the beam peak searches need to be performed for different channel bandwidths, SCS, modulation, waveforms has not been decided yet.

Observation 2: The beam peak results at the reference beam peak direction do not change between different modulations and waveforms

Proposal 1: Beam peak searches shall be performed for every CBW and SCS by default.

Proposal 2: Beam peak searches shall be performed for every modulation by default unless the device manufacturer explicitly declares that the beam peak at the QPSK modulation is applicable for the remaining 16QAM and 64QAM modulation

Proposal 3: Beam peak searches shall be performed for every waveform by default unless the device manufacturer explicitly declares that the beam peak from one waveform is applicable for the other waveform.

Discussion:

CRs R5-204187-8.

"This contribution addresses the need to perform TX and RX beam peak searches for different test configurations.

RF session1 comment

R5-204188, R5-204187 related CR's implementing prop1 , can be updated to include prop2/3

Qualcomm: supports the proposals1/2/3

Could be noted and Prop1/2//3 endorsed and implemented in 4188r1, 4187

noted and Prop1/2//3 endorsed and implemented in 4188r1, 4187"

Decision: 		The document was noted.

R5-204189	Preliminary QoQZ and EIRP MU results for ETC testing

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

This contribution is providing preliminary QoQZ and EIRP MU values for a test system capable of full 3D testing under ETC.

Discussion:

r1

Modified proposal 1 based on feedback received by R&S

Decision: 		The document was revised to R5-204739.

R5-204739	Preliminary QoQZ and EIRP MU results for ETC testing

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-204189)

Discussion:

Noted , Proposal endorsed

Decision: 		The document was noted.

R5-204191	On Larger Quiet Zone Sizes

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

This contribution addresses the need for larger quiet zone sizes and provides our view on this topic.

The following observations and proposals were made in this contribution

Observation 1: It is desirable to limit the total number of quiet zone sizes

Observation 2: It is unknown which quiet zone size will guarantee a 100% coverage for PC3 and PC1 devices.

Observation 3: A grey-box approach, i.e., declaration of a reference point to be aligned with the centre of the quiet zone and the maximum antenna panel displacement from this reference point, could significantly increase test case coverage and allow more compact FR2 OTA system sizes.

Proposal 1: RAN5 to strive for 100% test coverage for PC1 and PC3 devices and close AP#87e.22

Proposal 2: Hold off on defining a quiet zone larger than 30cm until sufficient feedback has been received on AP#87e.24 and AP#87e.23

Discussion:

Proposals were modified based on feedback from R&S.

r1, not needed.

Decision: 		The document was revised to R5-204747.

R5-204747	On Larger Quiet Zone Sizes

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-204191)

Discussion:

"Revised from: R5-204191r2.

Noted, proposals endorsed

"

Decision: 		The document was noted.

R5-204192	QoQZ Verification Clarification

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

The Quality of Quiet Zone (QoQZ) procedure has been defined initially in [1] and was later incorporated in [2]. After further review of the procedure, additional clarifications are needed.

Discussion:

The Quality of Quiet Zone (QoQZ) procedure has been defined initially in [1] and was later incorporated in [2]. After further review of the procedure, additional clarifications are needed.

8/24: no comments received.

Noted and  proposals endorsed

Decision: 		The document was noted.

R5-204194	On Re-Positioning Concept for RRM 2 AoA QoQZ Validation and DFF QoQZ MU

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

This contribution is addressing the need to clarify the re-positioning concept for QoQZ validation applied to RRM 2 AoA testing. Additionally, sample values of DFF QoQZ MU for 2 AoA RRM are presented.

The following observations and proposals were made in this contribution

Observation 1: The re-positioning approach for the QoQZ is generally not applicable to RRM 2 AoA testing

Proposal 1: It is proposed that the QoQZ validation and MTSU for RRM 2 AoA test cases does not consider the re-positioning concept.

Proposal 2: Set the MU element of Quality of Quiet Zone for FR2_A, FR2_B, and FR2_C to 1.2dB for Stage 2 and to 0.3dB for Stage 1 for 2 AoA RRM test cases based on DFF implementation.

Discussion:

draft r1 was presented.

This contribution is addressing the need to clarify the re-positioning concept for QoQZ validation applied to RRM 2 AoA testing. Additionally, sample values of DFF QoQZ MU for 2 AoA RRM are presented.

8/17: Offline discussions are occurring.

8/19 FR2 MU GTM#1:

Anritsu: not sure if we can apply the repositioning concept for RRM test cases. Could result in testing only in upper hemisphere. Baseline needs to be without re-positioning approach.

R&S: RAN4 has not specified that we need to test the entire sphere. The baseline should use repositioning approach to achieve lower MU. Most RRM test cases will have to move to position 4 due to power limitations. limited to 150 degrees around the beam peak.

KS: Table 2 shows the differences between repositioning and without repositioning. We are indifferent whether to apply repositioning or not for MTSU.

Anritsu: our understaning of RAN4 requirement is that we test the 2AoA test cases with the entire sphere.

R&S: RAN4 defines the set of angles and the different setups. RRM test cases are single directional and that the direction needs to be randomized. No indication of full sphere.

8/24 FR2 MU GTM#2:

KS: don't see this converging at this meeting.

R&S: share KS opinion.

KS: this can be noted. can also note 3310 from R&S.

AT&T: based on proponent feedback, this paper can be noted.

Noted

Decision: 		The document was noted.

R5-204200	Discussion on size of Quiet Zone above 30cm

Type: discussion		For: Endorsement
					38.521-2 v..
					Source: ROHDE & SCHWARZ

Abstract:

Following the discussion in previous meetings regarding QZ sizes bigger than 30cm in diameter, we present here our views on the next steps.

This is a resubmission of R5-202082 [1] with additional proposals.

In this contribution, the following observations and proposals were made:

Observation 1: The attempt to cover all possible devices sizes with a discrete number of QZ sizes is not a sustainable approach.

Observation 2: ~85% of the devices in the available dataset are covered with a 55cm QZ.

Observation 3: a cylindrical volume defining the maximum size of the DUT becomes a sphere when DUT is rotated.

Observation 4: maximum DUT volume defined as a cylinder has many practical advantages.

Proposal 1: Select 55cm as the QZ size to test devices larger than current QZ limited to 30cm.

Proposal 2: define the QZ size based on the full spherical volume occupied by the DUT.

Proposal 3: for devices not fitting the 30cm QZ, define the maximum DUT volume as a cylinder with 48cm diameter and 26cm height.

Discussion:

Following the discussion in previous meetings regarding QZ sizes bigger than 30cm in diameter, we present here our views on the next steps. This is a resubmission of R5-202082 with additional proposals.

Observation 1: The attempt to cover all possible devices sizes with a discrete number of QZ sizes is not a sustainable approach.

Observation 2: ~85% of the devices in the available dataset are covered with a 55cm QZ.

Observation 3: a cylindrical volume defining the maximum size of the DUT becomes a sphere when DUT is rotated.

Observation 4: maximum DUT volume defined as a cylinder has many practical advantages.

Proposal 1: Select 55cm as the QZ size to test devices larger than current QZ limited to 30cm.

Proposal 2: define the QZ size based on the full spherical volume occupied by the DUT.

Proposal 3: for devices not fitting the 30cm QZ, define the maximum DUT volume as a cylinder with 48cm diameter and 26cm height.

8/17: Offline discussions are occurring on this document and R5-204191.

8/24 FR2 MU GTM#2:

R&S: can note this paper and focus on the proposals from the KS paper.

AT&T: based on proponent feedback, this paper can be noted.

Noted

Decision: 		The document was noted.

R5-204213	Discussion on RAN5 impact of updated Multi-Band Relaxation requirements

Type: discussion		For: Endorsement
					Source: Ericsson

Abstract:

During the last 2 years RAN5 have worked on implementing the multi-band relaxation (MBR) requirements from 38.101-2 resulting in multiple LS exchanges with RAN4 and certification organisations GCF and PTCRB [1-5]. A solution involving multi-band testing in certification and UE declaration of MBR has been decided and implemented for a few test cases. When analysing the solution possible to achieve, RAN5 concluded that multiband relaxation cannot be fully verified in certification [6]. Hence, another LS was sent to RAN4 [5] at RAN5#85 to inform about the problems associated with MBR test implementation.

RAN4 have now changed the MBR requirements and have sent the following response to the LS.

Proposal 1: It is proposed that RAN5 go with option 2 above that completely remove the need of MBR declaration and multiband testing. Since this will impact certification, send LS to GCF and PTCRB to inform of the decision so that they can remove the multi-band testing requirement in certification.

Proposal 2: Update MU calculation in TR38.903 changing the worst case MBR assumption from 1.75 to 0.75 dB.

Discussion:

AT&T: from FR2 MU perspective, P2 can be endorsed.

P1 is not FR2 MU related, need author to initiate discussion with RF group if endorsement is needed.

Noted , Prop2 endorsed, On Wed prop 1 was not endorsed.

Decision: 		The document was noted.

R5-204214	Discussion on EN-DC reference sensitivity test case structure

Type: discussion		For: Endorsement
					Source: Ericsson

Abstract:

At RAN5#87-e meeting, a re-structuring of standalone refsens test cases in 38.521-1 was agreed in [1] with corresponding TP analysis in 38.905 [2]. This re-structuring was the outcome of AP#85.21 “Define framework for NR CA Rx test optimization by re-using higher order fallbacks results”.

Since [1] and [2] only considered standalone test cases, a new AP was created to expand with EN-DC and FR2.

AP#87e.25	Define framework for NR CA (ENDC and FR2) Rx test optimization by re-using higher order fallbacks results	E///, Huawei, Anritsu, Qualcomm, CAICT, Samsung, DCM, CMCC, DISH , WE Certrification	R5-202375

This paper addresses this action point for EN-DC Rx test cases.

This proposal includes a re-structuring of EN-DC Reference Sensitivity test cases in TS38.521-3 as well as a change of test coverage.

In this paper the definitions “default” and “additional” Reference Sensitivity (refsens) test cases that were created as part of AP#85.21 are re-used.

The purpose of “additional” test cases is to verify the exception requirements from 38.101-3. The exception requirement is only defined for two carriers normally where one is the aggressor and one is the victim. For this reason, there is no need for more than a 2CC test case.

The purpose of “default” test cases is to verify the non-exception requirements from 36.101 and 38.101-1. These test cases are defined from 2CC up to the max number of NR CCs possible so that the maximum NR configuration in the UE can be tested.

Discussion:

r3

AT&T: removing the contentious proposals might indicate that it was agreed not to pursue them, which is not accurate.

Decision: 		The document was revised to R5-204953.

R5-204953	Discussion on EN-DC reference sensitivity test case structure

Type: discussion		For: Endorsement
					Source: Ericsson

(Replaces R5-204214)

Discussion:

No agreement could be reached on proposals 1,3,4,7 as listed in R5-204214r3 and hence was adapted in the final R5-204953 to reach consensus , further discussion around these proposals and the deleted items are expected to happen at RAN5#89-e.

Qualcomm would like to mark Proposal 3 and 4 also need further discussion.

Prop1-9 Endorsed and implemented in CR's.

Decision: 		The document was noted.

R5-204253	On FR2 Minimum Output Power relaxation and measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

In RAN5#85, FR2 Transmit OFF power relaxations and impact of noise were agreed in [1] and [2], based on the way forward previously agreed in RAN5#84 in [3] and [4]. This way forward was based on inputs from different TE vendors according to [5], [6], [7] and [8]. Such relaxations were aligned with the statements already drafted in [13].

This document describes an analysis on FR2 Minimum output power feasibility and proposes relaxations and noise impact measurement uncertainty based on a comparison with previous agreements on FR2 Tx OFF power:

Proposal 1: define FR2 Minimum output power relaxation and noise impact as per tables 1 & 2 in this document.

Proposal 2: For PC3 devices, lLeverage from EIRP measurement for FR2 Transmit OFF power (IFF) all MU factor including values except for influence of noise, which should be defined as per tables 1 and 2 above

Discussion:

r2

Proposals 1 and 2 are endorsed.

Decision: 		The document was revised to R5-204740.

R5-204740	On FR2 Minimum Output Power relaxation and measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-204253)

Discussion:

noted, proposals endorsed

Decision: 		The document was noted.

R5-204260	Discussion on DC_41C_n41A and DC_41D_n41A

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

Since no exceptional requirements are defined these combinations would be tested with the anchor agnostic approach, i.e., in exactly the same way as DC_41A_n41A. Since an UE has to support the fallback DC_41A_n41A for these combinations, the test coverage is fulfilled.

The summary is as follows and for further details I refer to the content of the paper:

Observation 1: Exceptional requirements do not exist for DC_41C_n41A and DC_41D_n41A.

Observation 2: Due to the lack of exceptional requirements and the anchor agnostic test approach a test point analysis is not required.

Observation 3: An update of TS 38.521-4 is not required as there are no specific requirements for DC_41C-n41A and DC_41D_n41.

Observation 4: An update of the general section 5 of TS 38.521-3 is not required since the information is already present in the specification.

Proposal 1: Set the status of DC_41C-n41A and DC_41D_n41 as complete in the work plan without updating TS 38.521-3, TS 38.521-4, TR 38.903 and TR 38.905.

Discussion:

r1

Decision: 		The document was revised to R5-204846.

R5-204846	Discussion on DC_41C_n41A and DC_41D_n41A

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

(Replaces R5-204260)

Discussion:

RF closing session: noted and proposal is endorsed.

Decision: 		The document was noted.

R5-204269	On gNB emulator fading model impairments

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

For performance test cases of mode 1, i.e. testing under conditions with external noise, one of the MU contributors is the gNB emulator fading model impairments uncertainty. In this paper we present our assessment of this MU contributor for the baseline approach of baseband combining.

In summary, the uncertainty associated to gNB emulator fading model impairments been analyzed.

Observation 1: The fading model is implemented in the baseband and thus its uncertainty does not depend on the RF frequency range nor other RF characteristics.

Observation 2: For FR1 the MU contributor is called differently and depends on the number of TE Tx ports applied in the test.

Proposal 1: Discuss the interpretation of Fading profile power uncertainty and consider to apply the absolute DL power uncertainty in the test case.

Proposal 2: OEMs/UE vendors to clarify whether the absolute DL power in mode 1 performance test cases has an influence on the throughput.

Proposal 3: Apply a value of ±0.5 dB for the MU contributor gNB emulator fading model impairments for 1Tx and ±0.7 dB for 2Tx.

Discussion:

Anritsu: we need clarification on P1. Absolute level should not matter for performance test case since AWGN level is set and SNR will determine signal level.

R&S: confusion started with the name change. If we clarify that it is only impairments, no clarification for P1 is needed.

KS: P1 needs to more discussion.

QC: Absolute DL power uncertainty does not impact mode 1 Tput performance scenarios with the assumption that SNR is maintained in the test case.

Anritsu: if the absolute power falls, it could fall below the attended amount above the UE noise. need to ensure that it is sufficiently above the UE noise. this may impact the AWGN level that we apply.

KS: we could face some demod test cases with testability issues. for these cases, the test cases will not be able to be tested. Would need to address at that time.

Conclusion: proposal 3 is endorsed.

Decision: 		The document was noted.

R5-204270	On the MU of FR2 OBW

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

The measurement uncertainty (MU) of occupied bandwidth (OBW) has been discussed during the last meetings [1] to [15]. However, no final conclusion has been reached. This contribution is an updated version of the paper submitted to RAN5#87-e [13] with respect to the agreement under TE vendors to apply 28.0 GHz as center frequency for the data provided in [9].

Proposal 1: For the MU due to frequency response apply 1.0% for 50 MHz and 100 MHz CHBWs and 2.1% for 200 MHz and 400 MHz CHBWs.

It has been agreed to apply DFT-s-OFDM as waveform for OBW test in the last meeting in order to optimize the SNR ratio.

In order to combine the MU based due to SNR and frequency response, we propose the following equations: [..]

In the last equation a linear sum is used since the impact of noise is systematic and acts always in the same direction

Proposal 2: Calculate the total MU based on equations (1) to (3).

Discussion:

"8/19 FR2 MU GTM#1:

Anritsu: email sent on R&S paper concerning the equation when SNR is not good.

KS: same comments as Anritsu. Missing feasibility analysis.

R&S: need feedback from QC if the center frequency of the spec analyzer was 28 GHz or the device center frequency.

QC: need to check.

8/20: Further update from QC on center frequency received. ""The spectrum analyzer center frequency was set exactly at 28GHz. The device channel center freq for both 100MHz and 400MHz was 27998.4MHz as per test freq. table from 38.508-1 (1 year older version)."" This requires the simulations to be re-run for all three TE vendors. This also impacts R5-204085 and R5-204294.

8/25: OBW decision deadline will be deferred until 8/26 15:00 UTC to give more time due to late need for revised simulations.

8/26: This paper can be noted with no proposals endorsed."

Decision: 		The document was noted.

R5-204271	On the AWGN flatness and signal flatness

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Abstract:

Associated CRs in R5-204272 and R5-204273.

For performance test cases of mode 1, i.e. testing under conditions with external noise, one of the MU contributors is the Test System Frequency Flatness Uncertainty for AWGN. In this paper, we present our assessment of this MU contributor for the baseline approach of baseband combining.

In summary, the uncertainty associated to AWGN flatness and signal flatness been analyzed.

Proposal 1: Align the name and definition of the MU contributor Test System Frequency Flatness Uncertainty for AWGN to the one of LTE for FR1 and FR2 in TS 38.521-4 and TR 38.903.

Proposal 2: Apply a sensitivity factor of 0.25 in the MU calculation by specifying a divisor of 4 and Actual as the distribution in Table D-1 and Table D-2 of TR 38.903.

Proposal 3: Apply a value of ±3.6 dB for the MU Contributor AWGN flatness and signal flatness.

Discussion:

Anritsu: proposal 1 and 3 are ok.

Keysight: proposal 3 is ok.

noted, proposals endorsed

r1

Decision: 		The document was revised to R5-204748.

R5-204748	On the AWGN flatness and signal flatness

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

(Replaces R5-204271)

Discussion:

"Revised from: R5-204271r1.

Noted, proposal 1 & 3 endorsed

"

Decision: 		The document was noted.

R5-204274	On the SNR for FR2 TRx test cases

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Discussion:

late doc

not available

Decision: 		The document was withdrawn.

R5-204277	On FR2 EIRP OFF Power relaxation and measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd, Samsung

Abstract:

In RAN5#85, FR2 Transmit OFF power relaxations and impact of noise were agreed in [1] and [2], based on the way forward previously agreed in RAN5#84 in [3] and [4]. This way forward was based on inputs from different TE vendors according to [5], [6], [7] and [8]. Such relaxations were aligned with the statements already drafted in [13].

This document describes an analysis on FR2 EIRP OFF output power feasibility and proposes relaxations and noise impact measurement uncertainty based on a comparison with previous agreements on FR2 Tx OFF power (TRP):

Observation 1: EIRP OFF power requirement in PRACH Time Mask test case should be -30 dBm + TT according to core requirement and relaxations should be reviewed (correction over [14])

Proposal 1: define FR2 EIRP OFF power relaxation and noise impact as per table 1 in this document.

Discussion:

Keysight Spain: considering an equipment configuration closer to ACLR.

r1

Endorsed.

Huawei: we need to test on power and off power. Why is off mask a regulatory test case?.

Decision: 		The document was revised to R5-204741.

R5-204741	On FR2 EIRP OFF Power relaxation and measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd, Samsung

Discussion:

late doc

"LATE DOCUMENT

Revised from: R5-204277r1.

noted, proposals endorsed

"

Decision: 		The document was noted.

R5-204282	PC1 Assumptions for CDF Curve for MOP EIRP Spherical Coverage

Type: discussion		For: Endorsement
					Source: Qualcomm Incorporated

Abstract:

This contribution proposes assumptions for PC1 device type, for CDF curve for MOP CIRP Spherical Coverage, as a response to AP coming out of RAN5-87e, R5-202845, Proposal 9.#

Proposal 1: UE Antenna Element Pattern can be refrred from TR 38.803 Table 5.2.3.3-1, with appropriate changes adhering to agreement from R5-198203.

Proposal 2: Assume 120 equally spaced beams with constant density packed in a cone that represents 20% of the area of the sphere.

Discussion:

Anritsu: ok to apply noise floor assumption from ACLR.

Orange: should get feedback from regulatory bodies.

"PC1 Assumptions for CDF Curve for MOP EIRP Spherical Coverage

8/17: Offline discussions are occurring.

8/25: No revision provided or agreement reached based on offline comments. Propose to note this paper."

Decision: 		The document was noted.

R5-204293	On Spurious measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

This document includes some proposals in order to progress on spurious measurement uncertainty gaps of the specification.

Following proposals are made:

Proposal 1: Confirm SNR and relaxation for frequency range 57 GHz ≤  f  ≤  66GHz described in R5-202848 [1] for PC3 devices.

Proposal 2: Noise impact and relaxation for frequency range between 36 and 37 GHz for PC3 devices in spurious co-existence is defined as [1.0 dB] and [6 dB] respectively.

Proposal 3: For spurious co-existence test case, leverage other MU terms different from influence of noise from general spurious test.

Proposal 4: Follow Text proposal in Annex 1 to define MU terms for spurious co-existence test.

Proposal 5: For additional spurious test case, define influence of noise and relaxations as defined in tables 2 and 3.

Proposal 6: For additional spurious test case, leverage other MU terms different from influence of noise from general spurious test.

Proposal 7: Follow Text proposal in Annex 1 to define MU terms for additional spurious test.

Proposal 8: Adjust General spurious MU tables as shown in Annex 1.

Discussion:

r1

Qualcomm: further ongiong discussions. Deferred.

Decision: 		The document was revised to R5-204749.

R5-204749	On Spurious measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-204293)

Discussion:

"LATE DOCUMENT

Revised from: R5-204293r1.

Noted, proposals endorsed, P2 will be updated to remove the brackets in the final version"

Decision: 		The document was noted.

R5-204294	On OBW measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

Abstract:

RAN5 has been discussing FR2 Occupied bandwidth measurement uncertainty for several meetings already ([1-[16]) with the following agreements:

•	In [15] the following proposals were endorsed:

Proposal 1: Apply a span of 1.5 CHBW for 400 MHz and use the same span for the other channel bandwidth in order to optimize the impact of noise.

Proposal 2: Select DFT-s-OFDM QPSK as waveform and modulation since it has the lowest MPR and allows to reduce the impact of noise on the OBW MU.

•	In [16] the following proposals were endorsed:

Proposal 1: OEM and chipset vendors to provide the information on the Tx spectrum shape (PSD, slope), to help determine MU of FR2 OBW test for frequency band n260.

Proposal 2: Reduce FR2 OBW span from 2*CBW to 1.5 *CBW.

During offline discussions in RAN5#87e, it was indicated that same waveforms as defined in [10] could be used for FR2b (n260).

Additionally, simulations of noise impact and signal flatness from different test equipment vendors during RAN5#87e were diverging due to different centre frequencies. After double-checking which centre frequency was used in [10], it was agreed during offline discussions to use 28 GHz in the simulations as centre frequency.

This document provides updated simulation results on the noise and signal flatness impact on the FR2 OBW measurement uncertainty and makes proposals to progress/conclude on this discussion.

This document provides updated simulation results on the noise and signal flatness impact on the FR2 OBW measurement uncertainty and makes proposals to progress/conclude on this discussion.

Following proposals and observations are made:

Proposal 1: Use (OBWmeas - OBWsignal) / CBW *100 as the metric to define OBW MU.

Proposal 2: Analyze OBW MU for SNR=15-40 dB and signal flatness ±2.19 dB.

Observation 1: Big difference between RX signal flatness statistical analysis for Cases 2 & 3.

Proposal 3: Use normal distribution of variance ±2.19dB in each frequency point of the analyzed span to determine Rx signal flatness impact on FR2 OBW MU.

Observation 2: At least 18 dB SNR are required to avoid a failing OBW verdict when measuring 100 MHz CBW signals.

Observation 3: At least 25 dB SNR are required to avoid a failing OBW verdict when measuring 400 MHz CBW signals.

Observation 4: Around 2 dB improvement could be expected in OBW SNR dynamic range when using DFT-s-OFDM instead of CP-OFDM waveforms for the same channel bandwidth.

Observation 5: Around 4.5 dB improvement could be expected in OBW SNR dynamic range when using DFT-s-OFDM instead of CP-OFDM waveforms and CBW=400 MHz instead of CBW=4x100 MHz.

Observation 6: Different analysis should be performed for single CC CBW=400 MHz and CA CBW = 4x 100 MHz.

Proposal 4: Define measurement uncertainty for FR2 OBW as described in Table 4.

Discussion:

Rohde&Schwarz: different analysis method from Anritsu. Used variant? This looks like simulating noise.

r2

Decision: 		The document was revised to R5-204850.

R5-204850	On OBW measurement uncertainty

Type: discussion		For: Endorsement
					Source: Keysight Technologies UK Ltd

(Replaces R5-204294)

Discussion:

"LATE DOCUMENT

Revised from: R5-204294r2.

noted and proposal 1 is endorsed

"

Decision: 		The document was noted.

R5-204729	WF on SA 2Tx and NSA PC2

Type: discussion		For: discussion
					Source: Huawei, Hisilicon

Abstract:

Based on the online discussion, the RAN4 dependent CRs R5-203964 and R5-203966 can’t be agreed if RAN4 only agrees draft CR. So the Proposal 1 and Proposal 4 in this WF request RAN5 to endorse the contents of changes based on RAN4 agreed draft CR, so that TE vendors can start early investigation and development.

Discussion:

late doc

contains 3 draft_CRs, no cover.

Dish network: is the intention to introduce a full band table to cover the 2TX/TxDiv support?

Prop 1, 3, 4 are RAN4 dependent.

r2

Decision: 		The document was revised to R5-204954.

R5-204954	WF on SA 2Tx and NSA PC2

Type: discussion		For: discussion
					Source: Huawei, Hisilicon

(Replaces R5-204729)

Discussion:

late doc

noted, proposal 1 and 2 endorsed

Decision: 		The document was noted.

#### 5.3.3	Rel-15 LTE CA configurations (UID - 770064) LTE_CA_R15-UEConTest

##### 5.3.3.1	TS 36.508

##### 5.3.3.2	TS 36.521-1

R5-203561	Introduction of new TC 7.6.1A.9 In-band blocking for 6DL CA

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5141  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

R5-203562	Introduction of new TC 7.6.2A.9 Out-of-band blocking for 6DL CA

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5142  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

R5-203563	Introduction of new TC 7.6.3A.9 Narrow band blocking for 6DL CA

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5143  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

R5-203564	Introduction of new TC 7.7A.9 Spurious response for 6DL CA

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5144  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

R5-203570	Update of Annex F.1.3 and 3.3 for 6DL blocking and spurious response TCs

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5145  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

R5-203600	Introduction of  TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5146  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203601	Introduction of  TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5147  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203602	Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5148  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203604	Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5149  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203606	Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for FDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5150  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203607	Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for TDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5151  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203608	Update to TDD FDD 7 DL CA Single Antenna Port Performance for FDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5152  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

R5-203609	Update to TDD FDD 7 DL CA Single Antenna Port Performance for TDD PCell

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5153  Cat: F (Rel-16)

					Source: LG Electronics

Decision: 		The document was agreed.

##### 5.3.3.3	TS 36.521-2

R5-203573	Addition of applicability for newly introduced 6DL TCs

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0919  Cat: F (Rel-16)

					Source: Tejet , SRTC

Decision: 		The document was agreed.

##### 5.3.3.4	TS 36.521-3

##### 5.3.3.5	TS 37.571-1

##### 5.3.3.6	TS 37.571-3

##### 5.3.3.7	TS 37.571-5

##### 5.3.3.8	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.3.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.3.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.3.11	Discussion Papers, Work Plan, TC lists

#### 5.3.4	Rel-16 CA configurations (UID - 810061) LTE_CA_R16-UEConTest

##### 5.3.4.1	TS 36.508

##### 5.3.4.2	TS 36.521-1

##### 5.3.4.3	TS 36.521-2

##### 5.3.4.4	TS 36.521-3

##### 5.3.4.5	TS 37.571-1

##### 5.3.4.6	TS 37.571-3

##### 5.3.4.7	TS 37.571-5

##### 5.3.4.8	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.4.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.4.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.4.11	Discussion Papers, Work Plan, TC lists

#### 5.3.5	Shortened TTI and processing time for LTE (UID - 820064) LTE_sTTIandPT-UEConTest

##### 5.3.5.1	TS 36.508

##### 5.3.5.2	TS 36.521-1

R5-203927	Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5166  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203928	Update of message contents and test tolerance for transmitted power in sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5167  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203929	Update of test tolerance for demodulation performance in sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5168  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204892.

R5-204892	Update of test tolerance for demodulation performance in sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5168  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203929)

Decision: 		The document was agreed.

R5-203930	Update of test tolerance for CSI reporting in sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5169  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203931	Addition of acceptable uncertainty and test tolerance for sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5170  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204893.

R5-204893	Addition of acceptable uncertainty and test tolerance for sTTI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5170  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203931)

Decision: 		The document was agreed.

##### 5.3.5.3	TS 36.521-2

##### 5.3.5.4	TS 36.521-3

R5-203933	Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-3

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2520  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was agreed.

R5-203934	Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2521  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204798.

R5-204798	Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2521  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203934)

Decision: 		The document was agreed.

R5-203935	Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2522  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204799.

R5-204799	Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2522  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203935)

Decision: 		The document was agreed.

R5-203936	Addition of downlink RMC configuration with sTTI

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2523  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

##### 5.3.5.5	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.5.6	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.5.7	Discussion Papers, Work Plan, TC lists

R5-203932	Discussion on measurement uncertainty for sTTI test cases

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204955.

R5-204955	Discussion on measurement uncertainty for sTTI test cases

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

(Replaces R5-203932)

Decision: 		The document was noted.

#### 5.3.6	Enhancing LTE CA Utilization (UID - 820066) LTE_euCA-UEConTest

##### 5.3.6.1	TS 36.508

##### 5.3.6.2	TS 36.521-2

##### 5.3.6.3	TS 36.521-3

##### 5.3.6.4	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.6.5	Discussion Papers, Work Plan, TC lists

#### 5.3.7	REL-16 NR CA and DC; and NR and LTE DC Configurations (UID-830083)  NR_CADC_NR_LTE_DC_R16-UEConTest

##### 5.3.7.1	TS 38.508-1

R5-203224	Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1362  Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Discussion:

r1

Decision: 		The document was revised to R5-204800.

R5-204800	Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1362  rev 1 Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

(Replaces R5-203224)

Decision: 		The document was agreed.

R5-203634	Introduction of test frequencies for additional Rel-16 EN-DC inter-band configurations

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1429  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203944	Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1466  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

title change!! Adding the test frequency for DC_28A_n3A

Decision: 		The document was revised to R5-204702.

R5-204702	Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1466  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203944)

Discussion:

reissued as R5-204706 becaue of title change

Decision: 		The document was withdrawn.

R5-204706	Adding the test frequency for DC_28A_n3A

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1504  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

reissued from R5-204702 becaue of title change

Discussion:

First agreed, then withdrawn, as not implementable.

Decision: 		The document was withdrawn.

##### 5.3.7.2	TS 38.508-2

R5-203225	Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0084  Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Discussion:

r1

Decision: 		The document was revised to R5-204801.

R5-204801	Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0084  rev 1 Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

(Replaces R5-203225)

Decision: 		The document was agreed.

R5-203635	Introduction of UE capabilities for additional Rel-16 EN-DC inter-band configurations

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0091  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203911	Update of A.4.3.2A for intra-band contiguous CA capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0094  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2A for intra-band contiguous CA capabilities

Decision: 		The document was agreed.

R5-203912	Update of A.4.3.2A.3 for intra-band non-contiguous CA capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0095  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2A.3 for intra-band non-contiguous CA capabilities

Decision: 		The document was agreed.

R5-203913	Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0096  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities

Discussion:

r1

Decision: 		The document was revised to R5-204802.

R5-204802	Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0096  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203913)

Decision: 		The document was agreed.

R5-203914	Update of A.4.3.2B for NR-DC capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0097  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2B for NR-DC capabilities

Decision: 		The document was agreed.

R5-203915	Update of A.4.3.2B.2 for intra-band EN-DC capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0098  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2B.2 for intra-band EN-DC capabilities

Discussion:

r1

Decision: 		The document was revised to R5-204803.

R5-204803	Update of A.4.3.2B.2 for intra-band EN-DC capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0098  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203915)

Decision: 		The document was agreed.

R5-203916	Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0099  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities

Discussion:

r1

Decision: 		The document was revised to R5-204804.

R5-204804	Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0099  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203916)

Decision: 		The document was agreed.

R5-203917	Update of A.4.3.2B.2.3 for inter-band EN-DC including FR2 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0100  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2B.2.3 for inter-band EN-DC including FR2 capabilities

Decision: 		The document was agreed.

R5-203918	Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0101  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities

Discussion:

r1

Decision: 		The document was revised to R5-204805.

R5-204805	Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0101  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation

(Replaces R5-203918)

Decision: 		The document was agreed.

R5-204153	Introduction of UE capabilities for Rel-16 EN-DC configurations

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0104  Cat: F (Rel-16)

					Source: Bureau Veritas, Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204806.

R5-204806	Introduction of UE capabilities for Rel-16 EN-DC configurations

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0104  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas, Qualcomm Austria RFFE GmbH

(Replaces R5-204153)

Decision: 		The document was agreed.

##### 5.3.7.3	TS 38.521-1

###### 5.3.7.3.1	Tx Requirements (Clause 6)

R5-204131	Update of UE co-existence for CA_n1-n78

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0993  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

r3

Decision: 		The document was revised to R5-204807.

R5-204807	Update of UE co-existence for CA_n1-n78

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0993  rev 1 Cat: F (Rel-16)

					Source: China Unicom

(Replaces R5-204131)

Decision: 		The document was agreed.

###### 5.3.7.3.2	Rx Requirements (Clause 7)

R5-203558	Corrections and additions to 7.3A

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0930  Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

Discussion:

r1

Decision: 		The document was revised to R5-204722.

R5-204722	Corrections and additions to 7.3A

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0930  rev 1 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-203558)

Decision: 		The document was revised to R5-204980.

R5-204980	Corrections and additions to 7.3A

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0930  rev 2 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-204722)

Decision: 		The document was agreed.

R5-203560	Completing 3CA Rx cases 7.5A.2 and 7.7A.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0931  Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

Discussion:

r1

Decision: 		The document was revised to R5-204723.

R5-204723	Completing 3CA Rx cases 7.5A.2 and 7.7A.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0931  rev 1 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-203560)

Decision: 		The document was revised to R5-204981.

R5-204981	Completing 3CA Rx cases 7.5A.2 and 7.7A.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0931  rev 2 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-204723)

Decision: 		The document was agreed.

###### 5.3.7.3.3	Clauses 1-5, Annexes

R5-203285	Update of R16 CADC combos in TS 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0925  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

r1

Decision: 		The document was revised to R5-204808.

R5-204808	Update of R16 CADC combos in TS 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0925  rev 1 Cat: F (Rel-16)

					Source: China Unicom

(Replaces R5-203285)

Decision: 		The document was agreed.

##### 5.3.7.4	TS 38.521-2

###### 5.3.7.4.1	Tx Requirements (Clause 6)

###### 5.3.7.4.2	Rx Requirements (Clause 7)

###### 5.3.7.4.3	Clauses 1-5, Annexes

##### 5.3.7.5	TS 38.521-3

###### 5.3.7.5.1	Tx Requirements (Clause 6)

R5-203226	Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0643  Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Discussion:

conflict with R5-203945 and R5-203953.

r1

Decision: 		The document was revised to R5-204809.

R5-204809	Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0643  rev 1 Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

(Replaces R5-203226)

Decision: 		The document was agreed.

R5-203636	Editorial correction to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0654  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204810.

R5-204810	Editorial correction to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0654  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203636)

Decision: 		The document was agreed.

R5-203637	Introduction of additional Rel-16 EN-DC inter-band configurations to EN-DC MOP test case 6.2B.1.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0655  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203638	Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0656  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

r1

Decision: 		The document was revised to R5-204811.

R5-204811	Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0656  rev 1 Cat: F (Rel-16)

					Source: Ericsson, Telefonica

(Replaces R5-203638)

Decision: 		The document was agreed.

R5-203639	Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0657  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

r1

Removed the protected bands where no IM product occur from test requirement and editorial corrections.

Decision: 		The document was revised to R5-204812.

R5-204812	Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0657  rev 1 Cat: F (Rel-16)

					Source: Ericsson, Telefonica

(Replaces R5-203639)

Decision: 		The document was agreed.

R5-203640	Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0658  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

r1

Removed the protected bands where no IM product occur from test requirement and editorial corrections.

Decision: 		The document was revised to R5-204813.

R5-204813	Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0658  rev 1 Cat: F (Rel-16)

					Source: Ericsson, Telefonica

(Replaces R5-203640)

Decision: 		The document was agreed.

R5-203807	Updated to clause 6 for EN-DC Rel-16 band requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0662  Cat: F (Rel-16)

					Source: Sporton, Bureau Veritas, Ericsson

Discussion:

r1: Adding clauses affected; Removing the DC_2A_n66A as overlapping with T-doc: R5-203946; Modifying the test points for DC_66A_n2A; Adding the test requirement for DC_66A_n2A

WIC changed to NR_CADC_NR_LTE_DC_R16-UEConTest.

r2

Decision: 		The document was revised to R5-204724.

R5-204724	Updated to clause 6 for EN-DC Rel-16 band requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0662  rev 1 Cat: F (Rel-16)

					Source: Sporton, Bureau Veritas, Ericsson

(Replaces R5-203807)

Decision: 		The document was agreed.

R5-203919	Update of Tx test for DC_2_n41 and DC_66_n41

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0671  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Update of Tx test for DC_2_n41 and DC_66_n41

Discussion:

merged into R5-204207.

Decision: 		The document was withdrawn.

R5-203945	Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0677  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204703.

R5-204703	Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0677  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203945)

Discussion:

reissued as R5-204707 because of title change

Decision: 		The document was withdrawn.

R5-204707	Addition of MOP testing for DC_28A_n3A in 6.2B.1.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0740  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

reissued from R5-204703 because of title change

Decision: 		The document was agreed.

R5-203953	Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0679  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204814.

R5-204814	Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0679  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203953)

Decision: 		The document was agreed.

R5-203966	Update of MOP test cases for EN-DC PC2 Rel-16 requirements

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0683  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Depending on R4-2010809. Relevant Rel-15 changes in R5-203965

Discussion:

r1

Decision: 		The document was revised to R5-204845.

R5-204845	Update of MOP test cases for EN-DC PC2 Rel-16 requirements

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0683  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203966)

Discussion:

RAN4 CR is not pursued.

Decision: 		The document was withdrawn.

R5-204009	Correction to UE co-existence Test Case 6.5B.3.3.2

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0686  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

overlapping with R5-204207.

Decision: 		The document was withdrawn.

R5-204155	Updated to clause 6 for EN-DC Rel-16 configuration test requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0694  Cat: F (Rel-16)

					Source: Bureau Veritas, Qualcomm Austria RFFE GmbH

Discussion:

r1

Decision: 		The document was revised to R5-204815.

R5-204815	Updated to clause 6 for EN-DC Rel-16 configuration test requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0694  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas, Qualcomm Austria RFFE GmbH

(Replaces R5-204155)

Decision: 		The document was agreed.

R5-204210	Update Tx TC for Rel 16 DC combos

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0718  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Decision: 		The document was agreed.

###### 5.3.7.5.2	Rx Requirements (Clause 7)

R5-203227	Adding receiver requirements for Rel-16 inter-band EN-DC FR1 band combinations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0644  Cat: F (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was agreed.

R5-203527	Editorial correction of Tx spurious emissions for FR1 EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0652  Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

Discussion:

reissued as R5-204349 because of title change

Decision: 		The document was withdrawn.

R5-204349	Editorial correction of Rx spurious emissions for FR1 EN-DC

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0738  Cat: F (Rel-16)

					Source: DOCOMO Communications Lab.

Abstract:

reissued from R5-203527 because of title change

Discussion:

align with "5GS WP Rx Tx Iw FR1 and FR2 v10.1".

Decision: 		The document was agreed.

R5-203641	Introduction of additonal Rel-16 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0659  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Discussion:

-

Decision: 		The document was withdrawn.

R5-203808	Updated to clause 7 for EN-DC Rel-16 band requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0663  Cat: F (Rel-16)

					Source: Sporton, Bureau Veritas

Discussion:

r1

WIC changed to NR_CADC_NR_LTE_DC_R16-UEConTest.

Decision: 		The document was revised to R5-204956.

R5-204956	Updated to clause 7 for EN-DC Rel-16 band requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0663  rev 1 Cat: F (Rel-16)

					Source: Sporton, Bureau Veritas

(Replaces R5-203808)

Discussion:

Ericsson’s CR R5-204215 will only cover 3CC and not include 4CC.

Decision: 		The document was withdrawn.

R5-203907	Corrections on delta RIB due to Rel-16 EN-DC configurations

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0669  Cat: F (Rel-16)

					Source: ZTE Corporation

Abstract:

Corrections on delta RIB due to Rel-16 EN-DC configurations

Discussion:

r1

Decision: 		The document was agreed.

R5-204156	Updated to clause 7 for EN-DC Rel-16 configuration test requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0695  Cat: F (Rel-16)

					Source: Bureau Veritas

Discussion:

r1

Decision: 		The document was revised to R5-204957.

R5-204957	Updated to clause 7 for EN-DC Rel-16 configuration test requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0695  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas

(Replaces R5-204156)

Decision: 		The document was agreed.

R5-204218	Update Tx TC for Rel 16 DC combos

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0720  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

Discussion:

different tile: Add Rx TC for 2Rel 16 DC combos!

reissued as R5-204347 because of title change.

Decision: 		The document was withdrawn.

R5-204347	Add Rx TC for 2Rel 16 DC combos

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0737  Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH, Bureau Veritas

Abstract:

reissued from R5-204218 because of title change.

Discussion:

r2

Decision: 		The document was revised to R5-204958.

R5-204958	Add Rx TC for 2Rel 16 DC combos

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0737  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Austria RFFE GmbH

(Replaces R5-204347)

Decision: 		The document was agreed.

###### 5.3.7.5.3	Clauses 1-5, Annexes

R5-204152	Updated to EN-DC Rel-16 Configuration information in clause 5

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0692  Cat: F (Rel-16)

					Source: Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson

Abstract:

Added Rel-16 CA/DC configurations which has been assigned to company and at least 1 TC requirement included in the spec

Discussion:

r1

Decision: 		The document was revised to R5-204816.

R5-204816	Updated to EN-DC Rel-16 Configuration information in clause 5

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0692  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson

(Replaces R5-204152)

Decision: 		The document was agreed.

R5-204154	Updated to Annex M for EN-DC Rel-16 configuration requirement

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0693  Cat: F (Rel-16)

					Source: Bureau Veritas

Decision: 		The document was agreed.

##### 5.3.7.6	TS 38.521-4

###### 5.3.7.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

###### 5.3.7.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

###### 5.3.7.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.7.6.4	Clauses 1-4, Annexes

##### 5.3.7.7	TS 38.522

##### 5.3.7.8	TS 38.533

##### 5.3.7.9	TR 38.903 (NR MU &  TT analyses)

##### 5.3.7.10	TR 38.905 (NR Test Points Radio Transmission and Reception)

R5-203559	Updated TP analysis for 7.3A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0268  Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

Discussion:

r1

Decision: 		The document was revised to R5-204725.

R5-204725	Updated TP analysis for 7.3A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0268  rev 1 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-203559)

Decision: 		The document was revised to R5-204982.

R5-204982	Updated TP analysis for 7.3A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0268  rev 2 Cat: F (Rel-16)

					Source: WE Certification Oy, DISH Network

(Replaces R5-204725)

Decision: 		The document was agreed.

R5-203642	Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n1A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0269  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203643	Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n78A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0270  Cat: F (Rel-16)

					Source: Ericsson, Telefonica

Decision: 		The document was agreed.

R5-203751	Editorial correction to references to EN-DC configurations

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0275  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203806	Addition of test point analysis in Tx spurious emissions

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0278  Cat: F (Rel-16)

					Source: Sporton, Ericsson

Discussion:

r1: fix 3GU issue; Removing the TpAnalysis for DC_2A-n66A

WIC changed to NR_CADC_NR_LTE_DC_R16-UEConTest.

r2

Decision: 		The document was revised to R5-204726.

R5-204726	Addition of test point analysis in Tx spurious emissions

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0278  rev 1 Cat: F (Rel-16)

					Source: Sporton, Ericsson

(Replaces R5-203806)

Decision: 		The document was agreed.

R5-203954	Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0286  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204817.

R5-204817	Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0286  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203954)

Decision: 		The document was agreed.

R5-203955	Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0287  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204818.

R5-204818	Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0287  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203955)

Decision: 		The document was agreed.

R5-203956	Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0288  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204819.

R5-204819	Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0288  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203956)

Decision: 		The document was agreed.

R5-203957	Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0289  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r3????

Decision: 		The document was revised to R5-204820.

R5-204820	Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0289  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203957)

Decision: 		The document was agreed.

R5-203958	Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0290  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204821.

R5-204821	Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0290  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203958)

Decision: 		The document was agreed.

R5-203959	Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0291  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204822.

R5-204822	Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0291  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203959)

Decision: 		The document was agreed.

R5-204132	Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0994  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

cover 38.905!

withdrawn and reissued as R5-204132 because of wrong spec.

Decision: 		The document was withdrawn.

R5-204335	Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0301  Cat: F (Rel-16)

					Source: China Unicom

Abstract:

reissued from R5-204335 because of wrong spec.

Discussion:

associated with R5-204131.

r2

Decision: 		The document was revised to R5-204959.

R5-204959	Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0301  rev 1 Cat: F (Rel-16)

					Source: China Unicom

(Replaces R5-204335)

Decision: 		The document was agreed.

##### 5.3.7.11	Discussion Papers, Work Plan, TC lists

#### 5.3.8	Enhancements on Full-Dimension (FD) MIMO for LTE (UID - 830085) LTE_eFDMIMO-UEConTest

##### 5.3.8.1	TS 36.508

##### 5.3.8.2	TS 36.521-1

##### 5.3.8.3	TS 36.521-2

##### 5.3.8.4	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.8.5	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.8.6	Discussion Papers, Work Plan, TC lists

#### 5.3.9	Study on 5G NR User Equipment (UE) Application Layer Data Throughput Performance (UID - 840090) FS_UE_5GNR_App_Data_Perf

##### 5.3.9.1	TR 37.901-5

R5-204318	Text Proposal to update Clause 5.5 - Test Environment

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0001  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 : Update to clause 5.5 in TR 37.901-5

Decision: 		The document was agreed.

R5-204319	Text Proposal to update TC A.7.1.1.1

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0002  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 : Update additional test procedures/test cases in the SI for FR2

Discussion:

r1

feedback received from R&S.

Decision: 		The document was revised to R5-204894.

R5-204894	Text Proposal to update TC A.7.1.1.1

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0002  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204319)

Decision: 		The document was agreed.

R5-204320	Text Proposal to update TC A.9.1.1.1

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0003  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 : Update additional test procedures/test cases in the SI for FR2

Discussion:

r1

feedback received from R&S.

Decision: 		The document was revised to R5-204895.

R5-204895	Text Proposal to update TC A.9.1.1.1

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0003  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204320)

Decision: 		The document was agreed.

R5-204321	Text Proposal to update TC A.8.1

Type: CR		For: Agreement
					37.901-5 v16.0.0	  CR-0004  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 : Update additional test procedures/test cases in the SI for FR2

Decision: 		The document was agreed.

##### 5.3.9.2	Discussion Papers, Work Plan, TC lists

#### 5.3.10	LTE Advanced high power TDD UE (power class 2) for Rel-15 (UID - 850061) LTE_TDD_HPUE_R15-UEConTest

##### 5.3.10.1	TS 36.521-1

R5-203857	Update of Test Tolerance for HPUE

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5163  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203858	Update of MOP for HPUE

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5164  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

R5-203859	Update of MPR for HPUE

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5165  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

##### 5.3.10.2	TS 36.521-2

R5-203860	Update of capability for HPUE

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0923  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

##### 5.3.10.3	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.10.4	Discussion Papers, Work Plan, TC lists

#### 5.3.11	New Rel-16 NR bands and extension of existing NR bands (UID - 850062) NR_bands_BW_R16-UEConTest

##### 5.3.11.1	TS 38.508-1

R5-203278	n26 Default CH BW in 38.508-1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1367  Cat: F (Rel-16)

					Source: Dish Network

Decision: 		The document was agreed.

R5-203337	Addition of test frequencies for n28 with CBW of 30MHz

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1370  Cat: F (Rel-16)

					Source: CMCC, CBN, Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204896.

R5-204896	Addition of test frequencies for n28 with CBW of 30MHz

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1370  rev 1 Cat: F (Rel-16)

					Source: CMCC, CBN, Ericsson

(Replaces R5-203337)

Decision: 		The document was agreed.

R5-203767	Addition of test frequencies for new Rel-16 CBW for NR band n77

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1449  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203768	Addition of test frequencies for new Rel-16 CBW for NR band n78

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1450  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203769	Introduction of test frequencies for Rel-16 NR band n30

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1451  Cat: F (Rel-16)

					Source: Ericsson, AT&T

Decision: 		The document was agreed.

R5-203770	Introduction of test frequencies for Rel-19 NR band n259

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1452  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

reissued as R5-204346 because of wrong title

Decision: 		The document was withdrawn.

R5-204346	Introduction of test frequencies for Rel-16 NR band n259

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1502  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

reissued from R5-203770 because of wrong title

Decision: 		The document was agreed.

R5-203998	Addition of test frequencies for new Rel-16 CBW 25 and 50 MHz for NR band n1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1467  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204041	Addition of test channel bandwidths for n1 new CBW in 38.508-1 R16

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1473  Cat: F (Rel-16)

					Source: China Unicom

Decision: 		The document was agreed.

##### 5.3.11.2	TS 38.508-2

R5-203279	n26 Implementation baseline capabilities in 38.508-2

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0085  Cat: F (Rel-16)

					Source: Dish Network

Decision: 		The document was agreed.

R5-204046	Addition of R16 new channel bandwidths for n1 in 38.508-2

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0103  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

-

Decision: 		The document was withdrawn.

##### 5.3.11.3	TS 38.521-1

R5-203336	Addition of test cases for n28 with CBW of 30MHz

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0928  Cat: F (Rel-16)

					Source: CMCC, CBN, Huawei, HiSilicon, Orange

Discussion:

r2

Decision: 		The document was revised to R5-204960.

R5-204960	Addition of test cases for n28 with CBW of 30MHz

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0928  rev 1 Cat: F (Rel-16)

					Source: CMCC, CBN, Huawei, HiSilicon, Orange

(Replaces R5-203336)

Decision: 		The document was agreed.

###### 5.3.11.3.1	Tx Requirements (Clause 6)

R5-203259	Correction of test frequencies for NS_47

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0916  Cat: F (Rel-16)

					Source: Ericsson, SoftBank Corp.

Discussion:

r1

Decision: 		The document was revised to R5-204823.

R5-204823	Correction of test frequencies for NS_47

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0916  rev 1 Cat: F (Rel-16)

					Source: Ericsson, SoftBank Corp.

(Replaces R5-203259)

Decision: 		The document was agreed.

R5-203260	Adding NS_47 to Additional spurious emissions test case

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0917  Cat: F (Rel-16)

					Source: Ericsson, SoftBank Corp.

Decision: 		The document was agreed.

R5-203261	Adding UL MIMO additional spurious emissions test for NS_47

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0918  Cat: F (Rel-16)

					Source: Ericsson, SoftBank Corp.

Decision: 		The document was agreed.

R5-203262	Adding band n48 to maximum output power and maximum output power reduction tests

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0919  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r2

Decision: 		The document was revised to R5-204824.

R5-204824	Adding band n48 to maximum output power and maximum output power reduction tests

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0919  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203262)

Decision: 		The document was agreed.

R5-203777	Update of NR test case 6.2.1 UE MOP for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0960  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203778	Update of NR test case 6.2.2 UE MPR for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0961  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203780	Update of NR test case 6.2D.1 UE MOP for UL MIMO for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0962  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203781	Update of NR test case 6.2D.2 UE MPR for UL MIMO for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0963  Cat: F (Rel-16)

					Source: AT&T

Discussion:

-

Decision: 		The document was withdrawn.

R5-203783	Update of NR test case 6.5.3.2 Spurious Emissions for UE Co-Ex for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0964  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203976	Addition of 25MHz for NR band n1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0984  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204825.

R5-204825	Addition of 25MHz for NR band n1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0984  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203976)

Decision: 		The document was agreed.

R5-203977	Addition of AMPR NS_48 for NR band n1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0985  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

TP in R5-20xxxx

Discussion:

r1

Decision: 		The document was revised to R5-204826.

R5-204826	Addition of AMPR NS_48 for NR band n1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0985  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203977)

Decision: 		The document was agreed.

###### 5.3.11.3.2	Rx Requirements (Clause 7)

R5-203263	Adding band n48 to blocking characteristics tests

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0920  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

merged into R5-203699r1.

Decision: 		The document was withdrawn.

R5-203282	n26 Rx requirements in 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0922  Cat: F (Rel-16)

					Source: Dish Network

Discussion:

r1

Decision: 		The document was revised to R5-204961.

R5-204961	n26 Rx requirements in 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0922  rev 1 Cat: F (Rel-16)

					Source: Dish Network

(Replaces R5-203282)

Decision: 		The document was agreed.

R5-203786	Update of NR test case 7.3 UE Ref Sens for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0965  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203787	Update of NR test case 7.6.2 UE IBB for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0966  Cat: F (Rel-16)

					Source: AT&T, DISH Network, CAICT, Ericsson, HiSilicon

Discussion:

r1

overlapping revisions to Table 7.6.2.3-2 and Table 7.6.2.5-2 in R5-203282, R5-203878, R5-203699, and R5-203263 were merged into this CR.

Decision: 		The document was revised to R5-204962.

R5-204962	Update of NR test case 7.6.2 UE IBB for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0966  rev 1 Cat: F (Rel-16)

					Source: AT&T, DISH Network, CAICT, Ericsson, HiSilicon

(Replaces R5-203787)

Decision: 		The document was agreed.

R5-203788	Update of NR test case 7.6.3 UE OBB for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0967  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-203789	Update of NR test case 7.6.4 UE NBB for n30

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0968  Cat: F (Rel-16)

					Source: AT&T

Decision: 		The document was agreed.

R5-204129	Addition of n1 R16 new CBW into 38.521-1 Refsense test

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0992  Cat: F (Rel-16)

					Source: China Unicom

Discussion:

r1

Decision: 		The document was revised to R5-204827.

R5-204827	Addition of n1 R16 new CBW into 38.521-1 Refsense test

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0992  rev 1 Cat: F (Rel-16)

					Source: China Unicom

(Replaces R5-204129)

Decision: 		The document was agreed.

###### 5.3.11.3.3	Clauses 1-5, Annexes

R5-203281	n26 in common clauses in 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0921  Cat: F (Rel-16)

					Source: Dish Network

Discussion:

reflected in R5-203284r1 from China Unicom.

Decision: 		The document was withdrawn.

R5-203284	Update of R16 new bands and CBWs in 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0924  Cat: F (Rel-16)

					Source: China Unicom, AT&T, Dish Network, CMCC

Discussion:

r1

Decision: 		The document was revised to R5-204828.

R5-204828	Update of R16 new bands and CBWs in 38.521-1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0924  rev 1 Cat: F (Rel-16)

					Source: China Unicom, AT&T, Dish Network, CMCC

(Replaces R5-203284)

Decision: 		The document was agreed.

##### 5.3.11.4	TS 38.521-2

###### 5.3.11.4.1	Tx Requirements (Clause 6)

###### 5.3.11.4.2	Rx Requirements (Clause 7)

###### 5.3.11.4.3	Clauses 1-5, Annexes

##### 5.3.11.5	TS 38.521-4

###### 5.3.11.5.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

###### 5.3.11.5.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

###### 5.3.11.5.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.11.5.4	Clauses 1-4, Annexes

##### 5.3.11.6	TS 38.533

R5-203280	n26 addition to group of bands in 38.533

Type: CR		For: Agreement
					38.533 v16.4.0	  CR-0772  Cat: F (Rel-16)

					Source: Dish Network

Decision: 		The document was agreed.

##### 5.3.11.7	TS 37.571-1

##### 5.3.11.8	TR 38.903 ((NR MU &  TT analyses)

##### 5.3.11.9	TR 38.905 (NR Test Points Radio Transmission and Reception)

R5-203797	Update test point analysis for A-MPR NS_18 with CBW being 30MHz

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0276  Cat: F (Rel-16)

					Source: CMCC, Huawei, HiSilicon

Discussion:

r3

Decision: 		The document was revised to R5-204963.

R5-204963	Update test point analysis for A-MPR NS_18 with CBW being 30MHz

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0276  rev 1 Cat: F (Rel-16)

					Source: CMCC, Huawei, HiSilicon

(Replaces R5-203797)

Decision: 		The document was agreed.

R5-203978	Addition of test point analysis for AMPR NS_48

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0293  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

TC in R5-203977

Discussion:

r2

Decision: 		The document was revised to R5-204829.

R5-204829	Addition of test point analysis for AMPR NS_48

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0293  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203978)

Decision: 		The document was agreed.

R5-204023	Addition of test point analysis for additional spurious emission with NS_17

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0294  Cat: F (Rel-16)

					Source: Huawei, Orange, CMCC

Abstract:

TC in R5-203336

Discussion:

r1

Decision: 		The document was revised to R5-204964.

R5-204964	Addition of test point analysis for additional spurious emission with NS_17

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0294  rev 1 Cat: F (Rel-16)

					Source: Huawei, Orange, CMCC

(Replaces R5-204023)

Decision: 		The document was agreed.

##### 5.3.11.10	Discussion Papers, Work Plan, TC lists

R5-203525	Update of WF on Band n259

Type: discussion		For: Endorsement
					38.521-2 v..
					Source: DOCOMO Communications Lab.

Abstract:

During the RAN5#85 (Feb-2019), WF for handling Band n259 was defined in [1]. The purpose of this contribution is to update WF for handling Band n259 in terms of time plan and priority.

Proposal 1	: Add Inband blocking and ACS in Priority 2 (P2) test cases for Band n259 work.

Proposal 2	: Update the time plan for Band n259 work.

Proposal 3	: To set following action point to estimate the upper limit of FR2c (band n259) MU and relaxation for P1 and P2 test cases.

Discussion:

r2

Decision: 		The document was revised to R5-204851.

R5-204851	Update of WF on Band n259

Type: discussion		For: Endorsement
					38.521-2 v..
					Source: DOCOMO Communications Lab.

(Replaces R5-203525)

Discussion:

"Revised from: R5-203525r2.

noted and proposals are endorsed"

Decision: 		The document was noted.

R5-203526	Update Test tolerance of Band n259

Type: discussion		For: Endorsement
					38.521-2 v..
					Source: DOCOMO Communications Lab.

Discussion:

8/21: Anritsu asked for clarification that proposed TT values were not including any test requirement relaxation. DOCOMO confirmed.

8/24 : no further comments received .

Noted and Proposals  endorsed.

Decision: 		The document was noted.

#### 5.3.12	Addition of Power Class 2 UE for LTE bands 31 and 72 (UID – 860030) LTE_PC2_B31_B72-UEConTest

##### 5.3.12.1	TS 36.521-1

R5-203228	Introduction of PC2 UE for cat M1/M2 in LTE Bands 31 and 72

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5138  Cat: B (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was agreed.

##### 5.3.12.2	TS 36.521-2

R5-203229	Introduction of Baseline Implementation Capabilities for PC2 in LTE Bands 31 and 72

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0917  Cat: B (Rel-16)

					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was agreed.

##### 5.3.12.3	Discussion Papers, Work Plan, TC lists

#### 5.3.13	Further NB-IoT enhancements (UID – 860031) NB_IOTenh2-UEConTest

##### 5.3.13.1	TS 36.508

##### 5.3.13.2	TS 36.521-1

R5-203981	Updated to NB-IOT TC 6.3.5F.1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5171  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204830.

R5-204830	Updated to NB-IOT TC 6.3.5F.1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5171  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203981)

Decision: 		The document was agreed.

R5-203982	Updated to NB-IOT TC 6.3.5F.3

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5172  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Abstract:

Depending on R4-20xxxx

Discussion:

r1

Decision: 		The document was revised to R5-204965.

R5-204965	Updated to NB-IOT TC 6.3.5F.3

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5172  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203982)

Decision: 		The document was agreed.

R5-204162	Updated to test applicability for R15 NB-IoT requirement

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5186  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

applicability condition tdoc R5-204163

Discussion:

r1

Decision: 		The document was revised to R5-204831.

R5-204831	Updated to test applicability for R15 NB-IoT requirement

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5186  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas

(Replaces R5-204162)

Decision: 		The document was agreed.

##### 5.3.13.3	TS 36.521-2

R5-203804	Update additional information for test applicability for NB-IoT Test cases

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0922  Cat: F (Rel-16)

					Source: Sporton

Discussion:

-

Decision: 		The document was withdrawn.

R5-204163	Updated to applicability table of R15 NB-IoT tests

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0928  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

TC tdoc R5-204162

Decision: 		The document was agreed.

##### 5.3.13.4	TS 36.521-3

R5-203800	Addition of 6.1.23 NB-IOT TDD Inter-frequency RRC Re-establishment in In-Band mode under normal coverage

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2516  Cat: F (Rel-16)

					Source: Sporton

Decision: 		The document was agreed.

R5-203801	Addition of 6.1.24 NB-IOT TDD - TDD Intra-frequency RRC Re-establishment  in In-Band mode under enhanced coverage

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2517  Cat: F (Rel-16)

					Source: Sporton

Decision: 		The document was agreed.

R5-203802	Addition of 6.2.19 NB-IOT TDD Contention Based Random Access Test  in normal coverage

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2518  Cat: F (Rel-16)

					Source: Sporton

Decision: 		The document was agreed.

R5-203803	Addition of 6.2.20 NB-IOT TDD Contention Based Random Access Test  in enhanced coverage

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2519  Cat: F (Rel-16)

					Source: Sporton

Decision: 		The document was agreed.

##### 5.3.13.5	TS 37.571-1

##### 5.3.13.6	TS 37.571-3

##### 5.3.13.7	TS 37.571-5

##### 5.3.13.8	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.13.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.13.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.13.11	Discussion Papers, Work Plan, TC lists

#### 5.3.14	Even further enhanced MTC for LTE (UID – 860032) LTE_eMTC4-UEConTest

##### 5.3.14.1	TS 36.508

R5-204141	Updates to IEs for RF eMTC TCs

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1330  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

AI 5.3.14.1!

r1

Decision: 		The document was revised to R5-204966.

R5-204966	Updates to IEs for RF eMTC TCs

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1330  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204141)

Decision: 		The document was agreed.

##### 5.3.14.2	TS 36.521-1

R5-203775	Updating test case applicability for CSI test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5155  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203776	Adding test case applicability rules

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5156  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203779	Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.1.3.1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5157  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203782	Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.2.3.1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5158  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203784	Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5159  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204967.

R5-204967	Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5159  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203784)

Decision: 		The document was agreed.

R5-203790	Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5160  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204968.

R5-204968	Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5160  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203790)

Decision: 		The document was agreed.

R5-203791	Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5161  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204969.

R5-204969	Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5161  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203791)

Decision: 		The document was agreed.

R5-203792	Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5162  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204970.

R5-204970	Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5162  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203792)

Decision: 		The document was agreed.

R5-204001	Annex F based on updated Tx test cases for efeMTC

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5177  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204003	Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5178  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204971.

R5-204971	Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5178  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204003)

Decision: 		The document was agreed.

R5-204005	Adding PC6 to 6.3.5EA.1, Power Control Absolute power tolerance for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5179  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204007	Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5180  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204011	Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5181  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

-

Decision: 		The document was withdrawn.

R5-204013	Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5182  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204972.

R5-204972	Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5182  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204013)

Decision: 		The document was agreed.

R5-204014	Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5183  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204973.

R5-204973	Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5183  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204014)

Decision: 		The document was agreed.

R5-204017	Adding PC6 to 6.3.5EA.2, Power Control Relative power tolerance for UE category M1

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5184  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

##### 5.3.14.3	TS 36.521-2

R5-203773	Adding applicability for new efeMTC test cases 9.8.3.1, 9.8.3.2, 9.8.4.1, 9.8.4.2

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0921  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

##### 5.3.14.4	TS 36.521-3

##### 5.3.14.5	TS 37.571-1

##### 5.3.14.6	TS 37.571-3

##### 5.3.14.7	TS 37.571-5

##### 5.3.14.8	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.14.9	TR 36.904 (E-UTRAN Radio Reception TT analyses)

##### 5.3.14.10	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

##### 5.3.14.11	Discussion Papers, Work Plan, TC lists

#### 5.3.15	RF requirements for NR frequency range 1 (FR1) (UID-870061)  NR_RF_FR1-UEConTest

##### 5.3.15.1	TS 38.508-1

##### 5.3.15.2	TS 38.508-2

##### 5.3.15.3	TS 38.521-1

###### 5.3.15.3.1	Tx Requirements (Clause 6)

R5-203690	Introduce general requirement for UL CA test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0942  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203691	Updating NR test case 6.2A.1- MOP for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0943  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

RAN4 dependency with R4-2010231.

Discussion:

RAN4 dependent CR R4-2011476.

RAN4 CR that is dependent on MOP changes for Intraband contigous  UL CA is R4-2010231 and is agreed.

Decision: 		The document was agreed.

R5-203692	Update of NR test case 6.2A.2-MPR for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0944  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TT in R5-203689; Table 6.1A-1a in R5-203690; TP in R5-203693

RAN4 dependency

Discussion:

r1

The dependent content in R4-2011471 is revised into R4-2011728 and R4-2011729, and agreed.

Decision: 		The document was revised to R5-204984.

R5-204984	Update of NR test case 6.2A.2-MPR for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0944  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203692)

Decision: 		The document was agreed.

R5-203694	Updating of NR test case 6.2A.4-Configured output power for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0945  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TT in R5-203689; Table 6.1A-1a in R5-203690; TP in R5-203695

RAN4 dependency

Discussion:

r2

Decision: 		The document was revised to R5-204974.

R5-204974	Updating of NR test case 6.2A.4-Configured output power for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0945  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203694)

Decision: 		The document was agreed.

R5-203721	Introduce of new TC 6.3A.4.1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0952  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Discussion:

r1

Decision: 		The document was revised to R5-204832.

R5-204832	Introduce of new TC 6.3A.4.1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0952  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

(Replaces R5-203721)

Decision: 		The document was agreed.

R5-203723	Introduce of new TC 6.3A.4.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0953  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Discussion:

r1

Decision: 		The document was revised to R5-204833.

R5-204833	Introduce of new TC 6.3A.4.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0953  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

(Replaces R5-203723)

Decision: 		The document was agreed.

R5-203726	Introduce of new TC 6.3A.4.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0954  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Discussion:

r1

Decision: 		The document was revised to R5-204834.

R5-204834	Introduce of new TC 6.3A.4.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0954  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

(Replaces R5-203726)

Decision: 		The document was agreed.

R5-203734	Add intra-band contiguous CA to 6.3A.1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0955  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Discussion:

r1

Decision: 		The document was revised to R5-204835.

R5-204835	Add intra-band contiguous CA to 6.3A.1

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0955  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

(Replaces R5-203734)

Decision: 		The document was agreed.

R5-203735	Add intra-band contiguous CA to 6.3A.2

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0956  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Decision: 		The document was agreed.

R5-203736	Add intra-band contiguous CA to 6.3A.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0957  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

Discussion:

r1

Decision: 		The document was revised to R5-204836.

R5-204836	Add intra-band contiguous CA to 6.3A.3

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0957  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom.

(Replaces R5-203736)

Decision: 		The document was agreed.

###### 5.3.15.3.2	Rx Requirements (Clause 7)

R5-203530	Update to 7.5A.2 ACS for 3DL CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0929  Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH

Discussion:

r1

Decision: 		The document was revised to R5-204897.

R5-204897	Update to 7.5A.2 ACS for 3DL CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0929  rev 1 Cat: F (Rel-16)

					Source: Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH

(Replaces R5-203530)

Decision: 		The document was agreed.

R5-203696	Addition of general clause 7.1A

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0946  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203697	Updating REFSENS minimum requirements for Intra-band non-contiguous CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0947  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203698	Update of 7.4A.2-Maximum input level for 3DL CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0948  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203699	Adding band n48 for Blocking characteristics testing

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0949  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Ericsson

Discussion:

overlaps with R5-203263.

r1

Decision: 		The document was revised to R5-204837.

R5-204837	Adding band n48 for Blocking characteristics testing

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0949  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Ericsson

(Replaces R5-203699)

Decision: 		The document was agreed.

R5-203700	Update of test case 7.6A.2-Inband blocking for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0950  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203701	Update of test case 7.6A.2.2 Inband blocking for 3DL CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0951  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-204035	Updating NR test case 7.6A.3 for n48

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0987  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-204037	Update of NR test case 7.5A Adjacent Channel selectivity for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0988  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

was wrong WIC in 3GU! -> AI?

r1

Decision: 		The document was revised to R5-204898.

R5-204898	Update of NR test case 7.5A Adjacent Channel selectivity for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0988  rev 1 Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

(Replaces R5-204037)

Decision: 		The document was agreed.

R5-204040	Update of NR test case 7.7A Spurious response for CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0989  Cat: F (Rel-16)

					Source: Samsung R&D Institute UK

Discussion:

was wrong WIC in 3GU! -> AI  changed.

Decision: 		The document was agreed.

###### 5.3.15.3.3	Clauses 1-5, Annexes

R5-203687	Updating channel configurations for Intra-band UL contiguous CA

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0939  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203688	Updating intra-band CA UL and DL configurations

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0940  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203689	Adding MU and TTs for Intra-band UL CA test cases

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0941  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

##### 5.3.15.4	TS 38.521-3

###### 5.3.15.4.1	Tx Requirements (Clause 6)

###### 5.3.15.4.2	Rx Requirements (Clause 7)

###### 5.3.15.4.3	Clauses 1-5, Annexes

##### 5.3.15.5	TS 38.522

##### 5.3.15.6	TS 38.533

##### 5.3.15.7	TR 38.903 (NR MU &  TT analyses)

##### 5.3.15.8	TR 38.905 (NR Test Points Radio Transmission and Reception)

R5-203693	Updating TP analysis for 6.2A.2-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0273  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TC in R5-203692

Discussion:

r1

Decision: 		The document was revised to R5-204727.

R5-204727	Updating TP analysis for 6.2A.2-MPR for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0273  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203693)

Decision: 		The document was agreed.

R5-203695	Updating TP analysis for 6.2A.4-Configured output power for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0274  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Abstract:

TC in R5-203694

Discussion:

r1

Decision: 		The document was revised to R5-204838.

R5-204838	Updating TP analysis for 6.2A.4-Configured output power for CA

Type: CR		For: Agreement
					38.905 v16.4.0	  CR-0274  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203695)

Decision: 		The document was agreed.

##### 5.3.15.9	TS 36.521-3

##### 5.3.15.10	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.15.11	Discussion Papers, Work Plan, TC lists

#### 5.3.16	High power UE (power class 2) for EN-DC (1 LTE TDD band + 1 NR TDD band) (UID-870062)  ENDC_UE_PC2_TDD_TDD-UEConTest

##### 5.3.16.1	TS 38.508-1

##### 5.3.16.2	TS 38.508-2

##### 5.3.16.3	TS 38.521-3

###### 5.3.16.3.1	Tx Requirements (Clause 6)

###### 5.3.16.3.2	Rx Requirements (Clause 7)

###### 5.3.16.3.3	Clauses 1-5, Annexes

##### 5.3.16.4	TS 38.522

##### 5.3.16.5	TR 38.905 (NR Test Points Radio Transmission and Reception)

##### 5.3.16.6	Discussion Papers, Work Plan, TC lists

#### 5.3.17	Even Further Mobility Enhancement for E-UTRAN (UID – 880066) LTE_feMob-UEConTest

##### 5.3.17.1	TS 36.508

##### 5.3.17.2	TS 36.521-2

##### 5.3.17.3	TS 36.521-3

##### 5.3.17.4	TR 36.903 (E-UTRAN RRM TT analyses)

##### 5.3.17.5	Discussion Papers, Work Plan, TC lists

#### 5.3.18	NR Mobility Enhancements (UID-880068)  NR_Mob_enh-UEConTest

##### 5.3.18.1	TS 38.508-1

##### 5.3.18.2	TS 38.508-2

##### 5.3.18.3	TS 38.522

##### 5.3.18.4	TS 38.533

##### 5.3.18.5	TR 38.903 (NR MU &  TT analyses)

##### 5.3.18.6	Discussion Papers, Work Plan, TC lists

#### 5.3.19	5G V2X with NR sidelink (UID-880069)  5G_V2X_NRSL_eV2XARC-UEConTest

##### 5.3.19.1	TS 38.508-1

##### 5.3.19.2	TS 38.508-2

##### 5.3.19.3	TS 38.509

##### 5.3.19.4	TS 38.521-1

###### 5.3.19.4.1	Tx Requirements (Clause 6)

###### 5.3.19.4.2	Rx Requirements (Clause 7)

###### 5.3.19.4.3	Clauses 1-5, Annexes

R5-204160	Updated to FR1 general clauses for NRSL eV2X

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0995  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

TS 38.101-1 v16.4.0 core spec alignment

Discussion:

r1

Decision: 		The document was revised to R5-204839.

R5-204839	Updated to FR1 general clauses for NRSL eV2X

Type: CR		For: Agreement
					38.521-1 v16.4.0	  CR-0995  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas

(Replaces R5-204160)

Decision: 		The document was agreed.

##### 5.3.19.5	TS 38.521-3

###### 5.3.19.5.1	Tx Requirements (Clause 6)

###### 5.3.19.5.2	Rx Requirements (Clause 7)

###### 5.3.19.5.3	Clauses 1-5, Annexes

R5-204161	Updated to EN-DC general clauses for NRSL eV2X

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0696  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

TS 38.101-3 v16.4.0 core spec alignment

Discussion:

r1

Decision: 		The document was revised to R5-204840.

R5-204840	Updated to EN-DC general clauses for NRSL eV2X

Type: CR		For: Agreement
					38.521-3 v16.4.0	  CR-0696  rev 1 Cat: F (Rel-16)

					Source: Bureau Veritas

(Replaces R5-204161)

Decision: 		The document was agreed.

##### 5.3.19.6	TS 38.521-4

###### 5.3.19.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

###### 5.3.19.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

###### 5.3.19.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.19.6.4	Clauses 1-4, Annexes

##### 5.3.19.7	TS 38.522

##### 5.3.19.8	TS 38.533

##### 5.3.19.9	TS 36.509

##### 5.3.19.10	TR 38.903 (NR MU &  TT analyses)

##### 5.3.19.11	TR 38.905 (NR Test Points Radio Transmission and Reception)

##### 5.3.19.12	Discussion Papers, Work Plan, TC lists

R5-203980	WF of V2X RF testing

Type: discussion		For: Information
					Source: Huawei, HiSilicon

Abstract:

Proposal 1: For non-concurrent transmission, test cases are tested with out-of-coverage assumption, and no NR/E-UTRA cell is involved.

Proposal 2: Only PC3 will be tested in R16 since PC2 requirements are not complete yet.

Proposal 3: No proper test point can be found for MOP testing. The test case structure can be created for future use, but the applicability will indicate the test case needs not to be tested and will not be used for conformance testing.

Proposal 4: Power requirements in 6.2E (MPR, A-MPR, configured output power) need to be tested for each physical channel.

Proposal 5: Tx test cases need to be defined for all Tx configurations: single layer 1Tx, single layer 2Tx and MIMO. For Rx test cases a common Tx configurations can be defined and used.

Proposal 6: For con-current transmission without exceptional requirements, a simplified testing approach will be adopted:

- The con-current test case can be skipped if corresponding test case in non-concurrent scenario has been tested;

- If the con-current test case needs to be tested, only V2X requirements will be tested, NR will only be setup as an anchor carrier and NR requirements will not be tested;

- A default configuration of NR will be defined and used throughout all the con-current test cases without exceptional requirements.

Proposal 7: For intra-band V2X configurations, a simplified testing approach will be adopted:

- The intra-band V2X test case can be skipped if corresponding test cases in LTE V2X and NR V2X have been tested; the LTE V2X and NR V2X test cases can be skipped if corresponding intra-band V2X test case has been tested.

- The test case definition can refer to TS 36.521-1 and TS 38.521-1 as much as possible;

Proposal 8: Intra-band contiguous and non-contiguous V2X configurations can share the same test case.

Proposal 9: For Inter-band V2X con-current testing, test case defining need to consider both E-UTRA Uu + NR SL and E-UTRA SL + NR Uu.

Discussion:

proposals 1, 6, 7, 8 need supporting companies.

2, 3, 4, 5, 9 can be noted, as dependent on RAN4.

Deferred.

r1

Huawei: ok to postpone proposal 6 to the next meeting.

Decision: 		The document was revised to R5-204975.

R5-204975	WF of V2X RF testing

Type: discussion		For: Information
					Source: Huawei, HiSilicon

(Replaces R5-203980)

Discussion:

"Revised from: R5-203980r1.

Noted proposals 1, 7, 8 endorsed to be implemented in the WP. Rest of the proposals to be considered during WP updates.

"

Decision: 		The document was noted.

#### 5.3.20	Enhancements on MIMO for NR (UID-880070)  NR_eMIMO-UEConTest

##### 5.3.20.1	TS 38.508-1

##### 5.3.20.2	TS 38.508-2

##### 5.3.20.3	TS 38.521-1

###### 5.3.20.3.1	Tx Requirements (Clause 6)

###### 5.3.20.3.2	Rx Requirements (Clause 7)

###### 5.3.20.3.3	Clauses 1-5, Annexes

##### 5.3.20.4	TS 38.521-2

###### 5.3.20.4.1	Tx Requirements (Clause 6)

###### 5.3.20.4.2	Rx Requirements (Clause 7)

###### 5.3.20.4.3	Clauses 1-5, Annexes

##### 5.3.20.5	TS 38.521-3

###### 5.3.20.5.1	Tx Requirements (Clause 6)

###### 5.3.20.5.2	Rx Requirements (Clause 7)

###### 5.3.20.5.3	Clauses 1-5, Annexes

##### 5.3.20.6	TS 38.521-4

###### 5.3.20.6.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

###### 5.3.20.6.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

###### 5.3.20.6.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.20.6.4	Clauses 1-4, Annexes

##### 5.3.20.7	TS 38.522

##### 5.3.20.8	TS 38.533

##### 5.3.20.9	TR 38.903 (NR MU &  TT analyses)

##### 5.3.20.10	TR 38.905 (NR Test Points Radio Transmission and Reception)

##### 5.3.20.11	Discussion Papers, Work Plan, TC lists

R5-203979	WF of eMIMO testing

Type: discussion		For: Information
					Source: Huawei, HiSilicon, Samsung

Abstract:

Basically this document is providing the latest progress in other WGs, and corresponding plan of testing coverage in RAN5. It’s for information only.

Discussion:

no proposals , Rapp to take up with WI supporting companies and TS rapp's to decide on the WP

Decision: 		The document was noted.

#### 5.3.21	UE Power Saving in NR (UID-880071)  NR_UE_pow_sav-UEConTest

##### 5.3.21.1	TS 38.508-1

##### 5.3.21.2	TS 38.508-2

##### 5.3.21.3	TS 38.521-4

###### 5.3.21.3.1	Conducted Demod Performance and CSI Reporting Requirements (Clauses 5&6)

###### 5.3.21.3.2	Radiated Demod Performance and CSI Reporting Requirements (Clauses 7&8)

###### 5.3.21.3.3	Interworking Demod Performance and CSI Reporting Requirements (Clauses 9&10)

###### 5.3.21.3.4	Clauses 1-4, Annexes

##### 5.3.21.4	TS 38.522

##### 5.3.21.5	TS 38.533

##### 5.3.21.6	Discussion Papers, Work Plan, TC lists

### 5.4	Routine Maintenance for LTE only TEIx_Test

#### 5.4.1	LTE RF

##### 5.4.1.1	TS 36.508

##### 5.4.1.2	TS 36.521-1

R5-203335	Addition of B34 into UE Category 1bis and update B41 UE Category 1bis

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5139  Cat: F (Rel-16)

					Source: CMCC

Decision: 		The document was agreed.

###### 5.4.1.2.1	Tx Requirements (Clause 6)

R5-203983	Cleaning up of V2X RB allocation for non-concurrent transmission

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5173  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204841.

R5-204841	Cleaning up of V2X RB allocation for non-concurrent transmission

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5173  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203983)

Decision: 		The document was agreed.

R5-203984	Cleaning up of V2X RB allocation for simultaneous transmission

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5174  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204842.

R5-204842	Cleaning up of V2X RB allocation for simultaneous transmission

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5174  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203984)

Decision: 		The document was agreed.

R5-203985	Cleaning up of V2X RB allocation for multi-carrier operation

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5175  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Discussion:

r1

Decision: 		The document was revised to R5-204843.

R5-204843	Cleaning up of V2X RB allocation for multi-carrier operation

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5175  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon

(Replaces R5-203985)

Decision: 		The document was agreed.

###### 5.4.1.2.2	Rx Requirements (Clause 7)

R5-203514	Editorial correction to 3DL CA test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5140  Cat: F (Rel-16)

					Source: TTA

Discussion:

r1

Decision: 		The document was revised to R5-204844.

R5-204844	Editorial correction to 3DL CA test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5140  rev 1 Cat: F (Rel-16)

					Source: TTA

(Replaces R5-203514)

Discussion:

WIC inverted on cover.

Decision: 		The document was revised to R5-204983.

R5-204983	Editorial correction to 3DL CA test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5140  rev 2 Cat: F (Rel-16)

					Source: TTA

(Replaces R5-204844)

Decision: 		The document was agreed.

R5-203738	Cleanup in test case 7.3EC, Reference sensitivity level for UE category M2

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5154  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204157	Correction to RF NB-IoT test cases

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5185  Cat: F (Rel-16)

					Source: Bureau Veritas

Decision: 		The document was agreed.

R5-204275	Corrections to Reference Sensitivity for CA

Type: CR		For: Agreement
					36.521-1 v16.5.0	  CR-5187  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Update of test point analysis in CR R5-204276

Decision: 		The document was agreed.

###### 5.4.1.2.3	Clauses 1-5, 8-10, Annexes

##### 5.4.1.3	TS 36.521-2

R5-203334	Correction of UE Category 1bis test case applicability

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0918  Cat: F (Rel-16)

					Source: CMCC

Discussion:

r2

Decision: 		The document was revised to R5-204976.

R5-204976	Correction of UE Category 1bis test case applicability

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0918  rev 1 Cat: F (Rel-16)

					Source: CMCC

(Replaces R5-203334)

Decision: 		The document was agreed.

R5-203744	Editorial correcting of format for table headings

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0920  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Editoral

Decision: 		The document was agreed.

R5-203889	Adding branch of PC3 and HPUE for 6.6.2.1 and 6.6.2.2 in Table 4.1-1

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0924  Cat: F (Rel-16)

					Source: CAICT

Decision: 		The document was agreed.

R5-203921	Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0925  Cat: F (Rel-16)

					Source: Google Inc.

Abstract:

Correction title and description to align with 36.521-1

Discussion:

r1

Decision: 		The document was revised to R5-204977.

R5-204977	Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0925  rev 1 Cat: F (Rel-16)

					Source: Google Inc.

(Replaces R5-203921)

Decision: 		The document was agreed.

R5-204000	Correction Additional Information in Table 4.2-1 of test case 9.2.56 and 9.2.57

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0926  Cat: F (Rel-16)

					Source: Google Inc.

Abstract:

Remove 9.2.49, 9.2.50, 9.2.53 and 9.2.54 in Additional Information of Table 4.2-1 with test case 9.2.56 and 9.2.57

Decision: 		The document was agreed.

R5-204159	Correction to applicability table of NB-IoT tests

Type: CR		For: Agreement
					36.521-2 v16.5.0	  CR-0927  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

TC tdoc R5-204158

Decision: 		The document was agreed.

##### 5.4.1.4	TS 36.521-3

R5-203997	Correction Test applicability of test case 9.2.56 and 9.2.57

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2524  Cat: F (Rel-16)

					Source: Google Inc.

Abstract:

Remove 9.2.49, 9.2.50, 9.2.53 and 9.2.54 since these test cases are empty.

Decision: 		The document was agreed.

R5-204024	Correction of Table 9.2.18.1.3-2 and Table 9.2.18.2.3-2

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2525  Cat: F (Rel-16)

					Source: Google Inc.

Abstract:

Correct table number and add a table content

Decision: 		The document was agreed.

R5-204026	Editorial update of Annex C.3.3.1

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2526  Cat: F (Rel-16)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204731.

R5-204731	Editorial update of Annex C.3.3.1

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2526  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-204026)

Decision: 		The document was agreed.

R5-204047	Correction to intra-frequency event triggered reporting test case in CEModeA

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2527  Cat: F (Rel-16)

					Source: Anritsu

Discussion:

R4-2009534 was agreed.

Decision: 		The document was agreed.

R5-204048	Correction to E-UTRAN HD-FDD Radio Link Monitoring Test for Out-of-sync in DRX for CE UE in CEmodeA

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2528  Cat: F (Rel-16)

					Source: Anritsu

Decision: 		The document was agreed.

R5-204108	Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2529  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in RRM test cases

Discussion:

r1

no file included?

r2

Decision: 		The document was revised to R5-204978.

R5-204978	Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2529  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204108)

Decision: 		The document was agreed.

R5-204109	Correction of RRM feMTC Test Case 5.1.34 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2530  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in RRM test cases

Decision: 		The document was agreed.

R5-204110	Correction of RRM feMTC Test Case 6.1.18 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2531  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in RRM test cases

Decision: 		The document was agreed.

R5-204111	Correction of RRM feMTC Test Case 7.3.69 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2532  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in RRM test cases

Decision: 		The document was agreed.

R5-204112	Correction of RRM feMTC Test Cases 8.4.12 - 15 including Test Tolerance

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2533  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in RRM test cases

Decision: 		The document was agreed.

R5-204113	Test Tolerances for RRM feMTC Test Cases in Annex F

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2534  Cat: F (Rel-16)

					Source: Ericsson

Abstract:

Test tolerance udpate in Annex F

Decision: 		The document was agreed.

R5-204158	Correction to test applicability of NB-IoT RRM tests

Type: CR		For: Agreement
					36.521-3 v16.5.0	  CR-2535  Cat: F (Rel-16)

					Source: Bureau Veritas

Abstract:

applicability condition tdoc R5-204159

Decision: 		The document was agreed.

##### 5.4.1.5	RRM Test & Radio Reception Test Tolerances

###### 5.4.1.5.1	TR 36.903 (E-UTRAN RRM TT analyses)

R5-204114	Test Tolerance analysis for E-UTRAN HD-FDD inter frequency handover for Cat-M1 UEs in CEModeA test case

Type: CR		For: Agreement
					36.903 v15.3.0	  CR-0440  Cat: F (Rel-15)

					Source: Ericsson

Abstract:

Test tolerance analysis

Decision: 		The document was agreed.

R5-204115	Test Tolerance analysis for E-UTRAN HD-FDD Inter frequency RRC Re-establishment for Cat-M1 UE in CEModeA test case

Type: CR		For: Agreement
					36.903 v15.3.0	  CR-0441  Cat: F (Rel-15)

					Source: Ericsson

Abstract:

Test tolerance analysis

Decision: 		The document was agreed.

###### 5.4.1.5.2	TR 36.904 (E-UTRAN Radio Reception TT analyses)

###### 5.4.1.5.3	TR 36.905 (E-UTRAN Test Points Radio Transmission and Reception )

R5-204276	Update of test point analysis for CA_3A-7B

Type: CR		For: Agreement
					36.905 v16.4.0	  CR-0239  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Abstract:

Update of the test case in CR R5-204275

Decision: 		The document was agreed.

##### 5.4.1.6	TS 34.121-1

##### 5.4.1.7	TS 34.121-2

##### 5.4.1.8	TS 34.122

##### 5.4.1.9	TS 34.108

##### 5.4.1.10	TR 34.902 (UTRAN RRM Test Tolerance analyses)

##### 5.4.1.11	Discussion Papers, Work Plan, TC lists

### 5.5	Other Routine Maintenance TEIx_Test

#### 5.5.1	TS 34.108

#### 5.5.2	TS 34.121-1 All sections other than annexes

#### 5.5.3	TS 34.121-1 Annexes only

#### 5.5.4	TS 34.121-2

R5-204045	Update release applicability of TC 9.2.2D

Type: CR		For: Agreement
					34.121-2 v15.0.0	  CR-0178  Cat: F (Rel-15)

					Source: MediaTek Inc.

Decision: 		The document was revised to R5-204732.

R5-204732	Update release applicability of TC 9.2.2D

Type: CR		For: Agreement
					34.121-2 v15.0.0	  CR-0178  rev 1 Cat: F (Rel-15)

					Source: MediaTek Inc.

(Replaces R5-204045)

Decision: 		The document was agreed.

#### 5.5.5	TS 34.122

#### 5.5.6	TS 34.171

#### 5.5.7	TS 34.172

#### 5.5.8	TS 34.114

#### 5.5.9	TS 37.571-1

R5-204020	Clarification on frequency band test conditions for A-GNSS

Type: CR		For: Agreement
					37.571-1 v16.5.0	  CR-0309  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Discussion:

r1

R&S: why is it not possible at this stage to define the NR frequency band and frequency range test conditions for EN-DC? It is affecting validated test cases in an active GCF Work Item.

Decision: 		The document was revised to R5-204979.

R5-204979	Clarification on frequency band test conditions for A-GNSS

Type: CR		For: Agreement
					37.571-1 v16.5.0	  CR-0309  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204020)

Decision: 		The document was agreed.

#### 5.5.10	TS 37.571-3

#### 5.5.11	TS 37.571-5

#### 5.5.12	TS 51.010-1 (RF/Performance)

#### 5.5.13	TS 51.010-2 (RF/Performance)

#### 5.5.14	TS 51.010-7 (RF/Performance)

#### 5.5.15	TS 37.544

#### 5.5.16	Discussion Papers, Work Plan, TC lists

### 5.6	Outgoing liaison statements for provisional approval

R5-204847	LS response on Multiband relaxation for FR2 on testability analysis of MBR

Type: LS out		For: Approval
					to GCF CAG, PTCRB PVG
					Source: TSG WG RAN5

Discussion:

deadline in 2 weeks, 9.9.

Decision: 		The document was for email approval.

### 5.7	AOB

## 6	Signalling Protocol Functional Area

### 6.1	Review action points (fm A.I. 2.1)

### 6.2	Review incoming LS (fm A.I. 3) & new subject discussion papers

R5-203219	LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level

Type: LS in		For: Action
					Original outgoing LS: MCC-JTF-20-062r2, to -, cc -
					Source: GCF-TCCA Joint Taskforce #8

Abstract:

GCF and TCCA have created a temporary joint taskforce to pave the way for formal LTE/5G Mission Critical Services (MCX) testing and certification. The initial focus of the taskforce is to create a certification programme for (LTE) mission critical products.

As part of the task force activities a survey amongst its members (85 representatives from 39 organisations  with a good representation of the mission critical industry) was conducted. The question of the survey was on which 3GPP Release they will base their implementation and deployments.

The survey was filled out by 33 organisations (14 were vendor and 19 were from purchasing organisations like public safety operators, government authorities or public safety end users).

The outcome of the survey is depicted in Figure 1

Please note that some responses have ticked more than one release. All response, who have selected Rel-14 have also selected Rel-15, except 2 responses.

In its meeting #7 the taskforce discussed – based on the survey results – about the starting 3GPP Release for certification. A majority expects formal MCX testing and certification from Release 15 onwards. The GCF-TCCA joint taskforce decided to start MCX certification based on Release-15.

Later Releases (Release-16 onwards) will be considered and included into the certification in due time.

Until the 3GPP conformance test specifications for Release-15 are available, the usage of Release-13 or Release-14 conformance test specifications may be considered for MCX Certification as long as the signalling is backward/forward compatible with Release-15,

Actions: The GCF-TCCA Joint Taskforce kindly ask 3GPP RAN5 to:

1.	Take the results from the survey into account and take action to align the MCX related 3GPP RAN5 conformance test specifications 3GPP TS 36.579-x with Release-15.

The (temporary) GCF-TCCA Joint Task Force was closed in June 2020.

Its activities will be continued by the permanent GCF Mission Critical Agreement Group (MCAG).

TCCA will continue to support the MCAG and Mission Critical related certification activities.

Discussion:

moved to SIG.

New WIP submitted for Rel-15 update of MCX RAN5 test specs

Discussions on maintenace of Rel-13 & Rel-14 TTCN to be concluded via email.

Samsung to prepare response LS to GCF MCAG.

Decision: 		The document was noted.

### 6.3	Open Work Items

#### 6.3.1	Rel-14 LTE CA configurations (UID - 720098) LTE_CA_R14-UEConTest

##### 6.3.1.1	TS 36.508

##### 6.3.1.2	TS 36.523-1

##### 6.3.1.3	TS 36.523-2

##### 6.3.1.4	TS 36.523-3

##### 6.3.1.5	Discussion Papers, Work Plan, TC lists

#### 6.3.2	5G system with NR and LTE (UID - 760087) 5GS_NR_LTE-UEConTest

##### 6.3.2.1	TS 38.508-1

R5-203275	Editorial update IE ARFCN-ValueNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1364  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203357	Correction to Table 4.5.2.2-2-second SMC procedure for Selected EPS NAS security algorithms IE

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1389  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203358	Correction to Table 4.6.1-17 RRCResume

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1390  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

merge R5-203652.

r2

Decision: 		The document was revised to R5-204386.

R5-204386	Correction to Table 4.6.1-17 RRCResume

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1390  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203358)

Decision: 		The document was agreed.

R5-203359	Correction to Table 4.6.3-141 ReportConfigInterRAT

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1391  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203360	Correction to Table 4.6.3-142 ReportConfigNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1392  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

change has no effect.

Decision: 		The document was withdrawn.

R5-203361	Correction to Table 4.7.1-26 SECURITY MODE COMPLETE

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1393  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Keysight

Discussion:

comment from Samsung which did not agree to some aspects.

Orange objected. Qualcomm also preferred to postpone to next meeting, as >30 TCs are impacted. CT1 feedback would be needed.

Decision: 		The document was withdrawn.

R5-203362	Correction to Table 4.9.9.2.3-2 TRACKING AREA UPDATE REQUEST

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1394  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

R5-203499 has included this change.

Decision: 		The document was withdrawn.

R5-203455	Corrections to 4.5.1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1399  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203456	Updating usages of TS 34.229-1 to TS 34.229-5

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1400  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203484	Corrections to generic procedures for MO and MT speech call establishment

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1406  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

fix references to step number ranges as reported by the TF160 manager.

r2

Decision: 		The document was revised to R5-204387.

R5-204387	Corrections to generic procedures for MO and MT speech call establishment

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1406  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203484)

Decision: 		The document was agreed.

R5-203497	Correction to USIM configurations 7 and 13

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1407  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

r1

Decision: 		The document was revised to R5-204388.

R5-204388	Correction to USIM configurations 7 and 13

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1407  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK

(Replaces R5-203497)

Decision: 		The document was agreed.

R5-203498	Correction to switch off / power off procedures for IMS

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1408  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd, Qualcomm Incorporated

Discussion:

r1

Decision: 		The document was revised to R5-204389.

R5-204389	Correction to switch off / power off procedures for IMS

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1408  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd, Qualcomm Incorporated

(Replaces R5-203498)

Decision: 		The document was agreed.

R5-203499	Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1409  Cat: F (Rel-16)

					Source: Keysight Technologies UK, Huawei/HiSilicon

Discussion:

add co-author

Decision: 		The document was revised to R5-204384.

R5-204384	Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1409  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK, Huawei/HiSilicon

(Replaces R5-203499)

Decision: 		The document was agreed.

R5-203500	Update to Table 4.6.3-74: MeasObjectEUTRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1410  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203533	Update to PDSCH-ServingCellConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1417  Cat: F (Rel-16)

					Source: MCC TF160, Keysight Technologies UK

Decision: 		The document was agreed.

R5-203534	Updates to CellGroupConfig and RNTI-Value for NR-DC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1418  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203574	Correction of description of NGEN-DC in table 4.5.1-1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1421  Cat: F (Rel-16)

					Source: Tejet

Discussion:

was wrong WIC.

r1

Decision: 		The document was revised to R5-204390.

R5-204390	Correction of description of NGEN-DC in table 4.5.1-1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1421  rev 1 Cat: F (Rel-16)

					Source: Tejet

(Replaces R5-203574)

Decision: 		The document was agreed.

R5-203585	Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1425  Cat: F (Rel-16)

					Source: MediaTek Inc., Keysight Technologies

Discussion:

r2

Decision: 		The document was revised to R5-204391.

R5-204391	Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1425  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc., Keysight Technologies

(Replaces R5-203585)

Decision: 		The document was agreed.

R5-203587	Correction to test procedure of Table 4.9.9.2.2-1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1426  Cat: F (Rel-16)

					Source: MediaTek Inc., Keysight Technologies

Decision: 		The document was withdrawn.

R5-203588	Correction to NR inter-band CA configurations in FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1427  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

cover issues.

Decision: 		The document was revised to R5-204378.

R5-204378	Correction to NR inter-band CA configurations in FR1

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1427  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203588)

Decision: 		The document was agreed.

R5-203652	Corrections to Default contents of RRCResume message

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1430  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Discussion:

done in Huawei CR R5-203358r1.

Decision: 		The document was withdrawn.

R5-203653	Corrections to Generic procedure 4.9.9

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1431  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

Samsung CR for Multi PDN extension handles the change already.

Decision: 		The document was withdrawn.

R5-203662	Removal of USIM profile #16

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1432  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

R5-203704	Correction to Table 4.6.3-87 NZP-CSI-RS-ResourceSet

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1438  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203715	Addition of Generic Test Procedure for IMS MO SMS in 5GC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1439  Cat: F (Rel-16)

					Source: ZTE

Discussion:

new clause nr. xx has to be resolved!

r1

Decision: 		The document was revised to R5-204392.

R5-204392	Addition of Generic Test Procedure for IMS MO SMS in 5GC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1439  rev 1 Cat: F (Rel-16)

					Source: ZTE

(Replaces R5-203715)

Decision: 		The document was agreed.

R5-203716	Addition of Generic Test Procedure for IMS MT SMS in 5GC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1440  Cat: F (Rel-16)

					Source: ZTE

Discussion:

new clause nr. xx has to be resolved!

r1

Decision: 		The document was revised to R5-204393.

R5-204393	Addition of Generic Test Procedure for IMS MT SMS in 5GC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1440  rev 1 Cat: F (Rel-16)

					Source: ZTE

(Replaces R5-203716)

Decision: 		The document was agreed.

R5-203729	Update IE RACH-ConfigGeneric

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1443  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203743	Update IE RLC-BearerConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1446  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204394.

R5-204394	Update IE RLC-BearerConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1446  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203743)

Decision: 		The document was agreed.

R5-203755	Update IE SchedulingRequestResourceConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1447  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203774	Add Annex D

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1453  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was withdrawn.

R5-203796	Correction of EN-DC test frequency information for protocol testing

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1456  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203813	Correction to PUCCH-Config

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1457  Cat: F (Rel-16)

					Source: ANRITSU LTD

Decision: 		The document was agreed.

R5-204021	Correction of n51 and n76 test frequencies for protocol testing

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1469  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204038	Corrections of test frequency tables for EN-DC configuration DC_(n)41AA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1471  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204039	Corrections of test frequency tables for EN-DC configuration DC_(n)71AA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1472  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204043	Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1474  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

r1

Decision: 		The document was revised to R5-204385.

R5-204385	Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1474  rev 1 Cat: F (Rel-16)

					Source: ANRITSU LTD

(Replaces R5-204043)

Decision: 		The document was withdrawn.

R5-204092	Update IE ServingCellConfigCommon

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1480  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was withdrawn.

R5-204134	Update IE SIB2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1481  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204395.

R5-204395	Update IE SIB2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1481  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204134)

Decision: 		The document was agreed.

R5-204135	New procedure for PDU Session Release

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1482  Cat: F (Rel-16)

					Source: MCC TF160

Discussion:

r1

Decision: 		The document was revised to R5-204396.

R5-204396	New procedure for PDU Session Release

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1482  rev 1 Cat: F (Rel-16)

					Source: MCC TF160

(Replaces R5-204135)

Decision: 		The document was agreed.

R5-204137	Update to FreqBandList

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1483  Cat: F (Rel-16)

					Source: MCC TF160, Qualcomm, Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204397.

R5-204397	Update to FreqBandList

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1483  rev 1 Cat: F (Rel-16)

					Source: MCC TF160, Qualcomm, Anritsu

(Replaces R5-204137)

Decision: 		The document was agreed.

R5-204150	Update Table 5.4.2.0-2: ServingCellConfigCommon

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1484  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-204169	Update IE ServingCellConfigCommon

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1490  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204398.

R5-204398	Update IE ServingCellConfigCommon

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1490  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204169)

Decision: 		The document was agreed.

R5-204238	Correction to default contents of RRCReestablishmentRequest message

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1493  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

R5-204324	Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1494  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204399.

R5-204399	Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1494  rev 1 Cat: F (Rel-16)

					Source: Samsung

(Replaces R5-204324)

Decision: 		The document was agreed.

R5-204325	Adding procedure for establishment of multiple additional PDN connections in EPS (S1 mode)

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1495  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

R5-204326	Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1496  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204400.

R5-204400	Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1496  rev 1 Cat: F (Rel-16)

					Source: Samsung

(Replaces R5-204326)

Decision: 		The document was agreed.

R5-204327	Updates to Test procedure for UE for Tracking area updating / Inter-system change from N1 mode to S1 mode in 5GMM/EMM-IDLE mode

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1497  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

R5-204328	Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1498  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

r2

Decision: 		The document was revised to R5-204401.

R5-204401	Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1498  rev 1 Cat: F (Rel-16)

					Source: Samsung

(Replaces R5-204328)

Decision: 		The document was agreed.

R5-204329	Update of 4.5A.2 UE-requested PDU session establishment procedure

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1499  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

R5-204330	Updates Procedure to UE-requested PDU session modification after the first S1 to N1 mode change

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1500  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

R5-204331	Void 4.9.14 Procedure for UE-requested PDU session modification after the first S1 to N1 mode change

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1501  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

##### 6.3.2.2	TS 38.508-2

R5-203457	Fixing References

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0088  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203463	Addition of PICs for CSI-RS measurement without associated SSB

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0089  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203891	Introduction of Inter-band measurements capabilities for signalling test cases

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0093  Cat: F (Rel-16)

					Source: CAICT

Discussion:

empty cover

Decision: 		The document was withdrawn.

R5-204205	Addition and update of PICS

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0106  Cat: F (Rel-16)

					Source: Lenovo, Motorola Mobility

Discussion:

late doc

r2

Decision: 		The document was revised to R5-204544.

R5-204544	Addition and update of PICS

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0106  rev 1 Cat: F (Rel-16)

					Source: Lenovo, Motorola Mobility

(Replaces R5-204205)

Decision: 		The document was agreed.

R5-204332	Adding new ICS for handling inter-system change S1-N1 and aligning PDN and PDU handling

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0108  Cat: F (Rel-16)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

##### 6.3.2.3	TS 38.509

R5-204344	TMC Integrity and Ciphering Protection

Type: CR		For: Agreement
					38.509 v15.8.0	  CR-0031  Cat: F (Rel-15)

					Source: Apple

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204402.

R5-204402	TMC Integrity and Ciphering Protection

Type: CR		For: Agreement
					38.509 v15.8.0	  CR-0031  rev 1 Cat: F (Rel-15)

					Source: Apple

(Replaces R5-204344)

Decision: 		The document was agreed.

##### 6.3.2.4	TS 38.523-1

###### 6.3.2.4.1	Clauses 1 - 5

###### 6.3.2.4.2	Idle Mode (Clause 6)

R5-203363	Correction to NR TC 6.1.1.1-PLMN selection in automatic mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1590  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203364	Addition of NR TC 6.1.1.1a-PLMN selection in automatic mode Single Frequency operation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1591  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

"TF160 request to flag

Industry need of 'Single Frequency operation' not established "

Decision: 		The document was withdrawn.

R5-203365	Correction to NR TC 6.1.1.2-access technology combinations

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1592  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204403.

R5-204403	Correction to NR TC 6.1.1.2-access technology combinations

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1592  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203365)

Decision: 		The document was agreed.

R5-203366	Addition of NR TC 6.1.1.2a-PLMN selection of Other PLMN in automatic mode Single Frequency operation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1593  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

"TF160 request to flag

Industry need of 'Single Frequency operation' not established"

Decision: 		The document was withdrawn.

R5-203367	Correction to NR TC 6.1.1.5-PLMN selection in Automatic mode User reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1594  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203368	Addition of NR TC 6.1.1.5a-PLMN selection in Automatic mode User reselection Single Frequency operation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1595  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

"TF160 request to flag

Industry need of 'Single Frequency operation' not established"

Decision: 		The document was withdrawn.

R5-203369	Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1596  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204404.

R5-204404	Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1596  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203369)

Decision: 		The document was agreed.

R5-203370	Addition of NR TC 6.1.1.7a-PLMN selection of RPLMN or HPLMN in Automatic mode Single Frequency operation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1597  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

"TF160 request to flag

Industry need of 'Single Frequency operation' not established"

Decision: 		The document was withdrawn.

R5-203371	Correction to NR TC 6.1.2.19-Speed-dependent cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1598  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Keysight

Discussion:

r1

Decision: 		The document was revised to R5-204405.

R5-204405	Correction to NR TC 6.1.2.19-Speed-dependent cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1598  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Keysight

(Replaces R5-203371)

Decision: 		The document was agreed.

R5-203372	Correction to NR TC 6.1.2.21-Cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1599  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203373	Correction to NR TC 6.1.2.23-Cell Reselection MFBI

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1600  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203374	Correction to NR TC 6.2.1.1-Selection of correct RAT for OPLMN

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1601  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203375	Correction to NR TC 6.2.1.4-Inter-RAT PLMN Selection with Manual mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1602  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203376	Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1603  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204406.

R5-204406	Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1603  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203376)

Decision: 		The document was agreed.

R5-203377	Correction to NR TC 6.2.3.9-Inter-RAT Speed Dependent Cell Reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1604  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203378	Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1605  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204407.

R5-204407	Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1605  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203378)

Decision: 		The document was agreed.

R5-203379	Correction to NR TC 6.3.1.2-SOR during registration with security check successful but  no requested acknowledgement

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1606  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204408.

R5-204408	Correction to NR TC 6.3.1.2-SOR during registration with security check successful but  no requested acknowledgement

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1606  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203379)

Decision: 		The document was agreed.

R5-203380	Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1607  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester, ZTE

Discussion:

r1

changes in R5-203428 have been merged into this CR.

Decision: 		The document was revised to R5-204543.

R5-204543	Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1607  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester, ZTE

(Replaces R5-203380)

Decision: 		The document was agreed.

R5-203381	Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1608  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204409.

R5-204409	Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1608  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203381)

Decision: 		The document was agreed.

R5-203382	Correction to NR TC 6.4.1.1-PLMN Selection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1609  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203428	Correction to Idle Mode SoR TC 6.3.1.3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1644  Cat: F (Rel-16)

					Source: ZTE Corporation

Discussion:

merged into R5-203380.

Decision: 		The document was withdrawn.

R5-203429	Correction to Idle Mode SoR TC 6.3.1.7

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1645  Cat: F (Rel-16)

					Source: ZTE Corporation, Huawei, Hisilicon

Discussion:

r1

feedback from Qualcomm.

r2

Decision: 		The document was revised to R5-204410.

R5-204410	Correction to Idle Mode SoR TC 6.3.1.7

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1645  rev 1 Cat: F (Rel-16)

					Source: ZTE Corporation, Huawei, Hisilicon

(Replaces R5-203429)

Decision: 		The document was agreed.

R5-203478	Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1647  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204411.

R5-204411	Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1647  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203478)

Decision: 		The document was agreed.

R5-203481	Correction to NR TC 6.1.1.4-PLMN selection in shared network environment

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1648  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203501	Correction to 5G NR Idle mode Speed-dependent Cell reselection test case 6.1.2.19

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1651  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

merged in Huawei’s R5-203371.

Decision: 		The document was withdrawn.

R5-203502	Correction to 5G NR Idle mode test case 6.4.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1652  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203565	Correction to NR TC 6.2.2.1-N2L cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1669  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204412.

R5-204412	Correction to NR TC 6.2.2.1-N2L cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1669  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203565)

Decision: 		The document was agreed.

R5-203566	Correction to NR TC 6.2.2.2-L2N cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1670  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204413.

R5-204413	Correction to NR TC 6.2.2.2-L2N cell reselection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1670  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203566)

Decision: 		The document was agreed.

R5-203590	Correction to the power level of Idle mode test cases

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1677  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

ME!

r3

Decision: 		The document was revised to R5-204414.

R5-204414	Correction to the power level of Idle mode test cases

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1677  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203590)

Decision: 		The document was agreed.

R5-203591	Correction to Idle mode test case 6.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1678  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

cover issues.

Decision: 		The document was revised to R5-204379.

R5-204379	Correction to Idle mode test case 6.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1678  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203591)

Discussion:

agreed.

wrong Tdoc nr.

Decision: 		The document was revised to R5-204545.

R5-204545	Correction to Idle mode test case 6.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1678  rev 2 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-204379)

Decision: 		The document was agreed.

R5-203593	Correction to Idle mode test case 6.1.2.9

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1680  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

cover issues.

Decision: 		The document was revised to R5-204380.

R5-204380	Correction to Idle mode test case 6.1.2.9

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1680  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203593)

Decision: 		The document was agreed.

R5-203594	Correction to NR TC 6.3.1.8-SOR after registration with Automatic PLMN selection mode

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1681  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was withdrawn.

R5-203648	Editorial updates to NR5G Idle Mode TC 6.1.2.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1690  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

R5-203654	Corrections to NR5G Idle Mode TC 6.4.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1693  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

r1

Decision: 		The document was revised to R5-204415.

R5-204415	Corrections to NR5G Idle Mode TC 6.4.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1693  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-203654)

Decision: 		The document was agreed.

R5-203661	Corrections to NR5G Idle Mode TC 6.1.2.13

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1700  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

r2

Decision: 		The document was revised to R5-204416.

R5-204416	Corrections to NR5G Idle Mode TC 6.1.2.13

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1700  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-203661)

Decision: 		The document was agreed.

R5-203745	Correction to 5G NR Idle mode test case 6.4.3.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1721  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203746	Correction to 5G NR Idle mode inter-RAT test cases

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1722  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

r1

Decision: 		The document was revised to R5-204417.

R5-204417	Correction to 5G NR Idle mode inter-RAT test cases

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1722  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK

(Replaces R5-203746)

Decision: 		The document was agreed.

R5-203810	Correction to NR5GC test case 6.1.2.9

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1729  Cat: F (Rel-16)

					Source: ANRITSU LTD

Decision: 		The document was agreed.

R5-204015	Correction of NR TC 6.2.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1733  Cat: F (Rel-16)

					Source: TDIA, CATT

Decision: 		The document was agreed.

R5-204018	Correction of NR TC 6.2.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1735  Cat: F (Rel-16)

					Source: TDIA, CATT

Decision: 		The document was agreed.

###### 6.3.2.4.3	Layer 2

6.3.2.4.3.1	NR Layer 2

6.3.2.4.3.1.1	Common Test Case Specific Values for Layer 2 (Clause 7.1.0)

6.3.2.4.3.1.2	MAC

R5-203383	Correction to NR TC 7.1.1.1.1-Correct selection of RACH parameters

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1610  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203384	Correction to NR TC  7.1.1.4.1.3 and 7.1.1.4.1.4-DL TBS param combination leading to ambiguity

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1611  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

no rev marks! late doc

planned to provide the {I_MCS, N_PRB, L} combination leading to 3824.0 < N_info < 3825.0.

Decision: 		The document was withdrawn.

R5-203385	Correction to NR TC  7.1.1.4.2.4 and 7.1.1.4.2.5-UL TBS param combination leading to ambiguity

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1612  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

no rev marks! late doc

had planned to provide the {I_MCS, N_PRB, L} combination leading to 3824.0 < N_info < 3825.0.

withdrawn!

Decision: 		The document was withdrawn.

R5-203386	Correction to NR TC 7.1.1.9.1-MAC Reset

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1613  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204418.

R5-204418	Correction to NR TC 7.1.1.9.1-MAC Reset

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1613  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203386)

Decision: 		The document was agreed.

R5-203387	Correction to NR TC 7.1.1.2.2-PDSCH Aggregation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1614  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204419.

R5-204419	Correction to NR TC 7.1.1.2.2-PDSCH Aggregation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1614  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203387)

Decision: 		The document was agreed.

R5-203513	Correction to NR MAC test case 7.1.1.5.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1656  Cat: F (Rel-16)

					Source: Keysight Technologies UK, Starpoint

Discussion:

r1

Decision: 		The document was revised to R5-204420.

R5-204420	Correction to NR MAC test case 7.1.1.5.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1656  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK, Starpoint

(Replaces R5-203513)

Decision: 		The document was agreed.

R5-203524	Corrections to NR MAC Test Case 7.1.1.5.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1661  Cat: F (Rel-16)

					Source: Starpoint, TDIA

Decision: 		The document was agreed.

R5-203567	Correction to NR TC 7.1.1.1.2-Random access procedure for Preamble selected by MAC itself

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1671  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203649	Corrections to NR5G BWP TC 7.1.1.8.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1691  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, MCC TF160, Anritsu Ltd, Rohde & Schwarz

Decision: 		The document was agreed.

R5-203655	Corrections to NR5G MAC TC 7.1.1.2.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1694  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

r2

Comments from MCC TF160 and Rohde & Schwarz are handled.

Decision: 		The document was revised to R5-204421.

R5-204421	Corrections to NR5G MAC TC 7.1.1.2.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1694  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-203655)

Decision: 		The document was agreed.

R5-203656	Corrections to NR5G MAC DRX TC 7.1.1.5.3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1695  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Decision: 		The document was agreed.

R5-203659	Corrections to NR5G MAC TC 7.1.1.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1698  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Decision: 		The document was agreed.

R5-203660	Corrections to NR5G MAC TC 7.1.1.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1699  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Discussion:

r1

Decision: 		The document was revised to R5-204422.

R5-204422	Corrections to NR5G MAC TC 7.1.1.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1699  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

(Replaces R5-203660)

Decision: 		The document was agreed.

R5-204206	Addition of NR-DC MAC Test Case

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1743  Cat: F (Rel-16)

					Source: Lenovo, Motorola Mobility

Discussion:

late doc

r1

*.docx! +editorial

Decision: 		The document was revised to R5-204423.

R5-204423	Addition of NR-DC MAC Test Case

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1743  rev 1 Cat: F (Rel-16)

					Source: Lenovo, Motorola Mobility

(Replaces R5-204206)

Decision: 		The document was agreed.

6.3.2.4.3.1.3	RLC

R5-203388	Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1615  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Reduce the test case execution time by maximizing the number of RLC PDUs sent in each RLC PDU List.

Decision: 		The document was revised to R5-204424.

R5-204424	Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1615  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203388)

Decision: 		The document was withdrawn.

R5-203535	Splitting and updates to NR RLC test case 7.1.2.3.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1662  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203536	Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1663  Cat: F (Rel-16)

					Source: MCC TF160

Discussion:

Keysight UK: not able to pass the test case and execution time has also increased.

r1

Decision: 		The document was revised to R5-204425.

R5-204425	Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1663  rev 1 Cat: F (Rel-16)

					Source: MCC TF160

(Replaces R5-203536)

Decision: 		The document was withdrawn.

R5-203705	Correction to NR test case 7.1.2.2.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1707  Cat: F (Rel-16)

					Source: ZTE

Discussion:

change is not needed.

Decision: 		The document was withdrawn.

R5-203706	Correction to NR test case 7.1.2.3.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1708  Cat: F (Rel-16)

					Source: ZTE

Decision: 		The document was agreed.

R5-204107	Correction to NR test case 7.1.2.3.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1740  Cat: F (Rel-16)

					Source: ZTE

Decision: 		The document was agreed.

6.3.2.4.3.1.4	PDCP

R5-203596	Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1682  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r5

Transmission of SRs in the original proposal was found to be unnecessary and was removed!

Decision: 		The document was revised to R5-204426.

R5-204426	Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1682  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203596)

Decision: 		The document was agreed.

R5-203597	Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1683  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

Decision: 		The document was revised to R5-204427.

R5-204427	Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1683  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203597)

Decision: 		The document was withdrawn.

R5-203598	Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1684  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

Decision: 		The document was revised to R5-204428.

R5-204428	Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1684  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203598)

Decision: 		The document was withdrawn.

R5-203707	Correction to NR test case 7.1.3.5.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1709  Cat: F (Rel-16)

					Source: ZTE

Discussion:

r1

Decision: 		The document was revised to R5-204429.

R5-204429	Correction to NR test case 7.1.3.5.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1709  rev 1 Cat: F (Rel-16)

					Source: ZTE

(Replaces R5-203707)

Decision: 		The document was agreed.

R5-203749	Update to test case NR5GC 7.1.3.5.3 (NR-DC)

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1724  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204430.

R5-204430	Update to test case NR5GC 7.1.3.5.3 (NR-DC)

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1724  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203749)

Decision: 		The document was agreed.

R5-204363	Corrections to NR5G PDCP TC 7.1.3.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1755  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.3.1.5	SDAP

R5-203708	Correction to NR test case 7.1.4.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1710  Cat: F (Rel-16)

					Source: ZTE

Discussion:

merged into R5-203750.

Decision: 		The document was withdrawn.

R5-203750	Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1725  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, ZTE

Discussion:

r1

feedback from TF160.

Decision: 		The document was revised to R5-204431.

R5-204431	Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1725  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, ZTE

(Replaces R5-203750)

Decision: 		The document was agreed.

###### 6.3.2.4.4	RRC

6.3.2.4.4.1	NR RRC

6.3.2.4.4.2	MR-DC RRC

6.3.2.4.4.1.1	RRC Connection Management Procedures (clause 8.1.1)

R5-203389	Correction to NR TC 8.1.1.3.1-Redirection to another NR frequency

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1616  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203390	Correction to NR TC 8.1.1.3.3-With priority information

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1617  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204432.

R5-204432	Correction to NR TC 8.1.1.3.3-With priority information

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1617  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203390)

Decision: 		The document was agreed.

R5-203391	Correction to NR TC 8.1.1.4.1-RRC Resume Success

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1618  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

Merged into QC’s CR R5-204236

Decision: 		The document was withdrawn.

R5-203603	Addition of new RRC TC for checking extended / spare field handling in SI

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1685  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

wrong AI

is *.docx

r2

Decision: 		The document was revised to R5-204433.

R5-204433	Addition of new RRC TC for checking extended / spare field handling in SI

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1685  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203603)

Decision: 		The document was agreed.

R5-203645	Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1689  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

cover issues.

Decision: 		The document was revised to R5-204381.

R5-204381	Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1689  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203645)

Decision: 		The document was agreed.

R5-203747	Correction to NR RRC IRAT test case 8.1.1.3.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1723  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

r1

Decision: 		The document was revised to R5-204434.

R5-204434	Correction to NR RRC IRAT test case 8.1.1.3.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1723  rev 1 Cat: F (Rel-16)

					Source: Keysight Technologies UK

(Replaces R5-203747)

Decision: 		The document was agreed.

R5-204029	Correction to NR5GC testcase 8.1.1.3.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1737  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm

Discussion:

r3

Decision: 		The document was revised to R5-204435.

R5-204435	Correction to NR5GC testcase 8.1.1.3.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1737  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm

(Replaces R5-204029)

Decision: 		The document was agreed.

R5-204236	Correction to NR5G RRC TC 8.1.1.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1745  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

was wrong AI.

r1

Decision: 		The document was revised to R5-204436.

R5-204436	Correction to NR5G RRC TC 8.1.1.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1745  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204236)

Decision: 		The document was agreed.

6.3.2.4.4.2.1	RRC UE Capability / Others (clause 8.2.1)

6.3.2.4.4.1.2	RRC Reconfiguration (clause 8.1.2)

R5-204372	Correction to NR5GC CA RRC test cases 8.1.2.1.5.x

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1756  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)

R5-203392	Correction to NR TC 8.1.X on SINR related configuration

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1619  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204437.

R5-204437	Correction to NR TC 8.1.X on SINR related configuration

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1619  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203392)

Decision: 		The document was agreed.

R5-203393	Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1620  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204438.

R5-204438	Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1620  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203393)

Decision: 		The document was agreed.

R5-203394	Correction to NR TC 8.1.3.1.15A-Intra NR measurements Blacklisting

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1621  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)

R5-203397	Correction to ENDC TC 8.2.2.1.1-SRB3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1624  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Starpoint

Decision: 		The document was agreed.

R5-203398	Addition of NRDC TC 8.2.2.1.2-SRB3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1625  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203399	Addition of NRDC TC 8.2.2.3.2-Simultaneous SRB3 and Split SRB

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1626  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

TC 8.2.2.3.2 is agreed to be removed from WP?

Decision: 		The document was withdrawn.

R5-203400	Correction to ENDC TC 8.2.2.6.1-PDCP version change

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1627  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Starpoint

Discussion:

r2

Decision: 		The document was revised to R5-204439.

R5-204439	Correction to ENDC TC 8.2.2.6.1-PDCP version change

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1627  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Starpoint

(Replaces R5-203400)

Decision: 		The document was agreed.

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)

R5-203464	Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1646  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204440.

R5-204440	Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1646  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203464)

Decision: 		The document was agreed.

R5-203482	Addition of new test purpose to test case 8.1.3.1.23

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1649  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

*.docx !

r1

Decision: 		The document was revised to R5-204441.

R5-204441	Addition of new test purpose to test case 8.1.3.1.23

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1649  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203482)

Decision: 		The document was agreed.

R5-203503	Correction to NR CA RRC test cases 8.1.3.1.18.x

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1653  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203504	Correction to NR RRC test cases 8.1.3.2.3 and 8.1.3.2.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1654  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203521	Correction to NR RRC test case 8.1.3.1.20

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1659  Cat: F (Rel-16)

					Source: Starpoint, TDIA

Discussion:

r1

Decision: 		The document was revised to R5-204442.

R5-204442	Correction to NR RRC test case 8.1.3.1.20

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1659  rev 1 Cat: F (Rel-16)

					Source: Starpoint, TDIA

(Replaces R5-203521)

Decision: 		The document was agreed.

R5-203537	Correction to NR test case 8.1.3.1.13

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1664  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was withdrawn.

R5-203538	Correction to NR test case 8.1.3.1.14A

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1665  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was withdrawn.

R5-203539	Correction to NR test case 8.1.3.1.15A

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1666  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203576	Correction to NR5GC test case 8.1.3.1.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1673  Cat: F (Rel-16)

					Source: Starpoint, Huawei, HiSilicon,TDIA

Discussion:

r1

Decision: 		The document was revised to R5-204443.

R5-204443	Correction to NR5GC test case 8.1.3.1.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1673  rev 1 Cat: F (Rel-16)

					Source: Starpoint, Huawei, HiSilicon,TDIA

(Replaces R5-203576)

Decision: 		The document was agreed.

R5-203578	Correction to NR5GC test case 8.1.3.1.12

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1674  Cat: F (Rel-16)

					Source: Starpoint, Huawei, HiSilicon,TDIA

Discussion:

r1

Decision: 		The document was revised to R5-204444.

R5-204444	Correction to NR5GC test case 8.1.3.1.12

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1674  rev 1 Cat: F (Rel-16)

					Source: Starpoint, Huawei, HiSilicon,TDIA

(Replaces R5-203578)

Decision: 		The document was agreed.

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)

R5-203584	Addition of NR-DC RRC test case 8.2.2.8.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1675  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

r2

Decision: 		The document was revised to R5-204445.

R5-204445	Addition of NR-DC RRC test case 8.2.2.8.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1675  rev 1 Cat: F (Rel-16)

					Source: ANRITSU LTD

(Replaces R5-203584)

Decision: 		The document was agreed.

R5-203650	Corrections to NR5G RRC NR-DC TC 8.2.2.4.2 and 8.2.2.5.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1692  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)

R5-203657	Corrections to NR5G RRC TC 8.1.3.1.16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1696  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Decision: 		The document was agreed.

R5-203709	Correction to NR test case 8.1.3.1.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1711  Cat: F (Rel-16)

					Source: ZTE

Decision: 		The document was agreed.

R5-203710	Correction to NR test case 8.1.3.1.8

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1712  Cat: F (Rel-16)

					Source: ZTE

Decision: 		The document was agreed.

R5-203711	Correction to NR test case 8.1.3.1.13

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1713  Cat: F (Rel-16)

					Source: ZTE

Discussion:

-

Decision: 		The document was withdrawn.

R5-203728	Correction to NR test case 8.1.3.1.16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1715  Cat: F (Rel-16)

					Source: ZTE

Decision: 		The document was agreed.

R5-203811	Correction to NR CA RRC Test cases 8.1.3.1.17.x and 8.1.3.1.18.x

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1730  Cat: F (Rel-16)

					Source: ANRITSU LTD

Decision: 		The document was agreed.

R5-204106	Correction to NR RRC TC 8.1.3.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1739  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

cover issues.

Decision: 		The document was revised to R5-204382.

R5-204382	Correction to NR RRC TC 8.1.3.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1739  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-204106)

Decision: 		The document was agreed.

6.3.2.4.4.2.2	RRC Radio Bearer (clause 8.2.2)

R5-204217	Addition of NR-DC RRC test case 8.2.2.9.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1744  Cat: F (Rel-16)

					Source: Keysight Technologies UK Ltd

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)

R5-204341	Correction to the NR5GC testcase 8.1.3.1.12

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1751  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)

R5-203395	Correction to NR TC 8.1.4.1.7.X-Scell Release

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1622  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204446.

R5-204446	Correction to NR TC 8.1.4.1.7.X-Scell Release

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1622  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203395)

Decision: 		The document was agreed.

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)

R5-203401	Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1628  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204447.

R5-204447	Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1628  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203401)

Decision: 		The document was agreed.

R5-203402	Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1629  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204448.

R5-204448	Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1629  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203402)

Decision: 		The document was agreed.

R5-203403	Correction to ENDC TC 8.2.3.11.X-Measurement Gap

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1630  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203404	Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1631  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204449.

R5-204449	Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1631  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203404)

Decision: 		The document was agreed.

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)

R5-203483	Correction to include data path check after handover in test case 8.1.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1650  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

*.docx !

r1

Decision: 		The document was revised to R5-204450.

R5-204450	Correction to include data path check after handover in test case 8.1.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1650  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203483)

Decision: 		The document was agreed.

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)

R5-203540	Editorial correction to EN-DC test case 8.2.3.5.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1667  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203541	Correction to EN-DC test cases 8.2.3.9.1 and 8.2.3.10.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1668  Cat: F (Rel-16)

					Source: MCC TF160

Discussion:

Overlap with R5-203401 & R5-203402 to be resolved

Decision: 		The document was withdrawn.

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)

R5-203571	Correction to Inter-RAT HO test case 8.1.4.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1672  Cat: F (Rel-16)

					Source: China Telecommunications

Discussion:

.*docx

r2

Decision: 		The document was revised to R5-204451.

R5-204451	Correction to Inter-RAT HO test case 8.1.4.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1672  rev 1 Cat: F (Rel-16)

					Source: China Telecommunications

(Replaces R5-203571)

Discussion:

first agreed, then withdrawn after the meeting because of clash with agreed CR R5-204453.

Decision: 		The document was withdrawn.

R5-203592	Correction to Inter-RAT HO test case 8.1.4.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1679  Cat: F (Rel-16)

					Source: China Telecommunications

Discussion:

.*docx

r2

Decision: 		The document was revised to R5-204452.

R5-204452	Correction to Inter-RAT HO test case 8.1.4.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1679  rev 1 Cat: F (Rel-16)

					Source: China Telecommunications

(Replaces R5-203592)

Decision: 		The document was agreed.

R5-203664	Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1702  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

r1

Decision: 		The document was revised to R5-204453.

R5-204453	Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1702  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-203664)

Decision: 		The document was agreed.

R5-203665	Corrections to NR5G RRC CA TCs to add Data Path verification

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1703  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

R5-203712	Correction to NR test case 8.1.4.16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1714  Cat: F (Rel-16)

					Source: ZTE, MCC TF160

Discussion:

wrong title!

reissued as R5-204359 because of title change.

r1

Decision: 		The document was revised to R5-204360.

R5-204359	Correction to NR test case 8.1.4.1.6

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1754  Cat: F (Rel-16)

					Source: ZTE, MCC TF160

Abstract:

reissued from R5-203712 because of title change.

Decision: 		The document was agreed.

R5-204360	Correction to NR test case 8.1.4.16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1714  rev 1 Cat: F (Rel-16)

					Source: ZTE, MCC TF160

(Replaces R5-203712)

Decision: 		The document was withdrawn.

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)

R5-203814	Addition of NR-DC RRC test case 8.2.3.14.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1731  Cat: F (Rel-16)

					Source: ANRITSU LTD

Discussion:

r1

Decision: 		The document was revised to R5-204454.

R5-204454	Addition of NR-DC RRC test case 8.2.3.14.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1731  rev 1 Cat: F (Rel-16)

					Source: ANRITSU LTD

(Replaces R5-203814)

Decision: 		The document was agreed.

6.3.2.4.4.1.4	RRC Handover (clause 8.1.4)

R5-204016	Correction to NR TC 8.1.4.1.8.X-Scell no change

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1734  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

6.3.2.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)

R5-204133	Correction to MR-DC RRC TC 8.2.3.8.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1742  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

r3

Decision: 		The document was revised to R5-204455.

R5-204455	Correction to MR-DC RRC TC 8.2.3.8.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1742  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-204133)

Decision: 		The document was agreed.

6.3.2.4.4.1.5	RRC Others (clause 8.1.5)

R5-203396	Correction to NR TC 8.1.5.7.1.X-RLC Failure MCG

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1623  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203589	Correction to NR RRC TC 8.1.5.1.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1676  Cat: F (Rel-16)

					Source: MediaTek Inc., Keysight Technologies

Discussion:

r1

Decision: 		The document was revised to R5-204456.

R5-204456	Correction to NR RRC TC 8.1.5.1.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1676  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc., Keysight Technologies

(Replaces R5-203589)

Decision: 		The document was agreed.

6.3.2.4.4.2.4	RRC Carrier Aggregation (clause 8.2.4)

R5-203666	Corrections to ENDC RRC CA TCs to add Data Path verification

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1704  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

6.3.2.4.4.1.5	RRC Others (clause 8.1.5)

R5-204334	Correction to NR5GC RRC test case 8.1.5.2.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1749  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.4.2.5	RRC Reconfiguration / Radio Link Failure (clause 8.2.5)

6.3.2.4.4.2.6	RRC Others (clause 8.2.6)

R5-203405	Correction to ENDC TC 8.2.6.1.1.X-RLC Failure SCG

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1632  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203406	Addition of NRDC TC 8.2.6.1.2.1-RLC Failure SCG intra-band

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1633  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203407	Addition of NRDC TC 8.2.6.1.2.2-RLC Failure SCG inter-band

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1634  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203408	Addition of NRDC TC 8.2.6.1.2.3-RLC Failure SCG intra-band NC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1635  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203409	Correction to ENDC TC 8.2.6.2.1-Processing delay

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1636  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Starpoint

Decision: 		The document was agreed.

###### 6.3.2.4.5	5GS Mobility Management

6.3.2.4.5.1	MM Primary authentication and key agreement (clause 9.1.1)

R5-203410	Correction to NR TC 9.1.1.3-EAP message transport abnormal

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1637  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204457.

R5-204457	Correction to NR TC 9.1.1.3-EAP message transport abnormal

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1637  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203410)

Decision: 		The document was agreed.

R5-203411	Correction to NR TC 9.1.1.6-5G AKA abnormal

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1638  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204458.

R5-204458	Correction to NR TC 9.1.1.6-5G AKA abnormal

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1638  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203411)

Decision: 		The document was agreed.

6.3.2.4.5.2	MM Security mode control, Identification & Generic UE configuration update (clauses 9.1.2, 9.1.3 & 9.1.4)

R5-203737	Correction to 5GC TC 9.1.3.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1716  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

r2

Decision: 		The document was revised to R5-204459.

R5-204459	Correction to 5GC TC 9.1.3.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1716  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203737)

Decision: 		The document was agreed.

R5-203772	Correction to NR5GC testcase 9.1.4.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1727  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

6.3.2.4.5.3	MM Registration & De-registration (clauses 9.1.5 & 9.1.6)

R5-203412	Correction to NR TC 9.1.5.1.1-Initial registration with 5G-GUTI reallocation

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1639  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Decision: 		The document was agreed.

R5-203413	Correction to NR TC 9.1.5.1.8-Serving network not authorized

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1640  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, Anritsu, MediaTek Inc., ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203414	Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1641  Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

Discussion:

r1

Decision: 		The document was revised to R5-204460.

R5-204460	Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1641  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon, Datang Linktester

(Replaces R5-203414)

Decision: 		The document was agreed.

R5-203415	Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1642  Cat: F (Rel-16)

					Source: Huawei, HiSilicon, Anritsu

Discussion:

r1

Decision: 		The document was revised to R5-204461.

R5-204461	Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1642  rev 1 Cat: F (Rel-16)

					Source: Huawei, HiSilicon, Anritsu

(Replaces R5-203415)

Decision: 		The document was agreed.

R5-203505	Correction to 5GMM test case 9.1.5.1.13

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1655  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203658	Void NR5G NAS TC 9.1.5.2.6

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1697  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Decision: 		The document was agreed.

R5-203702	Correction to 5GC TC 9.1.5.2.9

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1706  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

r2

Decision: 		The document was revised to R5-204462.

R5-204462	Correction to 5GC TC 9.1.5.2.9

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1706  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203702)

Decision: 		The document was agreed.

R5-204342	Correction to NR TC 9.1.5.1.14

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1752  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204463.

R5-204463	Correction to NR TC 9.1.5.1.14

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1752  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204342)

Decision: 		The document was agreed.

R5-204343	Corrections to NR5G NAS TC 9.1.6.1.3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1753  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204464.

R5-204464	Corrections to NR5G NAS TC 9.1.6.1.3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1753  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA

(Replaces R5-204343)

Decision: 		The document was agreed.

6.3.2.4.5.4	MM Service Request (clause 9.1.7)

6.3.2.4.5.5	MM SMS Over NAS (clause 9.1.8)

6.3.2.4.5.6	Inter-system Mobility (clause 9.3)

###### 6.3.2.4.6	5GS Session Management

6.3.2.4.6.1	SM PDU session authentication and authorization (clause 10.1.1)

R5-203785	Correction to NR5GC testcase 10.1.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1728  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm

Decision: 		The document was agreed.

6.3.2.4.6.2	SM Network-requested PDU session modification & release (clauses 10.1.2 & 10.1.3)

6.3.2.4.6.3	SM UE-requested PDU session establishment, modification & release (clauses 10.1.4, 10.1.5 & 10.1.6)

###### 6.3.2.4.7	EN-DC Session Management

###### 6.3.2.4.8	5GS Multilayer and Services

6.3.2.4.8.1	EPS Fallback

R5-203752	Correction to Multilayer TC 11.1.2 and 11.1.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1726  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

r1

Decision: 		The document was revised to R5-204465.

R5-204465	Correction to Multilayer TC 11.1.2 and 11.1.5

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1726  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-203752)

Decision: 		The document was agreed.

R5-203996	Corrections to EPS Fallback regarding IMS procedures

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1732  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Decision: 		The document was revised to R5-204466.

R5-204466	Corrections to EPS Fallback regarding IMS procedures

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1732  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203996)

Decision: 		The document was agreed.

R5-204091	Correction to test case 11.1.7

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1738  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

r3

Decision: 		The document was revised to R5-204467.

R5-204467	Correction to test case 11.1.7

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1738  rev 1 Cat: F (Rel-16)

					Source: MediaTek Inc.

(Replaces R5-204091)

Decision: 		The document was agreed.

R5-204336	Correction to test case 11.1.3

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1750  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

late doc

Decision: 		The document was agreed.

6.3.2.4.8.2	RAT Fallback

6.3.2.4.8.3	Unified Access Control (UAC)

R5-203416	Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1643  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204468.

R5-204468	Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1643  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203416)

Decision: 		The document was agreed.

R5-203667	Correction to Multilayer TC 11.3.8

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1705  Cat: F (Rel-16)

					Source: MediaTek Inc.

Discussion:

overlapping with R5-204019.

Decision: 		The document was withdrawn.

R5-204019	Correction to NR5G UAC TC 11.3.8

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1736  Cat: F (Rel-16)

					Source: TDIA, CATT

Decision: 		The document was agreed.

R5-204239	Addition of NR5G UAC TC 11.3.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1747  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

wrong AI!

r1

Comments from TF160.

Decision: 		The document was revised to R5-204518.

R5-204518	Addition of NR5G UAC TC 11.3.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1747  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204239)

Decision: 		The document was agreed.

6.3.2.4.8.4	Emergency Services

##### 6.3.2.5	TS 38.523-2

R5-203417	Addition of applicability for NR TCs

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0088  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204469.

R5-204469	Addition of applicability for NR TCs

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0088  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203417)

Decision: 		The document was agreed.

R5-203418	Correction to applicability of NR TCs

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0089  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204470.

R5-204470	Correction to applicability of NR TCs

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0089  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203418)

Decision: 		The document was agreed.

R5-203475	Update of 5G-NR test cases applicability

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0090  Cat: F (Rel-16)

					Source: Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility

Discussion:

r2

Decision: 		The document was revised to R5-204471.

R5-204471	Update of 5G-NR test cases applicability

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0090  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility

(Replaces R5-203475)

Decision: 		The document was agreed.

R5-203542	Splitting and updates to applicability of NR RLC test case 7.1.2.3.5

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0092  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203612	Addition of new RRC TC for checking extended / spare field handling in SI

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0094  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

Decision: 		The document was revised to R5-204472.

R5-204472	Addition of new RRC TC for checking extended / spare field handling in SI

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0094  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203612)

Decision: 		The document was agreed.

R5-203890	Removal of void test case and correction of condition for Inter-band measurements test cases

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0095  Cat: F (Rel-16)

					Source: CAICT

Discussion:

cover says 38.522!!!

title wrong, no "correction of condition"!!

empty cover!!

r3

Decision: 		The document was revised to R5-204473.

R5-204473	Removal of void test case and correction of condition for Inter-band measurements test cases

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0095  rev 1 Cat: F (Rel-16)

					Source: CAICT

(Replaces R5-203890)

Decision: 		The document was agreed.

R5-203899	Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0096  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

Decision: 		The document was revised to R5-204474.

R5-204474	Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0096  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203899)

Decision: 		The document was withdrawn.

##### 6.3.2.6	TS 38.523-3

R5-203543	5G Test Models updates

Type: CR		For: Agreement
					38.523-3 v15.8.0	  CR-1233  Cat: F (Rel-15)

					Source: MCC TF160, Keysight, Samsung

Discussion:

R5-203496 was merged into here.

r1

Decision: 		The document was revised to R5-204475.

R5-204475	5G Test Models updates

Type: CR		For: Agreement
					38.523-3 v15.8.0	  CR-1233  rev 1 Cat: F (Rel-15)

					Source: MCC TF160, Keysight, Samsung

(Replaces R5-203543)

Decision: 		The document was agreed.

##### 6.3.2.7	TS 34.229-1

R5-203434	Adding cross-references to TS 34.229-5

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1440  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203435	Removing 5G content

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1441  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

##### 6.3.2.8	TS 34.229-2

R5-203436	Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases

Type: CR		For: Agreement
					34.229-2 v15.3.0	  CR-0271  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Discussion:

r2

TF160 comment.

Decision: 		The document was revised to R5-204476.

R5-204476	Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases

Type: CR		For: Agreement
					34.229-2 v15.3.0	  CR-0271  rev 1 Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

(Replaces R5-203436)

Decision: 		The document was agreed.

##### 6.3.2.9	TS 34.229-3

R5-203544	IMS over NR/5GC: Misc updates

Type: CR		For: Agreement
					34.229-3 v15.5.0	  CR-0631  Cat: F (Rel-15)

					Source: MCC TF160, ROHDE & SCHWARZ

Decision: 		The document was agreed.

##### 6.3.2.10	TS 34.229-5

R5-203423	Addition of IMS NR TC 9.4-MT Concatenated SMS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0001  Cat: F (Rel-15)

					Source: Huawei, Hisilicon

Discussion:

r1

no 3gpp formats!

r3

Decision: 		The document was revised to R5-204477.

R5-204477	Addition of IMS NR TC 9.4-MT Concatenated SMS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0001  rev 1 Cat: F (Rel-15)

					Source: Huawei, Hisilicon

(Replaces R5-203423)

Decision: 		The document was agreed.

R5-203424	Addition of IMS NR TC 9.5-MO SMS RP-ERROR

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0002  Cat: F (Rel-15)

					Source: Huawei, Hisilicon

Discussion:

r1

no 3gpp formats!

r3

Decision: 		The document was revised to R5-204478.

R5-204478	Addition of IMS NR TC 9.5-MO SMS RP-ERROR

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0002  rev 1 Cat: F (Rel-15)

					Source: Huawei, Hisilicon

(Replaces R5-203424)

Decision: 		The document was agreed.

R5-203425	Addition of IMS NR TC 10.1-emergency call with registration and Location

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0003  Cat: F (Rel-15)

					Source: Huawei, Hisilicon

Discussion:

r1

no 3gpp formats!

r3

Decision: 		The document was revised to R5-204479.

R5-204479	Addition of IMS NR TC 10.1-emergency call with registration and Location

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0003  rev 1 Cat: F (Rel-15)

					Source: Huawei, Hisilicon

(Replaces R5-203425)

Decision: 		The document was agreed.

R5-203437	Corrections to A.2 on IMS Registration

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0004  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203438	Adding details for A.3 for IMS Emergency Registration

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0005  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Discussion:

r1

fixes an editorial error in step numbering.

Decision: 		The document was revised to R5-204480.

R5-204480	Adding details for A.3 for IMS Emergency Registration

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0005  rev 1 Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

(Replaces R5-203438)

Decision: 		The document was agreed.

R5-203439	New generic procedure for MT Call Release

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0006  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203440	Adding references as needed

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0007  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203441	Corrections to test cases 7.6 and 7.7

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0008  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203442	Corrections to test case 6.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0009  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203443	Corrections to test case 6.2

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0010  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203444	Corrections to test case 6.3

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0011  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Discussion:

r2

TF160 comment.

Decision: 		The document was revised to R5-204481.

R5-204481	Corrections to test case 6.3

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0011  rev 1 Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

(Replaces R5-203444)

Decision: 		The document was agreed.

R5-203445	Corrections to test case 6.4

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0012  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203447	Corrections to test case 6.5

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0013  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203448	Corrections to test case 6.6

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0014  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203452	Corrections to test case 6.7

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0015  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203453	Corrections to test case 6.8

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0016  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203454	Corrections to test case 6.9

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0017  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203461	Corrections to MTSI MT Voice Call TC 7.6

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0018  Cat: F (Rel-15)

					Source: ZTE Corporation

Decision: 		The document was agreed.

R5-203462	Corrections to Annex A.5.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0019  Cat: F (Rel-15)

					Source: ZTE Corporation

Decision: 		The document was agreed.

R5-203713	Addition of new IMS 5GS test case 9.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0020  Cat: F (Rel-15)

					Source: ZTE

Discussion:

r2

comments from R&S.

r3

Decision: 		The document was revised to R5-204482.

R5-204482	Addition of new IMS 5GS test case 9.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0020  rev 1 Cat: F (Rel-15)

					Source: ZTE

(Replaces R5-203713)

Decision: 		The document was agreed.

R5-203714	Addition of new IMS 5GS test case 9.2

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0021  Cat: F (Rel-15)

					Source: ZTE

Discussion:

r2

comments from R&S.

r3

Decision: 		The document was revised to R5-204483.

R5-204483	Addition of new IMS 5GS test case 9.2

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0021  rev 1 Cat: F (Rel-15)

					Source: ZTE

(Replaces R5-203714)

Decision: 		The document was agreed.

R5-204093	New generic IMS procedures for use in EPS fallback

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0022  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Comments from TF160.

Decision: 		The document was revised to R5-204484.

R5-204484	New generic IMS procedures for use in EPS fallback

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0022  rev 1 Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

(Replaces R5-204093)

Decision: 		The document was agreed.

R5-204240	Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0023  Cat: F (Rel-15)

					Source: Qualcomm CDMA Technologies

Discussion:

r2

Decision: 		The document was revised to R5-204485.

R5-204485	Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0023  rev 1 Cat: F (Rel-15)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204240)

Decision: 		The document was agreed.

R5-204241	Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0024  Cat: F (Rel-15)

					Source: Qualcomm CDMA Technologies

Discussion:

r2

Decision: 		The document was revised to R5-204486.

R5-204486	Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0024  rev 1 Cat: F (Rel-15)

					Source: Qualcomm CDMA Technologies

(Replaces R5-204241)

Decision: 		The document was agreed.

R5-204248	Addition of new IMS test case 8.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0025  Cat: F (Rel-15)

					Source: Qualcomm Incorporated

Decision: 		The document was withdrawn.

R5-204251	Addition of new IMS test case 8.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0026  Cat: F (Rel-15)

					Source: Qualcomm Incorporated

Discussion:

r1

Decision: 		The document was revised to R5-204487.

R5-204487	Addition of new IMS test case 8.1

Type: CR		For: Agreement
					34.229-5 v15.0.0	  CR-0026  rev 1 Cat: F (Rel-15)

					Source: Qualcomm Incorporated

(Replaces R5-204251)

Decision: 		The document was agreed.

##### 6.3.2.11	TS 36.508

R5-203494	Update to ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST message

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1322  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203651	Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1325  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

Discussion:

r1

Decision: 		The document was revised to R5-204488.

R5-204488	Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1325  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies, Keysight Technologies UK Ltd.

(Replaces R5-203651)

Decision: 		The document was agreed.

##### 6.3.2.12	TS 36.509

##### 6.3.2.13	TS 36.523-1

##### 6.3.2.14	TS 36.523-2

##### 6.3.2.15	TS 36.523-3

R5-203496	Correction to postamble procedures to handle multi-PDN EN-DC devices

Type: CR		For: Agreement
					36.523-3 v16.5.1	  CR-4526  Cat: F (Rel-16)

					Source: Keysight Technologies UK, Samsung

Discussion:

merged into R5-203543.

Decision: 		The document was withdrawn.

##### 6.3.2.16	TS 37.571-2

R5-203273	Adding measurement gaps for OTDOA configuration

Type: CR		For: Agreement
					37.571-2 v16.4.0	  CR-0132  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

r1

Removed overlap with R5-203512 (PCTest)

Defined the procedure for configuring the measurement gaps more in detail, based on inputs from TF160

Decision: 		The document was revised to R5-204489.

R5-204489	Adding measurement gaps for OTDOA configuration

Type: CR		For: Agreement
					37.571-2 v16.4.0	  CR-0132  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203273)

Decision: 		The document was agreed.

##### 6.3.2.17	TS 37.571-3

##### 6.3.2.18	TS 37.571-4

##### 6.3.2.19	TS 37.571-5

##### 6.3.2.20	Discussion Papers, Work Plan, TC lists

R5-203460	Discussion paper on two consecutive invalid challenges

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Discussion:

Proposal endorsed. RAN5 agreed to send a LS to CT1 to clarify the spec text quoted.

Decision: 		The document was noted.

R5-204323	Flexible handling multi PDUs and PDNs in the 5G test specifications

Type: discussion		For: discussion
					Source: Samsung, MCC TF160

Discussion:

"LATE DOCUMENT

Seek feedback from Test Vendors on draft TTCN release made in July in TTCN Sidebar to be held on Thu - only 1 TP vendor trialed using draft TTCN. More testing to be done in the coming days

Proposed solution to cater for flexible PDU/PDN handling accepted in principle. Actual implementation to be proposed in CRs to RAN5#89-e meeting. RAN5 will then decide on CRs endorsement/agreement and TTCN implementation aspects"

Decision: 		The document was noted.

R5-204333	Aligning the RRC specific message in TS 38.523-1 contents with the default messages in TS 38.508-1

Type: discussion		For: discussion
					Source: Samsung

Discussion:

late doc

RAN5 approves alignment of the RRC specific message contents in TS 38.523-1 with the default messages in TS 38.508-1 to be done between the TS 38.523-1 Rapporteur (Mr S. Baev, Samsung) and the RAN5 Secretary as a post RAN Plenary meeting action following implementation of RP#89-e approved CRs"

Decision: 		The document was noted.

#### 6.3.3	Rel-15 CA configurations (UID - 770064) LTE_CA_R15-UEConTest

##### 6.3.3.1	TS 36.508

##### 6.3.3.2	TS 36.523-1

##### 6.3.3.3	TS 36.523-2

##### 6.3.3.4	TS 36.523-3

##### 6.3.3.5	Discussion Papers, Work Plan, TC lists

#### 6.3.4	Mission Critical Improvements (UID - 790052) MCImp-UEConTest

##### 6.3.4.1	TS 36.579-1

R5-204226	Addition of XML schema for MCVideo location information

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0082  Cat: F (Rel-14)

					Source: NIST

Decision: 		The document was agreed.

R5-204229	MCVideo and MCData in Clause 4

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0083  Cat: F (Rel-14)

					Source: NIST

Decision: 		The document was agreed.

R5-204230	MCVideo and MCData in Clause 5.5.7

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0084  Cat: F (Rel-14)

					Source: NIST

Discussion:

r1

Decision: 		The document was revised to R5-204490.

R5-204490	MCVideo and MCData in Clause 5.5.7

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0084  rev 1 Cat: F (Rel-14)

					Source: NIST

(Replaces R5-204230)

Decision: 		The document was agreed.

R5-204234	Updates to UE configuration document

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0085  Cat: F (Rel-14)

					Source: NIST

Discussion:

r1

Decision: 		The document was revised to R5-204491.

R5-204491	Updates to UE configuration document

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0085  rev 1 Cat: F (Rel-14)

					Source: NIST

(Replaces R5-204234)

Decision: 		The document was agreed.

R5-204371	Update of content with Rel-14 requirements

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0086  Cat: F (Rel-14)

					Source: Samsung

Discussion:

late doc

r1

Decision: 		The document was revised to R5-204492.

R5-204492	Update of content with Rel-14 requirements

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0086  rev 1 Cat: F (Rel-14)

					Source: Samsung

(Replaces R5-204371)

Decision: 		The document was agreed.

##### 6.3.4.2	TS 36.579-2

##### 6.3.4.3	TS 36.579-3

##### 6.3.4.4	TS 36.579-4

R5-204228	Corrections to MCVideo and MCData tables

Type: CR		For: Agreement
					36.579-4 v14.3.0	  CR-0010  Cat: F (Rel-14)

					Source: NIST

Discussion:

contains also 4226!!

r1

Decision: 		The document was revised to R5-204369.

R5-204369	Corrections to MCVideo and MCData tables

Type: CR		For: Agreement
					36.579-4 v14.3.0	  CR-0010  rev 1 Cat: F (Rel-14)

					Source: NIST

(Replaces R5-204228)

Decision: 		The document was agreed.

R5-204370	Update of test case applicability to Rel-14

Type: CR		For: Agreement
					36.579-4 v14.3.0	  CR-0011  Cat: F (Rel-14)

					Source: Samsung

Discussion:

late doc

Decision: 		The document was agreed.

##### 6.3.4.5	TS 36.579-5

R5-204233	Updates to IXIT Proforma for MCVideo and MCData

Type: CR		For: Agreement
					36.579-5 v13.6.0	  CR-0009  Cat: F (Rel-13)

					Source: NIST, MCC TF160

Discussion:

reissued as R5-204377 because of title change.

Decision: 		The document was withdrawn.

R5-204377	Updates to introduce support for MCVideo and MCData

Type: CR		For: Agreement
					36.579-5 v13.6.0	  CR-0010  Cat: F (Rel-13)

					Source: NIST, MCC TF160

Abstract:

reissued from R5-204233 because of title change.

Decision: 		The document was agreed.

##### 6.3.4.6	TS 36.579-6 (pCRs only)

R5-204232	PIXIT updates and table names

Type: pCR		For: Approval
					36.579-6 v1.0.0
					Source: NIST

Discussion:

r1

Decision: 		The document was revised to R5-204493.

R5-204493	PIXIT updates and table names

Type: pCR		For: Approval
					36.579-6 v1.0.0
					Source: NIST

(Replaces R5-204232)

Decision: 		The document was approved.

##### 6.3.4.7	TS 36.579-7 (pCRs only)

##### 6.3.4.8	TS 36.508

##### 6.3.4.9	TS 36.509

##### 6.3.4.10	TS 36.523-1

##### 6.3.4.11	TS 36.523-2

##### 6.3.4.12	TS 36.523-3

##### 6.3.4.13	Discussion Papers, Work Plan, TC lists

#### 6.3.5	Rel-16 LTE CA configurations (UID - 810061) LTE_CA_R16-UEConTest

##### 6.3.5.1	TS 36.508

##### 6.3.5.2	TS 36.523-1

##### 6.3.5.3	TS 36.523-2

##### 6.3.5.4	TS 36.523-3

##### 6.3.5.5	Discussion Papers, Work Plan, TC lists

#### 6.3.6	Shortened TTI and processing time for LTE (UID - 820064) LTE_sTTIandPT-UEConTest

##### 6.3.6.1	TS 36.508

R5-203922	Update of common test environment for short TTI and short processing time TCs

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1326  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

##### 6.3.6.2	TS 36.509

##### 6.3.6.3	TS 36.523-1

R5-203923	Update of test description for DL transmission test cases for sTTI and short processing time

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4948  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r2

Decision: 		The document was revised to R5-204494.

R5-204494	Update of test description for DL transmission test cases for sTTI and short processing time

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4948  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203923)

Decision: 		The document was agreed.

R5-203924	Update of message contents for UL transmission test cases for sTTI and short processing time

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4949  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

R5-203925	Correction to derivation path for SRS transmission test cases for sTTI and short processing time

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4950  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Decision: 		The document was agreed.

##### 6.3.6.4	TS 36.523-2

R5-203926	Correction to test applicability for sTTI test cases

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1318  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204495.

R5-204495	Correction to test applicability for sTTI test cases

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1318  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203926)

Decision: 		The document was agreed.

##### 6.3.6.5	TS 36.523-3

##### 6.3.6.6	Discussion Papers, Work Plan, TC lists

#### 6.3.7	Enhancing LTE CA Utilization (UID - 820066) LTE_euCA-UEConTest

##### 6.3.7.1	TS 36.508

##### 6.3.7.2	TS 36.523-1

##### 6.3.7.3	TS 36.523-2

##### 6.3.7.4	Discussion Papers, Work Plan, TC lists

#### 6.3.8	REL-16 NR CA and DC; and NR and LTE DC Configurations (UID-830083)  NR_CADC_NR_LTE_DC_R16-UEConTest

##### 6.3.8.1	TS 38.508-1

##### 6.3.8.2	TS 38.508-2

##### 6.3.8.3	TS 38.523-1

##### 6.3.8.4	TS 38.523-2

##### 6.3.8.5	TS 38.523-3

##### 6.3.8.6	Discussion Papers, Work Plan, TC lists

#### 6.3.9	LTE Advanced high power TDD UE (power class 2) for Rel-15 (UID - 850061) LTE_TDD_HPUE_R15-UEConTest

##### 6.3.9.1	TS 36.523-1

##### 6.3.9.2	TS 36.523-2

R5-203861	Update of capability for 6.1.2.5a cell re-selection for HPUE

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1316  Cat: F (Rel-16)

					Source: Huawei, HiSilicon

Decision: 		The document was agreed.

##### 6.3.9.3	TS 36.523-3

##### 6.3.9.4	Discussion Papers, Work Plan, TC lists

#### 6.3.10	New Rel-16 NR bands and extension of existing NR bands (UID - 850062) NR_bands_BW_R16-UEConTest

##### 6.3.10.1	TS 38.508-1

R5-203793	Correction of n29 test frequencies for protocol testing

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1454  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203794	Introduction of n30 test frequencies for protocol testing

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1455  Cat: F (Rel-16)

					Source: Ericsson, AT&T

Decision: 		The document was agreed.

R5-204032	Introduction of n259 test frequencies for protocol testing

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1470  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

##### 6.3.10.2	TS 38.508-2

##### 6.3.10.3	TS 38.523-3

##### 6.3.10.4	Discussion Papers, Work Plan, TC lists

#### 6.3.11	Further NB-IoT enhancements (UID – 860031) NB_IOTenh2-UEConTest

##### 6.3.11.1	TS 36.508

R5-204012	Update to Common contents of system information messages for NB_IOTenh2

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1328  Cat: F (Rel-16)

					Source: CATT, TDIA

Discussion:

r1

Comments from MCC160.

Decision: 		The document was revised to R5-204496.

R5-204496	Update to Common contents of system information messages for NB_IOTenh2

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1328  rev 1 Cat: F (Rel-16)

					Source: CATT, TDIA

(Replaces R5-204012)

Decision: 		The document was agreed.

##### 6.3.11.2	TS 36.509

##### 6.3.11.3	TS 36.523-1

R5-204002	Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4951  Cat: F (Rel-16)

					Source: TDIA, CATT

Discussion:

r1

comments from MCC160.

r2

Decision: 		The document was revised to R5-204497.

R5-204497	Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4951  rev 1 Cat: F (Rel-16)

					Source: TDIA, CATT

(Replaces R5-204002)

Decision: 		The document was agreed.

R5-204004	Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4952  Cat: F (Rel-16)

					Source: TDIA, CATT

Discussion:

r1

Comments from MCC160.

r2

Decision: 		The document was revised to R5-204498.

R5-204498	Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4952  rev 1 Cat: F (Rel-16)

					Source: TDIA, CATT

(Replaces R5-204004)

Decision: 		The document was agreed.

##### 6.3.11.4	TS 36.523-2

R5-204006	Update of test applicabilities for NB_IOTenh2

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1319  Cat: F (Rel-16)

					Source: CATT, TDIA

Decision: 		The document was agreed.

##### 6.3.11.5	TS 36.523-3

##### 6.3.11.6	Discussion Papers, Work Plan, TC lists

#### 6.3.12	Even further enhanced MTC for LTE (UID – 860032) LTE_eMTC4-UEConTest

##### 6.3.12.1	TS 36.508

R5-204140	Updates to IEs for Early Data Transmission test cases

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1329  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

comments from TF160.

Decision: 		The document was revised to R5-204499.

R5-204499	Updates to IEs for Early Data Transmission test cases

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1329  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204140)

Decision: 		The document was agreed.

##### 6.3.12.2	TS 36.509

##### 6.3.12.3	TS 36.523-1

R5-203473	Addition of new test case to test Paging with DRX and WUS in enhanced coverage

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4937  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

*.docx !

r1

Decision: 		The document was revised to R5-204500.

R5-204500	Addition of new test case to test Paging with DRX and WUS in enhanced coverage

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4937  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203473)

Decision: 		The document was agreed.

R5-203474	Addition of new test case to test Paging with eDRX and WUS in enhanced coverage

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4938  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

*.docx !

r1

Decision: 		The document was revised to R5-204501.

R5-204501	Addition of new test case to test Paging with eDRX and WUS in enhanced coverage

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4938  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203474)

Decision: 		The document was agreed.

R5-203477	Addition of new test case to test CE-level based access barring

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4939  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

*.docx !

r2

Decision: 		The document was revised to R5-204502.

R5-204502	Addition of new test case to test CE-level based access barring

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4939  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203477)

Decision: 		The document was agreed.

R5-204142	Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4953  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

comments from Qualcomm.

Decision: 		The document was revised to R5-204503.

R5-204503	Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4953  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204142)

Decision: 		The document was agreed.

##### 6.3.12.4	TS 36.523-2

R5-203479	Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1313  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

r3

Decision: 		The document was revised to R5-204504.

R5-204504	Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1313  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203479)

Decision: 		The document was agreed.

R5-203480	Addition of applicability for new test case to test CE-level based access barring

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1314  Cat: F (Rel-16)

					Source: Tech Mahindra Limited

Discussion:

r2

Decision: 		The document was revised to R5-204505.

R5-204505	Addition of applicability for new test case to test CE-level based access barring

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1314  rev 1 Cat: F (Rel-16)

					Source: Tech Mahindra Limited

(Replaces R5-203480)

Decision: 		The document was agreed.

R5-204143	Addition of applicability for eMTC4 TC 23.2.4

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1320  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

comments from Qualcomm and TF160.

Decision: 		The document was revised to R5-204506.

R5-204506	Addition of applicability for eMTC4 TC 23.2.4

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1320  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204143)

Decision: 		The document was agreed.

##### 6.3.12.5	TS 36.523-3

##### 6.3.12.6	Discussion Papers, Work Plan, TC lists

#### 6.3.13	RF requirements for NR frequency range 1 (FR1) (UID-870061)  NR_RF_FR1-UEConTest

##### 6.3.13.1	TS 38.508-1

##### 6.3.13.2	TS 38.508-2

##### 6.3.13.3	TS 38.523-1

##### 6.3.13.4	TS 38.523-2

##### 6.3.13.5	TS 38.523-3

##### 6.3.13.6	Discussion Papers, Work Plan, TC lists

#### 6.3.14	Even Further Mobility Enhancement for E-UTRAN (UID – 880066) LTE_feMob-UEConTest

##### 6.3.14.1	TS 36.508

##### 6.3.14.2	TS 36.523-1

##### 6.3.14.3	TS 36.523-2

##### 6.3.14.4	TS 36.523-3

##### 6.3.14.5	Discussion Papers, Work Plan, TC lists

#### 6.3.15	Support of NR Industrial Internet of Things (IoT) (UID-880067)  NR_IIOT-UEConTest

##### 6.3.15.1	TS 38.508-1

##### 6.3.15.2	TS 38.508-2

##### 6.3.15.3	TS 38.523-1

##### 6.3.15.4	TS 38.523-2

##### 6.3.15.5	TS 38.523-3

##### 6.3.15.6	TS 36.508

##### 6.3.15.7	TS 36.523-1

##### 6.3.15.8	TS 36.523-2

##### 6.3.15.9	TS 36.523-3

##### 6.3.15.10	Discussion Papers, Work Plan, TC lists

#### 6.3.16	NR Mobility Enhancements (UID-880068)  NR_Mob_enh-UEConTest

##### 6.3.16.1	TS 38.508-1

##### 6.3.16.2	TS 38.508-2

##### 6.3.16.3	TS 38.523-1

##### 6.3.16.4	TS 38.523-2

##### 6.3.16.5	TS 38.523-3

##### 6.3.16.6	Discussion Papers, Work Plan, TC lists

R5-203419	Discussion for NR Mobility Enhancements Testing

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

Discussion:

Rapporteur requested to initiate discussion among supporting companies and revert if any topics to be discussed at the RAN5 level.

Decision: 		The document was noted.

#### 6.3.17	5G V2X with NR sidelink (UID-880069)  5G_V2X_NRSL_eV2XARC-UEConTest

##### 6.3.17.1	TS 38.508-1

##### 6.3.17.2	TS 38.508-2

##### 6.3.17.3	TS 38.509

##### 6.3.17.4	TS 38.523-1

##### 6.3.17.5	TS 38.523-2

##### 6.3.17.6	TS 38.523-3

##### 6.3.17.7	TS 36.509

##### 6.3.17.8	Discussion Papers, Work Plan, TC lists

R5-203421	Discussion for NR V2X Testing

Type: discussion		For: Discussion
					Source: Huawei, Hisilicon

Discussion:

Rapporteur requested to initiate discussion among supporting companies and revert if any topics to be discussed at the RAN5 level.

Decision: 		The document was noted.

#### 6.3.18	Enhancements on MIMO for NR (UID-880070)  NR_eMIMO-UEConTest

##### 6.3.18.1	TS 38.508-1

##### 6.3.18.2	TS 38.508-2

##### 6.3.18.3	TS 38.523-1

##### 6.3.18.4	TS 38.523-2

##### 6.3.18.5	TS 38.523-3

##### 6.3.18.6	Discussion Papers, Work Plan, TC lists

#### 6.3.19	UE Power Saving in NR (UID-880071)  NR_UE_pow_sav-UEConTest

##### 6.3.19.1	TS 38.508-1

##### 6.3.19.2	TS 38.508-2

##### 6.3.19.3	TS 38.523-1

##### 6.3.19.4	TS 38.523-2

##### 6.3.19.5	TS 38.523-3

##### 6.3.19.6	Discussion Papers, Work Plan, TC lists

#### 6.3.20	Private Network Support for NG-RAN (UID-880072)  NG_RAN_PRN_Vertical_LAN-UEConTest

##### 6.3.20.1	TS 38.508-1

##### 6.3.20.2	TS 38.508-2

##### 6.3.20.3	TS 38.523-1

##### 6.3.20.4	TS 38.523-2

##### 6.3.20.5	TS 38.523-3

##### 6.3.20.6	Discussion Papers, Work Plan, TC lists

#### 6.3.21	Optimisations on UE radio capability signalling – NR/E-UTRA Aspects (UID-880073)  RACS-UEConTest

##### 6.3.21.1	TS 38.508-1

##### 6.3.21.2	TS 38.508-2

##### 6.3.21.3	TS 38.523-1

##### 6.3.21.4	TS 38.523-2

##### 6.3.21.5	TS 38.523-3

##### 6.3.21.6	TS 36.508

##### 6.3.21.7	TS 36.523-1

##### 6.3.21.8	TS 36.523-2

##### 6.3.21.9	TS 36.523-3

##### 6.3.21.10	Discussion Papers, Work Plan, TC lists

R5-204246	Discussion paper for RRC Segmentation in Rel-16 RACS

Type: discussion		For: Discussion
					Source: Qualcomm CDMA Technologies

Decision: 		The document was not pursued.

### 6.4	Routine Maintenance for TS 38 Series TEIx_Test

#### 6.4.1	TS 38.508-1

R5-203255	Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator-r16, AvailableRB-SetPerCell and BAP-Routing-ID

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1363  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was withdrawn.

R5-203276	Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1365  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was withdrawn.

R5-203277	Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1366  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203320	Add IE BeamFailureRecoverySCellConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1369  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203338	Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1371  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204507.

R5-204507	Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1371  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203338)

Decision: 		The document was agreed.

R5-203339	Add IE CGI-InfoEUTRALogging

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1372  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203340	Add IEs CGI-Info-Logging and CLI-RSSI-Range

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1373  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203341	Add IEs CommonLocationInfo, CondReconfigId, CondReconfigToAddModList and ConditionalReconfiguration

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1374  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203342	Add IEs ConfiguredGrantConfigIndex and ConfiguredGrantConfigIndexMAC

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1375  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203343	Add IE DRX-ConfigSecondaryGroup

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1376  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203344	Add IE HighSpeedConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1377  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203345	Add IE InvalidSymbolPattern

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1378  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203346	Add IEs LBT-FailureRecoveryConfig and LocationInfo

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1379  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203347	Add IE MeasIdleConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1380  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203348	Add IE MeasObjectCLI

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1381  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203349	Add IE MeasObjectNR-SL

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1382  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203350	Add IE MeasObjectUTRA-FDD

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1383  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203351	Add IEs MeasResultIdleEUTRA and MeasResultIdleNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1384  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203352	Add Es MeasResultsSL and MeasTriggerQuantityEUTRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1385  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was withdrawn.

R5-203353	Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0087  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

-

Decision: 		The document was withdrawn.

R5-203354	Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1386  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

comments from Rohde & Schwarz.

Decision: 		The document was revised to R5-204508.

R5-204508	Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1386  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203354)

Decision: 		The document was agreed.

R5-203355	Add IEs MsgA-ConfigCommon and MsgA-PUSCH-Config

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1387  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203356	Add IEs NeedForGapsConfigNR and NeedForGapsInfoNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1388  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203446	Add IEs NPN-Identity and NPN-IdentityInfoList

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1395  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203449	Add IE PLMN-IdentityList2

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1396  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203450	Add IE PUCCH-ConfigurationList

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1397  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203451	Add IE PUCCH-SpatialRelationInfo-Id

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1398  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203467	Add IE RACH-ConfigCommonTwoStepRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1401  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203470	Add IE RACH-ConfigGenericTwoStepRA

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1402  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203471	Add IE ReferenceTimeInfo

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1403  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was agreed.

R5-203472	Add IE RepetitionSchemeConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1404  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203476	Add IE ReportConfigNR-SL

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1405  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203506	Add IE RSSI-Range

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1411  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203507	Add IEs SemiStaticChannelAccessConfig and Sensor-LocationInfo

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1412  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203508	Add IE SI-RequestConfig

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1413  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203509	Add IEs SPS-ConfigIndex, SPS-PUCCH-AN and SPS-PUCCH-AN-List

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1414  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203510	Add IE SRS-RSRP-Range

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1415  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203523	Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1416  Cat: F (Rel-16)

					Source: China Telecom

Discussion:

Cat. B

r3

Decision: 		The document was revised to R5-204509.

R5-204509	Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1416  rev 1 Cat: F (Rel-16)

					Source: China Telecom

(Replaces R5-203523)

Decision: 		The document was agreed.

R5-203556	Add IE SSB-PositionQCL-Relation

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1419  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

comments from Rohde & Schwarz.

Decision: 		The document was revised to R5-204510.

R5-204510	Add IE SSB-PositionQCL-Relation

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1419  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-203556)

Decision: 		The document was agreed.

R5-203557	Add IEs UL-DelayValueConfig and UplinkCancellation

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1420  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203575	Add chapter Positioning System information blocks

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1422  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203577	Add IEs SIB10, SIB11, SIB12, SIB13 and SIB14

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1423  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203582	Add messages DedicatedSIBRequest, DLDedicatedMessageSegment, DLInformationTransferMRDC and IABOtherInformation

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1424  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203719	Add messages LoggedMeasurementConfiguration, MCGFailureInformation and SidelinkUEInformationNR

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1441  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

R5-203725	Add messages UEInformationRequest, UEInformationResponse, ULDedicatedMessageSegment and ULInformationTransferIRAT

Type: CR		For: Agreement
					38.508-1 v16.4.0	  CR-1442  Cat: F (Rel-16)

					Source: Ericsson

Decision: 		The document was agreed.

#### 6.4.2	TS 38.508-2

R5-204373	Addition of UE capability for voiceFallbackIndicationEPS-r16

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0109  Cat: F (Rel-16)

					Source: CATT, TDIA

Discussion:

late doc

TF160 manager: clashes with other CRs, e.g. R5-204205.

r1

Decision: 		The document was revised to R5-204511.

R5-204511	Addition of UE capability for voiceFallbackIndicationEPS-r16

Type: CR		For: Agreement
					38.508-2 v16.4.0	  CR-0109  rev 1 Cat: F (Rel-16)

					Source: CATT, TDIA

(Replaces R5-204373)

Decision: 		The document was agreed.

#### 6.4.3	TS 38.509

#### 6.4.4	TS 38.523-1

##### 6.4.4.1	Clauses 1 - 5

##### 6.4.4.2	Idle Mode (Clause 6)

##### 6.4.4.3	Layer 2

###### 6.4.4.3.1	NR Layer 2

6.4.4.3.1.1	Common Test Case Specific Values for Layer 2 (Clause 7.1.0)

6.4.4.3.1.2	MAC

6.4.4.3.1.3	RLC

R5-203663	Corrections to NR5G RLC TC 7.1.2.3.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1701  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

wrong AI! RLC, not MAC!

r1

Decision: 		The document was revised to R5-204512.

R5-204512	Corrections to NR5G RLC TC 7.1.2.3.11

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1701  rev 1 Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

(Replaces R5-203663)

Decision: 		The document was agreed.

6.4.4.3.1.4	PDCP

6.4.4.3.1.5	SDAP

##### 6.4.4.4	RRC

###### 6.4.4.4.1	NR RRC

6.4.4.4.1.1	RRC Connection Management Procedures (clause 8.1.1)

6.4.4.4.1.2	RRC Reconfiguration (clause 8.1.2)

6.4.4.4.1.3	RRC Measurement Configuration Control and Reporting (clause 8.1.3)

6.4.4.4.1.4	RRC Handover (clause 8.1.4)

R5-203522	Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1660  Cat: F (Rel-16)

					Source: China telecom, Datang linktester

Discussion:

*.docx, Cat.B

r2

Decision: 		The document was revised to R5-204513.

R5-204513	Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1660  rev 1 Cat: F (Rel-16)

					Source: China Telecom, Datang linktester

(Replaces R5-203522)

Decision: 		The document was agreed.

R5-204237	Correction to NR5G RRC TC 8.1.4.1.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1746  Cat: F (Rel-16)

					Source: Qualcomm CDMA Technologies

Discussion:

wrong AI!

Decision: 		The document was agreed.

6.4.4.4.1.5	RRC Others (clause 8.1.5)

R5-203610	Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1686  Cat: B (Rel-16)

					Source: China Telecom,Datang linktester

Discussion:

late doc

Decision: 		The document was withdrawn.

R5-203611	Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1687  Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

Discussion:

.*docx, Cat. F

r1

Decision: 		The document was revised to R5-204514.

R5-204514	Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1687  rev 1 Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

(Replaces R5-203611)

Discussion:

first agreed, then withdrawn!

Dependency on ‘nr-HO-ToEN-DC-r16' capability’ which hasn’t been catered for, thus could result in incorrectly failing a conformant Rel-16 UE.

Decision: 		The document was withdrawn.

R5-204254	Correction to NR UE Capability test case 8.1.5.1.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1748  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Discussion:

wrong AI!

Decision: 		The document was agreed.

###### 6.4.4.4.2	MR-DC RRC

6.4.4.4.2.1	RRC UE Capability / Others (clause 8.2.1)

R5-203644	Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1688  Cat: B (Rel-16)

					Source: China Telecom,Datang linktester

Discussion:

r1

Decision: 		The document was revised to R5-204515.

R5-204515	Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1688  rev 1 Cat: B (Rel-16)

					Source: China Telecom,Datang linktester

(Replaces R5-203644)

Discussion:

TF160 - missed to upload r1 and include this content in the final version so has to be withdrawn.

Decision: 		The document was withdrawn.

6.4.4.4.2.2	RRC Radio Bearer (clause 8.2.2)

6.4.4.4.2.3	RRC Measurement / Handovers (clause 8.2.3)

6.4.4.4.2.4	RRC Carrier Aggregation (clause 8.2.4)

6.4.4.4.2.5	RRC Reconfiguration / Radio Link Failure (clause 8.2.5)

6.4.4.4.2.6	RRC Others (clause 8.2.6)

##### 6.4.4.5	5GS Mobility Management

###### 6.4.4.5.1	MM Primary authentication and key agreement (clause 9.1.1)

###### 6.4.4.5.2	MM Security mode control, Identification & Generic UE configuration update (clauses 9.1.2, 9.1.3 & 9.1.4)

###### 6.4.4.5.3	MM Registration & De-registration (clauses 9.1.5 & 9.1.6)

###### 6.4.4.5.4	MM Service Request (clause 9.1.7)

###### 6.4.4.5.5	MM SMS Over NAS (clause 9.1.8)

##### 6.4.4.6	5GS Non-3GPP Access Mobility Management (clause 9.2)

R5-203739	Corrections to 5GS Non-3GPP Access TC 9.2.1.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1717  Cat: F (Rel-16)

					Source: ZTE Corporation

Decision: 		The document was agreed.

R5-203740	Corrections to 5GS Non-3GPP Access TC 9.2.5.1.4

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1718  Cat: F (Rel-16)

					Source: ZTE Corporation

Decision: 		The document was agreed.

R5-203741	Corrections to 5GS Non-3GPP Access TC 9.2.7.1

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1719  Cat: F (Rel-16)

					Source: ZTE Corporation

Decision: 		The document was agreed.

R5-203742	Corrections to 5GS Non-3GPP Access TC 9.2.7.2

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1720  Cat: F (Rel-16)

					Source: ZTE Corporation

Decision: 		The document was agreed.

##### 6.4.4.7	5GS Inter-system Mobility (clause 9.3)

##### 6.4.4.8	5GS Session Management

###### 6.4.4.8.1	SM PDU session authentication and authorization (clause 10.1.1)

###### 6.4.4.8.2	SM Network-requested PDU session modification & release (clauses 10.1.2 & 10.1.3)

###### 6.4.4.8.3	SM UE-requested PDU session establishment, modification & release (clauses 10.1.4, 10.1.5 & 10.1.6)

##### 6.4.4.9	EN-DC Session Management (clause 10.2)

##### 6.4.4.10	5GS Non-3GPP Access Session Management (clause 10.3)

##### 6.4.4.11	5GS Multilayer and Services

###### 6.4.4.11.1	EPS Fallback

R5-203518	Introduction of a new test case for voice fallback indication under EPS Fallback with handover

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1657  Cat: F (Rel-16)

					Source: CATT, TDIA

Discussion:

r1

comments from R&S and MCC160.

r3

withdrawn

Decision: 		The document was revised to R5-204516.

R5-204516	Introduction of a new test case for voice fallback indication under EPS Fallback with handover

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1657  rev 1 Cat: F (Rel-16)

					Source: CATT, TDIA

(Replaces R5-203518)

Decision: 		The document was withdrawn.

R5-203519	Introduction of a new test case for voice fallback indication under EPS Fallback with redirection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1658  Cat: F (Rel-16)

					Source: CATT, TDIA

Discussion:

r1

comments from MCC160.

r3

Decision: 		The document was revised to R5-204517.

R5-204517	Introduction of a new test case for voice fallback indication under EPS Fallback with redirection

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1658  rev 1 Cat: F (Rel-16)

					Source: CATT, TDIA

(Replaces R5-203519)

Decision: 		The document was agreed.

###### 6.4.4.11.2	RAT Fallback

###### 6.4.4.11.3	Unified Access Control (UAC)

###### 6.4.4.11.4	Emergency Services

#### 6.4.5	TS 38.523-2

R5-203520	Addition of test applicabilities of test cases for voice fallback indication

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0091  Cat: F (Rel-16)

					Source: CATT, TDIA

Discussion:

r3

Decision: 		The document was revised to R5-204519.

R5-204519	Addition of test applicabilities of test cases for voice fallback indication

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0091  rev 1 Cat: F (Rel-16)

					Source: CATT, TDIA

(Replaces R5-203520)

Decision: 		The document was agreed.

R5-203599	Update applicability of Inter-RAT handover from NR to EN-DC test case

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0093  Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

Discussion:

Cat. B

r1

Need to add PICS definition for 'nr-HO-ToEN-DC-r16' and update applicability condition to use this PICS (Action Point to be raised)"

Decision: 		The document was revised to R5-204520.

R5-204520	Update applicability of Inter-RAT handover from NR to EN-DC test case

Type: CR		For: Agreement
					38.523-2 v16.4.0	  CR-0093  rev 1 Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

(Replaces R5-203599)

Decision: 		The document was agreed.

#### 6.4.6	TS 38.523-3

#### 6.4.7	Discussion Papers, Work Plan, TC lists

### 6.5	Routine Maintenance for TS 36 Series TEIx_Test

#### 6.5.1	Routine Maintenance for TS 36.508

R5-203495	Correction to USIM content for eCall over IMS test cases

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1323  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Decision: 		The document was agreed.

R5-203605	Update the related RRC messages to support Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1324  Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

Discussion:

*.docx, Cat. B

r1

Decision: 		The document was revised to R5-204521.

R5-204521	Update the related RRC messages to support Inter-RAT handover from NR to EN-DC

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1324  rev 1 Cat: F (Rel-16)

					Source: China Telecom,Datang linktester

(Replaces R5-203605)

Decision: 		The document was agreed.

R5-204279	Updates to clauses 4.5A.3, 4.5A.30

Type: CR		For: Agreement
					36.508 v16.5.0	  CR-1331  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Discussion:

R&S: better to handle this in TS 34.229-1 cl A.1.1.

Decision: 		The document was withdrawn.

#### 6.5.2	Routine Maintenance for TS 36.509

R5-203286	Added definition of RSAP and RSARP in 36.509

Type: CR		For: Agreement
					36.509 v15.3.0	  CR-0207  Cat: F (Rel-15)

					Source: Keysight Technologies UK Ltd

Discussion:

cover 38.509

r1 was produced.

r2

TF160 manager: add full title for 36.214.

Decision: 		The document was revised to R5-204365.

R5-204365	Added definition of RSAP and RSARP in 36.509

Type: CR		For: Agreement
					36.509 v15.3.0	  CR-0207  rev 1 Cat: F (Rel-15)

					Source: Keysight Technologies UK Ltd

(Replaces R5-203286)

Discussion:

reference title of TS 36.214 has been corrected.

Decision: 		The document was agreed.

#### 6.5.3	Routine Maintenance for TS 36.523-1

##### 6.5.3.1	Idle Mode

R5-203812	Correction RRC idle mode test cases 6.1.1.x

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4946  Cat: F (Rel-16)

					Source: ANRITSU LTD

Decision: 		The document was agreed.

##### 6.5.3.2	Layer 2

###### 6.5.3.2.1	MAC

###### 6.5.3.2.2	RLC

###### 6.5.3.2.3	PDCP

##### 6.5.3.3	RRC

###### 6.5.3.3.1	RRC Part 1 (clauses 8.1 and 8.5)

###### 6.5.3.3.2	RRC Part 2 (clause 8.2),

###### 6.5.3.3.3	RRC Part 3 (clause 8.3)

R5-203809	Correction to RRC measurement testcase 8.3.1.11 for measGapConfig for CAT-M1

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4945  Cat: F (Rel-16)

					Source: ANRITSU LTD

Decision: 		The document was agreed.

###### 6.5.3.3.4	Inter-RAT (clauses 8.4 & 8.4A)

###### 6.5.3.3.5	RRC LTE MDT (clause 8.6)

R5-204300	Update of MDT test cases to handle IMS Re-registration

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4957  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Decision: 		The document was agreed.

R5-204339	Correction to MDT test case 8.6.4.13

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4958  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

Decision: 		The document was agreed.

R5-204340	Correction to MDT test case 8.6.8.8

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4959  Cat: F (Rel-16)

					Source: CMCC

Discussion:

late doc

Decision: 		The document was agreed.

###### 6.5.3.3.6	RRC ANR for UTRAN (clause 8.7)

##### 6.5.3.4	EPS Mobility Management

R5-203493	Updates to EMM test cases to handle IMS Re-registration

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4940  Cat: F (Rel-16)

					Source: Keysight Technologies UK

Discussion:

late doc

not available

Decision: 		The document was not pursued.

R5-203586	Update of TC 9.2.1.1.28b

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4942  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

comments from TF160 and Qualcomm.

Decision: 		The document was revised to R5-204522.

R5-204522	Update of TC 9.2.1.1.28b

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4942  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203586)

Decision: 		The document was agreed.

R5-203892	Addition of new NAS test case to test handling of extended octets

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4947  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r2

TF160 feedback.

Decision: 		The document was revised to R5-204523.

R5-204523	Addition of new NAS test case to test handling of extended octets

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4947  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203892)

Decision: 		The document was agreed.

R5-204130	Correction to 9.x test cases to handle IMS Re-registration  (moving between HPLMN and VPLMN)

Type: CR		For: Agreement
					38.523-1 v16.4.0	  CR-1741  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm

Discussion:

late doc

reissued as R5-204345 because of wrong spec.

Decision: 		The document was withdrawn.

R5-204345	Correction to 9.x test cases to handle IMS Re-registration  (moving between HPLMN and VPLMN)

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4960  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ, Qualcomm

Abstract:

reissued from R5-204130 because of wrong spec.

Decision: 		The document was agreed.

R5-204252	Editorial update to EMM test case 9.2.1.1.7b

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4955  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Abstract:

Editorial change

Decision: 		The document was agreed.

R5-204295	Update of EMM test cases to handle IMS Re-registration

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4956  Cat: F (Rel-16)

					Source: Qualcomm Incorporated

Discussion:

r1

comments received from MCC TF160.

Decision: 		The document was revised to R5-204524.

R5-204524	Update of EMM test cases to handle IMS Re-registration

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4956  rev 1 Cat: F (Rel-16)

					Source: Qualcomm Incorporated

(Replaces R5-204295)

Decision: 		The document was agreed.

##### 6.5.3.5	EPS Session Management

##### 6.5.3.6	General Tests

##### 6.5.3.7	Interoperability Radio Bearers

##### 6.5.3.8	Multilayer Procedures

R5-203427	Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4936  Cat: F (Rel-16)

					Source: Huawei, Hisilicon

Discussion:

r1

Decision: 		The document was revised to R5-204525.

R5-204525	Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4936  rev 1 Cat: F (Rel-16)

					Source: Huawei, Hisilicon

(Replaces R5-203427)

Decision: 		The document was agreed.

##### 6.5.3.9	PWS - ETWS, CMAS

##### 6.5.3.10	Non-3GPP

##### 6.5.3.11	Others (TS 36.523-1 clauses not covered by other AIs under AI 6.5.3, e.g. eMBMS, Home (e)NB, MBMS in LTE, D2D, SC-PTM, NB-IoT, CIoT...)

R5-203545	Correction to SC-PTM test case 21.2.1

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4941  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203595	Modification and editorial changes to NB-IoT TC 22.4.26

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4943  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Discussion:

r1

Decision: 		The document was revised to R5-204526.

R5-204526	Modification and editorial changes to NB-IoT TC 22.4.26

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4943  rev 1 Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

(Replaces R5-203595)

Decision: 		The document was agreed.

R5-203799	Correction to NB-IoT test case 22.4.5

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4944  Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

Discussion:

late doc

was wrong AI.

r1

Decision: 		The document was revised to R5-204527.

R5-204527	Correction to NB-IoT test case 22.4.5

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4944  rev 1 Cat: F (Rel-16)

					Source: ROHDE & SCHWARZ

(Replaces R5-203799)

Decision: 		The document was agreed.

R5-204145	Updates to legacy TCs for feMTC

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4954  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

Decision: 		The document was revised to R5-204528.

R5-204528	Updates to legacy TCs for feMTC

Type: CR		For: Agreement
					36.523-1 v16.5.0	  CR-4954  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204145)

Decision: 		The document was agreed.

#### 6.5.4	Routine Maintenance for TS 36.523-2

R5-203583	Updates to TC execution guidance

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1315  Cat: F (Rel-16)

					Source: MCC TF160

Decision: 		The document was agreed.

R5-203898	Test applicability for new NAS TC 9.2.1.1.31

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1317  Cat: F (Rel-16)

					Source: NTT DOCOMO INC.

Decision: 		The document was agreed.

R5-204146	Updates to legacy TC applicability for feMTC

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1321  Cat: F (Rel-16)

					Source: Ericsson

Discussion:

r1

cover fixes

Decision: 		The document was revised to R5-204529.

R5-204529	Updates to legacy TC applicability for feMTC

Type: CR		For: Agreement
					36.523-2 v16.5.0	  CR-1321  rev 1 Cat: F (Rel-16)

					Source: Ericsson

(Replaces R5-204146)

Decision: 		The document was agreed.

#### 6.5.5	Routine Maintenance for TS 36.523-3

R5-203546	Routine maintenance for TS 36.523-3

Type: CR		For: Agreement
					36.523-3 v16.5.1	  CR-4527  Cat: F (Rel-16)

					Source: MCC TF160, Bureau Veritas

Decision: 		The document was agreed.

#### 6.5.6	Discussion Papers, Work Plan, TC lists

R5-203759	TS 36.523-1 Status before RAN5#88-e

Type: other		For: Information
					Source: Samsung (Rapporteur)

Decision: 		The document was noted.

R5-203894	Proposal for new EPS Mobility Management test case for extended octets

Type: discussion		For: Discussion
					Source: NTT DOCOMO INC.

Discussion:

Proposal accepted

Decision: 		The document was noted.

R5-204144	Discussion paper on applicability of legacy test cases for Cat-M1/M2

Type: discussion		For: Endorsement
					Source: Ericsson

Discussion:

Proposal accepted

Decision: 		The document was noted.

### 6.6	Other Maintenance TEIx_Test

#### 6.6.1	Routine Maintenance for TDD (HCR & LCR)

##### 6.6.1.1	TS 34.108

##### 6.6.1.2	TS 34.123-1

##### 6.6.1.3	TS 34.123-2

##### 6.6.1.4	TS 34.123-3

##### 6.6.1.5	Discussion Papers, Work Plan, TC list & CR summary

#### 6.6.2	Routine Maintenance for TS 34.108

#### 6.6.3	Routine Maintenance for TS 34.109

#### 6.6.4	Routine Maintenance for TS 34.123

##### 6.6.4.1	TS 34.123-1

##### 6.6.4.2	TS 34.123-2

##### 6.6.4.3	TS 34.123-3

#### 6.6.5	Discussion Papers, Work Plan, TC lists

#### 6.6.6	Routine Maintenance for TS 34.229

##### 6.6.6.1	TS 34.229-1

R5-203426	Correction to IMS TCs-wait for UE IMS de-register

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1436  Cat: F (Rel-15)

					Source: Huawei, Hisilicon

Discussion:

TEI?

Title "Correction to EPC IMS TC13.1.19-wait for UE IMS de-register": does not match the database!

r1

Decision: 		The document was revised to R5-204530.

R5-204530	Correction to IMS TCs-wait for UE IMS de-register

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1436  rev 1 Cat: F (Rel-15)

					Source: Huawei, Hisilicon

(Replaces R5-203426)

Decision: 		The document was agreed.

R5-203430	Adding check to REGISTER regarding nonce-count

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1437  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, MCC TF160

Decision: 		The document was agreed.

R5-203432	Correction to A.1.2 regarding WWW-Authenticate

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1438  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203433	Extending default message for NOTIFY to cover de-registration scenarios

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1439  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ

Decision: 		The document was agreed.

R5-203547	Corrections of further XCAP test cases regarding rule elements

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1442  Cat: F (Rel-15)

					Source: MCC TF160

Discussion:

r1

Qualcomm’s comments incorporated - According to IR.92 cl 2.3.2 the <cp:conditions> element needs to contain the conditions as required by the supplementary service.

Decision: 		The document was revised to R5-204531.

R5-204531	Corrections of further XCAP test cases regarding rule elements

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1442  rev 1 Cat: F (Rel-15)

					Source: MCC TF160

(Replaces R5-203547)

Decision: 		The document was agreed.

R5-204374	On checking feature tags in REGISTER

Type: CR		For: Agreement
					34.229-1 v15.4.0	  CR-1443  Cat: F (Rel-15)

					Source: ROHDE & SCHWARZ, Qualcomm Incorporated

Discussion:

late doc

Decision: 		The document was agreed.

##### 6.6.6.2	TS 34.229-2

##### 6.6.6.3	TS 34.229-3

##### 6.6.6.4	TS 34.229-4

##### 6.6.6.5	Discussion Papers, Work Plan, TC lists

R5-203458	Discussion paper on old unverified IMS test cases

Type: discussion		For: Endorsement
					34.229-1 v..
					Source: ROHDE & SCHWARZ

Discussion:

"Proposals accepted. WLAN TCs G.15.19, G.15.22 also need to be voided.

LS to be send to GCF, PTCRB and GSMA seeking confirmation about lack of industry interst and support for these features before TCs are voided in RAN5#89-e

R&S to draft the LS"

Decision: 		The document was noted.

R5-203459	Discussion paper on IR.92 update

Type: discussion		For: Endorsement
					Source: ROHDE & SCHWARZ

Discussion:

No comments on analysis findings and proposals. More time given for IMS contributors to consider and provide feedback. If there are no comments/concerns all proposals are accepted

Decision: 		The document was noted.

#### 6.6.7	Routine Maintenance for TS 37.571

##### 6.6.7.1	TS 37.571-2

R5-203511	Correction of WLAN Assistance Data Element referenced clause

Type: CR		For: Agreement
					37.571-2 v16.4.0	  CR-0133  Cat: F (Rel-16)

					Source: PCTEST Engineering Laboratory, LLC

Abstract:

Correction of WLAN Assistance Data Element referenced clause

Decision: 		The document was agreed.

R5-203512	Addition of OTDOA information for pre-test conditions for test 9.3.3.1B

Type: CR		For: Agreement
					37.571-2 v16.4.0	  CR-0134  Cat: F (Rel-16)

					Source: PCTEST Engineering Laboratory, LLC

Abstract:

The OTDOA (LTE) information for pre-test conditions for test 9.3.3.1B is missing.

Discussion:

r1

Merged changes from R5-203273 (R&S).

Decision: 		The document was revised to R5-204532.

R5-204532	Addition of OTDOA information for pre-test conditions for test 9.3.3.1B

Type: CR		For: Agreement
					37.571-2 v16.4.0	  CR-0134  rev 1 Cat: F (Rel-16)

					Source: PCTEST Engineering Laboratory, LLC

(Replaces R5-203512)

Decision: 		The document was agreed.

##### 6.6.7.2	TS 37.571-3

##### 6.6.7.3	TS 37.571-4

##### 6.6.7.4	TS 37.571-5

##### 6.6.7.5	Discussion Papers, Work Plan, TC lists

#### 6.6.8	Routine Maintenance for TS 51.010

##### 6.6.8.1	TS 51.010-1 (Signalling)

##### 6.6.8.2	TS 51.010-2 (Signalling)

##### 6.6.8.3	TS 51.010-5 (Signalling)

##### 6.6.8.4	TS 51.010-7 (Signalling)

##### 6.6.8.5	Discussion Papers, Work Plan, TC list & CR summary

#### 6.6.9	Routine Maintenance for MCPTT

##### 6.6.9.1	TS 36.579-1

R5-203548	New MCPTT Common Procedures for CT/CO session establishment

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0078  Cat: F (Rel-14)

					Source: MCC TF160, UPV/EHU, Nemergent Solutions

Discussion:

r1

comments from Samsung & NIST incorporated.

r3

Decision: 		The document was revised to R5-204533.

R5-204533	New MCPTT Common Procedures for CT/CO session establishment

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0078  rev 1 Cat: F (Rel-14)

					Source: MCC TF160, UPV/EHU, Nemergent Solutions

(Replaces R5-203548)

Decision: 		The document was agreed.

R5-203549	Updates to MCX generic test procedures and default message contents

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0079  Cat: F (Rel-14)

					Source: MCC TF160, UPV/EHU, Nemergent Solutions

Discussion:

r1

MCPTT changes added from R5-204234 (CR#0085), one change removed to not overlap with R5-204371 (CR#0086).

r2

Test USIM parameters for MCVideo and MCData added in cl. 5.5.10.

Decision: 		The document was revised to R5-204534.

R5-204534	Updates to MCX generic test procedures and default message contents

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0079  rev 1 Cat: F (Rel-14)

					Source: MCC TF160, UPV/EHU, Nemergent Solutions

(Replaces R5-203549)

Decision: 		The document was agreed.

R5-204095	Group Communications Key download mechanism

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0080  Cat: F (Rel-14)

					Source: NEMERGENT

Discussion:

The TF160 manager spotted editorial issues.

Decision: 		The document was withdrawn.

R5-204096	Description of the distribution of MSCCK and MuSiK

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0081  Cat: F (Rel-14)

					Source: UPV/EHU, Nemergent Solutions

Discussion:

r1

Decision: 		The document was revised to R5-204535.

R5-204535	Description of the distribution of MSCCK and MuSiK

Type: CR		For: Agreement
					36.579-1 v14.7.0	  CR-0081  rev 1 Cat: F (Rel-14)

					Source: UPV/EHU, Nemergent Solutions

(Replaces R5-204096)

Discussion:

late upload

Decision: 		The document was agreed.

##### 6.6.9.2	TS 36.579-2

R5-203550	Update to MCPTT Test Case 6.1.1.3

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0089  Cat: F (Rel-14)

					Source: MCC TF160

Discussion:

r1

comments from Samsung and NIST incorporated.

r3

Decision: 		The document was revised to R5-204536.

R5-204536	Update to MCPTT Test Case 6.1.1.3

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0089  rev 1 Cat: F (Rel-14)

					Source: MCC TF160

(Replaces R5-203550)

Decision: 		The document was agreed.

R5-203551	Update to MCPTT Test Case 6.1.1.4

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0090  Cat: F (Rel-14)

					Source: MCC TF160

Discussion:

r1

comments from Samsung and NIST incorporated.

r2

Decision: 		The document was revised to R5-204537.

R5-204537	Update to MCPTT Test Case 6.1.1.4

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0090  rev 1 Cat: F (Rel-14)

					Source: MCC TF160

(Replaces R5-203551)

Decision: 		The document was agreed.

R5-203552	Update to MCPTT Test Case 6.1.1.7

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0091  Cat: F (Rel-14)

					Source: MCC TF160

Discussion:

r1

comments from Samsung and NIST incorporated.

r3

Decision: 		The document was revised to R5-204538.

R5-204538	Update to MCPTT Test Case 6.1.1.7

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0091  rev 1 Cat: F (Rel-14)

					Source: MCC TF160

(Replaces R5-203552)

Decision: 		The document was agreed.

R5-203553	Correction to MCPTT Test Case 6.1.1.8

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0092  Cat: F (Rel-14)

					Source: MCC TF160

Discussion:

r1

comments from Samsung and NIST incorporated.

r3

Decision: 		The document was revised to R5-204539.

R5-204539	Correction to MCPTT Test Case 6.1.1.8

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0092  rev 1 Cat: F (Rel-14)

					Source: MCC TF160

(Replaces R5-203553)

Decision: 		The document was agreed.

R5-204097	Integration of security features in MBMS procedures

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0093  Cat: F (Rel-14)

					Source: UPV/EHU, NEMERGENT

Discussion:

r1

Decision: 		The document was revised to R5-204540.

R5-204540	Integration of security features in MBMS procedures

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0093  rev 1 Cat: F (Rel-14)

					Source: UPV/EHU, NEMERGENT

(Replaces R5-204097)

Discussion:

late upload

Decision: 		The document was agreed.

R5-204227	Corrections to Chat Group Calls

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0094  Cat: F (Rel-14)

					Source: NIST

Discussion:

r1

Decision: 		The document was revised to R5-204541.

R5-204541	Corrections to Chat Group Calls

Type: CR		For: Agreement
					36.579-2 v14.7.0	  CR-0094  rev 1 Cat: F (Rel-14)

					Source: NIST

(Replaces R5-204227)

Decision: 		The document was agreed.

##### 6.6.9.3	TS 36.579-3

##### 6.6.9.4	TS 36.579-4

##### 6.6.9.5	TS 36.579-5

R5-203554	Routine maintenance for TS 36.579-5

Type: CR		For: Agreement
					36.579-5 v13.6.0	  CR-0008  Cat: F (Rel-13)

					Source: MCC TF160, UPV/EHU, Nemergent Solutions

Decision: 		The document was agreed.

##### 6.6.9.6	Other Specs

##### 6.6.9.7	Discussion Papers, Work Plan, TC lists

R5-203555	MCX message content issues

Type: discussion		For: Endorsement
					Source: MCC TF160, UPV/EHU, Nemergent Solutions

Discussion:

"Email discussion ongoing among interested companies - Conference Call to be set up if needed

Changes proposed in CR R5-203549 to be reviewed"

Decision: 		The document was noted.

R5-203579	MCPTT call establishment procedures

Type: discussion		For: Endorsement
					Source: MCC TF160

Discussion:

"Email discussion ongoing among interested companies - Conference Call to be set up if needed

Samsung raised concerns about adopting a generic procedures based approach for MCPTT test definition now as it can impact a large number of test cases which need to be carefully reviewed and updated. This requires a major effort and commitment from contributors which won't be forthcoming.

MCC TF160 sees generic procedures approach significantly aiding TTCN implementation and maintenance, acknowledges effort invovled now in updating test cases that were defined few years ago.

Samsung to review CRs and provide technical as well as PRD13 compliance feedback to TF160. Based on this CRs will be updated before being considered for agreement.

TF160 PM committed to make sure future contributions from TF160 on MCS to be fully compliant to PRD13

Way forward of generic procedures accepted"

Decision: 		The document was noted.

R5-204094	MCPTT IPCAN test environment

Type: discussion		For: Discussion
					Source: UPV/EHU

Abstract:

This discussion document proposes the introduction of a new test model, the IPCAN test model, to facilitate SS vendors to develop full qualified conformance testers which also follow the EUTRA TS 36.508 requirements for the MCPTT test cases.

Discussion:

"LATE DOCUMENT

This discussion document proposes the introduction of a new test model, the IPCAN test model, to facilitate SS vendors to develop full qualified conformance testers which also follow the EUTRA TS 36.508 requirements for the MCPTT test cases.

Email discussion ongoing among interested companies - Conference Call to be set up if needed

RAN5 acknowledges industry need to have a test solution enabling MCPTT certification which required verified and validated test cases. Proposed IPCAN test enviornment provides a pathway for this allowing MCPTT UE to be tested as a full device. Agreement in principle to adopt IPCAN-based MCPTT test model, following steps recommended to proceed further:

- Proponents to seek RAN approval to use IPCAN-based MCPTT test model for formal RAN5 veriifcation and publication of reference test suite

- Test definition in TS 36.579-x shall be updated making E-UTRA procedures and message sequence informative for IPCAN-based MCPTT test model"

Decision: 		The document was noted.

### 6.7	Outgoing liaison statements for provisional approval

R5-204361	LS on old unverified IMS test cases

Type: LS out		For: Approval
					to GCF CAG, PTCRB PVG, cc GSMA 5GJA
					Source: TSG WG RAN5

Abstract:

A number of test cases for IMS over EPC in 3GPP TS 34.229-1 have been available in prose and have been verifiable in TTCN for a long time but did not see progress in verification:

1)	Test case 8.14 on “Initial registration for three implicit registration sets” was introduced in Feb 2011 at RAN5#50, but never verified.

2)	Test case 12.16 on “MO MTSI Text call” was introduced in Feb 2008 at RAN5#38, but never verified.

3)	Test case 12.17 on “MT MTSI Text call” was introduced in Aug 2008 at RAN5#40, but never verified.

4)	Test case 15.21 on “Joining a conference after being invited to it” was introduced in Nov 2008 at RAN5#41, but never verified.

5)	Test case 15.21b on “Joining a conference after being invited to it / Video” was introduced in Aug 2014 at RAN5#64, but never verified.

6)	Test case G.15.19 on “Joining a conference after being invited to it / WLAN” was introduced in Nov 2016 at RAN5#73, but never verified.

7)	Test case G.15.22 on “Joining a conference after being invited to it with video / WLAN” was introduced in Nov 2016 at RAN5#73, but never verified.

Therefore, RAN5 intends to void these test cases and does not plan to add corresponding test cases to its Work Plan for IMS over 5GS.

Actions: To GCF CAG, PTCRB, GSMA 5GJA groups: Take note of above intention of RAN5 to void mentioned test cases.

Discussion:

Add IMS over WLAN test cases that are also to be voided

'IMS over EPC' test cas.

No actions

Decision: 		The document was approved.

R5-204362	LS on two consecutive invalid challenges

Type: LS out		For: Approval
					to TSG WG CT1
					Source: TSG WG RAN5

Abstract:

When investigating IMS core specification TS 24.229 for appropriate test coverage for IMS over 5GS, relevant ambiguous text was detected. Specifically, TS 24.229 cl 5.1.1.5.12 contains the following text:

A UE shall only respond to two consecutive invalid challenges and shall not automatically attempt authentication after receiving two consecutive invalid challenges. The UE may attempt to register with the network again after an implementation specific time.

First the text asks to respond to two consecutive challenges (which is understood to send another REGISTER request after the second invalid challenge) and then it says not to attempt authentication after two consecutive invalid challenges (which is understood not to send another REGISTER request after the second invalid challenge).

Does the core specification expect the UE to send another REGISTER request after the second invalid 401 Unauthorized response or not?

Actions: To TSG CT WG1 group: TSG RAN WG5 respectfully asks TSG CT WG1 to clarify the above ambiguity.

Discussion:

Update description and action as discussed

Decision: 		The document was approved.

R5-204376	Status of Conformance testing development for Mission Critical Services (MCS)

Type: LS out		For: Approval
					to PTCRB, PTCRB PVG
					Source: TSG WG RAN5

Abstract:

RAN5 would like to provide information on the status of the conformance testing development for Mission Critical Services (MCS) as per the end of RAN5#88 meeting.

•	At this RAN5#88e meeting RAN5 endorsed the introduction of a new Work Item (WI) on UE Conformance Test Aspects for Mission Critical Enhancements for MCPTT, MCVideo and MCData for Rel-15

o	This MCS Rel-15 WI is pending approval at the 3GPP TSG RAN plenary in September 2020. RAN5 expects the proposal to be approved.

o	After the approval the expectations from the supporting companies are work in the scope of the WI to start at the RAN5 meeting in November 2020.

o	Pending the approval, the target completion date for the WI is planned for Q4, 2021. Depending on the WI outcome the TTCN-3 test suite implementation could be expected to complete in 2022.

o	The intention of the supporting companies is to prioritise the work on the MCPTT Rel-15 in the WI Work Plan (WP) during the last quarter of 2020 and the first quarter of 2021. TTCN-3 test suite implementation is to follow during 2021.

•	At the same time, RAN5 agreed to continue with the development of the MCS test specification targeting the provision of TTCN-3 test suite which can be used for validating the conformance of MCS Clients compliant with the Rel-14 requirements.

o	RAN5 will not develop testing for any Rel-13-only specific requirements. All MCPTT test case introduced as part of the MCS Rel-13 WI are being updated with Rel-14 requirements in both test specifications and TTCN-3 test suite implementation, wherever needed.

o	The MCS Rel-14 WI is expected to be closed at the TSG RAN meeting in September. TTCN-3 test suite implementation is to follow in 2021.

Decision: 		The document was approved.

R5-204383	LS on MCS group document subscription procedures

Type: LS out		For: Approval
					to TSG WG CT1
					Source: TSG WG RAN5

Discussion:

post meeting doc

deadline in 2 weeks 9.9., draft next week

Decision: 		The document was for email approval.

### 6.8	AOB

## 7	Closing Joint Session

### 7.1	Pointer CRs

### 7.2	Open Issues

#### 7.2.1	RF group docs still requiring WG verdict/confirmation - original A.I. retained

#### 7.2.2	Sig group docs still requiring WG verdict/confirmation - original A.I. retained

#### 7.2.3	Other open issues from joint sessions - original A.I. retained

#### 7.2.4	UE Application Layer Data Throughput Performance - original A.I. retained

#### 7.2.5	Other

### 7.3	iWD/PRD Updates

R5-203761	PRD-17 on Guidance to Work Item Codes, version 3.21 (post RAN#89-e version)

Type: other		For: Approval
					Source: Samsung (Rapporteur)

Decision: 		The document was not treated.

### 7.4	Work Items/ Study Items

#### 7.4.1	Final version of Work Item Proposals

R5-204351	New WID on: UE Conformance Test Aspects - 410 – 430 MHz E-UTRA FDD Band(s) for LTE PPDR and PMR/PAMR in Europe (Bands 87 and 88)

Type: WID new		For: Endorsement
					Source: Nokia, Nokia Shanghai Bell

(Replaces R5-203230)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204352	New WID on UE Conformance Test Aspects – B1C Signal in A-BDS Positioning System Support for LTE and NR

Type: WID new		For: Endorsement
					Source: CATT, CMCC

(Replaces R5-203465)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204353	New WID on UE Conformance Test Aspects for SON and MDT support for NR

Type: WID new		For: Endorsement
					Source: China Mobile Com. Corporation, Ericsson

(Replaces R5-203703)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-203893	New UE Conformance NR Band n53 WID

Type: WID new		For: Endorsement
					Source: GLOBALSTAR Inc.

Abstract:

Justification

NR Band n53 has been introduced in 3GPP RAN WG4 core specifications as a new NR TDD band. Therefore, 3GPP RAN WG5 test specifications need to be updated accordingly. The characteristics of the new NR Band n53 are:

•	Band n53: 2483.5 MHz to 2495 MHz

•	Support of 5 and 10 MHz channel bandwidths

Objective

The objective of the present work item is to update the 3GPP RAN WG5 RF, RRM and protocol test specifications for NR Band n53.

Decision: 		The document was withdrawn.

R5-204354	New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band)

Type: WID new		For: Endorsement
					Source: China Unicom, CMCC

(Replaces R5-203900)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204355	New WID on UE Conformance Test Aspects – Single Radio Voice Call Continuity from 5G to 3G

Type: WID new		For: Endorsement
					Source: China Unicom

(Replaces R5-203901)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204356	New WID on UE Conformance Test Aspects for NR performance enhancement

Type: WID new		For: Endorsement
					Source: Qualcomm Korea

(Replaces R5-203906)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204357	New WID on UE Conformance Test Aspects - Mission Critical Enhancements

Type: WID new		For: Endorsement
					Source: NIST, Samsung

(Replaces R5-204231)

Discussion:

is endorsed.

Decision: 		The document was endorsed.

R5-204358	New WID - UE Conformance Test Aspects for CLI handling for NR

Type: WID new		For: Endorsement
					Source: Qualcomm Incorporated

(Replaces R5-204292)

Discussion:

not available

endorsed on 31.8.

Decision: 		The document was endorsed.

#### 7.4.2	Active Work Items/ Study Item: work plans (wp), status reports (sr), Work Item Descriptions (wid)

R5-203212	WI Progress and Target Completion Date Review

Type: other		For: Information
					Source: WG Chairman

Decision: 		The document was not treated.

R5-203253	WP UE Conformance Test Aspects – Addition of Power Class 2 UE for LTE bands 31 and 72

Type: Work Plan		For: Information
					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was noted.

R5-203254	SR UE Conformance Test Aspects – Addition of Power Class 2 UE for LTE bands 31 and 72

Type: WI status report		For: Information
					Source: Nokia, Nokia Shanghai Bell

Abstract:

completion level is 100%.

Decision: 		The document was noted.

R5-203257	Work plan: UE Conformance Test Aspects – Further NB-IoT enhancements

Type: Work Plan		For: Information
					Source: CATT

Decision: 		The document was noted.

R5-203258	SR UE Conformance Test Aspects - Further NB-IoT enhancements

Type: WI status report		For: Endorsement
					Source: CATT

Decision: 		The document was noted.

R5-203326	SR - Rel-16 IIOT after RAN5#88-e

Type: WI status report		For: (not specified)
					Source: CMCC

Decision: 		The document was noted.

R5-203327	WP - Rel-16 IIOT after RAN5#88-e

Type: Work Plan		For: (not specified)
					Source: CMCC

Decision: 		The document was noted.

R5-203328	SR - NR_Rel-16_CA_DC after RAN5#88-e

Type: WI status report		For: (not specified)
					Source: CMCC

Decision: 		The document was not treated.

R5-203329	WP - NR_Rel-16_CA_DC after RAN5#88-e

Type: Work Plan		For: (not specified)
					Source: CMCC

Decision: 		The document was not treated.

R5-203331	SR - ENDC_UE_PC2_TDD_TDD after RAN5#88-e

Type: WI status report		For: (not specified)
					Source: CMCC

Decision: 		The document was noted.

R5-203332	WP - ENDC_UE_PC2_TDD_TDD after RAN5#88-e

Type: Work Plan		For: (not specified)
					Source: CMCC

Decision: 		The document was noted.

R5-203333	Revised WID ENDC_UE_PC2_TDD_TDD-UEConTest

Type: WID revised		For: Approval
					Source: CMCC

Decision: 		The document was noted.

R5-203420	SR-NR Mobility Enhancements-Status after RAN5#88-e

Type: WI status report		For: Endorsement
					Source: Huawei, Hisilicon

Decision: 		The document was noted.

R5-203422	SR-NR V2X-Status after RAN5#88-e

Type: WI status report		For: Endorsement
					Source: Huawei, Hisilicon

Decision: 		The document was noted.

R5-203466	WP UE Conformance Test Aspects - UE Power Saving in NR

Type: Work Plan		For: Information
					Source: CATT

Decision: 		The document was noted.

R5-203468	SR UE Conformance Test Aspects - UE Power Saving in NR

Type: WI status report		For: Endorsement
					Source: CATT

Decision: 		The document was noted.

R5-203469	SR UE Conformance Test Aspects - UE Power Saving in NR

Type: WI status report		For: Endorsement
					Source: CATT

Decision: 		The document was withdrawn.

R5-203568	NR V2X WP after RAN5 88-e

Type: Work Plan		For: Information
					Source: Huawei, Hisilicon

Decision: 		The document was noted.

R5-203569	NR Mobile Enhancement WP after RAN5 88-e

Type: Work Plan		For: Information
					Source: Huawei, Hisilicon

Decision: 		The document was noted.

R5-203618	WP UE Conformance Test Aspects - Rel-14 LTE CA configurations

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203619	SR UE Conformance Test Aspects - Rel-14 LTE CA configurations

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203620	WP UE Conformance Test Aspects - Rel-15 LTE CA configurations

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203621	SR UE Conformance Test Aspects - Rel-15 LTE CA configurations

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203622	WP UE Conformance Test Aspects - Rel-16 LTE CA configurations

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203623	SR UE Conformance Test Aspects - Rel-16 LTE CA configurations

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203624	WP UE Conformance Test Aspects - 5G system with NR and LTE

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203625	SR UE Conformance Test Aspects - 5G system with NR and LTE

Type: WI status report		For: Information
					Source: Ericsson

Abstract:

overall completion reached 79% (+4%). SA NR (SA Option 2) reached 79% (+2%) and EN-DC (NSA Option 3) reached 89% (+7%).

Decision: 		The document was not treated.

R5-203628	WP UE Conformance Test Aspects - New Rel-16 NR bands and extension of existing NR bands

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203629	SR UE Conformance Test Aspects - New Rel-16 NR bands and extension of existing NR bands

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-203630	Revised WID - New Rel-16 NR bands and extension of existing NR bands

Type: WID revised		For: Information
					Source: Ericsson

Discussion:

not needed.

Decision: 		The document was withdrawn.

R5-203646	WP UE Conformance Test Aspects- Even further mobility enhancement for E-UTRAN after RAN5#88-e

Type: Work Plan		For: Information
					Source: China Telecom Corporation Ltd.

Decision: 		The document was noted.

R5-203647	SR UE Conformance Test Aspects- Even further mobility enhancement for E-UTRAN after RAN5#88-e

Type: WI status report		For: Endorsement
					Source: China Telecom Corporation Ltd.

Decision: 		The document was noted.

R5-203758	SR of Enhancing LTE CA Utilization WI for RAN5_88e

Type: WI status report		For: (not specified)
					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was not treated.

R5-203762	WP of Enhancing LTE CA Utilization for RAN5_88e

Type: WI status report		For: (not specified)
					Source: Nokia, Nokia Shanghai Bell

Decision: 		The document was not treated.

R5-203866	WP - R15 TDD HPUE – Status after RAN5#88-e

Type: Work Plan		For: Information
					Source: Huawei, HiSilicon

Abstract:

The overall completion is 50%

Decision: 		The document was noted.

R5-203867	SR - R15 TDD HPUE – Status after RAN5#88-e

Type: WI status report		For: Endorsement
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-203990	WP - Shortened TTI and processing time for LTE

Type: Work Plan		For: Information
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-203991	SR - Shortened TTI and processing time for LTE

Type: WI status report		For: Endorsement
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-203992	WP - RF requirements for NR frequency range 1 (FR1)

Type: Work Plan		For: Information
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-203993	SR - RF requirements for NR frequency range 1 (FR1)

Type: WI status report		For: Endorsement
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-203994	WP - Enhancements on MIMO for NR

Type: Work Plan		For: Information
					Source: Huawei, HiSilicon

Decision: 		The document was not treated.

R5-203995	SR - Enhancements on MIMO for NR

Type: WI status report		For: Endorsement
					Source: Huawei, HiSilicon

Decision: 		The document was noted.

R5-204138	WP UE Conformance Test Aspects - Even further enhanced MTC for LTE

Type: Work Plan		For: Information
					Source: Ericsson

Abstract:

overall completion is 47%

Decision: 		The document was noted.

R5-204139	SR UE Conformance Test Aspects - Even further enhanced MTC for LTE

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was noted.

R5-204211	WP UE Conformance Test Aspects – Rel14 Enhanced Full Dimension MIMO for LTE

Type: Work Plan		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-204212	SR UE Conformance Test Aspects – Rel14 Enhanced Full Dimension MIMO for LTE

Type: WI status report		For: Information
					Source: Ericsson

Decision: 		The document was not treated.

R5-204224	SR - UE Conformance Test Aspects - Mission Critical Improvements (UID - 790052) MCImp-UEConTest

Type: WI status report		For: Information
					Source: NIST

Decision: 		The document was noted.

R5-204225	WP - UE Conformance Test Aspects - Mission Critical Improvements (UID - 790052) MCImp-UEConTest

Type: Work Plan		For: Information
					Source: NIST

Decision: 		The document was noted.

R5-204242	WP UE Conformance Test Aspects - Rel-16 Private Network Support for NG-RAN

Type: Work Plan		For: Information
					Source: Qualcomm CDMA Technologies

Decision: 		The document was noted.

R5-204243	SR UE Conformance Test Aspects - Rel-16 Private Network Support for NG-RAN

Type: WI status report		For: Information
					Source: Qualcomm CDMA Technologies

Decision: 		The document was noted.

R5-204244	WP UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA

Type: Work Plan		For: Information
					Source: Qualcomm CDMA Technologies

Decision: 		The document was revised to R5-204542.

R5-204542	WP UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA

Type: Work Plan		For: Information
					Source: Qualcomm CDMA Technologies

(Replaces R5-204244)

Decision: 		The document was noted.

R5-204245	SR UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA

Type: WI status report		For: Information
					Source: Qualcomm CDMA Technologies

Decision: 		The document was noted.

R5-204316	Work Plan for TR 37.901-5

Type: Work Plan		For: Agreement
					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 post RAN87-e WP

Decision: 		The document was noted.

R5-204317	Status Report - Study on 5G NR UE Application Layer Data Throughput Performance

Type: WI status report		For: Agreement
					Source: Qualcomm CDMA Technologies

Abstract:

TR 37.901-5 post RAN87-e SR.

overall completion is 87%.

completion date is requested to be moved to Dec-2020 (+3 months).

Decision: 		The document was noted.

#### 7.4.3	Work Plan updates of recently closed work items

### 7.5	Docs still needing agreement/endorsement/approval (e.g. Outgoing LS, Reports, New Specs, Info for certification bodies etc.)

R5-203528	draft TS 36.579-6 v1.1.0

Type: draft TS		For: Information
					36.579-6 v1.1.0
					Source: NIST, Samsung

Decision: 		The document was not treated.

R5-203529	draft TS 36.579-7 v1.1.0

Type: draft TS		For: Information
					36.579-7 v1.1.0
					Source: NIST, Samsung

Decision: 		The document was not treated.

R5-204350	MCC TF160 Status Report

Type: report		For: Approval
					Source: MCC TF160

(Replaces R5-203531)

the following are endorsed:

•	The 2021 TTCN Tasks List presented in slides 13 & 14

•	The request from RAN5 to TSG RAN and 3GPP PCG/OP for funding of 58 man months in 2021

Decision: 		The document was approved.

R5-203615	RAN5#88-e summary of changes to RAN5 test cases with potential impact on GCF and PTCRB

Type: report		For: Information
					Source: Ericsson, Samsung

Abstract:

Post meeting document

Decision: 		The document was not treated.

R5-203617	3GPP RAN5 CA status list  (post-RAN5#88-e meeting)

Type: other		For: Information
					Source: Ericsson

Abstract:

Post meeting document

Decision: 		The document was not treated.

R5-203626	5GS progress report RAN5#88-e

Type: WI status report		For: Information
					Source: Ericsson

Abstract:

Post meeting document

Decision: 		The document was not treated.

R5-203627	Update of RAN5 5G NR phases and target update RAN5#88-e

Type: discussion		For: Endorsement
					Source: Ericsson

Abstract:

Post meeting document

Decision: 		The document was not treated.

R5-203760	TS 36.523-1 Status after RAN5#88-e

Type: other		For: Information
					Source: Samsung (Rapporteur)

Decision: 		The document was not treated.

R5-203771	FR2 Measurement Uncertainty (MU) / Test Tolerances (TT) Target Completion Update

Type: discussion		For: Discussion
					Source: AT&T

Abstract:

Post Meeting Document that will collect the status of the FR2 MU + TT target completion dates at the conclusion of the FR2 MU + TT items at RAN5 #88-e.

Decision: 		The document was noted.

R5-204364	Reply LS to LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level

Type: LS out		For: Approval
					to GCF Mission Critical Agreement Group (MCAG), cc TSG WG SA6
					Source: TSG WG RAN5

Abstract:

Response to:	LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level

RAN5 thanks GCF Mission Critical Agreement Group (MCAG) for the LS on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level and the valuable information from the industry on which 3GPP Release they will base their MCS implementation and deployments.

In regard to the Actions requested, RAN5 would like to provide the following information:

•	At this RAN5#88e meeting RAN5 endorsed the introduction of a new Work Item (WI) on UE Conformance Test Aspects for Mission Critical Enhancements for MCPTT, MCVideo and MCData for Rel-15

o	This MCS Rel-15 WI is pending approval at the 3GPP TSG RAN plenary in September 2020. RAN5 expects the proposal to be approved.

o	After the approval the expectations from the supporting companies are work in the scope of the WI to start at the RAN5 meeting in November 2020.

o	Pending the approval, the target completion date for the WI is planned for Q4, 2021. Depending on the WI outcome the TTCN-3 test suite implementation could be expected to complete in 2022.

o	The intention of the supporting companies is to prioritise the work on the MCPTT Rel-15 in the WI Work Plan (WP) during the last quarter of 2020 and the first quarter of 2021. TTCN-3 test suite implementation is to follow during 2021.

•	At the same time, RAN5 agreed to continue with the development of the MCS test specification targeting the provision of TTCN-3 test suite which can be used for validating the conformance of MCS Clients compliant with the Rel-14 requirements.

o	RAN5 will not develop testing for any Rel-13-only specific requirements. All MCPTT test case introduced as part of the MCS Rel-13 WI are being updated with Rel-14 requirements in both test specifications and TTCN-3 test suite implementation, wherever needed.

o	The MCS Rel-14 WI is expected to be closed at the TSG RAN meeting in September. TTCN-3 test suite implementation is to follow in 2021.

Decision: 		The document was approved.

R5-204367	TS 38.523-1 Status after RAN5#88-e

Type: other		For: Information
					Source: Samsung (Rapporteur)

Discussion:

post meeting doc

Decision: 		The document was noted.

### 7.6	Confirmation of Future RAN5 Matters

R5-203213	Review deadlines for next quarter

Type: other		For: Information
					Source: WG Chairman

Decision: 		The document was noted.

R5-204375	Critical prose CRs list for protocol test cases at RAN5#88-e

Type: LS out		For: Approval
					to GCF CAG, PTCRB PVG
					Source: TSG WG RAN5

Discussion:

post-meeting doc

Decision: 		The document was not treated.

### 7.7	AOB

R5-203214	draft RAN5#88-e meeting report

Type: report		For: Information
					Source: ETSI Secretariat

Decision: 		The document was noted.

Annex A: Contribution documents and status

## A1: List of TDocs

1658 documents were submitted at RAN5#88-e

| Document | Title | Source | Decision | Replaces | Replaced by |
| --- | --- | --- | --- | --- | --- |
| R5-203200 | Agenda - opening session | WG Chairman | revised |  | R5-204338 |
| R5-203201 | RAN5#88-e E-Meeting Timelines, Scope, Process | WG Chairman | noted |  |  |
| R5-203202 | RAN5 Leadership Team | WG Chairman | noted |  |  |
| R5-203203 | RAN5#87-e WG Minutes | ETSI Secretariat | approved |  |  |
| R5-203204 | RAN5#87-e WG Action Points | ETSI Secretariat | noted |  |  |
| R5-203205 | Latest RAN Plenary notes | WG Chairman | noted |  |  |
| R5-203206 | Latest RAN Plenary draft Report | WG Chairman | noted |  |  |
| R5-203207 | Post Plenary Active Work Item update | ETSI Secretariat | noted |  |  |
| R5-203208 | RAN5 SR to RP#88-e | WG Chairman | noted |  |  |
| R5-203209 | TF160 SR to RP#88-e | WG Chairman | noted |  |  |
| R5-203210 | RAN5#88-e LS Template | WG Chairman | noted |  |  |
| R5-203211 | Meeting schedule for 2020-21 | WG Chairman | noted |  |  |
| R5-203212 | WI Progress and Target Completion Date Review | WG Chairman | reserved |  |  |
| R5-203213 | Review deadlines for next quarter | WG Chairman | noted |  |  |
| R5-203214 | draft RAN5#88-e meeting report | ETSI Secretariat | noted |  |  |
| R5-203215 | NGMN Liaison Statement to 3GPP RAN4 on 5G NR Over The Air test methodologies and performance requirements | NGNM | noted |  |  |
| R5-203216 | Reply LS on support of eCall over NR | TSG WG CT1 | noted |  |  |
| R5-203217 | Reply LS to GSMA TS.48 publication | TSG WG CT6 | noted |  |  |
| R5-203218 | CAG-20-331_LS on replacement of 3CC to 5CC RRM TCs in GCF scheme | GCF CAG | noted |  |  |
| R5-203219 | LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level | GCF-TCCA Joint Taskforce #8 | noted |  |  |
| R5-203220 | LS response on Multiband relaxation for FR2 | TSG WG RAN4 | noted |  |  |
| R5-203221 | Reply LS to Reply LS on support for eCall over NR | TSG WG SA5 | noted |  |  |
| R5-203222 | dummy LS1 | ETSI Secretariat | withdrawn |  |  |
| R5-203223 | dummy LS2 | ETSI Secretariat | withdrawn |  |  |
| R5-203224 | Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1 | Nokia, Nokia Shanghai Bell | revised |  | R5-204800 |
| R5-203225 | Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities | Nokia, Nokia Shanghai Bell | revised |  | R5-204801 |
| R5-203226 | Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | revised |  | R5-204809 |
| R5-203227 | Adding receiver requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | agreed |  |  |
| R5-203228 | Introduction of PC2 UE for cat M1/M2 in LTE Bands 31 and 72 | Nokia, Nokia Shanghai Bell | agreed |  |  |
| R5-203229 | Introduction of Baseline Implementation Capabilities for PC2 in LTE Bands 31 and 72 | Nokia, Nokia Shanghai Bell | agreed |  |  |
| R5-203230 | New WID on: UE Conformance Test Aspects - 410 – 430 MHz E-UTRA FDD Band(s) for LTE PPDR and PMR/PAMR in Europe (Bands 87 and 88) | Nokia, Nokia Shanghai Bell | revised |  | R5-204351 |
| R5-203231 | TT analysis for RRM TC 8.5.2.1.1.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203232 | TT analysis for RRM TC 8.5.2.2.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203233 | TT analysis for RRM TC 8.5.2.3.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203234 | Update TC 8.5.2.1.1.1 with TT results and message contents | ROHDE & SCHWARZ | agreed |  |  |
| R5-203235 | Update TC 8.5.2.2.1 with TT results and message contents | ROHDE & SCHWARZ | agreed |  |  |
| R5-203236 | Update TC 8.5.2.3.1 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204783 |
| R5-203237 | TT analysis for RRM TC 4.7.4.1.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203238 | TT analysis for RRM TC 4.7.4.1.2 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203239 | TT analysis for RRM TC 4.7.4.2.1 | ROHDE & SCHWARZ | withdrawn |  |  |
| R5-203240 | TT analysis for RRM TC 4.7.4.2.2 | ROHDE & SCHWARZ | withdrawn |  |  |
| R5-203241 | Update TC 4.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204878 |
| R5-203242 | Update TC 4.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204775 |
| R5-203243 | Update TC 4.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204879 |
| R5-203244 | Update TC 4.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204776 |
| R5-203245 | Update TC 6.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204880 |
| R5-203246 | Update TC 6.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204778 |
| R5-203247 | Update TC 6.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204881 |
| R5-203248 | Update TC 6.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | revised |  | R5-204779 |
| R5-203249 | Annex E and F update with TT results for 8.5.2.x.x iRAT periodic reporting test cases | ROHDE & SCHWARZ | agreed |  |  |
| R5-203250 | Annex E and F update with TT results for 4.7.4.x.x EN-DC L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | agreed |  |  |
| R5-203251 | Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | revised |  | R5-204784 |
| R5-203252 | Void unnecessary TC 8.5.2.1.1.2 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203253 | WP UE Conformance Test Aspects – Addition of Power Class 2 UE for LTE bands 31 and 72 | Nokia, Nokia Shanghai Bell | noted |  |  |
| R5-203254 | SR UE Conformance Test Aspects – Addition of Power Class 2 UE for LTE bands 31 and 72 | Nokia, Nokia Shanghai Bell | noted |  |  |
| R5-203255 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator-r16, AvailableRB-SetPerCell and BAP-Routing-ID | Ericsson | withdrawn |  |  |
| R5-203256 | Template | Anritsu | withdrawn |  |  |
| R5-203257 | Work plan: UE Conformance Test Aspects – Further NB-IoT enhancements | CATT | noted |  |  |
| R5-203258 | SR UE Conformance Test Aspects - Further NB-IoT enhancements | CATT | noted |  |  |
| R5-203259 | Correction of test frequencies for NS_47 | Ericsson, SoftBank Corp. | revised |  | R5-204823 |
| R5-203260 | Adding NS_47 to Additional spurious emissions test case | Ericsson, SoftBank Corp. | agreed |  |  |
| R5-203261 | Adding UL MIMO additional spurious emissions test for NS_47 | Ericsson, SoftBank Corp. | agreed |  |  |
| R5-203262 | Adding band n48 to maximum output power and maximum output power reduction tests | Ericsson | revised |  | R5-204824 |
| R5-203263 | Adding band n48 to blocking characteristics tests | Ericsson | withdrawn |  |  |
| R5-203264 | Correction to the test procedure of NR SA event triggered tests | ROHDE & SCHWARZ | revised |  | R5-204780 |
| R5-203265 | Correction to the test procedure of NR SA event triggered tests inter-freq | ROHDE & SCHWARZ | revised |  | R5-204781 |
| R5-203266 | Correction to the test procedure of NR SA event triggered tests inter-RAT | ROHDE & SCHWARZ | revised |  | R5-204782 |
| R5-203267 | [EDITORIAL] Fix formatting issues throwing DOCX conversion errors in TS 38.533 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203268 | Correction of test applicability for EN-DC event-triggered tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-203269 | Correction of test applicability for NR SA event-triggered tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-203270 | Adding annex table for iRAT measurement configuration | ROHDE & SCHWARZ | agreed |  |  |
| R5-203271 | Clarification on the usage of auxiliary bands | ROHDE & SCHWARZ, Qualcomm Finland RFFE Oy | agreed |  |  |
| R5-203272 | Remove IE includeBeamMeasurements from 6.6.1.5 and 6.6.1.6 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203273 | Adding measurement gaps for OTDOA configuration | ROHDE & SCHWARZ | revised |  | R5-204489 |
| R5-203274 | Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap | ROHDE & SCHWARZ | revised |  | R5-204777 |
| R5-203275 | Editorial update IE ARFCN-ValueNR | Ericsson | agreed |  |  |
| R5-203276 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID | Ericsson | withdrawn |  |  |
| R5-203277 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID | Ericsson | agreed |  |  |
| R5-203278 | n26 Default CH BW in 38.508-1 | Dish Network | agreed |  |  |
| R5-203279 | n26 Implementation baseline capabilities in 38.508-2 | Dish Network | agreed |  |  |
| R5-203280 | n26 addition to group of bands in 38.533 | Dish Network | agreed |  |  |
| R5-203281 | n26 in common clauses in 38.521-1 | Dish Network | withdrawn |  |  |
| R5-203282 | n26 Rx requirements in 38.521-1 | Dish Network | revised |  | R5-204961 |
| R5-203283 | Update of clause5 into TS 38.521-1 R15 | China Unicom | revised |  | R5-204762 |
| R5-203284 | Update of R16 new bands and CBWs in 38.521-1 | China Unicom, AT&T, Dish Network, CMCC | revised |  | R5-204828 |
| R5-203285 | Update of R16 CADC combos in TS 38.521-1 | China Unicom | revised |  | R5-204808 |
| R5-203286 | Added definition of RSAP and RSARP in 36.509 | Keysight Technologies UK Ltd | revised |  | R5-204365 |
| R5-203287 | Correction PRB-Id for PUCCH secondHopPRB | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203288 | Added UE Phy layer capabilitity into 38.508-2 from 38.306 | Keysight Technologies UK Ltd | revised |  | R5-204853 |
| R5-203289 | Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities | Keysight Technologies UK Ltd | revised |  | R5-204902 |
| R5-203290 | Clarification of Interferer frequency selection in FR1 IBB test case 7.6.2 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203291 | Correction of K1 to achieve PUCCH Format 3 in FDD in EVM and in-band emission | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203292 | Clarification of Interferer frequency selection in FR2 IBB test case 7.6.2 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203293 | FR2 ACLR MBW correction according to RAN4 | Keysight Technologies UK Ltd | withdrawn |  |  |
| R5-203294 | Correction of MU definition for test case 6.5B.2.1.3 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203295 | definition of MU and TT for test case 6.3B.4.3 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203296 | definition of MU and TT for test case 6.5B.4.3 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203297 | Definition of MU and TT for test case 7.3B.2.4 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203298 | Activate Test Mode in NSA Demod Test Cases | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203299 | Corrected test description in non-DRX test case 6.5.1.2 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203300 | Correction of comment for monitoringSymbolsWithinSlot | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203301 | Correction of delta offset application for Cell 2 in test case 4.7.1.2.1 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203302 | Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133 | Keysight Technologies UK Ltd, Qualcomm Incorporated | revised |  | R5-204882 |
| R5-203303 | PUSCH allocation correction in test case 6.4.3.1 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203304 | Correction to the RRC Reconfiguration message for measurements | ROHDE & SCHWARZ | agreed |  |  |
| R5-203305 | Correction to the extreme conditions in TT analysis of 4.7.1.2.1 | ROHDE & SCHWARZ | revised |  | R5-204788 |
| R5-203306 | Update extreme conditions limits in TC 4.7.1.2.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203307 | Update extreme conditions limits in TC 6.7.1.2.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203308 | Update extreme conditions limits in TC 4.7.1.2.1 and TC 6.7.1.2.1 - Annex F | ROHDE & SCHWARZ | agreed |  |  |
| R5-203309 | Correction power offset for Band Group F | ROHDE & SCHWARZ | agreed |  |  |
| R5-203310 | Quality of the Quiet Zone measurement results for enhanced IFF | ROHDE & SCHWARZ | revised |  | R5-204737 |
| R5-203311 | Uncertainty assessment DL AWGN absolute power for enhanced IFF | ROHDE & SCHWARZ | revised |  | R5-204742 |
| R5-203312 | MTSU DL AWGN absolute power for RRM | ROHDE & SCHWARZ | noted |  |  |
| R5-203313 | CR to update the DL AWGN absolute power for RRM test cases | ROHDE & SCHWARZ | revised |  | R5-204887 |
| R5-203314 | CR to update the RRM FR2 MUs in Annex F | ROHDE & SCHWARZ | revised |  | R5-204885 |
| R5-203315 | Add information on the AoA change during test for RRM FR2 tests | ROHDE & SCHWARZ | revised |  | R5-204886 |
| R5-203316 | Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values | ROHDE & SCHWARZ | revised |  | R5-204785 |
| R5-203317 | Removing SearchSpaceId and ControlResourceSetId modification | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203318 | Test Procedure correction in test case 6.5.1.3 for definition of Point C | Keysight Technologies UK Ltd | revised |  | R5-204883 |
| R5-203319 | Unification of cell frequency for FR1-FR1 test cases | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203320 | Add IE BeamFailureRecoverySCellConfig | Ericsson | agreed |  |  |
| R5-203321 | FR2 RRM test cases: dB range in Spherical coverage | ANRITSU LTD | noted |  |  |
| R5-203322 | Test Tolerance review process for FR2 RRM Test cases | ANRITSU LTD | revised |  | R5-204848 |
| R5-203323 | Add Draft Test Tolerance analysis for FR2 Tx Timing Test cases | ANRITSU LTD | agreed |  |  |
| R5-203324 | Add Draft Test Tolerance analysis for FR2 Inter-freq Event-trig Test cases | ANRITSU LTD | agreed |  |  |
| R5-203325 | Add Draft Test Tolerance analysis for FR2 Intra-freq SS-RSRP Test case | ANRITSU LTD | agreed |  |  |
| R5-203326 | SR - Rel-16 IIOT after RAN5#88-e | CMCC | noted |  |  |
| R5-203327 | WP - Rel-16 IIOT after RAN5#88-e | CMCC | noted |  |  |
| R5-203328 | SR - NR_Rel-16_CA_DC after RAN5#88-e | CMCC | noted |  |  |
| R5-203329 | WP - NR_Rel-16_CA_DC after RAN5#88-e | CMCC | noted |  |  |
| R5-203330 | TP for TS 38.522 | CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm | revised |  | R5-204939 |
| R5-203331 | SR - ENDC_UE_PC2_TDD_TDD after RAN5#88-e | CMCC | noted |  |  |
| R5-203332 | WP - ENDC_UE_PC2_TDD_TDD after RAN5#88-e | CMCC | noted |  |  |
| R5-203333 | Revised WID ENDC_UE_PC2_TDD_TDD-UEConTest | CMCC | noted |  |  |
| R5-203334 | Correction of UE Category 1bis test case applicability | CMCC | revised |  | R5-204976 |
| R5-203335 | Addition of B34 into UE Category 1bis and update B41 UE Category 1bis | CMCC | agreed |  |  |
| R5-203336 | Addition of test cases for n28 with CBW of 30MHz | CMCC, CBN, Huawei, HiSilicon, Orange | revised |  | R5-204960 |
| R5-203337 | Addition of test frequencies for n28 with CBW of 30MHz | CMCC, CBN, Ericsson | revised |  | R5-204896 |
| R5-203338 | Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID | Ericsson | revised |  | R5-204507 |
| R5-203339 | Add IE CGI-InfoEUTRALogging | Ericsson | agreed |  |  |
| R5-203340 | Add IEs CGI-Info-Logging and CLI-RSSI-Range | Ericsson | agreed |  |  |
| R5-203341 | Add IEs CommonLocationInfo, CondReconfigId, CondReconfigToAddModList and ConditionalReconfiguration | Ericsson | agreed |  |  |
| R5-203342 | Add IEs ConfiguredGrantConfigIndex and ConfiguredGrantConfigIndexMAC | Ericsson | agreed |  |  |
| R5-203343 | Add IE DRX-ConfigSecondaryGroup | Ericsson | agreed |  |  |
| R5-203344 | Add IE HighSpeedConfig | Ericsson | agreed |  |  |
| R5-203345 | Add IE InvalidSymbolPattern | Ericsson | agreed |  |  |
| R5-203346 | Add IEs LBT-FailureRecoveryConfig and LocationInfo | Ericsson | agreed |  |  |
| R5-203347 | Add IE MeasIdleConfig | Ericsson | agreed |  |  |
| R5-203348 | Add IE MeasObjectCLI | Ericsson | agreed |  |  |
| R5-203349 | Add IE MeasObjectNR-SL | Ericsson | agreed |  |  |
| R5-203350 | Add IE MeasObjectUTRA-FDD | Ericsson | agreed |  |  |
| R5-203351 | Add IEs MeasResultIdleEUTRA and MeasResultIdleNR | Ericsson | agreed |  |  |
| R5-203352 | Add Es MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | withdrawn |  |  |
| R5-203353 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | withdrawn |  |  |
| R5-203354 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | revised |  | R5-204508 |
| R5-203355 | Add IEs MsgA-ConfigCommon and MsgA-PUSCH-Config | Ericsson | agreed |  |  |
| R5-203356 | Add IEs NeedForGapsConfigNR and NeedForGapsInfoNR | Ericsson | agreed |  |  |
| R5-203357 | Correction to Table 4.5.2.2-2-second SMC procedure for Selected EPS NAS security algorithms IE | Huawei, Hisilicon | agreed |  |  |
| R5-203358 | Correction to Table 4.6.1-17 RRCResume | Huawei, Hisilicon | revised |  | R5-204386 |
| R5-203359 | Correction to Table 4.6.3-141 ReportConfigInterRAT | Huawei, Hisilicon | agreed |  |  |
| R5-203360 | Correction to Table 4.6.3-142 ReportConfigNR | Huawei, Hisilicon | withdrawn |  |  |
| R5-203361 | Correction to Table 4.7.1-26 SECURITY MODE COMPLETE | Huawei, Hisilicon, Keysight | withdrawn |  |  |
| R5-203362 | Correction to Table 4.9.9.2.3-2 TRACKING AREA UPDATE REQUEST | Huawei, Hisilicon | withdrawn |  |  |
| R5-203363 | Correction to NR TC 6.1.1.1-PLMN selection in automatic mode | Huawei, Hisilicon | agreed |  |  |
| R5-203364 | Addition of NR TC 6.1.1.1a-PLMN selection in automatic mode Single Frequency operation | Huawei, Hisilicon | withdrawn |  |  |
| R5-203365 | Correction to NR TC 6.1.1.2-access technology combinations | Huawei, Hisilicon | revised |  | R5-204403 |
| R5-203366 | Addition of NR TC 6.1.1.2a-PLMN selection of Other PLMN in automatic mode Single Frequency operation | Huawei, Hisilicon | withdrawn |  |  |
| R5-203367 | Correction to NR TC 6.1.1.5-PLMN selection in Automatic mode User reselection | Huawei, Hisilicon | agreed |  |  |
| R5-203368 | Addition of NR TC 6.1.1.5a-PLMN selection in Automatic mode User reselection Single Frequency operation | Huawei, Hisilicon | withdrawn |  |  |
| R5-203369 | Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode | Huawei, Hisilicon | revised |  | R5-204404 |
| R5-203370 | Addition of NR TC 6.1.1.7a-PLMN selection of RPLMN or HPLMN in Automatic mode Single Frequency operation | Huawei, Hisilicon | withdrawn |  |  |
| R5-203371 | Correction to NR TC 6.1.2.19-Speed-dependent cell reselection | Huawei, Hisilicon, Keysight | revised |  | R5-204405 |
| R5-203372 | Correction to NR TC 6.1.2.21-Cell reselection | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203373 | Correction to NR TC 6.1.2.23-Cell Reselection MFBI | Huawei, Hisilicon | agreed |  |  |
| R5-203374 | Correction to NR TC 6.2.1.1-Selection of correct RAT for OPLMN | Huawei, Hisilicon | agreed |  |  |
| R5-203375 | Correction to NR TC 6.2.1.4-Inter-RAT PLMN Selection with Manual mode | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203376 | Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204406 |
| R5-203377 | Correction to NR TC 6.2.3.9-Inter-RAT Speed Dependent Cell Reselection | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203378 | Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1 | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204407 |
| R5-203379 | Correction to NR TC 6.3.1.2-SOR during registration with security check successful but no requested acknowledgement | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204408 |
| R5-203380 | Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode | Huawei, Hisilicon, Datang Linktester, ZTE | revised |  | R5-204543 |
| R5-203381 | Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204409 |
| R5-203382 | Correction to NR TC 6.4.1.1-PLMN Selection | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203383 | Correction to NR TC 7.1.1.1.1-Correct selection of RACH parameters | Huawei, Hisilicon | agreed |  |  |
| R5-203384 | Correction to NR TC 7.1.1.4.1.3 and 7.1.1.4.1.4-DL TBS param combination leading to ambiguity | Huawei, Hisilicon | withdrawn |  |  |
| R5-203385 | Correction to NR TC 7.1.1.4.2.4 and 7.1.1.4.2.5-UL TBS param combination leading to ambiguity | Huawei, Hisilicon | withdrawn |  |  |
| R5-203386 | Correction to NR TC 7.1.1.9.1-MAC Reset | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204418 |
| R5-203387 | Correction to NR TC 7.1.1.2.2-PDSCH Aggregation | Huawei, Hisilicon | revised |  | R5-204419 |
| R5-203388 | Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN | Huawei, Hisilicon | revised |  | R5-204424 |
| R5-203389 | Correction to NR TC 8.1.1.3.1-Redirection to another NR frequency | Huawei, Hisilicon | agreed |  |  |
| R5-203390 | Correction to NR TC 8.1.1.3.3-With priority information | Huawei, Hisilicon | revised |  | R5-204432 |
| R5-203391 | Correction to NR TC 8.1.1.4.1-RRC Resume Success | Huawei, Hisilicon | withdrawn |  |  |
| R5-203392 | Correction to NR TC 8.1.X on SINR related configuration | Huawei, Hisilicon | revised |  | R5-204437 |
| R5-203393 | Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq | Huawei, Hisilicon | revised |  | R5-204438 |
| R5-203394 | Correction to NR TC 8.1.3.1.15A-Intra NR measurements Blacklisting | Huawei, Hisilicon | agreed |  |  |
| R5-203395 | Correction to NR TC 8.1.4.1.7.X-Scell Release | Huawei, Hisilicon | revised |  | R5-204446 |
| R5-203396 | Correction to NR TC 8.1.5.7.1.X-RLC Failure MCG | Huawei, Hisilicon | agreed |  |  |
| R5-203397 | Correction to ENDC TC 8.2.2.1.1-SRB3 | Huawei, Hisilicon, Starpoint | agreed |  |  |
| R5-203398 | Addition of NRDC TC 8.2.2.1.2-SRB3 | Huawei, Hisilicon | agreed |  |  |
| R5-203399 | Addition of NRDC TC 8.2.2.3.2-Simultaneous SRB3 and Split SRB | Huawei, Hisilicon | withdrawn |  |  |
| R5-203400 | Correction to ENDC TC 8.2.2.6.1-PDCP version change | Huawei, Hisilicon, Starpoint | revised |  | R5-204439 |
| R5-203401 | Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements | Huawei, Hisilicon | revised |  | R5-204447 |
| R5-203402 | Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements | Huawei, Hisilicon | revised |  | R5-204448 |
| R5-203403 | Correction to ENDC TC 8.2.3.11.X-Measurement Gap | Huawei, Hisilicon | agreed |  |  |
| R5-203404 | Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting | Huawei, Hisilicon | revised |  | R5-204449 |
| R5-203405 | Correction to ENDC TC 8.2.6.1.1.X-RLC Failure SCG | Huawei, Hisilicon | agreed |  |  |
| R5-203406 | Addition of NRDC TC 8.2.6.1.2.1-RLC Failure SCG intra-band | Huawei, Hisilicon | agreed |  |  |
| R5-203407 | Addition of NRDC TC 8.2.6.1.2.2-RLC Failure SCG inter-band | Huawei, Hisilicon | agreed |  |  |
| R5-203408 | Addition of NRDC TC 8.2.6.1.2.3-RLC Failure SCG intra-band NC | Huawei, Hisilicon | agreed |  |  |
| R5-203409 | Correction to ENDC TC 8.2.6.2.1-Processing delay | Huawei, Hisilicon, Starpoint | agreed |  |  |
| R5-203410 | Correction to NR TC 9.1.1.3-EAP message transport abnormal | Huawei, Hisilicon | revised |  | R5-204457 |
| R5-203411 | Correction to NR TC 9.1.1.6-5G AKA abnormal | Huawei, Hisilicon | revised |  | R5-204458 |
| R5-203412 | Correction to NR TC 9.1.5.1.1-Initial registration with 5G-GUTI reallocation | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203413 | Correction to NR TC 9.1.5.1.8-Serving network not authorized | Huawei, HiSilicon, Anritsu, MediaTek Inc., ROHDE & SCHWARZ | agreed |  |  |
| R5-203414 | Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204460 |
| R5-203415 | Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers | Huawei, HiSilicon, Anritsu | revised |  | R5-204461 |
| R5-203416 | Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category | Huawei, Hisilicon | revised |  | R5-204468 |
| R5-203417 | Addition of applicability for NR TCs | Huawei, Hisilicon | revised |  | R5-204469 |
| R5-203418 | Correction to applicability of NR TCs | Huawei, Hisilicon | revised |  | R5-204470 |
| R5-203419 | Discussion for NR Mobility Enhancements Testing | Huawei, Hisilicon | noted |  |  |
| R5-203420 | SR-NR Mobility Enhancements-Status after RAN5#88-e | Huawei, Hisilicon | noted |  |  |
| R5-203421 | Discussion for NR V2X Testing | Huawei, Hisilicon | noted |  |  |
| R5-203422 | SR-NR V2X-Status after RAN5#88-e | Huawei, Hisilicon | noted |  |  |
| R5-203423 | Addition of IMS NR TC 9.4-MT Concatenated SMS | Huawei, Hisilicon | revised |  | R5-204477 |
| R5-203424 | Addition of IMS NR TC 9.5-MO SMS RP-ERROR | Huawei, Hisilicon | revised |  | R5-204478 |
| R5-203425 | Addition of IMS NR TC 10.1-emergency call with registration and Location | Huawei, Hisilicon | revised |  | R5-204479 |
| R5-203426 | Correction to IMS TCs-wait for UE IMS de-register | Huawei, Hisilicon | revised |  | R5-204530 |
| R5-203427 | Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register | Huawei, Hisilicon | revised |  | R5-204525 |
| R5-203428 | Correction to Idle Mode SoR TC 6.3.1.3 | ZTE Corporation | withdrawn |  |  |
| R5-203429 | Correction to Idle Mode SoR TC 6.3.1.7 | ZTE Corporation, Huawei, Hisilicon | revised |  | R5-204410 |
| R5-203430 | Adding check to REGISTER regarding nonce-count | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203431 | Addition of new RRM Test Cases in clause 7.5.5 | ZTE Corporation | revised |  | R5-204884 |
| R5-203432 | Correction to A.1.2 regarding WWW-Authenticate | ROHDE & SCHWARZ | agreed |  |  |
| R5-203433 | Extending default message for NOTIFY to cover de-registration scenarios | ROHDE & SCHWARZ | agreed |  |  |
| R5-203434 | Adding cross-references to TS 34.229-5 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203435 | Removing 5G content | ROHDE & SCHWARZ | agreed |  |  |
| R5-203436 | Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases | ROHDE & SCHWARZ | revised |  | R5-204476 |
| R5-203437 | Corrections to A.2 on IMS Registration | ROHDE & SCHWARZ | agreed |  |  |
| R5-203438 | Adding details for A.3 for IMS Emergency Registration | ROHDE & SCHWARZ | revised |  | R5-204480 |
| R5-203439 | New generic procedure for MT Call Release | ROHDE & SCHWARZ | agreed |  |  |
| R5-203440 | Adding references as needed | ROHDE & SCHWARZ | agreed |  |  |
| R5-203441 | Corrections to test cases 7.6 and 7.7 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203442 | Corrections to test case 6.1 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203443 | Corrections to test case 6.2 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203444 | Corrections to test case 6.3 | ROHDE & SCHWARZ, MCC TF160 | revised |  | R5-204481 |
| R5-203445 | Corrections to test case 6.4 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203446 | Add IEs NPN-Identity and NPN-IdentityInfoList | Ericsson | agreed |  |  |
| R5-203447 | Corrections to test case 6.5 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203448 | Corrections to test case 6.6 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203449 | Add IE PLMN-IdentityList2 | Ericsson | agreed |  |  |
| R5-203450 | Add IE PUCCH-ConfigurationList | Ericsson | agreed |  |  |
| R5-203451 | Add IE PUCCH-SpatialRelationInfo-Id | Ericsson | agreed |  |  |
| R5-203452 | Corrections to test case 6.7 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203453 | Corrections to test case 6.8 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203454 | Corrections to test case 6.9 | ROHDE & SCHWARZ, MCC TF160 | agreed |  |  |
| R5-203455 | Corrections to 4.5.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203456 | Updating usages of TS 34.229-1 to TS 34.229-5 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203457 | Fixing References | ROHDE & SCHWARZ | agreed |  |  |
| R5-203458 | Discussion paper on old unverified IMS test cases | ROHDE & SCHWARZ | noted |  |  |
| R5-203459 | Discussion paper on IR.92 update | ROHDE & SCHWARZ | noted |  |  |
| R5-203460 | Discussion paper on two consecutive invalid challenges | ROHDE & SCHWARZ | noted |  |  |
| R5-203461 | Corrections to MTSI MT Voice Call TC 7.6 | ZTE Corporation | agreed |  |  |
| R5-203462 | Corrections to Annex A.5.1 | ZTE Corporation | agreed |  |  |
| R5-203463 | Addition of PICs for CSI-RS measurement without associated SSB | Huawei, Hisilicon | agreed |  |  |
| R5-203464 | Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq | Huawei, Hisilicon | revised |  | R5-204440 |
| R5-203465 | New WID on UE Conformance Test Aspects – B1C Signal in A-BDS Positioning System Support for LTE and NR | CATT | revised |  | R5-204352 |
| R5-203466 | WP UE Conformance Test Aspects - UE Power Saving in NR | CATT | noted |  |  |
| R5-203467 | Add IE RACH-ConfigCommonTwoStepRA | Ericsson | agreed |  |  |
| R5-203468 | SR UE Conformance Test Aspects - UE Power Saving in NR | CATT | noted |  |  |
| R5-203469 | SR UE Conformance Test Aspects - UE Power Saving in NR | CATT | withdrawn |  |  |
| R5-203470 | Add IE RACH-ConfigGenericTwoStepRA | Ericsson | agreed |  |  |
| R5-203471 | Add IE ReferenceTimeInfo | Ericsson | agreed |  |  |
| R5-203472 | Add IE RepetitionSchemeConfig | Ericsson | agreed |  |  |
| R5-203473 | Addition of new test case to test Paging with DRX and WUS in enhanced coverage | Tech Mahindra Limited | revised |  | R5-204500 |
| R5-203474 | Addition of new test case to test Paging with eDRX and WUS in enhanced coverage | Tech Mahindra Limited | revised |  | R5-204501 |
| R5-203475 | Update of 5G-NR test cases applicability | Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility | revised |  | R5-204471 |
| R5-203476 | Add IE ReportConfigNR-SL | Ericsson | agreed |  |  |
| R5-203477 | Addition of new test case to test CE-level based access barring | Tech Mahindra Limited | revised |  | R5-204502 |
| R5-203478 | Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration | Huawei, Hisilicon | revised |  | R5-204411 |
| R5-203479 | Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode | Tech Mahindra Limited | revised |  | R5-204504 |
| R5-203480 | Addition of applicability for new test case to test CE-level based access barring | Tech Mahindra Limited | revised |  | R5-204505 |
| R5-203481 | Correction to NR TC 6.1.1.4-PLMN selection in shared network environment | Huawei, Hisilicon | agreed |  |  |
| R5-203482 | Addition of new test purpose to test case 8.1.3.1.23 | Tech Mahindra Limited | revised |  | R5-204441 |
| R5-203483 | Correction to include data path check after handover in test case 8.1.4.1.2 | Tech Mahindra Limited | revised |  | R5-204450 |
| R5-203484 | Corrections to generic procedures for MO and MT speech call establishment | ROHDE & SCHWARZ | revised |  | R5-204387 |
| R5-203485 | On ACS FR2 Measurement Uncertainty definition | Keysight Technologies UK Ltd | revised |  | R5-204743 |
| R5-203486 | Adjacent Channel Selectivity FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | revised |  | R5-204888 |
| R5-203487 | Adjacent Channel Selectivity FR2 MU updates in 38.521-2 | Keysight Technologies UK Ltd | withdrawn |  |  |
| R5-203488 | Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3 | Keysight Technologies UK Ltd | revised |  | R5-204869 |
| R5-203489 | On IBB FR2 Measurement Uncertainty definition | Keysight Technologies UK Ltd | revised |  | R5-204744 |
| R5-203490 | In-band Blocking FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | revised |  | R5-204889 |
| R5-203491 | In-band Blocking FR2 MU updates in 38.521-2 | Keysight Technologies UK Ltd | withdrawn |  |  |
| R5-203492 | In-band Blocking FR2 MU updates in 38.521-3 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203493 | Updates to EMM test cases to handle IMS Re-registration | Keysight Technologies UK | not pursued |  |  |
| R5-203494 | Update to ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST message | Keysight Technologies UK | agreed |  |  |
| R5-203495 | Correction to USIM content for eCall over IMS test cases | Keysight Technologies UK | agreed |  |  |
| R5-203496 | Correction to postamble procedures to handle multi-PDN EN-DC devices | Keysight Technologies UK, Samsung | withdrawn |  |  |
| R5-203497 | Correction to USIM configurations 7 and 13 | Keysight Technologies UK | revised |  | R5-204388 |
| R5-203498 | Correction to switch off / power off procedures for IMS | Keysight Technologies UK Ltd, Qualcomm Incorporated | revised |  | R5-204389 |
| R5-203499 | Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Keysight Technologies UK, Huawei/HiSilicon | revised |  | R5-204384 |
| R5-203500 | Update to Table 4.6.3-74: MeasObjectEUTRA | Keysight Technologies UK | agreed |  |  |
| R5-203501 | Correction to 5G NR Idle mode Speed-dependent Cell reselection test case 6.1.2.19 | Keysight Technologies UK | withdrawn |  |  |
| R5-203502 | Correction to 5G NR Idle mode test case 6.4.2.2 | Keysight Technologies UK | agreed |  |  |
| R5-203503 | Correction to NR CA RRC test cases 8.1.3.1.18.x | Keysight Technologies UK | agreed |  |  |
| R5-203504 | Correction to NR RRC test cases 8.1.3.2.3 and 8.1.3.2.4 | Keysight Technologies UK | agreed |  |  |
| R5-203505 | Correction to 5GMM test case 9.1.5.1.13 | Keysight Technologies UK | agreed |  |  |
| R5-203506 | Add IE RSSI-Range | Ericsson | agreed |  |  |
| R5-203507 | Add IEs SemiStaticChannelAccessConfig and Sensor-LocationInfo | Ericsson | agreed |  |  |
| R5-203508 | Add IE SI-RequestConfig | Ericsson | agreed |  |  |
| R5-203509 | Add IEs SPS-ConfigIndex, SPS-PUCCH-AN and SPS-PUCCH-AN-List | Ericsson | agreed |  |  |
| R5-203510 | Add IE SRS-RSRP-Range | Ericsson | agreed |  |  |
| R5-203511 | Correction of WLAN Assistance Data Element referenced clause | PCTEST Engineering Laboratory, LLC | agreed |  |  |
| R5-203512 | Addition of OTDOA information for pre-test conditions for test 9.3.3.1B | PCTEST Engineering Laboratory, LLC | revised |  | R5-204532 |
| R5-203513 | Correction to NR MAC test case 7.1.1.5.2 | Keysight Technologies UK, Starpoint | revised |  | R5-204420 |
| R5-203514 | Editorial correction to 3DL CA test cases | TTA | revised |  | R5-204844 |
| R5-203515 | Editorial correction of test case 6.5B.3.3.1 | TTA | agreed |  |  |
| R5-203516 | Update of test procedure for Minimum output power for CA in FR2 | TTA | withdrawn |  |  |
| R5-203517 | Update of test procedure for Error vector magnitude for CA in FR2 | TTA | withdrawn |  |  |
| R5-203518 | Introduction of a new test case for voice fallback indication under EPS Fallback with handover | CATT, TDIA | revised |  | R5-204516 |
| R5-203519 | Introduction of a new test case for voice fallback indication under EPS Fallback with redirection | CATT, TDIA | revised |  | R5-204517 |
| R5-203520 | Addition of test applicabilities of test cases for voice fallback indication | CATT, TDIA | revised |  | R5-204519 |
| R5-203521 | Correction to NR RRC test case 8.1.3.1.20 | Starpoint, TDIA | revised |  | R5-204442 |
| R5-203522 | Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC | China telecom, Datang linktester | revised |  | R5-204513 |
| R5-203523 | Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16 | China Telecom | revised |  | R5-204509 |
| R5-203524 | Corrections to NR MAC Test Case 7.1.1.5.4 | Starpoint, TDIA | agreed |  |  |
| R5-203525 | Update of WF on Band n259 | DOCOMO Communications Lab. | revised |  | R5-204851 |
| R5-203526 | Update Test tolerance of Band n259 | DOCOMO Communications Lab. | noted |  |  |
| R5-203527 | Editorial correction of Tx spurious emissions for FR1 EN-DC | DOCOMO Communications Lab. | withdrawn |  | - |
| R5-203528 | draft TS 36.579-6 v1.1.0 | NIST, Samsung | reserved |  |  |
| R5-203529 | draft TS 36.579-7 v1.1.0 | NIST, Samsung | reserved |  |  |
| R5-203530 | Update to 7.5A.2 ACS for 3DL CA | Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH | revised |  | R5-204897 |
| R5-203531 | MCC TF160 Status Report | MCC TF160 | revised |  | R5-204350 |
| R5-203532 | RAN5 PRD12 version 6.4 | MCC TF160 | withdrawn |  |  |
| R5-203533 | Update to PDSCH-ServingCellConfig | MCC TF160, Keysight Technologies UK | agreed |  |  |
| R5-203534 | Updates to CellGroupConfig and RNTI-Value for NR-DC | MCC TF160 | agreed |  |  |
| R5-203535 | Splitting and updates to NR RLC test case 7.1.2.3.5 | MCC TF160 | agreed |  |  |
| R5-203536 | Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4 | MCC TF160 | revised |  | R5-204425 |
| R5-203537 | Correction to NR test case 8.1.3.1.13 | MCC TF160 | withdrawn |  |  |
| R5-203538 | Correction to NR test case 8.1.3.1.14A | MCC TF160 | withdrawn |  |  |
| R5-203539 | Correction to NR test case 8.1.3.1.15A | MCC TF160 | agreed |  |  |
| R5-203540 | Editorial correction to EN-DC test case 8.2.3.5.1 | MCC TF160 | agreed |  |  |
| R5-203541 | Correction to EN-DC test cases 8.2.3.9.1 and 8.2.3.10.1 | MCC TF160 | withdrawn |  |  |
| R5-203542 | Splitting and updates to applicability of NR RLC test case 7.1.2.3.5 | MCC TF160 | agreed |  |  |
| R5-203543 | 5G Test Models updates | MCC TF160, Keysight, Samsung | revised |  | R5-204475 |
| R5-203544 | IMS over NR/5GC: Misc updates | MCC TF160, ROHDE & SCHWARZ | agreed |  |  |
| R5-203545 | Correction to SC-PTM test case 21.2.1 | MCC TF160 | agreed |  |  |
| R5-203546 | Routine maintenance for TS 36.523-3 | MCC TF160, Bureau Veritas | agreed |  |  |
| R5-203547 | Corrections of further XCAP test cases regarding rule elements | MCC TF160 | revised |  | R5-204531 |
| R5-203548 | New MCPTT Common Procedures for CT/CO session establishment | MCC TF160, UPV/EHU, Nemergent Solutions | revised |  | R5-204533 |
| R5-203549 | Updates to MCX generic test procedures and default message contents | MCC TF160, UPV/EHU, Nemergent Solutions | revised |  | R5-204534 |
| R5-203550 | Update to MCPTT Test Case 6.1.1.3 | MCC TF160 | revised |  | R5-204536 |
| R5-203551 | Update to MCPTT Test Case 6.1.1.4 | MCC TF160 | revised |  | R5-204537 |
| R5-203552 | Update to MCPTT Test Case 6.1.1.7 | MCC TF160 | revised |  | R5-204538 |
| R5-203553 | Correction to MCPTT Test Case 6.1.1.8 | MCC TF160 | revised |  | R5-204539 |
| R5-203554 | Routine maintenance for TS 36.579-5 | MCC TF160, UPV/EHU, Nemergent Solutions | agreed |  |  |
| R5-203555 | MCX message content issues | MCC TF160, UPV/EHU, Nemergent Solutions | noted |  |  |
| R5-203556 | Add IE SSB-PositionQCL-Relation | Ericsson | revised |  | R5-204510 |
| R5-203557 | Add IEs UL-DelayValueConfig and UplinkCancellation | Ericsson | agreed |  |  |
| R5-203558 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | revised |  | R5-204722 |
| R5-203559 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | revised |  | R5-204725 |
| R5-203560 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | revised |  | R5-204723 |
| R5-203561 | Introduction of new TC 7.6.1A.9 In-band blocking for 6DL CA | Tejet , SRTC | agreed |  |  |
| R5-203562 | Introduction of new TC 7.6.2A.9 Out-of-band blocking for 6DL CA | Tejet , SRTC | agreed |  |  |
| R5-203563 | Introduction of new TC 7.6.3A.9 Narrow band blocking for 6DL CA | Tejet , SRTC | agreed |  |  |
| R5-203564 | Introduction of new TC 7.7A.9 Spurious response for 6DL CA | Tejet , SRTC | agreed |  |  |
| R5-203565 | Correction to NR TC 6.2.2.1-N2L cell reselection | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204412 |
| R5-203566 | Correction to NR TC 6.2.2.2-L2N cell reselection | Huawei, Hisilicon, Datang Linktester | revised |  | R5-204413 |
| R5-203567 | Correction to NR TC 7.1.1.1.2-Random access procedure for Preamble selected by MAC itself | Huawei, Hisilicon, Datang Linktester | agreed |  |  |
| R5-203568 | NR V2X WP after RAN5 88-e | Huawei, Hisilicon | noted |  |  |
| R5-203569 | NR Mobile Enhancement WP after RAN5 88-e | Huawei, Hisilicon | noted |  |  |
| R5-203570 | Update of Annex F.1.3 and 3.3 for 6DL blocking and spurious response TCs | Tejet , SRTC | agreed |  |  |
| R5-203571 | Correction to Inter-RAT HO test case 8.1.4.2.2 | China Telecommunications | revised |  | R5-204451 |
| R5-203572 | Corrected test config for NS_24 in additional spurious emission test 6.5.3.3 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-203573 | Addition of applicability for newly introduced 6DL TCs | Tejet , SRTC | agreed |  |  |
| R5-203574 | Correction of description of NGEN-DC in table 4.5.1-1 | Tejet | revised |  | R5-204390 |
| R5-203575 | Add chapter Positioning System information blocks | Ericsson | agreed |  |  |
| R5-203576 | Correction to NR5GC test case 8.1.3.1.11 | Starpoint, Huawei, HiSilicon,TDIA | revised |  | R5-204443 |
| R5-203577 | Add IEs SIB10, SIB11, SIB12, SIB13 and SIB14 | Ericsson | agreed |  |  |
| R5-203578 | Correction to NR5GC test case 8.1.3.1.12 | Starpoint, Huawei, HiSilicon,TDIA | revised |  | R5-204444 |
| R5-203579 | MCPTT call establishment procedures | MCC TF160 | noted |  |  |
| R5-203580 | Beam correspondence - SRS configuration corrections in annex K.1.1 | Keysight Technologies UK Ltd | revised |  | R5-204865 |
| R5-203581 | Beam correspondence - SRS configuration corrections in section 6.6.1 | Keysight Technologies UK Ltd | revised |  | R5-204857 |
| R5-203582 | Add messages DedicatedSIBRequest, DLDedicatedMessageSegment, DLInformationTransferMRDC and IABOtherInformation | Ericsson | agreed |  |  |
| R5-203583 | Updates to TC execution guidance | MCC TF160 | agreed |  |  |
| R5-203584 | Addition of NR-DC RRC test case 8.2.2.8.2 | ANRITSU LTD | revised |  | R5-204445 |
| R5-203585 | Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR | MediaTek Inc., Keysight Technologies | revised |  | R5-204391 |
| R5-203586 | Update of TC 9.2.1.1.28b | NTT DOCOMO INC. | revised |  | R5-204522 |
| R5-203587 | Correction to test procedure of Table 4.9.9.2.2-1 | MediaTek Inc., Keysight Technologies | withdrawn |  | - |
| R5-203588 | Correction to NR inter-band CA configurations in FR1 | MediaTek Inc. | revised |  | R5-204378 |
| R5-203589 | Correction to NR RRC TC 8.1.5.1.1 | MediaTek Inc., Keysight Technologies | revised |  | R5-204456 |
| R5-203590 | Correction to the power level of Idle mode test cases | MediaTek Inc. | revised |  | R5-204414 |
| R5-203591 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | revised |  | R5-204379 |
| R5-203592 | Correction to Inter-RAT HO test case 8.1.4.2.1 | China Telecommunications | revised |  | R5-204452 |
| R5-203593 | Correction to Idle mode test case 6.1.2.9 | MediaTek Inc. | revised |  | R5-204380 |
| R5-203594 | Correction to NR TC 6.3.1.8-SOR after registration with Automatic PLMN selection mode | Huawei, Hisilicon | withdrawn |  |  |
| R5-203595 | Modification and editorial changes to NB-IoT TC 22.4.26 | NTT DOCOMO INC. | revised |  | R5-204526 |
| R5-203596 | Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs | NTT DOCOMO INC. | revised |  | R5-204426 |
| R5-203597 | Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath | NTT DOCOMO INC. | revised |  | R5-204427 |
| R5-203598 | Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC | NTT DOCOMO INC. | revised |  | R5-204428 |
| R5-203599 | Update applicability of Inter-RAT handover from NR to EN-DC test case | China Telecom,Datang linktester | revised |  | R5-204520 |
| R5-203600 | Introduction of TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell | LG Electronics | agreed |  |  |
| R5-203601 | Introduction of TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell | LG Electronics | agreed |  |  |
| R5-203602 | Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell | LG Electronics | agreed |  |  |
| R5-203603 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | revised |  | R5-204433 |
| R5-203604 | Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell | LG Electronics | agreed |  |  |
| R5-203605 | Update the related RRC messages to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | revised |  | R5-204521 |
| R5-203606 | Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for FDD PCell | LG Electronics | agreed |  |  |
| R5-203607 | Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for TDD PCell | LG Electronics | agreed |  |  |
| R5-203608 | Update to TDD FDD 7 DL CA Single Antenna Port Performance for FDD PCell | LG Electronics | agreed |  |  |
| R5-203609 | Update to TDD FDD 7 DL CA Single Antenna Port Performance for TDD PCell | LG Electronics | agreed |  |  |
| R5-203610 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | withdrawn |  |  |
| R5-203611 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | revised |  | R5-204514 |
| R5-203612 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | revised |  | R5-204472 |
| R5-203613 | Discussion paper on tracking of 5GS protocol test cases Rel-16 and beyond | Ericsson | revised |  | R5-204366 |
| R5-203614 | GCF 3GPP TCL after GCF CAG#63 | Ericsson | noted |  |  |
| R5-203615 | RAN5#88-e summary of changes to RAN5 test cases with potential impact on GCF and PTCRB | Ericsson, Samsung | reserved |  |  |
| R5-203616 | 3GPP RAN5 CA status list (pre-RAN5#88-e meeting) | Ericsson | noted |  |  |
| R5-203617 | 3GPP RAN5 CA status list (post-RAN5#88-e meeting) | Ericsson | noted |  |  |
| R5-203618 | WP UE Conformance Test Aspects - Rel-14 LTE CA configurations | Ericsson | noted |  |  |
| R5-203619 | SR UE Conformance Test Aspects - Rel-14 LTE CA configurations | Ericsson | noted |  |  |
| R5-203620 | WP UE Conformance Test Aspects - Rel-15 LTE CA configurations | Ericsson | noted |  |  |
| R5-203621 | SR UE Conformance Test Aspects - Rel-15 LTE CA configurations | Ericsson | noted |  |  |
| R5-203622 | WP UE Conformance Test Aspects - Rel-16 LTE CA configurations | Ericsson | noted |  |  |
| R5-203623 | SR UE Conformance Test Aspects - Rel-16 LTE CA configurations | Ericsson | noted |  |  |
| R5-203624 | WP UE Conformance Test Aspects - 5G system with NR and LTE | Ericsson | noted |  |  |
| R5-203625 | SR UE Conformance Test Aspects - 5G system with NR and LTE | Ericsson | noted |  |  |
| R5-203626 | 5GS progress report RAN5#88-e | Ericsson | noted |  |  |
| R5-203627 | Update of RAN5 5G NR phases and target update RAN5#88-e | Ericsson | reserved |  |  |
| R5-203628 | WP UE Conformance Test Aspects - New Rel-16 NR bands and extension of existing NR bands | Ericsson | noted |  |  |
| R5-203629 | SR UE Conformance Test Aspects - New Rel-16 NR bands and extension of existing NR bands | Ericsson | noted |  |  |
| R5-203630 | Revised WID - New Rel-16 NR bands and extension of existing NR bands | Ericsson | withdrawn |  |  |
| R5-203631 | Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | revised |  | R5-204751 |
| R5-203632 | Introduction of UE capabilities for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | agreed |  |  |
| R5-203633 | Introduction of additonal Rel-15 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3 | Ericsson, Telefonica | withdrawn |  |  |
| R5-203634 | Introduction of test frequencies for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | agreed |  |  |
| R5-203635 | Introduction of UE capabilities for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | agreed |  |  |
| R5-203636 | Editorial correction to spurious emission test case 6.5B.3.3.2 | Ericsson | revised |  | R5-204810 |
| R5-203637 | Introduction of additional Rel-16 EN-DC inter-band configurations to EN-DC MOP test case 6.2B.1.3 | Ericsson, Telefonica | agreed |  |  |
| R5-203638 | Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | revised |  | R5-204811 |
| R5-203639 | Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | revised |  | R5-204812 |
| R5-203640 | Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | revised |  | R5-204813 |
| R5-203641 | Introduction of additonal Rel-16 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3 | Ericsson, Telefonica | withdrawn |  |  |
| R5-203642 | Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n1A | Ericsson, Telefonica | agreed |  |  |
| R5-203643 | Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n78A | Ericsson, Telefonica | agreed |  |  |
| R5-203644 | Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | revised |  | R5-204515 |
| R5-203645 | Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1 | MediaTek Inc. | revised |  | R5-204381 |
| R5-203646 | WP UE Conformance Test Aspects- Even further mobility enhancement for E-UTRAN after RAN5#88-e | China Telecom Corporation Ltd. | noted |  |  |
| R5-203647 | SR UE Conformance Test Aspects- Even further mobility enhancement for E-UTRAN after RAN5#88-e | China Telecom Corporation Ltd. | noted |  |  |
| R5-203648 | Editorial updates to NR5G Idle Mode TC 6.1.2.11 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203649 | Corrections to NR5G BWP TC 7.1.1.8.1 | Qualcomm CDMA Technologies, MCC TF160, Anritsu Ltd, Rohde & Schwarz | agreed |  |  |
| R5-203650 | Corrections to NR5G RRC NR-DC TC 8.2.2.4.2 and 8.2.2.5.2 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203651 | Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | revised |  | R5-204488 |
| R5-203652 | Corrections to Default contents of RRCResume message | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | withdrawn |  |  |
| R5-203653 | Corrections to Generic procedure 4.9.9 | Qualcomm CDMA Technologies | withdrawn |  |  |
| R5-203654 | Corrections to NR5G Idle Mode TC 6.4.2.1 | Qualcomm CDMA Technologies | revised |  | R5-204415 |
| R5-203655 | Corrections to NR5G MAC TC 7.1.1.2.4 | Qualcomm CDMA Technologies | revised |  | R5-204421 |
| R5-203656 | Corrections to NR5G MAC DRX TC 7.1.1.5.3 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | agreed |  |  |
| R5-203657 | Corrections to NR5G RRC TC 8.1.3.1.16 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | agreed |  |  |
| R5-203658 | Void NR5G NAS TC 9.1.5.2.6 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203659 | Corrections to NR5G MAC TC 7.1.1.2.1 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | agreed |  |  |
| R5-203660 | Corrections to NR5G MAC TC 7.1.1.1.2 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | revised |  | R5-204422 |
| R5-203661 | Corrections to NR5G Idle Mode TC 6.1.2.13 | Qualcomm CDMA Technologies | revised |  | R5-204416 |
| R5-203662 | Removal of USIM profile #16 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203663 | Corrections to NR5G RLC TC 7.1.2.3.11 | Qualcomm CDMA Technologies | revised |  | R5-204512 |
| R5-203664 | Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1 | Qualcomm CDMA Technologies | revised |  | R5-204453 |
| R5-203665 | Corrections to NR5G RRC CA TCs to add Data Path verification | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203666 | Corrections to ENDC RRC CA TCs to add Data Path verification | Qualcomm CDMA Technologies | agreed |  |  |
| R5-203667 | Correction to Multilayer TC 11.3.8 | MediaTek Inc. | withdrawn |  |  |
| R5-203668 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | revised |  | R5-204937 |
| R5-203669 | FR2 Demod MU due to finite test time | Qualcomm Korea | revised |  | R5-204738 |
| R5-203670 | message contents correction for TC 5.2.3.1.2_1 | Qualcomm Korea | agreed |  |  |
| R5-203671 | Update of PDSCH-to-HARQ_feedback timing indicator (k1) value | Qualcomm Korea | agreed |  |  |
| R5-203672 | Jumbo CR for update to Demod message contents | Qualcomm Korea | revised |  | R5-204852 |
| R5-203673 | Update to FR2 PDSCH test case | Qualcomm Korea | revised |  | R5-204936 |
| R5-203674 | Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01 | Huawei, Hisilicon | revised |  | R5-204711 |
| R5-203675 | Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | revised |  | R5-204789 |
| R5-203676 | Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | revised |  | R5-204790 |
| R5-203677 | Cleaning up of Tx inter-band CA test cases | Huawei, Hisilicon | revised |  | R5-204760 |
| R5-203678 | Adding MU and TTs for Inter-band UL CA test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203679 | Updating message content in SUL test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203680 | Updating indicator for SUL FR1 test cases | Huawei, Hisilicon | revised |  | R5-204708 |
| R5-203681 | Editorial correction typos in annex C.2.3.2 | Huawei, Hisilicon | agreed |  |  |
| R5-203682 | Updating test case 6.5A.2.4.1-NR ACLR for CA | Huawei, Hisilicon | agreed |  |  |
| R5-203683 | Update frequencyDomainResources and nrofcandidates | Huawei, Hisilicon | revised |  | R5-204709 |
| R5-203684 | Adding FR1 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | revised |  | R5-204712 |
| R5-203685 | Adding FR2 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | revised |  | R5-204718 |
| R5-203686 | Discussion about proposals in LS R4-2005205 | Huawei, Hisilicon | revised |  | R5-204721 |
| R5-203687 | Updating channel configurations for Intra-band UL contiguous CA | Huawei, Hisilicon | agreed |  |  |
| R5-203688 | Updating intra-band CA UL and DL configurations | Huawei, Hisilicon | agreed |  |  |
| R5-203689 | Adding MU and TTs for Intra-band UL CA test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203690 | Introduce general requirement for UL CA test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203691 | Updating NR test case 6.2A.1- MOP for CA | Huawei, Hisilicon | agreed |  |  |
| R5-203692 | Update of NR test case 6.2A.2-MPR for CA | Huawei, Hisilicon | revised |  | R5-204984 |
| R5-203693 | Updating TP analysis for 6.2A.2-MPR for CA | Huawei, Hisilicon | revised |  | R5-204727 |
| R5-203694 | Updating of NR test case 6.2A.4-Configured output power for CA | Huawei, Hisilicon | revised |  | R5-204974 |
| R5-203695 | Updating TP analysis for 6.2A.4-Configured output power for CA | Huawei, Hisilicon | revised |  | R5-204838 |
| R5-203696 | Addition of general clause 7.1A | Huawei, Hisilicon | agreed |  |  |
| R5-203697 | Updating REFSENS minimum requirements for Intra-band non-contiguous CA | Huawei, Hisilicon | agreed |  |  |
| R5-203698 | Update of 7.4A.2-Maximum input level for 3DL CA | Huawei, Hisilicon | agreed |  |  |
| R5-203699 | Adding band n48 for Blocking characteristics testing | Huawei, Hisilicon, Ericsson | revised |  | R5-204837 |
| R5-203700 | Update of test case 7.6A.2-Inband blocking for CA | Huawei, Hisilicon | agreed |  |  |
| R5-203701 | Update of test case 7.6A.2.2 Inband blocking for 3DL CA | Huawei, Hisilicon | agreed |  |  |
| R5-203702 | Correction to 5GC TC 9.1.5.2.9 | MediaTek Inc. | revised |  | R5-204462 |
| R5-203703 | New WID on UE Conformance Test Aspects for SON and MDT support for NR | China Mobile Com. Corporation | revised |  | R5-204353 |
| R5-203704 | Correction to Table 4.6.3-87 NZP-CSI-RS-ResourceSet | Huawei, Hisilicon | agreed |  |  |
| R5-203705 | Correction to NR test case 7.1.2.2.5 | ZTE | withdrawn |  |  |
| R5-203706 | Correction to NR test case 7.1.2.3.1 | ZTE | agreed |  |  |
| R5-203707 | Correction to NR test case 7.1.3.5.5 | ZTE | revised |  | R5-204429 |
| R5-203708 | Correction to NR test case 7.1.4.2 | ZTE | withdrawn |  |  |
| R5-203709 | Correction to NR test case 8.1.3.1.5 | ZTE | agreed |  |  |
| R5-203710 | Correction to NR test case 8.1.3.1.8 | ZTE | agreed |  |  |
| R5-203711 | Correction to NR test case 8.1.3.1.13 | ZTE | withdrawn |  |  |
| R5-203712 | Correction to NR test case 8.1.4.16 | ZTE, MCC TF160 | revised |  | R5-204360 |
| R5-203713 | Addition of new IMS 5GS test case 9.1 | ZTE | revised |  | R5-204482 |
| R5-203714 | Addition of new IMS 5GS test case 9.2 | ZTE | revised |  | R5-204483 |
| R5-203715 | Addition of Generic Test Procedure for IMS MO SMS in 5GC | ZTE | revised |  | R5-204392 |
| R5-203716 | Addition of Generic Test Procedure for IMS MT SMS in 5GC | ZTE | revised |  | R5-204393 |
| R5-203717 | Correction to TC 5.2.3.1.1_1 4Rx FDD FR1 PDSCH mapping Type A performance | LG Electronics | agreed |  |  |
| R5-203718 | Correction to test configuration for Carrier leakage for CA | LG Electronics | revised |  | R5-204713 |
| R5-203719 | Add messages LoggedMeasurementConfiguration, MCGFailureInformation and SidelinkUEInformationNR | Ericsson | agreed |  |  |
| R5-203720 | Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA | LG Electronics | revised |  | R5-204714 |
| R5-203721 | Introduce of new TC 6.3A.4.1 | Guangdong OPPO Mobile Telecom. | revised |  | R5-204832 |
| R5-203722 | Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA | LG Electronics | revised |  | R5-204715 |
| R5-203723 | Introduce of new TC 6.3A.4.2 | Guangdong OPPO Mobile Telecom. | revised |  | R5-204833 |
| R5-203724 | Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA | LG Electronics | revised |  | R5-204716 |
| R5-203725 | Add messages UEInformationRequest, UEInformationResponse, ULDedicatedMessageSegment and ULInformationTransferIRAT | Ericsson | agreed |  |  |
| R5-203726 | Introduce of new TC 6.3A.4.3 | Guangdong OPPO Mobile Telecom. | revised |  | R5-204834 |
| R5-203727 | Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA | LG Electronics | revised |  | R5-204717 |
| R5-203728 | Correction to NR test case 8.1.3.1.16 | ZTE | agreed |  |  |
| R5-203729 | Update IE RACH-ConfigGeneric | Ericsson | agreed |  |  |
| R5-203730 | Scheduling Request Resource config for RRM test cases | ROHDE & SCHWARZ | agreed |  |  |
| R5-203731 | OSI scheduling config for RRM test cases | ROHDE & SCHWARZ | agreed |  |  |
| R5-203732 | Set ss-sinr request to false for EN-DC RRM measurement accuracy tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-203733 | Set ss-sinr request to false for NR SA RRM measurement accuracy tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-203734 | Add intra-band contiguous CA to 6.3A.1 | Guangdong OPPO Mobile Telecom. | revised |  | R5-204835 |
| R5-203735 | Add intra-band contiguous CA to 6.3A.2 | Guangdong OPPO Mobile Telecom. | agreed |  |  |
| R5-203736 | Add intra-band contiguous CA to 6.3A.3 | Guangdong OPPO Mobile Telecom. | revised |  | R5-204836 |
| R5-203737 | Correction to 5GC TC 9.1.3.1 | MediaTek Inc. | revised |  | R5-204459 |
| R5-203738 | Cleanup in test case 7.3EC, Reference sensitivity level for UE category M2 | Ericsson | agreed |  |  |
| R5-203739 | Corrections to 5GS Non-3GPP Access TC 9.2.1.1 | ZTE Corporation | agreed |  |  |
| R5-203740 | Corrections to 5GS Non-3GPP Access TC 9.2.5.1.4 | ZTE Corporation | agreed |  |  |
| R5-203741 | Corrections to 5GS Non-3GPP Access TC 9.2.7.1 | ZTE Corporation | agreed |  |  |
| R5-203742 | Corrections to 5GS Non-3GPP Access TC 9.2.7.2 | ZTE Corporation | agreed |  |  |
| R5-203743 | Update IE RLC-BearerConfig | Ericsson | revised |  | R5-204394 |
| R5-203744 | Editorial correcting of format for table headings | Ericsson | agreed |  |  |
| R5-203745 | Correction to 5G NR Idle mode test case 6.4.3.1 | Keysight Technologies UK | agreed |  |  |
| R5-203746 | Correction to 5G NR Idle mode inter-RAT test cases | Keysight Technologies UK | revised |  | R5-204417 |
| R5-203747 | Correction to NR RRC IRAT test case 8.1.1.3.4 | Keysight Technologies UK | revised |  | R5-204434 |
| R5-203748 | Change of RB allocation start for test case 6.3.4.3 | Ericsson, Keysight | agreed |  |  |
| R5-203749 | Update to test case NR5GC 7.1.3.5.3 (NR-DC) | ROHDE & SCHWARZ | revised |  | R5-204430 |
| R5-203750 | Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2 | ROHDE & SCHWARZ, ZTE | revised |  | R5-204431 |
| R5-203751 | Editorial correction to references to EN-DC configurations | Ericsson | agreed |  |  |
| R5-203752 | Correction to Multilayer TC 11.1.2 and 11.1.5 | MediaTek Inc. | revised |  | R5-204465 |
| R5-203753 | Update test procedure to 6.5B.3.3.1 | Guangdong OPPO Mobile Telecom. | agreed |  |  |
| R5-203754 | Correct UE output power configuration to some UL MIMO cases | Guangdong OPPO Mobile Telecom, Orange | revised |  | R5-204854 |
| R5-203755 | Update IE SchedulingRequestResourceConfig | Ericsson | agreed |  |  |
| R5-203756 | Removing unnecessary IE rbg-Size from message exceptions | Ericsson | agreed |  |  |
| R5-203757 | Update of PDSCH RMC in Annex A.1.1 | MediaTek Inc. | revised |  | R5-204730 |
| R5-203758 | SR of Enhancing LTE CA Utilization WI for RAN5_88e | Nokia, Nokia Shanghai Bell | reserved |  |  |
| R5-203759 | TS 36.523-1 Status before RAN5#88-e | Samsung (Rapporteur) | noted |  |  |
| R5-203760 | TS 36.523-1 Status after RAN5#88-e | Samsung (Rapporteur) | reserved |  |  |
| R5-203761 | PRD-17 on Guidance to Work Item Codes, version 3.21 (post RAN#89-e version) | Samsung (Rapporteur) | reserved |  |  |
| R5-203762 | WP of Enhancing LTE CA Utilization for RAN5_88e | Nokia, Nokia Shanghai Bell | reserved |  |  |
| R5-203763 | Editorial correction of referenced clause (6.2.3) in test case 6.2B.2.1.2 | Ericsson | agreed |  |  |
| R5-203764 | Adding default value for IE rbg-Size for demodulation and CSI reporting tests | Ericsson | revised |  | R5-204899 |
| R5-203765 | Core spec alignment for measurement BW in 6.5.2.3, ACLR | Ericsson | withdrawn |  |  |
| R5-203766 | Updates to test case 6.3.4.3, relative power tolerance | Ericsson | revised |  | R5-204914 |
| R5-203767 | Addition of test frequencies for new Rel-16 CBW for NR band n77 | Ericsson | agreed |  |  |
| R5-203768 | Addition of test frequencies for new Rel-16 CBW for NR band n78 | Ericsson | agreed |  |  |
| R5-203769 | Introduction of test frequencies for Rel-16 NR band n30 | Ericsson, AT&T | agreed |  |  |
| R5-203770 | Introduction of test frequencies for Rel-19 NR band n259 | Ericsson | withdrawn |  | - |
| R5-203771 | FR2 Measurement Uncertainty (MU) / Test Tolerances (TT) Target Completion Update | AT&T | noted |  |  |
| R5-203772 | Correction to NR5GC testcase 9.1.4.1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-203773 | Adding applicability for new efeMTC test cases 9.8.3.1, 9.8.3.2, 9.8.4.1, 9.8.4.2 | Ericsson | agreed |  |  |
| R5-203774 | Add Annex D | Ericsson | withdrawn |  |  |
| R5-203775 | Updating test case applicability for CSI test cases | Ericsson | agreed |  |  |
| R5-203776 | Adding test case applicability rules | Ericsson | agreed |  |  |
| R5-203777 | Update of NR test case 6.2.1 UE MOP for n30 | AT&T | agreed |  |  |
| R5-203778 | Update of NR test case 6.2.2 UE MPR for n30 | AT&T | agreed |  |  |
| R5-203779 | Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.1.3.1 | Ericsson | agreed |  |  |
| R5-203780 | Update of NR test case 6.2D.1 UE MOP for UL MIMO for n30 | AT&T | agreed |  |  |
| R5-203781 | Update of NR test case 6.2D.2 UE MPR for UL MIMO for n30 | AT&T | withdrawn |  |  |
| R5-203782 | Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.2.3.1 | Ericsson | agreed |  |  |
| R5-203783 | Update of NR test case 6.5.3.2 Spurious Emissions for UE Co-Ex for n30 | AT&T | agreed |  |  |
| R5-203784 | Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | revised |  | R5-204967 |
| R5-203785 | Correction to NR5GC testcase 10.1.1.2 | ROHDE & SCHWARZ, Qualcomm | agreed |  |  |
| R5-203786 | Update of NR test case 7.3 UE Ref Sens for n30 | AT&T | agreed |  |  |
| R5-203787 | Update of NR test case 7.6.2 UE IBB for n30 | AT&T, DISH Network, CAICT, Ericsson, HiSilicon | revised |  | R5-204962 |
| R5-203788 | Update of NR test case 7.6.3 UE OBB for n30 | AT&T | agreed |  |  |
| R5-203789 | Update of NR test case 7.6.4 UE NBB for n30 | AT&T | agreed |  |  |
| R5-203790 | Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | revised |  | R5-204968 |
| R5-203791 | Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | revised |  | R5-204969 |
| R5-203792 | Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | revised |  | R5-204970 |
| R5-203793 | Correction of n29 test frequencies for protocol testing | Ericsson | agreed |  |  |
| R5-203794 | Introduction of n30 test frequencies for protocol testing | Ericsson, AT&T | agreed |  |  |
| R5-203795 | Updated Check List for adding new NR bands and for new channel bandwidth to existing NR bands | Ericsson | noted |  |  |
| R5-203796 | Correction of EN-DC test frequency information for protocol testing | Ericsson | agreed |  |  |
| R5-203797 | Update test point analysis for A-MPR NS_18 with CBW being 30MHz | CMCC, Huawei, HiSilicon | revised |  | R5-204963 |
| R5-203798 | Checklist - NR_Rel-16_CA_DC for RAN5#88-e | CMCC, Bureau Veritas | noted |  |  |
| R5-203799 | Correction to NB-IoT test case 22.4.5 | ROHDE & SCHWARZ | revised |  | R5-204527 |
| R5-203800 | Addition of 6.1.23 NB-IOT TDD Inter-frequency RRC Re-establishment in In-Band mode under normal coverage | Sporton | agreed |  |  |
| R5-203801 | Addition of 6.1.24 NB-IOT TDD - TDD Intra-frequency RRC Re-establishment in In-Band mode under enhanced coverage | Sporton | agreed |  |  |
| R5-203802 | Addition of 6.2.19 NB-IOT TDD Contention Based Random Access Test in normal coverage | Sporton | agreed |  |  |
| R5-203803 | Addition of 6.2.20 NB-IOT TDD Contention Based Random Access Test in enhanced coverage | Sporton | agreed |  |  |
| R5-203804 | Update additional information for test applicability for NB-IoT Test cases | Sporton | withdrawn |  |  |
| R5-203805 | Addition of test point analysis of DC_66A_n2A in Tx spurious emissions | Sporton | withdrawn |  |  |
| R5-203806 | Addition of test point analysis in Tx spurious emissions | Sporton, Ericsson | revised |  | R5-204726 |
| R5-203807 | Updated to clause 6 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas, Ericsson | revised |  | R5-204724 |
| R5-203808 | Updated to clause 7 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas | revised |  | R5-204956 |
| R5-203809 | Correction to RRC measurement testcase 8.3.1.11 for measGapConfig for CAT-M1 | ANRITSU LTD | agreed |  |  |
| R5-203810 | Correction to NR5GC test case 6.1.2.9 | ANRITSU LTD | agreed |  |  |
| R5-203811 | Correction to NR CA RRC Test cases 8.1.3.1.17.x and 8.1.3.1.18.x | ANRITSU LTD | agreed |  |  |
| R5-203812 | Correction RRC idle mode test cases 6.1.1.x | ANRITSU LTD | agreed |  |  |
| R5-203813 | Correction to PUCCH-Config | ANRITSU LTD | agreed |  |  |
| R5-203814 | Addition of NR-DC RRC test case 8.2.3.14.2 | ANRITSU LTD | revised |  | R5-204454 |
| R5-203815 | FR2 PUSCH K2 values alignment to TS 38.214 | Qualcomm Wireless GmbH | agreed |  |  |
| R5-203816 | FR2 RefSens and EIS spherical PC3 MBR table update | Qualcomm Wireless GmbH | revised |  | R5-204920 |
| R5-203817 | FR2 RefSens inter-band EN-DC UL MIMO test cases | Qualcomm Wireless GmbH | revised |  | R5-204770 |
| R5-203818 | Spurious inter-band EN-DC FR2 UL MIMO test cases | Qualcomm Wireless GmbH | revised |  | R5-204766 |
| R5-203819 | Discussion on PCC prioritization for FR1 and FR2 UL CA testing | Qualcomm Inc, Verizon Inc. | noted |  |  |
| R5-203820 | Correction of RRM Test Case 6.1.1.1 | MediaTek Inc. | revised |  | R5-204733 |
| R5-203821 | Addition of FR1 Test tolerance analysis for DCI based BWP switch | Huawei, HiSilicon | revised |  | R5-205001 |
| R5-203822 | Addition of FR1 Test tolerance analysis for RRC based BWP switch | Huawei, HiSilicon | revised |  | R5-205002 |
| R5-203823 | Addition of FR1 Test tolerance analysis for SSB based BFR | Huawei, HiSilicon | revised |  | R5-205003 |
| R5-203824 | Addition of FR1 Test tolerance analysis for CSI-RS based BFR | Huawei, HiSilicon | revised |  | R5-205004 |
| R5-203825 | Addition of FR1 Test tolerance analysis for 6.3.2.1.3 RRC Re-establishment | Huawei, HiSilicon | agreed |  |  |
| R5-203826 | Update of grouping of test cases in clause 8 | Huawei, HiSilicon | agreed |  |  |
| R5-203827 | Addition of 4.5.5.0 minimum requirement for BFR | Huawei, HiSilicon | withdrawn |  | - |
| R5-203828 | Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | revised |  | R5-204985 |
| R5-203829 | Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | revised |  | R5-204986 |
| R5-203830 | Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance | Huawei, HiSilicon, CAICT | revised |  | R5-204987 |
| R5-203831 | Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon, CAICT | revised |  | R5-204988 |
| R5-203832 | Update of 4.5.6.1.0 minimum requirement for DCI-based BWP switch | Huawei, HiSilicon | agreed |  |  |
| R5-203833 | Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch | Huawei, HiSilicon | revised |  | R5-204989 |
| R5-203834 | Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell | Huawei, HiSilicon | revised |  | R5-204990 |
| R5-203835 | Update of 4.5.6.2.0 minimum requirement for RRC-based BWP switch | Huawei, HiSilicon | agreed |  |  |
| R5-203836 | Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | revised |  | R5-204991 |
| R5-203837 | Update of FR1 Test Tolerance in 6.3.2.1.3 RRC re-establishment without serving cell timing | Huawei, HiSilicon | agreed |  |  |
| R5-203838 | Addition of 6.5.2.0 minimum requirement for interruptions during measurements on NR SCC | Huawei, HiSilicon | agreed |  |  |
| R5-203839 | Update of 6.5.2.1 interruptions during measurements on deactivated NR SCC | Huawei, HiSilicon, CAICT | agreed |  |  |
| R5-203840 | Addition of new Test Case 6.5.3.1 SCell activation and deactivation for 160ms cycle | Huawei, HiSilicon, CAICT | agreed |  |  |
| R5-203841 | Addition of new Test Case 6.5.3.2 SCell activation and deactivation for 320ms cycle | Huawei, HiSilicon, CAICT | agreed |  |  |
| R5-203842 | Addition of new Test Case 6.5.3.3 SCell activation and deactivation of unknown SCell | Huawei, HiSilicon, CAICT | agreed |  |  |
| R5-203843 | Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | revised |  | R5-204992 |
| R5-203844 | Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | revised |  | R5-204993 |
| R5-203845 | Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX | Huawei, HiSilicon | revised |  | R5-204994 |
| R5-203846 | Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon | revised |  | R5-204995 |
| R5-203847 | Update of 6.5.6.1.0 minimum requirement for DCI-based BWP switch | Huawei, HiSilicon | agreed |  |  |
| R5-203848 | Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell | Huawei, HiSilicon | revised |  | R5-204996 |
| R5-203849 | Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance | Huawei, HiSilicon | revised |  | R5-204997 |
| R5-203850 | Update of 6.5.6.2.0 minimum requirement for RRC-based BWP switch | Huawei, HiSilicon | agreed |  |  |
| R5-203851 | Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | revised |  | R5-204998 |
| R5-203852 | Update of test parameters in 6.3.1.4 inter-RAT handover | Huawei, HiSilicon | revised |  | R5-204999 |
| R5-203853 | Correction to FR1 intra-frequency measurement with gap test cases | Huawei, HiSilicon | agreed |  |  |
| R5-203854 | Update of FR1 Test Tolerance in Annex F | Huawei, HiSilicon | revised |  | R5-204786 |
| R5-203855 | Update of Cell mapping in Annex E | Huawei, HiSilicon | agreed |  |  |
| R5-203856 | Update of default configurations for RMC scheduling in Annex A | Huawei, HiSilicon | revised |  | R5-205000 |
| R5-203857 | Update of Test Tolerance for HPUE | Huawei, HiSilicon | agreed |  |  |
| R5-203858 | Update of MOP for HPUE | Huawei, HiSilicon | agreed |  |  |
| R5-203859 | Update of MPR for HPUE | Huawei, HiSilicon | agreed |  |  |
| R5-203860 | Update of capability for HPUE | Huawei, HiSilicon | agreed |  |  |
| R5-203861 | Update of capability for 6.1.2.5a cell re-selection for HPUE | Huawei, HiSilicon | agreed |  |  |
| R5-203862 | Correction to default configurations in Annex H | Huawei, HiSilicon | revised |  | R5-204787 |
| R5-203863 | Correction to Table 7.3.1-3 SSB-MTC | Huawei, HiSilicon | withdrawn |  |  |
| R5-203864 | Correction to TCI-state related configurations | Huawei, HiSilicon | revised |  | R5-204752 |
| R5-203865 | Correction to CSI-RS related configurations | Huawei, HiSilicon | revised |  | R5-204753 |
| R5-203866 | WP - R15 TDD HPUE – Status after RAN5#88-e | Huawei, HiSilicon | noted |  |  |
| R5-203867 | SR - R15 TDD HPUE – Status after RAN5#88-e | Huawei, HiSilicon | noted |  |  |
| R5-203868 | Discussion on Scope, Purpose and drafting guideline for 38.522 | CAICT | revised |  | R5-204951 |
| R5-203869 | Correction of 38.522 | CAICT | revised |  | R5-204940 |
| R5-203870 | Update of Test applicability for some Inter-Band EN-DC including FR2 TCs | CAICT | revised |  | R5-204924 |
| R5-203871 | Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | revised |  | R5-204927 |
| R5-203872 | Adding RRCConnectionReconfiguration Table for E-UTRA on FDD band and UE does not support dynamic power sharing in 6.5B.3.3.1 and 6.5B.3.3.2 | CAICT | agreed |  |  |
| R5-203873 | Correction of UL power level requirement in 7.4 | CAICT | withdrawn |  |  |
| R5-203874 | Correction of test procedure of ACLR and SEM for SA FR2 | CAICT | withdrawn |  |  |
| R5-203875 | Alignment of general sections with core spec of SA FR2 R15 | CAICT | agreed |  |  |
| R5-203876 | Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec | CAICT | revised |  | R5-204855 |
| R5-203877 | Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec | CAICT | revised |  | R5-204910 |
| R5-203878 | Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4 | CAICT | revised |  | R5-204911 |
| R5-203879 | Correction of diversity characteristics requirement in section 7.2 | CAICT | agreed |  |  |
| R5-203880 | Correction of UE mean power requirements Table numbers in SEM and ACLR test cases for SA FR1 | CAICT | agreed |  |  |
| R5-203881 | Adding NOTEs to the test requirement tables in 6.2D.2 | CAICT | agreed |  |  |
| R5-203882 | Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2 | CAICT | revised |  | R5-204905 |
| R5-203883 | Correction of test requirement for 6.2.4 | CAICT | revised |  | R5-204906 |
| R5-203884 | Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04 | CAICT | revised |  | R5-204907 |
| R5-203885 | Correction of test requirement for 6.2.1 | CAICT | agreed |  |  |
| R5-203886 | Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4 | CAICT | revised |  | R5-204908 |
| R5-203887 | Introduction and correction of general capabilities and some band-combo information for EN-DC | CAICT | revised |  | R5-204903 |
| R5-203888 | Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs | CAICT | revised |  | R5-204900 |
| R5-203889 | Adding branch of PC3 and HPUE for 6.6.2.1 and 6.6.2.2 in Table 4.1-1 | CAICT | agreed |  |  |
| R5-203890 | Removal of void test case and correction of condition for Inter-band measurements test cases | CAICT | revised |  | R5-204473 |
| R5-203891 | Introduction of Inter-band measurements capabilities for signalling test cases | CAICT | withdrawn |  |  |
| R5-203892 | Addition of new NAS test case to test handling of extended octets | NTT DOCOMO INC. | revised |  | R5-204523 |
| R5-203893 | New UE Conformance NR Band n53 WID | GLOBALSTAR Inc. | withdrawn |  |  |
| R5-203894 | Proposal for new EPS Mobility Management test case for extended octets | NTT DOCOMO INC. | noted |  |  |
| R5-203895 | Correction of RRM Test Case 6.1.1.2 | MediaTek Inc. | revised |  | R5-204734 |
| R5-203896 | Correction of RRM Test Case 7.1.1.1 | MediaTek Inc. | revised |  | R5-204735 |
| R5-203897 | Correction of RRM Test Case 7.1.1.2 | MediaTek Inc. | revised |  | R5-204736 |
| R5-203898 | Test applicability for new NAS TC 9.2.1.1.31 | NTT DOCOMO INC. | agreed |  |  |
| R5-203899 | Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1 | NTT DOCOMO INC. | revised |  | R5-204474 |
| R5-203900 | New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) | China Unicom | revised |  | R5-204354 |
| R5-203901 | New WID on UE Conformance Test Aspects – Single Radio Voice Call Continuity from 5G to 3G | China Unicom | revised |  | R5-204355 |
| R5-203902 | Correction to Annex G minimum test time table | Qualcomm Korea | agreed |  |  |
| R5-203903 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | revised |  | R5-204870 |
| R5-203904 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | revised |  | R5-204774 |
| R5-203905 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | revised |  | R5-204871 |
| R5-203906 | New WID on UE Conformance Test Aspects for NR performance enhancement | Qualcomm Korea | revised |  | R5-204356 |
| R5-203907 | Corrections on delta RIB due to Rel-16 EN-DC configurations | ZTE Corporation | agreed |  |  |
| R5-203908 | Corrections on test frequencies for NR FR2 CA band n261 | ZTE Corporation | agreed |  |  |
| R5-203909 | Update of 6.2.3 for minimum conformance requirements for A-MPR | ZTE Corporation | revised |  | R5-204909 |
| R5-203910 | Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1 | ZTE Corporation | revised |  | R5-204771 |
| R5-203911 | Update of A.4.3.2A for intra-band contiguous CA capabilities | ZTE Corporation | agreed |  |  |
| R5-203912 | Update of A.4.3.2A.3 for intra-band non-contiguous CA capabilities | ZTE Corporation | agreed |  |  |
| R5-203913 | Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities | ZTE Corporation | revised |  | R5-204802 |
| R5-203914 | Update of A.4.3.2B for NR-DC capabilities | ZTE Corporation | agreed |  |  |
| R5-203915 | Update of A.4.3.2B.2 for intra-band EN-DC capabilities | ZTE Corporation | revised |  | R5-204803 |
| R5-203916 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities | ZTE Corporation | revised |  | R5-204804 |
| R5-203917 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR2 capabilities | ZTE Corporation | agreed |  |  |
| R5-203918 | Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities | ZTE Corporation | revised |  | R5-204805 |
| R5-203919 | Update of Tx test for DC_2_n41 and DC_66_n41 | ZTE Corporation | withdrawn |  |  |
| R5-203920 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | withdrawn |  |  |
| R5-203921 | Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3 | Google Inc. | revised |  | R5-204977 |
| R5-203922 | Update of common test environment for short TTI and short processing time TCs | Huawei, Hisilicon | agreed |  |  |
| R5-203923 | Update of test description for DL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | revised |  | R5-204494 |
| R5-203924 | Update of message contents for UL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | agreed |  |  |
| R5-203925 | Correction to derivation path for SRS transmission test cases for sTTI and short processing time | Huawei, Hisilicon | agreed |  |  |
| R5-203926 | Correction to test applicability for sTTI test cases | Huawei, Hisilicon | revised |  | R5-204495 |
| R5-203927 | Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-1 | Huawei, Hisilicon | agreed |  |  |
| R5-203928 | Update of message contents and test tolerance for transmitted power in sTTI test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203929 | Update of test tolerance for demodulation performance in sTTI test cases | Huawei, Hisilicon | revised |  | R5-204892 |
| R5-203930 | Update of test tolerance for CSI reporting in sTTI test cases | Huawei, Hisilicon | agreed |  |  |
| R5-203931 | Addition of acceptable uncertainty and test tolerance for sTTI test cases | Huawei, Hisilicon | revised |  | R5-204893 |
| R5-203932 | Discussion on measurement uncertainty for sTTI test cases | Huawei, Hisilicon | revised |  | R5-204955 |
| R5-203933 | Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-3 | Huawei, Hisilicon | agreed |  |  |
| R5-203934 | Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time | Huawei, Hisilicon | revised |  | R5-204798 |
| R5-203935 | Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time | Huawei, Hisilicon | revised |  | R5-204799 |
| R5-203936 | Addition of downlink RMC configuration with sTTI | Huawei, Hisilicon | agreed |  |  |
| R5-203937 | Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A | Huawei, Hisilicon | revised |  | R5-204700 |
| R5-203938 | Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1 | Huawei, Hisilicon | revised |  | R5-204701 |
| R5-203939 | Update of test point analysis of MOP for intra-band contiguous EN-DC | Huawei, Hisilicon | revised |  | R5-204728 |
| R5-203940 | Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x | Huawei, Hisilicon | revised |  | R5-204767 |
| R5-203941 | Addition of the test description to apply LTE agnostic approach in 7.4B.2 MIL | Huawei, Hisilicon | agreed |  |  |
| R5-203942 | Addition of intra-band contiguous EN-DC with more than 2CCs within FR1 in 7.4B.3_1 | Huawei, Hisilicon | withdrawn |  |  |
| R5-203943 | Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO | Huawei, Hisilicon | revised |  | R5-204772 |
| R5-203944 | Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | revised |  | R5-204702 |
| R5-203945 | Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | revised |  | R5-204703 |
| R5-203946 | Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | revised |  | R5-204768 |
| R5-203947 | Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204791 |
| R5-203948 | Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204792 |
| R5-203949 | Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204793 |
| R5-203950 | Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204794 |
| R5-203951 | Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204795 |
| R5-203952 | Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204796 |
| R5-203953 | Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC | Huawei, Hisilicon | revised |  | R5-204814 |
| R5-203954 | Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204817 |
| R5-203955 | Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204818 |
| R5-203956 | Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204819 |
| R5-203957 | Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204820 |
| R5-203958 | Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204821 |
| R5-203959 | Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence | Huawei, Hisilicon | revised |  | R5-204822 |
| R5-203960 | Correction to additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | agreed |  |  |
| R5-203961 | Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations | Huawei, Hisilicon | revised |  | R5-204797 |
| R5-203962 | Update of SA Rx test cases for 4Rx UEs | Huawei, HiSilicon | revised |  | R5-204912 |
| R5-203963 | Update of NSA Rx test cases for 4Rx UEs | Huawei, HiSilicon | revised |  | R5-204928 |
| R5-203964 | Update of test cases for UEs supporting Tx Diversity | Huawei, HiSilicon | withdrawn |  |  |
| R5-203965 | Update of MOP test cases for EN-DC PC2 Rel-15 requirements | Huawei, HiSilicon | withdrawn |  |  |
| R5-203966 | Update of MOP test cases for EN-DC PC2 Rel-16 requirements | Huawei, HiSilicon | revised |  | R5-204845 |
| R5-203967 | Editorial correction of 6.2.4 | Huawei, HiSilicon | agreed |  |  |
| R5-203968 | Miscellaneous corrections due to core spec alignment | Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson | revised |  | R5-204763 |
| R5-203969 | Updating beam correspondance capability | Huawei, HiSilicon | agreed |  |  |
| R5-203970 | Addition of UL power setting for Rx test cases | Huawei, HiSilicon, CAICT | revised |  | R5-204765 |
| R5-203971 | Addition of modified MPR behavior | Huawei, HiSilicon | revised |  | R5-204921 |
| R5-203972 | Discussion on QZ size | Huawei, HiSilicon | withdrawn |  |  |
| R5-203973 | Cleaning up of delta_TIB | Huawei, HiSilicon | agreed |  |  |
| R5-203974 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | revised |  | R5-204759 |
| R5-203975 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | withdrawn |  |  |
| R5-203976 | Addition of 25MHz for NR band n1 | Huawei, HiSilicon | revised |  | R5-204825 |
| R5-203977 | Addition of AMPR NS_48 for NR band n1 | Huawei, HiSilicon | revised |  | R5-204826 |
| R5-203978 | Addition of test point analysis for AMPR NS_48 | Huawei, HiSilicon | revised |  | R5-204829 |
| R5-203979 | WF of eMIMO testing | Huawei, HiSilicon, Samsung | noted |  |  |
| R5-203980 | WF of V2X RF testing | Huawei, HiSilicon | revised |  | R5-204975 |
| R5-203981 | Updated to NB-IOT TC 6.3.5F.1 | Huawei, HiSilicon | revised |  | R5-204830 |
| R5-203982 | Updated to NB-IOT TC 6.3.5F.3 | Huawei, HiSilicon | revised |  | R5-204965 |
| R5-203983 | Cleaning up of V2X RB allocation for non-concurrent transmission | Huawei, HiSilicon | revised |  | R5-204841 |
| R5-203984 | Cleaning up of V2X RB allocation for simultaneous transmission | Huawei, HiSilicon | revised |  | R5-204842 |
| R5-203985 | Cleaning up of V2X RB allocation for multi-carrier operation | Huawei, HiSilicon | revised |  | R5-204843 |
| R5-203986 | Updating test casees for several CA configurations | Huawei, HiSilicon | revised |  | R5-204750 |
| R5-203987 | Updating test point analysis for AMPR of NS_01 and NS_04 | Huawei, HiSilicon | agreed |  |  |
| R5-203988 | Updating test point analysis for 3A-41A to add SE-coex | Huawei, HiSilicon | agreed |  |  |
| R5-203989 | Adding signalling test frequency for 3A-41A | Huawei, HiSilicon | withdrawn |  | - |
| R5-203990 | WP - Shortened TTI and processing time for LTE | Huawei, HiSilicon | noted |  |  |
| R5-203991 | SR - Shortened TTI and processing time for LTE | Huawei, HiSilicon | noted |  |  |
| R5-203992 | WP - RF requirements for NR frequency range 1 (FR1) | Huawei, HiSilicon | noted |  |  |
| R5-203993 | SR - RF requirements for NR frequency range 1 (FR1) | Huawei, HiSilicon | noted |  |  |
| R5-203994 | WP - Enhancements on MIMO for NR | Huawei, HiSilicon | noted |  |  |
| R5-203995 | SR - Enhancements on MIMO for NR | Huawei, HiSilicon | noted |  |  |
| R5-203996 | Corrections to EPS Fallback regarding IMS procedures | ROHDE & SCHWARZ | revised |  | R5-204466 |
| R5-203997 | Correction Test applicability of test case 9.2.56 and 9.2.57 | Google Inc. | agreed |  |  |
| R5-203998 | Addition of test frequencies for new Rel-16 CBW 25 and 50 MHz for NR band n1 | Ericsson | agreed |  |  |
| R5-203999 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | revised |  | R5-204754 |
| R5-204000 | Correction Additional Information in Table 4.2-1 of test case 9.2.56 and 9.2.57 | Google Inc. | agreed |  |  |
| R5-204001 | Annex F based on updated Tx test cases for efeMTC | Ericsson | agreed |  |  |
| R5-204002 | Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection | TDIA, CATT | revised |  | R5-204497 |
| R5-204003 | Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1 | Ericsson | revised |  | R5-204971 |
| R5-204004 | Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement | TDIA, CATT | revised |  | R5-204498 |
| R5-204005 | Adding PC6 to 6.3.5EA.1, Power Control Absolute power tolerance for UE category M1 | Ericsson | agreed |  |  |
| R5-204006 | Update of test applicabilities for NB_IOTenh2 | CATT, TDIA | agreed |  |  |
| R5-204007 | Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1 | Ericsson | agreed |  |  |
| R5-204008 | Correction to UE co-existence Test Case 6.5B.3.3.2 | Huawei, Hisilicon | withdrawn |  |  |
| R5-204009 | Correction to UE co-existence Test Case 6.5B.3.3.2 | Huawei, Hisilicon | withdrawn |  |  |
| R5-204010 | Correction to target power level Pmin for SA UL MIMO TCs | Huawei, Hisilicon | agreed |  |  |
| R5-204011 | Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1 | Ericsson | withdrawn |  |  |
| R5-204012 | Update to Common contents of system information messages for NB_IOTenh2 | CATT, TDIA | revised |  | R5-204496 |
| R5-204013 | Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1 | Ericsson | revised |  | R5-204972 |
| R5-204014 | Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1 | Ericsson | revised |  | R5-204973 |
| R5-204015 | Correction of NR TC 6.2.2.1 | TDIA, CATT | agreed |  |  |
| R5-204016 | Correction to NR TC 8.1.4.1.8.X-Scell no change | Huawei, Hisilicon | agreed |  |  |
| R5-204017 | Adding PC6 to 6.3.5EA.2, Power Control Relative power tolerance for UE category M1 | Ericsson | agreed |  |  |
| R5-204018 | Correction of NR TC 6.2.2.2 | TDIA, CATT | agreed |  |  |
| R5-204019 | Correction to NR5G UAC TC 11.3.8 | TDIA, CATT | agreed |  |  |
| R5-204020 | Clarification on frequency band test conditions for A-GNSS | Qualcomm Incorporated | revised |  | R5-204979 |
| R5-204021 | Correction of n51 and n76 test frequencies for protocol testing | Ericsson | agreed |  |  |
| R5-204022 | Discussion on FR2 absolute power control MU | Samsung R&D Institute UK | noted |  |  |
| R5-204023 | Addition of test point analysis for additional spurious emission with NS_17 | Huawei, Orange, CMCC | revised |  | R5-204964 |
| R5-204024 | Correction of Table 9.2.18.1.3-2 and Table 9.2.18.2.3-2 | Google Inc. | agreed |  |  |
| R5-204025 | CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps | Samsung R&D Institute UK | revised |  | R5-204858 |
| R5-204026 | Editorial update of Annex C.3.3.1 | MediaTek Inc. | revised |  | R5-204731 |
| R5-204027 | Discussion on remaining parameters for FR2 EIRP Tx OFF power MU | Samsung R&D Institute UK | noted |  |  |
| R5-204028 | CR to 38.903 on some of the Transmit OFF power MU parameters | Samsung R&D Institute UK | revised |  | R5-204945 |
| R5-204029 | Correction to NR5GC testcase 8.1.1.3.2 | ROHDE & SCHWARZ, Qualcomm | revised |  | R5-204435 |
| R5-204030 | CR to 38.521-2 to update Transmit OFF Power | Samsung R&D Institute UK | revised |  | R5-204915 |
| R5-204031 | CR to TS 38.521-2: Correction to time mask requirements | Samsung R&D Institute UK | revised |  | R5-204916 |
| R5-204032 | Introduction of n259 test frequencies for protocol testing | Ericsson | agreed |  |  |
| R5-204033 | CR to TS 38.521-2: Annex F EIRP OFF Power | Samsung R&D Institute UK | revised |  | R5-204922 |
| R5-204034 | CR to 38.533 on RRM Test Cases in clause 7.5.3 | Samsung R&D Institute UK | agreed |  |  |
| R5-204035 | Updating NR test case 7.6A.3 for n48 | Huawei, Hisilicon | agreed |  |  |
| R5-204036 | CR to 38.533 on RRM Test Cases in clause 7.5.7 | Samsung R&D Institute UK | agreed |  |  |
| R5-204037 | Update of NR test case 7.5A Adjacent Channel selectivity for CA | Samsung R&D Institute UK | revised |  | R5-204898 |
| R5-204038 | Corrections of test frequency tables for EN-DC configuration DC_(n)41AA | Ericsson | agreed |  |  |
| R5-204039 | Corrections of test frequency tables for EN-DC configuration DC_(n)71AA | Ericsson | agreed |  |  |
| R5-204040 | Update of NR test case 7.7A Spurious response for CA | Samsung R&D Institute UK | agreed |  |  |
| R5-204041 | Addition of test channel bandwidths for n1 new CBW in 38.508-1 R16 | China Unicom | agreed |  |  |
| R5-204042 | Discussion on multi-band relaxation framework requirement enhancement | Samsung R&D Institute UK | noted |  |  |
| R5-204043 | Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents | ANRITSU LTD | revised |  | R5-204385 |
| R5-204044 | CR to TS 38.521-2: Correction to MB relaxation minimum requirements | Samsung R&D Institute UK | revised |  | R5-204859 |
| R5-204045 | Update release applicability of TC 9.2.2D | MediaTek Inc. | revised |  | R5-204732 |
| R5-204046 | Addition of R16 new channel bandwidths for n1 in 38.508-2 | China Unicom | withdrawn |  |  |
| R5-204047 | Correction to intra-frequency event triggered reporting test case in CEModeA | Anritsu | agreed |  |  |
| R5-204048 | Correction to E-UTRAN HD-FDD Radio Link Monitoring Test for Out-of-sync in DRX for CE UE in CEmodeA | Anritsu | agreed |  |  |
| R5-204049 | Correction to the procedure for determination of SSB and CORESET0 | Anritsu | agreed |  |  |
| R5-204050 | Correction to message configuration for performance tests | Anritsu | revised |  | R5-204901 |
| R5-204051 | Correction to PRB-Id | Anritsu | withdrawn |  |  |
| R5-204052 | PUCCH Resource ID for CSI TCs | Anritsu | agreed |  |  |
| R5-204053 | Correction to PDCCH-ConfigCommon for performance tests | Anritsu | agreed |  |  |
| R5-204054 | Correction to test Configuration of flatness for Pi/2 BPSK | Anritsu | agreed |  |  |
| R5-204055 | Clean up complete status for FR2 SA test cases | Anritsu | revised |  | R5-204917 |
| R5-204056 | CR to update MU and TT in 38.521-2 | Anritsu | revised |  | R5-204856 |
| R5-204057 | Update to UE maximum output power for CA | Anritsu | revised |  | R5-204918 |
| R5-204058 | Clean up complete status for EN-DC test cases | Anritsu | revised |  | R5-204925 |
| R5-204059 | Correction to default test setting of 7.3B.2.3_1.1 | Anritsu | withdrawn |  |  |
| R5-204060 | CR to update MU and TT in 38.521-3 | Anritsu | revised |  | R5-204866 |
| R5-204061 | Correction to frequencyDomainAllocation | Anritsu | revised |  | R5-204934 |
| R5-204062 | Correction to PDSCH reference channel | Anritsu | agreed |  |  |
| R5-204063 | Correction to 2Rx FDD FR1 periodic wideband CQI reporting under fading conditions | Anritsu | agreed |  |  |
| R5-204064 | Correction to LTE-NR coexistence performance | Anritsu | agreed |  |  |
| R5-204065 | CR to update MU and TT in 38.521-4 | Anritsu | revised |  | R5-204933 |
| R5-204066 | Correction to MU and TT for FR1 PMI and RI tests | Anritsu | revised |  | R5-204935 |
| R5-204067 | Correction to common test parameters for FR2 demod and CSI tests | Anritsu | withdrawn |  |  |
| R5-204068 | Correction to FR2 timing advance adjustment accuracy | Anritsu | agreed |  |  |
| R5-204069 | Correction to EN-DC FR2 interruptions at transitions between active and non-active during DRX | Anritsu | agreed |  |  |
| R5-204070 | Addition of E-UTRA Test frequency selection rule for IRAT test cases | Anritsu | agreed |  |  |
| R5-204071 | Correction on event-triggered reporting with gap in DRX and DRX configuration settings for NR serving cell | Anritsu | agreed |  |  |
| R5-204072 | Correction to EN-DC and SA FR1-FR1 SS-RSRP and SS-RSRQ periodical measurement accuracy | Anritsu | agreed |  |  |
| R5-204073 | Correction to SS-RSRQ periodical measurement accuracy | Anritsu | agreed |  |  |
| R5-204074 | Correction to connection diagram for radio link monitoring tests | Anritsu | revised |  | R5-204941 |
| R5-204075 | Correction to message configuration for radio link monitoring tests | Anritsu | agreed |  |  |
| R5-204076 | Correction to NR SA FR1 E-UTRA RRC connection release with redirection | Anritsu | agreed |  |  |
| R5-204077 | Correction to SRS PeriodicityAndOffset for Timing Advance tests | Anritsu | agreed |  |  |
| R5-204078 | Correction to PDSCH reference measurement channel | Anritsu | withdrawn |  |  |
| R5-204079 | Correction to CSI-RS for tracking for TDD FR2 | Anritsu | agreed |  |  |
| R5-204080 | CR to update MU in 38.903 | Anritsu, Keysight Technologies | revised |  | R5-204890 |
| R5-204081 | On AWGN and signal flatness uncertainty for FR2 Performance tests | Anritsu | noted |  |  |
| R5-204082 | On FR2 DL absolute level uncertainty for DFF. | Anritsu | revised |  | R5-204745 |
| R5-204083 | On gNB emulator fading model impairments for FR2 Performance tests | Anritsu | noted |  |  |
| R5-204084 | On FR2 ACS and IBB Test Implementation and MU | Anritsu | noted |  |  |
| R5-204085 | On FR2 OBW MU | Anritsu | revised |  | R5-204849 |
| R5-204086 | Noise impact for FR2 test case where MPR applies | Anritsu | revised |  | R5-204746 |
| R5-204087 | On MU for FR2 MPR Test | Anritsu | noted |  |  |
| R5-204088 | On frequency flatness uncertainty for FR2 RRM and Performance tests | Anritsu | withdrawn |  |  |
| R5-204089 | On gNB emulator SNR uncertainty for FR2 | Anritsu | noted |  |  |
| R5-204090 | Proposal of MUs for FR2 spurious emission UE co-existence | Anritsu | noted |  |  |
| R5-204091 | Correction to test case 11.1.7 | MediaTek Inc. | revised |  | R5-204467 |
| R5-204092 | Update IE ServingCellConfigCommon | Ericsson | withdrawn |  |  |
| R5-204093 | New generic IMS procedures for use in EPS fallback | ROHDE & SCHWARZ | revised |  | R5-204484 |
| R5-204094 | MCPTT IPCAN test environment | UPV/EHU | noted |  |  |
| R5-204095 | Group Communications Key download mechanism | NEMERGENT | withdrawn |  |  |
| R5-204096 | Description of the distribution of MSCCK and MuSiK | UPV/EHU, Nemergent Solutions | revised |  | R5-204535 |
| R5-204097 | Integration of security features in MBMS procedures | UPV/EHU, NEMERGENT | revised |  | R5-204540 |
| R5-204098 | Correct applicability EN-DC event-triggered inter-frequency tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-204099 | Correct applicability NR SA event-triggered inter-frequency tests | ROHDE & SCHWARZ | agreed |  |  |
| R5-204100 | Update to common test parameters and channel mappings | Rohde & Schwarz | agreed |  |  |
| R5-204101 | Update E-UTRA cell configuration for NSA | Rohde & Schwarz | agreed |  |  |
| R5-204102 | Update Refsense exceptions for EN-DC including n78 | Rohde & Schwarz | revised |  | R5-205006 |
| R5-204103 | Correction of QPSK UL RMC | Rohde & Schwarz | agreed |  |  |
| R5-204104 | Correction of QPSK UL RMC | Rohde & Schwarz | withdrawn |  |  |
| R5-204105 | Addition of missing FR1 RMC | Rohde & Schwarz | withdrawn |  |  |
| R5-204106 | Correction to NR RRC TC 8.1.3.2.2 | MediaTek Inc. | revised |  | R5-204382 |
| R5-204107 | Correction to NR test case 7.1.2.3.11 | ZTE | agreed |  |  |
| R5-204108 | Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance | Ericsson | revised |  | R5-204978 |
| R5-204109 | Correction of RRM feMTC Test Case 5.1.34 including Test Tolerance | Ericsson | agreed |  |  |
| R5-204110 | Correction of RRM feMTC Test Case 6.1.18 including Test Tolerance | Ericsson | agreed |  |  |
| R5-204111 | Correction of RRM feMTC Test Case 7.3.69 including Test Tolerance | Ericsson | agreed |  |  |
| R5-204112 | Correction of RRM feMTC Test Cases 8.4.12 - 15 including Test Tolerance | Ericsson | agreed |  |  |
| R5-204113 | Test Tolerances for RRM feMTC Test Cases in Annex F | Ericsson | agreed |  |  |
| R5-204114 | Test Tolerance analysis for E-UTRAN HD-FDD inter frequency handover for Cat-M1 UEs in CEModeA test case | Ericsson | agreed |  |  |
| R5-204115 | Test Tolerance analysis for E-UTRAN HD-FDD Inter frequency RRC Re-establishment for Cat-M1 UE in CEModeA test case | Ericsson | agreed |  |  |
| R5-204116 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.1 | Ericsson | agreed |  |  |
| R5-204117 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2 | Ericsson | revised |  | R5-204942 |
| R5-204118 | Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.3 | Ericsson | agreed |  |  |
| R5-204119 | Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.4 | Ericsson | agreed |  |  |
| R5-204120 | Correction of FR2 condition tables in Annex B | Ericsson | revised |  | R5-204943 |
| R5-204121 | Introduction of band n259 in clause 3 | Ericsson | revised |  | R5-204944 |
| R5-204122 | Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.1 | Ericsson | agreed |  |  |
| R5-204123 | Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.2 | Ericsson | agreed |  |  |
| R5-204124 | Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.3 | Ericsson | agreed |  |  |
| R5-204125 | Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.4 | Ericsson | agreed |  |  |
| R5-204126 | Correction of minimum conformance requirements 4.6.4.0 for EN-DC FR1 L1-RSRP measurement test cases | Ericsson | agreed |  |  |
| R5-204127 | Correction of minimum conformance requirements 5.6.3.0 for EN-DC FR2 L1-RSRP measurement test cases | Ericsson | agreed |  |  |
| R5-204128 | Correction of minimum conformance requirements 7.6.3.0 for SA FR2 L1-RSRP measurement test cases | Ericsson | agreed |  |  |
| R5-204129 | Addition of n1 R16 new CBW into 38.521-1 Refsense test | China Unicom | revised |  | R5-204827 |
| R5-204130 | Correction to 9.x test cases to handle IMS Re-registration (moving between HPLMN and VPLMN) | ROHDE & SCHWARZ, Qualcomm | withdrawn |  | - |
| R5-204131 | Update of UE co-existence for CA_n1-n78 | China Unicom | revised |  | R5-204807 |
| R5-204132 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | withdrawn |  | - |
| R5-204133 | Correction to MR-DC RRC TC 8.2.3.8.1 | MediaTek Inc. | revised |  | R5-204455 |
| R5-204134 | Update IE SIB2 | Ericsson | revised |  | R5-204395 |
| R5-204135 | New procedure for PDU Session Release | MCC TF160 | revised |  | R5-204396 |
| R5-204136 | Review on FR1 TRx test point analysis for Extreme Condition | DOCOMO Communications Lab. | revised |  | R5-204952 |
| R5-204137 | Update to FreqBandList | MCC TF160, Qualcomm, Anritsu | revised |  | R5-204397 |
| R5-204138 | WP UE Conformance Test Aspects - Even further enhanced MTC for LTE | Ericsson | noted |  |  |
| R5-204139 | SR UE Conformance Test Aspects - Even further enhanced MTC for LTE | Ericsson | noted |  |  |
| R5-204140 | Updates to IEs for Early Data Transmission test cases | Ericsson | revised |  | R5-204499 |
| R5-204141 | Updates to IEs for RF eMTC TCs | Ericsson | revised |  | R5-204966 |
| R5-204142 | Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT | Ericsson | revised |  | R5-204503 |
| R5-204143 | Addition of applicability for eMTC4 TC 23.2.4 | Ericsson | revised |  | R5-204506 |
| R5-204144 | Discussion paper on applicability of legacy test cases for Cat-M1/M2 | Ericsson | noted |  |  |
| R5-204145 | Updates to legacy TCs for feMTC | Ericsson | revised |  | R5-204528 |
| R5-204146 | Updates to legacy TC applicability for feMTC | Ericsson | revised |  | R5-204529 |
| R5-204147 | Addition of Test Point analysis for FR2 Transmit OFF Power for CA | DOCOMO Communications Lab. | revised |  | R5-204948 |
| R5-204148 | Addition of Test Point analysis for FR2 Occupied bandwidth for CA | DOCOMO Communications Lab. | withdrawn |  |  |
| R5-204149 | Addition of Test Point analysis for FR2 Transmitter Spurious emissions for CA | DOCOMO Communications Lab. | withdrawn |  |  |
| R5-204150 | Update Table 5.4.2.0-2: ServingCellConfigCommon | Ericsson | agreed |  |  |
| R5-204151 | Updated to EN-DC Rel-15 Configuration information in clause 5 | Bureau Veritas | withdrawn |  |  |
| R5-204152 | Updated to EN-DC Rel-16 Configuration information in clause 5 | Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson | revised |  | R5-204816 |
| R5-204153 | Introduction of UE capabilities for Rel-16 EN-DC configurations | Bureau Veritas, Qualcomm Austria RFFE GmbH | revised |  | R5-204806 |
| R5-204154 | Updated to Annex M for EN-DC Rel-16 configuration requirement | Bureau Veritas | agreed |  |  |
| R5-204155 | Updated to clause 6 for EN-DC Rel-16 configuration test requirement | Bureau Veritas, Qualcomm Austria RFFE GmbH | revised |  | R5-204815 |
| R5-204156 | Updated to clause 7 for EN-DC Rel-16 configuration test requirement | Bureau Veritas | revised |  | R5-204957 |
| R5-204157 | Correction to RF NB-IoT test cases | Bureau Veritas | agreed |  |  |
| R5-204158 | Correction to test applicability of NB-IoT RRM tests | Bureau Veritas | agreed |  |  |
| R5-204159 | Correction to applicability table of NB-IoT tests | Bureau Veritas | agreed |  |  |
| R5-204160 | Updated to FR1 general clauses for NRSL eV2X | Bureau Veritas | revised |  | R5-204839 |
| R5-204161 | Updated to EN-DC general clauses for NRSL eV2X | Bureau Veritas | revised |  | R5-204840 |
| R5-204162 | Updated to test applicability for R15 NB-IoT requirement | Bureau Veritas | revised |  | R5-204831 |
| R5-204163 | Updated to applicability table of R15 NB-IoT tests | Bureau Veritas | agreed |  |  |
| R5-204164 | Corrections of test frequency tables for CA_n258x | Ericsson | revised |  | R5-204755 |
| R5-204165 | Corrections of test frequency tables for CA_n260x | Ericsson | revised |  | R5-204756 |
| R5-204166 | Corrections of test frequency tables for CA_n261x | Ericsson | revised |  | R5-204757 |
| R5-204167 | Corrections of test frequency tables for CA_n260(A-I) | Ericsson | agreed |  |  |
| R5-204168 | Update Table 7.3.1-4: ServingCellConfigCommon | Ericsson | agreed |  |  |
| R5-204169 | Update IE ServingCellConfigCommon | Ericsson | revised |  | R5-204398 |
| R5-204170 | Update for TC 7.5B.0 Minimum Conformance Requirements of ACS for DC | CMCC | agreed |  |  |
| R5-204171 | Update for TC 7.5B.1 ACS for intra-band contiguous EN-DC 2CC | CMCC | withdrawn |  |  |
| R5-204172 | Update for TC 7.5B.2 ACS for intra-band non-contiguous EN-DC 2CC | CMCC | withdrawn |  |  |
| R5-204173 | Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC | CMCC | revised |  | R5-204929 |
| R5-204174 | Addition of TC 7.5B.3_1.3 ACS for EN-DC within FR1 5CC | CMCC | withdrawn |  |  |
| R5-204175 | Addition of TC 7.5B.3_1.4 ACS for EN-DC within FR1 6CC | CMCC | withdrawn |  |  |
| R5-204176 | Update for TC 7.5B.4 ACS for inter-band EN-DC including FR2 2CCs | CMCC | agreed |  |  |
| R5-204177 | Update for TC 7.5B.4_1.1 ACS for inter-band EN-DC including FR2 3CCs | CMCC | agreed |  |  |
| R5-204178 | Update for TC 7.5B.4_1.2 ACS for inter-band EN-DC including FR2 4CCs | CMCC | agreed |  |  |
| R5-204179 | Update for TC 7.5B.4_1.3 ACS for inter-band EN-DC including FR2 5CCs | CMCC | agreed |  |  |
| R5-204180 | Update for TC 7.5B.4_1.4 ACS for inter-band EN-DC including FR2 6CCs | CMCC | agreed |  |  |
| R5-204181 | Addition of TC 7.5B.4D ACS for inter-band EN-DC including FR2 for UL-MIMO | CMCC | withdrawn |  |  |
| R5-204182 | Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | revised |  | R5-204773 |
| R5-204183 | Addition of TC 7.6B.2.4D Inband blocking for inter-band EN-DC including FR2 for UL-MIMO | CMCC | withdrawn |  |  |
| R5-204184 | Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | revised |  | R5-204930 |
| R5-204185 | CR to 38.521-2 to adjust the test step sequences | Keysight Technologies UK Ltd | revised |  | R5-204860 |
| R5-204186 | On Beam Peak Searches for different test configurations | Keysight Technologies UK Ltd | noted |  |  |
| R5-204187 | CR to 38.508-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | revised |  | R5-204710 |
| R5-204188 | CR to 38.521-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | revised |  | R5-204861 |
| R5-204189 | Preliminary QoQZ and EIRP MU results for ETC testing | Keysight Technologies UK Ltd | revised |  | R5-204739 |
| R5-204190 | On Standard Deviation Definition in 38.903 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-204191 | On Larger Quiet Zone Sizes | Keysight Technologies UK Ltd | revised |  | R5-204747 |
| R5-204192 | QoQZ Verification Clarification | Keysight Technologies UK Ltd | noted |  |  |
| R5-204193 | CR to 38.521-2 on QoQZ Verification Clarification | Keysight Technologies UK Ltd | revised |  | R5-204862 |
| R5-204194 | On Re-Positioning Concept for RRM 2 AoA QoQZ Validation and DFF QoQZ MU | Keysight Technologies UK Ltd | noted |  |  |
| R5-204195 | Update 6.5.3.2 Spurious emission for UE co-existence | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204196 | TP analysis 6.5B.3 TX SpurEmission EN-DC V2 | Qualcomm Austria RFFE GmbH | revised |  | R5-204949 |
| R5-204197 | Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs | Qualcomm Austria RFFE GmbH | revised |  | R5-204931 |
| R5-204198 | Update for 7.3B.2.0 | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204199 | Update for Spurious Emissions for intra-band EN-DC | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204200 | Discussion on size of Quiet Zone above 30cm | ROHDE & SCHWARZ | noted |  |  |
| R5-204201 | Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs | Qualcomm Austria RFFE GmbH | revised |  | R5-204719 |
| R5-204202 | Update for 7.3A.0 Minimum conformance requirements for CA | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204203 | CR to TS 38.521-2 on DUT alignment options | ROHDE & SCHWARZ | revised |  | R5-204923 |
| R5-204204 | Update Uplink power control window size for SA RX TCs | Qualcomm Austria RFFE GmbH | revised |  | R5-204913 |
| R5-204205 | Addition and update of PICS | Lenovo, Motorola Mobility | revised |  | R5-204544 |
| R5-204206 | Addition of NR-DC MAC Test Case | Lenovo, Motorola Mobility | revised |  | R5-204423 |
| R5-204207 | Update for 6.5B.3.3.2 Spurious emission band UE co-existence | Qualcomm Austria RFFE GmbH | revised |  | R5-204867 |
| R5-204208 | Add_TP_analysis_table for TX_spurious_emission | Qualcomm Austria RFFE GmbH | revised |  | R5-204720 |
| R5-204209 | Update Uplink power control window size for NSA RX TCs | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204210 | Update Tx TC for Rel 16 DC combos | Qualcomm Austria RFFE GmbH | agreed |  |  |
| R5-204211 | WP UE Conformance Test Aspects – Rel14 Enhanced Full Dimension MIMO for LTE | Ericsson | noted |  |  |
| R5-204212 | SR UE Conformance Test Aspects – Rel14 Enhanced Full Dimension MIMO for LTE | Ericsson | noted |  |  |
| R5-204213 | Discussion on RAN5 impact of updated Multi-Band Relaxation requirements | Ericsson | noted |  |  |
| R5-204214 | Discussion on EN-DC reference sensitivity test case structure | Ericsson | revised |  | R5-204953 |
| R5-204215 | Re-organization of EN-DC refsens test cases | Ericsson | revised |  | R5-204932 |
| R5-204216 | Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1 | Ericsson | revised |  | R5-204950 |
| R5-204217 | Addition of NR-DC RRC test case 8.2.2.9.2 | Keysight Technologies UK Ltd | agreed |  |  |
| R5-204218 | Update Tx TC for Rel 16 DC combos | Qualcomm Austria RFFE GmbH | withdrawn |  | - |
| R5-204219 | Proposals for new GNSS scenarios for TS 37.571-X | Spirent Communications | noted |  |  |
| R5-204220 | Update missing SMTC and SSB configurations in H.2 | ROHDE & SCHWARZ | agreed |  |  |
| R5-204221 | Update missing SMTC and SSB configurations in H.3 | ROHDE & SCHWARZ | agreed |  |  |
| R5-204222 | Editorial: correct table placement in H.2 | ROHDE & SCHWARZ | agreed |  |  |
| R5-204223 | Update missing SMTC configurations in RRM message contents | ROHDE & SCHWARZ | agreed |  |  |
| R5-204224 | SR - UE Conformance Test Aspects - Mission Critical Improvements (UID - 790052) MCImp-UEConTest | NIST | noted |  |  |
| R5-204225 | WP - UE Conformance Test Aspects - Mission Critical Improvements (UID - 790052) MCImp-UEConTest | NIST | noted |  |  |
| R5-204226 | Addition of XML schema for MCVideo location information | NIST | agreed |  |  |
| R5-204227 | Corrections to Chat Group Calls | NIST | revised |  | R5-204541 |
| R5-204228 | Corrections to MCVideo and MCData tables | NIST | revised |  | R5-204369 |
| R5-204229 | MCVideo and MCData in Clause 4 | NIST | agreed |  |  |
| R5-204230 | MCVideo and MCData in Clause 5.5.7 | NIST | revised |  | R5-204490 |
| R5-204231 | New WID on UE Conformance Test Aspects - Mission Critical Enhancements | NIST, Samsung | revised |  | R5-204357 |
| R5-204232 | PIXIT updates and table names | NIST | revised |  | R5-204493 |
| R5-204233 | Updates to IXIT Proforma for MCVideo and MCData | NIST, MCC TF160 | withdrawn |  | - |
| R5-204234 | Updates to UE configuration document | NIST | revised |  | R5-204491 |
| R5-204235 | Add SSB subcarrier spacing configurations in RRM message contents | ROHDE & SCHWARZ | revised |  | R5-204758 |
| R5-204236 | Correction to NR5G RRC TC 8.1.1.4.1 | Qualcomm CDMA Technologies | revised |  | R5-204436 |
| R5-204237 | Correction to NR5G RRC TC 8.1.4.1.2 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-204238 | Correction to default contents of RRCReestablishmentRequest message | Qualcomm CDMA Technologies | agreed |  |  |
| R5-204239 | Addition of NR5G UAC TC 11.3.2 | Qualcomm CDMA Technologies | revised |  | R5-204518 |
| R5-204240 | Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS | Qualcomm CDMA Technologies | revised |  | R5-204485 |
| R5-204241 | Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS | Qualcomm CDMA Technologies | revised |  | R5-204486 |
| R5-204242 | WP UE Conformance Test Aspects - Rel-16 Private Network Support for NG-RAN | Qualcomm CDMA Technologies | noted |  |  |
| R5-204243 | SR UE Conformance Test Aspects - Rel-16 Private Network Support for NG-RAN | Qualcomm CDMA Technologies | noted |  |  |
| R5-204244 | WP UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA | Qualcomm CDMA Technologies | revised |  | R5-204542 |
| R5-204245 | SR UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA | Qualcomm CDMA Technologies | noted |  |  |
| R5-204246 | Discussion paper for RRC Segmentation in Rel-16 RACS | Qualcomm CDMA Technologies | not pursued |  |  |
| R5-204247 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | revised |  | R5-204919 |
| R5-204248 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | withdrawn |  |  |
| R5-204249 | Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC | Ericsson | withdrawn |  |  |
| R5-204250 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | agreed |  |  |
| R5-204251 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | revised |  | R5-204487 |
| R5-204252 | Editorial update to EMM test case 9.2.1.1.7b | Qualcomm Incorporated | agreed |  |  |
| R5-204253 | On FR2 Minimum Output Power relaxation and measurement uncertainty | Keysight Technologies UK Ltd | revised |  | R5-204740 |
| R5-204254 | Correction to NR UE Capability test case 8.1.5.1.1 | Qualcomm Incorporated | agreed |  |  |
| R5-204255 | FR2 Minimum output power MU updates | Keysight Technologies UK Ltd | revised |  | R5-204863 |
| R5-204256 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | revised |  | R5-204868 |
| R5-204257 | FR2 Minimum output power measurement uncertainty | Keysight Technologies UK Ltd | revised |  | R5-204891 |
| R5-204258 | Editorial correction to FR1 co-existence requirements | ROHDE & SCHWARZ | revised |  | R5-204761 |
| R5-204259 | Editorial correction to EN-DC co-existence requirements | ROHDE & SCHWARZ | revised |  | R5-204769 |
| R5-204260 | Discussion on DC_41C_n41A and DC_41D_n41A | ROHDE & SCHWARZ | revised |  | R5-204846 |
| R5-204261 | Editorial correction of message exceptions | ROHDE & SCHWARZ | agreed |  |  |
| R5-204262 | Update to reference sensitivity test case 7.3B.2.3_1 | ROHDE & SCHWARZ | withdrawn |  |  |
| R5-204263 | Update of CSI-RS definition for DL RMCs in TS 38.521-1 | ROHDE & SCHWARZ | agreed |  |  |
| R5-204264 | Editorial correction of ACLR CA test cases | ROHDE & SCHWARZ | agreed |  |  |
| R5-204265 | Editorial correction of Annex C.3 Connection | ROHDE & SCHWARZ | agreed |  |  |
| R5-204266 | Update of FR2 OBW test case | ROHDE & SCHWARZ | agreed |  |  |
| R5-204267 | Update of Tx signal quality test cases | ROHDE & SCHWARZ | revised |  | R5-204764 |
| R5-204268 | Update of CSI-RS definition for DL RMCs in TS 38.521-2 | ROHDE & SCHWARZ | withdrawn |  |  |
| R5-204269 | On gNB emulator fading model impairments | ROHDE & SCHWARZ | noted |  |  |
| R5-204270 | On the MU of FR2 OBW | ROHDE & SCHWARZ | noted |  |  |
| R5-204271 | On the AWGN flatness and signal flatness | ROHDE & SCHWARZ | revised |  | R5-204748 |
| R5-204272 | Update of AWGN flatness in TR 38.903 | ROHDE & SCHWARZ | revised |  | R5-204946 |
| R5-204273 | Update of AWGN flatness in TS 38.521-4 | ROHDE & SCHWARZ | revised |  | R5-204938 |
| R5-204274 | On the SNR for FR2 TRx test cases | ROHDE & SCHWARZ | withdrawn |  |  |
| R5-204275 | Corrections to Reference Sensitivity for CA | ROHDE & SCHWARZ | agreed |  |  |
| R5-204276 | Update of test point analysis for CA_3A-7B | ROHDE & SCHWARZ | agreed |  |  |
| R5-204277 | On FR2 EIRP OFF Power relaxation and measurement uncertainty | Keysight Technologies UK Ltd, Samsung | revised |  | R5-204741 |
| R5-204278 | FR2 EIRP OFF power MU updates | Keysight Technologies UK Ltd | revised |  | R5-204864 |
| R5-204279 | Updates to clauses 4.5A.3, 4.5A.30 | Qualcomm Incorporated | withdrawn |  |  |
| R5-204280 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | withdrawn |  |  |
| R5-204281 | FR2 EIRP OFF power measurement uncertainty | Keysight Technologies UK Ltd | revised |  | R5-204947 |
| R5-204282 | PC1 Assumptions for CDF Curve for MOP EIRP Spherical Coverage | Qualcomm Incorporated | noted |  |  |
| R5-204283 | Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy | Qualcomm Incorporated | revised |  | R5-204872 |
| R5-204284 | Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy | Qualcomm Incorporated | revised |  | R5-204873 |
| R5-204285 | Correction to Message Exceptions for 4.6.2.5 EN-DC FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection | Qualcomm Incorporated | agreed |  |  |
| R5-204286 | Correction to General Test Parameters for 6.6.2.5 NR SA FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection | Qualcomm Incorporated | withdrawn |  |  |
| R5-204287 | Correction to General Test Parameters for 6.6.2.2 NR SA FR1-FR1 event-triggered reporting in DRX | Qualcomm Incorporated | withdrawn |  |  |
| R5-204288 | Correction to General Test Parameters for 6.6.2.6 NR SA FR1-FR1 event-triggered reporting in DRX with SSB time index detection | Qualcomm Incorporated | withdrawn |  |  |
| R5-204289 | Correction to 6.3.1.1 NR SA FR1 handover with known target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204290 | Correction to 6.3.1.2 NR SA FR1 handover with unknown target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204291 | Correction to 6.3.1.3 NR SA FR1-FR1 handover with unknown target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204292 | New WID - UE Conformance Test Aspects for CLI handling for NR | Qualcomm Incorporated | revised |  | R5-204358 |
| R5-204293 | On Spurious measurement uncertainty | Keysight Technologies UK Ltd | revised |  | R5-204749 |
| R5-204294 | On OBW measurement uncertainty | Keysight Technologies UK Ltd | revised |  | R5-204850 |
| R5-204295 | Update of EMM test cases to handle IMS Re-registration | Qualcomm Incorporated | revised |  | R5-204524 |
| R5-204296 | Addition of test case 6.4B.2.4.1D | ROHDE & SCHWARZ | agreed |  |  |
| R5-204297 | Addition of test case 6.4B.2.4.2D | ROHDE & SCHWARZ | agreed |  |  |
| R5-204298 | Addition of test case 6.4B.2.4.3D | ROHDE & SCHWARZ | agreed |  |  |
| R5-204299 | Addition of test case 6.4B.2.4.4D | ROHDE & SCHWARZ | agreed |  |  |
| R5-204300 | Update of MDT test cases to handle IMS Re-registration | Qualcomm Incorporated | agreed |  |  |
| R5-204301 | Add new PICS | Qualcomm Incorporated | revised |  | R5-204904 |
| R5-204302 | Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | revised |  | R5-204874 |
| R5-204303 | Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | revised |  | R5-204875 |
| R5-204304 | Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | revised |  | R5-204876 |
| R5-204305 | Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | revised |  | R5-204877 |
| R5-204306 | Correction to 4.5.1.1 EN-DC FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204307 | Correction to 6.5.1.2 EN-DC RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204308 | Correction to 6.5.1.3 EN-DC FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204309 | Correction to 6.5.1.4 EN-DC FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | withdrawn |  |  |
| R5-204310 | Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC | Ericsson | agreed |  |  |
| R5-204311 | Addition of pending UL-MIMO tests (FR2) in Clause 6 | Qualcomm CDMA Technologies | revised |  | R5-204926 |
| R5-204312 | Addition of pending UL-MIMO tests (FR2) in Clause 7 | Qualcomm CDMA Technologies | withdrawn |  |  |
| R5-204313 | TS 38.521-3 Section 1-5 and Annex updates to align with core specification | Qualcomm CDMA Technologies | agreed |  |  |
| R5-204314 | Common updates across tests in Clause 6 | Qualcomm CDMA Technologies | withdrawn |  |  |
| R5-204315 | Common updates across tests in Clause 7 | Qualcomm CDMA Technologies | withdrawn |  |  |
| R5-204316 | Work Plan for TR 37.901-5 | Qualcomm CDMA Technologies | noted |  |  |
| R5-204317 | Status Report - Study on 5G NR UE Application Layer Data Throughput Performance | Qualcomm CDMA Technologies | noted |  |  |
| R5-204318 | Text Proposal to update Clause 5.5 - Test Environment | Qualcomm CDMA Technologies | agreed |  |  |
| R5-204319 | Text Proposal to update TC A.7.1.1.1 | Qualcomm CDMA Technologies | revised |  | R5-204894 |
| R5-204320 | Text Proposal to update TC A.9.1.1.1 | Qualcomm CDMA Technologies | revised |  | R5-204895 |
| R5-204321 | Text Proposal to update TC A.8.1 | Qualcomm CDMA Technologies | agreed |  |  |
| R5-204322 | Update for TC 7.5B.5 ACS for inter-band EN-DC including both FR1 and FR2 | CMCC | agreed |  |  |
| R5-204323 | Flexible handling multi PDUs and PDNs in the 5G test specifications | Samsung, MCC TF160 | noted | - | - |
| R5-204324 | Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections | Samsung | revised | - | R5-204399 |
| R5-204325 | Adding procedure for establishment of multiple additional PDN connections in EPS (S1 mode) | Samsung | agreed | - | - |
| R5-204326 | Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling | Samsung | revised | - | R5-204400 |
| R5-204327 | Updates to Test procedure for UE for Tracking area updating / Inter-system change from N1 mode to S1 mode in 5GMM/EMM-IDLE mode | Samsung | agreed | - | - |
| R5-204328 | Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Samsung | revised | - | R5-204401 |
| R5-204329 | Update of 4.5A.2 UE-requested PDU session establishment procedure | Samsung | agreed | - | - |
| R5-204330 | Updates Procedure to UE-requested PDU session modification after the first S1 to N1 mode change | Samsung | agreed | - | - |
| R5-204331 | Void 4.9.14 Procedure for UE-requested PDU session modification after the first S1 to N1 mode change | Samsung | agreed | - | - |
| R5-204332 | Adding new ICS for handling inter-system change S1-N1 and aligning PDN and PDU handling | Samsung | agreed | - | - |
| R5-204333 | Aligning the RRC specific message in TS 38.523-1 contents with the default messages in TS 38.508-1 | Samsung | noted | - | - |
| R5-204334 | Correction to NR5GC RRC test case 8.1.5.2.2 | Keysight Technologies UK | agreed | - | - |
| R5-204335 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | revised | - | R5-204959 |
| R5-204336 | Correction to test case 11.1.3 | MediaTek Inc. | agreed | - | - |
| R5-204337 | Addition of 4.5.5.0 minimum requirement for BFR | Huawei, HiSilicon | agreed | - | - |
| R5-204338 | Agenda - opening session | WG Chairman | approved | R5-203200 | - |
| R5-204339 | Correction to MDT test case 8.6.4.13 | CMCC | agreed | - | - |
| R5-204340 | Correction to MDT test case 8.6.8.8 | CMCC | agreed | - | - |
| R5-204341 | Correction to the NR5GC testcase 8.1.3.1.12 | ANRITSU LTD | agreed | - | - |
| R5-204342 | Correction to NR TC 9.1.5.1.14 | Qualcomm CDMA Technologies | revised | - | R5-204463 |
| R5-204343 | Corrections to NR5G NAS TC 9.1.6.1.3 | Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA | revised | - | R5-204464 |
| R5-204344 | TMC Integrity and Ciphering Protection | Apple | revised | - | R5-204402 |
| R5-204345 | Correction to 9.x test cases to handle IMS Re-registration (moving between HPLMN and VPLMN) | ROHDE & SCHWARZ, Qualcomm | agreed | - | - |
| R5-204346 | Introduction of test frequencies for Rel-16 NR band n259 | Ericsson | agreed | - | - |
| R5-204347 | Add Rx TC for 2Rel 16 DC combos | Qualcomm Austria RFFE GmbH, Bureau Veritas | revised | - | R5-204958 |
| R5-204348 | Adding signalling test frequency for 1A-38A | Huawei, HiSilicon | agreed | - | - |
| R5-204349 | Editorial correction of Rx spurious emissions for FR1 EN-DC | DOCOMO Communications Lab. | agreed | - | - |
| R5-204350 | MCC TF160 Status Report | MCC TF160 | approved | R5-203531 | - |
| R5-204351 | New WID on: UE Conformance Test Aspects - 410 – 430 MHz E-UTRA FDD Band(s) for LTE PPDR and PMR/PAMR in Europe (Bands 87 and 88) | Nokia, Nokia Shanghai Bell | endorsed | R5-203230 | - |
| R5-204352 | New WID on UE Conformance Test Aspects – B1C Signal in A-BDS Positioning System Support for LTE and NR | CATT, CMCC | endorsed | R5-203465 | - |
| R5-204353 | New WID on UE Conformance Test Aspects for SON and MDT support for NR | China Mobile Com. Corporation, Ericsson | endorsed | R5-203703 | - |
| R5-204354 | New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) | China Unicom, CMCC | endorsed | R5-203900 | - |
| R5-204355 | New WID on UE Conformance Test Aspects – Single Radio Voice Call Continuity from 5G to 3G | China Unicom | endorsed | R5-203901 | - |
| R5-204356 | New WID on UE Conformance Test Aspects for NR performance enhancement | Qualcomm Korea | endorsed | R5-203906 | - |
| R5-204357 | New WID on UE Conformance Test Aspects - Mission Critical Enhancements | NIST, Samsung | endorsed | R5-204231 | - |
| R5-204358 | New WID - UE Conformance Test Aspects for CLI handling for NR | Qualcomm Incorporated | endorsed | R5-204292 | - |
| R5-204359 | Correction to NR test case 8.1.4.1.6 | ZTE, MCC TF160 | agreed | - | - |
| R5-204360 | Correction to NR test case 8.1.4.16 | ZTE, MCC TF160 | withdrawn | R5-203712 | - |
| R5-204361 | LS on old unverified IMS test cases | TSG WG RAN5 | approved | - | - |
| R5-204362 | LS on two consecutive invalid challenges | TSG WG RAN5 | approved | - | - |
| R5-204363 | Corrections to NR5G PDCP TC 7.1.3.4.1 | Qualcomm CDMA Technologies | agreed | - | - |
| R5-204364 | Reply LS to LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level | TSG WG RAN5 | approved | - | - |
| R5-204365 | Added definition of RSAP and RSARP in 36.509 | Keysight Technologies UK Ltd | agreed | R5-203286 | - |
| R5-204366 | Discussion paper on tracking of 5GS protocol test cases Rel-16 and beyond | Ericsson | noted | R5-203613 | - |
| R5-204367 | TS 38.523-1 Status after RAN5#88-e | Samsung (Rapporteur) | noted | - | - |
| R5-204369 | Corrections to MCVideo and MCData tables | NIST | agreed | R5-204228 | - |
| R5-204370 | Update of test case applicability to Rel-14 | Samsung | agreed | - | - |
| R5-204371 | Update of content with Rel-14 requirements | Samsung | revised | - | R5-204492 |
| R5-204372 | Correction to NR5GC CA RRC test cases 8.1.2.1.5.x | Keysight Technologies UK | agreed | - | - |
| R5-204373 | Addition of UE capability for voiceFallbackIndicationEPS-r16 | CATT, TDIA | revised | - | R5-204511 |
| R5-204374 | On checking feature tags in REGISTER | ROHDE & SCHWARZ, Qualcomm Incorporated | agreed | - | - |
| R5-204375 | Critical prose CRs list for protocol test cases at RAN5#88-e | TSG WG RAN5 | reserved | - | - |
| R5-204376 | Status of Conformance testing development for Mission Critical Services (MCS) | TSG WG RAN5 | approved | - | - |
| R5-204377 | Updates to introduce support for MCVideo and MCData | NIST, MCC TF160 | agreed | - | - |
| R5-204378 | Correction to NR inter-band CA configurations in FR1 | MediaTek Inc. | agreed | R5-203588 | - |
| R5-204379 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | revised | R5-203591 | R5-204545 |
| R5-204380 | Correction to Idle mode test case 6.1.2.9 | MediaTek Inc. | agreed | R5-203593 | - |
| R5-204381 | Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1 | MediaTek Inc. | agreed | R5-203645 | - |
| R5-204382 | Correction to NR RRC TC 8.1.3.2.2 | MediaTek Inc. | agreed | R5-204106 | - |
| R5-204383 | LS on MCS group document subscription procedures | TSG WG RAN5 | for email approval | - | - |
| R5-204384 | Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Keysight Technologies UK, Huawei/HiSilicon | agreed | R5-203499 | - |
| R5-204385 | Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents | ANRITSU LTD | withdrawn | R5-204043 | - |
| R5-204386 | Correction to Table 4.6.1-17 RRCResume | Huawei, Hisilicon | agreed | R5-203358 | - |
| R5-204387 | Corrections to generic procedures for MO and MT speech call establishment | ROHDE & SCHWARZ | agreed | R5-203484 | - |
| R5-204388 | Correction to USIM configurations 7 and 13 | Keysight Technologies UK | agreed | R5-203497 | - |
| R5-204389 | Correction to switch off / power off procedures for IMS | Keysight Technologies UK Ltd, Qualcomm Incorporated | agreed | R5-203498 | - |
| R5-204390 | Correction of description of NGEN-DC in table 4.5.1-1 | Tejet | agreed | R5-203574 | - |
| R5-204391 | Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR | MediaTek Inc., Keysight Technologies | agreed | R5-203585 | - |
| R5-204392 | Addition of Generic Test Procedure for IMS MO SMS in 5GC | ZTE | agreed | R5-203715 | - |
| R5-204393 | Addition of Generic Test Procedure for IMS MT SMS in 5GC | ZTE | agreed | R5-203716 | - |
| R5-204394 | Update IE RLC-BearerConfig | Ericsson | agreed | R5-203743 | - |
| R5-204395 | Update IE SIB2 | Ericsson | agreed | R5-204134 | - |
| R5-204396 | New procedure for PDU Session Release | MCC TF160 | agreed | R5-204135 | - |
| R5-204397 | Update to FreqBandList | MCC TF160, Qualcomm, Anritsu | agreed | R5-204137 | - |
| R5-204398 | Update IE ServingCellConfigCommon | Ericsson | agreed | R5-204169 | - |
| R5-204399 | Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections | Samsung | agreed | R5-204324 | - |
| R5-204400 | Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling | Samsung | agreed | R5-204326 | - |
| R5-204401 | Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Samsung | agreed | R5-204328 | - |
| R5-204402 | TMC Integrity and Ciphering Protection | Apple | agreed | R5-204344 | - |
| R5-204403 | Correction to NR TC 6.1.1.2-access technology combinations | Huawei, Hisilicon | agreed | R5-203365 | - |
| R5-204404 | Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode | Huawei, Hisilicon | agreed | R5-203369 | - |
| R5-204405 | Correction to NR TC 6.1.2.19-Speed-dependent cell reselection | Huawei, Hisilicon, Keysight | agreed | R5-203371 | - |
| R5-204406 | Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode | Huawei, Hisilicon, Datang Linktester | agreed | R5-203376 | - |
| R5-204407 | Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1 | Huawei, Hisilicon, Datang Linktester | agreed | R5-203378 | - |
| R5-204408 | Correction to NR TC 6.3.1.2-SOR during registration with security check successful but no requested acknowledgement | Huawei, Hisilicon, Datang Linktester | agreed | R5-203379 | - |
| R5-204409 | Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received | Huawei, Hisilicon, Datang Linktester | agreed | R5-203381 | - |
| R5-204410 | Correction to Idle Mode SoR TC 6.3.1.7 | ZTE Corporation, Huawei, Hisilicon | agreed | R5-203429 | - |
| R5-204411 | Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration | Huawei, Hisilicon | agreed | R5-203478 | - |
| R5-204412 | Correction to NR TC 6.2.2.1-N2L cell reselection | Huawei, Hisilicon, Datang Linktester | agreed | R5-203565 | - |
| R5-204413 | Correction to NR TC 6.2.2.2-L2N cell reselection | Huawei, Hisilicon, Datang Linktester | agreed | R5-203566 | - |
| R5-204414 | Correction to the power level of Idle mode test cases | MediaTek Inc. | agreed | R5-203590 | - |
| R5-204415 | Corrections to NR5G Idle Mode TC 6.4.2.1 | Qualcomm CDMA Technologies | agreed | R5-203654 | - |
| R5-204416 | Corrections to NR5G Idle Mode TC 6.1.2.13 | Qualcomm CDMA Technologies | agreed | R5-203661 | - |
| R5-204417 | Correction to 5G NR Idle mode inter-RAT test cases | Keysight Technologies UK | agreed | R5-203746 | - |
| R5-204418 | Correction to NR TC 7.1.1.9.1-MAC Reset | Huawei, Hisilicon, Datang Linktester | agreed | R5-203386 | - |
| R5-204419 | Correction to NR TC 7.1.1.2.2-PDSCH Aggregation | Huawei, Hisilicon | agreed | R5-203387 | - |
| R5-204420 | Correction to NR MAC test case 7.1.1.5.2 | Keysight Technologies UK, Starpoint | agreed | R5-203513 | - |
| R5-204421 | Corrections to NR5G MAC TC 7.1.1.2.4 | Qualcomm CDMA Technologies | agreed | R5-203655 | - |
| R5-204422 | Corrections to NR5G MAC TC 7.1.1.1.2 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | agreed | R5-203660 | - |
| R5-204423 | Addition of NR-DC MAC Test Case | Lenovo, Motorola Mobility | agreed | R5-204206 | - |
| R5-204424 | Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN | Huawei, Hisilicon | withdrawn | R5-203388 | - |
| R5-204425 | Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4 | MCC TF160 | withdrawn | R5-203536 | - |
| R5-204426 | Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs | NTT DOCOMO INC. | agreed | R5-203596 | - |
| R5-204427 | Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath | NTT DOCOMO INC. | withdrawn | R5-203597 | - |
| R5-204428 | Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC | NTT DOCOMO INC. | withdrawn | R5-203598 | - |
| R5-204429 | Correction to NR test case 7.1.3.5.5 | ZTE | agreed | R5-203707 | - |
| R5-204430 | Update to test case NR5GC 7.1.3.5.3 (NR-DC) | ROHDE & SCHWARZ | agreed | R5-203749 | - |
| R5-204431 | Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2 | ROHDE & SCHWARZ, ZTE | agreed | R5-203750 | - |
| R5-204432 | Correction to NR TC 8.1.1.3.3-With priority information | Huawei, Hisilicon | agreed | R5-203390 | - |
| R5-204433 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | agreed | R5-203603 | - |
| R5-204434 | Correction to NR RRC IRAT test case 8.1.1.3.4 | Keysight Technologies UK | agreed | R5-203747 | - |
| R5-204435 | Correction to NR5GC testcase 8.1.1.3.2 | ROHDE & SCHWARZ, Qualcomm | agreed | R5-204029 | - |
| R5-204436 | Correction to NR5G RRC TC 8.1.1.4.1 | Qualcomm CDMA Technologies | agreed | R5-204236 | - |
| R5-204437 | Correction to NR TC 8.1.X on SINR related configuration | Huawei, Hisilicon | agreed | R5-203392 | - |
| R5-204438 | Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq | Huawei, Hisilicon | agreed | R5-203393 | - |
| R5-204439 | Correction to ENDC TC 8.2.2.6.1-PDCP version change | Huawei, Hisilicon, Starpoint | agreed | R5-203400 | - |
| R5-204440 | Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq | Huawei, Hisilicon | agreed | R5-203464 | - |
| R5-204441 | Addition of new test purpose to test case 8.1.3.1.23 | Tech Mahindra Limited | agreed | R5-203482 | - |
| R5-204442 | Correction to NR RRC test case 8.1.3.1.20 | Starpoint, TDIA | agreed | R5-203521 | - |
| R5-204443 | Correction to NR5GC test case 8.1.3.1.11 | Starpoint, Huawei, HiSilicon,TDIA | agreed | R5-203576 | - |
| R5-204444 | Correction to NR5GC test case 8.1.3.1.12 | Starpoint, Huawei, HiSilicon,TDIA | agreed | R5-203578 | - |
| R5-204445 | Addition of NR-DC RRC test case 8.2.2.8.2 | ANRITSU LTD | agreed | R5-203584 | - |
| R5-204446 | Correction to NR TC 8.1.4.1.7.X-Scell Release | Huawei, Hisilicon | agreed | R5-203395 | - |
| R5-204447 | Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements | Huawei, Hisilicon | agreed | R5-203401 | - |
| R5-204448 | Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements | Huawei, Hisilicon | agreed | R5-203402 | - |
| R5-204449 | Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting | Huawei, Hisilicon | agreed | R5-203404 | - |
| R5-204450 | Correction to include data path check after handover in test case 8.1.4.1.2 | Tech Mahindra Limited | agreed | R5-203483 | - |
| R5-204451 | Correction to Inter-RAT HO test case 8.1.4.2.2 | China Telecommunications | withdrawn | R5-203571 | - |
| R5-204452 | Correction to Inter-RAT HO test case 8.1.4.2.1 | China Telecommunications | agreed | R5-203592 | - |
| R5-204453 | Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1 | Qualcomm CDMA Technologies | agreed | R5-203664 | - |
| R5-204454 | Addition of NR-DC RRC test case 8.2.3.14.2 | ANRITSU LTD | agreed | R5-203814 | - |
| R5-204455 | Correction to MR-DC RRC TC 8.2.3.8.1 | MediaTek Inc. | agreed | R5-204133 | - |
| R5-204456 | Correction to NR RRC TC 8.1.5.1.1 | MediaTek Inc., Keysight Technologies | agreed | R5-203589 | - |
| R5-204457 | Correction to NR TC 9.1.1.3-EAP message transport abnormal | Huawei, Hisilicon | agreed | R5-203410 | - |
| R5-204458 | Correction to NR TC 9.1.1.6-5G AKA abnormal | Huawei, Hisilicon | agreed | R5-203411 | - |
| R5-204459 | Correction to 5GC TC 9.1.3.1 | MediaTek Inc. | agreed | R5-203737 | - |
| R5-204460 | Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area | Huawei, Hisilicon, Datang Linktester | agreed | R5-203414 | - |
| R5-204461 | Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers | Huawei, HiSilicon, Anritsu | agreed | R5-203415 | - |
| R5-204462 | Correction to 5GC TC 9.1.5.2.9 | MediaTek Inc. | agreed | R5-203702 | - |
| R5-204463 | Correction to NR TC 9.1.5.1.14 | Qualcomm CDMA Technologies | agreed | R5-204342 | - |
| R5-204464 | Corrections to NR5G NAS TC 9.1.6.1.3 | Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA | agreed | R5-204343 | - |
| R5-204465 | Correction to Multilayer TC 11.1.2 and 11.1.5 | MediaTek Inc. | agreed | R5-203752 | - |
| R5-204466 | Corrections to EPS Fallback regarding IMS procedures | ROHDE & SCHWARZ | agreed | R5-203996 | - |
| R5-204467 | Correction to test case 11.1.7 | MediaTek Inc. | agreed | R5-204091 | - |
| R5-204468 | Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category | Huawei, Hisilicon | agreed | R5-203416 | - |
| R5-204469 | Addition of applicability for NR TCs | Huawei, Hisilicon | agreed | R5-203417 | - |
| R5-204470 | Correction to applicability of NR TCs | Huawei, Hisilicon | agreed | R5-203418 | - |
| R5-204471 | Update of 5G-NR test cases applicability | Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility | agreed | R5-203475 | - |
| R5-204472 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | agreed | R5-203612 | - |
| R5-204473 | Removal of void test case and correction of condition for Inter-band measurements test cases | CAICT | agreed | R5-203890 | - |
| R5-204474 | Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1 | NTT DOCOMO INC. | withdrawn | R5-203899 | - |
| R5-204475 | 5G Test Models updates | MCC TF160, Keysight, Samsung | agreed | R5-203543 | - |
| R5-204476 | Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases | ROHDE & SCHWARZ | agreed | R5-203436 | - |
| R5-204477 | Addition of IMS NR TC 9.4-MT Concatenated SMS | Huawei, Hisilicon | agreed | R5-203423 | - |
| R5-204478 | Addition of IMS NR TC 9.5-MO SMS RP-ERROR | Huawei, Hisilicon | agreed | R5-203424 | - |
| R5-204479 | Addition of IMS NR TC 10.1-emergency call with registration and Location | Huawei, Hisilicon | agreed | R5-203425 | - |
| R5-204480 | Adding details for A.3 for IMS Emergency Registration | ROHDE & SCHWARZ | agreed | R5-203438 | - |
| R5-204481 | Corrections to test case 6.3 | ROHDE & SCHWARZ, MCC TF160 | agreed | R5-203444 | - |
| R5-204482 | Addition of new IMS 5GS test case 9.1 | ZTE | agreed | R5-203713 | - |
| R5-204483 | Addition of new IMS 5GS test case 9.2 | ZTE | agreed | R5-203714 | - |
| R5-204484 | New generic IMS procedures for use in EPS fallback | ROHDE & SCHWARZ | agreed | R5-204093 | - |
| R5-204485 | Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS | Qualcomm CDMA Technologies | agreed | R5-204240 | - |
| R5-204486 | Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS | Qualcomm CDMA Technologies | agreed | R5-204241 | - |
| R5-204487 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | agreed | R5-204251 | - |
| R5-204488 | Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | agreed | R5-203651 | - |
| R5-204489 | Adding measurement gaps for OTDOA configuration | ROHDE & SCHWARZ | agreed | R5-203273 | - |
| R5-204490 | MCVideo and MCData in Clause 5.5.7 | NIST | agreed | R5-204230 | - |
| R5-204491 | Updates to UE configuration document | NIST | agreed | R5-204234 | - |
| R5-204492 | Update of content with Rel-14 requirements | Samsung | agreed | R5-204371 | - |
| R5-204493 | PIXIT updates and table names | NIST | approved | R5-204232 | - |
| R5-204494 | Update of test description for DL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | agreed | R5-203923 | - |
| R5-204495 | Correction to test applicability for sTTI test cases | Huawei, Hisilicon | agreed | R5-203926 | - |
| R5-204496 | Update to Common contents of system information messages for NB_IOTenh2 | CATT, TDIA | agreed | R5-204012 | - |
| R5-204497 | Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection | TDIA, CATT | agreed | R5-204002 | - |
| R5-204498 | Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement | TDIA, CATT | agreed | R5-204004 | - |
| R5-204499 | Updates to IEs for Early Data Transmission test cases | Ericsson | agreed | R5-204140 | - |
| R5-204500 | Addition of new test case to test Paging with DRX and WUS in enhanced coverage | Tech Mahindra Limited | agreed | R5-203473 | - |
| R5-204501 | Addition of new test case to test Paging with eDRX and WUS in enhanced coverage | Tech Mahindra Limited | agreed | R5-203474 | - |
| R5-204502 | Addition of new test case to test CE-level based access barring | Tech Mahindra Limited | agreed | R5-203477 | - |
| R5-204503 | Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT | Ericsson | agreed | R5-204142 | - |
| R5-204504 | Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode | Tech Mahindra Limited | agreed | R5-203479 | - |
| R5-204505 | Addition of applicability for new test case to test CE-level based access barring | Tech Mahindra Limited | agreed | R5-203480 | - |
| R5-204506 | Addition of applicability for eMTC4 TC 23.2.4 | Ericsson | agreed | R5-204143 | - |
| R5-204507 | Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID | Ericsson | agreed | R5-203338 | - |
| R5-204508 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | agreed | R5-203354 | - |
| R5-204509 | Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16 | China Telecom | agreed | R5-203523 | - |
| R5-204510 | Add IE SSB-PositionQCL-Relation | Ericsson | agreed | R5-203556 | - |
| R5-204511 | Addition of UE capability for voiceFallbackIndicationEPS-r16 | CATT, TDIA | agreed | R5-204373 | - |
| R5-204512 | Corrections to NR5G RLC TC 7.1.2.3.11 | Qualcomm CDMA Technologies | agreed | R5-203663 | - |
| R5-204513 | Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC | China Telecom, Datang linktester | agreed | R5-203522 | - |
| R5-204514 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | withdrawn | R5-203611 | - |
| R5-204515 | Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | withdrawn | R5-203644 | - |
| R5-204516 | Introduction of a new test case for voice fallback indication under EPS Fallback with handover | CATT, TDIA | withdrawn | R5-203518 | - |
| R5-204517 | Introduction of a new test case for voice fallback indication under EPS Fallback with redirection | CATT, TDIA | agreed | R5-203519 | - |
| R5-204518 | Addition of NR5G UAC TC 11.3.2 | Qualcomm CDMA Technologies | agreed | R5-204239 | - |
| R5-204519 | Addition of test applicabilities of test cases for voice fallback indication | CATT, TDIA | agreed | R5-203520 | - |
| R5-204520 | Update applicability of Inter-RAT handover from NR to EN-DC test case | China Telecom,Datang linktester | agreed | R5-203599 | - |
| R5-204521 | Update the related RRC messages to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | agreed | R5-203605 | - |
| R5-204522 | Update of TC 9.2.1.1.28b | NTT DOCOMO INC. | agreed | R5-203586 | - |
| R5-204523 | Addition of new NAS test case to test handling of extended octets | NTT DOCOMO INC. | agreed | R5-203892 | - |
| R5-204524 | Update of EMM test cases to handle IMS Re-registration | Qualcomm Incorporated | agreed | R5-204295 | - |
| R5-204525 | Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register | Huawei, Hisilicon | agreed | R5-203427 | - |
| R5-204526 | Modification and editorial changes to NB-IoT TC 22.4.26 | NTT DOCOMO INC. | agreed | R5-203595 | - |
| R5-204527 | Correction to NB-IoT test case 22.4.5 | ROHDE & SCHWARZ | agreed | R5-203799 | - |
| R5-204528 | Updates to legacy TCs for feMTC | Ericsson | agreed | R5-204145 | - |
| R5-204529 | Updates to legacy TC applicability for feMTC | Ericsson | agreed | R5-204146 | - |
| R5-204530 | Correction to IMS TCs-wait for UE IMS de-register | Huawei, Hisilicon | agreed | R5-203426 | - |
| R5-204531 | Corrections of further XCAP test cases regarding rule elements | MCC TF160 | agreed | R5-203547 | - |
| R5-204532 | Addition of OTDOA information for pre-test conditions for test 9.3.3.1B | PCTEST Engineering Laboratory, LLC | agreed | R5-203512 | - |
| R5-204533 | New MCPTT Common Procedures for CT/CO session establishment | MCC TF160, UPV/EHU, Nemergent Solutions | agreed | R5-203548 | - |
| R5-204534 | Updates to MCX generic test procedures and default message contents | MCC TF160, UPV/EHU, Nemergent Solutions | agreed | R5-203549 | - |
| R5-204535 | Description of the distribution of MSCCK and MuSiK | UPV/EHU, Nemergent Solutions | agreed | R5-204096 | - |
| R5-204536 | Update to MCPTT Test Case 6.1.1.3 | MCC TF160 | agreed | R5-203550 | - |
| R5-204537 | Update to MCPTT Test Case 6.1.1.4 | MCC TF160 | agreed | R5-203551 | - |
| R5-204538 | Update to MCPTT Test Case 6.1.1.7 | MCC TF160 | agreed | R5-203552 | - |
| R5-204539 | Correction to MCPTT Test Case 6.1.1.8 | MCC TF160 | agreed | R5-203553 | - |
| R5-204540 | Integration of security features in MBMS procedures | UPV/EHU, NEMERGENT | agreed | R5-204097 | - |
| R5-204541 | Corrections to Chat Group Calls | NIST | agreed | R5-204227 | - |
| R5-204542 | WP UE Conformance Test Aspects - Rel-16 Optimisations on UE radio capability signalling – NR/E-UTRA | Qualcomm CDMA Technologies | noted | R5-204244 | - |
| R5-204543 | Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode | Huawei, Hisilicon, Datang Linktester, ZTE | agreed | R5-203380 | - |
| R5-204544 | Addition and update of PICS | Lenovo, Motorola Mobility | agreed | R5-204205 | - |
| R5-204545 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | agreed | R5-204379 | - |
| R5-204700 | Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A | Huawei, Hisilicon | withdrawn | R5-203937 | - |
| R5-204701 | Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1 | Huawei, Hisilicon | withdrawn | R5-203938 | - |
| R5-204702 | Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | withdrawn | R5-203944 | - |
| R5-204703 | Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | withdrawn | R5-203945 | - |
| R5-204704 | Adding the test frequency for DC_3A-7A_n78A | Huawei, Hisilicon | agreed | - | - |
| R5-204705 | Addition of test configuration for 71AA in 6.2B.1.1 MOP | Huawei, Hisilicon | agreed | - | - |
| R5-204706 | Adding the test frequency for DC_28A_n3A | Huawei, Hisilicon | withdrawn | - | - |
| R5-204707 | Addition of MOP testing for DC_28A_n3A in 6.2B.1.3 | Huawei, Hisilicon | agreed | - | - |
| R5-204708 | Updating indicator for SUL FR1 test cases | Huawei, Hisilicon | agreed | R5-203680 | - |
| R5-204709 | Update frequencyDomainResources and nrofcandidates | Huawei, Hisilicon | agreed | R5-203683 | - |
| R5-204710 | CR to 38.508-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | agreed | R5-204187 | - |
| R5-204711 | Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01 | Huawei, Hisilicon | agreed | R5-203674 | - |
| R5-204712 | Adding FR1 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | withdrawn | R5-203684 | - |
| R5-204713 | Correction to test configuration for Carrier leakage for CA | LG Electronics | agreed | R5-203718 | - |
| R5-204714 | Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA | LG Electronics | agreed | R5-203720 | - |
| R5-204715 | Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA | LG Electronics | agreed | R5-203722 | - |
| R5-204716 | Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA | LG Electronics | agreed | R5-203724 | - |
| R5-204717 | Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA | LG Electronics | agreed | R5-203727 | - |
| R5-204718 | Adding FR2 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | withdrawn | R5-203685 | - |
| R5-204719 | Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs | Qualcomm Austria RFFE GmbH | agreed | R5-204201 | - |
| R5-204720 | Add_TP_analysis_table for TX_spurious_emission | Qualcomm Austria RFFE GmbH | agreed | R5-204208 | - |
| R5-204721 | Discussion about proposals in LS R4-2005205 | Huawei, Hisilicon | noted | R5-203686 | - |
| R5-204722 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | revised | R5-203558 | R5-204980 |
| R5-204723 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | revised | R5-203560 | R5-204981 |
| R5-204724 | Updated to clause 6 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas, Ericsson | agreed | R5-203807 | - |
| R5-204725 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | revised | R5-203559 | R5-204982 |
| R5-204726 | Addition of test point analysis in Tx spurious emissions | Sporton, Ericsson | agreed | R5-203806 | - |
| R5-204727 | Updating TP analysis for 6.2A.2-MPR for CA | Huawei, Hisilicon | agreed | R5-203693 | - |
| R5-204728 | Update of test point analysis of MOP for intra-band contiguous EN-DC | Huawei, Hisilicon | agreed | R5-203939 | - |
| R5-204729 | WF on SA 2Tx and NSA PC2 | Huawei, Hisilicon | revised | - | R5-204954 |
| R5-204730 | Update of PDSCH RMC in Annex A.1.1 | MediaTek Inc. | agreed | R5-203757 | - |
| R5-204731 | Editorial update of Annex C.3.3.1 | MediaTek Inc. | agreed | R5-204026 | - |
| R5-204732 | Update release applicability of TC 9.2.2D | MediaTek Inc. | agreed | R5-204045 | - |
| R5-204733 | Correction of RRM Test Case 6.1.1.1 | MediaTek Inc. | agreed | R5-203820 | - |
| R5-204734 | Correction of RRM Test Case 6.1.1.2 | MediaTek Inc. | agreed | R5-203895 | - |
| R5-204735 | Correction of RRM Test Case 7.1.1.1 | MediaTek Inc. | agreed | R5-203896 | - |
| R5-204736 | Correction of RRM Test Case 7.1.1.2 | MediaTek Inc. | agreed | R5-203897 | - |
| R5-204737 | Quality of the Quiet Zone measurement results for enhanced IFF | ROHDE & SCHWARZ | noted | R5-203310 | - |
| R5-204738 | FR2 Demod MU due to finite test time | Qualcomm Korea | noted | R5-203669 | - |
| R5-204739 | Preliminary QoQZ and EIRP MU results for ETC testing | Keysight Technologies UK Ltd | noted | R5-204189 | - |
| R5-204740 | On FR2 Minimum Output Power relaxation and measurement uncertainty | Keysight Technologies UK Ltd | noted | R5-204253 | - |
| R5-204741 | On FR2 EIRP OFF Power relaxation and measurement uncertainty | Keysight Technologies UK Ltd, Samsung | noted | - | - |
| R5-204742 | Uncertainty assessment DL AWGN absolute power for enhanced IFF | ROHDE & SCHWARZ | noted | R5-203311 | - |
| R5-204743 | On ACS FR2 Measurement Uncertainty definition | Keysight Technologies UK Ltd | noted | R5-203485 | - |
| R5-204744 | On IBB FR2 Measurement Uncertainty definition | Keysight Technologies UK Ltd | noted | R5-203489 | - |
| R5-204745 | On FR2 DL absolute level uncertainty for DFF. | Anritsu | noted | R5-204082 | - |
| R5-204746 | Noise impact for FR2 test case where MPR applies | Anritsu | noted | R5-204086 | - |
| R5-204747 | On Larger Quiet Zone Sizes | Keysight Technologies UK Ltd | noted | R5-204191 | - |
| R5-204748 | On the AWGN flatness and signal flatness | ROHDE & SCHWARZ | noted | R5-204271 | - |
| R5-204749 | On Spurious measurement uncertainty | Keysight Technologies UK Ltd | noted | R5-204293 | - |
| R5-204750 | Updating test casees for several CA configurations | Huawei, HiSilicon | agreed | R5-203986 | - |
| R5-204751 | Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | agreed | R5-203631 | - |
| R5-204752 | Correction to TCI-state related configurations | Huawei, HiSilicon | agreed | R5-203864 | - |
| R5-204753 | Correction to CSI-RS related configurations | Huawei, HiSilicon | agreed | R5-203865 | - |
| R5-204754 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | agreed | R5-203999 | - |
| R5-204755 | Corrections of test frequency tables for CA_n258x | Ericsson | agreed | R5-204164 | - |
| R5-204756 | Corrections of test frequency tables for CA_n260x | Ericsson | agreed | R5-204165 | - |
| R5-204757 | Corrections of test frequency tables for CA_n261x | Ericsson | agreed | R5-204166 | - |
| R5-204758 | Add SSB subcarrier spacing configurations in RRM message contents | ROHDE & SCHWARZ | agreed | R5-204235 | - |
| R5-204759 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | agreed | R5-203974 | - |
| R5-204760 | Cleaning up of Tx inter-band CA test cases | Huawei, Hisilicon | agreed | R5-203677 | - |
| R5-204761 | Editorial correction to FR1 co-existence requirements | ROHDE & SCHWARZ | agreed | R5-204258 | - |
| R5-204762 | Update of clause5 into TS 38.521-1 R15 | China Unicom | agreed | R5-203283 | - |
| R5-204763 | Miscellaneous corrections due to core spec alignment | Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson | agreed | R5-203968 | - |
| R5-204764 | Update of Tx signal quality test cases | ROHDE & SCHWARZ | agreed | R5-204267 | - |
| R5-204765 | Addition of UL power setting for Rx test cases | Huawei, HiSilicon, CAICT | agreed | R5-203970 | - |
| R5-204766 | Spurious inter-band EN-DC FR2 UL MIMO test cases | Qualcomm Wireless GmbH | agreed | R5-203818 | - |
| R5-204767 | Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x | Huawei, Hisilicon | agreed | R5-203940 | - |
| R5-204768 | Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | agreed | R5-203946 | - |
| R5-204769 | Editorial correction to EN-DC co-existence requirements | ROHDE & SCHWARZ | agreed | R5-204259 | - |
| R5-204770 | FR2 RefSens inter-band EN-DC UL MIMO test cases | Qualcomm Wireless GmbH | agreed | R5-203817 | - |
| R5-204771 | Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1 | ZTE Corporation | agreed | R5-203910 | - |
| R5-204772 | Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO | Huawei, Hisilicon | agreed | R5-203943 | - |
| R5-204773 | Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | agreed | R5-204182 | - |
| R5-204774 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | revised | R5-203904 | R5-205009 |
| R5-204775 | Update TC 4.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203242 | - |
| R5-204776 | Update TC 4.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203244 | - |
| R5-204777 | Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap | ROHDE & SCHWARZ | agreed | R5-203274 | - |
| R5-204778 | Update TC 6.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203246 | - |
| R5-204779 | Update TC 6.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203248 | - |
| R5-204780 | Correction to the test procedure of NR SA event triggered tests | ROHDE & SCHWARZ | agreed | R5-203264 | - |
| R5-204781 | Correction to the test procedure of NR SA event triggered tests inter-freq | ROHDE & SCHWARZ | agreed | R5-203265 | - |
| R5-204782 | Correction to the test procedure of NR SA event triggered tests inter-RAT | ROHDE & SCHWARZ | agreed | R5-203266 | - |
| R5-204783 | Update TC 8.5.2.3.1 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203236 | - |
| R5-204784 | Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | agreed | R5-203251 | - |
| R5-204785 | Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values | ROHDE & SCHWARZ | agreed | R5-203316 | - |
| R5-204786 | Update of FR1 Test Tolerance in Annex F | Huawei, HiSilicon | agreed | R5-203854 | - |
| R5-204787 | Correction to default configurations in Annex H | Huawei, HiSilicon | agreed | R5-203862 | - |
| R5-204788 | Correction to the extreme conditions in TT analysis of 4.7.1.2.1 | ROHDE & SCHWARZ | agreed | R5-203305 | - |
| R5-204789 | Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | agreed | R5-203675 | - |
| R5-204790 | Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | agreed | R5-203676 | - |
| R5-204791 | Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203947 | - |
| R5-204792 | Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203948 | - |
| R5-204793 | Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203949 | - |
| R5-204794 | Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203950 | - |
| R5-204795 | Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203951 | - |
| R5-204796 | Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203952 | - |
| R5-204797 | Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations | Huawei, Hisilicon | agreed | R5-203961 | - |
| R5-204798 | Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time | Huawei, Hisilicon | agreed | R5-203934 | - |
| R5-204799 | Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time | Huawei, Hisilicon | agreed | R5-203935 | - |
| R5-204800 | Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1 | Nokia, Nokia Shanghai Bell | agreed | R5-203224 | - |
| R5-204801 | Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities | Nokia, Nokia Shanghai Bell | agreed | R5-203225 | - |
| R5-204802 | Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities | ZTE Corporation | agreed | R5-203913 | - |
| R5-204803 | Update of A.4.3.2B.2 for intra-band EN-DC capabilities | ZTE Corporation | agreed | R5-203915 | - |
| R5-204804 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities | ZTE Corporation | agreed | R5-203916 | - |
| R5-204805 | Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities | ZTE Corporation | agreed | R5-203918 | - |
| R5-204806 | Introduction of UE capabilities for Rel-16 EN-DC configurations | Bureau Veritas, Qualcomm Austria RFFE GmbH | agreed | R5-204153 | - |
| R5-204807 | Update of UE co-existence for CA_n1-n78 | China Unicom | agreed | R5-204131 | - |
| R5-204808 | Update of R16 CADC combos in TS 38.521-1 | China Unicom | agreed | R5-203285 | - |
| R5-204809 | Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | agreed | R5-203226 | - |
| R5-204810 | Editorial correction to spurious emission test case 6.5B.3.3.2 | Ericsson | agreed | R5-203636 | - |
| R5-204811 | Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | agreed | R5-203638 | - |
| R5-204812 | Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | agreed | R5-203639 | - |
| R5-204813 | Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | agreed | R5-203640 | - |
| R5-204814 | Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC | Huawei, Hisilicon | agreed | R5-203953 | - |
| R5-204815 | Updated to clause 6 for EN-DC Rel-16 configuration test requirement | Bureau Veritas, Qualcomm Austria RFFE GmbH | agreed | R5-204155 | - |
| R5-204816 | Updated to EN-DC Rel-16 Configuration information in clause 5 | Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson | agreed | R5-204152 | - |
| R5-204817 | Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203954 | - |
| R5-204818 | Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203955 | - |
| R5-204819 | Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203956 | - |
| R5-204820 | Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203957 | - |
| R5-204821 | Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203958 | - |
| R5-204822 | Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence | Huawei, Hisilicon | agreed | R5-203959 | - |
| R5-204823 | Correction of test frequencies for NS_47 | Ericsson, SoftBank Corp. | agreed | R5-203259 | - |
| R5-204824 | Adding band n48 to maximum output power and maximum output power reduction tests | Ericsson | agreed | R5-203262 | - |
| R5-204825 | Addition of 25MHz for NR band n1 | Huawei, HiSilicon | agreed | R5-203976 | - |
| R5-204826 | Addition of AMPR NS_48 for NR band n1 | Huawei, HiSilicon | agreed | R5-203977 | - |
| R5-204827 | Addition of n1 R16 new CBW into 38.521-1 Refsense test | China Unicom | agreed | R5-204129 | - |
| R5-204828 | Update of R16 new bands and CBWs in 38.521-1 | China Unicom, AT&T, Dish Network, CMCC | agreed | R5-203284 | - |
| R5-204829 | Addition of test point analysis for AMPR NS_48 | Huawei, HiSilicon | agreed | R5-203978 | - |
| R5-204830 | Updated to NB-IOT TC 6.3.5F.1 | Huawei, HiSilicon | agreed | R5-203981 | - |
| R5-204831 | Updated to test applicability for R15 NB-IoT requirement | Bureau Veritas | agreed | R5-204162 | - |
| R5-204832 | Introduce of new TC 6.3A.4.1 | Guangdong OPPO Mobile Telecom. | agreed | R5-203721 | - |
| R5-204833 | Introduce of new TC 6.3A.4.2 | Guangdong OPPO Mobile Telecom. | agreed | R5-203723 | - |
| R5-204834 | Introduce of new TC 6.3A.4.3 | Guangdong OPPO Mobile Telecom. | agreed | R5-203726 | - |
| R5-204835 | Add intra-band contiguous CA to 6.3A.1 | Guangdong OPPO Mobile Telecom. | agreed | R5-203734 | - |
| R5-204836 | Add intra-band contiguous CA to 6.3A.3 | Guangdong OPPO Mobile Telecom. | agreed | R5-203736 | - |
| R5-204837 | Adding band n48 for Blocking characteristics testing | Huawei, Hisilicon, Ericsson | agreed | R5-203699 | - |
| R5-204838 | Updating TP analysis for 6.2A.4-Configured output power for CA | Huawei, Hisilicon | agreed | R5-203695 | - |
| R5-204839 | Updated to FR1 general clauses for NRSL eV2X | Bureau Veritas | agreed | R5-204160 | - |
| R5-204840 | Updated to EN-DC general clauses for NRSL eV2X | Bureau Veritas | agreed | R5-204161 | - |
| R5-204841 | Cleaning up of V2X RB allocation for non-concurrent transmission | Huawei, HiSilicon | agreed | R5-203983 | - |
| R5-204842 | Cleaning up of V2X RB allocation for simultaneous transmission | Huawei, HiSilicon | agreed | R5-203984 | - |
| R5-204843 | Cleaning up of V2X RB allocation for multi-carrier operation | Huawei, HiSilicon | agreed | R5-203985 | - |
| R5-204844 | Editorial correction to 3DL CA test cases | TTA | revised | R5-203514 | R5-204983 |
| R5-204845 | Update of MOP test cases for EN-DC PC2 Rel-16 requirements | Huawei, HiSilicon | withdrawn | R5-203966 | - |
| R5-204846 | Discussion on DC_41C_n41A and DC_41D_n41A | ROHDE & SCHWARZ | noted | R5-204260 | - |
| R5-204847 | LS response on Multiband relaxation for FR2 on testability analysis of MBR | TSG WG RAN5 | for email approval | - | - |
| R5-204848 | Test Tolerance review process for FR2 RRM Test cases | ANRITSU LTD | noted | R5-203322 | - |
| R5-204849 | On FR2 OBW MU | Anritsu | noted | R5-204085 | - |
| R5-204850 | On OBW measurement uncertainty | Keysight Technologies UK Ltd | noted | R5-204294 | - |
| R5-204851 | Update of WF on Band n259 | DOCOMO Communications Lab. | noted | R5-203525 | - |
| R5-204852 | Jumbo CR for update to Demod message contents | Qualcomm Korea, Anritsu | revised | R5-203672 | R5-205007 |
| R5-204853 | Added UE Phy layer capabilitity into 38.508-2 from 38.306 | Keysight Technologies UK Ltd | agreed | R5-203288 | - |
| R5-204854 | Correct UE output power configuration to some UL MIMO cases | Guangdong OPPO Mobile Telecom, Orange | agreed | R5-203754 | - |
| R5-204855 | Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec | CAICT | agreed | R5-203876 | - |
| R5-204856 | CR to update MU and TT in 38.521-2 | Anritsu | agreed | R5-204056 | - |
| R5-204857 | Beam correspondence - SRS configuration corrections in section 6.6.1 | Keysight Technologies UK Ltd | agreed | R5-203581 | - |
| R5-204858 | CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps | Samsung R&D Institute UK | agreed | R5-204025 | - |
| R5-204859 | CR to TS 38.521-2: Correction to MB relaxation minimum requirements | Samsung R&D Institute UK | agreed | R5-204044 | - |
| R5-204860 | CR to 38.521-2 to adjust the test step sequences | Keysight Technologies UK Ltd | agreed | R5-204185 | - |
| R5-204861 | CR to 38.521-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | agreed | R5-204188 | - |
| R5-204862 | CR to 38.521-2 on QoQZ Verification Clarification | Keysight Technologies UK Ltd | agreed | R5-204193 | - |
| R5-204863 | FR2 Minimum output power MU updates | Keysight Technologies UK Ltd | agreed | R5-204255 | - |
| R5-204864 | FR2 EIRP OFF power MU updates | Keysight Technologies UK Ltd | agreed | R5-204278 | - |
| R5-204865 | Beam correspondence - SRS configuration corrections in annex K.1.1 | Keysight Technologies UK Ltd | agreed | R5-203580 | - |
| R5-204866 | CR to update MU and TT in 38.521-3 | Anritsu | agreed | R5-204060 | - |
| R5-204867 | Update for 6.5B.3.3.2 Spurious emission band UE co-existence | Qualcomm Austria RFFE GmbH | agreed | R5-204207 | - |
| R5-204868 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | withdrawn | R5-204256 | - |
| R5-204869 | Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3 | Keysight Technologies UK Ltd | agreed | R5-203488 | - |
| R5-204870 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | revised | R5-203903 | R5-205008 |
| R5-204871 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | revised | R5-203905 | R5-205010 |
| R5-204872 | Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy | Qualcomm Incorporated | agreed | R5-204283 | - |
| R5-204873 | Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy | Qualcomm Incorporated | agreed | R5-204284 | - |
| R5-204874 | Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | agreed | R5-204302 | - |
| R5-204875 | Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | agreed | R5-204303 | - |
| R5-204876 | Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | agreed | R5-204304 | - |
| R5-204877 | Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | agreed | R5-204305 | - |
| R5-204878 | Update TC 4.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203241 | - |
| R5-204879 | Update TC 4.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203243 | - |
| R5-204880 | Update TC 6.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203245 | - |
| R5-204881 | Update TC 6.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | agreed | R5-203247 | - |
| R5-204882 | Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133 | Keysight Technologies UK Ltd, Qualcomm Incorporated | agreed | R5-203302 | - |
| R5-204883 | Test Procedure correction in test case 6.5.1.3 for definition of Point C | Keysight Technologies UK Ltd | agreed | R5-203318 | - |
| R5-204884 | Addition of new RRM Test Cases in clause 7.5.5 | ZTE Corporation | agreed | R5-203431 | - |
| R5-204885 | CR to update the RRM FR2 MUs in Annex F | ROHDE & SCHWARZ | agreed | R5-203314 | - |
| R5-204886 | Add information on the AoA change during test for RRM FR2 tests | ROHDE & SCHWARZ | agreed | R5-203315 | - |
| R5-204887 | CR to update the DL AWGN absolute power for RRM test cases | ROHDE & SCHWARZ | agreed | R5-203313 | - |
| R5-204888 | Adjacent Channel Selectivity FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | agreed | R5-203486 | - |
| R5-204889 | In-band Blocking FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | agreed | R5-203490 | - |
| R5-204890 | CR to update MU in 38.903 | Anritsu, Keysight Technologies | agreed | R5-204080 | - |
| R5-204891 | FR2 Minimum output power measurement uncertainty | Keysight Technologies UK Ltd | agreed | R5-204257 | - |
| R5-204892 | Update of test tolerance for demodulation performance in sTTI test cases | Huawei, Hisilicon | agreed | R5-203929 | - |
| R5-204893 | Addition of acceptable uncertainty and test tolerance for sTTI test cases | Huawei, Hisilicon | agreed | R5-203931 | - |
| R5-204894 | Text Proposal to update TC A.7.1.1.1 | Qualcomm CDMA Technologies | agreed | R5-204319 | - |
| R5-204895 | Text Proposal to update TC A.9.1.1.1 | Qualcomm CDMA Technologies | agreed | R5-204320 | - |
| R5-204896 | Addition of test frequencies for n28 with CBW of 30MHz | CMCC, CBN, Ericsson | agreed | R5-203337 | - |
| R5-204897 | Update to 7.5A.2 ACS for 3DL CA | Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH | agreed | R5-203530 | - |
| R5-204898 | Update of NR test case 7.5A Adjacent Channel selectivity for CA | Samsung R&D Institute UK | agreed | R5-204037 | - |
| R5-204899 | Adding default value for IE rbg-Size for demodulation and CSI reporting tests | Ericsson | agreed | R5-203764 | - |
| R5-204900 | Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs | CAICT | agreed | R5-203888 | - |
| R5-204901 | Correction to message configuration for performance tests | Anritsu | agreed | R5-204050 | - |
| R5-204902 | Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities | Keysight Technologies UK Ltd | agreed | R5-203289 | - |
| R5-204903 | Introduction and correction of general capabilities and some band-combo information for EN-DC | CAICT | agreed | R5-203887 | - |
| R5-204904 | Add new PICS | Qualcomm Incorporated | agreed | R5-204301 | - |
| R5-204905 | Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2 | CAICT | agreed | R5-203882 | - |
| R5-204906 | Correction of test requirement for 6.2.4 | CAICT | agreed | R5-203883 | - |
| R5-204907 | Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04 | CAICT | agreed | R5-203884 | - |
| R5-204908 | Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4 | CAICT | agreed | R5-203886 | - |
| R5-204909 | Update of 6.2.3 for minimum conformance requirements for A-MPR | ZTE Corporation | agreed | R5-203909 | - |
| R5-204910 | Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec | CAICT | agreed | R5-203877 | - |
| R5-204911 | Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4 | CAICT | agreed | R5-203878 | - |
| R5-204912 | Update of SA Rx test cases for 4Rx UEs | Huawei, HiSilicon | agreed | R5-203962 | - |
| R5-204913 | Update Uplink power control window size for SA RX TCs | Qualcomm Austria RFFE GmbH | agreed | R5-204204 | - |
| R5-204914 | Updates to test case 6.3.4.3, relative power tolerance | Ericsson | agreed | R5-203766 | - |
| R5-204915 | CR to 38.521-2 to update Transmit OFF Power | Samsung R&D Institute UK | agreed | R5-204030 | - |
| R5-204916 | CR to TS 38.521-2: Correction to time mask requirements | Samsung R&D Institute UK | agreed | R5-204031 | - |
| R5-204917 | Clean up complete status for FR2 SA test cases | Anritsu | agreed | R5-204055 | - |
| R5-204918 | Update to UE maximum output power for CA | Anritsu | agreed | R5-204057 | - |
| R5-204919 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | agreed | R5-204247 | - |
| R5-204920 | FR2 RefSens and EIS spherical PC3 MBR table update | Qualcomm Wireless GmbH | agreed | R5-203816 | - |
| R5-204921 | Addition of modified MPR behavior | Huawei, HiSilicon | agreed | R5-203971 | - |
| R5-204922 | CR to TS 38.521-2: Annex F EIRP OFF Power | Samsung R&D Institute UK | agreed | R5-204033 | - |
| R5-204923 | CR to TS 38.521-2 on DUT alignment options | ROHDE & SCHWARZ | agreed | R5-204203 | - |
| R5-204924 | Update of Test applicability for some Inter-Band EN-DC including FR2 TCs | CAICT | agreed | R5-203870 | - |
| R5-204925 | Clean up complete status for EN-DC test cases | Anritsu | agreed | R5-204058 | - |
| R5-204926 | Addition of pending UL-MIMO tests (FR2) in Clause 6 | Qualcomm CDMA Technologies | agreed | R5-204311 | - |
| R5-204927 | Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | withdrawn | R5-203871 | - |
| R5-204928 | Update of NSA Rx test cases for 4Rx UEs | Huawei, HiSilicon | agreed | R5-203963 | - |
| R5-204929 | Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC | CMCC | agreed | R5-204173 | - |
| R5-204930 | Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | agreed | R5-204184 | - |
| R5-204931 | Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs | Qualcomm Austria RFFE GmbH | agreed | R5-204197 | - |
| R5-204932 | Re-organization of EN-DC refsens test cases | Ericsson | agreed | R5-204215 | - |
| R5-204933 | CR to update MU and TT in 38.521-4 | Anritsu | agreed | R5-204065 | - |
| R5-204934 | Correction to frequencyDomainAllocation | Anritsu | agreed | R5-204061 | - |
| R5-204935 | Correction to MU and TT for FR1 PMI and RI tests | Anritsu | agreed | R5-204066 | - |
| R5-204936 | Update to FR2 PDSCH test case | Qualcomm Korea | revised | R5-203673 | R5-205011 |
| R5-204937 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | revised | R5-203668 | R5-205012 |
| R5-204938 | Update of AWGN flatness in TS 38.521-4 | ROHDE & SCHWARZ | agreed | R5-204273 | - |
| R5-204939 | TP for TS 38.522 | CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm | agreed | R5-203330 | - |
| R5-204940 | Correction of 38.522 | CAICT | agreed | R5-203869 | - |
| R5-204941 | Correction to connection diagram for radio link monitoring tests | Anritsu | agreed | R5-204074 | - |
| R5-204942 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2 | Ericsson | agreed | R5-204117 | - |
| R5-204943 | Correction of FR2 condition tables in Annex B | Ericsson | agreed | R5-204120 | - |
| R5-204944 | Introduction of band n259 in clause 3 | Ericsson | agreed | R5-204121 | - |
| R5-204945 | CR to 38.903 on some of the Transmit OFF power MU parameters | Samsung R&D Institute UK | agreed | R5-204028 | - |
| R5-204946 | Update of AWGN flatness in TR 38.903 | ROHDE & SCHWARZ | agreed | R5-204272 | - |
| R5-204947 | FR2 EIRP OFF power measurement uncertainty | Keysight Technologies UK Ltd | agreed | R5-204281 | - |
| R5-204948 | Addition of Test Point analysis for FR2 Transmit OFF Power for CA | DOCOMO Communications Lab. | agreed | R5-204147 | - |
| R5-204949 | TP analysis 6.5B.3 TX SpurEmission EN-DC V2 | Qualcomm Austria RFFE GmbH | agreed | R5-204196 | - |
| R5-204950 | Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1 | Ericsson | agreed | R5-204216 | - |
| R5-204951 | Discussion on Scope, Purpose and drafting guideline for 38.522 | CAICT | noted | R5-203868 | - |
| R5-204952 | Review on FR1 TRx test point analysis for Extreme Condition | DOCOMO Communications Lab. | noted | R5-204136 | - |
| R5-204953 | Discussion on EN-DC reference sensitivity test case structure | Ericsson | noted | R5-204214 | - |
| R5-204954 | WF on SA 2Tx and NSA PC2 | Huawei, Hisilicon | noted | R5-204729 | - |
| R5-204955 | Discussion on measurement uncertainty for sTTI test cases | Huawei, Hisilicon | noted | R5-203932 | - |
| R5-204956 | Updated to clause 7 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas | withdrawn | R5-203808 | - |
| R5-204957 | Updated to clause 7 for EN-DC Rel-16 configuration test requirement | Bureau Veritas | agreed | R5-204156 | - |
| R5-204958 | Add Rx TC for 2Rel 16 DC combos | Qualcomm Austria RFFE GmbH | agreed | R5-204347 | - |
| R5-204959 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | agreed | R5-204335 | - |
| R5-204960 | Addition of test cases for n28 with CBW of 30MHz | CMCC, CBN, Huawei, HiSilicon, Orange | agreed | R5-203336 | - |
| R5-204961 | n26 Rx requirements in 38.521-1 | Dish Network | agreed | R5-203282 | - |
| R5-204962 | Update of NR test case 7.6.2 UE IBB for n30 | AT&T, DISH Network, CAICT, Ericsson, HiSilicon | agreed | R5-203787 | - |
| R5-204963 | Update test point analysis for A-MPR NS_18 with CBW being 30MHz | CMCC, Huawei, HiSilicon | agreed | R5-203797 | - |
| R5-204964 | Addition of test point analysis for additional spurious emission with NS_17 | Huawei, Orange, CMCC | agreed | R5-204023 | - |
| R5-204965 | Updated to NB-IOT TC 6.3.5F.3 | Huawei, HiSilicon | agreed | R5-203982 | - |
| R5-204966 | Updates to IEs for RF eMTC TCs | Ericsson | agreed | R5-204141 | - |
| R5-204967 | Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | agreed | R5-203784 | - |
| R5-204968 | Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | agreed | R5-203790 | - |
| R5-204969 | Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | agreed | R5-203791 | - |
| R5-204970 | Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | agreed | R5-203792 | - |
| R5-204971 | Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1 | Ericsson | agreed | R5-204003 | - |
| R5-204972 | Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1 | Ericsson | agreed | R5-204013 | - |
| R5-204973 | Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1 | Ericsson | agreed | R5-204014 | - |
| R5-204974 | Updating of NR test case 6.2A.4-Configured output power for CA | Huawei, Hisilicon | agreed | R5-203694 | - |
| R5-204975 | WF of V2X RF testing | Huawei, HiSilicon | noted | R5-203980 | - |
| R5-204976 | Correction of UE Category 1bis test case applicability | CMCC | agreed | R5-203334 | - |
| R5-204977 | Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3 | Google Inc. | agreed | R5-203921 | - |
| R5-204978 | Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance | Ericsson | agreed | R5-204108 | - |
| R5-204979 | Clarification on frequency band test conditions for A-GNSS | Qualcomm Incorporated | agreed | R5-204020 | - |
| R5-204980 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | agreed | R5-204722 | - |
| R5-204981 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | agreed | R5-204723 | - |
| R5-204982 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | agreed | R5-204725 | - |
| R5-204983 | Editorial correction to 3DL CA test cases | TTA | agreed | R5-204844 | - |
| R5-204984 | Update of NR test case 6.2A.2-MPR for CA | Huawei, Hisilicon | agreed | R5-203692 | - |
| R5-204985 | Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | agreed | R5-203828 | - |
| R5-204986 | Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | agreed | R5-203829 | - |
| R5-204987 | Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance | Huawei, HiSilicon, CAICT | agreed | R5-203830 | - |
| R5-204988 | Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon, CAICT | agreed | R5-203831 | - |
| R5-204989 | Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch | Huawei, HiSilicon | agreed | R5-203833 | - |
| R5-204990 | Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell | Huawei, HiSilicon | agreed | R5-203834 | - |
| R5-204991 | Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | agreed | R5-203836 | - |
| R5-204992 | Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | agreed | R5-203843 | - |
| R5-204993 | Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | agreed | R5-203844 | - |
| R5-204994 | Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX | Huawei, HiSilicon | agreed | R5-203845 | - |
| R5-204995 | Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon | agreed | R5-203846 | - |
| R5-204996 | Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell | Huawei, HiSilicon | agreed | R5-203848 | - |
| R5-204997 | Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance | Huawei, HiSilicon | agreed | R5-203849 | - |
| R5-204998 | Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | agreed | R5-203851 | - |
| R5-204999 | Update of test parameters in 6.3.1.4 inter-RAT handover | Huawei, HiSilicon | agreed | R5-203852 | - |
| R5-205000 | Update of default configurations for RMC scheduling in Annex A | Huawei, HiSilicon | agreed | R5-203856 | - |
| R5-205001 | Addition of FR1 Test tolerance analysis for DCI based BWP switch | Huawei, HiSilicon | agreed | R5-203821 | - |
| R5-205002 | Addition of FR1 Test tolerance analysis for RRC based BWP switch | Huawei, HiSilicon | agreed | R5-203822 | - |
| R5-205003 | Addition of FR1 Test tolerance analysis for SSB based BFR | Huawei, HiSilicon | agreed | R5-203823 | - |
| R5-205004 | Addition of FR1 Test tolerance analysis for CSI-RS based BFR | Huawei, HiSilicon | agreed | R5-203824 | - |
| R5-205005 | Update of OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | agreed | - | - |
| R5-205006 | Update Refsense exceptions for EN-DC including n78 | Rohde & Schwarz | agreed | R5-204102 | - |
| R5-205007 | Jumbo CR for update to Demod message contents | Qualcomm Korea, Anritsu | agreed | R5-204852 | - |
| R5-205008 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | agreed | R5-204870 | - |
| R5-205009 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | agreed | R5-204774 | - |
| R5-205010 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | agreed | R5-204871 | - |
| R5-205011 | Update to FR2 PDSCH test case | Qualcomm Korea | agreed | R5-204936 | - |
| R5-205012 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | agreed | R5-204937 | - |

### A2: Tdoc decision timing

-

## Annex B: List of change requests

1444 CRs and final revisions at RAN5#88-e (646 intermediate not shown)

| Document | Title | Source | Spec | CR | Rev | Rel | Cat | WI | Decision |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| R5-204045 | Update release applicability of TC 9.2.2D | MediaTek Inc. | 34.121-2 | 0178 | - | Rel-15 | F | TEI6_Test | revised |
| R5-204732 | Update release applicability of TC 9.2.2D | MediaTek Inc. | 34.121-2 | 0178 | 1 | Rel-15 | F | TEI6_Test | agreed |
| R5-203426 | Correction to IMS TCs-wait for UE IMS de-register | Huawei, Hisilicon | 34.229-1 | 1436 | - | Rel-15 | F | TEI9_Test | revised |
| R5-204530 | Correction to IMS TCs-wait for UE IMS de-register | Huawei, Hisilicon | 34.229-1 | 1436 | 1 | Rel-15 | F | TEI9_Test | agreed |
| R5-203430 | Adding check to REGISTER regarding nonce-count | ROHDE & SCHWARZ, MCC TF160 | 34.229-1 | 1437 | - | Rel-15 | F | TEI8_Test | agreed |
| R5-203432 | Correction to A.1.2 regarding WWW-Authenticate | ROHDE & SCHWARZ | 34.229-1 | 1438 | - | Rel-15 | F | TEI8_Test | agreed |
| R5-203433 | Extending default message for NOTIFY to cover de-registration scenarios | ROHDE & SCHWARZ | 34.229-1 | 1439 | - | Rel-15 | F | TEI8_Test | agreed |
| R5-203434 | Adding cross-references to TS 34.229-5 | ROHDE & SCHWARZ | 34.229-1 | 1440 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203435 | Removing 5G content | ROHDE & SCHWARZ | 34.229-1 | 1441 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203547 | Corrections of further XCAP test cases regarding rule elements | MCC TF160 | 34.229-1 | 1442 | - | Rel-15 | F | TEI8_Test | revised |
| R5-204531 | Corrections of further XCAP test cases regarding rule elements | MCC TF160 | 34.229-1 | 1442 | 1 | Rel-15 | F | TEI8_Test | agreed |
| R5-204374 | On checking feature tags in REGISTER | ROHDE & SCHWARZ, Qualcomm Incorporated | 34.229-1 | 1443 | - | Rel-15 | F | TEI8_Test | agreed |
| R5-203436 | Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases | ROHDE & SCHWARZ | 34.229-2 | 0271 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204476 | Extending TS 34.229-2 to host applicabilities for 5GS IMS test cases | ROHDE & SCHWARZ | 34.229-2 | 0271 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203544 | IMS over NR/5GC: Misc updates | MCC TF160, ROHDE & SCHWARZ | 34.229-3 | 0631 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203423 | Addition of IMS NR TC 9.4-MT Concatenated SMS | Huawei, Hisilicon | 34.229-5 | 0001 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204477 | Addition of IMS NR TC 9.4-MT Concatenated SMS | Huawei, Hisilicon | 34.229-5 | 0001 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203424 | Addition of IMS NR TC 9.5-MO SMS RP-ERROR | Huawei, Hisilicon | 34.229-5 | 0002 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204478 | Addition of IMS NR TC 9.5-MO SMS RP-ERROR | Huawei, Hisilicon | 34.229-5 | 0002 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203425 | Addition of IMS NR TC 10.1-emergency call with registration and Location | Huawei, Hisilicon | 34.229-5 | 0003 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204479 | Addition of IMS NR TC 10.1-emergency call with registration and Location | Huawei, Hisilicon | 34.229-5 | 0003 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203437 | Corrections to A.2 on IMS Registration | ROHDE & SCHWARZ | 34.229-5 | 0004 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203438 | Adding details for A.3 for IMS Emergency Registration | ROHDE & SCHWARZ | 34.229-5 | 0005 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204480 | Adding details for A.3 for IMS Emergency Registration | ROHDE & SCHWARZ | 34.229-5 | 0005 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203439 | New generic procedure for MT Call Release | ROHDE & SCHWARZ | 34.229-5 | 0006 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203440 | Adding references as needed | ROHDE & SCHWARZ | 34.229-5 | 0007 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203441 | Corrections to test cases 7.6 and 7.7 | ROHDE & SCHWARZ | 34.229-5 | 0008 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203442 | Corrections to test case 6.1 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0009 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203443 | Corrections to test case 6.2 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0010 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203444 | Corrections to test case 6.3 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0011 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204481 | Corrections to test case 6.3 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0011 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203445 | Corrections to test case 6.4 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0012 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203447 | Corrections to test case 6.5 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0013 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203448 | Corrections to test case 6.6 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0014 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203452 | Corrections to test case 6.7 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0015 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203453 | Corrections to test case 6.8 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0016 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203454 | Corrections to test case 6.9 | ROHDE & SCHWARZ, MCC TF160 | 34.229-5 | 0017 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203461 | Corrections to MTSI MT Voice Call TC 7.6 | ZTE Corporation | 34.229-5 | 0018 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203462 | Corrections to Annex A.5.1 | ZTE Corporation | 34.229-5 | 0019 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203713 | Addition of new IMS 5GS test case 9.1 | ZTE | 34.229-5 | 0020 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204482 | Addition of new IMS 5GS test case 9.1 | ZTE | 34.229-5 | 0020 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203714 | Addition of new IMS 5GS test case 9.2 | ZTE | 34.229-5 | 0021 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204483 | Addition of new IMS 5GS test case 9.2 | ZTE | 34.229-5 | 0021 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204093 | New generic IMS procedures for use in EPS fallback | ROHDE & SCHWARZ | 34.229-5 | 0022 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204484 | New generic IMS procedures for use in EPS fallback | ROHDE & SCHWARZ | 34.229-5 | 0022 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204240 | Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS | Qualcomm CDMA Technologies | 34.229-5 | 0023 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204485 | Addition of NR TC 8.18 Barring of All Incoming Calls / except for a specific user / 5GS | Qualcomm CDMA Technologies | 34.229-5 | 0023 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204241 | Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS | Qualcomm CDMA Technologies | 34.229-5 | 0024 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204486 | Addition of NR TC 9.3 Mobile Originating Concatenated SMS / 5GS | Qualcomm CDMA Technologies | 34.229-5 | 0024 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204248 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | 34.229-5 | 0025 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204251 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | 34.229-5 | 0026 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204487 | Addition of new IMS test case 8.1 | Qualcomm Incorporated | 34.229-5 | 0026 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203494 | Update to ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST message | Keysight Technologies UK | 36.508 | 1322 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203495 | Correction to USIM content for eCall over IMS test cases | Keysight Technologies UK | 36.508 | 1323 | - | Rel-16 | F | TEI14_Test | agreed |
| R5-203605 | Update the related RRC messages to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | 36.508 | 1324 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204521 | Update the related RRC messages to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | 36.508 | 1324 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203651 | Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 36.508 | 1325 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204488 | Corrections to Default contents of ACTIVATE DEFAULT EPS BEARER CONTEXT REQUEST MESSAGE for S1 to N1 mode | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 36.508 | 1325 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203922 | Update of common test environment for short TTI and short processing time TCs | Huawei, Hisilicon | 36.508 | 1326 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203989 | Adding signalling test frequency for 3A-41A | Huawei, HiSilicon | 36.508 | 1327 | - | Rel-16 | F | LTE_CA_R14-UEConTest | withdrawn |
| R5-204012 | Update to Common contents of system information messages for NB_IOTenh2 | CATT, TDIA | 36.508 | 1328 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204496 | Update to Common contents of system information messages for NB_IOTenh2 | CATT, TDIA | 36.508 | 1328 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-204140 | Updates to IEs for Early Data Transmission test cases | Ericsson | 36.508 | 1329 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204499 | Updates to IEs for Early Data Transmission test cases | Ericsson | 36.508 | 1329 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204141 | Updates to IEs for RF eMTC TCs | Ericsson | 36.508 | 1330 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204966 | Updates to IEs for RF eMTC TCs | Ericsson | 36.508 | 1330 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204279 | Updates to clauses 4.5A.3, 4.5A.30 | Qualcomm Incorporated | 36.508 | 1331 | - | Rel-16 | F | TEI8_Test | withdrawn |
| R5-204348 | Adding signalling test frequency for 1A-38A | Huawei, HiSilicon | 36.508 | 1332 | - | Rel-16 | F | LTE_CA_R14-UEConTest | agreed |
| R5-203286 | Added definition of RSAP and RSARP in 36.509 | Keysight Technologies UK Ltd | 36.509 | 0207 | - | Rel-15 | F | TEI15_Test | revised |
| R5-204365 | Added definition of RSAP and RSARP in 36.509 | Keysight Technologies UK Ltd | 36.509 | 0207 | 1 | Rel-15 | F | TEI15_Test | agreed |
| R5-203228 | Introduction of PC2 UE for cat M1/M2 in LTE Bands 31 and 72 | Nokia, Nokia Shanghai Bell | 36.521-1 | 5138 | - | Rel-16 | B | LTE_PC2_B31_B72-UEConTest | agreed |
| R5-203335 | Addition of B34 into UE Category 1bis and update B41 UE Category 1bis | CMCC | 36.521-1 | 5139 | - | Rel-16 | F | TEI14_Test | agreed |
| R5-203514 | Editorial correction to 3DL CA test cases | TTA | 36.521-1 | 5140 | - | Rel-16 | F | TEI13_Test, LTE_CA_Rel13-UEConTest | revised |
| R5-204844 | Editorial correction to 3DL CA test cases | TTA | 36.521-1 | 5140 | 1 | Rel-16 | F | TEI13_Test, LTE_CA_Rel13-UEConTest | revised |
| R5-204983 | Editorial correction to 3DL CA test cases | TTA | 36.521-1 | 5140 | 2 | Rel-16 | F | TEI13_Test, LTE_CA_Rel13-UEConTest | agreed |
| R5-203561 | Introduction of new TC 7.6.1A.9 In-band blocking for 6DL CA | Tejet , SRTC | 36.521-1 | 5141 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203562 | Introduction of new TC 7.6.2A.9 Out-of-band blocking for 6DL CA | Tejet , SRTC | 36.521-1 | 5142 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203563 | Introduction of new TC 7.6.3A.9 Narrow band blocking for 6DL CA | Tejet , SRTC | 36.521-1 | 5143 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203564 | Introduction of new TC 7.7A.9 Spurious response for 6DL CA | Tejet , SRTC | 36.521-1 | 5144 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203570 | Update of Annex F.1.3 and 3.3 for 6DL blocking and spurious response TCs | Tejet , SRTC | 36.521-1 | 5145 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203600 | Introduction of TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell | LG Electronics | 36.521-1 | 5146 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203601 | Introduction of TDD FDD 7 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell | LG Electronics | 36.521-1 | 5147 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203602 | Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for FDD PCell | LG Electronics | 36.521-1 | 5148 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203604 | Update to TDD FDD 6 DL CA PDSCH Closed Loop Multi Layer Spatial Multiplexing 4x2 for TDD PCell | LG Electronics | 36.521-1 | 5149 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203606 | Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for FDD PCell | LG Electronics | 36.521-1 | 5150 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203607 | Update to TDD FDD 7 DL CA PDSCH Open Loop Spatial Multiplexing 2x2 for TDD PCell | LG Electronics | 36.521-1 | 5151 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203608 | Update to TDD FDD 7 DL CA Single Antenna Port Performance for FDD PCell | LG Electronics | 36.521-1 | 5152 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203609 | Update to TDD FDD 7 DL CA Single Antenna Port Performance for TDD PCell | LG Electronics | 36.521-1 | 5153 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203738 | Cleanup in test case 7.3EC, Reference sensitivity level for UE category M2 | Ericsson | 36.521-1 | 5154 | - | Rel-16 | F | TEI14_Test | agreed |
| R5-203775 | Updating test case applicability for CSI test cases | Ericsson | 36.521-1 | 5155 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203776 | Adding test case applicability rules | Ericsson | 36.521-1 | 5156 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203779 | Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.1.3.1 | Ericsson | 36.521-1 | 5157 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203782 | Adding tests for CRS muting, 64QAM and 200Hz doppler spread to test case 8.11.1.2.3.1 | Ericsson | 36.521-1 | 5158 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203784 | Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | 36.521-1 | 5159 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204967 | Addition of test case 9.8.3.1 FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | 36.521-1 | 5159 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203790 | Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | 36.521-1 | 5160 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204968 | Addition of test case 9.8.3.2 TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and 64QAM | Ericsson | 36.521-1 | 5160 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203791 | Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | 36.521-1 | 5161 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204969 | Addition of test case 9.8.4.1 FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | 36.521-1 | 5161 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203792 | Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | 36.521-1 | 5162 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204970 | Addition of test case 9.8.4.2TDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table | Ericsson | 36.521-1 | 5162 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203857 | Update of Test Tolerance for HPUE | Huawei, HiSilicon | 36.521-1 | 5163 | - | Rel-16 | F | LTE_TDD_HPUE_R15-UEConTest | agreed |
| R5-203858 | Update of MOP for HPUE | Huawei, HiSilicon | 36.521-1 | 5164 | - | Rel-16 | F | LTE_TDD_HPUE_R15-UEConTest | agreed |
| R5-203859 | Update of MPR for HPUE | Huawei, HiSilicon | 36.521-1 | 5165 | - | Rel-16 | F | LTE_TDD_HPUE_R15-UEConTest | agreed |
| R5-203927 | Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-1 | Huawei, Hisilicon | 36.521-1 | 5166 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203928 | Update of message contents and test tolerance for transmitted power in sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5167 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203929 | Update of test tolerance for demodulation performance in sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5168 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204892 | Update of test tolerance for demodulation performance in sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5168 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203930 | Update of test tolerance for CSI reporting in sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5169 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203931 | Addition of acceptable uncertainty and test tolerance for sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5170 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204893 | Addition of acceptable uncertainty and test tolerance for sTTI test cases | Huawei, Hisilicon | 36.521-1 | 5170 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203981 | Updated to NB-IOT TC 6.3.5F.1 | Huawei, HiSilicon | 36.521-1 | 5171 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204830 | Updated to NB-IOT TC 6.3.5F.1 | Huawei, HiSilicon | 36.521-1 | 5171 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203982 | Updated to NB-IOT TC 6.3.5F.3 | Huawei, HiSilicon | 36.521-1 | 5172 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204965 | Updated to NB-IOT TC 6.3.5F.3 | Huawei, HiSilicon | 36.521-1 | 5172 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203983 | Cleaning up of V2X RB allocation for non-concurrent transmission | Huawei, HiSilicon | 36.521-1 | 5173 | - | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | revised |
| R5-204841 | Cleaning up of V2X RB allocation for non-concurrent transmission | Huawei, HiSilicon | 36.521-1 | 5173 | 1 | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | agreed |
| R5-203984 | Cleaning up of V2X RB allocation for simultaneous transmission | Huawei, HiSilicon | 36.521-1 | 5174 | - | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | revised |
| R5-204842 | Cleaning up of V2X RB allocation for simultaneous transmission | Huawei, HiSilicon | 36.521-1 | 5174 | 1 | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | agreed |
| R5-203985 | Cleaning up of V2X RB allocation for multi-carrier operation | Huawei, HiSilicon | 36.521-1 | 5175 | - | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | revised |
| R5-204843 | Cleaning up of V2X RB allocation for multi-carrier operation | Huawei, HiSilicon | 36.521-1 | 5175 | 1 | Rel-16 | F | TEI14_Test, LTE_V2X-UEConTest | agreed |
| R5-203986 | Updating test casees for several CA configurations | Huawei, HiSilicon | 36.521-1 | 5176 | - | Rel-16 | F | LTE_CA_R14-UEConTest | revised |
| R5-204750 | Updating test casees for several CA configurations | Huawei, HiSilicon | 36.521-1 | 5176 | 1 | Rel-16 | F | LTE_CA_R14-UEConTest | agreed |
| R5-204001 | Annex F based on updated Tx test cases for efeMTC | Ericsson | 36.521-1 | 5177 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204003 | Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1 | Ericsson | 36.521-1 | 5178 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204971 | Adding sub PRB allocation to 6.5.2.3EA, In-band emissions for non allocated RB for UE category M1 | Ericsson | 36.521-1 | 5178 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204005 | Adding PC6 to 6.3.5EA.1, Power Control Absolute power tolerance for UE category M1 | Ericsson | 36.521-1 | 5179 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204007 | Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1 | Ericsson | 36.521-1 | 5180 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204011 | Adding PC6 to 6.2.5EA, Configured UE transmitted Power for UE category M1 | Ericsson | 36.521-1 | 5181 | - | Rel-16 | F | LTE_eMTC4-UEConTest | withdrawn |
| R5-204013 | Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1 | Ericsson | 36.521-1 | 5182 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204972 | Adding PC6 to 6.2.2EA, UE Maximum Output Power for UE category M1 | Ericsson | 36.521-1 | 5182 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204014 | Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1 | Ericsson | 36.521-1 | 5183 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204973 | Adding PC6 to 6.2.3EA, Maximum Power Reduction (MPR) for UE category M1 | Ericsson | 36.521-1 | 5183 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204017 | Adding PC6 to 6.3.5EA.2, Power Control Relative power tolerance for UE category M1 | Ericsson | 36.521-1 | 5184 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204157 | Correction to RF NB-IoT test cases | Bureau Veritas | 36.521-1 | 5185 | - | Rel-16 | F | TEI13_Test | agreed |
| R5-204162 | Updated to test applicability for R15 NB-IoT requirement | Bureau Veritas | 36.521-1 | 5186 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204831 | Updated to test applicability for R15 NB-IoT requirement | Bureau Veritas | 36.521-1 | 5186 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-204275 | Corrections to Reference Sensitivity for CA | ROHDE & SCHWARZ | 36.521-1 | 5187 | - | Rel-16 | F | TEI13_Test, LTE_CA_Rel13-UEConTest | agreed |
| R5-203229 | Introduction of Baseline Implementation Capabilities for PC2 in LTE Bands 31 and 72 | Nokia, Nokia Shanghai Bell | 36.521-2 | 0917 | - | Rel-16 | B | LTE_PC2_B31_B72-UEConTest | agreed |
| R5-203334 | Correction of UE Category 1bis test case applicability | CMCC | 36.521-2 | 0918 | - | Rel-16 | F | TEI14_Test | revised |
| R5-204976 | Correction of UE Category 1bis test case applicability | CMCC | 36.521-2 | 0918 | 1 | Rel-16 | F | TEI14_Test | agreed |
| R5-203573 | Addition of applicability for newly introduced 6DL TCs | Tejet , SRTC | 36.521-2 | 0919 | - | Rel-16 | F | LTE_CA_R15-UEConTest | agreed |
| R5-203744 | Editorial correcting of format for table headings | Ericsson | 36.521-2 | 0920 | - | Rel-16 | F | TEI14_Test | agreed |
| R5-203773 | Adding applicability for new efeMTC test cases 9.8.3.1, 9.8.3.2, 9.8.4.1, 9.8.4.2 | Ericsson | 36.521-2 | 0921 | - | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203804 | Update additional information for test applicability for NB-IoT Test cases | Sporton | 36.521-2 | 0922 | - | Rel-16 | F | NB_IOTenh2-UEConTest | withdrawn |
| R5-203860 | Update of capability for HPUE | Huawei, HiSilicon | 36.521-2 | 0923 | - | Rel-16 | F | LTE_TDD_HPUE_R15-UEConTest | agreed |
| R5-203889 | Adding branch of PC3 and HPUE for 6.6.2.1 and 6.6.2.2 in Table 4.1-1 | CAICT | 36.521-2 | 0924 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-203921 | Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3 | Google Inc. | 36.521-2 | 0925 | - | Rel-16 | F | TEI10_Test | revised |
| R5-204977 | Correction title and description of 6.2.3A.1_3 and 6.2.4A.1_3 | Google Inc. | 36.521-2 | 0925 | 1 | Rel-16 | F | TEI10_Test | agreed |
| R5-204000 | Correction Additional Information in Table 4.2-1 of test case 9.2.56 and 9.2.57 | Google Inc. | 36.521-2 | 0926 | - | Rel-16 | F | TEI11_Test | agreed |
| R5-204159 | Correction to applicability table of NB-IoT tests | Bureau Veritas | 36.521-2 | 0927 | - | Rel-16 | F | TEI13_Test | agreed |
| R5-204163 | Updated to applicability table of R15 NB-IoT tests | Bureau Veritas | 36.521-2 | 0928 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203800 | Addition of 6.1.23 NB-IOT TDD Inter-frequency RRC Re-establishment in In-Band mode under normal coverage | Sporton | 36.521-3 | 2516 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203801 | Addition of 6.1.24 NB-IOT TDD - TDD Intra-frequency RRC Re-establishment in In-Band mode under enhanced coverage | Sporton | 36.521-3 | 2517 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203802 | Addition of 6.2.19 NB-IOT TDD Contention Based Random Access Test in normal coverage | Sporton | 36.521-3 | 2518 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203803 | Addition of 6.2.20 NB-IOT TDD Contention Based Random Access Test in enhanced coverage | Sporton | 36.521-3 | 2519 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-203933 | Addition of sTTI related definitions, symbols and abbreviations to TS 36.521-3 | Huawei, Hisilicon | 36.521-3 | 2520 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203934 | Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time | Huawei, Hisilicon | 36.521-3 | 2521 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204798 | Addition of new test case 7.2.13 E-UTRAN FDD Timing Advance Adjustment Delay Test for sTTI and short processing time | Huawei, Hisilicon | 36.521-3 | 2521 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203935 | Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time | Huawei, Hisilicon | 36.521-3 | 2522 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204799 | Addition of new test case 7.2.14 E-UTRAN TDD Timing Advance Adjustment Accuracy Test for sTTI and short processing time | Huawei, Hisilicon | 36.521-3 | 2522 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203936 | Addition of downlink RMC configuration with sTTI | Huawei, Hisilicon | 36.521-3 | 2523 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203997 | Correction Test applicability of test case 9.2.56 and 9.2.57 | Google Inc. | 36.521-3 | 2524 | - | Rel-16 | F | TEI11_Test | agreed |
| R5-204024 | Correction of Table 9.2.18.1.3-2 and Table 9.2.18.2.3-2 | Google Inc. | 36.521-3 | 2525 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-204026 | Editorial update of Annex C.3.3.1 | MediaTek Inc. | 36.521-3 | 2526 | - | Rel-16 | F | TEI10_Test | revised |
| R5-204731 | Editorial update of Annex C.3.3.1 | MediaTek Inc. | 36.521-3 | 2526 | 1 | Rel-16 | F | TEI10_Test | agreed |
| R5-204047 | Correction to intra-frequency event triggered reporting test case in CEModeA | Anritsu | 36.521-3 | 2527 | - | Rel-16 | F | TEI13_Test, LTE_MTCe2_L1-UEConTest | agreed |
| R5-204048 | Correction to E-UTRAN HD-FDD Radio Link Monitoring Test for Out-of-sync in DRX for CE UE in CEmodeA | Anritsu | 36.521-3 | 2528 | - | Rel-16 | F | TEI13_Test, LTE_MTCe2_L1-UEConTest | agreed |
| R5-204108 | Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance | Ericsson | 36.521-3 | 2529 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | revised |
| R5-204978 | Correction of RRM feMTC Test Case 5.1.28 including Test Tolerance | Ericsson | 36.521-3 | 2529 | 1 | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204109 | Correction of RRM feMTC Test Case 5.1.34 including Test Tolerance | Ericsson | 36.521-3 | 2530 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204110 | Correction of RRM feMTC Test Case 6.1.18 including Test Tolerance | Ericsson | 36.521-3 | 2531 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204111 | Correction of RRM feMTC Test Case 7.3.69 including Test Tolerance | Ericsson | 36.521-3 | 2532 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204112 | Correction of RRM feMTC Test Cases 8.4.12 - 15 including Test Tolerance | Ericsson | 36.521-3 | 2533 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204113 | Test Tolerances for RRM feMTC Test Cases in Annex F | Ericsson | 36.521-3 | 2534 | - | Rel-16 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204158 | Correction to test applicability of NB-IoT RRM tests | Bureau Veritas | 36.521-3 | 2535 | - | Rel-16 | F | TEI13_Test | agreed |
| R5-203427 | Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register | Huawei, Hisilicon | 36.523-1 | 4936 | - | Rel-16 | F | TEI9_Test | revised |
| R5-204525 | Correction to EPC IMS TC 13.1.19-wait for UE IMS de-register | Huawei, Hisilicon | 36.523-1 | 4936 | 1 | Rel-16 | F | TEI9_Test | agreed |
| R5-203473 | Addition of new test case to test Paging with DRX and WUS in enhanced coverage | Tech Mahindra Limited | 36.523-1 | 4937 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204500 | Addition of new test case to test Paging with DRX and WUS in enhanced coverage | Tech Mahindra Limited | 36.523-1 | 4937 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203474 | Addition of new test case to test Paging with eDRX and WUS in enhanced coverage | Tech Mahindra Limited | 36.523-1 | 4938 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204501 | Addition of new test case to test Paging with eDRX and WUS in enhanced coverage | Tech Mahindra Limited | 36.523-1 | 4938 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203477 | Addition of new test case to test CE-level based access barring | Tech Mahindra Limited | 36.523-1 | 4939 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204502 | Addition of new test case to test CE-level based access barring | Tech Mahindra Limited | 36.523-1 | 4939 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203493 | Updates to EMM test cases to handle IMS Re-registration | Keysight Technologies UK | 36.523-1 | 4940 | - | Rel-16 | F | TEI8_Test | not pursued |
| R5-203545 | Correction to SC-PTM test case 21.2.1 | MCC TF160 | 36.523-1 | 4941 | - | Rel-16 | F | TEI13_Test, LTE_SC_PTM-UEConTest | agreed |
| R5-203586 | Update of TC 9.2.1.1.28b | NTT DOCOMO INC. | 36.523-1 | 4942 | - | Rel-16 | F | TEI8_Test | revised |
| R5-204522 | Update of TC 9.2.1.1.28b | NTT DOCOMO INC. | 36.523-1 | 4942 | 1 | Rel-16 | F | TEI8_Test | agreed |
| R5-203595 | Modification and editorial changes to NB-IoT TC 22.4.26 | NTT DOCOMO INC. | 36.523-1 | 4943 | - | Rel-16 | F | TEI13_Test, NB_IOT-UEConTest | revised |
| R5-204526 | Modification and editorial changes to NB-IoT TC 22.4.26 | NTT DOCOMO INC. | 36.523-1 | 4943 | 1 | Rel-16 | F | TEI13_Test, NB_IOT-UEConTest | agreed |
| R5-203799 | Correction to NB-IoT test case 22.4.5 | ROHDE & SCHWARZ | 36.523-1 | 4944 | - | Rel-16 | F | TEI13_Test, NB_IOT-UEConTest | revised |
| R5-204527 | Correction to NB-IoT test case 22.4.5 | ROHDE & SCHWARZ | 36.523-1 | 4944 | 1 | Rel-16 | F | TEI13_Test, NB_IOT-UEConTest | agreed |
| R5-203809 | Correction to RRC measurement testcase 8.3.1.11 for measGapConfig for CAT-M1 | ANRITSU LTD | 36.523-1 | 4945 | - | Rel-16 | F | TEI13_Test, LTE_MTCe2_L1-UEConTest | agreed |
| R5-203812 | Correction RRC idle mode test cases 6.1.1.x | ANRITSU LTD | 36.523-1 | 4946 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-203892 | Addition of new NAS test case to test handling of extended octets | NTT DOCOMO INC. | 36.523-1 | 4947 | - | Rel-16 | F | TEI8_Test | revised |
| R5-204523 | Addition of new NAS test case to test handling of extended octets | NTT DOCOMO INC. | 36.523-1 | 4947 | 1 | Rel-16 | F | TEI8_Test | agreed |
| R5-203923 | Update of test description for DL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | 36.523-1 | 4948 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204494 | Update of test description for DL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | 36.523-1 | 4948 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203924 | Update of message contents for UL transmission test cases for sTTI and short processing time | Huawei, Hisilicon | 36.523-1 | 4949 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-203925 | Correction to derivation path for SRS transmission test cases for sTTI and short processing time | Huawei, Hisilicon | 36.523-1 | 4950 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-204002 | Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection | TDIA, CATT | 36.523-1 | 4951 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204497 | Addition of NB-IoT R15 testcase 22.3.2.8 NB-IoT / UM RLC / Correct use of sequence numbering / Concatenation, segmentation and reassembly / Duplicate detection | TDIA, CATT | 36.523-1 | 4951 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-204004 | Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement | TDIA, CATT | 36.523-1 | 4952 | - | Rel-16 | F | NB_IOTenh2-UEConTest | revised |
| R5-204498 | Addition of NB-IoT R15 testcase 22.4.27 NB-IoT / RRC connection establishment / Access barring enhancement | TDIA, CATT | 36.523-1 | 4952 | 1 | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-204142 | Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT | Ericsson | 36.523-1 | 4953 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204503 | Addition of new TC 23.2.4 CIoT Optimization / User Plane / EDT | Ericsson | 36.523-1 | 4953 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204145 | Updates to legacy TCs for feMTC | Ericsson | 36.523-1 | 4954 | - | Rel-16 | F | TEI14_Test, LTE_feMTC-UEConTest | revised |
| R5-204528 | Updates to legacy TCs for feMTC | Ericsson | 36.523-1 | 4954 | 1 | Rel-16 | F | TEI14_Test, LTE_feMTC-UEConTest | agreed |
| R5-204252 | Editorial update to EMM test case 9.2.1.1.7b | Qualcomm Incorporated | 36.523-1 | 4955 | - | Rel-16 | F | TEI10_Test | agreed |
| R5-204295 | Update of EMM test cases to handle IMS Re-registration | Qualcomm Incorporated | 36.523-1 | 4956 | - | Rel-16 | F | TEI8_Test | revised |
| R5-204524 | Update of EMM test cases to handle IMS Re-registration | Qualcomm Incorporated | 36.523-1 | 4956 | 1 | Rel-16 | F | TEI8_Test | agreed |
| R5-204300 | Update of MDT test cases to handle IMS Re-registration | Qualcomm Incorporated | 36.523-1 | 4957 | - | Rel-16 | F | TEI11_Test | agreed |
| R5-204339 | Correction to MDT test case 8.6.4.13 | CMCC | 36.523-1 | 4958 | - | Rel-16 | F | TEI15_Test, LTE_MDT_BT_WLAN-UEConTest | agreed |
| R5-204340 | Correction to MDT test case 8.6.8.8 | CMCC | 36.523-1 | 4959 | - | Rel-16 | F | TEI15_Test, LTE_MDT_BT_WLAN-UEConTest | agreed |
| R5-204345 | Correction to 9.x test cases to handle IMS Re-registration (moving between HPLMN and VPLMN) | ROHDE & SCHWARZ, Qualcomm | 36.523-1 | 4960 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-203479 | Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode | Tech Mahindra Limited | 36.523-2 | 1313 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204504 | Addition of Applicability for new test cases to test Paging with WUS in enhanced coverage in Idle mode | Tech Mahindra Limited | 36.523-2 | 1313 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203480 | Addition of applicability for new test case to test CE-level based access barring | Tech Mahindra Limited | 36.523-2 | 1314 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204505 | Addition of applicability for new test case to test CE-level based access barring | Tech Mahindra Limited | 36.523-2 | 1314 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-203583 | Updates to TC execution guidance | MCC TF160 | 36.523-2 | 1315 | - | Rel-16 | F | TEI10_Test | agreed |
| R5-203861 | Update of capability for 6.1.2.5a cell re-selection for HPUE | Huawei, HiSilicon | 36.523-2 | 1316 | - | Rel-16 | F | LTE_TDD_HPUE_R15-UEConTest | agreed |
| R5-203898 | Test applicability for new NAS TC 9.2.1.1.31 | NTT DOCOMO INC. | 36.523-2 | 1317 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-203926 | Correction to test applicability for sTTI test cases | Huawei, Hisilicon | 36.523-2 | 1318 | - | Rel-16 | F | LTE_sTTIandPT-UEConTest | revised |
| R5-204495 | Correction to test applicability for sTTI test cases | Huawei, Hisilicon | 36.523-2 | 1318 | 1 | Rel-16 | F | LTE_sTTIandPT-UEConTest | agreed |
| R5-204006 | Update of test applicabilities for NB_IOTenh2 | CATT, TDIA | 36.523-2 | 1319 | - | Rel-16 | F | NB_IOTenh2-UEConTest | agreed |
| R5-204143 | Addition of applicability for eMTC4 TC 23.2.4 | Ericsson | 36.523-2 | 1320 | - | Rel-16 | F | LTE_eMTC4-UEConTest | revised |
| R5-204506 | Addition of applicability for eMTC4 TC 23.2.4 | Ericsson | 36.523-2 | 1320 | 1 | Rel-16 | F | LTE_eMTC4-UEConTest | agreed |
| R5-204146 | Updates to legacy TC applicability for feMTC | Ericsson | 36.523-2 | 1321 | - | Rel-16 | F | TEI14_Test, LTE_feMTC-UEConTest | revised |
| R5-204529 | Updates to legacy TC applicability for feMTC | Ericsson | 36.523-2 | 1321 | 1 | Rel-16 | F | TEI14_Test, LTE_feMTC-UEConTest | agreed |
| R5-203496 | Correction to postamble procedures to handle multi-PDN EN-DC devices | Keysight Technologies UK, Samsung | 36.523-3 | 4526 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203546 | Routine maintenance for TS 36.523-3 | MCC TF160, Bureau Veritas | 36.523-3 | 4527 | - | Rel-16 | F | TEI8_Test | agreed |
| R5-203548 | New MCPTT Common Procedures for CT/CO session establishment | MCC TF160, UPV/EHU, Nemergent Solutions | 36.579-1 | 0078 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204533 | New MCPTT Common Procedures for CT/CO session establishment | MCC TF160, UPV/EHU, Nemergent Solutions | 36.579-1 | 0078 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-203549 | Updates to MCX generic test procedures and default message contents | MCC TF160, UPV/EHU, Nemergent Solutions | 36.579-1 | 0079 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204534 | Updates to MCX generic test procedures and default message contents | MCC TF160, UPV/EHU, Nemergent Solutions | 36.579-1 | 0079 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204095 | Group Communications Key download mechanism | NEMERGENT | 36.579-1 | 0080 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | withdrawn |
| R5-204096 | Description of the distribution of MSCCK and MuSiK | UPV/EHU, Nemergent Solutions | 36.579-1 | 0081 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204535 | Description of the distribution of MSCCK and MuSiK | UPV/EHU, Nemergent Solutions | 36.579-1 | 0081 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204226 | Addition of XML schema for MCVideo location information | NIST | 36.579-1 | 0082 | - | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-204229 | MCVideo and MCData in Clause 4 | NIST | 36.579-1 | 0083 | - | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-204230 | MCVideo and MCData in Clause 5.5.7 | NIST | 36.579-1 | 0084 | - | Rel-14 | F | MCImp-UEConTest | revised |
| R5-204490 | MCVideo and MCData in Clause 5.5.7 | NIST | 36.579-1 | 0084 | 1 | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-204234 | Updates to UE configuration document | NIST | 36.579-1 | 0085 | - | Rel-14 | F | MCImp-UEConTest | revised |
| R5-204491 | Updates to UE configuration document | NIST | 36.579-1 | 0085 | 1 | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-204371 | Update of content with Rel-14 requirements | Samsung | 36.579-1 | 0086 | - | Rel-14 | F | MCImp-UEConTest | revised |
| R5-204492 | Update of content with Rel-14 requirements | Samsung | 36.579-1 | 0086 | 1 | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-203550 | Update to MCPTT Test Case 6.1.1.3 | MCC TF160 | 36.579-2 | 0089 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204536 | Update to MCPTT Test Case 6.1.1.3 | MCC TF160 | 36.579-2 | 0089 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-203551 | Update to MCPTT Test Case 6.1.1.4 | MCC TF160 | 36.579-2 | 0090 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204537 | Update to MCPTT Test Case 6.1.1.4 | MCC TF160 | 36.579-2 | 0090 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-203552 | Update to MCPTT Test Case 6.1.1.7 | MCC TF160 | 36.579-2 | 0091 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204538 | Update to MCPTT Test Case 6.1.1.7 | MCC TF160 | 36.579-2 | 0091 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-203553 | Correction to MCPTT Test Case 6.1.1.8 | MCC TF160 | 36.579-2 | 0092 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204539 | Correction to MCPTT Test Case 6.1.1.8 | MCC TF160 | 36.579-2 | 0092 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204097 | Integration of security features in MBMS procedures | UPV/EHU, NEMERGENT | 36.579-2 | 0093 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204540 | Integration of security features in MBMS procedures | UPV/EHU, NEMERGENT | 36.579-2 | 0093 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204227 | Corrections to Chat Group Calls | NIST | 36.579-2 | 0094 | - | Rel-14 | F | TEI13_Test, MCPTT-ConTest | revised |
| R5-204541 | Corrections to Chat Group Calls | NIST | 36.579-2 | 0094 | 1 | Rel-14 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204228 | Corrections to MCVideo and MCData tables | NIST | 36.579-4 | 0010 | - | Rel-14 | F | MCImp-UEConTest | revised |
| R5-204369 | Corrections to MCVideo and MCData tables | NIST | 36.579-4 | 0010 | 1 | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-204370 | Update of test case applicability to Rel-14 | Samsung | 36.579-4 | 0011 | - | Rel-14 | F | MCImp-UEConTest | agreed |
| R5-203554 | Routine maintenance for TS 36.579-5 | MCC TF160, UPV/EHU, Nemergent Solutions | 36.579-5 | 0008 | - | Rel-13 | F | TEI13_Test, MCPTT-ConTest | agreed |
| R5-204233 | Updates to IXIT Proforma for MCVideo and MCData | NIST, MCC TF160 | 36.579-5 | 0009 | - | Rel-13 | F | MCImp-UEConTest | withdrawn |
| R5-204377 | Updates to introduce support for MCVideo and MCData | NIST, MCC TF160 | 36.579-5 | 0010 | - | Rel-13 | F | MCImp-UEConTest | agreed |
| R5-204114 | Test Tolerance analysis for E-UTRAN HD-FDD inter frequency handover for Cat-M1 UEs in CEModeA test case | Ericsson | 36.903 | 0440 | - | Rel-15 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-204115 | Test Tolerance analysis for E-UTRAN HD-FDD Inter frequency RRC Re-establishment for Cat-M1 UE in CEModeA test case | Ericsson | 36.903 | 0441 | - | Rel-15 | F | TEI12_Test, LTE_feMTC-UEConTest | agreed |
| R5-203987 | Updating test point analysis for AMPR of NS_01 and NS_04 | Huawei, HiSilicon | 36.905 | 0237 | - | Rel-16 | F | LTE_CA_R14-UEConTest | agreed |
| R5-203988 | Updating test point analysis for 3A-41A to add SE-coex | Huawei, HiSilicon | 36.905 | 0238 | - | Rel-16 | F | LTE_CA_R14-UEConTest | agreed |
| R5-204276 | Update of test point analysis for CA_3A-7B | ROHDE & SCHWARZ | 36.905 | 0239 | - | Rel-16 | F | TEI13_Test, LTE_CA_Rel13-UEConTest | agreed |
| R5-204020 | Clarification on frequency band test conditions for A-GNSS | Qualcomm Incorporated | 37.571-1 | 0309 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204979 | Clarification on frequency band test conditions for A-GNSS | Qualcomm Incorporated | 37.571-1 | 0309 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203273 | Adding measurement gaps for OTDOA configuration | ROHDE & SCHWARZ | 37.571-2 | 0132 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204489 | Adding measurement gaps for OTDOA configuration | ROHDE & SCHWARZ | 37.571-2 | 0132 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203511 | Correction of WLAN Assistance Data Element referenced clause | PCTEST Engineering Laboratory, LLC | 37.571-2 | 0133 | - | Rel-16 | F | TEI15_Test | agreed |
| R5-203512 | Addition of OTDOA information for pre-test conditions for test 9.3.3.1B | PCTEST Engineering Laboratory, LLC | 37.571-2 | 0134 | - | Rel-16 | F | TEI15_Test | revised |
| R5-204532 | Addition of OTDOA information for pre-test conditions for test 9.3.3.1B | PCTEST Engineering Laboratory, LLC | 37.571-2 | 0134 | 1 | Rel-16 | F | TEI15_Test | agreed |
| R5-204318 | Text Proposal to update Clause 5.5 - Test Environment | Qualcomm CDMA Technologies | 37.901-5 | 0001 | - | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | agreed |
| R5-204319 | Text Proposal to update TC A.7.1.1.1 | Qualcomm CDMA Technologies | 37.901-5 | 0002 | - | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | revised |
| R5-204894 | Text Proposal to update TC A.7.1.1.1 | Qualcomm CDMA Technologies | 37.901-5 | 0002 | 1 | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | agreed |
| R5-204320 | Text Proposal to update TC A.9.1.1.1 | Qualcomm CDMA Technologies | 37.901-5 | 0003 | - | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | revised |
| R5-204895 | Text Proposal to update TC A.9.1.1.1 | Qualcomm CDMA Technologies | 37.901-5 | 0003 | 1 | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | agreed |
| R5-204321 | Text Proposal to update TC A.8.1 | Qualcomm CDMA Technologies | 37.901-5 | 0004 | - | Rel-16 | F | FS_UE_5GNR_App_Data_Perf | agreed |
| R5-203224 | Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1 | Nokia, Nokia Shanghai Bell | 38.508-1 | 1362 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204800 | Introduction of test frequencies for Rel-16 inter-band EN-DC combinations within FR1 | Nokia, Nokia Shanghai Bell | 38.508-1 | 1362 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203255 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator-r16, AvailableRB-SetPerCell and BAP-Routing-ID | Ericsson | 38.508-1 | 1363 | - | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203275 | Editorial update IE ARFCN-ValueNR | Ericsson | 38.508-1 | 1364 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203276 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID | Ericsson | 38.508-1 | 1365 | - | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203277 | Add IEs ARFCN-ValueUTRA-FDD, AvailabilityCombinationsPerCell, AvailabilityIndicator and BAP-Routing-ID | Ericsson | 38.508-1 | 1366 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203278 | n26 Default CH BW in 38.508-1 | Dish Network | 38.508-1 | 1367 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203287 | Correction PRB-Id for PUCCH secondHopPRB | Keysight Technologies UK Ltd | 38.508-1 | 1368 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203320 | Add IE BeamFailureRecoverySCellConfig | Ericsson | 38.508-1 | 1369 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203337 | Addition of test frequencies for n28 with CBW of 30MHz | CMCC, CBN, Ericsson | 38.508-1 | 1370 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204896 | Addition of test frequencies for n28 with CBW of 30MHz | CMCC, CBN, Ericsson | 38.508-1 | 1370 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203338 | Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID | Ericsson | 38.508-1 | 1371 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204507 | Add IEs BH-RLC-ChannelConfig, BH-LogicalChannelIdentity, BH-LogicalChannelIdentity-Ext and BH-RLC-ChannelID | Ericsson | 38.508-1 | 1371 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203339 | Add IE CGI-InfoEUTRALogging | Ericsson | 38.508-1 | 1372 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203340 | Add IEs CGI-Info-Logging and CLI-RSSI-Range | Ericsson | 38.508-1 | 1373 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203341 | Add IEs CommonLocationInfo, CondReconfigId, CondReconfigToAddModList and ConditionalReconfiguration | Ericsson | 38.508-1 | 1374 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203342 | Add IEs ConfiguredGrantConfigIndex and ConfiguredGrantConfigIndexMAC | Ericsson | 38.508-1 | 1375 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203343 | Add IE DRX-ConfigSecondaryGroup | Ericsson | 38.508-1 | 1376 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203344 | Add IE HighSpeedConfig | Ericsson | 38.508-1 | 1377 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203345 | Add IE InvalidSymbolPattern | Ericsson | 38.508-1 | 1378 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203346 | Add IEs LBT-FailureRecoveryConfig and LocationInfo | Ericsson | 38.508-1 | 1379 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203347 | Add IE MeasIdleConfig | Ericsson | 38.508-1 | 1380 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203348 | Add IE MeasObjectCLI | Ericsson | 38.508-1 | 1381 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203349 | Add IE MeasObjectNR-SL | Ericsson | 38.508-1 | 1382 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203350 | Add IE MeasObjectUTRA-FDD | Ericsson | 38.508-1 | 1383 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203351 | Add IEs MeasResultIdleEUTRA and MeasResultIdleNR | Ericsson | 38.508-1 | 1384 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203352 | Add Es MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | 38.508-1 | 1385 | - | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203354 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | 38.508-1 | 1386 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204508 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | 38.508-1 | 1386 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203355 | Add IEs MsgA-ConfigCommon and MsgA-PUSCH-Config | Ericsson | 38.508-1 | 1387 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203356 | Add IEs NeedForGapsConfigNR and NeedForGapsInfoNR | Ericsson | 38.508-1 | 1388 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203357 | Correction to Table 4.5.2.2-2-second SMC procedure for Selected EPS NAS security algorithms IE | Huawei, Hisilicon | 38.508-1 | 1389 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203358 | Correction to Table 4.6.1-17 RRCResume | Huawei, Hisilicon | 38.508-1 | 1390 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204386 | Correction to Table 4.6.1-17 RRCResume | Huawei, Hisilicon | 38.508-1 | 1390 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203359 | Correction to Table 4.6.3-141 ReportConfigInterRAT | Huawei, Hisilicon | 38.508-1 | 1391 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203360 | Correction to Table 4.6.3-142 ReportConfigNR | Huawei, Hisilicon | 38.508-1 | 1392 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203361 | Correction to Table 4.7.1-26 SECURITY MODE COMPLETE | Huawei, Hisilicon, Keysight | 38.508-1 | 1393 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203362 | Correction to Table 4.9.9.2.3-2 TRACKING AREA UPDATE REQUEST | Huawei, Hisilicon | 38.508-1 | 1394 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203446 | Add IEs NPN-Identity and NPN-IdentityInfoList | Ericsson | 38.508-1 | 1395 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203449 | Add IE PLMN-IdentityList2 | Ericsson | 38.508-1 | 1396 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203450 | Add IE PUCCH-ConfigurationList | Ericsson | 38.508-1 | 1397 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203451 | Add IE PUCCH-SpatialRelationInfo-Id | Ericsson | 38.508-1 | 1398 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203455 | Corrections to 4.5.1 | ROHDE & SCHWARZ | 38.508-1 | 1399 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203456 | Updating usages of TS 34.229-1 to TS 34.229-5 | ROHDE & SCHWARZ | 38.508-1 | 1400 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203467 | Add IE RACH-ConfigCommonTwoStepRA | Ericsson | 38.508-1 | 1401 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203470 | Add IE RACH-ConfigGenericTwoStepRA | Ericsson | 38.508-1 | 1402 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203471 | Add IE ReferenceTimeInfo | Ericsson | 38.508-1 | 1403 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203472 | Add IE RepetitionSchemeConfig | Ericsson | 38.508-1 | 1404 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203476 | Add IE ReportConfigNR-SL | Ericsson | 38.508-1 | 1405 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203484 | Corrections to generic procedures for MO and MT speech call establishment | ROHDE & SCHWARZ | 38.508-1 | 1406 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204387 | Corrections to generic procedures for MO and MT speech call establishment | ROHDE & SCHWARZ | 38.508-1 | 1406 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203497 | Correction to USIM configurations 7 and 13 | Keysight Technologies UK | 38.508-1 | 1407 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204388 | Correction to USIM configurations 7 and 13 | Keysight Technologies UK | 38.508-1 | 1407 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203498 | Correction to switch off / power off procedures for IMS | Keysight Technologies UK Ltd, Qualcomm Incorporated | 38.508-1 | 1408 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204389 | Correction to switch off / power off procedures for IMS | Keysight Technologies UK Ltd, Qualcomm Incorporated | 38.508-1 | 1408 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203499 | Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Keysight Technologies UK, Huawei/HiSilicon | 38.508-1 | 1409 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204384 | Correction to test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Keysight Technologies UK, Huawei/HiSilicon | 38.508-1 | 1409 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203500 | Update to Table 4.6.3-74: MeasObjectEUTRA | Keysight Technologies UK | 38.508-1 | 1410 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203506 | Add IE RSSI-Range | Ericsson | 38.508-1 | 1411 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203507 | Add IEs SemiStaticChannelAccessConfig and Sensor-LocationInfo | Ericsson | 38.508-1 | 1412 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203508 | Add IE SI-RequestConfig | Ericsson | 38.508-1 | 1413 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203509 | Add IEs SPS-ConfigIndex, SPS-PUCCH-AN and SPS-PUCCH-AN-List | Ericsson | 38.508-1 | 1414 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203510 | Add IE SRS-RSRP-Range | Ericsson | 38.508-1 | 1415 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203523 | Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16 | China Telecom | 38.508-1 | 1416 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204509 | Modification to InterRAT-Parameters to add the UE capability nr-HO-ToEN-DC-r16 | China Telecom | 38.508-1 | 1416 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203533 | Update to PDSCH-ServingCellConfig | MCC TF160, Keysight Technologies UK | 38.508-1 | 1417 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203534 | Updates to CellGroupConfig and RNTI-Value for NR-DC | MCC TF160 | 38.508-1 | 1418 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203556 | Add IE SSB-PositionQCL-Relation | Ericsson | 38.508-1 | 1419 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204510 | Add IE SSB-PositionQCL-Relation | Ericsson | 38.508-1 | 1419 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203557 | Add IEs UL-DelayValueConfig and UplinkCancellation | Ericsson | 38.508-1 | 1420 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203574 | Correction of description of NGEN-DC in table 4.5.1-1 | Tejet | 38.508-1 | 1421 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204390 | Correction of description of NGEN-DC in table 4.5.1-1 | Tejet | 38.508-1 | 1421 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203575 | Add chapter Positioning System information blocks | Ericsson | 38.508-1 | 1422 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203577 | Add IEs SIB10, SIB11, SIB12, SIB13 and SIB14 | Ericsson | 38.508-1 | 1423 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203582 | Add messages DedicatedSIBRequest, DLDedicatedMessageSegment, DLInformationTransferMRDC and IABOtherInformation | Ericsson | 38.508-1 | 1424 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203585 | Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR | MediaTek Inc., Keysight Technologies | 38.508-1 | 1425 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204391 | Correction to UE-CapabilityRAT-RequestList and UE-CapabilityRequestFilterNR | MediaTek Inc., Keysight Technologies | 38.508-1 | 1425 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203587 | Correction to test procedure of Table 4.9.9.2.2-1 | MediaTek Inc., Keysight Technologies | 38.508-1 | 1426 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203588 | Correction to NR inter-band CA configurations in FR1 | MediaTek Inc. | 38.508-1 | 1427 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204378 | Correction to NR inter-band CA configurations in FR1 | MediaTek Inc. | 38.508-1 | 1427 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203631 | Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | 38.508-1 | 1428 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204751 | Introduction of test frequencies for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | 38.508-1 | 1428 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203634 | Introduction of test frequencies for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | 38.508-1 | 1429 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203652 | Corrections to Default contents of RRCResume message | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.508-1 | 1430 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203653 | Corrections to Generic procedure 4.9.9 | Qualcomm CDMA Technologies | 38.508-1 | 1431 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203662 | Removal of USIM profile #16 | Qualcomm CDMA Technologies | 38.508-1 | 1432 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203671 | Update of PDSCH-to-HARQ_feedback timing indicator (k1) value | Qualcomm Korea | 38.508-1 | 1433 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203672 | Jumbo CR for update to Demod message contents | Qualcomm Korea | 38.508-1 | 1434 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204852 | Jumbo CR for update to Demod message contents | Qualcomm Korea, Anritsu | 38.508-1 | 1434 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205007 | Jumbo CR for update to Demod message contents | Qualcomm Korea, Anritsu | 38.508-1 | 1434 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203680 | Updating indicator for SUL FR1 test cases | Huawei, Hisilicon | 38.508-1 | 1435 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204708 | Updating indicator for SUL FR1 test cases | Huawei, Hisilicon | 38.508-1 | 1435 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203681 | Editorial correction typos in annex C.2.3.2 | Huawei, Hisilicon | 38.508-1 | 1436 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203683 | Update frequencyDomainResources and nrofcandidates | Huawei, Hisilicon | 38.508-1 | 1437 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204709 | Update frequencyDomainResources and nrofcandidates | Huawei, Hisilicon | 38.508-1 | 1437 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203704 | Correction to Table 4.6.3-87 NZP-CSI-RS-ResourceSet | Huawei, Hisilicon | 38.508-1 | 1438 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203715 | Addition of Generic Test Procedure for IMS MO SMS in 5GC | ZTE | 38.508-1 | 1439 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204392 | Addition of Generic Test Procedure for IMS MO SMS in 5GC | ZTE | 38.508-1 | 1439 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203716 | Addition of Generic Test Procedure for IMS MT SMS in 5GC | ZTE | 38.508-1 | 1440 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204393 | Addition of Generic Test Procedure for IMS MT SMS in 5GC | ZTE | 38.508-1 | 1440 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203719 | Add messages LoggedMeasurementConfiguration, MCGFailureInformation and SidelinkUEInformationNR | Ericsson | 38.508-1 | 1441 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203725 | Add messages UEInformationRequest, UEInformationResponse, ULDedicatedMessageSegment and ULInformationTransferIRAT | Ericsson | 38.508-1 | 1442 | - | Rel-16 | F | TEI16_Test | agreed |
| R5-203729 | Update IE RACH-ConfigGeneric | Ericsson | 38.508-1 | 1443 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203730 | Scheduling Request Resource config for RRM test cases | ROHDE & SCHWARZ | 38.508-1 | 1444 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203731 | OSI scheduling config for RRM test cases | ROHDE & SCHWARZ | 38.508-1 | 1445 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203743 | Update IE RLC-BearerConfig | Ericsson | 38.508-1 | 1446 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204394 | Update IE RLC-BearerConfig | Ericsson | 38.508-1 | 1446 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203755 | Update IE SchedulingRequestResourceConfig | Ericsson | 38.508-1 | 1447 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203764 | Adding default value for IE rbg-Size for demodulation and CSI reporting tests | Ericsson | 38.508-1 | 1448 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204899 | Adding default value for IE rbg-Size for demodulation and CSI reporting tests | Ericsson | 38.508-1 | 1448 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203767 | Addition of test frequencies for new Rel-16 CBW for NR band n77 | Ericsson | 38.508-1 | 1449 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203768 | Addition of test frequencies for new Rel-16 CBW for NR band n78 | Ericsson | 38.508-1 | 1450 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203769 | Introduction of test frequencies for Rel-16 NR band n30 | Ericsson, AT&T | 38.508-1 | 1451 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203770 | Introduction of test frequencies for Rel-19 NR band n259 | Ericsson | 38.508-1 | 1452 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | withdrawn |
| R5-203774 | Add Annex D | Ericsson | 38.508-1 | 1453 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203793 | Correction of n29 test frequencies for protocol testing | Ericsson | 38.508-1 | 1454 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203794 | Introduction of n30 test frequencies for protocol testing | Ericsson, AT&T | 38.508-1 | 1455 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203796 | Correction of EN-DC test frequency information for protocol testing | Ericsson | 38.508-1 | 1456 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203813 | Correction to PUCCH-Config | ANRITSU LTD | 38.508-1 | 1457 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203815 | FR2 PUSCH K2 values alignment to TS 38.214 | Qualcomm Wireless GmbH | 38.508-1 | 1458 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203863 | Correction to Table 7.3.1-3 SSB-MTC | Huawei, HiSilicon | 38.508-1 | 1459 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203864 | Correction to TCI-state related configurations | Huawei, HiSilicon | 38.508-1 | 1460 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204752 | Correction to TCI-state related configurations | Huawei, HiSilicon | 38.508-1 | 1460 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203865 | Correction to CSI-RS related configurations | Huawei, HiSilicon | 38.508-1 | 1461 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204753 | Correction to CSI-RS related configurations | Huawei, HiSilicon | 38.508-1 | 1461 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203888 | Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs | CAICT | 38.508-1 | 1462 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204900 | Introduction of definition of Mid, Low, High test channel bandwidth and removal of NOTEs that incorrectly permit UE not to support mandatory BWs | CAICT | 38.508-1 | 1462 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203908 | Corrections on test frequencies for NR FR2 CA band n261 | ZTE Corporation | 38.508-1 | 1463 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203920 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | 38.508-1 | 1464 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203937 | Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A | Huawei, Hisilicon | 38.508-1 | 1465 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204700 | Adding test frequencies for DC_1A-7A_n78A and DC_3A-7A_n78A | Huawei, Hisilicon | 38.508-1 | 1465 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203944 | Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | 38.508-1 | 1466 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204702 | Adding test frequencies for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | 38.508-1 | 1466 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203998 | Addition of test frequencies for new Rel-16 CBW 25 and 50 MHz for NR band n1 | Ericsson | 38.508-1 | 1467 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203999 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | 38.508-1 | 1468 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204754 | Update on test frequencies for EN-DC configurations including FR2 | ZTE Corporation | 38.508-1 | 1468 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204021 | Correction of n51 and n76 test frequencies for protocol testing | Ericsson | 38.508-1 | 1469 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204032 | Introduction of n259 test frequencies for protocol testing | Ericsson | 38.508-1 | 1470 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204038 | Corrections of test frequency tables for EN-DC configuration DC_(n)41AA | Ericsson | 38.508-1 | 1471 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204039 | Corrections of test frequency tables for EN-DC configuration DC_(n)71AA | Ericsson | 38.508-1 | 1472 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204041 | Addition of test channel bandwidths for n1 new CBW in 38.508-1 R16 | China Unicom | 38.508-1 | 1473 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204043 | Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents | ANRITSU LTD | 38.508-1 | 1474 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204385 | Update to PDU SESSION ESTABLISHMENT ACCEPTED message contents | ANRITSU LTD | 38.508-1 | 1474 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204049 | Correction to the procedure for determination of SSB and CORESET0 | Anritsu | 38.508-1 | 1475 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204050 | Correction to message configuration for performance tests | Anritsu | 38.508-1 | 1476 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204901 | Correction to message configuration for performance tests | Anritsu | 38.508-1 | 1476 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204051 | Correction to PRB-Id | Anritsu | 38.508-1 | 1477 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204052 | PUCCH Resource ID for CSI TCs | Anritsu | 38.508-1 | 1478 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204053 | Correction to PDCCH-ConfigCommon for performance tests | Anritsu | 38.508-1 | 1479 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204092 | Update IE ServingCellConfigCommon | Ericsson | 38.508-1 | 1480 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204134 | Update IE SIB2 | Ericsson | 38.508-1 | 1481 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204395 | Update IE SIB2 | Ericsson | 38.508-1 | 1481 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204135 | New procedure for PDU Session Release | MCC TF160 | 38.508-1 | 1482 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204396 | New procedure for PDU Session Release | MCC TF160 | 38.508-1 | 1482 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204137 | Update to FreqBandList | MCC TF160, Qualcomm, Anritsu | 38.508-1 | 1483 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204397 | Update to FreqBandList | MCC TF160, Qualcomm, Anritsu | 38.508-1 | 1483 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204150 | Update Table 5.4.2.0-2: ServingCellConfigCommon | Ericsson | 38.508-1 | 1484 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204164 | Corrections of test frequency tables for CA_n258x | Ericsson | 38.508-1 | 1485 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204755 | Corrections of test frequency tables for CA_n258x | Ericsson | 38.508-1 | 1485 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204165 | Corrections of test frequency tables for CA_n260x | Ericsson | 38.508-1 | 1486 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204756 | Corrections of test frequency tables for CA_n260x | Ericsson | 38.508-1 | 1486 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204166 | Corrections of test frequency tables for CA_n261x | Ericsson | 38.508-1 | 1487 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204757 | Corrections of test frequency tables for CA_n261x | Ericsson | 38.508-1 | 1487 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204167 | Corrections of test frequency tables for CA_n260(A-I) | Ericsson | 38.508-1 | 1488 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204168 | Update Table 7.3.1-4: ServingCellConfigCommon | Ericsson | 38.508-1 | 1489 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204169 | Update IE ServingCellConfigCommon | Ericsson | 38.508-1 | 1490 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204398 | Update IE ServingCellConfigCommon | Ericsson | 38.508-1 | 1490 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204223 | Update missing SMTC configurations in RRM message contents | ROHDE & SCHWARZ | 38.508-1 | 1491 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204235 | Add SSB subcarrier spacing configurations in RRM message contents | ROHDE & SCHWARZ | 38.508-1 | 1492 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204758 | Add SSB subcarrier spacing configurations in RRM message contents | ROHDE & SCHWARZ | 38.508-1 | 1492 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204238 | Correction to default contents of RRCReestablishmentRequest message | Qualcomm CDMA Technologies | 38.508-1 | 1493 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204324 | Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections | Samsung | 38.508-1 | 1494 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204399 | Adding generic procedure E-UTRA RRC_IDLE with unrestricted number of PDN connections | Samsung | 38.508-1 | 1494 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204325 | Adding procedure for establishment of multiple additional PDN connections in EPS (S1 mode) | Samsung | 38.508-1 | 1495 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204326 | Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling | Samsung | 38.508-1 | 1496 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204400 | Update of PDU SESSION ESTABLISHMENT ACCEPT for multi PDU-PDN handling | Samsung | 38.508-1 | 1496 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204327 | Updates to Test procedure for UE for Tracking area updating / Inter-system change from N1 mode to S1 mode in 5GMM/EMM-IDLE mode | Samsung | 38.508-1 | 1497 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204328 | Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Samsung | 38.508-1 | 1498 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204401 | Updates of Test procedure for UE for Tracking area updating / Inter-system change from S1 mode to N1 mode in 5GMM/EMM-IDLE mode | Samsung | 38.508-1 | 1498 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204329 | Update of 4.5A.2 UE-requested PDU session establishment procedure | Samsung | 38.508-1 | 1499 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204330 | Updates Procedure to UE-requested PDU session modification after the first S1 to N1 mode change | Samsung | 38.508-1 | 1500 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204331 | Void 4.9.14 Procedure for UE-requested PDU session modification after the first S1 to N1 mode change | Samsung | 38.508-1 | 1501 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204346 | Introduction of test frequencies for Rel-16 NR band n259 | Ericsson | 38.508-1 | 1502 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204704 | Adding the test frequency for DC_3A-7A_n78A | Huawei, Hisilicon | 38.508-1 | 1503 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204706 | Adding the test frequency for DC_28A_n3A | Huawei, Hisilicon | 38.508-1 | 1504 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203225 | Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities | Nokia, Nokia Shanghai Bell | 38.508-2 | 0084 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204801 | Introduction of Rel-16 inter-band EN-DC configurations within FR1 for physical layer baseline implementation capabilities | Nokia, Nokia Shanghai Bell | 38.508-2 | 0084 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203279 | n26 Implementation baseline capabilities in 38.508-2 | Dish Network | 38.508-2 | 0085 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203288 | Added UE Phy layer capabilitity into 38.508-2 from 38.306 | Keysight Technologies UK Ltd | 38.508-2 | 0086 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204853 | Added UE Phy layer capabilitity into 38.508-2 from 38.306 | Keysight Technologies UK Ltd | 38.508-2 | 0086 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203289 | Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities | Keysight Technologies UK Ltd | 38.508-2 | 0087 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204902 | Updated table A.4.3.9-4 - 4 Rx antenna ports capabilities | Keysight Technologies UK Ltd | 38.508-2 | 0087 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203457 | Fixing References | ROHDE & SCHWARZ | 38.508-2 | 0088 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203463 | Addition of PICs for CSI-RS measurement without associated SSB | Huawei, Hisilicon | 38.508-2 | 0089 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203632 | Introduction of UE capabilities for additional Rel-15 band EN-DC inter-band configurations | Ericsson, Telefonica | 38.508-2 | 0090 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203635 | Introduction of UE capabilities for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | 38.508-2 | 0091 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203887 | Introduction and correction of general capabilities and some band-combo information for EN-DC | CAICT | 38.508-2 | 0092 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204903 | Introduction and correction of general capabilities and some band-combo information for EN-DC | CAICT | 38.508-2 | 0092 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203891 | Introduction of Inter-band measurements capabilities for signalling test cases | CAICT | 38.508-2 | 0093 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203911 | Update of A.4.3.2A for intra-band contiguous CA capabilities | ZTE Corporation | 38.508-2 | 0094 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203912 | Update of A.4.3.2A.3 for intra-band non-contiguous CA capabilities | ZTE Corporation | 38.508-2 | 0095 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203913 | Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities | ZTE Corporation | 38.508-2 | 0096 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204802 | Update of A.4.3.2A.4 for inter-band CA within FR1 capabilities | ZTE Corporation | 38.508-2 | 0096 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203914 | Update of A.4.3.2B for NR-DC capabilities | ZTE Corporation | 38.508-2 | 0097 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203915 | Update of A.4.3.2B.2 for intra-band EN-DC capabilities | ZTE Corporation | 38.508-2 | 0098 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204803 | Update of A.4.3.2B.2 for intra-band EN-DC capabilities | ZTE Corporation | 38.508-2 | 0098 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203916 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities | ZTE Corporation | 38.508-2 | 0099 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204804 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR1 and FR2 capabilities | ZTE Corporation | 38.508-2 | 0099 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203917 | Update of A.4.3.2B.2.3 for inter-band EN-DC including FR2 capabilities | ZTE Corporation | 38.508-2 | 0100 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203918 | Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities | ZTE Corporation | 38.508-2 | 0101 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204805 | Update of A.4.3.2B.2.3 for inter-band EN-DC within FR1 capabilities | ZTE Corporation | 38.508-2 | 0101 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203974 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | 38.508-2 | 0102 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204759 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | 38.508-2 | 0102 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204046 | Addition of R16 new channel bandwidths for n1 in 38.508-2 | China Unicom | 38.508-2 | 0103 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | withdrawn |
| R5-204153 | Introduction of UE capabilities for Rel-16 EN-DC configurations | Bureau Veritas, Qualcomm Austria RFFE GmbH | 38.508-2 | 0104 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204806 | Introduction of UE capabilities for Rel-16 EN-DC configurations | Bureau Veritas, Qualcomm Austria RFFE GmbH | 38.508-2 | 0104 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204187 | CR to 38.508-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | 38.508-2 | 0105 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204710 | CR to 38.508-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | 38.508-2 | 0105 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204205 | Addition and update of PICS | Lenovo, Motorola Mobility | 38.508-2 | 0106 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204544 | Addition and update of PICS | Lenovo, Motorola Mobility | 38.508-2 | 0106 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204301 | Add new PICS | Qualcomm Incorporated | 38.508-2 | 0107 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204904 | Add new PICS | Qualcomm Incorporated | 38.508-2 | 0107 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204332 | Adding new ICS for handling inter-system change S1-N1 and aligning PDN and PDU handling | Samsung | 38.508-2 | 0108 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204373 | Addition of UE capability for voiceFallbackIndicationEPS-r16 | CATT, TDIA | 38.508-2 | 0109 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204511 | Addition of UE capability for voiceFallbackIndicationEPS-r16 | CATT, TDIA | 38.508-2 | 0109 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-204344 | TMC Integrity and Ciphering Protection | Apple | 38.509 | 0031 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204402 | TMC Integrity and Ciphering Protection | Apple | 38.509 | 0031 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203256 | Template | Anritsu | 38.521-1 | 0915 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203259 | Correction of test frequencies for NS_47 | Ericsson, SoftBank Corp. | 38.521-1 | 0916 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204823 | Correction of test frequencies for NS_47 | Ericsson, SoftBank Corp. | 38.521-1 | 0916 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203260 | Adding NS_47 to Additional spurious emissions test case | Ericsson, SoftBank Corp. | 38.521-1 | 0917 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203261 | Adding UL MIMO additional spurious emissions test for NS_47 | Ericsson, SoftBank Corp. | 38.521-1 | 0918 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203262 | Adding band n48 to maximum output power and maximum output power reduction tests | Ericsson | 38.521-1 | 0919 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204824 | Adding band n48 to maximum output power and maximum output power reduction tests | Ericsson | 38.521-1 | 0919 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203263 | Adding band n48 to blocking characteristics tests | Ericsson | 38.521-1 | 0920 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | withdrawn |
| R5-203281 | n26 in common clauses in 38.521-1 | Dish Network | 38.521-1 | 0921 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | withdrawn |
| R5-203282 | n26 Rx requirements in 38.521-1 | Dish Network | 38.521-1 | 0922 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204961 | n26 Rx requirements in 38.521-1 | Dish Network | 38.521-1 | 0922 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203283 | Update of clause5 into TS 38.521-1 R15 | China Unicom | 38.521-1 | 0923 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204762 | Update of clause5 into TS 38.521-1 R15 | China Unicom | 38.521-1 | 0923 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203284 | Update of R16 new bands and CBWs in 38.521-1 | China Unicom, AT&T, Dish Network, CMCC | 38.521-1 | 0924 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204828 | Update of R16 new bands and CBWs in 38.521-1 | China Unicom, AT&T, Dish Network, CMCC | 38.521-1 | 0924 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203285 | Update of R16 CADC combos in TS 38.521-1 | China Unicom | 38.521-1 | 0925 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204808 | Update of R16 CADC combos in TS 38.521-1 | China Unicom | 38.521-1 | 0925 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203290 | Clarification of Interferer frequency selection in FR1 IBB test case 7.6.2 | Keysight Technologies UK Ltd | 38.521-1 | 0926 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203291 | Correction of K1 to achieve PUCCH Format 3 in FDD in EVM and in-band emission | Keysight Technologies UK Ltd | 38.521-1 | 0927 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203336 | Addition of test cases for n28 with CBW of 30MHz | CMCC, CBN, Huawei, HiSilicon, Orange | 38.521-1 | 0928 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204960 | Addition of test cases for n28 with CBW of 30MHz | CMCC, CBN, Huawei, HiSilicon, Orange | 38.521-1 | 0928 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203530 | Update to 7.5A.2 ACS for 3DL CA | Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH | 38.521-1 | 0929 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204897 | Update to 7.5A.2 ACS for 3DL CA | Guangdong OPPO Mobile Telecom, China Telecom, Samsung, WE Certification, DISH | 38.521-1 | 0929 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203558 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | 38.521-1 | 0930 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204722 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | 38.521-1 | 0930 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204980 | Corrections and additions to 7.3A | WE Certification Oy, DISH Network | 38.521-1 | 0930 | 2 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203560 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | 38.521-1 | 0931 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204723 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | 38.521-1 | 0931 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204981 | Completing 3CA Rx cases 7.5A.2 and 7.7A.2 | WE Certification Oy, DISH Network | 38.521-1 | 0931 | 2 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203572 | Corrected test config for NS_24 in additional spurious emission test 6.5.3.3 | Keysight Technologies UK Ltd | 38.521-1 | 0932 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203674 | Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01 | Huawei, Hisilicon | 38.521-1 | 0933 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204711 | Updating 6.2A.3-AMPR for CA for NS_43 and NS_01,NS_43U and NS_01 | Huawei, Hisilicon | 38.521-1 | 0933 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203677 | Cleaning up of Tx inter-band CA test cases | Huawei, Hisilicon | 38.521-1 | 0934 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204760 | Cleaning up of Tx inter-band CA test cases | Huawei, Hisilicon | 38.521-1 | 0934 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203678 | Adding MU and TTs for Inter-band UL CA test cases | Huawei, Hisilicon | 38.521-1 | 0935 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203679 | Updating message content in SUL test cases | Huawei, Hisilicon | 38.521-1 | 0936 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203682 | Updating test case 6.5A.2.4.1-NR ACLR for CA | Huawei, Hisilicon | 38.521-1 | 0937 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203684 | Adding FR1 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | 38.521-1 | 0938 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204712 | Adding FR1 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | 38.521-1 | 0938 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203687 | Updating channel configurations for Intra-band UL contiguous CA | Huawei, Hisilicon | 38.521-1 | 0939 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203688 | Updating intra-band CA UL and DL configurations | Huawei, Hisilicon | 38.521-1 | 0940 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203689 | Adding MU and TTs for Intra-band UL CA test cases | Huawei, Hisilicon | 38.521-1 | 0941 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203690 | Introduce general requirement for UL CA test cases | Huawei, Hisilicon | 38.521-1 | 0942 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203691 | Updating NR test case 6.2A.1- MOP for CA | Huawei, Hisilicon | 38.521-1 | 0943 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203692 | Update of NR test case 6.2A.2-MPR for CA | Huawei, Hisilicon | 38.521-1 | 0944 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204984 | Update of NR test case 6.2A.2-MPR for CA | Huawei, Hisilicon | 38.521-1 | 0944 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203694 | Updating of NR test case 6.2A.4-Configured output power for CA | Huawei, Hisilicon | 38.521-1 | 0945 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204974 | Updating of NR test case 6.2A.4-Configured output power for CA | Huawei, Hisilicon | 38.521-1 | 0945 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203696 | Addition of general clause 7.1A | Huawei, Hisilicon | 38.521-1 | 0946 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203697 | Updating REFSENS minimum requirements for Intra-band non-contiguous CA | Huawei, Hisilicon | 38.521-1 | 0947 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203698 | Update of 7.4A.2-Maximum input level for 3DL CA | Huawei, Hisilicon | 38.521-1 | 0948 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203699 | Adding band n48 for Blocking characteristics testing | Huawei, Hisilicon, Ericsson | 38.521-1 | 0949 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204837 | Adding band n48 for Blocking characteristics testing | Huawei, Hisilicon, Ericsson | 38.521-1 | 0949 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203700 | Update of test case 7.6A.2-Inband blocking for CA | Huawei, Hisilicon | 38.521-1 | 0950 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203701 | Update of test case 7.6A.2.2 Inband blocking for 3DL CA | Huawei, Hisilicon | 38.521-1 | 0951 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203721 | Introduce of new TC 6.3A.4.1 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0952 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204832 | Introduce of new TC 6.3A.4.1 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0952 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203723 | Introduce of new TC 6.3A.4.2 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0953 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204833 | Introduce of new TC 6.3A.4.2 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0953 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203726 | Introduce of new TC 6.3A.4.3 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0954 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204834 | Introduce of new TC 6.3A.4.3 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0954 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203734 | Add intra-band contiguous CA to 6.3A.1 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0955 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204835 | Add intra-band contiguous CA to 6.3A.1 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0955 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203735 | Add intra-band contiguous CA to 6.3A.2 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0956 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203736 | Add intra-band contiguous CA to 6.3A.3 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0957 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204836 | Add intra-band contiguous CA to 6.3A.3 | Guangdong OPPO Mobile Telecom. | 38.521-1 | 0957 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203748 | Change of RB allocation start for test case 6.3.4.3 | Ericsson, Keysight | 38.521-1 | 0958 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203754 | Correct UE output power configuration to some UL MIMO cases | Guangdong OPPO Mobile Telecom, Orange | 38.521-1 | 0959 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204854 | Correct UE output power configuration to some UL MIMO cases | Guangdong OPPO Mobile Telecom, Orange | 38.521-1 | 0959 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203777 | Update of NR test case 6.2.1 UE MOP for n30 | AT&T | 38.521-1 | 0960 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203778 | Update of NR test case 6.2.2 UE MPR for n30 | AT&T | 38.521-1 | 0961 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203780 | Update of NR test case 6.2D.1 UE MOP for UL MIMO for n30 | AT&T | 38.521-1 | 0962 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203781 | Update of NR test case 6.2D.2 UE MPR for UL MIMO for n30 | AT&T | 38.521-1 | 0963 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | withdrawn |
| R5-203783 | Update of NR test case 6.5.3.2 Spurious Emissions for UE Co-Ex for n30 | AT&T | 38.521-1 | 0964 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203786 | Update of NR test case 7.3 UE Ref Sens for n30 | AT&T | 38.521-1 | 0965 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203787 | Update of NR test case 7.6.2 UE IBB for n30 | AT&T, DISH Network, CAICT, Ericsson, HiSilicon | 38.521-1 | 0966 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204962 | Update of NR test case 7.6.2 UE IBB for n30 | AT&T, DISH Network, CAICT, Ericsson, HiSilicon | 38.521-1 | 0966 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203788 | Update of NR test case 7.6.3 UE OBB for n30 | AT&T | 38.521-1 | 0967 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203789 | Update of NR test case 7.6.4 UE NBB for n30 | AT&T | 38.521-1 | 0968 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203876 | Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec | CAICT | 38.521-1 | 0969 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204855 | Removal of editors note about missing of Rel-15 In-gap OOB blocking requirement in RAN4 spec | CAICT | 38.521-1 | 0969 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203877 | Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec | CAICT | 38.521-1 | 0970 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204910 | Alignment of requirements in 7.6.3 and 7.6A.3 with the core spec | CAICT | 38.521-1 | 0970 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203878 | Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4 | CAICT | 38.521-1 | 0971 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204911 | Removal of SDL bands from single carrier Rx TCs 7.6.2, 7.6.3 and 7.6.4 | CAICT | 38.521-1 | 0971 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203879 | Correction of diversity characteristics requirement in section 7.2 | CAICT | 38.521-1 | 0972 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203880 | Correction of UE mean power requirements Table numbers in SEM and ACLR test cases for SA FR1 | CAICT | 38.521-1 | 0973 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203881 | Adding NOTEs to the test requirement tables in 6.2D.2 | CAICT | 38.521-1 | 0974 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203882 | Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2 | CAICT | 38.521-1 | 0975 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204905 | Correction of of 6.2D.1 and Test applicability of 6.5.2.4.2 | CAICT | 38.521-1 | 0975 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203883 | Correction of test requirement for 6.2.4 | CAICT | 38.521-1 | 0976 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204906 | Correction of test requirement for 6.2.4 | CAICT | 38.521-1 | 0976 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203884 | Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04 | CAICT | 38.521-1 | 0977 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204907 | Addition of test procedure and test requirement for PC2 fallback to PC3 for network signalling value NS_04 | CAICT | 38.521-1 | 0977 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203885 | Correction of test requirement for 6.2.1 | CAICT | 38.521-1 | 0978 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203886 | Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4 | CAICT | 38.521-1 | 0979 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204908 | Adding additional tolerance to test requirement of 6.2.1, 6.2.2, 6.2.3 and 6.2.4 | CAICT | 38.521-1 | 0979 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203909 | Update of 6.2.3 for minimum conformance requirements for A-MPR | ZTE Corporation | 38.521-1 | 0980 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204909 | Update of 6.2.3 for minimum conformance requirements for A-MPR | ZTE Corporation | 38.521-1 | 0980 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203962 | Update of SA Rx test cases for 4Rx UEs | Huawei, HiSilicon | 38.521-1 | 0981 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204912 | Update of SA Rx test cases for 4Rx UEs | Huawei, HiSilicon | 38.521-1 | 0981 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203964 | Update of test cases for UEs supporting Tx Diversity | Huawei, HiSilicon | 38.521-1 | 0982 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203967 | Editorial correction of 6.2.4 | Huawei, HiSilicon | 38.521-1 | 0983 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203976 | Addition of 25MHz for NR band n1 | Huawei, HiSilicon | 38.521-1 | 0984 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204825 | Addition of 25MHz for NR band n1 | Huawei, HiSilicon | 38.521-1 | 0984 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203977 | Addition of AMPR NS_48 for NR band n1 | Huawei, HiSilicon | 38.521-1 | 0985 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204826 | Addition of AMPR NS_48 for NR band n1 | Huawei, HiSilicon | 38.521-1 | 0985 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204010 | Correction to target power level Pmin for SA UL MIMO TCs | Huawei, Hisilicon | 38.521-1 | 0986 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204035 | Updating NR test case 7.6A.3 for n48 | Huawei, Hisilicon | 38.521-1 | 0987 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-204037 | Update of NR test case 7.5A Adjacent Channel selectivity for CA | Samsung R&D Institute UK | 38.521-1 | 0988 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204898 | Update of NR test case 7.5A Adjacent Channel selectivity for CA | Samsung R&D Institute UK | 38.521-1 | 0988 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-204040 | Update of NR test case 7.7A Spurious response for CA | Samsung R&D Institute UK | 38.521-1 | 0989 | - | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-204054 | Correction to test Configuration of flatness for Pi/2 BPSK | Anritsu | 38.521-1 | 0990 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204103 | Correction of QPSK UL RMC | Rohde & Schwarz | 38.521-1 | 0991 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204129 | Addition of n1 R16 new CBW into 38.521-1 Refsense test | China Unicom | 38.521-1 | 0992 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204827 | Addition of n1 R16 new CBW into 38.521-1 Refsense test | China Unicom | 38.521-1 | 0992 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204131 | Update of UE co-existence for CA_n1-n78 | China Unicom | 38.521-1 | 0993 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204807 | Update of UE co-existence for CA_n1-n78 | China Unicom | 38.521-1 | 0993 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204132 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | 38.521-1 | 0994 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-204160 | Updated to FR1 general clauses for NRSL eV2X | Bureau Veritas | 38.521-1 | 0995 | - | Rel-16 | F | 5G_V2X_NRSL_eV2XARC-UEConTest | revised |
| R5-204839 | Updated to FR1 general clauses for NRSL eV2X | Bureau Veritas | 38.521-1 | 0995 | 1 | Rel-16 | F | 5G_V2X_NRSL_eV2XARC-UEConTest | agreed |
| R5-204195 | Update 6.5.3.2 Spurious emission for UE co-existence | Qualcomm Austria RFFE GmbH | 38.521-1 | 0996 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204202 | Update for 7.3A.0 Minimum conformance requirements for CA | Qualcomm Austria RFFE GmbH | 38.521-1 | 0997 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204204 | Update Uplink power control window size for SA RX TCs | Qualcomm Austria RFFE GmbH | 38.521-1 | 0998 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204913 | Update Uplink power control window size for SA RX TCs | Qualcomm Austria RFFE GmbH | 38.521-1 | 0998 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204249 | Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC | Ericsson | 38.521-1 | 0999 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204258 | Editorial correction to FR1 co-existence requirements | ROHDE & SCHWARZ | 38.521-1 | 1000 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204761 | Editorial correction to FR1 co-existence requirements | ROHDE & SCHWARZ | 38.521-1 | 1000 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204263 | Update of CSI-RS definition for DL RMCs in TS 38.521-1 | ROHDE & SCHWARZ | 38.521-1 | 1001 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203292 | Clarification of Interferer frequency selection in FR2 IBB test case 7.6.2 | Keysight Technologies UK Ltd | 38.521-2 | 0373 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203293 | FR2 ACLR MBW correction according to RAN4 | Keysight Technologies UK Ltd | 38.521-2 | 0374 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203487 | Adjacent Channel Selectivity FR2 MU updates in 38.521-2 | Keysight Technologies UK Ltd | 38.521-2 | 0375 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203491 | In-band Blocking FR2 MU updates in 38.521-2 | Keysight Technologies UK Ltd | 38.521-2 | 0376 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203516 | Update of test procedure for Minimum output power for CA in FR2 | TTA | 38.521-2 | 0377 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203517 | Update of test procedure for Error vector magnitude for CA in FR2 | TTA | 38.521-2 | 0378 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203580 | Beam correspondence - SRS configuration corrections in annex K.1.1 | Keysight Technologies UK Ltd | 38.521-2 | 0379 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204865 | Beam correspondence - SRS configuration corrections in annex K.1.1 | Keysight Technologies UK Ltd | 38.521-2 | 0379 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203581 | Beam correspondence - SRS configuration corrections in section 6.6.1 | Keysight Technologies UK Ltd | 38.521-2 | 0380 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204857 | Beam correspondence - SRS configuration corrections in section 6.6.1 | Keysight Technologies UK Ltd | 38.521-2 | 0380 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203685 | Adding FR2 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | 38.521-2 | 0381 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204718 | Adding FR2 PDCCH Aggregation Level in Annex C.3 | Huawei, Hisilicon | 38.521-2 | 0381 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203718 | Correction to test configuration for Carrier leakage for CA | LG Electronics | 38.521-2 | 0382 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204713 | Correction to test configuration for Carrier leakage for CA | LG Electronics | 38.521-2 | 0382 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203720 | Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA | LG Electronics | 38.521-2 | 0383 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204714 | Correction to TC 6.4A.2.3.1 In-band emissions for 2UL CA | LG Electronics | 38.521-2 | 0383 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203722 | Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA | LG Electronics | 38.521-2 | 0384 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204715 | Correction to test cases 6.4A.2.3.x In-band emissions for 3 to 6 UL CA | LG Electronics | 38.521-2 | 0384 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203724 | Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA | LG Electronics | 38.521-2 | 0385 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204716 | Introduction of New TC 6.4A.2.3.6 In-band emissions for 7UL CA | LG Electronics | 38.521-2 | 0385 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203727 | Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA | LG Electronics | 38.521-2 | 0386 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204717 | Introduction of New TC 6.4A.2.3.7 In-band emissions for 8UL CA | LG Electronics | 38.521-2 | 0386 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203765 | Core spec alignment for measurement BW in 6.5.2.3, ACLR | Ericsson | 38.521-2 | 0387 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203766 | Updates to test case 6.3.4.3, relative power tolerance | Ericsson | 38.521-2 | 0388 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204914 | Updates to test case 6.3.4.3, relative power tolerance | Ericsson | 38.521-2 | 0388 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203816 | FR2 RefSens and EIS spherical PC3 MBR table update | Qualcomm Wireless GmbH | 38.521-2 | 0389 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204920 | FR2 RefSens and EIS spherical PC3 MBR table update | Qualcomm Wireless GmbH | 38.521-2 | 0389 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203873 | Correction of UL power level requirement in 7.4 | CAICT | 38.521-2 | 0390 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203874 | Correction of test procedure of ACLR and SEM for SA FR2 | CAICT | 38.521-2 | 0391 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203875 | Alignment of general sections with core spec of SA FR2 R15 | CAICT | 38.521-2 | 0392 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203968 | Miscellaneous corrections due to core spec alignment | Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson | 38.521-2 | 0393 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204763 | Miscellaneous corrections due to core spec alignment | Huawei, HiSilicon, Rohde & Schwarz, Keysight, Ericsson | 38.521-2 | 0393 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203969 | Updating beam correspondance capability | Huawei, HiSilicon | 38.521-2 | 0394 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203970 | Addition of UL power setting for Rx test cases | Huawei, HiSilicon, CAICT | 38.521-2 | 0395 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204765 | Addition of UL power setting for Rx test cases | Huawei, HiSilicon, CAICT | 38.521-2 | 0395 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203971 | Addition of modified MPR behavior | Huawei, HiSilicon | 38.521-2 | 0396 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204921 | Addition of modified MPR behavior | Huawei, HiSilicon | 38.521-2 | 0396 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204025 | CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps | Samsung R&D Institute UK | 38.521-2 | 0397 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204858 | CR to 38.521-2 to update Absolute Power Tolerance for CA on the order of test steps | Samsung R&D Institute UK | 38.521-2 | 0397 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204030 | CR to 38.521-2 to update Transmit OFF Power | Samsung R&D Institute UK | 38.521-2 | 0398 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204915 | CR to 38.521-2 to update Transmit OFF Power | Samsung R&D Institute UK | 38.521-2 | 0398 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204031 | CR to TS 38.521-2: Correction to time mask requirements | Samsung R&D Institute UK | 38.521-2 | 0399 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204916 | CR to TS 38.521-2: Correction to time mask requirements | Samsung R&D Institute UK | 38.521-2 | 0399 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204033 | CR to TS 38.521-2: Annex F EIRP OFF Power | Samsung R&D Institute UK | 38.521-2 | 0400 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204922 | CR to TS 38.521-2: Annex F EIRP OFF Power | Samsung R&D Institute UK | 38.521-2 | 0400 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204044 | CR to TS 38.521-2: Correction to MB relaxation minimum requirements | Samsung R&D Institute UK | 38.521-2 | 0401 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204859 | CR to TS 38.521-2: Correction to MB relaxation minimum requirements | Samsung R&D Institute UK | 38.521-2 | 0401 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204055 | Clean up complete status for FR2 SA test cases | Anritsu | 38.521-2 | 0402 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204917 | Clean up complete status for FR2 SA test cases | Anritsu | 38.521-2 | 0402 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204056 | CR to update MU and TT in 38.521-2 | Anritsu | 38.521-2 | 0403 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204856 | CR to update MU and TT in 38.521-2 | Anritsu | 38.521-2 | 0403 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204057 | Update to UE maximum output power for CA | Anritsu | 38.521-2 | 0404 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204918 | Update to UE maximum output power for CA | Anritsu | 38.521-2 | 0404 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204104 | Correction of QPSK UL RMC | Rohde & Schwarz | 38.521-2 | 0405 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204185 | CR to 38.521-2 to adjust the test step sequences | Keysight Technologies UK Ltd | 38.521-2 | 0406 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204860 | CR to 38.521-2 to adjust the test step sequences | Keysight Technologies UK Ltd | 38.521-2 | 0406 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204188 | CR to 38.521-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | 38.521-2 | 0407 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204861 | CR to 38.521-2 to allow vendor declarations related to beam peak searches | Keysight Technologies UK Ltd | 38.521-2 | 0407 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204193 | CR to 38.521-2 on QoQZ Verification Clarification | Keysight Technologies UK Ltd | 38.521-2 | 0408 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204862 | CR to 38.521-2 on QoQZ Verification Clarification | Keysight Technologies UK Ltd | 38.521-2 | 0408 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204203 | CR to TS 38.521-2 on DUT alignment options | ROHDE & SCHWARZ | 38.521-2 | 0409 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204923 | CR to TS 38.521-2 on DUT alignment options | ROHDE & SCHWARZ | 38.521-2 | 0409 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204247 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | 38.521-2 | 0410 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204919 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | 38.521-2 | 0410 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204255 | FR2 Minimum output power MU updates | Keysight Technologies UK Ltd | 38.521-2 | 0411 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204863 | FR2 Minimum output power MU updates | Keysight Technologies UK Ltd | 38.521-2 | 0411 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204264 | Editorial correction of ACLR CA test cases | ROHDE & SCHWARZ | 38.521-2 | 0412 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204265 | Editorial correction of Annex C.3 Connection | ROHDE & SCHWARZ | 38.521-2 | 0413 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204266 | Update of FR2 OBW test case | ROHDE & SCHWARZ | 38.521-2 | 0414 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204267 | Update of Tx signal quality test cases | ROHDE & SCHWARZ | 38.521-2 | 0415 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204764 | Update of Tx signal quality test cases | ROHDE & SCHWARZ | 38.521-2 | 0415 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204268 | Update of CSI-RS definition for DL RMCs in TS 38.521-2 | ROHDE & SCHWARZ | 38.521-2 | 0416 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204278 | FR2 EIRP OFF power MU updates | Keysight Technologies UK Ltd | 38.521-2 | 0417 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204864 | FR2 EIRP OFF power MU updates | Keysight Technologies UK Ltd | 38.521-2 | 0417 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203226 | Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | 38.521-3 | 0643 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204809 | Adding transmitter requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | 38.521-3 | 0643 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203227 | Adding receiver requirements for Rel-16 inter-band EN-DC FR1 band combinations | Nokia, Nokia Shanghai Bell | 38.521-3 | 0644 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203294 | Correction of MU definition for test case 6.5B.2.1.3 | Keysight Technologies UK Ltd | 38.521-3 | 0645 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203295 | definition of MU and TT for test case 6.3B.4.3 | Keysight Technologies UK Ltd | 38.521-3 | 0646 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203296 | definition of MU and TT for test case 6.5B.4.3 | Keysight Technologies UK Ltd | 38.521-3 | 0647 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203297 | Definition of MU and TT for test case 7.3B.2.4 | Keysight Technologies UK Ltd | 38.521-3 | 0648 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203488 | Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3 | Keysight Technologies UK Ltd | 38.521-3 | 0649 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204869 | Adjacent Channel Selectivity FR2 MU and TT updates in 38.521-3 | Keysight Technologies UK Ltd | 38.521-3 | 0649 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203492 | In-band Blocking FR2 MU updates in 38.521-3 | Keysight Technologies UK Ltd | 38.521-3 | 0650 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203515 | Editorial correction of test case 6.5B.3.3.1 | TTA | 38.521-3 | 0651 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203527 | Editorial correction of Tx spurious emissions for FR1 EN-DC | DOCOMO Communications Lab. | 38.521-3 | 0652 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203633 | Introduction of additonal Rel-15 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3 | Ericsson, Telefonica | 38.521-3 | 0653 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203636 | Editorial correction to spurious emission test case 6.5B.3.3.2 | Ericsson | 38.521-3 | 0654 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204810 | Editorial correction to spurious emission test case 6.5B.3.3.2 | Ericsson | 38.521-3 | 0654 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203637 | Introduction of additional Rel-16 EN-DC inter-band configurations to EN-DC MOP test case 6.2B.1.3 | Ericsson, Telefonica | 38.521-3 | 0655 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203638 | Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | 38.521-3 | 0656 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204811 | Introduction of dTIBc for additional Rel-16 EN-DC inter-band configurations | Ericsson, Telefonica | 38.521-3 | 0656 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203639 | Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | 38.521-3 | 0657 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204812 | Introduction of Rel-16 EN-DC configuration DC_40A_n1A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | 38.521-3 | 0657 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203640 | Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | 38.521-3 | 0658 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204813 | Introduction of Rel-16 EN-DC configuration DC_40A_n78A to spurious emission test case 6.5B.3.3.2 | Ericsson, Telefonica | 38.521-3 | 0658 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203641 | Introduction of additonal Rel-16 EN-DC configurations to EN-DC reference sensitivity test case 7.3B.2.3 | Ericsson, Telefonica | 38.521-3 | 0659 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203753 | Update test procedure to 6.5B.3.3.1 | Guangdong OPPO Mobile Telecom. | 38.521-3 | 0660 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203763 | Editorial correction of referenced clause (6.2.3) in test case 6.2B.2.1.2 | Ericsson | 38.521-3 | 0661 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203807 | Updated to clause 6 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas, Ericsson | 38.521-3 | 0662 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204724 | Updated to clause 6 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas, Ericsson | 38.521-3 | 0662 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203808 | Updated to clause 7 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas | 38.521-3 | 0663 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204956 | Updated to clause 7 for EN-DC Rel-16 band requirement | Sporton, Bureau Veritas | 38.521-3 | 0663 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203817 | FR2 RefSens inter-band EN-DC UL MIMO test cases | Qualcomm Wireless GmbH | 38.521-3 | 0664 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204770 | FR2 RefSens inter-band EN-DC UL MIMO test cases | Qualcomm Wireless GmbH | 38.521-3 | 0664 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203818 | Spurious inter-band EN-DC FR2 UL MIMO test cases | Qualcomm Wireless GmbH | 38.521-3 | 0665 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204766 | Spurious inter-band EN-DC FR2 UL MIMO test cases | Qualcomm Wireless GmbH | 38.521-3 | 0665 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203870 | Update of Test applicability for some Inter-Band EN-DC including FR2 TCs | CAICT | 38.521-3 | 0666 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204924 | Update of Test applicability for some Inter-Band EN-DC including FR2 TCs | CAICT | 38.521-3 | 0666 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203871 | Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | 38.521-3 | 0667 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204927 | Update of editors note for OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | 38.521-3 | 0667 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203872 | Adding RRCConnectionReconfiguration Table for E-UTRA on FDD band and UE does not support dynamic power sharing in 6.5B.3.3.1 and 6.5B.3.3.2 | CAICT | 38.521-3 | 0668 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203907 | Corrections on delta RIB due to Rel-16 EN-DC configurations | ZTE Corporation | 38.521-3 | 0669 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203910 | Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1 | ZTE Corporation | 38.521-3 | 0670 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204771 | Update of 7.3B.3.3 for REFSENS relaxation due to inter-band EN-DC within FR1 | ZTE Corporation | 38.521-3 | 0670 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203919 | Update of Tx test for DC_2_n41 and DC_66_n41 | ZTE Corporation | 38.521-3 | 0671 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203938 | Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1 | Huawei, Hisilicon | 38.521-3 | 0672 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204701 | Addition of test configuration for DC_(n)71AA MOP testing in 6.2B.1.1 | Huawei, Hisilicon | 38.521-3 | 0672 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203940 | Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x | Huawei, Hisilicon | 38.521-3 | 0673 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204767 | Addition of test requirement of dropped NR carrier for non-DPS UE in 6.2B.4.x | Huawei, Hisilicon | 38.521-3 | 0673 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203941 | Addition of the test description to apply LTE agnostic approach in 7.4B.2 MIL | Huawei, Hisilicon | 38.521-3 | 0674 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203942 | Addition of intra-band contiguous EN-DC with more than 2CCs within FR1 in 7.4B.3_1 | Huawei, Hisilicon | 38.521-3 | 0675 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203943 | Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO | Huawei, Hisilicon | 38.521-3 | 0676 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204772 | Addition of new test case 7.4B.5D MIL for inter-band EN-DC including FR1 and FR2 for UL-MIMO | Huawei, Hisilicon | 38.521-3 | 0676 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203945 | Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | 38.521-3 | 0677 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204703 | Addition of MOP testing for a few Rel-16 inter-band EN-DC within FR1 | Huawei, Hisilicon | 38.521-3 | 0677 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203946 | Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | 38.521-3 | 0678 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204768 | Addition of additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | 38.521-3 | 0678 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203953 | Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC | Huawei, Hisilicon | 38.521-3 | 0679 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204814 | Addition of additional test points for spurious emission UE co-existence for a few Rel-16 inter-band EN-DC | Huawei, Hisilicon | 38.521-3 | 0679 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203960 | Correction to additional test points for spurious emission UE co-existence for a few Rel-15 inter-band EN-DC | Huawei, Hisilicon | 38.521-3 | 0680 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203963 | Update of NSA Rx test cases for 4Rx UEs | Huawei, HiSilicon | 38.521-3 | 0681 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204928 | Update of NSA Rx test cases for 4Rx UEs | Huawei, HiSilicon | 38.521-3 | 0681 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203965 | Update of MOP test cases for EN-DC PC2 Rel-15 requirements | Huawei, HiSilicon | 38.521-3 | 0682 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203966 | Update of MOP test cases for EN-DC PC2 Rel-16 requirements | Huawei, HiSilicon | 38.521-3 | 0683 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204845 | Update of MOP test cases for EN-DC PC2 Rel-16 requirements | Huawei, HiSilicon | 38.521-3 | 0683 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-203973 | Cleaning up of delta_TIB | Huawei, HiSilicon | 38.521-3 | 0684 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204008 | Correction to UE co-existence Test Case 6.5B.3.3.2 | Huawei, Hisilicon | 38.521-3 | 0685 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204009 | Correction to UE co-existence Test Case 6.5B.3.3.2 | Huawei, Hisilicon | 38.521-3 | 0686 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-204058 | Clean up complete status for EN-DC test cases | Anritsu | 38.521-3 | 0687 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204925 | Clean up complete status for EN-DC test cases | Anritsu | 38.521-3 | 0687 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204059 | Correction to default test setting of 7.3B.2.3_1.1 | Anritsu | 38.521-3 | 0688 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204060 | CR to update MU and TT in 38.521-3 | Anritsu | 38.521-3 | 0689 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204866 | CR to update MU and TT in 38.521-3 | Anritsu | 38.521-3 | 0689 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204102 | Update Refsense exceptions for EN-DC including n78 | Rohde & Schwarz | 38.521-3 | 0690 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205006 | Update Refsense exceptions for EN-DC including n78 | Rohde & Schwarz | 38.521-3 | 0690 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204151 | Updated to EN-DC Rel-15 Configuration information in clause 5 | Bureau Veritas | 38.521-3 | 0691 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204152 | Updated to EN-DC Rel-16 Configuration information in clause 5 | Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson | 38.521-3 | 0692 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204816 | Updated to EN-DC Rel-16 Configuration information in clause 5 | Bureau Veritas, Nokia, Qualcomm, KDDI, Ericsson | 38.521-3 | 0692 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204154 | Updated to Annex M for EN-DC Rel-16 configuration requirement | Bureau Veritas | 38.521-3 | 0693 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204155 | Updated to clause 6 for EN-DC Rel-16 configuration test requirement | Bureau Veritas, Qualcomm Austria RFFE GmbH | 38.521-3 | 0694 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204815 | Updated to clause 6 for EN-DC Rel-16 configuration test requirement | Bureau Veritas, Qualcomm Austria RFFE GmbH | 38.521-3 | 0694 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204156 | Updated to clause 7 for EN-DC Rel-16 configuration test requirement | Bureau Veritas | 38.521-3 | 0695 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204957 | Updated to clause 7 for EN-DC Rel-16 configuration test requirement | Bureau Veritas | 38.521-3 | 0695 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204161 | Updated to EN-DC general clauses for NRSL eV2X | Bureau Veritas | 38.521-3 | 0696 | - | Rel-16 | F | 5G_V2X_NRSL_eV2XARC-UEConTest | revised |
| R5-204840 | Updated to EN-DC general clauses for NRSL eV2X | Bureau Veritas | 38.521-3 | 0696 | 1 | Rel-16 | F | 5G_V2X_NRSL_eV2XARC-UEConTest | agreed |
| R5-204170 | Update for TC 7.5B.0 Minimum Conformance Requirements of ACS for DC | CMCC | 38.521-3 | 0697 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204171 | Update for TC 7.5B.1 ACS for intra-band contiguous EN-DC 2CC | CMCC | 38.521-3 | 0698 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204172 | Update for TC 7.5B.2 ACS for intra-band non-contiguous EN-DC 2CC | CMCC | 38.521-3 | 0699 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204173 | Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC | CMCC | 38.521-3 | 0700 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204929 | Addition of TC 7.5B.3_1.2 ACS for EN-DC within FR1 4CC | CMCC | 38.521-3 | 0700 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204174 | Addition of TC 7.5B.3_1.3 ACS for EN-DC within FR1 5CC | CMCC | 38.521-3 | 0701 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204175 | Addition of TC 7.5B.3_1.4 ACS for EN-DC within FR1 6CC | CMCC | 38.521-3 | 0702 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204176 | Update for TC 7.5B.4 ACS for inter-band EN-DC including FR2 2CCs | CMCC | 38.521-3 | 0703 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204177 | Update for TC 7.5B.4_1.1 ACS for inter-band EN-DC including FR2 3CCs | CMCC | 38.521-3 | 0704 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204178 | Update for TC 7.5B.4_1.2 ACS for inter-band EN-DC including FR2 4CCs | CMCC | 38.521-3 | 0705 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204179 | Update for TC 7.5B.4_1.3 ACS for inter-band EN-DC including FR2 5CCs | CMCC | 38.521-3 | 0706 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204180 | Update for TC 7.5B.4_1.4 ACS for inter-band EN-DC including FR2 6CCs | CMCC | 38.521-3 | 0707 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204181 | Addition of TC 7.5B.4D ACS for inter-band EN-DC including FR2 for UL-MIMO | CMCC | 38.521-3 | 0708 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204182 | Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | 38.521-3 | 0709 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204773 | Addition of TC 7.5B.5D ACS for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | 38.521-3 | 0709 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204183 | Addition of TC 7.6B.2.4D Inband blocking for inter-band EN-DC including FR2 for UL-MIMO | CMCC | 38.521-3 | 0710 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204184 | Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | 38.521-3 | 0711 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204930 | Addition of TC 7.6B.2.5D Inband blocking for inter-band EN-DC including FR1 and FR2 for UL-MIMO | CMCC | 38.521-3 | 0711 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204197 | Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs | Qualcomm Austria RFFE GmbH | 38.521-3 | 0712 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204931 | Update for 7.3B.2.3 Ref sense for Inter-band EN-DC within FR1-2 CCs | Qualcomm Austria RFFE GmbH | 38.521-3 | 0712 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204198 | Update for 7.3B.2.0 | Qualcomm Austria RFFE GmbH | 38.521-3 | 0713 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204199 | Update for Spurious Emissions for intra-band EN-DC | Qualcomm Austria RFFE GmbH | 38.521-3 | 0714 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204201 | Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs | Qualcomm Austria RFFE GmbH | 38.521-3 | 0715 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204719 | Update for 7.3B.2.3_1.3 Reference sensitivity for EN-DC within FR1 5CCs | Qualcomm Austria RFFE GmbH | 38.521-3 | 0715 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204207 | Update for 6.5B.3.3.2 Spurious emission band UE co-existence | Qualcomm Austria RFFE GmbH | 38.521-3 | 0716 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204867 | Update for 6.5B.3.3.2 Spurious emission band UE co-existence | Qualcomm Austria RFFE GmbH | 38.521-3 | 0716 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204209 | Update Uplink power control window size for NSA RX TCs | Qualcomm Austria RFFE GmbH | 38.521-3 | 0717 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204210 | Update Tx TC for Rel 16 DC combos | Qualcomm Austria RFFE GmbH | 38.521-3 | 0718 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204215 | Re-organization of EN-DC refsens test cases | Ericsson | 38.521-3 | 0719 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204932 | Re-organization of EN-DC refsens test cases | Ericsson | 38.521-3 | 0719 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204218 | Update Tx TC for Rel 16 DC combos | Qualcomm Austria RFFE GmbH | 38.521-3 | 0720 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | withdrawn |
| R5-204250 | FR2 Minimum output power measurement period definition | Keysight Technologies UK Ltd | 38.521-3 | 0721 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204256 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | 38.521-3 | 0722 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204868 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | 38.521-3 | 0722 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204259 | Editorial correction to EN-DC co-existence requirements | ROHDE & SCHWARZ | 38.521-3 | 0723 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204769 | Editorial correction to EN-DC co-existence requirements | ROHDE & SCHWARZ | 38.521-3 | 0723 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204262 | Update to reference sensitivity test case 7.3B.2.3_1 | ROHDE & SCHWARZ | 38.521-3 | 0724 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204280 | FR2 Minimum output power measurement uncertainties updates | Keysight Technologies UK Ltd | 38.521-3 | 0725 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204296 | Addition of test case 6.4B.2.4.1D | ROHDE & SCHWARZ | 38.521-3 | 0726 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204297 | Addition of test case 6.4B.2.4.2D | ROHDE & SCHWARZ | 38.521-3 | 0727 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204298 | Addition of test case 6.4B.2.4.3D | ROHDE & SCHWARZ | 38.521-3 | 0728 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204299 | Addition of test case 6.4B.2.4.4D | ROHDE & SCHWARZ | 38.521-3 | 0729 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204310 | Update of test case 6.2B.3.1 UE Additional Maximum Output Power reduction for Intra-band contiguous EN-DC | Ericsson | 38.521-3 | 0730 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204311 | Addition of pending UL-MIMO tests (FR2) in Clause 6 | Qualcomm CDMA Technologies | 38.521-3 | 0731 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204926 | Addition of pending UL-MIMO tests (FR2) in Clause 6 | Qualcomm CDMA Technologies | 38.521-3 | 0731 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204312 | Addition of pending UL-MIMO tests (FR2) in Clause 7 | Qualcomm CDMA Technologies | 38.521-3 | 0732 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204313 | TS 38.521-3 Section 1-5 and Annex updates to align with core specification | Qualcomm CDMA Technologies | 38.521-3 | 0733 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204314 | Common updates across tests in Clause 6 | Qualcomm CDMA Technologies | 38.521-3 | 0734 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204315 | Common updates across tests in Clause 7 | Qualcomm CDMA Technologies | 38.521-3 | 0735 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204322 | Update for TC 7.5B.5 ACS for inter-band EN-DC including both FR1 and FR2 | CMCC | 38.521-3 | 0736 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204347 | Add Rx TC for 2Rel 16 DC combos | Qualcomm Austria RFFE GmbH, Bureau Veritas | 38.521-3 | 0737 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204958 | Add Rx TC for 2Rel 16 DC combos | Qualcomm Austria RFFE GmbH | 38.521-3 | 0737 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204349 | Editorial correction of Rx spurious emissions for FR1 EN-DC | DOCOMO Communications Lab. | 38.521-3 | 0738 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-204705 | Addition of test configuration for 71AA in 6.2B.1.1 MOP | Huawei, Hisilicon | 38.521-3 | 0739 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204707 | Addition of MOP testing for DC_28A_n3A in 6.2B.1.3 | Huawei, Hisilicon | 38.521-3 | 0740 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-205005 | Update of OOBB and Spurious Response of Inter-band EN-DC within FR1 | CAICT | 38.521-3 | 0741 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203298 | Activate Test Mode in NSA Demod Test Cases | Keysight Technologies UK Ltd | 38.521-4 | 0215 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203668 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | 38.521-4 | 0216 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204937 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | 38.521-4 | 0216 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205012 | Annex F Update of MU and TT for FR2 PDSCH and PDCCH Demodulation scenario | Qualcomm Korea | 38.521-4 | 0216 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203670 | message contents correction for TC 5.2.3.1.2_1 | Qualcomm Korea | 38.521-4 | 0217 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203673 | Update to FR2 PDSCH test case | Qualcomm Korea | 38.521-4 | 0218 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204936 | Update to FR2 PDSCH test case | Qualcomm Korea | 38.521-4 | 0218 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205011 | Update to FR2 PDSCH test case | Qualcomm Korea | 38.521-4 | 0218 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203717 | Correction to TC 5.2.3.1.1_1 4Rx FDD FR1 PDSCH mapping Type A performance | LG Electronics | 38.521-4 | 0219 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203756 | Removing unnecessary IE rbg-Size from message exceptions | Ericsson | 38.521-4 | 0220 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203902 | Correction to Annex G minimum test time table | Qualcomm Korea | 38.521-4 | 0221 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203903 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | 38.521-4 | 0222 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204870 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | 38.521-4 | 0222 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205008 | Addition of FR1 2Rx TDD PDSCH mapping type B test case | Qualcomm Korea | 38.521-4 | 0222 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203904 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | 38.521-4 | 0223 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204774 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | 38.521-4 | 0223 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205009 | Test applicability update for all PDSCH mapping type B test cases | Qualcomm Korea | 38.521-4 | 0223 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203905 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | 38.521-4 | 0224 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204871 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | 38.521-4 | 0224 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205010 | Addition of 4Rx FDD FR1 RI reporting test case | Qualcomm Korea | 38.521-4 | 0224 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204061 | Correction to frequencyDomainAllocation | Anritsu | 38.521-4 | 0225 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204934 | Correction to frequencyDomainAllocation | Anritsu | 38.521-4 | 0225 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204062 | Correction to PDSCH reference channel | Anritsu | 38.521-4 | 0226 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204063 | Correction to 2Rx FDD FR1 periodic wideband CQI reporting under fading conditions | Anritsu | 38.521-4 | 0227 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204064 | Correction to LTE-NR coexistence performance | Anritsu | 38.521-4 | 0228 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204065 | CR to update MU and TT in 38.521-4 | Anritsu | 38.521-4 | 0229 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204933 | CR to update MU and TT in 38.521-4 | Anritsu | 38.521-4 | 0229 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204066 | Correction to MU and TT for FR1 PMI and RI tests | Anritsu | 38.521-4 | 0230 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204935 | Correction to MU and TT for FR1 PMI and RI tests | Anritsu | 38.521-4 | 0230 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204067 | Correction to common test parameters for FR2 demod and CSI tests | Anritsu | 38.521-4 | 0231 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204100 | Update to common test parameters and channel mappings | Rohde & Schwarz | 38.521-4 | 0232 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204101 | Update E-UTRA cell configuration for NSA | Rohde & Schwarz | 38.521-4 | 0233 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204105 | Addition of missing FR1 RMC | Rohde & Schwarz | 38.521-4 | 0234 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204261 | Editorial correction of message exceptions | ROHDE & SCHWARZ | 38.521-4 | 0235 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204273 | Update of AWGN flatness in TS 38.521-4 | ROHDE & SCHWARZ | 38.521-4 | 0236 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204938 | Update of AWGN flatness in TS 38.521-4 | ROHDE & SCHWARZ | 38.521-4 | 0236 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203330 | TP for TS 38.522 | CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm | 38.522 | 0043 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204939 | TP for TS 38.522 | CMCC, T-mobile USA, SGS, ZTE, TTA, Huawei, HiSilicon, Qualcomm | 38.522 | 0043 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203869 | Correction of 38.522 | CAICT | 38.522 | 0044 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204940 | Correction of 38.522 | CAICT | 38.522 | 0044 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203975 | Addition of PICS for intra-band EN-DC PC2 | Huawei, HiSilicon | 38.522 | 0045 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204098 | Correct applicability EN-DC event-triggered inter-frequency tests | ROHDE & SCHWARZ | 38.522 | 0046 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204099 | Correct applicability NR SA event-triggered inter-frequency tests | ROHDE & SCHWARZ | 38.522 | 0047 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203363 | Correction to NR TC 6.1.1.1-PLMN selection in automatic mode | Huawei, Hisilicon | 38.523-1 | 1590 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203364 | Addition of NR TC 6.1.1.1a-PLMN selection in automatic mode Single Frequency operation | Huawei, Hisilicon | 38.523-1 | 1591 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203365 | Correction to NR TC 6.1.1.2-access technology combinations | Huawei, Hisilicon | 38.523-1 | 1592 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204403 | Correction to NR TC 6.1.1.2-access technology combinations | Huawei, Hisilicon | 38.523-1 | 1592 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203366 | Addition of NR TC 6.1.1.2a-PLMN selection of Other PLMN in automatic mode Single Frequency operation | Huawei, Hisilicon | 38.523-1 | 1593 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203367 | Correction to NR TC 6.1.1.5-PLMN selection in Automatic mode User reselection | Huawei, Hisilicon | 38.523-1 | 1594 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203368 | Addition of NR TC 6.1.1.5a-PLMN selection in Automatic mode User reselection Single Frequency operation | Huawei, Hisilicon | 38.523-1 | 1595 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203369 | Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode | Huawei, Hisilicon | 38.523-1 | 1596 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204404 | Correction to NR TC 6.1.1.7-PLMN selection of RPLMN or HPLMN in Automatic mode | Huawei, Hisilicon | 38.523-1 | 1596 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203370 | Addition of NR TC 6.1.1.7a-PLMN selection of RPLMN or HPLMN in Automatic mode Single Frequency operation | Huawei, Hisilicon | 38.523-1 | 1597 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203371 | Correction to NR TC 6.1.2.19-Speed-dependent cell reselection | Huawei, Hisilicon, Keysight | 38.523-1 | 1598 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204405 | Correction to NR TC 6.1.2.19-Speed-dependent cell reselection | Huawei, Hisilicon, Keysight | 38.523-1 | 1598 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203372 | Correction to NR TC 6.1.2.21-Cell reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1599 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203373 | Correction to NR TC 6.1.2.23-Cell Reselection MFBI | Huawei, Hisilicon | 38.523-1 | 1600 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203374 | Correction to NR TC 6.2.1.1-Selection of correct RAT for OPLMN | Huawei, Hisilicon | 38.523-1 | 1601 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203375 | Correction to NR TC 6.2.1.4-Inter-RAT PLMN Selection with Manual mode | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1602 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203376 | Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1603 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204406 | Correction to NR TC 6.2.1.5-Inter-RAT Background HPLMN Search with Automatic Mode | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1603 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203377 | Correction to NR TC 6.2.3.9-Inter-RAT Speed Dependent Cell Reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1604 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203378 | Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1 | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1605 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204407 | Correction to NR TC 6.3.1.1-SOR during registration with security check successful using List Type 1 | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1605 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203379 | Correction to NR TC 6.3.1.2-SOR during registration with security check successful but no requested acknowledgement | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1606 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204408 | Correction to NR TC 6.3.1.2-SOR during registration with security check successful but no requested acknowledgement | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1606 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203380 | Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode | Huawei, Hisilicon, Datang Linktester, ZTE | 38.523-1 | 1607 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204543 | Correction to NR TC 6.3.1.3-SOR during registration with security check unsuccessful for Automatic mode | Huawei, Hisilicon, Datang Linktester, ZTE | 38.523-1 | 1607 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203381 | Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1608 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204409 | Correction to NR TC 6.3.1.5-SOR during registration with no SOR inforamtion received | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1608 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203382 | Correction to NR TC 6.4.1.1-PLMN Selection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1609 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203383 | Correction to NR TC 7.1.1.1.1-Correct selection of RACH parameters | Huawei, Hisilicon | 38.523-1 | 1610 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203384 | Correction to NR TC 7.1.1.4.1.3 and 7.1.1.4.1.4-DL TBS param combination leading to ambiguity | Huawei, Hisilicon | 38.523-1 | 1611 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203385 | Correction to NR TC 7.1.1.4.2.4 and 7.1.1.4.2.5-UL TBS param combination leading to ambiguity | Huawei, Hisilicon | 38.523-1 | 1612 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203386 | Correction to NR TC 7.1.1.9.1-MAC Reset | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1613 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204418 | Correction to NR TC 7.1.1.9.1-MAC Reset | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1613 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203387 | Correction to NR TC 7.1.1.2.2-PDSCH Aggregation | Huawei, Hisilicon | 38.523-1 | 1614 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204419 | Correction to NR TC 7.1.1.2.2-PDSCH Aggregation | Huawei, Hisilicon | 38.523-1 | 1614 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203388 | Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN | Huawei, Hisilicon | 38.523-1 | 1615 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204424 | Correction to NR TC 7.1.2.3.3-AM RLC 12-bit SN Correct use of SN | Huawei, Hisilicon | 38.523-1 | 1615 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203389 | Correction to NR TC 8.1.1.3.1-Redirection to another NR frequency | Huawei, Hisilicon | 38.523-1 | 1616 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203390 | Correction to NR TC 8.1.1.3.3-With priority information | Huawei, Hisilicon | 38.523-1 | 1617 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204432 | Correction to NR TC 8.1.1.3.3-With priority information | Huawei, Hisilicon | 38.523-1 | 1617 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203391 | Correction to NR TC 8.1.1.4.1-RRC Resume Success | Huawei, Hisilicon | 38.523-1 | 1618 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203392 | Correction to NR TC 8.1.X on SINR related configuration | Huawei, Hisilicon | 38.523-1 | 1619 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204437 | Correction to NR TC 8.1.X on SINR related configuration | Huawei, Hisilicon | 38.523-1 | 1619 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203393 | Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq | Huawei, Hisilicon | 38.523-1 | 1620 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204438 | Correction to NR TC 8.1.3.1.13-CSI-RS based intra-freq | Huawei, Hisilicon | 38.523-1 | 1620 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203394 | Correction to NR TC 8.1.3.1.15A-Intra NR measurements Blacklisting | Huawei, Hisilicon | 38.523-1 | 1621 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203395 | Correction to NR TC 8.1.4.1.7.X-Scell Release | Huawei, Hisilicon | 38.523-1 | 1622 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204446 | Correction to NR TC 8.1.4.1.7.X-Scell Release | Huawei, Hisilicon | 38.523-1 | 1622 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203396 | Correction to NR TC 8.1.5.7.1.X-RLC Failure MCG | Huawei, Hisilicon | 38.523-1 | 1623 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203397 | Correction to ENDC TC 8.2.2.1.1-SRB3 | Huawei, Hisilicon, Starpoint | 38.523-1 | 1624 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203398 | Addition of NRDC TC 8.2.2.1.2-SRB3 | Huawei, Hisilicon | 38.523-1 | 1625 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203399 | Addition of NRDC TC 8.2.2.3.2-Simultaneous SRB3 and Split SRB | Huawei, Hisilicon | 38.523-1 | 1626 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203400 | Correction to ENDC TC 8.2.2.6.1-PDCP version change | Huawei, Hisilicon, Starpoint | 38.523-1 | 1627 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204439 | Correction to ENDC TC 8.2.2.6.1-PDCP version change | Huawei, Hisilicon, Starpoint | 38.523-1 | 1627 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203401 | Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements | Huawei, Hisilicon | 38.523-1 | 1628 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204447 | Correction to ENDC TC 8.2.3.9.1-CSI-RS based Intra-frequency measurements | Huawei, Hisilicon | 38.523-1 | 1628 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203402 | Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements | Huawei, Hisilicon | 38.523-1 | 1629 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204448 | Correction to ENDC TC 8.2.3.10.1-CSI-RS based Inter-frequency measurements | Huawei, Hisilicon | 38.523-1 | 1629 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203403 | Correction to ENDC TC 8.2.3.11.X-Measurement Gap | Huawei, Hisilicon | 38.523-1 | 1630 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203404 | Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting | Huawei, Hisilicon | 38.523-1 | 1631 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204449 | Addition of NRDC TC 8.2.3.16.2-Intra-NR Measurement configuration control and reporting | Huawei, Hisilicon | 38.523-1 | 1631 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203405 | Correction to ENDC TC 8.2.6.1.1.X-RLC Failure SCG | Huawei, Hisilicon | 38.523-1 | 1632 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203406 | Addition of NRDC TC 8.2.6.1.2.1-RLC Failure SCG intra-band | Huawei, Hisilicon | 38.523-1 | 1633 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203407 | Addition of NRDC TC 8.2.6.1.2.2-RLC Failure SCG inter-band | Huawei, Hisilicon | 38.523-1 | 1634 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203408 | Addition of NRDC TC 8.2.6.1.2.3-RLC Failure SCG intra-band NC | Huawei, Hisilicon | 38.523-1 | 1635 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203409 | Correction to ENDC TC 8.2.6.2.1-Processing delay | Huawei, Hisilicon, Starpoint | 38.523-1 | 1636 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203410 | Correction to NR TC 9.1.1.3-EAP message transport abnormal | Huawei, Hisilicon | 38.523-1 | 1637 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204457 | Correction to NR TC 9.1.1.3-EAP message transport abnormal | Huawei, Hisilicon | 38.523-1 | 1637 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203411 | Correction to NR TC 9.1.1.6-5G AKA abnormal | Huawei, Hisilicon | 38.523-1 | 1638 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204458 | Correction to NR TC 9.1.1.6-5G AKA abnormal | Huawei, Hisilicon | 38.523-1 | 1638 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203412 | Correction to NR TC 9.1.5.1.1-Initial registration with 5G-GUTI reallocation | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1639 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203413 | Correction to NR TC 9.1.5.1.8-Serving network not authorized | Huawei, HiSilicon, Anritsu, MediaTek Inc., ROHDE & SCHWARZ | 38.523-1 | 1640 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203414 | Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1641 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204460 | Correction to NR TC 9.1.5.1.9-Initial registration with Change of cell into a new tracking area | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1641 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203415 | Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers | Huawei, HiSilicon, Anritsu | 38.523-1 | 1642 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204461 | Correction to NR TC 9.1.6.1.4-Transmission failure with TAI change from lower layers | Huawei, HiSilicon, Anritsu | 38.523-1 | 1642 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203416 | Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category | Huawei, Hisilicon | 38.523-1 | 1643 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204468 | Correction to NR TC 11.3.9-UAC AI-0 Operator Defined Access Category | Huawei, Hisilicon | 38.523-1 | 1643 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203428 | Correction to Idle Mode SoR TC 6.3.1.3 | ZTE Corporation | 38.523-1 | 1644 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203429 | Correction to Idle Mode SoR TC 6.3.1.7 | ZTE Corporation, Huawei, Hisilicon | 38.523-1 | 1645 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204410 | Correction to Idle Mode SoR TC 6.3.1.7 | ZTE Corporation, Huawei, Hisilicon | 38.523-1 | 1645 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203464 | Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq | Huawei, Hisilicon | 38.523-1 | 1646 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204440 | Correction to NR TC 8.1.3.1.14A-CSI-RS based inter-freq | Huawei, Hisilicon | 38.523-1 | 1646 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203478 | Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration | Huawei, Hisilicon | 38.523-1 | 1647 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204411 | Correction to NR TC 6.3.1.8-Steering of UE in roaming after registration | Huawei, Hisilicon | 38.523-1 | 1647 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203481 | Correction to NR TC 6.1.1.4-PLMN selection in shared network environment | Huawei, Hisilicon | 38.523-1 | 1648 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203482 | Addition of new test purpose to test case 8.1.3.1.23 | Tech Mahindra Limited | 38.523-1 | 1649 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204441 | Addition of new test purpose to test case 8.1.3.1.23 | Tech Mahindra Limited | 38.523-1 | 1649 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203483 | Correction to include data path check after handover in test case 8.1.4.1.2 | Tech Mahindra Limited | 38.523-1 | 1650 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204450 | Correction to include data path check after handover in test case 8.1.4.1.2 | Tech Mahindra Limited | 38.523-1 | 1650 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203501 | Correction to 5G NR Idle mode Speed-dependent Cell reselection test case 6.1.2.19 | Keysight Technologies UK | 38.523-1 | 1651 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203502 | Correction to 5G NR Idle mode test case 6.4.2.2 | Keysight Technologies UK | 38.523-1 | 1652 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203503 | Correction to NR CA RRC test cases 8.1.3.1.18.x | Keysight Technologies UK | 38.523-1 | 1653 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203504 | Correction to NR RRC test cases 8.1.3.2.3 and 8.1.3.2.4 | Keysight Technologies UK | 38.523-1 | 1654 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203505 | Correction to 5GMM test case 9.1.5.1.13 | Keysight Technologies UK | 38.523-1 | 1655 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203513 | Correction to NR MAC test case 7.1.1.5.2 | Keysight Technologies UK, Starpoint | 38.523-1 | 1656 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204420 | Correction to NR MAC test case 7.1.1.5.2 | Keysight Technologies UK, Starpoint | 38.523-1 | 1656 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203518 | Introduction of a new test case for voice fallback indication under EPS Fallback with handover | CATT, TDIA | 38.523-1 | 1657 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204516 | Introduction of a new test case for voice fallback indication under EPS Fallback with handover | CATT, TDIA | 38.523-1 | 1657 | 1 | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203519 | Introduction of a new test case for voice fallback indication under EPS Fallback with redirection | CATT, TDIA | 38.523-1 | 1658 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204517 | Introduction of a new test case for voice fallback indication under EPS Fallback with redirection | CATT, TDIA | 38.523-1 | 1658 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203521 | Correction to NR RRC test case 8.1.3.1.20 | Starpoint, TDIA | 38.523-1 | 1659 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204442 | Correction to NR RRC test case 8.1.3.1.20 | Starpoint, TDIA | 38.523-1 | 1659 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203522 | Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC | China telecom, Datang linktester | 38.523-1 | 1660 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204513 | Addtion of new test case 8.1.4.2.1.2 for Inter-RAT handover from NR to EN-DC | China Telecom, Datang linktester | 38.523-1 | 1660 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203524 | Corrections to NR MAC Test Case 7.1.1.5.4 | Starpoint, TDIA | 38.523-1 | 1661 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203535 | Splitting and updates to NR RLC test case 7.1.2.3.5 | MCC TF160 | 38.523-1 | 1662 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203536 | Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4 | MCC TF160 | 38.523-1 | 1663 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204425 | Updates to NR RLC test cases 7.1.2.3.3 and 7.1.2.3.4 | MCC TF160 | 38.523-1 | 1663 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203537 | Correction to NR test case 8.1.3.1.13 | MCC TF160 | 38.523-1 | 1664 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203538 | Correction to NR test case 8.1.3.1.14A | MCC TF160 | 38.523-1 | 1665 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203539 | Correction to NR test case 8.1.3.1.15A | MCC TF160 | 38.523-1 | 1666 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203540 | Editorial correction to EN-DC test case 8.2.3.5.1 | MCC TF160 | 38.523-1 | 1667 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203541 | Correction to EN-DC test cases 8.2.3.9.1 and 8.2.3.10.1 | MCC TF160 | 38.523-1 | 1668 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203565 | Correction to NR TC 6.2.2.1-N2L cell reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1669 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204412 | Correction to NR TC 6.2.2.1-N2L cell reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1669 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203566 | Correction to NR TC 6.2.2.2-L2N cell reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1670 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204413 | Correction to NR TC 6.2.2.2-L2N cell reselection | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1670 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203567 | Correction to NR TC 7.1.1.1.2-Random access procedure for Preamble selected by MAC itself | Huawei, Hisilicon, Datang Linktester | 38.523-1 | 1671 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203571 | Correction to Inter-RAT HO test case 8.1.4.2.2 | China Telecommunications | 38.523-1 | 1672 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204451 | Correction to Inter-RAT HO test case 8.1.4.2.2 | China Telecommunications | 38.523-1 | 1672 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203576 | Correction to NR5GC test case 8.1.3.1.11 | Starpoint, Huawei, HiSilicon,TDIA | 38.523-1 | 1673 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204443 | Correction to NR5GC test case 8.1.3.1.11 | Starpoint, Huawei, HiSilicon,TDIA | 38.523-1 | 1673 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203578 | Correction to NR5GC test case 8.1.3.1.12 | Starpoint, Huawei, HiSilicon,TDIA | 38.523-1 | 1674 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204444 | Correction to NR5GC test case 8.1.3.1.12 | Starpoint, Huawei, HiSilicon,TDIA | 38.523-1 | 1674 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203584 | Addition of NR-DC RRC test case 8.2.2.8.2 | ANRITSU LTD | 38.523-1 | 1675 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204445 | Addition of NR-DC RRC test case 8.2.2.8.2 | ANRITSU LTD | 38.523-1 | 1675 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203589 | Correction to NR RRC TC 8.1.5.1.1 | MediaTek Inc., Keysight Technologies | 38.523-1 | 1676 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204456 | Correction to NR RRC TC 8.1.5.1.1 | MediaTek Inc., Keysight Technologies | 38.523-1 | 1676 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203590 | Correction to the power level of Idle mode test cases | MediaTek Inc. | 38.523-1 | 1677 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204414 | Correction to the power level of Idle mode test cases | MediaTek Inc. | 38.523-1 | 1677 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203591 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | 38.523-1 | 1678 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204379 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | 38.523-1 | 1678 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204545 | Correction to Idle mode test case 6.4.1.2 | MediaTek Inc. | 38.523-1 | 1678 | 2 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203592 | Correction to Inter-RAT HO test case 8.1.4.2.1 | China Telecommunications | 38.523-1 | 1679 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204452 | Correction to Inter-RAT HO test case 8.1.4.2.1 | China Telecommunications | 38.523-1 | 1679 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203593 | Correction to Idle mode test case 6.1.2.9 | MediaTek Inc. | 38.523-1 | 1680 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204380 | Correction to Idle mode test case 6.1.2.9 | MediaTek Inc. | 38.523-1 | 1680 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203594 | Correction to NR TC 6.3.1.8-SOR after registration with Automatic PLMN selection mode | Huawei, Hisilicon | 38.523-1 | 1681 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203596 | Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs | NTT DOCOMO INC. | 38.523-1 | 1682 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204426 | Modification of PDCP TC 7.1.3.5.2 to add testing for change of ul-DataSplitThreshold and transmission of SRs | NTT DOCOMO INC. | 38.523-1 | 1682 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203597 | Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath | NTT DOCOMO INC. | 38.523-1 | 1683 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204427 | Addition of new PDCP TC 7.1.3.5.6 Change of primaryPath | NTT DOCOMO INC. | 38.523-1 | 1683 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203598 | Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC | NTT DOCOMO INC. | 38.523-1 | 1684 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204428 | Addition of new PDCP TC 7.1.3.5.7.1 Change of primaryPath / SCG Release and Addition / EN-DC | NTT DOCOMO INC. | 38.523-1 | 1684 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203603 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | 38.523-1 | 1685 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204433 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | 38.523-1 | 1685 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203610 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | 38.523-1 | 1686 | - | Rel-16 | B | TEI16_Test | withdrawn |
| R5-203611 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | 38.523-1 | 1687 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204514 | Update test case 8.1.5.1.1 to add UE capability nr-HO-ToEN-DC-r16 | China Telecom,Datang linktester | 38.523-1 | 1687 | 1 | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203644 | Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | 38.523-1 | 1688 | - | Rel-16 | B | TEI16_Test | revised |
| R5-204515 | Update of test case 8.2.1.1.1 to support Inter-RAT handover from NR to EN-DC | China Telecom,Datang linktester | 38.523-1 | 1688 | 1 | Rel-16 | B | TEI16_Test | withdrawn |
| R5-203645 | Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1 | MediaTek Inc. | 38.523-1 | 1689 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204381 | Correction to the power level of NR RRC TC 8.1.1.2.1 and 8.1.1.4.1 | MediaTek Inc. | 38.523-1 | 1689 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203648 | Editorial updates to NR5G Idle Mode TC 6.1.2.11 | Qualcomm CDMA Technologies | 38.523-1 | 1690 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203649 | Corrections to NR5G BWP TC 7.1.1.8.1 | Qualcomm CDMA Technologies, MCC TF160, Anritsu Ltd, Rohde & Schwarz | 38.523-1 | 1691 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203650 | Corrections to NR5G RRC NR-DC TC 8.2.2.4.2 and 8.2.2.5.2 | Qualcomm CDMA Technologies | 38.523-1 | 1692 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203654 | Corrections to NR5G Idle Mode TC 6.4.2.1 | Qualcomm CDMA Technologies | 38.523-1 | 1693 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204415 | Corrections to NR5G Idle Mode TC 6.4.2.1 | Qualcomm CDMA Technologies | 38.523-1 | 1693 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203655 | Corrections to NR5G MAC TC 7.1.1.2.4 | Qualcomm CDMA Technologies | 38.523-1 | 1694 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204421 | Corrections to NR5G MAC TC 7.1.1.2.4 | Qualcomm CDMA Technologies | 38.523-1 | 1694 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203656 | Corrections to NR5G MAC DRX TC 7.1.1.5.3 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.523-1 | 1695 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203657 | Corrections to NR5G RRC TC 8.1.3.1.16 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.523-1 | 1696 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203658 | Void NR5G NAS TC 9.1.5.2.6 | Qualcomm CDMA Technologies | 38.523-1 | 1697 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203659 | Corrections to NR5G MAC TC 7.1.1.2.1 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.523-1 | 1698 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203660 | Corrections to NR5G MAC TC 7.1.1.1.2 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.523-1 | 1699 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204422 | Corrections to NR5G MAC TC 7.1.1.1.2 | Qualcomm CDMA Technologies, Keysight Technologies UK Ltd. | 38.523-1 | 1699 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203661 | Corrections to NR5G Idle Mode TC 6.1.2.13 | Qualcomm CDMA Technologies | 38.523-1 | 1700 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204416 | Corrections to NR5G Idle Mode TC 6.1.2.13 | Qualcomm CDMA Technologies | 38.523-1 | 1700 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203663 | Corrections to NR5G RLC TC 7.1.2.3.11 | Qualcomm CDMA Technologies | 38.523-1 | 1701 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204512 | Corrections to NR5G RLC TC 7.1.2.3.11 | Qualcomm CDMA Technologies | 38.523-1 | 1701 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203664 | Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1 | Qualcomm CDMA Technologies | 38.523-1 | 1702 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204453 | Corrections to NR5G RRC IRAT TC 8.1.4.2.2.1 | Qualcomm CDMA Technologies | 38.523-1 | 1702 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203665 | Corrections to NR5G RRC CA TCs to add Data Path verification | Qualcomm CDMA Technologies | 38.523-1 | 1703 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203666 | Corrections to ENDC RRC CA TCs to add Data Path verification | Qualcomm CDMA Technologies | 38.523-1 | 1704 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203667 | Correction to Multilayer TC 11.3.8 | MediaTek Inc. | 38.523-1 | 1705 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203702 | Correction to 5GC TC 9.1.5.2.9 | MediaTek Inc. | 38.523-1 | 1706 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204462 | Correction to 5GC TC 9.1.5.2.9 | MediaTek Inc. | 38.523-1 | 1706 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203705 | Correction to NR test case 7.1.2.2.5 | ZTE | 38.523-1 | 1707 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203706 | Correction to NR test case 7.1.2.3.1 | ZTE | 38.523-1 | 1708 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203707 | Correction to NR test case 7.1.3.5.5 | ZTE | 38.523-1 | 1709 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204429 | Correction to NR test case 7.1.3.5.5 | ZTE | 38.523-1 | 1709 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203708 | Correction to NR test case 7.1.4.2 | ZTE | 38.523-1 | 1710 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203709 | Correction to NR test case 8.1.3.1.5 | ZTE | 38.523-1 | 1711 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203710 | Correction to NR test case 8.1.3.1.8 | ZTE | 38.523-1 | 1712 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203711 | Correction to NR test case 8.1.3.1.13 | ZTE | 38.523-1 | 1713 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203712 | Correction to NR test case 8.1.4.16 | ZTE, MCC TF160 | 38.523-1 | 1714 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204360 | Correction to NR test case 8.1.4.16 | ZTE, MCC TF160 | 38.523-1 | 1714 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203728 | Correction to NR test case 8.1.3.1.16 | ZTE | 38.523-1 | 1715 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203737 | Correction to 5GC TC 9.1.3.1 | MediaTek Inc. | 38.523-1 | 1716 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204459 | Correction to 5GC TC 9.1.3.1 | MediaTek Inc. | 38.523-1 | 1716 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203739 | Corrections to 5GS Non-3GPP Access TC 9.2.1.1 | ZTE Corporation | 38.523-1 | 1717 | - | Rel-16 | F | TEI15_Test, 5GS_Ph1-CT_n3GPPA-UEConTest | agreed |
| R5-203740 | Corrections to 5GS Non-3GPP Access TC 9.2.5.1.4 | ZTE Corporation | 38.523-1 | 1718 | - | Rel-16 | F | TEI15_Test, 5GS_Ph1-CT_n3GPPA-UEConTest | agreed |
| R5-203741 | Corrections to 5GS Non-3GPP Access TC 9.2.7.1 | ZTE Corporation | 38.523-1 | 1719 | - | Rel-16 | F | TEI15_Test, 5GS_Ph1-CT_n3GPPA-UEConTest | agreed |
| R5-203742 | Corrections to 5GS Non-3GPP Access TC 9.2.7.2 | ZTE Corporation | 38.523-1 | 1720 | - | Rel-16 | F | TEI15_Test, 5GS_Ph1-CT_n3GPPA-UEConTest | agreed |
| R5-203745 | Correction to 5G NR Idle mode test case 6.4.3.1 | Keysight Technologies UK | 38.523-1 | 1721 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203746 | Correction to 5G NR Idle mode inter-RAT test cases | Keysight Technologies UK | 38.523-1 | 1722 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204417 | Correction to 5G NR Idle mode inter-RAT test cases | Keysight Technologies UK | 38.523-1 | 1722 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203747 | Correction to NR RRC IRAT test case 8.1.1.3.4 | Keysight Technologies UK | 38.523-1 | 1723 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204434 | Correction to NR RRC IRAT test case 8.1.1.3.4 | Keysight Technologies UK | 38.523-1 | 1723 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203749 | Update to test case NR5GC 7.1.3.5.3 (NR-DC) | ROHDE & SCHWARZ | 38.523-1 | 1724 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204430 | Update to test case NR5GC 7.1.3.5.3 (NR-DC) | ROHDE & SCHWARZ | 38.523-1 | 1724 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203750 | Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2 | ROHDE & SCHWARZ, ZTE | 38.523-1 | 1725 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204431 | Correction to NR5GC SDAP test cases 7.1.4.1 and 7.1.4.2 | ROHDE & SCHWARZ, ZTE | 38.523-1 | 1725 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203752 | Correction to Multilayer TC 11.1.2 and 11.1.5 | MediaTek Inc. | 38.523-1 | 1726 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204465 | Correction to Multilayer TC 11.1.2 and 11.1.5 | MediaTek Inc. | 38.523-1 | 1726 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203772 | Correction to NR5GC testcase 9.1.4.1 | ROHDE & SCHWARZ | 38.523-1 | 1727 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203785 | Correction to NR5GC testcase 10.1.1.2 | ROHDE & SCHWARZ, Qualcomm | 38.523-1 | 1728 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203810 | Correction to NR5GC test case 6.1.2.9 | ANRITSU LTD | 38.523-1 | 1729 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203811 | Correction to NR CA RRC Test cases 8.1.3.1.17.x and 8.1.3.1.18.x | ANRITSU LTD | 38.523-1 | 1730 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203814 | Addition of NR-DC RRC test case 8.2.3.14.2 | ANRITSU LTD | 38.523-1 | 1731 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204454 | Addition of NR-DC RRC test case 8.2.3.14.2 | ANRITSU LTD | 38.523-1 | 1731 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203996 | Corrections to EPS Fallback regarding IMS procedures | ROHDE & SCHWARZ | 38.523-1 | 1732 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204466 | Corrections to EPS Fallback regarding IMS procedures | ROHDE & SCHWARZ | 38.523-1 | 1732 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204015 | Correction of NR TC 6.2.2.1 | TDIA, CATT | 38.523-1 | 1733 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204016 | Correction to NR TC 8.1.4.1.8.X-Scell no change | Huawei, Hisilicon | 38.523-1 | 1734 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204018 | Correction of NR TC 6.2.2.2 | TDIA, CATT | 38.523-1 | 1735 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204019 | Correction to NR5G UAC TC 11.3.8 | TDIA, CATT | 38.523-1 | 1736 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204029 | Correction to NR5GC testcase 8.1.1.3.2 | ROHDE & SCHWARZ, Qualcomm | 38.523-1 | 1737 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204435 | Correction to NR5GC testcase 8.1.1.3.2 | ROHDE & SCHWARZ, Qualcomm | 38.523-1 | 1737 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204091 | Correction to test case 11.1.7 | MediaTek Inc. | 38.523-1 | 1738 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204467 | Correction to test case 11.1.7 | MediaTek Inc. | 38.523-1 | 1738 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204106 | Correction to NR RRC TC 8.1.3.2.2 | MediaTek Inc. | 38.523-1 | 1739 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204382 | Correction to NR RRC TC 8.1.3.2.2 | MediaTek Inc. | 38.523-1 | 1739 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204107 | Correction to NR test case 7.1.2.3.11 | ZTE | 38.523-1 | 1740 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204130 | Correction to 9.x test cases to handle IMS Re-registration (moving between HPLMN and VPLMN) | ROHDE & SCHWARZ, Qualcomm | 38.523-1 | 1741 | - | Rel-16 | F | TEI8_Test | withdrawn |
| R5-204133 | Correction to MR-DC RRC TC 8.2.3.8.1 | MediaTek Inc. | 38.523-1 | 1742 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204455 | Correction to MR-DC RRC TC 8.2.3.8.1 | MediaTek Inc. | 38.523-1 | 1742 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204206 | Addition of NR-DC MAC Test Case | Lenovo, Motorola Mobility | 38.523-1 | 1743 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204423 | Addition of NR-DC MAC Test Case | Lenovo, Motorola Mobility | 38.523-1 | 1743 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204217 | Addition of NR-DC RRC test case 8.2.2.9.2 | Keysight Technologies UK Ltd | 38.523-1 | 1744 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204236 | Correction to NR5G RRC TC 8.1.1.4.1 | Qualcomm CDMA Technologies | 38.523-1 | 1745 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204436 | Correction to NR5G RRC TC 8.1.1.4.1 | Qualcomm CDMA Technologies | 38.523-1 | 1745 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204237 | Correction to NR5G RRC TC 8.1.4.1.2 | Qualcomm CDMA Technologies | 38.523-1 | 1746 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204239 | Addition of NR5G UAC TC 11.3.2 | Qualcomm CDMA Technologies | 38.523-1 | 1747 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204518 | Addition of NR5G UAC TC 11.3.2 | Qualcomm CDMA Technologies | 38.523-1 | 1747 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204254 | Correction to NR UE Capability test case 8.1.5.1.1 | Qualcomm Incorporated | 38.523-1 | 1748 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204334 | Correction to NR5GC RRC test case 8.1.5.2.2 | Keysight Technologies UK | 38.523-1 | 1749 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204336 | Correction to test case 11.1.3 | MediaTek Inc. | 38.523-1 | 1750 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204341 | Correction to the NR5GC testcase 8.1.3.1.12 | ANRITSU LTD | 38.523-1 | 1751 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204342 | Correction to NR TC 9.1.5.1.14 | Qualcomm CDMA Technologies | 38.523-1 | 1752 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204463 | Correction to NR TC 9.1.5.1.14 | Qualcomm CDMA Technologies | 38.523-1 | 1752 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204343 | Corrections to NR5G NAS TC 9.1.6.1.3 | Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA | 38.523-1 | 1753 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204464 | Corrections to NR5G NAS TC 9.1.6.1.3 | Qualcomm CDMA Technologies, MCC TF160, Starpoint, TDIA | 38.523-1 | 1753 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204359 | Correction to NR test case 8.1.4.1.6 | ZTE, MCC TF160 | 38.523-1 | 1754 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204363 | Corrections to NR5G PDCP TC 7.1.3.4.1 | Qualcomm CDMA Technologies | 38.523-1 | 1755 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204372 | Correction to NR5GC CA RRC test cases 8.1.2.1.5.x | Keysight Technologies UK | 38.523-1 | 1756 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203353 | Add IEs MeasResultsSL and MeasTriggerQuantityEUTRA | Ericsson | 38.523-2 | 0087 | - | Rel-16 | F | TEI16_Test | withdrawn |
| R5-203417 | Addition of applicability for NR TCs | Huawei, Hisilicon | 38.523-2 | 0088 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204469 | Addition of applicability for NR TCs | Huawei, Hisilicon | 38.523-2 | 0088 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203418 | Correction to applicability of NR TCs | Huawei, Hisilicon | 38.523-2 | 0089 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204470 | Correction to applicability of NR TCs | Huawei, Hisilicon | 38.523-2 | 0089 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203475 | Update of 5G-NR test cases applicability | Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility | 38.523-2 | 0090 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204471 | Update of 5G-NR test cases applicability | Qualcomm Incorporated, MCC TF160, MediaTek Inc., Anritsu Ltd, Keysight Technologies UK, Lenovo, Motorola Mobility | 38.523-2 | 0090 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203520 | Addition of test applicabilities of test cases for voice fallback indication | CATT, TDIA | 38.523-2 | 0091 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204519 | Addition of test applicabilities of test cases for voice fallback indication | CATT, TDIA | 38.523-2 | 0091 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203542 | Splitting and updates to applicability of NR RLC test case 7.1.2.3.5 | MCC TF160 | 38.523-2 | 0092 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203599 | Update applicability of Inter-RAT handover from NR to EN-DC test case | China Telecom,Datang linktester | 38.523-2 | 0093 | - | Rel-16 | F | TEI16_Test | revised |
| R5-204520 | Update applicability of Inter-RAT handover from NR to EN-DC test case | China Telecom,Datang linktester | 38.523-2 | 0093 | 1 | Rel-16 | F | TEI16_Test | agreed |
| R5-203612 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | 38.523-2 | 0094 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204472 | Addition of new RRC TC for checking extended / spare field handling in SI | NTT DOCOMO INC. | 38.523-2 | 0094 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203890 | Removal of void test case and correction of condition for Inter-band measurements test cases | CAICT | 38.523-2 | 0095 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204473 | Removal of void test case and correction of condition for Inter-band measurements test cases | CAICT | 38.523-2 | 0095 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203899 | Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1 | NTT DOCOMO INC. | 38.523-2 | 0096 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204474 | Test applicability for new PDCP TC 7.1.3.5.6 and TC7.1.3.5.7.1 | NTT DOCOMO INC. | 38.523-2 | 0096 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203543 | 5G Test Models updates | MCC TF160, Keysight, Samsung | 38.523-3 | 1233 | - | Rel-15 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204475 | 5G Test Models updates | MCC TF160, Keysight, Samsung | 38.523-3 | 1233 | 1 | Rel-15 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203234 | Update TC 8.5.2.1.1.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0747 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203235 | Update TC 8.5.2.2.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0748 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203236 | Update TC 8.5.2.3.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0749 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204783 | Update TC 8.5.2.3.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0749 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203241 | Update TC 4.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0750 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204878 | Update TC 4.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0750 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203242 | Update TC 4.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0751 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204775 | Update TC 4.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0751 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203243 | Update TC 4.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0752 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204879 | Update TC 4.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0752 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203244 | Update TC 4.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0753 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204776 | Update TC 4.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0753 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203245 | Update TC 6.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0754 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204880 | Update TC 6.7.4.1.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0754 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203246 | Update TC 6.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0755 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204778 | Update TC 6.7.4.1.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0755 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203247 | Update TC 6.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0756 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204881 | Update TC 6.7.4.2.1 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0756 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203248 | Update TC 6.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0757 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204779 | Update TC 6.7.4.2.2 with TT results and message contents | ROHDE & SCHWARZ | 38.533 | 0757 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203249 | Annex E and F update with TT results for 8.5.2.x.x iRAT periodic reporting test cases | ROHDE & SCHWARZ | 38.533 | 0758 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203250 | Annex E and F update with TT results for 4.7.4.x.x EN-DC L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | 38.533 | 0759 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203251 | Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | 38.533 | 0760 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204784 | Annex E and F update with TT results for 6.7.4.x.x NR SA L1-RSRP periodic reporting test cases | ROHDE & SCHWARZ | 38.533 | 0760 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203252 | Void unnecessary TC 8.5.2.1.1.2 | ROHDE & SCHWARZ | 38.533 | 0761 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203264 | Correction to the test procedure of NR SA event triggered tests | ROHDE & SCHWARZ | 38.533 | 0762 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204780 | Correction to the test procedure of NR SA event triggered tests | ROHDE & SCHWARZ | 38.533 | 0762 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203265 | Correction to the test procedure of NR SA event triggered tests inter-freq | ROHDE & SCHWARZ | 38.533 | 0763 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204781 | Correction to the test procedure of NR SA event triggered tests inter-freq | ROHDE & SCHWARZ | 38.533 | 0763 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203266 | Correction to the test procedure of NR SA event triggered tests inter-RAT | ROHDE & SCHWARZ | 38.533 | 0764 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204782 | Correction to the test procedure of NR SA event triggered tests inter-RAT | ROHDE & SCHWARZ | 38.533 | 0764 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203267 | [EDITORIAL] Fix formatting issues throwing DOCX conversion errors in TS 38.533 | ROHDE & SCHWARZ | 38.533 | 0765 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203268 | Correction of test applicability for EN-DC event-triggered tests | ROHDE & SCHWARZ | 38.533 | 0766 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203269 | Correction of test applicability for NR SA event-triggered tests | ROHDE & SCHWARZ | 38.533 | 0767 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203270 | Adding annex table for iRAT measurement configuration | ROHDE & SCHWARZ | 38.533 | 0768 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203271 | Clarification on the usage of auxiliary bands | ROHDE & SCHWARZ, Qualcomm Finland RFFE Oy | 38.533 | 0769 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203272 | Remove IE includeBeamMeasurements from 6.6.1.5 and 6.6.1.6 | ROHDE & SCHWARZ | 38.533 | 0770 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203274 | Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap | ROHDE & SCHWARZ | 38.533 | 0771 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204777 | Correction of measurement gap configuration for intra-frequency even-triggered tests needing gap | ROHDE & SCHWARZ | 38.533 | 0771 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203280 | n26 addition to group of bands in 38.533 | Dish Network | 38.533 | 0772 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203299 | Corrected test description in non-DRX test case 6.5.1.2 | Keysight Technologies UK Ltd | 38.533 | 0773 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203300 | Correction of comment for monitoringSymbolsWithinSlot | Keysight Technologies UK Ltd | 38.533 | 0774 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203301 | Correction of delta offset application for Cell 2 in test case 4.7.1.2.1 | Keysight Technologies UK Ltd | 38.533 | 0775 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203302 | Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133 | Keysight Technologies UK Ltd, Qualcomm Incorporated | 38.533 | 0776 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204882 | Gap Pattern Id correction in section 6.6.2 to align to core spec 38.133 | Keysight Technologies UK Ltd, Qualcomm Incorporated | 38.533 | 0776 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203303 | PUSCH allocation correction in test case 6.4.3.1 | Keysight Technologies UK Ltd | 38.533 | 0777 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203304 | Correction to the RRC Reconfiguration message for measurements | ROHDE & SCHWARZ | 38.533 | 0778 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203306 | Update extreme conditions limits in TC 4.7.1.2.1 | ROHDE & SCHWARZ | 38.533 | 0779 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203307 | Update extreme conditions limits in TC 6.7.1.2.1 | ROHDE & SCHWARZ | 38.533 | 0780 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203308 | Update extreme conditions limits in TC 4.7.1.2.1 and TC 6.7.1.2.1 - Annex F | ROHDE & SCHWARZ | 38.533 | 0781 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203309 | Correction power offset for Band Group F | ROHDE & SCHWARZ | 38.533 | 0782 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203314 | CR to update the RRM FR2 MUs in Annex F | ROHDE & SCHWARZ | 38.533 | 0783 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204885 | CR to update the RRM FR2 MUs in Annex F | ROHDE & SCHWARZ | 38.533 | 0783 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203315 | Add information on the AoA change during test for RRM FR2 tests | ROHDE & SCHWARZ | 38.533 | 0784 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204886 | Add information on the AoA change during test for RRM FR2 tests | ROHDE & SCHWARZ | 38.533 | 0784 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203316 | Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values | ROHDE & SCHWARZ | 38.533 | 0785 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204785 | Correction in A.1.4 CSI-RS for nzp-CSI-RS-ResourceId values | ROHDE & SCHWARZ | 38.533 | 0785 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203317 | Removing SearchSpaceId and ControlResourceSetId modification | Keysight Technologies UK Ltd | 38.533 | 0786 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203318 | Test Procedure correction in test case 6.5.1.3 for definition of Point C | Keysight Technologies UK Ltd | 38.533 | 0787 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204883 | Test Procedure correction in test case 6.5.1.3 for definition of Point C | Keysight Technologies UK Ltd | 38.533 | 0787 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203319 | Unification of cell frequency for FR1-FR1 test cases | Keysight Technologies UK Ltd | 38.533 | 0788 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203431 | Addition of new RRM Test Cases in clause 7.5.5 | ZTE Corporation | 38.533 | 0789 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204884 | Addition of new RRM Test Cases in clause 7.5.5 | ZTE Corporation | 38.533 | 0789 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203732 | Set ss-sinr request to false for EN-DC RRM measurement accuracy tests | ROHDE & SCHWARZ | 38.533 | 0790 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203733 | Set ss-sinr request to false for NR SA RRM measurement accuracy tests | ROHDE & SCHWARZ | 38.533 | 0791 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203757 | Update of PDSCH RMC in Annex A.1.1 | MediaTek Inc. | 38.533 | 0792 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204730 | Update of PDSCH RMC in Annex A.1.1 | MediaTek Inc. | 38.533 | 0792 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203820 | Correction of RRM Test Case 6.1.1.1 | MediaTek Inc. | 38.533 | 0793 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204733 | Correction of RRM Test Case 6.1.1.1 | MediaTek Inc. | 38.533 | 0793 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203828 | Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0794 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204985 | Update of FR1 Test Tolerance in 4.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0794 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203829 | Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | 38.533 | 0795 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204986 | Update of FR1 Test Tolerance in 4.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | 38.533 | 0795 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203830 | Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance | Huawei, HiSilicon, CAICT | 38.533 | 0796 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204987 | Addition of new Test Case 4.5.5.3 CSI-RS based BFR non-DRX with FR1 Test Tolerance | Huawei, HiSilicon, CAICT | 38.533 | 0796 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203831 | Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon, CAICT | 38.533 | 0797 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204988 | Update of FR1 Test Tolerance in 4.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon, CAICT | 38.533 | 0797 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203832 | Update of 4.5.6.1.0 minimum requirement for DCI-based BWP switch | Huawei, HiSilicon | 38.533 | 0798 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203833 | Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch | Huawei, HiSilicon | 38.533 | 0799 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204989 | Update of FR1 Test Tolerance in 4.5.6.1.1 DCI-based BWP switch | Huawei, HiSilicon | 38.533 | 0799 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203834 | Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell | Huawei, HiSilicon | 38.533 | 0800 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204990 | Update of FR1 Test Tolerance in 4.5.6.1.2 DCI-based BWP switch with SCell | Huawei, HiSilicon | 38.533 | 0800 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203835 | Update of 4.5.6.2.0 minimum requirement for RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0801 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203836 | Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0802 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204991 | Update of FR1 Test Tolerance in 4.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0802 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203837 | Update of FR1 Test Tolerance in 6.3.2.1.3 RRC re-establishment without serving cell timing | Huawei, HiSilicon | 38.533 | 0803 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203838 | Addition of 6.5.2.0 minimum requirement for interruptions during measurements on NR SCC | Huawei, HiSilicon | 38.533 | 0804 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203839 | Update of 6.5.2.1 interruptions during measurements on deactivated NR SCC | Huawei, HiSilicon, CAICT | 38.533 | 0805 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203840 | Addition of new Test Case 6.5.3.1 SCell activation and deactivation for 160ms cycle | Huawei, HiSilicon, CAICT | 38.533 | 0806 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203841 | Addition of new Test Case 6.5.3.2 SCell activation and deactivation for 320ms cycle | Huawei, HiSilicon, CAICT | 38.533 | 0807 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203842 | Addition of new Test Case 6.5.3.3 SCell activation and deactivation of unknown SCell | Huawei, HiSilicon, CAICT | 38.533 | 0808 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203843 | Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0809 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204992 | Update of FR1 Test Tolerance in 6.5.5.1 SSB based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0809 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203844 | Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | 38.533 | 0810 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204993 | Update of FR1 Test Tolerance in 6.5.5.2 SSB based BFR in DRX | Huawei, HiSilicon | 38.533 | 0810 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203845 | Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0811 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204994 | Update of FR1 Test Tolerance in 6.5.5.3 CSI-RS based BFR in non-DRX | Huawei, HiSilicon | 38.533 | 0811 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203846 | Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon | 38.533 | 0812 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204995 | Update of FR1 Test Tolerance in 6.5.5.4 CSI-RS based BFR in DRX | Huawei, HiSilicon | 38.533 | 0812 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203847 | Update of 6.5.6.1.0 minimum requirement for DCI-based BWP switch | Huawei, HiSilicon | 38.533 | 0813 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203848 | Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell | Huawei, HiSilicon | 38.533 | 0814 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204996 | Update of FR1 Test Tolerance in 6.5.6.1.1 DCI-based BWP switch with SCell | Huawei, HiSilicon | 38.533 | 0814 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203849 | Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance | Huawei, HiSilicon | 38.533 | 0815 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204997 | Addition of new Test Case 6.5.6.1.2 DCI-based BWP switch with FR1 Test Tolerance | Huawei, HiSilicon | 38.533 | 0815 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203850 | Update of 6.5.6.2.0 minimum requirement for RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0816 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203851 | Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0817 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204998 | Update of FR1 Test Tolerance in 6.5.6.2.1 RRC-based BWP switch | Huawei, HiSilicon | 38.533 | 0817 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203852 | Update of test parameters in 6.3.1.4 inter-RAT handover | Huawei, HiSilicon | 38.533 | 0818 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204999 | Update of test parameters in 6.3.1.4 inter-RAT handover | Huawei, HiSilicon | 38.533 | 0818 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203853 | Correction to FR1 intra-frequency measurement with gap test cases | Huawei, HiSilicon | 38.533 | 0819 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203854 | Update of FR1 Test Tolerance in Annex F | Huawei, HiSilicon | 38.533 | 0820 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204786 | Update of FR1 Test Tolerance in Annex F | Huawei, HiSilicon | 38.533 | 0820 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203855 | Update of Cell mapping in Annex E | Huawei, HiSilicon | 38.533 | 0821 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203856 | Update of default configurations for RMC scheduling in Annex A | Huawei, HiSilicon | 38.533 | 0822 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205000 | Update of default configurations for RMC scheduling in Annex A | Huawei, HiSilicon | 38.533 | 0822 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203862 | Correction to default configurations in Annex H | Huawei, HiSilicon | 38.533 | 0823 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204787 | Correction to default configurations in Annex H | Huawei, HiSilicon | 38.533 | 0823 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203895 | Correction of RRM Test Case 6.1.1.2 | MediaTek Inc. | 38.533 | 0824 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204734 | Correction of RRM Test Case 6.1.1.2 | MediaTek Inc. | 38.533 | 0824 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203896 | Correction of RRM Test Case 7.1.1.1 | MediaTek Inc. | 38.533 | 0825 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204735 | Correction of RRM Test Case 7.1.1.1 | MediaTek Inc. | 38.533 | 0825 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203897 | Correction of RRM Test Case 7.1.1.2 | MediaTek Inc. | 38.533 | 0826 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204736 | Correction of RRM Test Case 7.1.1.2 | MediaTek Inc. | 38.533 | 0826 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204034 | CR to 38.533 on RRM Test Cases in clause 7.5.3 | Samsung R&D Institute UK | 38.533 | 0827 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204036 | CR to 38.533 on RRM Test Cases in clause 7.5.7 | Samsung R&D Institute UK | 38.533 | 0828 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204068 | Correction to FR2 timing advance adjustment accuracy | Anritsu | 38.533 | 0829 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204069 | Correction to EN-DC FR2 interruptions at transitions between active and non-active during DRX | Anritsu | 38.533 | 0830 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204070 | Addition of E-UTRA Test frequency selection rule for IRAT test cases | Anritsu | 38.533 | 0831 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204071 | Correction on event-triggered reporting with gap in DRX and DRX configuration settings for NR serving cell | Anritsu | 38.533 | 0832 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204072 | Correction to EN-DC and SA FR1-FR1 SS-RSRP and SS-RSRQ periodical measurement accuracy | Anritsu | 38.533 | 0833 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204073 | Correction to SS-RSRQ periodical measurement accuracy | Anritsu | 38.533 | 0834 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204074 | Correction to connection diagram for radio link monitoring tests | Anritsu | 38.533 | 0835 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204941 | Correction to connection diagram for radio link monitoring tests | Anritsu | 38.533 | 0835 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204075 | Correction to message configuration for radio link monitoring tests | Anritsu | 38.533 | 0836 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204076 | Correction to NR SA FR1 E-UTRA RRC connection release with redirection | Anritsu | 38.533 | 0837 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204077 | Correction to SRS PeriodicityAndOffset for Timing Advance tests | Anritsu | 38.533 | 0838 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204078 | Correction to PDSCH reference measurement channel | Anritsu | 38.533 | 0839 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204079 | Correction to CSI-RS for tracking for TDD FR2 | Anritsu | 38.533 | 0840 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204116 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.1 | Ericsson | 38.533 | 0841 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204117 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2 | Ericsson | 38.533 | 0842 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204942 | Correction of EN-DC FR2 SSB-based L1-RSRP measurement test case 5.6.3.2 | Ericsson | 38.533 | 0842 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204118 | Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.3 | Ericsson | 38.533 | 0843 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204119 | Correction of EN-DC FR2 CSI-RS-based L1-RSRP measurement test case 5.6.3.4 | Ericsson | 38.533 | 0844 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204120 | Correction of FR2 condition tables in Annex B | Ericsson | 38.533 | 0845 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204943 | Correction of FR2 condition tables in Annex B | Ericsson | 38.533 | 0845 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204121 | Introduction of band n259 in clause 3 | Ericsson | 38.533 | 0846 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204944 | Introduction of band n259 in clause 3 | Ericsson | 38.533 | 0846 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204122 | Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.1 | Ericsson | 38.533 | 0847 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204123 | Correction of NR SA FR2 SSB-based L1-RSRP measurement test case 7.6.3.2 | Ericsson | 38.533 | 0848 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204124 | Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.3 | Ericsson | 38.533 | 0849 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204125 | Correction of NR SA FR2 CSI-RS-based L1-RSRP measurement test case 7.6.3.4 | Ericsson | 38.533 | 0850 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204126 | Correction of minimum conformance requirements 4.6.4.0 for EN-DC FR1 L1-RSRP measurement test cases | Ericsson | 38.533 | 0851 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204127 | Correction of minimum conformance requirements 5.6.3.0 for EN-DC FR2 L1-RSRP measurement test cases | Ericsson | 38.533 | 0852 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204128 | Correction of minimum conformance requirements 7.6.3.0 for SA FR2 L1-RSRP measurement test cases | Ericsson | 38.533 | 0853 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204220 | Update missing SMTC and SSB configurations in H.2 | ROHDE & SCHWARZ | 38.533 | 0854 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204221 | Update missing SMTC and SSB configurations in H.3 | ROHDE & SCHWARZ | 38.533 | 0855 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204222 | Editorial: correct table placement in H.2 | ROHDE & SCHWARZ | 38.533 | 0856 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204283 | Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy | Qualcomm Incorporated | 38.533 | 0857 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204872 | Correction to Test Procedure and sync to latest RAN4 in 4.4.1.1 EN-DC FR1 UE transmit timing accuracy | Qualcomm Incorporated | 38.533 | 0857 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204284 | Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy | Qualcomm Incorporated | 38.533 | 0858 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204873 | Correction to Test Procedure and sync to latest RAN4 in 6.4.1.1 NR SA FR1 UE transmit timing accuracy | Qualcomm Incorporated | 38.533 | 0858 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204285 | Correction to Message Exceptions for 4.6.2.5 EN-DC FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection | Qualcomm Incorporated | 38.533 | 0859 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204286 | Correction to General Test Parameters for 6.6.2.5 NR SA FR1-FR1 event-triggered reporting in non-DRX with SSB time index detection | Qualcomm Incorporated | 38.533 | 0860 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204287 | Correction to General Test Parameters for 6.6.2.2 NR SA FR1-FR1 event-triggered reporting in DRX | Qualcomm Incorporated | 38.533 | 0861 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204288 | Correction to General Test Parameters for 6.6.2.6 NR SA FR1-FR1 event-triggered reporting in DRX with SSB time index detection | Qualcomm Incorporated | 38.533 | 0862 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204289 | Correction to 6.3.1.1 NR SA FR1 handover with known target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0863 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204290 | Correction to 6.3.1.2 NR SA FR1 handover with unknown target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0864 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204291 | Correction to 6.3.1.3 NR SA FR1-FR1 handover with unknown target cell sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0865 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204302 | Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0866 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204874 | Correction to 6.5.1.1 NR SA FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0866 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204303 | Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0867 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204875 | Correction to 6.5.1.2 NR SA FR1 RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0867 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204304 | Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0868 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204876 | Correction to 6.5.1.3 NR SA FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0868 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204305 | Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0869 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204877 | Correction to 6.5.1.4 NR SA FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0869 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204306 | Correction to 4.5.1.1 EN-DC FR1 RLM OOS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0870 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204307 | Correction to 6.5.1.2 EN-DC RLM IS test with SSB-based RLM RS in non-DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0871 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204308 | Correction to 6.5.1.3 EN-DC FR1 RLM OOS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0872 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204309 | Correction to 6.5.1.4 EN-DC FR1 RLM IS test with SSB-based RLM RS in DRX mode, sync to latest RAN4 Core Spec | Qualcomm Incorporated | 38.533 | 0873 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204337 | Addition of 4.5.5.0 minimum requirement for BFR | Huawei, HiSilicon | 38.533 | 0874 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203231 | TT analysis for RRM TC 8.5.2.1.1.1 | ROHDE & SCHWARZ | 38.903 | 0131 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203232 | TT analysis for RRM TC 8.5.2.2.1 | ROHDE & SCHWARZ | 38.903 | 0132 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203233 | TT analysis for RRM TC 8.5.2.3.1 | ROHDE & SCHWARZ | 38.903 | 0133 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203237 | TT analysis for RRM TC 4.7.4.1.1 | ROHDE & SCHWARZ | 38.903 | 0134 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203238 | TT analysis for RRM TC 4.7.4.1.2 | ROHDE & SCHWARZ | 38.903 | 0135 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203239 | TT analysis for RRM TC 4.7.4.2.1 | ROHDE & SCHWARZ | 38.903 | 0136 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203240 | TT analysis for RRM TC 4.7.4.2.2 | ROHDE & SCHWARZ | 38.903 | 0137 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203305 | Correction to the extreme conditions in TT analysis of 4.7.1.2.1 | ROHDE & SCHWARZ | 38.903 | 0138 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204788 | Correction to the extreme conditions in TT analysis of 4.7.1.2.1 | ROHDE & SCHWARZ | 38.903 | 0138 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203313 | CR to update the DL AWGN absolute power for RRM test cases | ROHDE & SCHWARZ | 38.903 | 0139 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204887 | CR to update the DL AWGN absolute power for RRM test cases | ROHDE & SCHWARZ | 38.903 | 0139 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203323 | Add Draft Test Tolerance analysis for FR2 Tx Timing Test cases | ANRITSU LTD | 38.903 | 0140 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203324 | Add Draft Test Tolerance analysis for FR2 Inter-freq Event-trig Test cases | ANRITSU LTD | 38.903 | 0141 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203325 | Add Draft Test Tolerance analysis for FR2 Intra-freq SS-RSRP Test case | ANRITSU LTD | 38.903 | 0142 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203486 | Adjacent Channel Selectivity FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | 38.903 | 0143 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204888 | Adjacent Channel Selectivity FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | 38.903 | 0143 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203490 | In-band Blocking FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | 38.903 | 0144 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204889 | In-band Blocking FR2 MU definition in 38.903 | Keysight Technologies UK Ltd | 38.903 | 0144 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203821 | Addition of FR1 Test tolerance analysis for DCI based BWP switch | Huawei, HiSilicon | 38.903 | 0145 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205001 | Addition of FR1 Test tolerance analysis for DCI based BWP switch | Huawei, HiSilicon | 38.903 | 0145 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203822 | Addition of FR1 Test tolerance analysis for RRC based BWP switch | Huawei, HiSilicon | 38.903 | 0146 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205002 | Addition of FR1 Test tolerance analysis for RRC based BWP switch | Huawei, HiSilicon | 38.903 | 0146 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203823 | Addition of FR1 Test tolerance analysis for SSB based BFR | Huawei, HiSilicon | 38.903 | 0147 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205003 | Addition of FR1 Test tolerance analysis for SSB based BFR | Huawei, HiSilicon | 38.903 | 0147 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203824 | Addition of FR1 Test tolerance analysis for CSI-RS based BFR | Huawei, HiSilicon | 38.903 | 0148 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-205004 | Addition of FR1 Test tolerance analysis for CSI-RS based BFR | Huawei, HiSilicon | 38.903 | 0148 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203825 | Addition of FR1 Test tolerance analysis for 6.3.2.1.3 RRC Re-establishment | Huawei, HiSilicon | 38.903 | 0149 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203826 | Update of grouping of test cases in clause 8 | Huawei, HiSilicon | 38.903 | 0150 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203827 | Addition of 4.5.5.0 minimum requirement for BFR | Huawei, HiSilicon | 38.903 | 0151 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204028 | CR to 38.903 on some of the Transmit OFF power MU parameters | Samsung R&D Institute UK | 38.903 | 0152 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204945 | CR to 38.903 on some of the Transmit OFF power MU parameters | Samsung R&D Institute UK | 38.903 | 0152 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204080 | CR to update MU in 38.903 | Anritsu, Keysight Technologies | 38.903 | 0153 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204890 | CR to update MU in 38.903 | Anritsu, Keysight Technologies | 38.903 | 0153 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204190 | On Standard Deviation Definition in 38.903 | Keysight Technologies UK Ltd | 38.903 | 0154 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204257 | FR2 Minimum output power measurement uncertainty | Keysight Technologies UK Ltd | 38.903 | 0155 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204891 | FR2 Minimum output power measurement uncertainty | Keysight Technologies UK Ltd | 38.903 | 0155 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204272 | Update of AWGN flatness in TR 38.903 | ROHDE & SCHWARZ | 38.903 | 0156 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204946 | Update of AWGN flatness in TR 38.903 | ROHDE & SCHWARZ | 38.903 | 0156 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204281 | FR2 EIRP OFF power measurement uncertainty | Keysight Technologies UK Ltd | 38.903 | 0157 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204947 | FR2 EIRP OFF power measurement uncertainty | Keysight Technologies UK Ltd | 38.903 | 0157 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203559 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | 38.905 | 0268 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204725 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | 38.905 | 0268 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204982 | Updated TP analysis for 7.3A | WE Certification Oy, DISH Network | 38.905 | 0268 | 2 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203642 | Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n1A | Ericsson, Telefonica | 38.905 | 0269 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203643 | Introduction of spurious emission TP analysis for Rel-16 EN-DC configuration DC_40A_n78A | Ericsson, Telefonica | 38.905 | 0270 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203675 | Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | 38.905 | 0271 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204789 | Update of TP analysis for NS_43 and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | 38.905 | 0271 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203676 | Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | 38.905 | 0272 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204790 | Update of TP analysis for NS_43U and NS_01 in FR1 A-MPR for CA | Huawei, Hisilicon | 38.905 | 0272 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203693 | Updating TP analysis for 6.2A.2-MPR for CA | Huawei, Hisilicon | 38.905 | 0273 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204727 | Updating TP analysis for 6.2A.2-MPR for CA | Huawei, Hisilicon | 38.905 | 0273 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203695 | Updating TP analysis for 6.2A.4-Configured output power for CA | Huawei, Hisilicon | 38.905 | 0274 | - | Rel-16 | F | NR_RF_FR1-UEConTest | revised |
| R5-204838 | Updating TP analysis for 6.2A.4-Configured output power for CA | Huawei, Hisilicon | 38.905 | 0274 | 1 | Rel-16 | F | NR_RF_FR1-UEConTest | agreed |
| R5-203751 | Editorial correction to references to EN-DC configurations | Ericsson | 38.905 | 0275 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203797 | Update test point analysis for A-MPR NS_18 with CBW being 30MHz | CMCC, Huawei, HiSilicon | 38.905 | 0276 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204963 | Update test point analysis for A-MPR NS_18 with CBW being 30MHz | CMCC, Huawei, HiSilicon | 38.905 | 0276 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-203805 | Addition of test point analysis of DC_66A_n2A in Tx spurious emissions | Sporton | 38.905 | 0277 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-203806 | Addition of test point analysis in Tx spurious emissions | Sporton, Ericsson | 38.905 | 0278 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204726 | Addition of test point analysis in Tx spurious emissions | Sporton, Ericsson | 38.905 | 0278 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203939 | Update of test point analysis of MOP for intra-band contiguous EN-DC | Huawei, Hisilicon | 38.905 | 0279 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204728 | Update of test point analysis of MOP for intra-band contiguous EN-DC | Huawei, Hisilicon | 38.905 | 0279 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203947 | Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0280 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204791 | Updating test point analysis for DC_1A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0280 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203948 | Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0281 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204792 | Updating test point analysis for DC_2A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0281 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203949 | Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0282 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204793 | Updating test point analysis for DC_2A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0282 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203950 | Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0283 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204794 | Updating test point analysis for DC_3A-n7A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0283 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203951 | Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0284 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204795 | Updating test point analysis for DC_3A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0284 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203952 | Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0285 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204796 | Updating test point analysis for DC_7A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0285 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203954 | Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0286 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204817 | Updating test point analysis for DC_3A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0286 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203955 | Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0287 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204818 | Updating test point analysis for DC_7A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0287 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203956 | Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0288 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204819 | Updating test point analysis for DC_7A-n66A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0288 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203957 | Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0289 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204820 | Updating test point analysis for DC_8A-n1A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0289 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203958 | Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0290 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204821 | Updating test point analysis for DC_12A-n78A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0290 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203959 | Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0291 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204822 | Updating test point analysis for DC_28A-n3A for spurious emissions UE co-existence | Huawei, Hisilicon | 38.905 | 0291 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |
| R5-203961 | Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations | Huawei, Hisilicon | 38.905 | 0292 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204797 | Correction to test point analysis for spurious emissions UE co-existence for a few inter-band EN-DC configurations | Huawei, Hisilicon | 38.905 | 0292 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-203978 | Addition of test point analysis for AMPR NS_48 | Huawei, HiSilicon | 38.905 | 0293 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204829 | Addition of test point analysis for AMPR NS_48 | Huawei, HiSilicon | 38.905 | 0293 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204023 | Addition of test point analysis for additional spurious emission with NS_17 | Huawei, Orange, CMCC | 38.905 | 0294 | - | Rel-16 | F | NR_bands_BW_R16-UEConTest | revised |
| R5-204964 | Addition of test point analysis for additional spurious emission with NS_17 | Huawei, Orange, CMCC | 38.905 | 0294 | 1 | Rel-16 | F | NR_bands_BW_R16-UEConTest | agreed |
| R5-204147 | Addition of Test Point analysis for FR2 Transmit OFF Power for CA | DOCOMO Communications Lab. | 38.905 | 0295 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204948 | Addition of Test Point analysis for FR2 Transmit OFF Power for CA | DOCOMO Communications Lab. | 38.905 | 0295 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204148 | Addition of Test Point analysis for FR2 Occupied bandwidth for CA | DOCOMO Communications Lab. | 38.905 | 0296 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204149 | Addition of Test Point analysis for FR2 Transmitter Spurious emissions for CA | DOCOMO Communications Lab. | 38.905 | 0297 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | withdrawn |
| R5-204196 | TP analysis 6.5B.3 TX SpurEmission EN-DC V2 | Qualcomm Austria RFFE GmbH | 38.905 | 0298 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204949 | TP analysis 6.5B.3 TX SpurEmission EN-DC V2 | Qualcomm Austria RFFE GmbH | 38.905 | 0298 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204208 | Add_TP_analysis_table for TX_spurious_emission | Qualcomm Austria RFFE GmbH | 38.905 | 0299 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204720 | Add_TP_analysis_table for TX_spurious_emission | Qualcomm Austria RFFE GmbH | 38.905 | 0299 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204216 | Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1 | Ericsson | 38.905 | 0300 | - | Rel-16 | F | 5GS_NR_LTE-UEConTest | revised |
| R5-204950 | Updated TP analysis for 7.3B Reference sensitivity for EN-DC in FR1 | Ericsson | 38.905 | 0300 | 1 | Rel-16 | F | 5GS_NR_LTE-UEConTest | agreed |
| R5-204335 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | 38.905 | 0301 | - | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | revised |
| R5-204959 | Update of TPanalysis 6.5A.3.2.1_SECoex for CA_n1A-n78A | China Unicom | 38.905 | 0301 | 1 | Rel-16 | F | NR_CADC_NR_LTE_DC_R16-UEConTest | agreed |

## Annex C: Lists of liaisons

### C1: Incoming liaison statements

7 incoming LSs at RAN5#88-e

| Document | Original | Title | From | Decision |
| --- | --- | --- | --- | --- |
| R5-203215 | 200603 Liaison Statement from NGMN to 3GPP RAN4 on 5G NR OTA_V1.1 | NGMN Liaison Statement to 3GPP RAN4 on 5G NR Over The Air test methodologies and performance requirements | NGNM | noted |
| R5-203216 | C1-203221 | Reply LS on support of eCall over NR | TSG WG CT1 | noted |
| R5-203217 | C6-200331 | Reply LS to GSMA TS.48 publication | TSG WG CT6 | noted |
| R5-203218 | CAG-20-331_LS on replacement of 3CC to 5CC RRM TCs in GCF scheme | CAG-20-331_LS on replacement of 3CC to 5CC RRM TCs in GCF scheme | GCF CAG | noted |
| R5-203219 | MCC-JTF-20-062r2 | LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level | GCF-TCCA Joint Taskforce #8 | noted |
| R5-203220 | R4-2006351 | LS response on Multiband relaxation for FR2 | TSG WG RAN4 | noted |
| R5-203221 | S5-203369 | Reply LS to Reply LS on support for eCall over NR | TSG WG SA5 | noted |

### C2: Outgoing liaison statements

4 outgoing LSs at RAN5#88-e, 2 for email approval

| Document | Title | To | Cc | status |
| --- | --- | --- | --- | --- |
| R5-204361 | LS on old unverified IMS test cases | GCF CAG, PTCRB PVG | GSMA 5GJA | approved |
| R5-204362 | LS on two consecutive invalid challenges | TSG WG CT1 | - | approved |
| R5-204364 | Reply LS to LS to 3GPP RAN5 on Requirement for Mission Critical Services (MCX) Testing and Certification 3GPP Release level | GCF Mission Critical Agreement Group (MCAG) | TSG WG SA6 | approved |
| R5-204376 | Status of Conformance testing development for Mission Critical Services (MCS) | PTCRB, PTCRB PVG | - | approved |
| R5-204383 | LS on MCS group document subscription procedures | TSG WG CT1 | - | for email approval |
| R5-204847 | LS response on Multiband relaxation for FR2 on testability analysis of MBR | GCF CAG, PTCRB PVG | - | for email approval |

## Annex D: List of agreed/approved new and revised Work Items

8 new WIDs were endorsed at RAN5#88-e

| Document | Title | Source | status |
| --- | --- | --- | --- |
| R5-204351 | New WID on: UE Conformance Test Aspects - 410 – 430 MHz E-UTRA FDD Band(s) for LTE PPDR and PMR/PAMR in Europe (Bands 87 and 88) | Nokia, Nokia Shanghai Bell | endorsed |
| R5-204352 | New WID on UE Conformance Test Aspects – B1C Signal in A-BDS Positioning System Support for LTE and NR | CATT, CMCC | endorsed |
| R5-204353 | New WID on UE Conformance Test Aspects for SON and MDT support for NR | China Mobile Com. Corporation, Ericsson | endorsed |
| R5-204354 | New WID on UE Conformance Test Aspects – High power UE (power class 2) for EN-DC (1 LTE FDD band + 1 NR TDD band) | China Unicom, CMCC | endorsed |
| R5-204355 | New WID on UE Conformance Test Aspects – Single Radio Voice Call Continuity from 5G to 3G | China Unicom | endorsed |
| R5-204356 | New WID on UE Conformance Test Aspects for NR performance enhancement | Qualcomm Korea | endorsed |
| R5-204357 | New WID on UE Conformance Test Aspects - Mission Critical Enhancements | NIST, Samsung | endorsed |
| R5-204358 | New WID - UE Conformance Test Aspects for CLI handling for NR | Qualcomm Incorporated | endorsed |

## Annex E: List of draft Technical Specifications and Reports

2 draft TSs were presented at RAN5#88-e

| Document | Spec | vers | Doc title | For |
| --- | --- | --- | --- | --- |
| R5-203528 | 36.579-6 | 1.1.0 | draft TS 36.579-6 v1.1.0 | approval |
| R5-203529 | 36.579-7 | 1.1.0 | draft TS 36.579-7 v1.1.0 | approval |

## Annex F: List of action items

### SIG:

### Action Points at RAN5#88-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#88.01 | SIG | Add ICS definition for 'nr-HO-ToEN-DC-r16' capability in TS 38.508-2 and update applicability condition of Inter-RAT handover from NR to EN-DC test case 8.1.4.2.1.2 using this ICS | China Telecom | R5-204520 | RAN5#89 | Pending |
| AP#88.02 | SIG | Review and update as needed all existing ICS definition to be compliant with TS 38.306 definition - UE capability field can have a different value for FDD and TDD if 'FDD-TDD DIFF' is set as 'Yes', and for FR1 and FR2 if 'FR1-FR2 DIFF' is set as 'Yes' | Motorola Mobility (TS 38.508-2 Rapporteur) | R5-204853 | RAN5#89 | Pending |

### Action Points at RAN5#87-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#87.01 | SIG | Study into how to make NR multifrequency tests (test case using more than three radio frequencies) applicable for NR ‘Bands’ with limited frequency range | Huawei, TF160, Qualcomm | R5-201338 | RAN5#88 | Closed R5-203363 R5-203364 R5-203365 R5-203366 R5-203367 R5-203368 R5-203369 R5-203370 |
| AP#87.02 | SIG | Review how timer delays are being applied in NB-IoT test cases during SIB modification and come up with a generic proposal | R&S, TF160 | R5-203066 | RAN5#89 | Pending R5-203799 |

### Action Points at RAN5#86-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#86.04 | SIG | Review applicability of legacy LTE test cases for Cat M2 and update applicability definitions accordingly | Ericsson, TF160 | R5-200293 | RAN5#88 | Closed R5-202018 R5-202019 R5-204144 R5-204145 R5-204146 |

### Action Points at RAN5#85 - Reno

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#85.03 | SIG | Update impacted LTE test cases in VPLMN environment due to media restriction policy | Qualcomm, TF160, Anritsu, R&S, Keysight | R5-198276 | RAN5#89 | Pending R5-200387 R5-200624 R5-200626 R5-200677 R5-204374 R5-204295 R5-204300 R5-204345 R5-203812 |

## RF:

## Action Points at RAN5#88-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#88e.21 | RF | For FR2 absolute power control test cases analyze to determine if we can test both upper and lower limits with a very large span when the aggregated BW is smaller than or equal to 400 MHz. | Samsung, E///, Anritsu, Keysight, R&S, Huawei | R5-204022 | RAN5#89e | Open |
| AP#88e.22 | RF | Analyze the value of the, FR2 time mask tests with OFF power relaxation, taking into account they don’t belong to regulatory specifications | E///, Nokia, Huawei, DISH, Orange, DCM, CMCC, China Unicom, TMO, AT&T, Verizon, Samsung | R5-187480 R5-204741 R5-204278r3 | RAN5#89e | Open |

## Action Points at RAN5#87-e

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#87e.21 | RF | Review the existing test point analysis of NR (FR1, FR2) RF tests for optimization. | DCM, E///, Huawei, Qualcomm, Oppo, DISH, China Unicom, TMO, CAICT, CMCC, Sporton | R5-201818 R5-202375 R5-204136 | RAN5#89e | Open |
| AP#87e.23 | RF | OEM vendors and Operators to provide feedback on how to handle test coverage for large devices in case 100% coverage cannot be ensured. Any TP allowance, MU relaxations allowed for meeting the requirements | OEMs and Operators | R5-202082 R5-202083 R5-202084 R5-202085 R5-198262 R5-198262 R5-204191 R5-204200 | RAN5#89e | Open |
| AP#87e.24 | RF | OEM vendors and operators to provide data on max antenna separation distances and device size for NR FR2 devices that can currently not be tested with the largest QZ size of 30cm in diameter. | OEMs and Operators | R5-202082 R5-202083 R5-202084 R5-202085 R5-198262 R5-204191 R5-204200 | RAN5#89e | Open |
| AP#87e.25 | RF | Define framework for NR CA (ENDC and FR2) Rx test optimization by re-using higher order fallbacks results | E///, Huawei, Anritsu, Qualcomm, CAICT, Samsung, DCM, CMCC, DISH , WE Certrification | R5-202375 R5-204214 | RAN5#89e | Open |
| AP#87e.26 | RF | OEM and chipset vendors provide an acceptable PC1 assumption for the CDF curve for MOP EIRP spherical coverage | OEMs and chipset vendors | R5-202124 R5-204282 | RAN5#89e | Open |

## Action Points at RAN5#85 Reno

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#85.27 | RF | Analyze and update NSA Tx and Rx tests to incorporate tx power levels assumptions provided by RAN4 (several Tx tests and all Rx tests) | RAN5 | R5-198774 | RAN5#88e RAN5#89e | Open |

## Action Points at RAN5#84 Ljubljana

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#84.21 | RF | Alignment of MPR/ACLR/SEM test points for NR and come with a combined TP analysis (separate analysis required for FR1, FR2 and Interworking) to TR38.905, and associated CRs | Ericsson, KEYS, CAICT | R5-197586 R5-201930 R5-201936/7 R5-201931 R5-201946 R5-201947/8 R5-201786/201919 | RAN5#89e | Open |

## Action Points at RAN5#83 Reno

| Action ID | sWG | Action | Responsible | Relevant Tdoc | Deadline | Status |
| --- | --- | --- | --- | --- | --- | --- |
| AP#83.22 | RF | To provide feedback on the maximum difference in direction between the beam peak at NTC when compared to ETC to determine the Test procedure and framework for peak EIRP and peak EIS test cases | RAN5 | R5-194596 R5-196361 R5-204189 | RAN5#89e | Open |

## Annex G: List of decisions

| Meeting/Number | Agenda item | Document | Details |
| --- | --- | --- | --- |

## Annex H: List of participants

146 delegates and officials attended electronically the RAN5#88-e meeting from remote

| TITLE | Family Name | Given Name | Email | Organization Represented |
| --- | --- | --- | --- | --- |
| Mr. | Akao | Takashi | takashi.akao.wa@nttdocomo.com | DOCOMO Communications Lab. |
| Mr. | Aquino | Alan | aquino.alan.zk@nttdocomo.com | NTT DOCOMO INC. |
| Mr. | Arroyo Narvaez | Carlos | carlos.arroyonarvaez@adare.de | adare GmbH |
| Mr. | Baba | Hiroyuki | hiroyuki.baba@anritsu.com | Anritsu Corporation |
| Mr. | Baev | Stoyan | stoyan.baev@partner.samsung.com | SAMSUNG R&D INSTITUTE JAPAN |
| Mr. | Balasubramanian | Vijay | vijayb@qti.qualcomm.com | Qualcomm Korea |
| Ms. | Bardaux | Virginie | virginie.bardaux_tf160@vbtelecom.fr | ANRITSU LTD |
| Miss | Basurto | Estrella | estrella.basurto@nemergent-solutions.com | NEMERGENT |
| Mr. | Bhise | Parikshit | parikshit.bhise@rohde-schwarz.com | ROHDE & SCHWARZ |
| Mr. | Booth | Ryan | ryan_booth@apple.com | Apple (UK) Limited |
| Mr. | Borsato | Ronald | rb354e@att.com | AT&T |
| Mr. | Brand | Graham | graham.brand@intel.com | Intel Corporation (UK) Ltd |
| Mrs. | Buis | Marija | marija.buis@adare.de | adare GmbH |
| Mr. | Cardalda Garcia | Adrian | adrian.cardalda-garcia@rohde-schwarz.com | ROHDE & SCHWARZ |
| Mr. | Catmur | Richard | richard.catmur@spirent.com | Spirent Communications |
| Mr. | Chan | William | william.chan@spirent.com | Spirent Communications |
| Mr. | Chander | Sharat | sc1303@att.com | AT&T GNS Belgium SPRL |
| Mr. | Chen | Wenhong | chenwenhong@oppo.com | Beijing OPPO Com. corp., ltd |
| Mr. | Chen | Xiaozhong | chenxiaozhong@catt.cn | CATT |
| Mr. | Chen | Zeyan | zeyan.chen@smartermicro.com | SmarterMicro Inc. |
| Mr. | Chen | Zidong | chenzidong@tejet.cn | Shanghai Tejet Com Technology |
| Mr. | Cheng | Ivan | IvanCheng@sporton.com.tw | Sporton International Inc |
| Mr. | Cheruvu | Bharadwaj Kumar | bcheruvu@qti.qualcomm.com | Qualcomm communications-France |
| Mr. | Chung | Standy | standychung@google.com | Google Inc. |
| Mr. | Coston | Steven G. | steve.coston@pctest.com | PCTEST Engineering Lab |
| Mr. | Cui | Shengjiang | cuishengjiang@oppo.com | Beijing OPPO Com. corp., ltd |
| Mr. | Dhuppad | Taran | tdhuppad@qti.qualcomm.com | Qualcomm Finland RFFE Oy |
| Ms. | Dong | Wenjia | dongwenjia@chinamobile.com | China Mobile Com. Corporation |
| Mr. | Dooley | John | john.dooley@globalstar.com | GLOBALSTAR Inc. |
| Dr. | Du | Yuxin | duyuxin@chinamobile.com | China Mobile Com. Corporation |
| Mr. | Dutta | Pranab | Pranab.dutta1@TechMahindra.com | Tech Mahindra Limited |
| Miss | Fernandez Martos | Flores | flores_fernandez@keysight.com | Keysight Technologies UK Ltd |
| Dr. | Fischer | Sven | sfischer@qti.qualcomm.com | Qualcomm CDMA Technologies |
| Mr. | Fortes Lopez | Jose M. | Jose.Fortes@rohde-schwarz.com | ROHDE & SCHWARZ |
| Ms. | GAO | JIN | gaoj8@chinatelecom.cn | China Telecommunications |
| Mrs. | GAO | Ting | gaoting@starpointcomm.com | Starpoint |
| Mr. | Genoud | Olivier | olivier.genoud@etsi.org | ETSI |
| Mr. | Georgeaux | Eric | eric.georgeaux@airbus.com | Airbus |
| Mr. | Gowda | Pradeep | pgowda@qti.qualcomm.com | Qualcomm Incorporated |
| Mr. | Grant | Marc | marc.grant@att.com | AT&T GNS Belgium SPRL |
| Ms. | Gu | Chunying | guchunying@huawei.com | Huawei Technologies Sweden AB |
| Dr. | Guo | Li | guoli@oppo.com | Dongguan OPPO Precision Elec. |
| Mr. | Hagenfeldt | Calle | calle.hagenfeldt@ericsson.com | Ericsson Inc. |
| Miss | Hao | Yuxin | haoyuxin@hisilicon.com | Huawei Telecommunication India |
| Mr. | He | Chuanfeng | hechuanfeng@oppo.com | Chengdu OPPO Mobile Com. corp. |
| Mr. | Heino | Aleksi | aleksi.heino@wecertification.com | WE Certification Oy |
| Dr. | Hertel | Thorsten | thorsten.hertel@keysight.com | Keysight Technologies UK Ltd |
| Mr. | Hong | Tae Howan | taehowan.hong@lge.com | LG Electronics Inc. |
| Mr. | Hsueh | Bruce | bruce.hsueh@intertek.com | Intertek |
| Mr. | Huang | Yingpei | huangyingpei@oppo.com | Shenzhen YZF Network Technolog |
| Dr. | Johansson | Mats | mats.e.johansson@ericsson.com | Nanjing Ericsson Panda Com Ltd |
| Mr. | John | Jacob | Jacob.John@motorola.com | Motorola Mobility UK Ltd. |
| Mr. | Jönsson | Bo | bo.jonsson@ericsson.com | Ericsson Limited |
| Mr. | Kahn | Jason | jason.kahn@nist.gov | NIST |
| Mr. | Kalahasti | Narendra | narendra.kalahasti@anritsu.com | ANRITSU LTD |
| Mr. | Kanchan | Mohit | mohit.kanchan@keysight.com | Keysight Technologies UK Ltd |
| Dr. | Kang | Ting-Wei | ting-wei.kang@mediatek.com | MediaTek Beijing Inc. |
| Mr. | Kangas | Matti | matti.kangas@nokia.com | Nokia Corporation |
| Mr. | Karlsson | Petter | petter.karlsson@ericsson.com | Ericsson España S.A. |
| Mr. | Kawakami | Katsuji | katsuji.kawakami@sony.com | Sony Mobile Communications |
| Dr. | Khanfir | Hajer | hajer.khanfir@orange.com | Orange UK |
| Mr. | Kolodziej | Jakub | jakub.kolodziej@ericsson.com | Ericsson-LG Co., LTD |
| Mr. | Kum | Donghyun | kdh0313@tta.or.kr | TTA |
| Mr. | Kuusisto | Jussi | jussi_kuusisto@outlook.com | Dish Network |
| Mr. | Lai | Kenny | kenny.lai@sgs.com | SGS Wireless |
| Mr. | Li | Jianqiang | lijq@gdcni.cn | GDCNI |
| Mrs. | li | pei | lipei@h3c.com | New H3C Technologies Co., Ltd. |
| Mr. | Li | Shuang | lishuang@cbn.cn | CBN |
| Dr. | Liberal | Fidel | fidel.liberal@ehu.eus | UPV/EHU |
| Mr. | lin | hao | lin.hao@oppo.com | OPPO |
| Dr. | Lin | Kevin | kevin.lin@oppo.com | Chengdu OPPO Mobile Com. corp. |
| Mr. | Liu | Bing | leo.liubing@huawei.com | Huawei Device Co., Ltd |
| Dr. | Ma | Jinwen | jinwen.ma@verizonwireless.com | Verizon Switzerland AG |
| Mr. | Ma | Wei | ma.wei4@zte.com.cn | ZTE Corporation |
| Mr. | Ma | Zhaorui | mazhaorui@huawei.com | HUAWEI TECHNOLOGIES Co. Ltd. |
| Dr. | Ma | Zhifeng | ma.zhifeng@zte.com.cn | ShenZhen Zhongxing Shitong |
| Mr. | Matsuyoshi | Taiki | ta-matsuyoshi@kddi.com | KDDI Corporation |
| Mr. | Mattisson | Leif | leif.mattisson@ericsson.com | L.M. Ericsson Limited |
| Mr. | Mendivil | Edwin | Edwin.Mendivil@ETS-lindgren.com | ETS-Lindgren Europe |
| Dr. | Menzel | Edwin | edwin.menzel@rohde-schwarz.com | ROHDE & SCHWARZ |
| Mr. | Mohammad | Shahab | shahab@qti.qualcomm.com | Qualcomm Incorporated |
| Mr. | Mohammed | Abdul Rasheed | A17043@motorola.com | Motorola Mobility France S.A.S |
| Mr. | Mohan | Ashwin | mohana@qti.qualcomm.com | Qualcomm CDMA Technologies |
| Mr. | Nakatogawa | Tsuyoshi | nakatogawa.t-iq@nhk.or.jp | NHK |
| Mr. | Oh | Jongok | jongok.oh@lge.com | LG Electronics Inc. |
| Ms. | Panchapakesan | Padma | PP00345770@Techmahindra.com | Tech Mahindra Limited |
| Dr. | Parikh | Hemish | hparikh@qti.qualcomm.com | Qualcomm Wireless GmbH |
| Mr. | Petrovic | Niels | niels.petrovic@rohde-schwarz.com | ROHDE & SCHWARZ |
| Mr. | Probasco | Scott | scott.probasco@t-mobile.com | T-Mobile USA |
| Dr. | Ramamurthi | Vishwanath | vishwanath.ramamurthi@verizonwireless.com | Verizon Sweden |
| Mrs. | Rauer | Petra | petra.rauer@vodafone.com | Vodafone GmbH |
| Mr. | Rohnert | Hans | hans.rohnert@rohde-schwarz.com | ROHDE & SCHWARZ |
| Mr. | Rose | Ian | ian.rose@anritsu.com | ANRITSU LTD |
| Mr. | Ruiz | Emilio | emilio_ruiz@keysight.com | Keysight Technologies UK Ltd |
| Miss | Rutkowski | Kimberly | Kim.Rutkowski@MVG-US.COM | MVG Industries |
| Mrs. | Saunders | Hellen | hellen.saunders@non.keysight.com | Keysight Technologies UK Ltd |
| Mr. | Säynäjäkangas | Tuomo | tuomo.saynajakangas@nokia.com | Nokia Germany |
| Mr. | Scannavini | Alessandro | alessandro.scannavini@mvg-world.com | MVG Industries |
| Miss | Shi | Yu | shiyu19@chinaunicom.cn | China Unicom |
| Dr. | SHI | Zhihua | szh@oppo.com | Hangzhou Douku |
| Mr. | Sigovich | Ingbert | ingbert.sigovich@etsi.org | ETSI |
| Mr. | Sinsathitchai | Wisuit | wsinsathitchai@apple.com | Apple Europe Limited |
| Ms. | Sokondar | Eniko | eniko.sokondar@mediatek.com | MediaTek Inc. |
| Dr. | Song | Dan | songdan@chinamobile.com | China Mobile Com. Corporation |
| Miss | Song | Huayue | hy.song@tta.or.kr | TTA |
| Mr. | Suzuki | Takao | takao.suzuki.td@nttdocomo.com | NTT DOCOMO INC. |
| Miss | Tao | Amy | amy.tao@bureauveritas.com | Bureau Veritas |
| Dr. | Taylor | Carolyn | carolyn.t@samsung.com | Samsung R&D Institute UK |
| Mr. | Thiruvathirai | Ramakrishnan | Ramakrishnan.Thiruvathirai@rohde-schwarz.com | ROHDE & SCHWARZ |
| Miss | Tian | Jiejiao | tianjiejiao@oppo.com | Hangzhou Mengyuxiang |
| Dr. | Tian | Wenqiang | tianwenqiang@oppo.com | OnePlus |
| Mr. | Toril | Adan | adan_toril@keysight.com | Keysight Technologies UK Ltd |
| Mr. | Tseng | Eric | eric.tseng@mediatek.com | MediaTek Inc. |
| Mr. | tugnawat | yogesh | yogesht@qti.qualcomm.com | QUALCOMM JAPAN LLC. |
| Mr. | Ubicini | Massimiliano | massimiliano.ubicini@telecomitalia.it | TELECOM ITALIA S.p.A. |
| Mr. | Vogedes | Jerome | jvogedes@nextnav.com | NextNav |
| Mr. | Vora | Mayur | mvora@qti.qualcomm.com | Qualcomm Austria RFFE GmbH |
| Mr. | Vorisek | Michael | vorisekm@ctu.cz | Czech Telecommunication Office |
| Mr. | Wang | Fu | wangfu@datangmobile.cn | Datang Linktester Technology |
| Mr. | Wang | Kevin | kevinw@qti.qualcomm.com | Qualcomm Austria RFFE GmbH |
| Mr. | Wang | Murphy | murphy.wang@dekra.com | DEKRA |
| Dr. | Wang | Ruixin | ruixin.wang@vivo.com | vivo Communication Technology |
| Dr. | Wang | Xuesong | cedar.wang@hisilicon.com | HUAWEI Technologies Japan K.K. |
| Mr. | Watts | Simon | Simon.Watts@avantiplc.com | Avanti Communications Ltd |
| Mr. | Wu | Jingzhou | wujingzhou@chinatelecom.cn | China Telecom Corporation Ltd. |
| Mr. | Wu | Yuchun | wuyuchun@huawei.com | HiSilicon Technologies Co. Ltd |
| Miss | Wu | Zuomin | wuzuomin@oppo.com | Orope Germany GmbH |
| Mrs. | Xu | Jing | xj@oppo.com | Dongguan OPPO Precision Elec. |
| Mr. | Xu | Weijie | xuweijie@oppo.com | Shenzhen YZF Network Technolog |
| Mr. | Yang | Kun | yang.kun15@zte.com.cn | Sanechips |
| Miss | Yang | Shan | yangshan.bri@chinatelecom.cn | China Telecommunications |
| Ms. | yang | zhaobing | yangzhaobing@hisilicon.com | Huawei Tech.(UK) Co., Ltd |
| Mr. | Zhan | Wenhao | zhanwenhao@oppo.com | Guangdong OPPO Mobile Telecom. |
| Miss | Zhang | Huiying | zhanghuiying@catt.cn | CATT |
| Ms. | Zhang | Nuoya | zhangnuoy@chinatelecom.cn | China Telecommunications |
| Mr. | ZHANG | Shichang | shichangzhang@oppo.com | Hangzhou Mengyuxiang |
| Miss | Zhang | Yaping | zhangyaping13@huawei.com | HuaWei Technologies Co., Ltd |
| Ms. | Zhang | Yufeng | zhangyufeng@caict.ac.cn | CAICT |
| Ms. | ZHAO | JING | zhaoj16@chinatelecom.cn | China Telecommunications |
| Mr. | Zhao | Zheng | zheng.zhao@verizon.com | Verizon Denmark |
| Mr. | Zhao | Zhenshan | zhaozhenshan@oppo.com | Guangdong OPPO Mobile Telecom. |
| Mr. | Zhou | Daiwei | daiwei.zhou@mediatek.com | MediaTek Beijing Inc. |
| Mr. | Zhou | Xutao | xutao.zhou@samsung.com | BEIJING SAMSUNG TELECOM R&D |
| Miss | Zhu | Ziyuan | zhuzy50@chinaunicom.cn | China Unicom |
| Mr. | Ziren | Mikael | mikael.ziren@ericsson.com | Ericsson France S.A.S |
| Mr. | Zuo | Zhisong | zuozhisong@oppo.com | Hangzhou Douku |

## Annex I: List of future meetings

| Meeting | Confirmed Dates | Location | Host |
| --- | --- | --- | --- |
| RAN5#88 | 17 – 28 Aug 20 | Electronic Meeting | - |
| RAN5#89 | 9 – 20 Nov 20 | Electronic Meeting | - |
| RAN5#90 | 1 – 5 Mar 21 | EU | EF3 |
| RAN5#91 | 24 – 28 May 21 | US | NAF3 |
| RAN5#92 | 23 – 27 Aug 21 | Toulouse (FR) | EF3 |
| RAN5#93 | 15 – 19 Nov 21 | US | NAF3 |