3GPP TSG RAN5 Meeting #91-e	R5-213398

Electronic meeting, 17 – 28 May, 2021	(Revision of R5-213109)

3GPP TSG RAN Meeting #92e	RP-21zzzz

Electronic meeting, 14 – 18 June, 2021

# Source:	Ligado Networks

# Title:	New WID: UE Conformance – Modification of LTE Band 24 Specifications to comply with updated regulatory emission limits

# Document for:	Endorsement

Agenda Item:	4.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	UE Conformance– Modification of LTE Band 24 Specifications to comply with updated regulatory emission limits

## Acronym: LTE_B24_mod-UEConTest

## Unique identifier:

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network |  |
|  | Services |  |

Potential target Release: Rel-17

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  |  |  |  |  |
| No | X | X | X | X |  |
| Don't know |  |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a …

|  | Feature |
| --- | --- |
| X | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

The following lists of RAN4 work items that will be tested in this RAN5 work item will be maintained in future revisions of this WI description:

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| LTE_B24_mod | R4 | 880081 | Modification of LTE Band 24 Specifications to comply with updated regulatory emission limits |
| LTE_B24_mod-Core | R4 | 880181 | Core part: Modification of LTE Band 24 Specifications to comply with updated regulatory emission limits |
| LTE_B24_mod-Perf | R4 | 880281 | Perf. part: Modification of LTE Band 24 Specifications to comply with updated regulatory emission limits |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

On April 19, 2020, the FCC adopted an Order updating the technical rules for terrestrial deployment utilizing spectrum associated with Band 24.  The FCC also reauthorized Ligado’s licenses and its ability to deploy terrestrial network within the United States using equipment that complies with the revised technical rules specified in the FCC Order 20-48.

The core and performance work items in RAN4 for modifications to existing LTE Band 24 in 3GPP specifications as a result of regulatory updates are 95% and 100% completed respectively at RAN#91 Mar-2021.  The WI is planned to be 100% complete at RAN#92e in June-2021.

Following updates have been made to the LTE Band 24:

- Limits the DL and UL frequency ranges that can be used for terrestrial deployment

- Addition of a second Tx-Rx spacing

- New emission requirements

- New NS and associated additions spurious emissions requirements as well as A-MPR values.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

- The objective of this work item is to update relevant UE conformance test cases for the RF, RRM and protocol aspects of the Rel-17 core and performance parts for LTE Band 24.

- This update is expected to be release independent starting from Release 9 onwards.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 34.108 | Assess and if required update common test environment for co-existence requirement to protect LTE band 24. | TSG RAN#94 (Dec-21) |  |
| TS 34.121-1 | Assess and if required update UTRA FDD test cases for co-existence requirements to protect LTE band 24. | TSG RAN#94 (Dec-21) |  |
| TS 34.121--2 | Assess and if required update UTRA FDD test cases for co-existence requirements to protect LTE band 24. | TSG RAN#94 (Dec-21) |  |
| TS 36.508 | Assess and update definition of common test environment for LTE band 24. (Clauses 4.3.1.1.24 and potentially 6.2.3.1) | TSG RAN#94 (Dec-21) |  |
| TS 36.521-1 | Assess and update notes for the operating band 24, Tx-Rx spacing, and relevant transmitter and receiver clauses | TSG RAN#94 (Dec-21) |  |
| TS 36.521-2 | Assess and if required update the physical implementation capabilities for LTE band 24 for the RF & RRM testing. | TSG RAN#94 (Dec-21) |  |
| TS 36.521-3 | Assess and if required update band 24 in groups of band definition. | TSG RAN#94 (Dec-21) |  |
| TS 36.523-2 | Assess and if required update physical implementation capabilities for LTE band 24 for the protocol testing. | TSG RAN#94 (Dec-21) |  |
| TS 36.523-3 | Assess and update of the test case execution guidelines for LTE Band 24 Note: Progress of TTCN development of the new protocol test cases is tracked in MCC TF160 reports to RAN5/RAN. | TSG RAN#94 (Dec-21) |  |
| TR 36.902 | Assess and if required update RRM test cases | TSG RAN#94 (Dec-21) |  |
| TR 36.903 | Assess and if required update RRM test cases | TSG RAN#94 (Dec-21) |  |
| TR 36.905 | Addition of TP for Band 24 A-MPR | TSG RAN#94 (Dec-21) |  |

## 6	Work item Rapporteur(s)

Choksi, Ojas (Ligado Networks)

ojas.choksi@ligado.com

## 7	Work item leadership

R5

## 8	Aspects that involve other WGs

None

## 9	Supporting Individual Members

Supporting IM name

Ligado Networks

Mavenir

Nokia

Saankhya Labs

DEKRA

Rohde & Schwarz