3GPP TSG-RAN5 Meeting #91-e	Tdoc ( R5-213219

# Electronic Meeting, 17th – 28th May 2021

# Title:						FR2 RRM test cases: Known Issue List

Source:			Ericsson

Agenda Item:			5.3.2.17

Document for:			Discussion

# 1.	Introduction

R5-210823 [1] gave a summary of known FR2 RRM Test case issues. R5-212634 [2] outlines the issue with summary, example and possible way forward. This document is for tracking the issues together with assigned company, progress, Tdoc numbers etc.

# 2.	Issue List

| # | Issue | Test types | Owner | RAN4 Status | RAN4 Target | RAN5 Status | RAN5 Tdoc# | RAN5 Target | Comments |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Angle of Arrival or Beam type undefined | Various | Ericsson | Done | RAN4#99-e | Will be handled by TC owners | NA. (issue resolved in | RAN5#91-e | Newly introduced cases may have issue. No need for |
| 2 | Angle of Arrival gives insufficient dB range | CSI-RS based |  | Unresolved |  | Unresolved |  |  | Consider changing to beam peak in RAN4 |
| 3 | Full 66RBs gives insufficient dB range | Various | Anritsu | done | RAN4#99-e | Will be handled by TC owners | NA. (issue resolved in | RAN5#91-e | Reduce allocation to 24RBs for SCS 120kHz |
| 4 | Parameters don’t fit 240kHz SSB SCS | Various | Anritsu | done | RAN4#99-e | Will be handled by TC owners | NA. (issue resolved in | RAN5#91-e | Review 240 kHz SCS cases |
| 5 | Angle of Arrival/dB values incompatible | Various | R&S | Needs research | RAN4#100-e | Needs research | R5-213105 | RAN5#92-e | Resolvable |
| 6 | Set uplink power to defined target value | Random Access |  | N/A? |  | Needs research |  |  | Is there solution in RF tests? |
| 7 | Absolute thresholds /large UE gain range | Various | Ericsson | Needs research | RAN4 #100-e | Needs research |  | RAN5 #92-e | RSRP calibration? |
| 8 | Handling of 2 Angles of Arrival from 1 cell | RLM, TCI state switch | R&S | Needs research | RAN4 #100-e | Needs research |  | RAN5 #92-e | Define TDM? |
| 9 | RLM Out-Of-Sync criteria | RLM | Keysight | Needs research | - | Needs research | R5-213336 | RAN5 #92-e | Eventually new criteria to evaluate OOS |
| … |  |  |  |  |  |  |  |  |  |

# References

[1] R5-210823, Anritsu, Summary of known issues for NR RRM Test cases in 38.533

[2] R5-212634, Anritsu, FR2 RRM test cases: Known Issues