3GPP TSG-RAN5 Meeting #94-e	R5-221381

Electronic Meeting, 21st Feb– 4th Mar 2022

3GPP TSG RAN Meeting #95-e	RP-22xxxx

Electronic Meeting, 17 March – 23 March 2022

# Source:	China Unicom, Hisilicon, Ericsson, Huawei, Qualcomm

# Title:	New WID on UE Conformance – Support of reduced capability NR devices

# Document for:	Approval

Agenda Item:	7.4.1

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	UE Conformance – Support of reduced capability NR devices

## Acronym: NR_redcap_plus_ARCH-UEConTest

## Unique identifier:

| This WID includes a Testing part | X |
| --- | --- |
| and it addresses the following 3GPP work area: | Radio Access | X |
|  | Core Network | X |
|  | Services |  |

Potential target Release: Rel-17

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  |  |  |  |  |
| No | X | X | X | X |  |
| Don't know |  |  |  |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

|  | Feature |
| --- | --- |
| X | Building Block |
|  | Work Task |
|  | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |
| NR_redcap-core | RAN1 | 900162 | Core part: NR_redcap |
| NR_redcap-Perf | RAN4 | 900262 | Perf. part: NR_redcap |
| ARCH_NR_REDCAP | CT1 | 940005 | CT1 aspects of NR_redcap |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

## 3	Justification

With rapid development of 5G industry, there is an increasing industrial market demand for 5G products with low power consumption and low cost. In Rel-17, a study item Study on support of reduced capability NR devices has  introduced the reduced capability NR devices at RP#86 meeting, enabling the advanced features and spectral efficiency of NR to be available for devices that do not require the full high data rate capabilities of NR. Such 5G devices include video surveillance, industrial sensors and wearable products, which will open up a broad space for 5G consumer market and facilitate the development of vertical industry. At the RP#90 meeting, the follow-up WI NR_redcap with 2 sub-WIs Core part: NR_redcap and Perf. part: NR_redcap has been introduced into 3GPP, and the overall completion of the core part of NR_redcap  is already achieved 75% at the RP#94 meeting in Dec 2021. The core part of NR_redcap WI and CT1 WI ARCH_NR_REDCAP  are expected  to be 100% completed at March 2022, and the performance WI is expected to complete at Sep 2022.

To fulfill the strong demand of low cost 5G product, it is proposed to introduce an associated RAN5 work item to enable UE conformance test for supporting of reduced capability NR devices as soon as possible.

## 4	Objective

### 4.1	Objective of SI or Core part WI or Testing part WI

The objective of this WI is to enable UE conformance testing for the corresponding R17 NR redcap device WIs listed under clause 2.2, including the following areas:

- Protocol test case to support NR Redcap device.

- RF test cases to support NR RedCap device.

- RRM test cases to support the NR RedCap devices.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Remarks |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |
| TS 38.508-1 | Definition of common test environment for R17 reduced capability NR devices | TSG RAN#100 (June-23) |  |
| TS 38.508-2 | Introduction of common implementation conformance statement (ICS) for R17 reduced capability NR devices | TSG RAN#100 (June-23) |  |
| TS 38.521-1 | Introduction of R17 reduced capability NR device RF requirements - FR1 | TSG RAN#98 (Dec-22) |  |
| TS 38.521-2 | Introduction of FR2 R17 reduced capability NR device RF requirements - FR2 | TSG RAN#98 (Dec-22) |  |
| TS 38.521-4 | Introduction of demodulation and CSI requirements for R17 reduced capability NR device . | TSG RAN#100 (June-23) |  |
| TS 38.522 | Applicability statements of the R17 reduced capability NR devices for the RF & RRM test cases | TSG RAN#100 (June-23) |  |
| TS 38.523-1 | Introduction of protocol test cases for R17 reduced capability NR devices | TSG RAN#98 (Dec-22) |  |
| TS 38.523-2 | Applicability statements of the R17 reduced capability NR devices for the SIG test cases. | TSG RAN#98 (Dec-22) |  |
| TS 38.523-3 | Introduction of test model for R17 reduced capability NR devices | TSG RAN#100 (June-23) | Progress of TTCN development of the new protocol test cases is tracked in MCC TF160 reports to RAN5/RAN. |
| TS 38.533 | Introduction of RRM test cases for R17 reduced capability NR devices | TSG RAN#100 (June-23) |  |
| TR 38.903 | Derivation of test tolerances and measurement uncertainty for R17 reduced capability NR device conformance test cases | TSG RAN#100 (June-23) |  |
| TR 38.905 | Derivation of test points for R17 reduced capability NR device requirements in radio transmission and reception User Equipment (UE) conformance test cases. | TSG RAN#98 (Dec-22) |  |

## 6	Work item Rapporteur(s)

Shi, Yu  (China Unicom)

shiyu19@chinaunicom.cn

Zhaobing, Yang (Hisilicon)

yangzhaobing@hisilicon.com

Calle Hagenfeldt (Ericsson)

calle.hagenfeldt@ericsson.com

Yogesh Tugnawat  (Qualcomm)

yogesht@qti.qualcomm.com

## 7	Work item leadership

RAN5

## 8	Aspects that involve other WGs

None

## 9	Supporting Individual Members

Supporting IM name

China Unicom

Hisilicon

Ericsson

Huawei

CATT

Spreadtrum Communications

ZTE Corporation

Qualcomm

CMCC

Nokia

CAICT

Verizon

Dish Network

Orange

Apple

T-Mobile USA

Telecom Italia

Lenovo

Motorola Mobility