## Slide 1: FR1 TT Way Forward update
3GPP TSG-RAN WG5 Meeting #5-5G-NR Adhoc
Xian, China, 9th – 12th April 2019
R5-19xxxx
Telecom Italia

## Slide 2: Background FR1
At RAN5#79 the Maximum Test System Uncertainty for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952
At RAN5#79 a Way Forward on FR1 TTs for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952 (Except the FFS items)
At RAN5#80 New FR1 MU values introduced in R5-184484 for the following TCs: 6.3.4.2, 6.3.4.3, 6.3.4.4, 6.4.2.1, 6.4.2.2, 6.4.2.3, 6.4.2.4. New TT values agreed based on the WF assumption in R5-185564
At RAN5#80 RAN5 also agreed to maintain the document until the TT for FR1 and FR2 are finalized
At RAN5 5G-AH#3 a WF for FR1 NSA in TS 38.521-3 has been agreed in R5-185657
At RAN5#81 an update has been presented in R5-187813
At RAN5 5G-AH#4 an update has been presented in R5-190940
At RAN5#82 an update has been presented in R5-192596

## Slide 3: Agreed FR1 Way Forward: TT < MU
At RAN5#79 TT WF agreed in R5-183952
WF: Except the FFS Items, the proposed FR1 TT Values are included in the spreadsheet file, based on the following assumption:
  The SA FR1 TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.

## Slide 4: Agreed FR1 NSA WF TS 38.521-3
At 5G-AH#3 RAN5 agreed NSA MU in R5-185641
At 5G-AH#3 RAN5 agreed WF in R5-185657 for TS 38.521-3 FR1 EN-DC as follow:
  In case TTLTE, TTSA = 0, TTNSA to be defined as zero.
  In case MUNSA = MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.
  In case MUNSA > MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.

## Slide 5: Attached Spreadsheets update
TS 38.521-1 SA FR1 TT
  Introduces the still missing UL-MIMO Test cases and minor few TC alignment.
  Introduced UL-MIMO MU (R5-190955) and TT (R5-190954 and R5-190956)
  Introduced New CA TCs and RefSense for SUL and 4RX new tests
  New TCs introduced at RAN5#82 added
  Some misalignment among WF, Annex F and TC highlighted in yellow
TS 38.521-3 NSA FR1 TT
  Added missing Test Cases: 6.3B.3.1, 6.3B.3.2, 6.3B.3.3, 6.3B.3.4
  New TCs introduced at RAN5#82 added