## Slide 1: Agreement of noise impact during RAN5 NR#5 AdHoc
Anritsu, R&S, Keysight
R5-193444
3GPP TSG-RAN5 Meeting #5-5G-NR Adhoc
Xi’an, China, 8th-12th Apr 2019

## Slide 2: Agreements
In RAN5 NR#5 AdHoc, documents [1] – [3] are discussed and following agreements are made.
Test case | Applicable Frequency Range[GHz] | Agreement in RAN5#82 (For information) | Offline Agreement in RAN5 NR#5
MOP (TRP, PC3) | 23.45GHz ≤ f ≤ 32.125 GHz | ΔSNR=0.1, Relaxation=0, for EIRPMAX≤ 33dBm | ΔSNR=0.1dB, Relaxation=0dB (Remove limit of EIRPMAX)
 | 32.125 GHz ≤ f ≤ 40.8 GHz | ΔSNR=0.3, Relaxation=0, for EIRPMAX≤ 33dBm | ΔSNR=0.3dB, Relaxation=0dB (Remove limit of EIRPMAX)
Off power | 23.45 GHz ≤ f ≤ 32.125 GHz | - | Test cannot be carried out without relaxation. Relaxation amount is in the range 28 - 42.7dB for 400MHz BW if threshold SNR is 10dB
 | 32.125 GHz < f ≤ 40.8 GHz | - | Test cannot be carried out without relaxation. Relaxation amount is in the range 35 - 45.9dB for 400MHz BW if threshold SNR is 10dB
SEM | 23.45 GHz ≤ f ≤ 32.125 GHz | - | ΔSNR=0.62dB, Relaxation=0dB
 | 32.125 GHz < f ≤ 40.8 GHz | - | TBD
Proposal 1 : For MOP (TRP, PC3) FR2a, ΔSNR=0.1dB, Relaxation=0dB for IFF 30cm and 15cm
Proposal 2 : For MOP (TRP, PC3) FR2b, ΔSNR=0.3dB, Relaxation=0dB for IFF 30cm and 15cm
Proposal 3 : For SEM(TRP, PC3) FR2a, ΔSNR=0.62dB, Relaxation=0dB for IFF 30cm and 15cm
Observation 1 : For OFF Power, test cannot be carried out without relaxation. Required relaxation is in the range 28 - 42.7dB for FR2a 400MHz BW if threshold SNR is 10dB for IFF 30cm and 15cm
Observation 2 : For OFF Power, test cannot be carried out without relaxation. Required relaxation is in the range 35 – 45.9dB for FR2b 400MHz BW if threshold SNR is 10dB for IFF 30cm and 15cm

## Slide 3: Reference
[1] R5-193104, “SNR estimation update for FR2 priority 1 and 2 TRx TCs”, Anritsu, RAN5 NR#5 AdHoc
[2] R5-192984, “On the SNR for FR2 TRx test cases”, Rohde & Schwarz, RAN5 NR#5 AdHoc
[3] R5-193187, “On noise impact”, Keysight Technology, RAN5 NR#5 AdHoc