## Slide 1: Progress on Proposal-2 : TS 38.522 early study and challenges in implementation
Qualcomm
3GPP TSG-RAN5 Meeting #100 R5-234319
Toulouse, France, Aug 21-25th

## Slide 2
Updates, Agenda for Discussion
TS 38.522 early study and challenges in implementation
How to classify sub-tests
Needs harmonization across SDOs
How to handle branching
Next Steps

## Slide 3: Background – Overall Industry value
Updates:
Based on proposal in R5-233200 and outcome in RAN5#99, a separate exploder has been created - 3GPP_TSG_RAN_WG5_APPLICABILITY
Green items above now have Prototype SW Implementation
3GPP RAN5 Defined Tests
Extracted OEM PICS Compliance
TS 38.508-2
TS 38.523-2
Protocol
TS 38.522
RF+Perf (RRM, Demod)
OEM Augments Band, CA and other Information
TS 34.229-2
IMS (5G, 4G)
Output = No. of Applicable Tests per Device Capability
(All Automated in RAN5)
Execution Rules (Cert Industry Logic)
Final List of Test Cases

## Slide 4: Proposal 2 – SW implementation of TS 38.522 (RF, RRM, Demod)
Identify Relevant PICS (including bands), from TS 38.508-2 for the DUT
Apply CA/DC Configuration (E) in TS 38.522
New SW Implementation of TS 38.522
(Handle Additional Comments, Notes)
Output = List of Applicable Tests per Device Capability
UE Features in Condition
Set (C) in TS 38.522
Apply Tested Bands Selection
Set (D) in TS 38.522
Apply Branching Criteria –
PC, RX
(C) Conditions are similar to Signaling
However, RF/RRM/Demod has unique – super conditions,
Selection Set (D),
CA/DC Configuration (E)
Branching criteria unique
Also, unlike SIGNALLING, RF/RRM/Demod subtest cases may have different applicability, while 38.522 doesn’t capture in that level of granularity

## Slide 5: Proposal 2 – SW implementation of TS 38.522 (RF, RRM, Demod)
(C) Conditions are binary, similar to Signaling
  However, RF/RRM/Demod works differently,
  it can create multiple instances/branches of test cases from the same core requirements,
    based on Code D or Code E

## Slide 6: Proposed Output Templates
Matrix Format | DCC Format | Hybrid Format
Each Test case/subtest case will have their own row Branches (AKA Bands, CA, PCs, Number of Rx etc) will be captured in Columns | Each test case/subtests and all possible branches will have their own row | Each test case/subtests will have its own row All possible branches will have their own tab

## Slide 7
Ongoing\Next Steps
For the next level of automation, need more participation from RAN5 Performance Subgroup
Need More Individual Members\Delegates to contribute to code
Send LS to GCF/PTCRB
  How to handle subtests, bands, power class etc, to bring harmonization in the ecosystem
Conclude on output format –
  Proposal1 - Matrix
  Proposal 2 - DCC (GCF)
  Proposal 3 - Hybrid View

## Slide 8
References:-
RAN5#100 R5-233200 SW Implementation of RAN5 Applicability, Qualcomm