## Slide 1: Discussion on handling of RF UL MIMO test case applicability
CMCC, Huawei
3GPP TSG-RAN5 Meeting #100 R5-234753
Toulouse, France, Aug 21 – 25, 2023

## Slide 2: Common test environment “PUSCH-Config” in TS 38.508-1
Observation 1: In TS 38.508-1 Section “4.6 Default NG-RAN RRC message and information elements contents/4.6.3 Radio resource control information elements”, 2 kinds of “Value/remark” are defined for IE “txConfig”.
When “txConfig=Not Present”, UE is scheduled for PUSCH transmission by DCI format 0_0 (“Short_DCI” Condition) for non-codebook based transmission
When “txConfig=codebook”, UE is scheduled for PUSCH transmission by DCI format 0_1 for codebook based transmission
TS 38.508-1 V17.9.0 (2023-06)

## Slide 3: Test configuration for UL MIMO in TS 38.521-1
Observation 2: Only DCI format 0_1 is used for codebook based UL transmission.
TS 38.521-1 V17.9.0 (2023-06)

## Slide 4: Common ICS for CB and NonCB in TS 38.508-2
14 | Supports MIMO layers at the UE for PUSCH transmission with codebook precoding. UE indicating support of this feature shall also indicate support of PUSCH codebook coherency subset | 38.306, 4.2.7.8 | Rel-15 | pc_nrMIMO_CB_PUSCH | No |  | Set to true if maxNumberMIMO-LayersCB-PUSCHhas value different from "oneLayer" | 
15 | Supports MIMO layers at the UE for PUSCH transmission using non-codebook precoding | 38.306, 4.2.7.8 | Rel-15 | pc_nrMIMO_NonCB_PUSCH | No |  | Set to true if maxNumberMIMO-LayersNonCB-PUSCHhas value different from "oneLayer" | 
Table A.4.3.2-1: UE Physical Layer Baseline Implementation Capabilities
Item | UE Physical Layer Baseline Implementation Capabilities | Ref. | Release | Mnemonic | M | If indicated “Yes”the feature shall be implemented and successfully tested for the corresponding release | Comments | 
A.4.3.2 Physical Layer Baseline Implementation Capabilities
Observation 3: In TS 38.508-2, both CB and NonCB have been defined as UE Physical Layer Baseline Implementation Capabilities, and Item 15 has been used in TS 38522-h90 (2023-06)
TS 38.508-2 V17.9.0 (2023-06)

## Slide 5: RF UL MIMO test cases applicability in TS 38.522
C003a IF A.4.1-1/1 AND A.4.1-2/7 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A
C060 IF A.4.1-1/2 AND A.4.1-2/8 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A
Observation 4: Quite a few conformance test cases conditions have used ICS “A.4.3.2-1/15” in TS 38522-h90 (2023-06), including C003a and C060/C151. However, ICS “A.4.3.2-1/15” (NonCB) should NOT be used in test case applicability conditions considering only “DCI format 0_1”(CB) has been used in RF UL MIMO test cases in TS 38.521-1.
C151 IF A.4.1-1/2 AND A.4.1-2/8 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A
TS 38.522 V17.9.0 (2023-06)
C003a IF NR FDD AND FR1 AND Option2 AND (CB OR NonCB) THEN R ELSE N/A
C060 IF NR TDD AND FR2 AND Option2 AND (CB OR NonCB) THEN R ELSE N/A
Observation 5: C060 and C151 are duplicated.

## Slide 6: Proposals
C003a IF A.4.1-1/1 AND A.4.1-2/7 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A
C060 IF A.4.1-1/2 AND A.4.1-2/8 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A
Proposal 1: In TS 38.522 “Table 4.0-1: Applicability of conformance test cases conditions” in Clause “4.0 Test case conditions and selection criteria”, to revise C003a and C060 as below.
C151 IF A.4.1-1/2 AND A.4.1-2/8 AND A.4.1-3/1 AND (A.4.3.2-1/14 OR A.4.3.2-1/15) THEN R ELSE N/A Void
C003a IF NR FDD AND FR1 AND Option2 AND (CB OR NonCB) THEN R ELSE N/A
C060 IF NR TDD AND FR2 AND Option2 AND (CB OR NonCB) THEN R ELSE N/A
Proposal 2: To replace C151 with C060, and have “Void” for C151.
Proposal 3: Considering ICS “A.4.3.2-1/15” is not used in TS 38.522 or TS 38.523-2, to replace the content of ICS “A.4.3.2-1/15” with “Void” in TS 38.508-2.

## Slide 7: Thank You!