## Slide 1: Discussion on handling of R18 NB-IoT/eMTC NTN test cases in TS 36.521-4
China Mobile, Mediatek, Keysight, Thales, Google, China Telecom, [R&S, Qualcomm]
3GPP TSG-RAN5 Meeting #100 R5-234756
Toulouse, France, Aug 21 – 25, 2023

## Slide 2: RAN4 Guidance on how to re-use TS 36.101 Clause 8 and 9 for IoT NTN
Observation 1: For IoT NTN Demod requirement in TS 36.102, it is indicated by Note in Table 8.2.1.2-1 that “For UE supports NTN access (ntn-Connectivity-EPC-r17), the requirements in TS 36.101 Clause 8 and Clause 9 also applies to UE according to the UE category and capability”.
Proposal 1: RAN5 to analyse how to re-use TS 36.521-1 Clause 8 and Clause 9 TCs for IoT NTN UEs in TS 36.521-4, one by one.

## Slide 3: How to leverage NB-IoT NTN Clause 8 TCs from TS 36.521-1 (1/3)
Observation 2.1: For TS 36.521-1 TC 8.12.1.1.1 “Demodulation of NPDSCH (Cell-Specific Reference Symbols) in In-band mode for category NB1 and NB2”, it is NOT applied for NB-IoT NTN considering there is no In-band mode for Rel-17/Rel-18 NB-IoT NTN.
Observation 2.2: For TS 36.521-1 TC 8.12.1.1.2 “Demodulation of NPDSCH (Cell-Specific Reference Symbols) in standalone and Guard-band mode for category NB1 and NB2”, “Guard-band mode” is NOT applied for NB-IoT NTN considering there is no Guard-band mode for Rel-17/Rel-18 NB-IoT NTN. Please check the snapshot from RAN4 revised WID RP-223437.
RAN4 WID RP-223437

## Slide 4: How to leverage NB-IoT NTN Clause 8 TCs from TS 36.521-1 (2/3)
Observation 2.3: For TS 36.521-1 TC 8.12.1.1.3 “Demodulation of NPDSCH (Cell-Specific Reference Symbols) in standalone for NB2”, it is applied for NB-IoT NTN.
Observation 2.4: For TS 36.521-1 TC 8.12.2.1.1 “Demodulation of NPDCCH single-antenna performance for category NB1 and NB2”, it is applied for NB-IoT NTN.
Observation 2.5: For TS 36.521-1 TC 8.12.2.1.2 “Demodulation of NPDCCH Transmit diversity performance for category NB1 and NB2”, it is NOT applied for NB-IoT NTN considering there is no transmit diversity 2*1 for Rel-17/Rel-18 NB-IoT NTN. Please Check the snapshot from R4-2220278 below, which was approved in RAN4#105 Meeting Report.
R4-2220278 WF on IoT-NTN UE demodulation and CQI reporting requirements

## Slide 5: How to leverage NB-IoT NTN Clause 8 TCs from TS 36.521-1 (3/3)
Proposal 2.1: RAN5 to re-use the following demod TCs from TS 36.521-1 for IoT NTN demod test cases in TS 36.521-4
  TC 8.12.1.1.3 “Demodulation of NPDSCH (Cell-Specific Reference Symbols) in standalone for NB2”
  TC 8.12.2.1.1 “Demodulation of NPDCCH single-antenna performance for category NB1 and NB2”
Proposal 2.2: RAN5 to partially re-use TC 8.12.1.1.2 from TS 36.521-1 by removing “Guard-band mode” for IoT NTN demod test cases in TS 36.521-4
  TC 8.12.1.1.2 “Demodulation of NPDSCH (Cell-Specific Reference Symbols) in standalone and Guard-band mode for category NB1 and NB2”

## Slide 6: How to leverage eMTC NTN Clause 8 TCs from TS 36.521-1 (1/2)
Observation 3.1: For TS 36.521-1 TC 8.11.1.1.1 “FDD and half-duplex FDD Closed-loop spatial multiplexing performance for UE supporting CE”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” are not applied for Rel-17/Rel-18 NTN.
Observation 3.2: For TS 36.521-1 TC 8.11.1.1.2 “FDD and half-duplex FDD PDSCH Single-layer Spatial Multiplexing on antenna ports 7 or 8 for UE supporting CE”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” or “2*2” or “2*4” are not applied for Rel-17/Rel-18 NTN.
Observation 3.3: For TS 36.521-1 TC 8.11.1.1.3.1 “FDD and half-duplex FDD PDSCH Transmit Diversity 2x1 for UE category M1”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” are not applied for Rel-17/Rel-18 NTN.
Observation 3.4: For TS 36.521-1 TC 8.11.1.1.3.1_1 “FDD and half-duplex FDD PDSCH Transmit Diversity 2x1 for UE category M1 (CEmodeB)”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” are not applied for Rel-17/Rel-18 NTN.
TS 36.102 V18.2.0 (2023-06)

## Slide 7: How to leverage eMTC NTN Clause 8 TCs from TS 36.521-1 (2/2)
Observation 3.6: For TS 36.521-1 TC 8.11.1.1.3.2_1 “FDD and half-duplex FDD PDSCH Transmit Diversity 2x1 for UE category M2 (CEmodeB)”, it is NOT applied for eMTC NTN considering there is no “category M2” for Rel-17/Rel-18 e-MTC NTN.
Observation 3.7: For TS 36.521-1 TC 8.11.2.1.1 “FDD and HD-FDD demodulation of MPDCCH in CE Mode A”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” are not applied for Rel-17/Rel-18 NTN.
Observation 3.8: For TS 36.521-1 TC 8.11.2.1.2 “FDD and half-duplex FDD demodulation of MPDCCH in CE Mode B”, it is NOT applied for eMTC NTN considering “10MHz” or “2*1” are not applied for Rel-17/Rel-18 NTN.
Proposal 3: Considering no legacy TS 36.521-1 TCs in Clause 8 “Performance Requirements” can be applied to eMTC NTN UEs due to lack of requirements for “CBW=1.4MHz and Antenna Configuration=1*1”, to send LS to RAN4 about the Observations 3.1~3.9 above and to ask RAN4 about the plan to adapt LTE performance requirements for UEs supporting eMTC NTN only (not supporting TN).
Observation 3.5: For TS 36.521-1 TC 8.11.1.1.3.2 “FDD and half-duplex FDD PDSCH Transmit Diversity 2x1 for UE category M2”, it is NOT applied for eMTC NTN considering there is no “category M2” for Rel-17/Rel-18 e-MTC NTN.
Observation 3.9: Only TS 36.102 cl. 8.2.1.1.1 can be used as the performance requirement for Rel-17/Rel-18 eMTC NTN at this stage.

## Slide 8: How to leverage TS 36.521-1 Clause 9 TCs for IoT NTN UE? (1/2)
Observation 4.1: For TS 36.521-1 TC 9.8.1.1 “FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement”, it is NOT applied for eMTC NTN considering “10MHz” is not applied for Rel-17/Rel-18 NTN.
Observation 4.2: For TS 36.521-1 TC 9.8.2.1 “FDD and half-duplex FDD UE-selected subband CQI for UE supporting coverage enhancement”, it is NOT applied for eMTC NTN considering “10MHz” is not applied for Rel-17/Rel-18 NTN.
Observation 4.3: For TS 36.521-1 TC 9.8.3.1 “FDD and Half duplex FDD CQI reporting definition under AWGN conditions for UE supporting coverage enhancement and 64QAM”, it is NOT applied for eMTC NTN considering “10MHz” is not applied for Rel-17/Rel-18 NTN.
Observation 4.0: As indicated in RAN4 revised WID (RP-223437), “NOTE: Rel-17 IoT NTN specifications do not cover reuse of TN NB-IoT/eMTC functionality defined later than Rel-16”. For Rel-16 and backward NB-IoT UE or eMTC Mode B UE, CSI reporting is not supported considering no CSI requirements have been defined in TS 36.211/TS 36.212/TS 36.213. For Rel-16 and backward eMTC Mode A UE, CSI reporting is supported. Please check the snapshot for “CEModeB” below from TS 36.213 V17.5.0 (2023-03) .
TS 36.213 V16.9.0 (2022-09)

## Slide 9: How to leverage TS 36.521-1 Clause 9 TCs for IoT NTN UE? (2/2)
Observation 4.4: For TS 36.521-1 TC 9.8.4.1 “FDD and half duplex FDD CQI reporting under AWGN conditions for UE supporting coverage enhancement and alternative table”, it is NOT applied for eMTC NTN considering “10MHz” is not applied for Rel-17/Rel-18 NTN.
Proposal 4.1: RAN5 NOT to consider CSI reporting for NB-IoT NTN UE or eMTC NTN Mode B UE.
Proposal 4.2: Considering no TCs in Clause 9 “Reporting of Channel State Information” can be applied to eMTC NTN UEs due to lack of requirements for “CBW=1.4MHz”, to send LS to RAN4 about the Observations 4.1~4.6 above and to ask RAN4 about the plan to define reporting of CSI requirements for UEs supporting eMTC NTN only (not supporting TN).
Observation 4.5: No leveraging can be done from TS 36.521-1 Clause 9 TCs for eMTC NTN Mode A UE due to different channel bandwidth.
Observation 4.6: No need to consider CSI reporting for NB-IoT NTN UE or eMTC NTN Mode B UE.

## Slide 10: How to handle TS 36.621-4 and R18 IoT NTN RF/RRM/Demod WI in R5
Proposal 5.1: Considering TS 36.521-4 target release time (Dec. 2023), RAN4 pending issues and the urgent market demands, suggest to mainly cover NB-IoT NTN in TS 36.521-4 (v1.0.0) which to be submitted to RAN#102 (Dec. 2023) for one-step approval, and to address eMTC NTN part in the following updated versions of TS 36.521-4 once RAN4 core requirements are ready.
Proposal 5.2: In order to kick-off/facilitate IoT NTN UEs certification, to calculate the completion level of NB-IoT NTN besides the whole completion level of “LTE_NBIOT_eMTC_NTN_req-UEConTest” WI for certification bodies’ (e.g. GCF, PTCRB, etc) reference.
Notes: R4-2307116

## Slide 11: Thank you!