## Slide 1: Discussion on handling of PRD21 v160
CMCC, China Telecom, [Huawei], [Ericsson]
3GPP TSG-RAN5 Meeting #100 R5-234772
Toulouse, France, Aug 21st – 25th, 2023

## Slide 2: Some R18 High power CA/DC configs are put into RAN4 R17 WI incorrectly
Observation 1 : Based on the approved WF R4-2217119[1] and CR R4-2303706[2], many higher order PC2/PC1.5 configs which are requested in Rel-18 HPUE WI, have already been incorrectly added in the Rel-17 specification under Rel-17 WI.

## Slide 3: These R18 High power CA/DC configs have already been introduced in RAN5 R17 WI
Observation 2: When importing these fivefour RAN4 completed R18 CADC Configs into PRD21 list (including: CA_n78(2A) with UL n78 PC2, CA_n77(3A) with UL n77 PC2, CA_n77C with UL CA_n77C PC2, DC_13A-48A-66A_n77A with UL DC_13A_n77A, DC_13A-48A-66A_n77A with UL DC_66A_n77A), it is found these R18 high power CADC configs had already been introduced into RAN5 in R17.
As per Observation 1, these R18 High power CA/DC configs are put into RAN4 R17 WI and Spec incorrectly. As a result, RAN5 introduced these configs into RAN5 R17 WI accordingly. Later on RAN4 introduced these R18 configs into R18 spec under R18 WI again. However, these five configs had already been introduced into PRD21 list in Rel-17.

## Slide 4
Observation 3:
Config CA_n77(3A) with UL n77 PC2 and CA_n77C with UL CA_n77C PC2 are in both RAN4 R17 Spec(38.101-1 ha0) and R18 Spec(38.101-1 i20);
Configs DC_13A-48A-66A_n77A with UL DC_13A_n77A PC2 and with UL DC_66A_n77A PC2 have been moved from RAN4 R17 Spec to R18 Spec(38.101-3 i20);
These R18 High power CA/DC configs status in R17 and R18 RAN4 Spec
Figure 1 CA_n77(3A) with UL n77 PC2
Figure 2 DC_13A-48A-66A_n77A with UL DC_13A_n77A/DC_66A_n77A PC2
Figure 3 CA_n77(3A) with UL n77 PC2
Configs | in RAN4 Rel-17 Spec? | in RAN4 Rel-18 Spec?
CA_n77(3A) with UL n77 PC2 | Yes | Yes
CA_n77C with UL CA_n77C PC2 | Yes | Yes
DC_13A-48A-66A_n77A with UL DC_13A_n77A PC2 | No | Yes
DC_13A-48A-66A_n77A with UL DC_66A_n77A PC2 | No | Yes
TS 38.101-1 V17.10.0 (2023-06)
TS 38.101-1 V18.2.0 (2023-06)
TS 38.101-3 V18.2.0 (2023-06)
TS 38.101-1 V18.2.0 (2023-06)
TS 38.101-1 V17.10.0 (2023-06)

## Slide 5: PRD21 guideline for importing new configs/bands/BWs
Observation 4: As per PRD21[3] guideline Section 4.1 Point 13, No new configs/new bands/new BWs shall be introduced into Chapter 5 of TS 38.521-1/2/3, unless they have already been introduced in RAN4.
Proposal 1: PRD21 list only imports RAN4 completed configs which have already been introduced in RAN4 spec(38.101-1/2/3).

## Slide 6: To update PRD21 list for these R18 High power CA/DC configs
Proposal 2: For R18 HP CADC Configs in both RAN4 R17 and R18 spec, to add "Rel-17, Rel-18" into "Release" Column, to add RAN5 R17 and R18 high power WIC “HPUE_NR_CADC_NR_LTE_DC_R18-UEConTest” into "WIC" Column, and to add corresponding comment for guidance.
Proposal 3: For R18 HP CADC Configs removed from RAN4 R17 spec to R18 spec, to repalce “Rel-17” with "Rel-18" in "Release" Column, and to replace RAN5 R17 HP WIC with R18 HP WIC “HPUE_NR_CADC_NR_LTE_DC_R18-UEConTest” into "WIC" Column.
Proposal 4: For further RAN4 newly completed R18 high power configs which share the similar situation above, Proposal 2-3 also are to be applied.

## Slide 7: Reference
[1] R4-2217119, WF on HPUE_Basket_Intra-CA_TDD; 3GPP TSG-RAN4 Meeting #104-bis-e, Emeeting, 10– 19 October 2022
[2] R4-2303706, CR on R17 TS38.101-1 Modification on the PC2 and PC1.5 note on the CA configuration with UL single carrier
[3] R5-232824, PRD21 on NR bands and 5G NR CADC config handling v1.5.0

## Slide 8: Thank you!