## Slide 1: Overview Update on AI/ML Progress in 3GPP RAN Core Groups
CMCC, Lenovo
3GPP TSG-RAN5 Meeting #106
Athens, Greece, February 17 – 21, 2025 R5-251237

## Slide 2
AI/ML for Air Interface SI
3GPP RAN AI/ML Layout
RAN1
RAN2
RAN4/RAN5
Rel-17
Rel-18
Rel-19
AI/ML for RAN SI: Initiate the exploration of 5G+AI integration, develop a unified functional framework, and study solutions for network energy saving, load balancing, and mobility use cases
AI/ML for RAN WI: Define solutions for three major use cases, develop a unified protocol process, and focus on Xn interface enhancement
Study the model Life Cycle Management framework; Study and simulate major use cases, including CSI feedback enh., Beam Management enh., Positioning enh.
R19 SI+WI: Solutions for AI-based dynamic slice resource allocation and management, coverage and capacity optimization, and NR-DC mobility optimization
AI/ML for Air Interface WI: Standardize three major use cases, and continue to study CSI compression solutions
AI/ML for Mobility SI: Study AI-based mobility management: RRM measurement prediction, measurement event prediction, HOF/RLF prediction; Evaluate testability, interoperability, and the impacts of the prediction use cases above on RRM requirements
Study data collection processes, potential schemes for model transmission, and other life cycle management processes on the network/terminal side.
RAN3
Study the interoperability and testability of major use cases, including CSI feedback enh., Beam Management enh., Positioning enh..
Rel-16 pre-AI
Big Data Collection SI: Study network intelligence use cases and corresponding solutions, including MRO and MLB
Big Data Collection SI: Define a unified data collection framework for network intelligence, laying the foundation for subsequent AI training data collection
AI/ML

## Slide 3
AI/ML for Air Interface-AI based Beam Management (RAN1, R18 SI+R19 WI)
To reduce measurement overhead and beam indication delay of traditional BM, AI based BM simplifies UE implementation. 3GPP enhances inference configuration to adapt standards to AI algorithms, designs monitoring mechanism to make AI models controllable.
use case：predict Top K beams based on the measurement results of partial beams
performance gain：reduce measurement overhead, increase beam indication accuracy
standardization progress：LCM operation design
  inference：support the configuration of prediction beam set
  monitoring：support NW side monitoring and UE assisted monitoring, support beam prediction accuracy as KPI
  consistent performance between training and inference：associated ID to be configured per cell to enable the consistency
spatial domain beam prediction (WI)
time domain beam prediction (WI)
use case：predict Top K beams of future instances based on the measurement of beams in past instances
performance gain：increase beam prediction accuracy by 50%~60%
standardization progress：
  inference：support prediction instance indication
  monitoring：support the association of monitoring report configuration and inference report configuration for calculation of monitoring KPI
predict narrow beams(Set A) basing on wide beams(Set B)
predict narrow beams basing on narrow beams
predict Top K beams for 4 future instances based on the real beam measurement results of the 4 past instances

## Slide 4
AI/ML for Air Interface-Positioning Enhancement (RAN1, R18 SI+R19 WI)
To address the challenge of positioning in heavy NLOS indoor factory scenarios, sub-meter positioning accuracy is achieved through AI/ML-based direct and assisted positioning technologies, expanding the applicable scenarios of 5G positioning technology
Current Progress in 3GPP
Scenario: Indoor factory with heavy NLOS
Model Location：UE-side, gNB-side, LMF-side
Sub Use Cases：
  Direct AI/ML positioning: The output of AI/ML model is UE location
  AI/ML assisted positioning: The output of AI/ML model is the results of new measurement and/or enhancement of existing measurement, basing on which UE location can be calculated.
Performance：
  Both direct and assisted AI/ML positioning can significantly improve the positioning accuracy compared to existing RAT-dependent positioning methods when the generalization aspects are not considered.
  For example: For InF-DH with clutter parameter setting {60%, 6m, 2m}, evaluation results indicate that both direct and assisted AI/ML positioning can achieve horizontal positioning accuracy of <1m at CDF=90%, as compared to >15m for conventional positioning methods.
Standardization Progress (WI)：
  For each sub use cases, defining model input and output
  LCM and performance monitoring procedure for different Model Locations
  Method to ensure consistency between training and inference
  Definition of sample-based measurement for Case 3b
AI Based Positioning accuracy<1m

## Slide 5
AI/ML for Air Interface-CSI enhancement (RAN1, R18 SI+R19 SI/WI)
Addressing the issues of low CSI acquisition accuracy of traditional codebook and significant CSI acquisition latency in high-speed scenarios, AI-based CSI compression and CSI prediction can increase system throughput by 7%~16%, further improving the spectral efficiency of 5G networks
Use case：Based on past CSI measurement results, predict the CSI of several future time slots.
Performance Gain：
The average system throughput can be increased by up to 7%, and the edge throughput can be increased by up to 20%
up to ~30 times of complexity improvement is observed in AI compared to traditional methods
Through mixed data training, the decent generalization performance is observed in aspects, including UE speed, channel scenario and carrier frequency.
Standardization Progress：
The first phase of R19 has completed performance evaluation and CSI prediction was successfully converted into WI in RAN#105@September 2024.
Use case：A two-sided model is deployed with encoders and decoders on the UE side and gNB side to compress and reconstruct CSI
Performance Gain：
The average system throughput can be increased by about 7~16%, and the edge throughput can be increased by about 13~40%.
The decent generalization performance is observed in some aspects, including the number of base station ports and channel scenarios.
Standardization Progress：
CSI compression (SI)
CSI prediction (WI)
Since this use case employs a two-sided model, it requires inter-vendor collaboration, which makes the model deployment much challenging. R19 continues to study this use case:
  By introducing additional temporal CSI information, the benefits of the use case can be expanded through spatial-temporal-frequency CSI compression.
  R19 is studying the two-sided model deployment methods through model/data transfer, standardization of models/model structure

## Slide 6
AI/ML for Air Interface-UE side data collection SI (RAN2, R18+R19)
It is controversial in RAN2 on how to perform data collection for UE-side model training, since companies (e.g. MNO, network vendor, UE vendor, chipset vendor) have different concerns on data privacy, which have been captured in TR 38.843.
RAN2 will further discuss option 2/3 and take into account SA inputs when available.
Option 1a：UE collects and directly transfers training data to the data collection entity outside the MNO (e.g. Over-The-Top (OTT) server) for UE-side model training
  Transparent to 3GPP, and no 3GPP impact is expected
  Offline efforts between Chipset vendors and UE vendors may be needed to acquire the UE modem data
Option 1b：UE collects training data and transfers it to the server for data collection for UE-side model training (inside the MNO) and then optionally transferred to the OTT server (outside the MNO)
  EVEX-like solution (UP-based solution), where the UE modem data is transferred via DCAF (Data Collection Application Function) to OTT server, which is transparent to MNO
  Option 1b has been excluded in RAN#106@December 2024
Option 2：UE collects training data and transfers it to Core Network. Core Network transfers the training data to the server for data collection for UE-side model training/OTT server
  Data format and data content to be specified
  Spec impacts on RAN2/SA2 may be considered
Option 3：UE collects training data and transfers it to OAM. OAM transfers the training data to the server for data collection for UE-side model training/OTT server
  Data format and data content to be specified
  Spec impacts on RAN2/SA5 may be considered
Potential solutions
Fig 2：Option 2/3 (CN/OAM)
UE modem
Fig 1：Option 1b (EVEX-like)
Data transmission
New interface

## Slide 7
AI/ML for Air Interface—NW side data collection (RAN2, R18 SI+R19 WI)
The data is collected for NW-side model training. For the NW-side data collection related to beam management use cases, gNB-centric and OAM-centirc approaches are considered, where the same measurement framework is applied, and the details are still under discussion.
For Beam Management (prioritized)：
  NW-side model refers to gNB-side model, and model training is performed by gNB or OAM
  Solutions for data collection
    Immediate MDT is the baseline framework for OAM-centric data collection for model training
    Support the logged L1 measurement results to reduce the signaling overhead, which is an optional feature
      Periodic logging
      Event-triggered logging (e.g. radio condition based)
    Logged measurement reporting
      On-demand reporting is supported
      Periodic logging is not supported
For positioning：
  NW-side model refers to gNB-side model or LMF-sided model, and model training is performed by gNB or LMF
  Will be discussed based on RAN1’s progress, and the agreements for BM will be reused as much as possible
Progress in RAN2 (WI)
Enhanced immediate MDT
common measurement feamework

## Slide 8
AI/ML for Mobility SI (RAN2, R19)
With existing L3 handover mechanism, handover is triggered and executed based on reported historical measurement result and/or measurement event(s). It may work well among macro cells when UE’s mobility is low for existing services.
But it could be problematic when either UE’s mobility is high or among micro cells of high density or both for existing services or future services (e.g. XR), where such reactive scheme may result in more unintended event e.g., Handover Failure, Radio Link Failure, Ping-Pong phenomenon, throughput loss or too early/too late handover, etc.
RRM measurement prediction (highest priority)
  Temporal domain prediction, spatial domain prediction, frequency domain prediction
    Case 1: L1 beam level measurement results-> L1 beam level event-> L3 cell level event
    Case 2: L1 beam level measurement results-> L3 cell level event
    Case 3: L3 cell level measurement results-> L3 cell level event
  Both UE-side model and NW-side model are considered
Measurement event prediction
  Direct prediction, indirect prediction (prioritized)
  UE-side model is considered
RLF/HOF prediction
  Direct prediction, indirect prediction (prioritized)
  HOF prediction is de-prioritized
  UE-side model is considered
Note: “Indirect prediction” refers to deducing whether a measurement event or RLF occurs based on the RRM measurement prediction results
Use cases
General
  Focus on RRM measurement prediction, some agreements have been achieved in RAN2
  Simulations on model generalization, measurement event and RLF prediction are ongoing, and results are expected in February and April 2025
Study goal of RRM measurement prediction
  1st goal: reduce UEs’ measurement overhead
  2nd goal: improve handover performance
Evaluation scenarios for RRM measurement prediction
  FR1-FR1 intra-frequency temporal domain case B
  FR2-FR2 intra-frequency temporal domain case A
  FR1-FR1 inter-frequency (frequency domain)
  FR2-FR2 intra-frequency spatial domain
  FR1-FR1intra-frequency temporal domain case A
  FR2-FR2 intra-frequency temporal domain case B
Simulation
Temporal domain case B
（1st goal)
Spatial domain
Frequency domain
Legacy MG
AI-based
High priority
Low
Priority
Medium
Priority
Temporal domain case A (2nd goal)

## Slide 9
AI/ML for RAN SI (RAN3, R17 )
The 1st AI + RAN research project, has selected and studied 3 high-priority use cases: Network Energy Saving, Load Balancing, and Mobility Optimization. A unified functional framework has been defined and captured in TR 37.817.
Data Collection: Provides input data to Model training and Model inference functions Model Training: Performs AI/ML Model training, validation and testing Model Inference: Provides AI/ML model inference output (e.g., predictions or decisions) Model Performance Feedback: Monitors the performance of the AI/ML models, when available (e.g. comparing AI/ML prediction results with real results (ground truth) to evaluate the performance of the model) Actor: Receives the output from the Model Inference function and triggers or performs corresponding actions
Network Energy Saving
Realize better cell activation/deactivation by predicting energy consumption efficiency and cell load
Load balancing
Predict handover schemes based on the wireless resource status information of local base stations/neighboring stations to improve load balancing performance and user experience
Mobility optimization
Predict the movement trajectory of UE to optimize the handover strategy, in order to avoid potential problems such as too early handover, too late handover, and handover to the wrong cells
The cell shutdown duration is increased by 90%.
The maximum energy savings can reach 1.24 KW×H
AI functional framework for wireless network
Three typical use cases
No direct impacts to RAN5 Just for whole RAN picture

## Slide 10
AI/ML for RAN WI (RAN3, R18 )
The solutions for the SI 3 major use cases are defined, and a unified Xn protocol process for AI data request and feedback is developed.
Define the AI/ML data request and feedback process, applicable to all use cases and data types including input/output/feedback, etc.
  Data Collection Reporting Initiation procedure: Used to trigger AI/ML-related data collection
  Data Collection Reporting procedure: Used to report AI/ML-related information
Prediction information interaction:
  Predicted UE trajectory information: Pre-configure resources for the UE being about to handover to improve resource utilization efficiency
  Predicted resource status information: Predicted wireless resource status, RRC connection number, etc., enabling the current node to understand the future resource status of neighboring nodes for model training
Feedback information interaction:
  UE performance feedback information: Uplink and downlink throughput, packet loss rate, etc., monitoring the prediction accuracy of AI models
  For the mobility optimization use case, UE trajectory information feedback scheme is proposed, which is based on specific trigger conditions, including time, number of handovers, and state transitions to improve the flexibility of feedback
  For the network energy saving use case, the energy consumption index is introduced, where the mapping relationship between the energy consumption index and the energy consumption value is defined by the operators
Unified protocol process
Interface enhancement
No direct impacts to RAN5 Just for whole RAN picture

## Slide 11
AI/ML for RAN SI+WI (RAN3, R19 )
Study solutions for use cases, including dynamic slice resource allocation, coverage and capacity optimization, and mobility optimization in NR-DC scenario, and enter into WI phase
Dynamic slice resource allocation
Dynamically allocating slice resources within/among nodes by predicting slice-level resource status, UE mobility, etc., to improve the slice resource utilization efficiency
Exchange the information on predicted slice-level resource status, UE to be handed over, etc. among nodes, in order to assist neighboring nodes in pre-configuring slice resources for the handed-over UE
Coverage and capacity optimization (CCO)
Use AI to predict coverage and capacity problems, and adjust relevant configurations in advance to reduce the impact of coverage and capacity problems on system performance
Exchange the coverage configuration adjustment time among nodes to ensure that neighboring nodes synchronously adjust the corresponding coverage configuration to avoid coverage holes
Mobility optimization in NR-DC scenario
MN perform inference and prediction based on resource status, UE trajectory, transmission delay, etc. to optimize the selection of the target SN and PSCell during the SN addition/change process
Study the start and end mechanisms of the measurement of the UE performance and other feedback information to make it more suitable for the dual-connection scenario (e.g., the status change of UE between single connection and dual connection)
Coverage and capacity optimization
New use case study
MN-initiated SN Addition/Change
Inter-Maste Node handover with/without SN change
No direct impacts to RAN5 Just for whole RAN picture

## Slide 12
AI/ML for Air Interface/Mobility (RAN4, R18 SI+R19 WI/SI)
Study the interoperability and testability of major use cases, including CSI feedback, Beam Management, Positioning. Study AI/ML for Mobility (R19).
Post deployment handling (WI)
To ensure the AI performance after device deployment, ongoing disucssions with 2 options below without significant progress
Option1: Conduct the validation of a change in functionality before its deployment/activation in already deployed UEs.
Option2: Using performance monitoring and LCM procedures
Testing environment/framework (WI)
Static: channel model and SNR settings are fixed and do not change over the test, specific channel realizations may be dynamic
Non-static: Non-static scenarios/configuration can be further considered in application to use cases. The details of models are FFS and may include non-stationary SNR and other conditions.
Reference and test encoder/decoder (SI)
Test decoder (for UE side test): the decoder to be used in RAN4 tests and implemented in TE. it will be captured in the specifications if necessary. Test decoder definition covers Option 3 (Full decoder specified in standard) and Option 4 (TE vendor provides the decoder)
AIML two-sided model logistical issues (SI)
Data sharing among interested companies is ongoing, only for the CSI compression use case feasibility study.
LCM Requirements (WI)
RAN4 considers defining RRM requirements for LCM procedures based on the specific use cases (beam management and positioning), and candidates include: identification, selection, activation, deactivation, switching, fallback to non-AI operation, performance monitoring
Legacy RRM requirements handling (WI)
UE shall meet all legacy RRM requirements (non-AI/ML) even during the AI/ML operation mode.
Positioning (WI)
No positioning accuracy requirements for case 3a/3b
No requirements on LMF for positioning accuracy for case 2a/2b
CSI Prediction (WI)
Throughput should be the default metric for inference only
AI/ML based performance req. should not be worse than the legacy (non-AI/ML) if a relevant equivalent legacy req./feature exists

## Slide 13
Observations and Proposals
Observations:
Observation 1: AI has shown some performance gains in multiple use cases, but it still faces many challenges in terms of model training data acquisition, data privacy security, model generalization, additional computing power and system complexity required for model training and inference.
Observation 2: No significant progress has been observed in RAN1/RAN2/RAN4 groups for AIML in Q4 2024.
Proposals:
Proposal 1: RAN5 continues to look for opportunity to start contributing to topics that could speed up the work of Rel-19 AIML core WI.
Proposal 2: Besides the areas below, RAN5 continues to identify more areas where RAN5 expertise may help to progress core group work.
    AIML conformance test framework.
    MU/TT analysis based on RAN4 test parameters and test setup.
    UE lab conformance aspects of post-deployment testing.

## Slide 14: Thank you !