## Slide 1: Disc on handling XR PDCP discard TCs
CMCC
3GPP TSG-RAN5 Meeting #106
Athens, Greece, February 17 – 21, 2025 R5-251367

## Slide 2
XR PDCP discard TCs need to define RTP header extension
Observation 1: RTP header extension includes some key parameters related to XR PDCP discard PDUSet Discard/PSI and DSR triggering TCs.
TS 26.522 i10
TS 26.522 i10

## Slide 3
Some test assumptions for XR PDCP discard TCs
Assumption 1 (SS side): SS/TTCN can create RTP packet in internet PDU session without IMS voice/video call and RTP packets include RTP header extension for PDU set Marking.
Assumption 2 (UE side): UE can recognize the loop backed packet as RTP packet and perform PDU set/PSI identification based on RTP header extension.
Assumption 3 (UE side): UE can treat the PSI=15 (lowest value) packet as low importance, and can treat the PSI=1 (highest value) packet as high importance.
Proposal 1: PDCP discard TCs are tested based on these assumptions and can be tested only if all assumptions are met.
Proposal 2a: It is proposed to capture these assmuptions in TCs editor notes in TS 38.523-1.
Proposal 2b: It is proposed to capture these assmuptions in TS 38.508-2 PICS.

## Slide 4
XR PDCP discard TCs need to define RTP header extension
Proposal 3: It is proposed to endorse the methodology in R5-250135 to define RTP header extension for PDU Set Marking.
R5-250135

## Slide 5
TC 7.1.3.5.8 PDU Set based discard
PDU Set based discard flow chart
R5-250133
RTP header extension definition

## Slide 6
TC 7.1.3.5.9 PSI based discard
PSI based discard flow chart
R5-250134
RTP header extension definition

## Slide 7
TC 7.1.3.5.10 PSI based discard and DSR triggering
Proposal 4: It is proposed to endorse methdologies in Slide 4,5 and 6 as test procedures of PDCP discard TCs .
DSR triggering flow chart
RTP header extension definition
R5-250135

## Slide 8: Thank you !