## Slide 1: Update on AI/ML WI Progress in 3GPP RAN4 and RAN2
CMCC, Lenovo
3GPP TSG-RAN5 Meeting #107
Malta, MT, May 19 – 23, 2025 R5-252119

## Slide 2: Progress on AI/ML air interfance WI during RAN4#114(Feb. 2025) & RAN4#114bis(Apr. 2025)

## Slide 3
RAN4: CSI reporting requirement framework for CSI prediction
Issue 1-2: Reference model for CSI prediction[1]
Agreement:
n Assume no reference AI model for CSI prediction as baseline
n If it is difficult to align the results corresponding to test metric, RAN4 will discuss the reference model.
Issue 1-3: Training and test data consistency[1]
Agreement:
n further discuss the following options
n Option 1: Consistency between training data and test data should be ensured
u RAN4 to study how to ensure consistency between training data(simulation) and test data (conformance test) and whether anything special should be done during the test
n Option 2: Consistency will be implicit as test emulated channel will be very similar to the one used in RAN4 simulations
Issue 1-4: Generalization[1]
Agreement:
n Postpone this discussion until the requirement and test definition is clear

## Slide 4
RAN4: CSI reporting requirement framework for CSI prediction
Issue 1-1: Codebook to be used in the tests[3]
Agreement:
l In Rel-19 only PMI requirements based on AI/ML CSI prediction will be defined
l use Rel-18 eType II Doppler codebook for AI/ML based CSI predictions
Issue 1-2: Requirement baseline[3]
Agreement:
o Requirement to be introduced for Dopler domain basis N4=1
· N4>1 can be further discussed in the future if needed
Issue 1-4: Test metric[3]
Requirements to be defined based on the ratio (same metric as for the current PMI reporting requirements in 38.101-4)
· tue_AI/ML is 90% of the maximum throughput obtained at SNRue_AI/ML [a given SNR] using the precoders configured according to the UE reports,
· trnd is the throughput measured at SNRue_AI/ML [the same SNR] with random precoding.
  o trnd is obtained with Rel-15 type I single panel codebook
· Note: SNRue_AI/ML is calculated in the same way as SNRue and SNRfollow1,follow2 in section 6.3 of 38.101-4

## Slide 5
RAN4: Testability and interoperability issues for beam management
Issue 2-1: Metrics/KPIs for beam prediction[1]
If RSRP and beam ID are reported:
· RSRP accuracy will be one of the KPIs.
o How option 1 is applied is FFS
· Beam ID prediction accuracy will be one of the KPIs
o FFS whether beam ID prediction accuracy refers to a combination of Option 2 and/or Option 3 or modified Option 2/3 or other options
If only beam ID is reported:
· Beam ID prediction accuracy will be used as the KPI
o FFS whether beam ID prediction accuracy refers to a combination of Option 2 and/or Option 3 or modified Option 2/3 or other options
Issue 2-4: QCL Source RS for TCI states[1]
Agreement:
wait for RAN1 discussion to conclude without sending any LS
For metrics for beam management requirements/tests, the following test metrics are identified and could be considered [2]
- Option 1: RSRP accuracy
- Option 2: Beam prediction accuracy
-Top-1 (%) : the percentage of "the Top-1 strongest beam is Top-1 predicted beam"
-Top-K/1 (%) : the percentage of "the Top-1 strongest beam is one of the Top-K predicted beams"
-Top-1/K (%) : the percentage of "the Top-1 predicted beam is one of the Top-K strongest beams"
- Option 3: The successful rate for the correct prediction which is considered as maximum RSRP among top-K predicted beams is larger than the RSRP of the strongest beam – x dB,
-Related measurement accuracy can be considered to determine x

## Slide 6
RAN4: RRM core requirement and testing framework for beam management
Issue 2-1: Metrics/KPIs for beam ID prediction[3]
Agreement:
n Metrics/KPIs for beam ID prediction, at least for the case if only beam ID is reported:
The successful rate for the correct prediction,
n The correct prediction is considered as maximum ground-truth RSRP among top-K predicted beams larger than or equal to the ground-truth RSRP of the strongest genie-aided beam(s) – x dB,
n FFS on top-N (N</=K) predicted beams have to be considered in the success rate evaluation
u FFS on N values
n FFS on x values
Note: if x=0 and N=1, it means Top-K/1 (%) : the percentage of "the Top-1 strongest beam is one of the Top-K predicted beams"
Issue 2-2: Absolute RSRP accuracy[3]
Agreement:
n Absolute RSRP accuracy requirement applies to Top-1 of predicted beams at least
n FFS whether to apply to other beams

## Slide 7
RAN4: RRM core requirement and testing framework for beam management
Issue 2-3: Relative RSRP accuracy[3]
Agreement:
n RAN4 to use the follow as baseline for further discussions, if the relative RSRP accuracy requirement is defined
Ø Relative RSRP accuracy for reported beams during inference reporting = (predicted L1-RSRP of beam index i - reported L1-RSRP of beam index n) - (ground truth of L1-RSRP of beam index i - ground truth of L1-RSRP of beam index n), [where the beam index n owns the largest reported value].
² Reported L1-RSRP can be predicted,
² FFS whether reported L1-RSRP can be measured RSRP
Ø Relative RSRP accuracy requirements apply for Case 1, and FFS on whether it can apply for Case 2
Issue 2-4: Measurement period for inference[3]
Agreement:
n For measurement delay component of the prediction delay:
Ø Use “legacy” L1-RSRP measurement as the baseline for Case 1
² FFS whether same values for M,N,P should be reused
FFS for case 2
Beam management use case
BM-Case1: Spatial-domain Downlink beam prediction for Set A of beams based on measurement results of Set B of beams
BM-Case2: Temporal Downlink beam prediction for Set A of beams based on the historic measurement results of Set B of beams

## Slide 8
RAN4: Requirements for positioning
Issue 3-4: Report mapping for UL SRS-RSRP[1]
Agreement:
Reuse the report mapping for UL SRS-RSRP to Case 3a.
Positioning use case
- Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
- Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
- Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
- Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
- Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 9
RAN4: RRM core requirement and testing framework for Positioning accuracy enhancement
Issue 3-2: LOS/NLOS indicator[3]
Agreement:
the LOS/NLOS indicator is out of scope of WID. Stop discussions on it.
Issue 3-3: Rx-Tx time difference for case 3a[3]
Agreement:
n Introduce gNB Rx-Tx time difference reporting accuracy requirements
- Reuse legacy accuracy requirements
Issue 3-4: Report mapping for gNB Rx-Tx time difference[3]
Agreement:
n Reuse the existing report mapping for gNB Rx-Tx time difference measurements

## Slide 10
RAN4: Testing for one sided models
Issue 4-1: Baseline test setup[1]
Agreement:
n Discuss both single AoA based and multiple AoA based set up
n Continue to study the two multiple AoA candidate setups
u One option to continue the discussion proposed as following:
l Multi AoA setup – evaluation of already feasible systems for AI/ML BM testing suitability
n AI/ML BM performance centric, not CDL channel emulation centric.
n Define test system candidates which are already feasible
l Perform system level simulations including the probe layout of candidate systems to address the impact on the UE AI ML BM performance.
n Start with the set up with Set A = 32 beams, Set B = 8 beams, and develop the test procedures with single AoA and multiple AoAs
Issue 4-2: Channel model[1]
Agreement:
n Use CDL-based channel model as starting point

## Slide 11: Progress on AI/ML air interfance WI during RAN2#129(Feb. 2025) & RAN2#129bis(Apr. 2025)

## Slide 12
RAN2: Organizational
Agreements on positioning[5]
Þ RAN2 has not and will not study Case 2a and Case 2b in Rel-19
Þ Respond to SA2 indicating our current situation
Positioning use case
- Case 1: UE-based positioning with UE-side model, direct AI/ML or AI/ML assisted positioning
- Case 2a: UE-assisted/LMF-based positioning with UE-side model, AI/ML assisted positioning
- Case 2b: UE-assisted/LMF-based positioning with LMF-side model, direct AI/ML positioning
- Case 3a: NG-RAN node assisted positioning with gNB-side model, AI/ML assisted positioning
- Case 3b: NG-RAN node assisted positioning with LMF-side model, direct AI/ML positioning

## Slide 13
RAN2: Functionality based LCM for UE-sided model for Beam Management use case
Agreements on LCM for UE-sided model for Beam Management use case[5]
1. Inference configuration/parameters can be signalled in step 3 and/or Inference configuration can be signalled in step 5 (i.e. option a and option b from RAN1).
2. The full inference configuration is sent in CSI-ReportConfig.
3. Upon receiving a full inference configuration, the UE sends the initial applicability report in RRCReconfigurationComplete. UAI can be sent to update applicability.
4. FFS signaling details for option B (e.g. whether it is signaling in CSI-Report Config or otherconfig)
In Step 3, following configurations are provided from NW to UE[8]
- A) One or more of CSI-ReportConfig for inference configuration (wherein the associated ID may be configured in CSI framework as working assumption applied)
- B) One set or multiple sets of inference related parameters for applicability report only (not for inference)
Signalling procedure on applicable functionality reporting for beam management UE-sided model[7]

## Slide 14
RAN2: Functionality based LCM for UE-sided model for Beam Management use case
Agreements applicability reporting and management [5]
Þ Support the explicit reporting of applicability/inapplicability in initial report and subsequent reporting it reports only applicability it changed. FFS if we report explicit cause
Þ If option A is configured in Step 3, for periodic CSI reporting, the UE autonomously activate the applicable functionalities upon reporting applicable functionalities via RRCReconfigurationComplete in step 4 (i.e. without need to wait RRCReconfiguration in Step 5).
Þ The provided periodic CSI configuration should be consistent with reported UE capabilities
Þ FFS option B
Þ Semi-persistent and aperiodic CSI reporting of applicable functionality is activated following legacy CSI framework:
Semi-persistent reporting, activated by MAC CE/DCI
Aperiodic CSI reporting, activated by DCI

## Slide 15
RAN2: Functionality based LCM for UE-sided model for Beam Management use case
Agreements on option B [6]
1 RAN2 assumes UE receives RRCReconfiguration message including one set or multiple sets of inference related parameters via OtherConfig for option B. This assumption can be confirmed (i.e., whether to reconsider CSI-ReportConfig) after receiving Option B inference related parameters (e.g., in RAN1 RRC parameters list).
Potential aspects to consider if RAN2 revisit:
- To reconsider CSI-ReportConfig for option B, for example, if the list of inference related parameters is fully contained within existing CSI-ReportConfig.
- to take into accounts UE behaviour when confirming the assumption e.g., whether option A and option B result in different UE behavior
Agreements on applicability reporting [6]
1 Together with inapplicability reporting, UE further indicates a simple cause value of inapplicability FFS how to define this simple cause related to model availability and how we capture it in the spec
2 Upon receiving one or more full inference configuration(s) via RRCReconfiguration message, UE shall maintain all the full inference configuration(s) no matter the full inference configuration is applicable or inapplicable until the network releases it explicitly.
3 No prohibit timer is introduced

## Slide 16
RAN2: Functionality based LCM for UE-sided model for Beam Management use case
Agreements on data collection configuration[6]
Þ The UE can request measurement configuration for data collection of AI/ML based beam management. The request can contain one or more of the following:
• An indication on start/stop of data collection
• Preferred configuration from a list of candidate configurations provided by NW. Details of signaling are FFS. It is up to network what it configures at the end.
Þ Introduce UAI message for UE request of data collection measurement configuration. And it is up to UE implementation when to send the request.

## Slide 17
RAN2: Functionality based LCM for Positioning use case
Agreements [5]
1: Introduce AI/ML positioning Case 1 as a new positioning method.
2: Existing LPP procedures related to Location Information Transfer (RequestLocationInformation/ ProvideLocationInformation messages) are used for providing and requesting the results of the UE sided model inference operation. The detail stage 3 message extention can be disucssed while drafting the stage 3 CR.
3: FFS UE autonomous switching between AI/ML and non-AI/ML methods is not allowed. FFS if this is unconditional or linked to condition of multiple positioning method are not configured in RequestLocationInformation,
4: The content of error cause is discussed while drafting stage3 CRs.
5: As a baseline, UE receives the needed assistance data for calculating UE location for AI/ML in step3 (ProvideAssistanceData) and UE receives the instruction to perform the inference in step 5 (RequestLocationInformation). The content of Assistance Data and the content of request location information is based upon RAN1 parameter list.
6: UE reports the applicable functionality to the LMF by the LPP provide capabilities message if there is a change of applicable functionality. FFS if any additional LMF control is needed.

## Slide 18
RAN2: Functionality based LCM for Positioning use case
Agreements for positioning case 1 [6]
1 LMF is responsible for functionality management
2 UE reports the applicable functionality to the LMF by the LPP provide capabilities message without any additional LMF control.
3 Switching/fallback to non-AI/ML positioning can be supported by including multiple positioning methods in a LPP Request Location Information message. No additional specification work is foreseen specifically for supporting "switching/fallback operation".
4 An AIML positioning functionality is considered “activated” once UE receives an LPP RequestLocationInformation from the LMF requesting inferred location information.
5 For triggered and periodical reporting, we rely on existing positioning framework mechanisms to deactivate AI/ML positioning (no spec impact is foreseen)

## Slide 19
RAN2: NW side data collection
All agreements for NW side data collection[5]
1. Support the use of L3 measurement event triggered (i.e. L3 serving cell measurements becoming worse/better than a threshold for TTT) to determine whether the UE performs logging or not. L1 measurement event triggered will not be supported. FFS what to log
2. Low power bit indication is supported
3. Data availability indication is supported. FFS when this would be triggered
4. As baseline, the UEInformationResponse contains one or more logged measurement entries in chronological order (i.e. starting from the oldest measurement entries stored in the UE memory), and an availability indication if there are further data available for transmission. Same principles as for logged MDT.
5. UE retains logged data during handover (HO). FFS if there is scenarios where the UE needs to release the data and how does the UE know and if control from network is needed
6. UE indicates availability of logged data during handover (i.e., within the RRCReconfigurationComplete message) (if data is retained in the UE).
7. FFS how to handle idle/inactive and RLF cases and whether we have a unified.

## Slide 20
RAN2: NW side data collection
Agreements on Idle/inactive and HO [6]
Þ Introduce 1-bit indication on whether to release or retain un-retrieved data in RRCReconfiguration during/before HO. Source gNB decides whether the data should be kept. The indication is provided in RRCReconfiguration (i.e. not in RRC Reconfiguration from target cell). FFS signaling details.
Þ Upon going to RRC_IDLE, RLF, or RRC_INACTIVE, UE discards any logged data
Agreements on availability indication [6]
Availability indication can be triggered due to:
o Full buffer being reached (if configured)
o Buffer threshold being reached (if configured).
o Low power (if configured)
The UE send a UAI that indicates:
o Data is available
o Reason for trigger (full buffer, threshold)
o Low power indication
The encoding of the data is available/UAI and the cause value is FFS
NOTE: it is up to UE Implementation how buffer threshold reached and low power is determined

## Slide 21
RAN2: NW side data collection
Agreements [6]
1. For temporal domain, the network is made aware whether there is a gap between two consecutive samples. FFS amount of gap and whether this is implicit or explicit
2. New SRB can be configured for NW-side data collection (with lower priority)
Agreements on data collection configuration [6]
1 The measurement configuration of AI/ML data collection can configure measurements for multiple sets of resources and use cases (e.g. BM, Mobility, etc)

## Slide 22
Observations and Proposals
Observations:
Observation 1: Progress has been observed in RAN2/RAN4 groups for AIML from Feb 2025 to April 2025.
Observation 2: Rel-19 AIML core WI in RAN1 will be closed in May/June 2025, while Rel-19 AIML core WI in RAN2/RAN4 will be closed in Aug/Sep 2025.
Proposals:
Proposal 1: RAN5 continues to look for opportunity to start contributing to topics that could speed up the work of Rel-19 AIML core WI.
Proposal 2: Besides the areas below, RAN5 continues to identify more areas where RAN5 expertise may help to progress core group work.
    AIML conformance test framework.
    MU/TT analysis based on RAN4 test parameters and test setup.
    UE lab conformance aspects of post-deployment testing.

## Slide 23
Reference
R4-2502856, WF on the requirements for AI/ML air interfance, 3GPP TSG-RAN WG4 Meeting#114, Athens, Greece, 17th – 21st February, 2025
R4-2503012, AI/ML ad-hoc meeting minutes-1, 3GPP TSG-RAN WG4 Meeting#114, Athens, Greece, 17th – 21st February, 2025
R4-2505105, WF on requirements for AI/ML air interface normative work, 3GPP TSG-RAN WG4 Meeting#114bis, Wuhan, Hubei, China, 7th – 11th April, 2025
R4-2505106, Ad hoc minutes on AI/ML air interface, 3GPP TSG-RAN WG4 Meeting#114bis, Wuhan, Hubei, China, 7th – 11th April, 2025
R2-2501702, Report of 3GPP TSG RAN WG2 meeting #129, Athens, Greece
R2-250xxxx, Report of 3GPP TSG RAN WG2 meeting #129bis, Wuhan, China
R2-2407848, LS on applicable functionality reporting for beam management UE-sided model, 3GPP TSG RAN WG2#127, Maastricht, Netherlands, Aug 19th – 23rd, 2024
R1-2410898, Reply LS on applicable functionality reporting for beam management UE-sided model, 3GPP TSG RAN WG1 #119, Orlando, US, November 18th – 22nd, 2024

## Slide 24: Thank you !