## Slide 1: Handling of test frequency tables containing too many BW combinations.
R5-252586
3GPP TSG-RAN5 Meeting #107
Malta, May 19 – 23 2025

## Slide 2: Introduction
- Since there are many issues to solve to be able to include a python tool to the standard, there is a new/updated proposal for way forward regarding handling too large word tables in 38.508-1. This discussion paper will keep the former working assumption, to add python code to the standard, as an option. The differences in the two presented options have not been very clear in earlier discussion papers related to this topic.
- This discussion paper will focus on how to handle missing test frequencies for CA combinations with too many BW combinations. Additional functionality of the python tool, like creating CRs for smaller test frequency tables will not be addressed in this paper.

## Slide 3: Proposal 1
In case of too many BW combinations for a specific CA combination, a JSON file containing all possible BW combinations will be added too the standard and stored in the forge server.
Proposal 1A:
  A reference to JSON table will be provided in 38.508-1. No BW combinations to be added in word table.
Proposal 1B:
  A limited number of BW combinations to be added in in 38.508-, word table and a reference to JSON table will be provided.
In case of few number of BW combinations for a new CA combination, a word table will be added in 38.508-1 only, as normal.

## Slide 4: Pros and cons Proposal 1
Pros:
  More straight forward process to review CRs containing test frequencies for new CA configurations with many BW combinations. There will be a need to define a process for contribute and review a JSON file, but the process will be less complicated compared to contributing to and reviewing a python tool.
  Contributions can be generated using any tool.
Cons:
  Most likely there will be a need for development of a tool to extract and present needed BW combination from the JSON file. Possibly this can be done internally within companies.
  Over time, number of possible BW combinations for a CA combination might be so large that size of JSON might be difficult to handle, even in GIT server.
  If common python tool not part of the standard, availability/quality/functionality of tool not secured (as present status).

## Slide 5: Way forward, proposal 1
Definition of JSON format for a table like Table 4.3.1.1.5.77.1-3: “NR Intra-Band non-contiguous CA configuration CA_n77(2A) with UL CA (PCC=CC1 and SCC=CC2), SCS 15kHz”. See draft in attachment of this CR. Note that the draft only includes one BW configuration. The draft is not in a state to be reviewed in a detailed way. However, feedback is welcome!
Update tool to produce output according to JSON format definition.
Create GIT repo for RAN5 tables.
Define CR process for adding JSON tables into standard/GitLab.
Sort out legal matters (copyright, etc) on how to handle the python tool.
  Maybe also sort out if/how to facilitate contributions from any company.
Introduce tables 4.3.1.1.5.77.1-3, 4.3.1.1.5.77.1-4, 4.3.1.1.5.78.1-3, 4.3.1.1.5.78.1-4 to the standard/GitLab, including all BW combinations. And include references to the server in required tables, in 38.508-1.

## Slide 6: Proposal 2
In case of too many BW combinations for a specific CA combination, a python tool included in the standard is to be used for test frequency calculations.
Proposal 1A:
  A reference to a tool will be provided in 38.508-1. No BW combinations to be added in word table.
Proposal 1B:
  A limited number of BW combinations to be added in in 38.508-1 word table and a reference to tool will be provided.
In case of few number of BW combinations for a new CA combination, a word table will be added in 38.508-1 only, as normal.

## Slide 7: Pros and cons Proposal 2
Pros:
  Presentation of needed test frequencies will be part of the tool.
  No risk of problems in the future with too large JSON files.
  Availability/quality/functionality of common python tool will be better compared to option 1.
Cons:
  There will be a need to define a process for contribute and review a python tool. This will be complex since this is not done before.
  Big effort is needed to maintain availability/quality/functionality of a tool that is part of the standard.

## Slide 8: Way forward, proposal 2
Define 3GPP/ETSI Copyright for a 3GPP tool.
Define CR process for updating/contribute to a python tool in GitLab.
Create GIT repo for python tool.
Introduce all BW combinations for tables 4.3.1.1.5.77.1-3, 4.3.1.1.5.77.1-4, 4.3.1.1.5.78.1-3, 4.3.1.1.5.78.1-4 to the standard, by including reference to tool in required tables in 38.508-1.