## Slide 1: Discussion on how to reduce the measurement complexity of Out-of-Band Blocking in RAN5
Huawei, HiSilicon
3GPP TSG-RAN5 Meeting #107 R5-252669
St Julian’s, Malta, May 19-23, 2025

## Slide 2: Out-of-band blocking
This discussion paper is focused on how to reduce the measurement complexity of Out-of-Band Blocking into RAN5.
Minimum requirements in RAN4(38.101-1)
Table 7.6.3-2 Out of-band blocking for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
Table 7.6.3-4 Out of-band blocking for NR bands with FDL_low ≥ 3300 MHz and FDL_low ≥ 3300MHz
NR band | Parameter | Unit | Range 1 | Range 2 | Range 3
n1, n2, n3, n5, n7, n8, n12, n13, n14, n20, n24, n25, n26, n28, n30, n31, n34, n38, n39, n40, n41, n485, n50, n51, n538, n54, n65, n66, n70, n71, n72, n74, n85, n91, n92, n93, n94, n100, n101, n105, n106 | Pinterferer | dBm | -44 | -30 | -15
 | Finterferer (CW) | MHz | -60 < f – FDL_low < -15 or 15 < f – FDL_high < 60 | -85 < f – FDL_low ≤ -60 or 60 ≤ f – FDL_high < 85 | 1 ≤ f ≤ FDL_low – 85 or FDL_high + 85 ≤ f ≤ 12750
NOTE 1: … |  |  |  |  | 
NR band | Parameter | Unit | Range1 | Range 2 | Range 3
n77, n78 (NOTE 3) | Pinterferer | dBm | -44 | -30 | -15
 | Finterferer (CW) | MHz | -60 < f – FDL_low ≤ -3*BWChannel or 3*BWChannel ≤ f – FDL_high < 60 | -200 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 200 | 1 ≤ f ≤ FDL_low – MAX(200,3*BWChannel) or FDL_high + MAX(200,3*BWChannel) ≤ f ≤ 12750
n79 (NOTE 4) | Finterferer (CW) | MHz | N/A | -150 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 150 | 1 ≤ f ≤ FDL_low – MAX(150,3*BWChannel) or FDL_high+ MAX(150,3*BWChannel) ≤ f ≤ 12750
n104 (NOTE 5) | Finterferer (CW) | MHz | N/A | -150 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 150 | 1 ≤ f ≤ FDL_low – MAX(150,3*BWChannel) or FDL_high + MAX(150,3*BWChannel) ≤ f ≤ 12750
NOTE 1: … |  |  |  |  | 

## Slide 3
Test procedure in RAN5(38.521-1):
Out-of-band blocking
  The frequency step size is MHz.
  The frequency range of interfering signal is from 1 MHz to 12750 MHz.
  Two test frequencies and three CBWs need to be executed.
Observation 1:
  With current test procedure, the number of interferer frequencies to be measured is large, so that the time costing is high in the Out-of-Band Blocking measurements. More specifically, the number of interferer frequencies for frequencies Band n3 is 10200, the test duration is about 10 hours.
Table 7.6.3.4.1-1: Test Configuration Table
Default Conditions |  |  |  |  | 
Test Environment as specified in TS 38.508-1 [5] subclause 4.1 |  |  | Normal |  | 
Test Frequencies as specified in TS 38.508-1 [5] subclause 4.3.1 |  |  | One frequency chosen arbitrarily from low or high range |  | 
Test Channel Bandwidths as specified in TS 38.508-1 [5] subclause 4.3.1 |  |  | Lowest, Mid, Highest Lowest UL / Lowest DL, Lowest UL / Highest DL (NOTE 3) |  | 
Test SCS as specified in TS 38.508-1 [5] subclause 4.3.1 |  |  | Lowest |  | 
Test Parameters |  |  |  |  | 
 | Downlink Configuration |  |  | Uplink Configuration | 
Test ID | Mod'n | RB allocation |  | Mod'n | RB allocation
1 | CP-OFDM QPSK | NOTE 1 |  | DFT-s-OFDM QPSK | NOTE 1
NOTE 1: … |  |  |  |  | 
7.6.3.4.2 Test Procedure
1.SS transmits PDSCH via PDCCH DCI format 1_1 for C_RNTI to transmit the DL RMC according to Table 7.6.3.4.1-1. The SS sends downlink MAC padding bits on the DL RMC.
2.SS sends uplink scheduling information for each UL HARQ process via PDCCH DCI format 0_1 for C_RNTI to schedule the UL RMC according to Table 7.6.3.4.1-1. Since the UE has no payload data to send, the UE transmits uplink MAC padding bits on the UL RMC.
3.Set the parameters of the CW signal generator for an interfering signal below the wanted signal according to Table 7.6.3.5-2 or 7.6.3.5-4. The frequency step size is MHz.
4.Set …
…
7.Repeat steps from 3 to 6, using an interfering signal above the wanted signal at step 3.

## Slide 4: Impact analysis of band filter for Out-of-band blocking test
Fig.1 RF receiver Schematic diagram
Fig.2 signal variation diagram at Band Filter
Fig.1 is the RF Chain of a receiver.
Wanted signals and interfering signals are received by the receiver antenna and out-of-band interference is suppressed by the band filter as shown in Fig.2.
Wanted signals and interfering signals are amplified in the LNA as shown in Fig.3. It's worth noting that a high-power interference signal will saturate the LNA and distort wanted signal.
Fig.3 signal variation diagram at LNA
Observation 2:
  The closer the interfering signal is to the passband of the filter, the greater the impact on the wanted signal.
Proposal 1:
  The interferer frequencies near the passband of Band Filter should be tested to check the characteristics of band filter and LNA, such as FDL_low – [100MHz] to FDL_High + [100MHz].

## Slide 5: Impact analysis of non-linearity of Rx Chain for Out-of-band blocking
The non-linearity of Rx Chain will cause intermodulation products and harmonic products of input wanted signal and interferer signal.
If the intermodulation products caused by amplifiers such as LNA, VGA, and mixer fall into the bandwidth of wanted carrier, the RF performance will be degraded.
  i.e.:
At the mixer, when the interferer is mixed with the harmonic products generated by LO, and the mixed signal falls in the baseband, the RF performance will be degraded.
  i.e.:
There might be other intermodulation/harmonic products caused by the non-linearity of Rx chain, but the impact could be neglected comparing with above bullet 3 and 4.
Fig.1 RF receiver Schematic diagram
Fig.4 intermodulation products diagram from Amplifier
Fig.5 odd harmonic products diagram from Mixer
Observation 3:
  The non-linearity of Rx chain will have impact on the RF performance when the frequencies of wanted signal and interferer satisfies certain restriction.

## Slide 6: Intermodulation and harmonic products of interfering signal and wanted signal
Intermodulation :
  Input signal: .
  Output signal:
  the device has generated multiple frequencies that were not present in the input signal. By developing (Ui)3, it will generate products with frequencies such as 3ω1, 3ω2, 2ω1 + ω2, 2ω1 – ω2, ω1 + 2ω2, and 2ω2 – ω1. The mixtures between the original frequencies, 2ω1 + ω2, 2ω1 – ω2, and 2ω2 – ω1, are also called third-order intermodulation products (IM3). They fall in the same bands as the wanted signal bands and thus cause unrecoverable jamming and interferences. The same process can be applied to the term (x1 + x2)n. Hopefully, for practical devices the higher-order terms vanish rapidly and can be neglected—this is usually true above IM7 and even sometimes with IM5.
Observation 4:
  The higher the order of the intermodulation and harmonic products of the receivers, the smaller the impact on signals. For practical devices the higher-order terms vanish rapidly and can be neglected—this is usually true above IM7 and even sometimes with IM5.
  Proposal 2:
  Execute the test when the IM3/IM5 of wanted signal and interferer or the mixer product of interferer and 3rd /5th harmonic products of the wanted signal have impacts on the RF performance, i.e.,
  IM3/IM5 of wanted signal and interfering signal falls into [,
  , , and fall into [,

## Slide 7: Conclusion
Observation 1:
  With current test procedure, the number of interferer frequencies to be measured is large, so that the time costing is high in the Out-of-Band Blocking measurements. More specifically, the number of interferer frequencies for frequencies Band n3 is 10200, the test duration is about 10 hours.
Observation 2:
  The closer the interfering signal is to the passband of the filter, the greater the impact on the wanted signal.
Observation 3:
  The non-linearity of Rx chain will have impact on the RF performance when the frequencies of wanted signal and interferer satisfies certain restriction.
Observation 4:
  The higher the order of the intermodulation and harmonic products of the receivers, the smaller the impact on signals. For practical devices the higher-order terms vanish rapidly and can be neglected—this is usually true above IM7 and even sometimes with IM5.
Proposal 1:
  The interferer frequencies near the passband of Band Filter should be tested to check the characteristics of band filter and LNA, such as FDL_low – [100MHz] to FDL_High + [100MHz].
  Proposal 2:
  Execute the test when the IM3/IM5 of wanted signal and interferer or the mixer product of interferer and 3rd /5th harmonic products of the wanted signal have impacts on the RF performance, i.e.,
  IM3/IM5 of wanted signal and interfering signal falls into [,
  , , and fall into [,

## Slide 8: The test requirements of Out-of-Band Blocking
Modification Ideas for CR (38.521-1):
Table 7.6.3-2 Out of-band blocking for NR bands with FDL_high < 2700 MHz and FUL_high < 2700 MHz
Table 7.6.3-4 Out of-band blocking for NR bands with FDL_low ≥ 3300 MHz and FDL_low ≥ 3300MHz
NR band | Parameter | Unit | Range 1 | Range 2 | Range 3
n1, n2, n3, n5, n7, n8, n12, n13, n14, n20, n24, n25, n26, n28, n30, n31, n34, n38, n39, n40, n41, n485, n50, n51, n538, n54, n65, n66, n70, n71, n72, n74, n85, n91, n92, n93, n94, n100, n101, n105, n106 | Pinterferer | dBm | -44 | -30 | -15
 | Finterferer (CW) | MHz | -60 < f – FDL_low < -15 or 15 < f – FDL_high < 60 | -85 < f – FDL_low ≤ -60 or 60 ≤ f – FDL_high < 85 | 1≤ f ≤ FDL_low – 85 or FDL_high + 85 ≤ f ≤ 12750
NOTE 1: ... NOTE 10: For frequency range 1≤ f < FDL_low – [100] and FDL_high + [100] < f ≤ 12750, execute the test when the IM3/IM5 products of wanted signal and interfering signal fall into [fc – CHBW/2, fc + CHBW/2], or the mixer product of interferer and 1/3rd, 1/5th , 3rd, 5th harmonic of wanted signal fall into [-CHBW/2, CHBW/2] |  |  |  |  | 
NR band | Parameter | Unit | Range1 | Range 2 | Range 3
n77, n78 | Pinterferer | dBm | -44 | -30 | -15
 | Finterferer (CW) | MHz | -60 < f – FDL_low ≤ -3*BWChannel or 3*BWChannel ≤ f – FDL_high < 60 | -200 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 200 | 1≤ f ≤ FDL_low – MAX(200,3*BWChannel) or FDL_high + MAX(200,3*BWChannel) ≤ f ≤ 12750
n79 | Finterferer (CW) | MHz | N/A | -150 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 150 | 1≤ f ≤ FDL_low – MAX(150,3*BWChannel) or FDL_high+ MAX(150,3*BWChannel) ≤ f ≤12750
n104 | Finterferer (CW) | MHz | N/A | -150 < f – FDL_low ≤ -MAX(60,3*BWChannel) or MAX(60,3*BWChannel) ≤ f – FDL_high < 150 | 1≤ f ≤ FDL_low – MAX(150,3*BWChannel) or FDL_high + MAX(150,3*BWChannel) ≤ f ≤ 12750
NOTE 1: ... NOTE 10: For frequency range 1≤ f < FDL_low – [100] and FDL_high + [100] < f ≤ 12750, execute the test when the IM3/IM5 products of wanted signal and interfering signal fall into [fc – CHBW/2, fc + CHBW/2], or the mixer product of interferer and 1/3rd, 1/5th , 3rd, 5th harmonic of wanted signal fall into [-CHBW/2, CHBW/2] |  |  |  |  | 

## Slide 9: THANK YOU