## Slide 1: Handling of test frequency tables containing too many BW combinations.
Document for discussion and endorsement.
Agenda Item:5.3.3.10
R5-254694
3GPP TSG-RAN5 Meeting #108
Bangalore, Aug 25 – 29 2025

## Slide 2: Introduction
This discussion paper are proposing a JSON format to represent a table with test frequencies for intra band noncontiguous CA combination, including UL CA.
The attached “jsonSchema” file is defining what is allowed and not allowed to add in the table. Among other tings, the type of the values can be restricted to “int”, “number”, “string” etc. The jsonSchema file will be a valuable tool to automatically review the table.
The .JSON file (attached in “dummy CR”) is representing all BW combinations for CA_n77(2A), including UL CA (for SCS = 30). Table 4.3.1.1.5.77.1-4 is already present in 38.508-1, however only containing a subset of the BW combinations.
The schema file are prepared to represent the Notes in table 4.3.1.1.5.77.1-4 however, at this stage, all Notes are not reflected properly in the JSON representation of the table.

## Slide 3: Proposal 1
Proposal 1:
In case of too many BW combinations for a specific CA combination, a JSON file containing all possible BW combinations will be added to the standard and stored in the forge server. A subset of the BW combinations will be added to table in 38.508-1 and a reference to the JSON table will be provided in the table (see attached dummy CR).
This proposal is based on proposal 1B in R5-253615, according to agreement in RAN5#107.
Note that to be able to approve the first table in .JSON format, there is a need to also approve the “jsonSchema” that is generic for all tables representing that type of table. In this case a table for non contiguous CA including, UL CA.

## Slide 4: Way forward, proposal 1
Create GIT repo in Forge for RAN5 tables.
Define/Agree on naming convention for .JSON files.
Define/Agree CR process for adding JSON tables into standard/Forge server.
Sort out and define how non 3GPP members will get access to the .JSON files stored in the Forge server.
Introduce tables 4.3.1.1.5.77.1-3, 4.3.1.1.5.77.1-4, 4.3.1.1.5.78.1-3, 4.3.1.1.5.78.1-4 to the standard/Forge server, including all BW combinations. And include references to the Forge server in required tables, in 38.508-1 (see dummy CR in .zip file).
Longterm: Define/Implement a (WEB ?) tool that will facilitate extraction of .JSON table information for non ETSI members? (related to bullet 4).

## Slide 5: References
R5-253615 (RAN5#107): Handling of test frequency tables containing too many BW combinations.
R5-254695 (RAN5#108): Test frequency calculation tool, updates and way forward.