## Slide 1: Discussion on test frequency simplification for inter-band CA and DC band combinations
ZTE Corporation, Huawei
3GPP TSG-RAN5 Meeting #109 R5-256701
Dallas, US, November 17 – 21, 2025

## Slide 2: Overview on test frequencies for inter-band CA/DC band combinations
In TS 38.508-1, test frequencies are specified for bands and band combinations.
For inter-band CA configurations, the test frequencies are specified by NR CA downlink / uplink configuration component bands / band combinations and applicable for protocol testing. The single component band and intra-band CA test frequencies can be further referred to the related test frequency tables in the spec. For example, for three bands inter-band CA_n1A-n3A-n78A, the test frequencies can be shown as below, in which the reference test frequencies for n1, n3 and n78 are further specified in clause 4.3.1.1.1.1/3/78 respectively. However, it can also be seen that in Table 4.3.1.1.2.2-1 most cases have similar test frequencies for CA_nXA-nYA-nZA with similar downlink and uplink configurations.
Observation 1 In TS 38.508-1, test frequencies for inter-band NR CA band combinations are specified by NR CA downlink / uplink configuration component bands / band combinations and applicable for protocol testing.
Observation 2 All “Applicable for protocol testing” are “no” for inter-band NR CA/DC with three or more bands, “no” for EN-DC within FR1 with four or more bands, “no” for EN-DC including FR2 with three or more bands.

## Slide 3: Overview on test frequencies for inter-band CA/DC band combinations
In TS 38.508-1, many typos are found in the test frequency tables for inter-band CA due to the redundant contents.
CA_n8A-n78(2A)
(TS 38.508-1) (TS 38.521-1)
CA_n29A-n66B
(TS 38.508-1) (TS 38.521-1)
Observation 3 In TS 38.508-1, there are many typos in the test frequency tables due to the redundant contents are collected in different specs and different tables.

## Slide 4: Overview on test frequencies for inter-band CA/DC band combinations
However, it is also noted that the test frequency tables for inter-band CA/DC band combinations are also essential in signalling as they specify which combinations are applicable and are used for the TTCN implementation. There are some concerns for signalling test if the explicit CA, NR-DC and EN-DC combinations are lost. To simplify the test frequency tables, it is suggested to
Keep all combinations with the “Applicable for protocol testing” = “Yes”.
For configurations with “Applicable for protocol testing” having values “No”, the general rule for deciding test frequencies apply if no explicit value defined. The inter-band CA configurations are represented by symbolic CA configurations using nX and nY as the different bands in the CA Configuration E.g. CA_nXA-nY(2A) could be representing the configuration CA_n1A-n78(2A) by interpreting of nX=n1, nY=n78.
The general rules for deciding test frequencies applied to
  Inter-band NR CA within FR1 for ≥ 3 bands.
  Inter-band EN-DC within FR1 for ≥ 4 bands.
  Inter-band EN-DC including FR2 for ≥ 3 bands.
Observation 4 Test frequency tables for inter-band CA/DC band combinations are also essential in signalling as they specify which combinations are applicable and are used for the TTCN implementation. The general rules for deciding test frequencies applied to different cases for NR CA and EN-DC.

## Slide 5: Simplification on inter-band CA/DC test frequency tables
Proposal 1 It is suggested to simplify the inter-band CA test frequency table with the general rules for inter-band NR CA within FR1 for ≥ 3 bands.
The general rule for deciding test frequencies for inter-band CA configurations are represented by symbolic CA configurations using nX, nY and nZ as the different bands in the CA Configuration. E.g. CA_nXA-nYA-nZA could be representing the configuraion CA_n1A-n3A-n78A by interpreting of nX=n1, nY=n3 and nZ=n78.
The specified NR inter-band CA configurations can be found in 38.521-1 clauses 5.5A.3.
Remove all the configurations if the general rule applies.
Any CA configurations not applying the general rule could be listed separately in the table.
General rule Example

## Slide 6: Example for inter-band NR CA/DC test frequency tables
General rules for test frequencies
When general rule does not apply. Keep it in the table.
When general rule applies, remove configurations
Refer to 38.521-1

## Slide 7: Benefits from the test frequency simplification approach
Observation 5 At least the following benefits can be seen from the test frequency simplification approach.
Special configurations such as with different Pcell configured configurations will be highlighted.
No need to specify the test frequencies for the future ≥ 3 bands NR CA configuration explicitly if the general rules have already been defined.
No more errors or redundant info for the specified configurations since it refers to TS 38.521-1.
The size of the table will be reduced.
Proposal 2 It is suggested to simplify the inter-band EN-DC test frequency table with the similar general rules as CA configurations.
  Inter-band EN-DC within FR1 for ≥ 4 bands.
  Inter-band EN-DC including FR2 for ≥ 3 bands.

## Slide 8: Thank you!