## Slide 1: NR FR1 TT Way Forward update
3GPP TSG-RAN WG5 Meeting #81
Spokane, USA, 12th – 16th November 2018
R5-186887r1
Telecom Italia, Orange, AT&T, CMCC

## Slide 2: Background
At RAN5#79 the Maximum Test System Uncertainty for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952
At RAN5#79 a Way Forward on FR1 TTs for NR FR1 TRx tests in TS 38.521-1 has been agreed in R5-183952 (Except the FFS items)
At RAN5#80 New FR1 MU values introduced in R5-184484 for the following TCs: 6.3.4.2, 6.3.4.3, 6.3.4.4, 6.4.2.1, 6.4.2.2, 6.4.2.3, 6.4.2.4. New TT values agreed based on the WF assumption in R5-185564
At RAN5#80 RAN5 also agreed to maintain the document until the TT for FR1 and FR2 are finalized
At RAN5 5G-AH#3 a WF for FR1 NSA in TS 38.521-3 has been agreed in R5-185657
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344

## Slide 3: Agreed FR1 Way Forward: TT < MU
At RAN5#79 TT WF agreed in R5-183952
WF: Except the FFS Items, the proposed FR1 TT Values are included in the spreadsheet file, based on the following assumption:
  The SA FR1 TT values should not exceed the value adopted in pure LTE (TS 36.521-1 BW ≤ 20 MHz f ≤ 4.2 GHz). It is assumed that the amount of uncertainty exceeding the E-UTRAN shall not be considered.

## Slide 4: Agreed FR1 NSA WF TS 38.521-3
At 5G-AH#3 RAN5 agreed NSA MU in R5-185641
At 5G-AH#3 RAN5 agreed WF in R5-185657 for TS 38.521-3 FR1 EN-DC as follow:
  In case TTLTE, TTSA = 0, TTNSA to be defined as zero.
  In case MUNSA = MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.
  In case MUNSA > MUSA, same FR1 WF to be applied to corresponding FR1 TCs in TS 38.521-3.

## Slide 5: Attached Spreadsheets update
TS 38.521-1 SA FR1 TT
  Introduced SUL and UL-MIMO Test cases agreed at RAN5 5G-AH#3 in Jaipur.
TS 38.521-3 NSA FR1 TT
  Replaced reference to TS 38.521-1 with actual TT numbers