## Slide 1: R6-160138: Outcome of TSG RAN WG6 #1
Juergen Hofmann
Nokia

## Slide 2: Document allocation
Incoming: 54
Total: 136
Chart: 
| eDRX | EC-GSM-IoT | CSPS_COORD_GERAN | ePOS_GERAN | DECOR-GERAN | DL MIMO | Other Rel-14 topics
 | 3 | 30 | 1 | 7 | 2 | 5 | 3

## Slide 3: 3 General Matters
Meeting Organization
  No need for subgroups identified
Submission Deadline
  will be on Friday in second week prior to meeting, 21.00 CET/CEST
  applies for all contributions.
Reflectors
  Need for the TSG_RAN_WG6_DRAFTS reflector will be checked after few meetings.

## Slide 4: 4 Liaisons / reports from other groups / meetings
R6-160055 LS on CS/PS coordination in GERAN Shared Networks (RAN3 to SA2, cc RAN6)
  noted (Cc to RAN6).
R6-160064 LS on enhancing legacy GSM security (SA3 to RAN6, CT1, cc CT6)
  RAN6 to review one CR. Response sent at RAN6#1 (see item 8).

## Slide 5: 5.1 eDRX_GSM
CR 44.018 Clarification of CCCH_GROUP Determination agreed in R6-160104
Set of CRs agreed to modify PEO One Phase Access Request using TS 4:
CR 44.018 Clarification of PEO Code Point Usage in R6-160107
CR 44.060 Clarification of PEO Code Point Usage in R6-160108
CR 45.001 Clarification of PEO Code Point Usage in R6-160122
CR 45.002 Clarification of PEO Code Point Usage in R6-160106

## Slide 6: 5.2.1 EC-GSM-IoT, Radio aspects (1/2)
Miscellaneous corrections to EC-GSM-IoT agreed to 43.022 in R6-160065
Corrections to EC-GSM-IoT agreed to 45.001 in R6-160116
Miscellaneous corrections to EC-GSM-IoT agreed to 45.002 in in R6-160067
Corrections to EC-GSM-IoT agreed to 45.002 in R6-160130
Miscellaneous corrections to EC-GSM-IoT agreed to 45.003 in in R6-160099
Miscellaneous corrections to EC-GSM-IoT agreed to 45.008 in in R6-160110
Corrections to EC-GSM-IoT agreed to 45.008 in R6-160114
Corrections to EC-GSM-IoT agreed to 45.010 in R6-160118

## Slide 7: 5.2.1 EC-GSM-IoT, Radio aspects (2/2)
Corrections to EC-GSM-IoT agreed to 45.004 in R6-160117
Miscellaneous corrections to EC-GSM-IoT agreed to 45.005 in R6-160134
Corrections to EC-GSM-IoT agreed to 45.005 in R6-160135

## Slide 8: 5.2.2 EC-GSM-IoT, Perf. aspects (1/1)
MS Rx performance requirements in 45.005 agreed in R6-160082
BTS sensitivity performance in 45.005 agreed in R6-160111
BTS interference performance in 45.005 agreed in R6-160112
BTS sensitivity performance for OL-CDMA in 45.005 agreed in R6-160136
Incremental redundancy requirement for EC-GSM-IoT, R6-160013. CR to 45.005 agreed in R6-160093
EC-GSM-IoT, Normalized Coherency Error Requirement for MS, R6-160027. CR to 45.005 agreed in R6-160094
Corrections to EC-GSM-IoT agreed to 51.021 in R6-160098

## Slide 9: 5.2.3 EC-GSM-IoT, Prot. aspects (1/2)
Misc EC-GSM IoT Changes agreed to 44.014 in R6-160056
  Related to test of FUA with SS
Misc EC-GSM IoT Changes agreed to 44.018 in in R6-160100
Misc EC-GSM IoT Changes agreed to 44.060 in R6-160058
Misc EC-GSM IoT Changes agreed to 48.018 in R6-160059
Miscellaneous Corrections to 44.018 in R6-160119
Miscellaneous Corrections to 44.060 in R6-160121
Miscellaneous Corrections to 48.018 in R6-160132

## Slide 10: 5.2.3 EC-GSM-IoT, Prot. aspects (2/2)
Transmission Opportunities indicated in FUA R6-160040
  No capacity issue for traffic channel identified, although not all blocks for higher CCs can be scheduled.
  CR in R6-160041 not agreed.

## Slide 11: 5.3 CSPS_Coord_GERAN (1/1)
Correction CR to 48.018 agreed in R6-160007

## Slide 12: 5.4 Any other documents related to Rel-13 or earlier features
No contributions.

## Slide 13: 6.1 ePOS_GERAN (1/3)
Multilateration Signaling for GERAN (R6-160018,rev R6-160124)
  Signalling procedures for TA multilateration
  4 WA’s agreed on PS LCS capability, RRLP, RRLP TOM, applicability to PS domain
  Energy consumption analysis presented in R6-160083, WA‘s on energy consumption agreed
  Assumptions for position accuracy simulation of TA multilateration, R6-160011 (rev R6-160087): all WA‘s agreed
  Simulation Results for position accuracy simulation of TA multilateration, R6-160012

## Slide 14: 6.1 ePOS_GERAN (2/3)
Radio Interface Enhancements for TA based multilateration (R6-160034,rev R6-160085)
  Investigates improvements of radio interface signalling for TA multilateration
  Proposal to use a code point in the EC-NumberOfBlocks to differentiate EC and PEO access attempt not agreed.
Energy efficient hybrid TA/OTD multilateration for neighbour cells in extended coverage (R6-160035)
  Investigates power consumption improvement by combining OTD and TA multilateration
Energy Consumption Analysis of Radio Interface Procedures for Positioning Enhancements (R6-160036, rev R6-160086)
  Energy consumption analysis for both investigated concepts

## Slide 15: 6.1 ePOS_GERAN (3/3)
Positioning enhancements for GERAN - Workplan/Agreements (R6-160131) was agreed:
  Work plan for ePOS_GERAN
  Agreements and working assumptions collected from other Tdocs
  Initial study phase conclusions (reflecting the status after the 3 month study phase)

## Slide 16: 6.2 DECOR_GERAN (1/1)
DÉCOR Way Forward (R6-160017, rev R6-160089) was agreed:
  Rerouting procedure based on new Information elements (UE Usage Type, SGSN Group Identity, Additional P-TMSI)
  Inclusion into GERAN Rel-14 specifications.
  Accompanying CR 48.018 Introduction of Dedicated Core Networks in GERAN agreed in R6-160123.
  With the agreed change the feature is complete.

## Slide 17: 6.3 Small technical enhancements and improvements (work item TEI)
No contributions.

## Slide 18: 6.4 Downlink MIMO for GERAN (study item DOMIMO)
One discussion paper and 4 pCRs were presented and agreed:
  pCR 45.871 Downlink MIMO – Mode and Link Adaptation, R6-160042
  pCR 45.871 Downlink MIMO – Signalling, R6-160043
  Compatibility Analysis of Downlink MIMO for GERAN, R6-160044
  pCR 45.871 Downlink MIMO – Compatibility Analysis, R6-160045
  pCR 45.871 Downlink MIMO – Conclusion, R6-160046
The agreed pCRs are included to TR 45.871 v1.1.0 in R6-160091,
which will be presented to RAN#73 for approval for SI completion.

## Slide 19: 6.5 Any other Rel-14 documents
Alternative mappings for EC-GSM-IoT higher coverage classes, R6-160031
  Investigates the usage of alternative mappings for CC2 to CC4 with lesser PDCH resources than in Rel-13
EC-GSM-IoT New Channel Formats for Short Packets with NIDD CN, R6-160032
  Investigates usage of shorter radio blocks to align with shorter payloads due to Non IP data delivery from CN.
WID on Radio Interface Enhancements for EC-GSM-IoT (R6-160033, rev R6-160092) modified to focus on
  Introduction of alternative mappings for Coverage Classes 2 to 4
  MCL improvement on uplink for devices with 23 dBm output power.
  Further offline discussion needed.

## Slide 20: 7 Any other technical work
No contributions.

## Slide 21: 9 Work Plan
Presented in R6-160137 and agreed.

## Slide 22: 8 Letters to other groups
“Response LS on Legacy Security Issues” agreed to be sent in R6-160125 to SA3, CT1, cc CT6
  RAN6 provides feedback on security issues in the CS domain as requested by SA3.

## Slide 23: 10 Future meetings
Meetings
  RAN6#2, 14-18 November 2016, Reno, USA
  RAN6#3, 13-17 February 2017, Athens, Greece

## Slide 24: Annex

## Slide 25
Revised Draft Schedule for 3GPP RAN WG6#1 (Room R2)
After 4th Day