## Slide 1: Moderator's summary AI 8.2.1.1 “Deployment Scenarios”
Axel Klatt
Deutsche Telekom AG / Co-Rapporteur RAN P SI
3GPP TSG RAN #109
Beijing, China, Sept. 15th – 18th, 2025
RP-252809

## Slide 2: Summary of inputs
Summary/conclusions:
27 contributions uploaded until deadline Sept. 3rd
  2 misplaced and hence not handled; moved to appropriate agenda items
2 contributions uploaded after deadline Sept. 3rd
  1 submission misplaced and hence not handled; moved to appropriate agenda item
Many New Scenario proposals and intensive – often contradicting - updates of existing scenario parameters (mainly on bands, antenna configurations, user distribution)
Some contributions discussed generic aspects [RP-252180, RP-252312]
  Further discussion needed in plenary first

## Slide 3: Why are we creating the deployment scenarios ?
Summary/conclusions:
There seems to be still different understanding of chapter 4 of TR 38.914
Define scenarios to:
  analyse that the air interface design (aka “6GR”) to be developed during the 6G Radio Study fullfills the requirements of IMT-2030 (for the ITU process)
  analyse technical benefits of the “6GR” in realistic/practical deployment scenarios and allow comparsison to 5G-Advanced (with baseline to be agreed, e.g. NGMN RPAF, 3GPP internal, …)
  document interesting deployment scenarios which might or might not be realised
Moderator Proposal: RAN should endorse that the focus is only on 1 and 2

## Slide 4: Do we add new deployment scenarios ?
Summary/conclusions:
The following new deployment scenarios were proposed:
  Urban Grid (Subchapter existed -> details proposed) [RP-252001, RP-252218, RP-252127, RP-252177, RP-252470]
  Highway (Subchapter existed -> details proposed) [RP-252218, RP-252127, RP-252177, RP-252470]
  High Speed (train) (Subchapter existed -> details proposed) [RP-252121]
  Single cell with large coverage [RP-252118]
  Indoor Factory (InF) [RP-252118, RP-252127, RP-252021, RP-252581]
  UAV [RP-252126]
  Multi-layer heterogeneous network with assisting node [RP-252021]
  Nearshore water [RP-252021]
Moderator Proposal: RAN should endorse that those 8 scenarios should be added and detailed. This work has lower priority than finalising the updates for the existing scenarios.

## Slide 5: Additional considerations for RAN?
Discussion from RP-252312:
Proposal 1: Streamline the deployment scenarios and/or prioritize deployment scenarios to facilitate working group discussions when possible.
Proposal 2: In TR 38.914, capture the following for each sub-scenario (e.g., Around 4 GHz + Around 7 GHz):
  the number of antenna elements at a TRP
  the number of TXRUs at a TRP
  the Tx power at a 4GHz/7GHz TXRU
In TR 38.914, capture network backhaul assumptions (e.g., ideal, non-ideal with 10 ms latency) and TRP synchronization assumptions such as timing/frequency/phase at least for some scenarios including dense macro and urban macro.
Moderator Proposal: Discussion/Decision needed where, how and for what we do the prioritisation needed -> but update of tables is independent at the moment

## Slide 6: To which level does RAN needs to detail parameters?
Discussion:
One company [RP-252118] proposed to define only the max. antenna configurations and let RAN WGs to decide the configuration for the evaluations
  BS up to 1024 antenna elements / BS up to 2048 antenna elements for 7 GHz [RP-252021, 2121]
      Note: The number may be lower for certain deployment scenarios and carrier frequencies.
  UE up to 8 antenna elements / UE up to 32 antenna elements@700 [RP-252126, RP-252581]
      Note: The number may be lower for certain deployment scenarios and carrier frequencies.
Moderator Proposal: Answer depends on the outcome of discussing the previous slide and is also related to the “device type discussion”

## Slide 7: Diverse views on antenna configurations
Summary/conclusions:
For BS and UE per band wide range of antenna assumptions have been proposed:
  For BS from 1T2R to up to 2048 antenna elements; often depending on the band and on deployment scenario
  For UE from 1T1R to up to 32 antenna elements; often depending on the band and device type
Moderator Proposal:
For BS antenna configuration RAN P shall decide the typical configuration per band and deployment scenario
For UE it is dependend on the device type discussion (see next slides)

## Slide 8: How do we handle different “Device Types”?
Summary/conclusions:
For 5G the corresponding TR for deployment scenarios has been developed concentrating on eMBB; IoT and automotive were treated as specific scenarios
Today we have suggestions to consider wider range of devices which specific characteristics in all deployment scenarios, as an illustrative example:
It is clear that all different types of devices will need to operate in all deployment scenarios of chapter 4 (except the “specific ones” like indoor hotspot, Indoor Factory and UAV ;-) )
Moderator Proposal: Adopt the style as proposed on the next slide
 | eMBB | IoT | FWA | Automotive
Antennas | 4 / 8 | 1 / 1 | 8 / 8 | 1 / 2
Tx Power | Normal | Low | High | High
Velocity | 3 .. [120] | 3 .. [120] | 0 | 30 … [250]

## Slide 9: UE: Adopt the style in the deployment tables
…
UE antenna elements
eMBB
FWA
IoT
Automotive
User distribution and UE speed
eMBB
FWA
IoT
Automotive
Moderator Proposal: RAN should decide if we add parameters per device type

## Slide 10: Network configuration for different assessements: Adopt the style in the deployment tables ?
…
BS antenna elements
ITU IMTS-2030 evaluation
3GPP internal performance evaluation (5G-A vs. 6G Radio)
UE antenna elements
ITU IMTS-2030 evaluation
3GPP internal performance evaluation (5G-A vs. 6G Radio)

## Slide 11: Sensing: Add Sensing block per scenario ?
…
BS antenna elements
ITU IMTS-2030 evaluation
3GPP internal performance evaluation (5G-A vs. 6G Radio)
Sensing Parameters
Parameter 1
Parameter 2
Parameter 3
…

## Slide 12: Suggested sensing parameters per deployment scenario [RP-252202]
Urban Macro for ISAC
Indoor hotspot for ISAC
Moderator Proposal: We add those parameters in a dedicated block of the tables per deployment scenario

## Slide 13: Moderator‘s consolidated changes for further discussion/alignment (sent as draft pCR)
Moderator Proposal: Use ONLY moderator’s draft “pCR” as starting point for further discussion/agreements

## Slide 14: Notes on the pCR

## Slide 15: List of contributions considered in this Agenda Item
Tdoc | Title | Source
RP-252323 | Deployment Scenarios for 6G Evaluations | AT&T
RP-252330 | NTN deployment scenarios | Sharp
RP-252220 | Discussion on 6G Deployment Scenarios | China Unicom
RP-252312 | Views on 6G Deployment Scenarios | Apple Inc.
RP-252340 | Deployment Scenarios for 6G | Google
RP-252232 | Urban Coverage for Massive Connection | FUTUREWEI
RP-252121 | Discussion on 6GR deployment scenarios for 38.914 | CMCC
RP-252123 | pCR for 38.914 on Deployment scenarios | Deutsche Telekom, Vodafone, Orange, Telecom Italia, Turkcell, Spark NZ, Odido, BT, Telefonica, KPN, Rakuten Mobile, CK Hutchison, Telenor
RP-252117 | Discussion on 6G Deployment Scenarios | Tejas Networks Limited, CEWiT, IIT MADRAS
RP-252118 | Discussion on 6G Deployment Scenarios | Tejas Networks Limited, CEWiT, IIT MADRAS
RP-252084 | Discussion on 6GR deployment scenarios for 38.914 | CMCC
RP-252126 | Consideration on 6G deployment scenarios | Huawei, HiSilicon
RP-252127 | Discussion on 6G ISAC deployment scenarios | Huawei, HiSilicon, CAICT, China Telcom, China Unicom, KT Corp., LG Uplus, SK Telecom
RP-252140 | Support indoor factory as one of 6G scenarios | CATT, CICTCI, China Telecom, China Unicom, ZTE
RP-252144 | Views on 6G NTN scenarios | CATT
RP-252165 | Discussion on 6G communication deployment scenarios | Xiaomi
RP-252168 | FWA evaluation scenarios | MediaTek Inc., T-Mobile USA
RP-252180 | Antenna Configurations for 6G Deployment Scenarios | Nokia
RP-252218 | Views on Urban grid and Highway scenarios | CATT, CICTCI
RP-252216 | Text proposal on Updates to Deployment scenarios | Qualcomm
RP-252208 | Views on 6G NTN Scenarios | CSCN, CATT
RP-252202 | Deployment scenarios for ISAC | Xiaomi
RP-252177 | Text proposal for TR 38.914 for deployment scenarios for Vehicular Use Cases | ROBERT BOSCH GmbH, Volkswagen AG, BMW AG, Toyota ITC, Continental Automotive, Fraunhofer IIS
RP-251935 | Text proposal for TR 38.914 for NTN deployment scenarios | THALES
RP-251944 | On deployment scenarios | Ericsson
RP-251955 | Requirements for 6G-6G Spectrum Aggregation | Samsung, Verizon
RP-251964 | Low-Cost 6G Base Station Options for Upper Mid-Band (6.425–7.125?GHz) | IITH and WiSig
RP-252001 | Discussion on 6G Deployment scenarios | vivo
RP-251993 | Views on 6G deployment scenarios | NTT DOCOMO, INC.
RP-252021 | General views on 6G deployment scenarios | ZTE Corporation, Sanechips
RP-251999 | Discussion on 6G deployment scenarios | Guangdong OPPO Mobile Telecom.
Not available at Sept. 3 deadline; Wrong Agenda Item
Double allocation
Double allocation
Wrong Agenda Item
Wrong Agenda Item
RP-252470 | Discussion on 6G deployment scenarios | LG Electronics
late