## Slide 1: Splitting FGI 3
Qualcomm, Ericsson, Nokia-Siemens Networks, ZTE, CATT
Nokia, Mediatek, LGE, ST-Ericsson, Renesas Technology Europe,
ATT, NTT DoCoMo, TeliaSonera, Deutsche Telekom, KDDI
3GPP TSG RAN Meeting #50 RP-101412
Istanbul, Turkey, December 7 - 10, 2010 Agenda Item 8.2.2

## Slide 2: Splitting FGI 3: way forward
FGI 3 currently is:
  Semi Persistent Scheduling
  TTI bundling
  5-bit RLC Sequence Number & 7-bit PDCP Sequence Number
In order to facilitate introduction of features related to voice over LTE, the following is proposed
  Allow independent indication of support of SPS and of TTI bundling, without having dependency of one with the other
  Make the shorter RLC/PDCP sequence number mandatory for voice over LTE devices

## Slide 3: Splitting FGI 3: the way forward in practice
TTI bundling | Move to FGI 28 (newly created) & have no dependency on any other bit
Semi Persistent Scheduling | Keep in FGI 3 & change meaning of FGI 3 removing dependency from TTI-b / FGI 28 or any other bit
5-bit RLC & 7-bit PDCP Sequence Number | Move to FGI 7 (already mandatory for voice over LTE devices)
What happens to FGI 3? | FGI 3 meaning is changed (but no backward compatibility issues are envisaged in the real world)
It is also proposed to
  Realize the previously described changes in Release 9