## Slide 1: Way Forward on supplemental downlink for TD-LTE in Rel.12
NTT DOCOMO, INC.
RP-140515
Revision of RP-140483
3GPP TSG-RAN#63
Fukuoka, Japan, 3-6 March 2014
Agenda: 14.1.1

## Slide 2: Introduction
The followings are proposed in this document
  Way forward on new WI on supplemental downlink for TD-LTE
  A technical analysis in terms of the co-existence with the existing UL-DL configurations

## Slide 3: Way Forward
Rel-12 CRs for a DL-only configuration for TDD are approved at RAN#64.
  The CRs are reviewed by RAN1/2 until RAN#64.

## Slide 4: Technical analysis on co-existence
Co-existence b/w UL/DL configs #2 and #5
  One of two UL SFs in config #2 is blocked by a DL SF in config #5
  Lost of one UL SF in config #2 results in 50% DL + 50% UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  50% DL/UL transmission resources are lost
Co-existence b/w UL/DL configs #5 and DL-only
  A UL SF is blocked by a DL SF in DL-only config
  Lost of one UL SF in config #5 results in 100% DL and UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  100% DL/UL transmission resources are lost
#2
#5
#5
#”7”
Both cases are not acceptable from operator’s point of view

## Slide 5: Technical analysis on co-existence
Co-existence b/w UL/DL configs #2 and #5
  One of two UL SFs in config #2 is blocked by a DL SF in config #5
  Lost of one UL SF in config #2 results in 50% DL + 50% UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  50% DL/UL transmission resources are lost
Co-existence b/w UL/DL configs #5 and DL-only
  A UL SF is blocked by a DL SF in DL-only config
  Lost of one UL SF in config #5 results in 100% DL and UL losses
    Since the UL SF is responsible for both UL data and DL HARQ-ACK
  100% DL/UL transmission resources are lost
#2
#5
#5
#”7”
In principle, it is not allowed to decrease someone’s assets coming from co-existence using different UL/DL configs, regardless of whether or not new DL-only configuration is introduced
Consensus b/w operators is essential for TDD co-existence cases
Negotiation among 7 configures makes no difference with that among 8 configurations

## Slide 6: Technical analysis on co-existence
If an operator has multiple carriers, a TDD band can be utilized as DL-only carrier even without DL-only configuration
If the operator wants to damage intentionally or accidentally to the neighboring operator, the operator can use UL/DL config #5 without UL transmission on the carrier
#5
#2
#”7”
#2
There is no fundamental difference b/w existing case and DL-only config

## Slide 7: Summary on co-existence aspect
A consensus on the configuration among associated operators is essential to make maximum use of TD-LTE system.
If the consensus was not reached, co-existence issues happen regardless of the configurations.
Otherwise, some guard band(s) is required, however, the advantage of TD-LTE system is lost.

## Slide 8: Regarding to the concerns raised
Co-existence and impact to stand-alone existed even in existing configurations, there is no new impact due to the introduction of new configuration. (To emphasize this problem is similar to say that TDD is not good…)
We should not always assume there is operator who wants to damage other operator. Actually in this case regulator will take action to guide that operator.
If in some country or region that regulation could not effectively solve this problem, we should not block the use of this configuration in other country and region since this is the requirement from majority of the operators.