## Slide 1: TDD support for NB-IoT in Rel-15
3GPP TSG RAN Meeting #74 RP-162161
Vienna, Austria, December 5-8, 2016
Agenda Item: 10.1.1
Source: Huawei, HiSilicon
Document for: Information

## Slide 2: Background
  Support of TDD in NB-IoT was considered in Rel-13 in RAN1 and RAN
  RAN1 #83
    Conclusion:
    - NB-IoT in Rel-13 supports at least the necessary forward compatibility to support TDD
    - FFS which TDD configurations are to be prioritized; companies are encouraged to check further until the next meeting
  RAN #70
    - Conclusion: REL-13: FDD only + forward compatibility for TDD
  TDD was also considered during Rel-14 WI approval, but not included due to availability of TU after accounting for other objectives
  Competing M2M radio technologies around the world are not limited to FDD

## Slide 3: Justification
  Half-duplex FDD NB-IoT addresses a wide range of the use cases and applications for cellular M2M thanks to the expedited Rel-13 work, and Rel-14 enhancements:
    Ultra-low cost, ≥52 000 devices/cell, ≥ 20 dB extra coverage than GPRS, ≤10 sec alarm latency
    Positioning
    SC-PTM multi-cast for firmware update and group messaging
    Peak rate increases supported by firmware or hardware upgrade
    Non-anchor carrier paging and RACH for offloading cell access traffic
  However, TDD spectrum also exists globally, including regulatory environments and operator markets where there is strong un-met demand for NB-IoT
  This demand has existed since the early days of the Rel-13 evaluations phase, and there are competing non-3GPP technologies which could use TDD spectrum
  Rel-15 is the right time to add TDD support into NB-IoT, with the same deployment, cost, coverage, complexity, and capacity targets as HD-FDD

## Slide 4: Principles for TDD design
  Prioritize in-band design
  In-band operation requires compatibility with LTE, similar to FDD, so will have the largest number of constraints to meet
  Therefore, design for TDD is in-band oriented, and re-use as much as possible for standalone/guard-band
  Alternative design for stand-alone/guard band operation modes where necessary issues are identified
  Same MCL and connection capacity targets as FDD
  Keep ultra-low device complexity and 10-year battery life
  No UL compensation gaps are needed by UE
  UE will be required to re-tune to DL naturally to re-acquire synchronization

## Slide 5: Frame structure – UL:DL configurations
  Compatible with LTE TDD UL/DL configuration
  Possible issues
  NB-IoT may not support all of existing LTE TDD UL/DL configurations.
    Some configurations only have two complete downlink sub-frames in each frame, but NB-IoT needs at least four sub-frames to map common downlink signals (NPSS/NSSS/NPBCH/SIB1) as in FDD.
    NPDCCH/NDPSCH also need room
    Limited uplink resources will impact the uplink performance and latency
  Decide which UL:DL configurations to support, and if some specialized to NB-IoT are needed
Uplink-downlink configuration | Downlink-to-Uplink Switch-point periodicity | Subframe number |  |  |  |  |  |  |  |  | 
 |  | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9
0 | 5 ms | D | S | U | U | U | D | S | U | U | U
1 | 5 ms | D | S | U | U | D | D | S | U | U | D
2 | 5 ms | D | S | U | D | D | D | S | U | D | D
3 | 10 ms | D | S | U | U | U | D | D | D | D | D
4 | 10 ms | D | S | U | U | D | D | D | D | D | D
5 | 10 ms | D | S | U | D | D | D | D | D | D | D
6 | 5 ms | D | S | U | U | U | D | S | U | U | D
Notes: Ask operator what is the typical configuration in real deployment for LTE?

## Slide 6: Frame structure – Special subframe configurations
  Compatible with LTE special sub-frame configuration
  Possible issues
  Special subframes with fixed time location could map common signals, especially when few ‘D’ resources.
  Some configurations may not have enough REs to map NB-IoT signals due to 1 PRB bandwidth
  LTE control region assumed as 3 symbols for NPSS/NSSS/NPBCH/SIB1-NB reduces DL resources
Notes: Ask operator what is the typical configuration in real deployment for LTE?

## Slide 7: DL resource mapping
  Exploit the always present DL resource to map common signals
  E.g. NPSS in sub-frame 5, NSSS/NSIB1 multiplex in sub-frame 0
  Consider how to use DwPTS
  Support SIB-NB in non-anchor carriers
  NB-IoT may have busy downlink due to use of resources for NB-SIB transmissions
  A chance for the ‘unfinished business’ from Rel-14 non-anchor enhancement
Notes: Ask operator what is the typical configuration in real deployment for LTE?

## Slide 8: NPRACH design for TDD
  Existing NPRACH in FDD
  NPRACH transmits consecutively in time duration
  Symbol duration is 266.7us and each 1ms sub-frame contains 3.75 symbols
  Possible issues
  Lack of successive uplink resource to directly map NPRACH.
  Scattered TDD resource is harmful for detection performance and also latency of initial access
45kHz
3.75kHz
3.75kHz
Notes: Ask operator what is the typical configuration in real deployment for LTE?

## Slide 9: TDD performance improvements
  Target to compensate for performance losses due to non-continuous resources in TDD
  NRS/NB DMRS
    Increase density of reference symbol for more robust channel estimation
    Balanced against data rate
  PRB- (i.e. NB-IoT carrier) level frequency-hopping
    When multi-carriers are deployed
    To acquire frequency diversity gain
  Faster NPDSCH scheduling if resources are available sooner on a different DL carrier
  Note that NPRACH design for TDD is part of this performance improvement effort
Notes: Ask operator what is the typical configuration in real deployment for LTE?