## Slide 1: A preliminary survey of regulations for unlicensed operation in the 60 GHz range
3GPP TSG RAN Meeting #74
Vienna, Austria, December 5 - 8, 2016
RP-162212
AI: 9.4
Huawei, HiSilicon

## Slide 2: Content
Regulations of 60GHz unlicensed band in region 3 countries
  Channel bandwidth
  Effective isotropic radiated power (EIRP)
  Antenna power (conductive power) and antenna gain
  Maximum channel occupancy time (MCOT)
  Occupied channel bandwidth (OCB)
  Listen before talk (LBT)
ITU Radio Regulation RESOLUTION 238 (WRC-15)
References

## Slide 3: 60GHz Unlicensed Bands in Region 3
Fc = 58.32 GHz
Fc = 60.48 GHz
Fc = 62.64 GHz
Fc= 64.80 GHz
2.16 GHz
Japan (57.00 – 66.00 GHz)
China (59.00 – 64.00 GHz)
59.40 GHz
57.24 GHz
2.16 GHz
2.16 GHz
2.16 GHz
61.56 GHz
63.72 GHz
65.88 GHz
Channel 1
Channel 2
Channel 3
Channel 4
South Korea (57.00 – 64.00 GHz)
Australia (59.40 – 62.90 GHz)
Note: there is no 60GHz unlicensed band in India
Singapore (59.00 – 64.00 GHz)

## Slide 4: Channel bandwidth in ITU Recommendation
There is no channel bandwidth regulation except that Japan limited the maximum bandwidth to 2.5GHz
The text of channel bandwidth and center frequencies in [1]
  A 2160 MHz channel bandwidth is required. It is important that MGWS standards employ the same channelization in order to promote better coexistence. Four center frequencies are recommended to be at 58.32, 60.48, 62.64, and 64.80 GHz.
  * Reference [1]: Recommendation ITU-R M.2003-1 Multiple Gigabit Wireless Systems in frequencies around 60 GHz

## Slide 5: Channelization in IEEE 802.11ad/aj for countries of Region 3
Area | Channel starting frequency (GHz) | Channel spacing (MHz) | Channel set | Channel frequency band (GHz)
China | 56.16 | 2160 | 2,3 | 59~64
 | 56.70 | 1080 | 35,36,37,38 | 
Japan | 56.16 | 2160 | 1, 2, 3, 4, | 57~66
Europe | 56.16 | 2160 | 1, 2, 3, 4, | 57~66
ad/ay: Channel center frequency = Channel starting frequency + Channel spacing X Channel number
aj: Channel center frequency = Channel starting frequency + Channel spacing × (Channel number mod 32)
Reference [2]: Draft P802.11REVmc_D8.0.pdf

## Slide 6: EIRP
Country Name | Effective isotropic radiated power (EIRP)
China | The average EIRP is 44dBm, the peak EIRP is 47dbm
Japan | Not specified
Korean | 43 dBm or 57 dBm (fixed: Point-to-Point)
Australia | A maximum EIRP limit of 150 W and a maximum total peak transmitter output of 10 mW are recommended.
Singapore | 10 W

## Slide 7: Antenna gain
Country Name | Effective isotropic radiated power (EIRP)
China | Antenna power: 10 dBm (10 mW) max. Antenna gain: 34 dBi max.
Japan | Antenna power: 10 dBm (10 mW) max. Antenna gain: 47 dBi max.
Korea | In the case of directional antennas: Antenna power: 27 dBm (0.5 W) max. In the case of omni-directional antennas: Antenna power: 20 dBm (0.1 W) max.
Australia | Not specified
Singapore | Not specified

## Slide 8: Other Aspects
For 60GHz, there is no maximum channel occupancy time (MCOT) requirements in regulations for China, Japan, Korea and Australia.
For 60GHz, there is no occupied channel bandwidth (OCB) requirements in regulations for China, Japan, Korea and Australia.
For 60GHz, there is no LBT requirements in regulations for China, Japan, Korea and Australia.

## Slide 9: ITU Radio Regulation RESOLUTION 238 (WRC-15)
Studies on frequency-related matters for International Mobile Telecommunications identification including possible additional allocations to the mobile services on a primary basis in portion(s) of the frequency range between 24.25 and 86 GHz for the future development of International Mobile Telecommunications for 2020 and beyond
66-71GHz is being studied for potential IMT identification.

## Slide 10: References on the regulations
Country/Organization | Regulation
China | 2005-423微功率（短距离）无线电设备的技术要求
 | 2006-082关于60GHz 频段微功率（短距离）无线电技术应用有关问题的通知
Japan | MIC - Ordinance Regulating Radio Equipment
Australia | 60 GHz Band millimeter wave technology
Singapore | https://www.imda.gov.sg/regulations-licensing-and-consultations/acts-and-regulations
ITU | Recommendation ITU-R M.2003-1 Multiple Gigabit Wireless Systems in frequencies around 60 GHz
 | Report ITU-R M.2227-1 Multiple Gigabit Wireless Systems in frequencies around 60 GHz
 | ITU Radio Regulation RESOLUTION 238 (WRC-15) Studies on frequency-related matters for International Mobile Telecommunications identification including possible additional allocations to the mobile services on a primary basis in portion(s) of the frequency range between 24.25 and 86 GHz for the future development of International Mobile Telecommunications for 2020 and beyond