## Slide 1: Motivation for New WI on Even further enhanced MTC for LTE
Ericsson
RP-162286
3GPP TSG RAN Meeting #74
Vienna, Austria, 5th - 8th December 2016
Agenda item 10.1.1

## Slide 2: Power consumption improvements
Justification
  In order to achieve ultra-long battery life for applications with low data activity, it is critical to keep the power consumption in idle mode as low as possible. Therefore, is proposed to target reduced power consumption in particular related to paging and cell (re)selection.
Objective
  Relaxed monitoring for paging [RAN1 lead, RAN2, RAN4]
    E.g. wake-up receiver type signaling
  Relaxed monitoring for cell reselection [RAN2 lead]
    Make UE requirements on monitoring for cell (re)selection more flexible and dependent on network configuration. Other optimizations of idle mode behavior are not precluded.

## Slide 3: Improved support for high number of devices
Justification
  As the number of devices that need to be managed efficiently increases, it is desired that the network has effective tools for access load control in idle mode as well as congestion/overload control in connected mode. Physical layer improvements for increased spectral efficiency especially in uplink may also be needed.
Objective
  Increased spectral efficiency for UEs in deep coverage scenarios [RAN1 lead, RAN2, RAN4]
    E.g. sub-PRB resource allocation, CDMA or MU-MIMO approaches
  Improved access load control [RAN2 lead]
    Improved congestion control taking the specifics of the LTE MTC radio interface into consideration, e.g. CE-level-based access class barring
  Congestion/overload control in connected mode [RAN2 lead]
    The network shall be able to control the behavior of UEs in connected mode to prevent mobile originating signalling and/or data traffic (cf. TS 22.011 section 4.6).

## Slide 4: Coverage improvements
Justification
  Rel-13 introduced coverage enhancement through repetition techniques for most channels, and the achievable coverage overshoots the original coverage enhancement target for several of the channels. By identifying and improving coverage for the limiting channel(s), it may be possible to improve coverage even further using a relatively modest effort. It is also worth considering whether the mode selection (the RRC reconfiguration between CE and non-CE modes, and the starting PRACH CE level selection procedure) can be optimized.
Objective
  Identify and address coverage limiting channel(s) [RAN1 lead, RAN2, RAN4]
    E.g. introducing further repetition for one or more of PSS/SSS, PBCH, SI, PUCCH
  Improved UL coverage for lower UE power classes [RAN1 lead, RAN2, RAN4]
    Aim for similar coverage with lower UE power classes as for the 23-dBm UE power class.
  Identify and address potential issues when switching between CE mode and non-CE [RAN2 lead]
    Ensure that all UE categories can always operate in the most optimal (CE or non-CE) mode.
  Improved starting PRACH CE level selection [RAN4 lead, RAN1, RAN2]
    E.g. changes to the starting PRACH CE level selection criteria

## Slide 5: Latency improvements
Justification
  Many IoT sessions are brief and the lion part of the total latency comes for the delays related to the connection setup procedure. It is proposed to support data transmission in Msg3 and Msg4 in the RRC Suspend/Resume procedure to reduce the latency. Latency improvements in connected mode, e.g. based on UL prescheduling mechanism, can also be considered.
Objective
  Support for data transmission in Msg3 and Msg4 [RAN2 lead, RAN1, RAN3]
    Support data transmission in Msg3 and Msg4 in the RRC Suspend/Resume procedure.
  Latency reduction in connected mode [RAN2 lead, RAN1]
    Consider potential improvements using e.g. UL prescheduling mechanism.

## Slide 6: Improved support for flexible deployment
Justification
  In Release 13 it is assumed that BL UEs have no need for CRS transmissions outside their allocated narrowband but there is nothing precluding that BL UEs monitor CRS outside their allocated narrowband. In order to improve the possibility for CRS muting (for reduced inter-cell interference), it is proposed to allow the UE to indicate that it does not rely on CRS outside its narrowband. It is also proposed to allow the eNB to make use of the legacy control channel (PDCCH, etc.) region e.g. for data transmission to BL/CE UEs.
Objective
  Improved support for CRS muting [RAN1 lead, RAN2]
    Enable UEs to indicate that they do not rely on CRS transmission outside their allocated bandwidth.
  Improved support for standalone MTC carrier [RAN1 lead, RAN2]
    Enable use of the legacy control channel (PDCCH, etc.) region e.g. for data transmission.

## Slide 7: Improved support for new use cases
Justification
  Earlier releases have focused on low-mobility cases such as metering devices in basements. As BL UEs are increasingly becoming interesting for other use cases such as wearables, it is relevant to consider improvements for scenarios with higher mobility. Therefore, it is proposed to consider specifying support for higher UE velocities and lower UE power classes.
Objective
  Lower UE power class [RAN4 lead, RAN2]
    Specify for a lower (e.g. 14 dBm) UE power class suitable for e.g. wearables and logistics.
  Supporting higher velocities in CE mode A [RAN4 lead]
    Specify support for higher (e.g. 200 km/h) velocities suitable for e.g. wearables and logistics.

## Slide 8: Next Generation access technologies requirements and scenarios
Justification
  3GPP have in TR 38.913 agreed a set of scenarios and requirements for the Next Generation Access Technologies among which a specific set of requirements associated with the massive MTC (mMTC) use case is found. It has also been agreed to include LTE and NB-IoT as part of the 3GPP IMT-2020 submission to ITU. It is therefore time to study the feasibility of LTE MTC to meet the mMTC requirements, and if necessary specify any improvements needed to secure the fulfilment of the same.
Objective
  Study the support for the mMTC set of requirements and, if needed, specify necessary enhancements to fulfill the same. [RAN1 lead, RAN2, RAN3, RAN4]
    Support latency of at least 10 seconds.
    Support coverage of 164 dB Maximum Coupling Loss (MCL).
    Support UE battery life beyond 10 years.
    Support connection density of 1,000,000 devices per square km.