## Slide 1: simplified HS-SCCH for UMTS
RP-162289 - Motivation for New proposed WI

## Slide 2: Background (1/2)
The HS-SCCH is a downlink control channel used for scheduling HS-DSCH transmissions, as well as for instructing the UE to perform specific actions via HS-SCCH orders.
The HS-SCCH should be listened by the UE at any path-loss ratio within the cell, however according to current observations the HS-SCCH becomes costly in bad radio conditions, which puts a limitation on its usability.
Being more specific, in bad radio conditions the power invested in the control information bits carried on the HS-SCCH limits the available power for the HS-PDSCH.

## Slide 3: Background (2/2)
In addition, decoding the HS-SCCH in bad radio conditions becomes more challenging since in principle all the codewords that can be carried over the HS-SCCH are equally likely to occur, nonetheless under those bad radio conditions only small subset of those codewords can occur in practice.
It is therefore important to enhance the performance of the HS-SCCH channel for its usage in presence of bad radio conditions.

## Slide 4: Proposed RAN Work Item
Introduce a simplified version of the HS-SCCH Type1 where some of the control information bits carried on the HS-SCCH part I are made deterministic (e.g., CCS bits and MS bit). The following aspects shall be taken into consideration:
  The L1 processing chain as described in the current UMTS standard shall be reused and no changes are allowed (i.e., adding/removing blocks to the L1 processing chain is not allowed).
  Keep backward compatibility (e.g., re-ordering bits is not allowed).
Introduce a mechanism for triggering the usage of the simplified version of the HS-SCCH Type 1, if possible by making use of legacy mechanisms.

## Slide 5: benefits
The main advantages of using a simplified HS-SCCH are the following ones:
  Better performance in poor radio conditions
    Improves BLER
    Improves Miss detection Performance
    Improves False detection Performance
  Power savings in DL (can be translated to coverage improvements)
  Backward compatibility: The gains will be seen for the Rel-15 UEs, while legacy UEs can decode the HS-SCCH as usual providing the legacy performance.
  Minimum standard impact (the HS-SCCH ”L1 processing chain” is not modified at all).