## Slide 1
Ericsson
Motivation for new WI proposal:
Enhancement of Dedicated Core Networks (eDECOR)
3GPP TSG RAN-74 Vienna, Austria, December 5 - 8, 2016
RP-162291

## Slide 2: Overview: Enhancement of Dedicated Core Network
Add on to REL-13 DECOR
Functionalities Included (in the SA2 WI):
  UE assisted DCN selection
  Load balancing over DCNs
  Congestion control per DCN
  DCN-ID change in CN due to re-configuration
UE assisted DCN selection and Load balancing over DCNs have RAN impacts.

## Slide 3: UE assisted DCN selection
  This feature is to reduce the need for REL 13 DECOR reroute by using an indication (DCN-ID) sent from the UE and used by RAN to select the correct DCN.
  The DCN-ID shall be assigned to the UE by the serving operator and is stored in the UE per PLMN ID. Both standardized and operator specific values for DCN-ID are possible.
  SA2 has agreed that in the RRC Connection Complete message transferring the NAS Request message, the UE provides the DCN-ID, if available. The NAS Request message is sent to the selected node.
  RAN selects serving node (MME or SGSN) based on the DCN-ID provided by the UE and configuration in RAN. The DCN-ID is provided by the RAN to the MME/SGSN together with the NAS Request message.

## Slide 4: Load balancing over DCNs
E-UTRAN
  When an MME serves multiple DCNs and one DCN is supported by multiple MMEs, in order to achieve load balancing across the MMEs of the same MME pool area supporting the same DCN, each DCN supported by this MME may have its own Weight Factor (Weight Factor per DCN). The Weight Factor per DCN is set according to the capacity of an MME node for a specific DCN relative to other MME nodes’ capacity for that DCN within the same MME pool area. The eNB is provided with per DCN Weight Factors, if any, by the connected MMEs at the set-up of the S1 connection.
UTRAN/GERAN
  When dedicated core networks (DCNs) are used, load balancing by RNC/BSC is only performed between SGSNs that belong to the same DCN within the same SGSN pool area. Load balancing may also be performed per DCN in the case of an SGSN serving multiple DCNs when one DCN is supported by multiple SGSNs.