## Slide 1: WF on 5G C-IoT
Telecom Italia, Vodafone, Qualcomm Incorporated, Huawei
3GPP TSG RAN Meeting #83
Shenzhen, China, 18th – 21st March 2019
RP-190498

## Slide 2
Current status:
  SA2 informed RAN, RAN2 and RAN3 about the completion of the “Study on Cellular IoT support and evolution for the 5G System” (LS in [1])
    SA2 discussed whether to support “UP CIoT optimization” solution for NB-IoT and eMTC connected to 5GC in addition to “RRC_INACTIVE” solution
  Revision of Rel-16 WIs: additional enhancements for both eMTC [2] and NB-IoT [3] were agreed in RAN#82 (Dec. 2018) to include objectives allowing for eMTC and NB-IoT to be connected to the 5GC
    Among the objectives, support of extended DRX (eDRX) in CM-CONNECTED with RRC_INACTIVE (with sleep cycles up to the NAS and SMS retransmission timers) is also included
  In RAN2#105 (Feb. 19) RAN2 replied to SA2, RAN and RAN3 with the LS in [4] stating that both solutions are feasible but there is not consensus on whether to support “RRC_INACTIVE” and/or “UP CIoT optimization”
Observations:
  In our understanding, “UP optimization” is the only user-plane solution that meets the CIoT objective for battery life set in Rel-13 [5]
  Based on the technical analysis in R2-1900424 [6] and further RAN2 discussions:
    “RRC_INACTIVE” with sleep cycles up to NAS/SMS retransmission timers does not meet the CIoT objective for battery life
    Mobile-Initiated Connection Only (MICO) is currently not supported in RRC_INACTIVE
    Potential changes to RRC_INACTIVE would be needed to meet the power consumption objective (e.g. RAN Notification Area Update occasions)
  “UP CIoT optimization” solution is already supported for EPS
  IoT devices will need to support both EPS and 5GS for quite some time (migration will take time; IoT devices are often used in roaming scenarios to maximize coverage; some markets may migrate more slowly than others)
  Supporting both “UP CIoT optimization” and “RRC_INACTIVE” leads to increased complexity (i.e. higher costs) of IoT devices

## Slide 3
Operators’ needs:
  It is of importance for operators that both UE power consumption (impacting the battery life) and complexity (i.e. cost) requirements meet the C-IoT objectives set in Rel-13 in order to meet IoT market requirements (as in TR 45.820 [5]) and support migration from EPC to 5GC:
    UE battery life of at least 10 years
    Reduced complexity devices
  Therefore, leverage EPS CIoT specification as much as possible and only introduce the absolute minimum changes needed to operate with 5GS.
Proposals
  Ensure devices supporting EPS and 5GS C-IoT are able to meet C-IoT objectives set in Rel-13, in particular UE battery life and complexity
    Note: Fundamentally different solutions for 5GS CIoT compared to EPS CIoT will lead to increased device complexity and cost. (i.e. multiple options to implement and test)
  Send a response LS to SA2, RAN2 and RAN3 stating the desire to have a common UP solution for EPC and 5GC.

## Slide 4
References
[1] RP-182700 - LS on Completion of Study on Cellular IoT support and evolution for the 5G System (S2-1813400); RAN#82 meeting, Sorrento (Italy), Dec. 2018
[2] RP-182891 - Revised WID: Additional MTC enhancements for LTE; RAN#82 meeting, Sorrento (Italy), Dec. 2018
[3] RP-182902 - Revised WID: Additional enhancements for NB-IoT; RAN#82 meeting, Sorrento (Italy), Dec. 2018
[4] RP-XXXX - Response LS on Completion of Study on Cellular IoT support and evolution for the 5G System (R2-1902436); RAN#83 meeting, Shenzhen (China), Mar. 2019
[5] TR 45.820 - Cellular system support for ultra-low complexity and low throughput Internet of Things (CIoT); Rel-13
[6] R2-1900424 - Support for User Plane CIoT optimisation for 5GC; Qualcomm Inc.; RAN2#105 meeting, Athens (Greece), Feb. 2019