## Slide 1: Motivation for SI on Multi-SIM devices in RAN
China Telecom, vivo, CAICT, Xiaomi, Spreadtrum, Apple, AT&T, Charter Communications, [Huawei], [CMCC], [China Unicom], [OPPO], [Lenovo], [Nokia], [Qualcomm], [MTK], [Samsung], [ZTE], [Ericssion], [Intel], […] , …

## Slide 2: Background
Increasing number of UE vendors begin to provide Multi-SIM devices
  Apple, Huawei, Lenovo, OPPO, Samsung, vivo, Xiaomi, ZTE ……
Multi-SIM device to address the following use cases
  One SIM card for private communication and another one for business purpose
  One SIM card for local operator and another one for home operator while roaming
  Different SIM card for different service
    E.g. SIM A with “family circle” plan for voice service and SIM B with “mobile data” plan for data service

## Slide 3: Motivation
  Multi-SIM is currently supported in implementation-specific manner
  Common radio and baseband components shared among multiple SIMs is widely used
    UE communicates with multiple systems in TDM manner, e.g. via UE autonomous gap
    No coordination between UE and NW
  Implementation-specific manner may lead to
  Messed up NW statistics
    Short UE autonomous gaps (tens of ms) in system 1 due to UE switching for paging monitoring in system 2 may be interpreted as radio problem by system 1
    Long UE autonomous gaps in system 1 due to UE switching to establish connection in system 2 will certainly be classified as erroneous case
  Degraded user experience
    Paging collision can cause paging missing
    Service interruption in the first system due to UE communicating with the secondary system
    Date loss due to paging reception in another system
    Long latency for cell selection and reselection
  Related ongoing AS study item(SP-181251)
  it is necessary to begin RAN side impact study ASAP in order to speed up full support of Multi-SIM feature

## Slide 4: Paging Collision
UE monitors one PO for paging in a DRX cycle per SIM
  The time of Paging Occasions (POs) is calculated based on the UE identifier (IMSI and 5G-S-TMSI for EPS and 5GS, respectively) and RAN configurations, e.g. PF_offset, firstPDCCH-monitoringOccasionOfPO, pagingSearchSpace, SSB number and ssb-PositionsInBurst, uplink symbol and flexible symbol etc
  Paging collision occurs when the UE identifier values associated with the different SIMs lead to POs overlapping in time domain. Paging collision may result in missing of paging
  Paging collision cannot be totally solved by CN alone, since the radio frame/slot a PO mapped to in Uu is highly dependent on RAN configurations, which are transparent to CN
Proposal
  Identify the paging collision solution, include CN paging and RAN initiated paging

## Slide 5: Service Interruption
  Ongoing service in the first system is interrupted while
  UE occasionally switch to the secondary system
    E.g. to read the paging, perform measurements, or read the system information
  UE initiates a high priority service in the secondary system
    E.g. to respond to paging from the secondary system or initiate a voice call in the secondary system
  Similar issue may exist for UE with dual RX/TX when the UE establishes dual connectivity to one system
  Proposal
  Identify the issues and potential solutions for delivering paging to UE on SIM A while the UE is actively communicating with SIM B(for both single and dual connectivity configurations)
  Identify the issues and potential solutions for UE enters RRC Connected state in one system from Idle/Inactive while the UE is already in RRC Connected state in another system

## Slide 6: Dual RX/TX UE
  Dual Rx / dual Tx Multi-SIM UE may work in two modes
    Mode1: dual connectivity with one system, e.g. EN-DC
    Mode2: single connectivity per system, e.g. one for voice with SIM A and the other for data with SIM B
  Capabilities reporting for different mode
    In mode1, UE may indicate supporting EN-DC; while it may indicate not supporting EN-DC in mode2
    Impact on power control is also foreseen as the maximum UE power indicated in the two modes may be different
  Proposal
  Identify the issues and potential solutions when both SIM A and SIM B are in RRC connection state

## Slide 7: Cell Selection/Reselection
  Cell Selection/Reselection performed per SIM
  Optimization can be considered in case both SIMs belongs to the same operator
  Gain on UE power consumption, latency reduction for cell selection/reselection can be studied
  Proposal
  Identify the necessary Cell selection/reselection enhancement for intra-MNO case

## Slide 8: Suggestion
  RAN starts the multi-SIM study to cover the items that have been identified by SA with RAN impacts and the items that are identified by RAN itself after SID scope email discussion in RAN.