## Slide 1: Motivation for new WI on NR performance requirement enhancement
China Telecom
June 2019
3GPP TSG RAN Meeting #84
Newport Beach, USA, June 3-6, 2019
Agenda: 9.1.4
RP-190926

## Slide 2: General motivation
With the very tight time schedule for NR Rel-15 performance work, several important NR features specified in Rel-15 core part are not covered when developing the Rel-15 performance requirements, such as:
  UE and BS receivers for handling inter-cell, inter-layer or inter-user interference
  URLLC-related requirements
  PDSCH CA, EN-DC and NE-DC demodulation requirements
  Other Rel-15 leftovers
  Meanwhile, these features are very important Rel-15 features, and some operators have plans to deploy them in the early deployments.
Thus it is proposed to open a new Rel-16 WI to define performance requirements for the selected NR features that are specified in Rel-15 core part but not covered in Rel-15 performance part.

## Slide 3: Interference-aware receivers (1/2)
  Motivation
  Co-channel interference has substantial impact on DL and UL performance.
  In LTE, several interference-aware receivers have been introduced for data channel throughput improvement, and some of them have no impact on core specification:
    PDSCH: inter-cell interference rejection combining (IRC), inter-stream interference cancellation (IC) [1]
    PUSCH: inter-cell IRC, intra-cell inter-user IC [2]
  In NR Rel-15,
    PDSCH and PUSCH performance requirements are defined without explicit modeling of inter-cell interference, i.e., inter-cell IRC is not considered [3] [4].
    Meanwhile, PUSCH performance requirements are defined without considering intra-cell inter-stream/user interference handling [3].
  In NR NOMA SI [5], two main classes of receiver architecture are considered based on linear filters with IC for handling intra-cell inter-user interference
    Low complexity: hard-IC (hard L-CWIC)
    Medium complexity: hybrid-IC (mixing hard-IC and soft-IC/turbo L-CWIC)
  It is an efficient way to improve NR spectral efficiency by employing interference-aware receiver.

## Slide 4
  UE interference-aware receivers for FR1
  1st priority: inter-cell interference scenario
    Reference receiver: LMMSE-IRC, RML receiver with interference pre-whitening
    Focus on PDSCH performance enhancements
  2nd priority:
    Intra-cell MU-MIMO interference scenario
      Reference receiver: LMMSE-IRC
    Study whether to introduce PDSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream interference for SU-MIMO
      Up to 4 transmission layers for SU-MIMO are to be considered, and parallel - soft IC can be considered as reference receiver
  BS interference-aware receivers for FR1
  1st priority: inter-cell interference scenario
    Reference receiver: LMMSE-IRC
    Focus on PUSCH performance enhancements
  2nd priority:
    Study whether to introduce PUSCH requirements with enhanced receivers for handling co-channel intra-cell inter-stream/user interference
      For intra-cell inter-user interference handling, hard-IC (hard L-CWIC) and hybrid-IC (mixing hard-IC and soft-IC) receivers as defined in NOMA TR 38.812 can be considered as reference receiver
  Interference-aware receivers (2/2)

## Slide 5: URLLC related requirements
Motivation
  In NR Rel-15, in order to meet the requirements of 10-5 reliability and 1 ms latency for URLLC, a number of features have been introduced.
  However, the corresponding RAN4 performance requirements are still absent [3] [4].
Propose to consider the following performance requirements:
  UE and BS demodulation and CSI requirements for URLLC features
    99.999% Reliability
    Slot Aggregation
    PDSCH Mapping Type B
    Pre-emption indication
    Shortened UE processing time
    Self-contained slot
    Low latency CSI feedback

## Slide 6: UE CA , EN-DC and NE-DC requirements
  Motivation
  CA, EN-DC and NE-DC requirements in Rel-15
    For NR CA, only SDR requirements are defined, while the other requirements have been de-prioritized [6].
    For DC, PDSCH normal demodulation performance requirements and SDR requirements are defined. For normal demodulation requirements, only the PDSCH performance on the NR cell(s) are verified during the test [7].
  To verify the correct implementation of CA and DC feature, PDSCH CA normal demodulation requirements and CA/DC specific requirements need to be defined.
  Propose to consider the following performance requirements:
  NR CA PDSCH normal demodulation requirements
  NR CA, EN-DC and NE-DC power imbalance requirements for intra-band case
  NR CA, EN-DC and NE-DC soft buffer management

## Slide 7: Other Rel-15 leftovers
  UE demodulation and CSI requirements
  Requirements for the number of TX ports larger than 8 and up to 32
    PDSCH demodulation requirements
    CSI reporting requirements
  Requirements with 2 TCI states
  Requirements for additional TDD configurations (subject to operator request)
    Option 1: Additional TDD configurations based on operator request, including {DDSU} with S=10D:2G:2U for FR1 and {DSUU} with S=12D:2G for FR2
  Requirements for additional CBW/SCS combinations (subject to operator request)
  Requirements for additional channel models, including TDL-D and TDL-E
  BS demodulation requirements
  PUSCH requirements for 30% TP test point
  1 PRB PUSCH performance requirements
  Requirements for additional channel models, including TDL-D and TDL-E
  FR2 PUSCH 2T2R requirements for 16QAM with MCS lower than 16, considering the OTA testability limit.

## Slide 8: References
[1] TS 36.101, E-UTRA User Equipment (UE) radio transmission and reception
[2] TS 36.104, E-UTRA Base Station (BS) radio transmission and reception
[3] R4-1813942, WF for NR PUSCH demodulation, Nokia, Nokia Shanghai Bell, RAN4 #88bis, Oct 2018.
[4] R4-1814239, Simulation assumptions for NR PDSCH demodulation performance requirements, Intel, RAN4 #88bis, Oct 2018.
[5] RP-182478, TR 38.812 v1.0.0 on Study on Non-Orthogonal Multiple Access (NOMA) for NR, ZTE, RAN #82, Dec 2018.
[6] R4-1814238, Way forward on NR UE PDSCH demodulation requirements and General aspects, Intel, RAN4 #88bis, Oct 2018.
[7] TS 36.101-4, NR User Equipment (UE) radio transmission and reception; Part 4: Performance requirements

## Slide 9
Thanks!