## Slide 1: Title: « NWI proposal on NTN for Rel-17 » Type: discussion For: Discussion Agenda item: 8 Sources: Thales
3GPP RAN#84 plenary
Newport beach/USA, 3-6 June 2019
NB: This presentation relates to NWI description in RP-190964

## Slide 2: SatCom overview
Satellite communications (SatCom) refers to a wide range of systems operating in various frequency bands allocated to the Broadcast Satellite Services (BSS), Fixed Satellite Services (FSS) or Mobile Satellite Services (MSS).
It is possible to distinguish between two types of SatCom systems according to the type of terminals targeted:
  Terminals with directional antennas: The targeted terminals are mounted on a fixed building or on a moving platform (e.g. bus, train, vessel, aircraft, etc.). The service links typically operate in frequency bands above 6 GHz. The systems typically provide direct to home / office or backhaul services.
  Terminals with omni-directional antenna: The targeted terminals are Handheld, portable or IoT devices. The service links operating in frequency bands below 6 GHz. The systems typically provide low data rate up to wide band services.
SatCom refers to wide range of solutions in terms of targeted terminals, orbit (GEO, Non GEO), frequency bands and services (Unicast/broadcast)

## Slide 3: Roles of SatComs/HAPS in 5G
Foster the roll out of 5G service in un-served areas that cannot be covered economically by terrestrial 5G network (isolated/remote areas, on board aircrafts or vessels) and underserved areas (e.g. sub-urban/rural areas) to upgrade the performance of limited terrestrial networks in cost effective manner;
Reinforce the 5G service availability by providing service continuity for Machine-to-Machine (M2M)/IoT devices or for passengers on board moving platforms (e.g. passenger vehicles-aircraft, ships, high speed trains, bus and cars) or ensuring service anywhere especially for critical communications, future railway communications or maritime communications;
Enable 5G network scalability by providing efficient multicast/broadcast resources for data delivery towards the network edges or even user terminal.
Provide resiliency in case of natural or man-made disaster impacting terrestrial networks
See 3GPP TR22.822 & 38.811

## Slide 4: Why standards for future Non-Terrestrial networks ?
Users, service providers and verticals desire standards to simplify implementation, maintenance and application development
  transport & logistics, public safety, agriculture, utilities, mining/oil & gas, broadcasters, maritime, aeronautic, high speed train, automotive…
Open and global standards ensure
  future proof solutions
  multi-vendor interoperability
Technology commonality with cellular
  Ensure access to economies of scale
  Allows cost reduction, large product diversity & a wider eco-system.
Long term vision: future NTN based on global 3GPP defined standards

## Slide 5: 3GPP standardisation action plan
Objectives
  Providing guidance to future NTN solutions for full integration with the 5G network
  Ease accomodation of legacy SatComs in 5G network
Approach
  Specify the full integration of NTN in 5G
    minimising impact on existing 5G systems
  Enable the native support of NTN by 5G and NR
Enabling integration of legacy SatCom in 5G
preparing 5G future NTN solutions

## Slide 6: Standardisation goals in 3GPP
NTN friendly network management framework
  Service level agreement/traffic demand description and resource management for 3rd parties (e.g. Service providers, telcos) across non-terrestrial networks integrated with 5G
NTN friendly NG-RAN protocols/functions & related tests
  enabling 5G system to support non-terrestrial networks (access or transport) in single or multi connectivity context
NTN friendly New Radio (NR) interface & the related tests
  Enabling multi-vendor interoperability for all non-terrestrial networks (orbit, frequency bands and targeted UEs)
See 3GPP TR22.822 & 38.811
Full integration in 5G at management, control and user plane

## Slide 7: Why now and not in previous 3GPP releases ?
5G system is inherently designed to be
  A network of networks
    Natively supporting inter access hand-over/multi connectivity
  Flexible to support a wide range of services/applications
3GPP is now open to new stakeholders
  Verticals: requirements on coverage and availability
  Other industry: satellite, wireline etc..
5G a flexible technology framework to define global standard for future NTN services, whatever orbits, frequency bands or terminal types

## Slide 8: Past / on going 3GPP effort on SatCom
Item ref | Lead WG | Title | 3GPP doc | Completion
SI ”FS_NR_nonterr_nw on NR” | RAN | Study on New Radio (NR) to support Non Terrestrial Networks (Release 15) | TR 38.811 | June 2018
SI ”FS_NR_NTN_solutions” | RAN3 | Solutions for NR to support non-terrestrial networks (NTN) (Release 16) | TR 38.821 | Dec 2019
SI ”FS_5GSAT” | SA1 | Study on using Satellite Access in 5G; Stage 1 (Release 16) | TR 22.822 | June 2018
WI ”5GSAT” | SA1 | Service requirements for the 5G system; Stage 1 (Release 16) | TS 22.261 | Dec 2018
WI ”FS_5GSAT_ARCH” | SA2 | Study on architecture aspects for using satellite access in 5G (Release 16) | TR 23.737 | Sept 2019
WI ”FS_5G_SAT_MO” | SA5 | Study on management and orchestration aspects of integrated satellite components in a 5G network | TR 28.808 | Dec 2019

## Slide 9: Reference architectures - 1
Non 3GPP access (satellite)
N3IWF
UE
5G CN
N2, N3
N1
Y1
Y2
See figure 4.2.8.2.1-1 in TS 23.501
NWu
2) Non 3GPP defined Satellite access
UE
NG RAN (gNB)
5G CN
NR-Uu
NG
N6
Data Network
1) Satellite transport network
Out of RAN scope
Out of RAN scope

## Slide 10: Reference architectures - 2
UE
NG RAN
5G CN
NR-Uu
NG
N6
Data Network
UE
NG RAN
5G CN
NR-Uu
NG
N6
Data Network
3) Satellite access with transparent satellite
4) Satellite access with regenerative satellite

## Slide 11: Reference architectures - 3
UE
IAB node or relay
5G CN
NR-Uu
Or NR-PC5
NG
N6
Data Network
IAB
donor
NR-Uu
5) Transparent Satellite access with IAB node or relay
UE
IAB node
5G CN
NR-Uu
NG
N6
Data Network
IAB
donor
NR-Uu
6) Regenerative Satellite access with IAB node

## Slide 12: RAN Rel 17 NTN standardisation planning
New Work item RAN1/2/3/4 « NR support non-terrestrial networks »
  Using outcomes of Rel-16 Study item FS_NR_NTN_solutions
  Adaptations to enable NR to support Non-Terrestrial networks
  Considering reference frequency bands such as S band (Band 65) and other bands TBD
    New frequency bands may be proposed (e.g. Ka, Q/V bands as indicated in RP-190995). ETSI harmonised standards may be considered as starting points

## Slide 13: RAN Rel 16/17 NTN standardisation planning
2021 Q1
2019 Q2
2019 Q3
2019 Q4
RAN1/SI: NR non-terrestrial
RAN2/SI: NR non-terrestrial
RAN3/SI: NR non-terrestrial
Phy
layer
Access
layer
RAN
architecture
Release 16
2020 Q3
2020 Q4
2020 Q1
2020 Q2
Release 17
RAN1/WI: NR supports non-terrestrial
RAN2/WI: NR supports non-terrestrial
RAN3/WI: NR supports non-terrestrial
2021 Q2
RAN4/WI: NR supports non-terrestrial
RAN RF
Performance
RAN4/WI: NR Frequency bands for NTN specifications
RAN Spectrum

## Slide 14: NR supports NTN: potential impacts
RAN1: timing and frequency acquisition, timing advance, random access, control loops (power, ACM, CSI), HARQ turned off / enhancements, transmission timing
RAN2: user plane timer extension, HARQ turned off/enhancements, mobility handling, paging, radio link monitoring , adaptation of 2 step RACH, SN and window sizes for RLC and PDCP
RAN3: Tracking Area management, network identities, Hand-over robustness to latency, feeder link switch over
RAN4: Radio Resource Management, reference frequency bands to be defined
To be refined with outcomes of the on going study item FS_NR_NTN_solutions

## Slide 15: RAN Rel 17 NTN standardisation planning - 2
New Work item RAN1/2/4 « NB-IoT evolution »
  Including study on
    NB-IoT supports Non-terrestrial networks integrated with 5G core network (leveraging outcomes of study & specifications on solutions for NR to support NTN)
2021 Q1
2019 Q2
2019 Q3
2019 Q4
Release 16
2020 Q3
2020 Q4
2020 Q1
2020 Q2
Release 17
2021 Q2
RAN1/2/4-WI: NB-IoT evolution

## Slide 16: NB-IoT supports NTN: potential impacts
Limited study required
  System information, common signalling [RAN2]
  Mobility management [RAN2, RAN4]
    Idle mode beam re-selection
    RRM measurements
  RRM/RF performance requirements [RAN4]
  HARQ / RACH procedures mainly for GEO [RAN1, RAN2]

## Slide 17: END
Point of contact:
Nicolas.chuberre@thalesaleniaspace.com