## Slide 1
On Rel-17 IAB scope
3GPP TSG-RAN Meeting #84 Tdoc RP-190971 Newport Beach, California, USA, June 3rd – 6th 2019 Agenda Item: 8 - Proposals for Release 17 Source: Ericsson

## Slide 2: Overview
IAB Rel-16 provide basic support for multi-hop and multi-path relaying.
The solution supports
  QoS prioritization of traffic on the backhaul link
  Flexible resource usage between access and backhaul
  Topology adaptivity in case link failure
In Rel-17 it would be possible to further evolve the IAB solution targeting increased efficiency and support for new use cases

## Slide 3: New IAB use cases for Rel-17
The Rel-16 IAB work focused mainly on inband relaying (FR2) for enhanced mobile broadband services
In Rel-17 it would be beneficial to expand into additional use cases e.g. to
Improve support for ad-hoc, temporary and portable/mobile IAB node deployments, e.g., IAB network for operation in disaster areas
Improved support for IAB in critical IoT scenarios including improved latency and reliability mechanisms
Enhancements to enable energy efficient operation
IAB enhancement for rural coverage, include support for lower frequency bands, longer distances, etc.
Notes: Aspects parked in speakers notes until Ericsson view is further clarified:
IAB nodes for IoT deployments
Multiplexing between different links of an IAB node (parent/child/access links)
  Enhanced SDM between parent links and child links
  May include new timing relations between links within the IAB node

## Slide 4: Possible areas for improvements in Rel-17
Improved multi-connectivity, including improved load balancing, support for more alternative paths (e.g. using multiple MTs), multi-connectivity with different Donor CUs
Improvement to seamless migration e.g. at inter-donor CU change
Improvements to energy efficiency, including node wake-up, support for dormant state (e.g. INACTIVE), …
Latency improvements, and other QoS related improvements for real-time and URLLC services
Flow control improvements to minimize buffering in intermediate nodes
Improvement to dynamic access / backhaul radio resource sharing