## Slide 1
Suggestions on NR Rel 17
05/17/2019
RP-191017

## Slide 2: NR for FWA Applications
High capacity transport/FWA links in 71-76 and 81-86 GHz bands
Support of non-3GPP backhauling technologies
Complement the wired (FTTH, 10G DOCSIS) infrastructure in residential areas
Expand the fiber nodes reach in urban areas.
Increased spectral efficiency
Features
User data throughput: 20+ Gbps
Channel Bandwidth: 400, 800 and 1.2 GHz
Increased number of beams with faster beam control
Increased Spectral Efficiency:
  QAM1024 for sub 7 GHz NR apps
  QAM256 for mm wave links

## Slide 3: NR in Unlicensed Bands
The licensed spectrum is the preferred mode of operation for NR.
The licensed spectrum traffic should be able to offload traffic onto unlicensed spectrum available access technologies
  The most widely available access technology supporting unlicensed spectrum (5/6 GHz) is Wi-Fi (802.11ac/ax)
Any NR-U specifications should be based on an an optimized coexistence with other access technologies existent or projected to have a large mass scale deployment in unlicensed spectrum
NR Rel 17 should target licensed and unlicensed bands in the 52.6 - 114 GHz bands
Enhanced NR-U (Rel 17)
5/6 GHz: Optimized performance in coverage areas coexistent with 802.11ac and 802.11ax networks (5 and 6 GHz).
  Implement the common preamble supporting full coexistence with Wi-Fi 802.11ax/ac (5/6 GHz)
60 GHz: NR-U coexistence with 802.11ad and 802.11ay
  Target Directional LBT for highly directive links.
52.6-114 GHz: Increase the foot print of unlicensed bands specifications, by protecting existent satellite services.
  Target Highly directional FWA links providing protecting existent ESS links
  Short range/D2D applications

## Slide 4: IAB
Multiple hops able to cover fiber nodes ISD=500…800m
Support of Fixed Wireless Applications
Support of non-3GPP backhauling technologies
Features:
  Reduced latency over multi-hop connectivity
  Large channel BW (0.8, 1.2 GHz) supporting 20+ Gbps user data
  Hybrid synchronization: re-use other FWA technologies synchronization (on the donor gNB side)
  gNB spatial multiplexing (SDM support)
  Topology redundancy (support of more than one parent node).

## Slide 5
Suggestions on NR Rel 17