## Slide 1: Proposed WI scope for Power Saving in RAN2

## Slide 2: Observations on TU allocation for RAN2
RAN2 chairman emphasized the followings for RAN2 TU allocation in RP-190750.
  For remainder of Release 16:
    No proposal to increase time of existing WIs can be accommodated.
    If your WI is under pressure then reduce the scope, don’t increase the time.
    No further WIs requiring RAN2 time can be agreed.
  UDC and IDC WIs were also not approved due to TU overload issue in RAN#83.
Only 4 TUs are allocated to Power saving WI in RAN2.
If power saving WI needs more than 4 TUs, the scope of power saving WI should be reduced.
RAN2 meeting | 107 | 107bis | 108 | 109
UE power consumption WI | 1 | 1 | 1 | 1

## Slide 3: Discussion in RAN2
RAN2 discussion was diverged in SI phase. Finally, the following objectives are identified as a candidate for power saving WI.
  PDCCH-based power saving signal/channel scheme for wake-up purpose
  DCI-based PDCCH monitoring skipping
  MIMO layer adaptation
  Fast RRC state transition
  UE assistance information
  Power saving in CA/DC
  RRM measurement relaxation
  Power saving for paging procedure
There are too many objectives to be completed within 4 TUs.
Only the feasible number of objectives should be selected and included in power saving WID.

## Slide 4: Recommendation from RAN2
It was agreed in RAN2 e-mail discussion that following three items are recommended for WI.
  PDCCH-based power saving signal/channel scheme for wake-up purpose
    It is recommended that the PDCCH-based power saving signal/channel for wake-up purpose is used to indicate to the UE to wake up to monitor the PDCCH during the next occurrence of the drx-onDurationTimer.
  MIMO layer adaptation
    It is recommended to support the possibility to configure a different MIMO layer configuration for the initial/default BWP compared with other BWPs of a Serving Cell.
  Fast RRC state transition
    It is recommended to support a mechanism for a UE to indicate its preference of transitioning out of RRC_CONNECTED state.
Above three items should be included in power saving WID.

## Slide 5: What else can be included?
DCI-based PDCCH monitoring skipping
  Could be included if there is no/minimal impact to RAN2
UE assistance information
  So diverged views in RAN2.. may be difficult to converge within 4 TUs.
Power saving in CA/DC
  Not fully discussed during SI phase. Could be discussed in Rel-17.
RRM measurement relaxation
  Have consensus on limited scope, e.g. RRM measurement for neighbor cell
Power saving for paging procedure
  Not fully discussed during SI phase. Could be discussed in Rel-17.
RRM measurement relaxation could be included in power saving WID.

## Slide 6: Proposals for Power Saving WI scope update
Following objectives should be included in the work scope updated in RAN#84
  PDCCH-based power saving signal/channel scheme for wake-up purpose [RAN1/RAN2]
    Impacts to both RAN1 and RAN2
  MIMO layer adaptation [RAN1/RAN2]
    Impacts to both RAN1 and RAN2
  Fast RRC state transition [RAN2]
    No/marginal impact to RAN1
  RRM Measurement relaxation [RAN2/RAN4]
    No/marginal impact to RAN1
Other items can be included as long as there is no/minimal impact to RAN2.