## Slide 1: Motivation of UE and Network Power Saving in Rel-17
China Academy of Telecommunications Technology (CATT)
3GPP TSG RAN Meeting #84 RP-191140
Newport Beach, USA, June 3-6, 2019

## Slide 2: Vision of 5G
5G is expected to change every aspects of modern society
  Smart city, education, health, industry, transportation, environment, entertainment, finance, agricultures…
Agriculture
Health
Education
Transportation
Finance
Environment
Wearable devices
Home
AR
VR
Entertainment
Cloud
Mobile device
Industry

## Slide 3: NR Evolution to Rel-17 and Beyond
User-oriented system evolution –
  Better user experience is one important aspects in marketing NR and further development
  NR power consumption is more than double of that in LTE (RP-181155 by MediaTeck)
    NR PDCCH monitoring in CONNECTED mode is more than double of that in LTE
    Initial access power is more than double of that in LTE
  Power consumption is high in EN-DC due to individual configuration of DRX for LTE and NR
Green project – reduce power consumptions
  Power consumption reduction at gNB
    Additional benefit in OPEX reduction
Rel-16 power Saving Works provide the framework for UE power saving for eMBB
  Continue power consumption reduction at UE and gNB

## Slide 4: Power Saving Study and Work in Rel-16
RAN1 study on UE power saving in NR had been completed in Rel-16
RAN1 work on UE power saving gains had been shown in multiple dimensions
  UE adaptation to the DRX operations in RRC_CONNECTED mode
    Power saving signal/channel in triggering UE adaptation
    Dynamic DRX configuration
  Reduce PDCCH monitoring
    PDCCH skipping
    Switching PDCCH monitoring periodicity
    Blind decoding reduction
  UE adaptation to the BWP/SCell operation
  UE adaptation to the maximum number of MIMO layers/ number of antenna
  UE assistance information
  RRM measurements reduction
    Relaxing in time domain
    Relaxing in intra and inter-frequency measurements
    Measurements with Additional RS
UE assistance for fast transition from RRC_CONNECTED to RRC_IDLE/RRC_Inactive

## Slide 5: Power Saving Study and Work in Rel-16
RAN1 study on UE power saving in NR had been completed in Rel-16
RAN1 work on UE power saving starting in 2nd quarter 2019
  Specify the power saving techniques with power saving signal/channel
  Specify the procedure of cross-slot scheduling power saving techniques
  Evaluate the required switching and interruption times for UE dynamic adaptation to the maximum number of MIMO layers [RAN4]
  Specify the power saving techniques with power saving signal/channel as the wakeup signal/channel in triggering UE adaptation to the DRX operation in RRC_CONNECTED mode
  Specify DCI-based mechanism in skipping PDCCH monitoring or switching PDCCH monitoring periodicity
  Specify the power saving techniques of UE adaptation to the BWP/SCell operation
  Specify the power saving techniques of UE dynamic adaptation to the maximum number of MIMO layers
  Specify the UE assistance information for the associated power saving techniques.
  Specify the power saving techniques in RRM measurements in synchronous and asynchronous network deployment
RAN2 continues study until June 2019
  DRX operation, PDCCH skipping/switching PDCCH monitoring periodicity, UE adaptation to the BWP/SCell operation, adaption to the MIMO layer, UE assistance information, RRM
  Study the enhancement of UE paging procedure based on the additional power saving signal/channel/procedure
  Study the enhancement of UE power saving procedure in supporting efficient transition from RRC_CONNECTED to RRC_IDLE/RRC_INACTIVE mode
To be revised in RAN#84

## Slide 6: Revolution to “Green”
Power consumption reduction for both UE and gNB through antenna adaptation
    The number of Tx/Rx antenna for UE and gNB would be dynamic adapted based on the traffic
      Both of UE and gNB would reduce the number of Tx/Rx antenna during monitoring and no traffic
        Low system load
        Time of day
      Fast antenna adaptation for high load and heavy traffic
Multi-RAT UE power saving
  Power Saving signal/channel to indicate the wakeup of selected RAT
    Preparation period – for channel tracking and triggering RS transmission
    Measurements
gNB: 4Tx/Rx for high data rate
UE: 4Tx/Rx for high data rate
gN: 2Tx/Rx for no traffic
UE: 2Tx/Rx for
PDCCH monitoring
LTE: DRX ON
NR: DRX ON
Low power
Power Saving signal triggering
Preparation
period
Preparation
period

## Slide 7: Rel-17 UE and Network Power Saving WI
Tx/Rx antenna adaptation for UE and Network
  UE dynamic adaptation to the MIMO layer
  UE adaptation to the number of Rx/Tx antenna
  Network adaptation to the number of Tx/Rx antenna based on system load and the day of use
    UE procedures in support of gNB antenna adaptation
    UE procedure in support of network cells ON/OFF in both CONNECTED and IDLE/INACTIVE states
Power saving signal/channel triggering UE adaptation to the power saving techniques in multi-RAT network [RAN1]
  Power saving signal/channel for triggering UE adaptation in both CONNECTED and IDLE/Inactive
    Study the low power consumption power saving signal
    Study and specify the interaction to Rel-16 PDCCH-based power saving signal/channel
    Specify the power saving signal triggering UE adaptation to DRX operation in multi-RAT operation, such as EN-DC, NE-DC, NR-DC, NR-CA
  Study and specify the power saving signal triggering preparation period in multi-RAT operation
    Configuration additional RS in assisting UE measurements, such as RRM and CSI measurements
    Enhancements of CSI feedbacks
Multi-RAT UE PDCCH monitoring reduction
  Power saving signal triggering PDCCH monitoring reduction
  PDCCH blind decoding reduction techniques