## Slide 1: Motivation of NR Network Synchronization in Rel-17
RP-191145
3GPP TSG RAN WG Meeting #84
Newport Beach, California, USA
June 3 – 6, 2019
Agenda Item: 8
China Academy of Telecommunications Technology (CATT)

## Slide 2: Network Synchronization
It is essential to support cost-effective techniques for precise frequency, time and phase synchronization for wireless networks
Frequency synchronization
  Baseband signals are mixed with the carrier frequency for transmission and the reception. Carrier frequency accuracy and stability have direct impact on the performance of the wireless communication
Time synchronization
  Accurate timing is critical for supporting the various operations, such as frequency tuning, antenna switching, start/stop of data sampling, carrier aggregation, and NR positioning
Phase synchronization
  Phase synchronization is between frequency synchronized signals. Phase synchronization is crucial for beamforming, MIMO, and carrier frequency based precise NR positioning

## Slide 3: NR Synchronization Requirements
Network synchronization requirements for NR wireless communication
  Frequency synchronization accuracy [TS 38.104]
    ±0.05 ppm for wide area BS
    ±0.1 ppm for medium range and local area BS
  Cell phase synchronization accuracy [TS 38.133]
    the maximum absolute deviation in frame start timing between any pair of cells on the same frequency that have overlapping coverage areas within 3 µs for TDD cells
  Time alignment error [TS 38.104]
    For MIMO or TX diversity transmissions, at each carrier frequency, TAE shall not exceed 65 ns.
    For intra-band contiguous carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 260ns.
    For intra-band non-contiguous carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 3µs.
    For inter-band carrier aggregation, with or without MIMO or TX diversity, TAE shall not exceed 3µs.
Network synchronization requirements for NR positioning
  3GPP has not defined the network synchronization requirements for positioning yet.
  It is well-understood that network synchronization requirements for NR positioning will be much tighter than that for NR wireless communication

## Slide 4: Existing Network Synchronization Techniques
Techniques popularly used for the time and frequency synchronization of wireless networks include GNSS-based and IEEE 1588 PTP based methods
  GNSS based
    Based on GNSS signals
    Capable of supporting from µs-level to ns-level synchronization
    Major drawbacks :
      Not suitable for environments where GNSS signals are weak or blocked, such as indoor scenarios
      Significantly high installation and operational costs especially in city area
  IEEE 1588 PTP (Precision Time Protocol)
    Based master/slave synchronization paradigm
    PTP estimates the time difference between the master and slave devices from the round-trip delay
    Major drawbacks:
      Synchronization accuracy is impacted by network asymmetry (delay difference between the send path and receive path) and Packet Delay Variation (PDV)
      A chain of network elements between the master and the slave with variable network load and varying queuing and processing delays can cause delay variations in the PTP messages
      Changes in packet arrival time are problematic, since the slave cannot identify the difference between variation in packet delay and a timing drift in the master

## Slide 5: Network Synchronization based on NR Signals
Precise network synchronization based on NR reference signals were proposed recently for supporting NR positioning[Ref. 1 – 4]
  Example 1: One cell transmits the NR reference signals (e.g., PRS) periodically for time synchronization. A neighboring cell estimates the time offsets between the cells
    The time synchronization accuracy between the cells depends mainly on the configuration of the NR RS (periodicity, bandwidth, etc.), the clock drifts of the cells, and channel conditions.
  Example 2: On top of transmitting PRS, Cell 1 also transmits continuously the carrier reference signals (C-PRS). Cell 2 monitors PRS and C-PRS for precise synchronization
    When Cell 2 phase lock loop (PLL) is locked to the C-PRS from Cell 1 , two cells are frequency and phase fully synchronized, i.e., the time and phase changes between cells, caused by clock drifts and frequency offset and other factors, can be captured by the PLL.
The technique can be used to whole network synchronization where multiple cells monitor the PRS and C-PRS from multiple other cells, supporting the network synchronization for both wireless data communication and positioning.

## Slide 6: Rel-17 WI: NR Network Synchronization
WI Objectives
  Explore the methods of supporting precise frequency, time, and phase synchronization for NR data communication and NR positioning based on NR radio network reference signals [RAN1]
  Identify the environments where the network synchronization based on NR signals may work properly, and/or more cost-effectively than GNSS-based and IEEE 1588 PTP based techniques [RAN1]
  Investigate and develop the NR reference signals and the methods for precise frequency, time, and phase synchronization for the Identified environments [RAN1]
  Investigate and develop high-layer architecture, protocols, messages, and configuration for supporting the synchronization approaches based on NR signals [RAN3, RAN2]
  Investigate potential and benefits of the integration of NR-based and existing synchronization approaches for supporting precise frequency, time, and phase synchronization for whole NR networks [RAN3, RAN1, RAN2]
  Define the core and performance requirements, and test cases for precise frequency, time, and phase synchronization for NR networks based on NR radio network reference signals [RAN4]

## Slide 7: References
3GPP TS 38.104, “NR; Base Station (BS) radio transmission and reception”
3GPP TS 38.133, “NR; Requirements for support of radio resource management”
R1-1902344, “Discussion on measurement reporting for network synchronization error compensation scheme”, CMCC
R1-1901849, “DL and UL based NR Positioning”, Nokia, Nokia Shanghai Bell
R1-1903141, “On the use of RTT for positioning”, Ericsson
R1-1905350, “Network synchronization based on RAT-dependent signals”, CATT
3GPP TR 36.898, “Network Assistance for Network Synchronization”