## Slide 1: LTE-LAA based Access in 6GHz Spectrum
3GPP TSG-RAN #84
Newport Beach, CA, USA, June 3-6, 2019
Agenda: 10.1.5
Ericsson
RP-191232

## Slide 2: Background
Licensed assisted access for LTE has been specified for DL in Rel-13 under LAA WI, for UL in Rel-14 eLAA WI, and has been further enhanced in Rel-15 in the Further Enhanced LAA (feLAA) WI
  LAA, eLAA and feLAA channelization is similar to other unlicensed systems e.g. Wi-Fi systems in 5GHz spectrum.
  Band 46 is defined in RAN4 with the span of 5150-5925MHz spectrum for downlink and uplink LAA operation.
  An additional LAA/eLAA band was defined in the 3.5GHz CBRS band in the US as Band 49 (3550-3700MHz).
Recent developments in the regulatory domain may make more unlicensed spectrum available.
  E.g. 6GHz spectrum is being opened for MBB usage for different parts of the world
  The range of the spectrum available in 6GHz is open to discussions in regulatory fora in different parts of the world
Unlicensed 6GHz spectrum should be considered as greenfield spectrum since no radio LAN networks are currently deployed in this spectrum.
  In the 6 GHz band, technology neutral channel access amongst RATs including at least LTE-LAA, NR-U, and Wi-Fi must be ensured.
  It is assumed that regulation will provide the framework concerning protection for technologies not using unlicensed access in the band, e.g., existing fixed services.
As a baseline, all downlink and uplink LAA (LAA, eLAA and feLAA) procedures and requirements can be extended to 6GHz for LTE-LAA usage
  The existing channel access mechanism for LAA can enable technology neutral channel access amongst RATs including at least LTE-LAA, NR-U, and Wi-Fi.

## Slide 3: Proposed WI
Objective
  Extend downlink and uplink LAA features as part of the WI to 6GHz spectrum
    Specify new unlicensed band using frame structure # 3 in the band
    Define the channelization in the 6 GHz band
    Specify UE, BS and RRM for downlink and uplink LAA in the above frequency band
      E.g. adjacent channel interference requirements related to TX and RX, LBT threshold requirements, etc.
    Specify limited set of example band combinations involving new LAA band in 6GHz
  Note that:
    Within 6GHz band, 5925 MHz -6425MHz is common spectrum in 6GHz frequency range in both Europe and US, and is expected to be available for unlicensed usage.
      RAN4 should at least define this range for LAA operation in the 6 GHz band.
      The actual frequency range for specification can be further discussed based on regulatory updates in the US and Europe.
    The WI can be completed provided requirements for at least one band combination involving new LAA band in 6GHz are specified.
Timeline:
  Core part completion: RAN4#85 (September 2019)
    RAN4#90bis, 91 and 92, Q2-Q3 2019 for core part (0.5 TU in each meeting)
  Performance part completion: RAN4#87 (March 2020)
    RAN4#92bis, 93 and 94, Q4 2019-Q1 2020 for performance part (0.25 TU in each meeting)