## Slide 1
Discussion on NR MIMO progress and down scoping
3GPP TSG RAN Meeting #84 RP-191309
Newport Beach, USA, June 3-6, 2019
Notes: 1st,

## Slide 2: Rel-16 NR_eMIMO progress
Over all progress on NR_eMIMO
  MU CSI
    The progress on MU CSI enhancement is on track, few remaining details to be agreed.
  Multi TRP
    The overall progress is lagging behind with several open issues, no time for discussion on single and multi PDCCH based multi TRP enhancement for FR2, RS signal(s), CSI reporting enhancement.
  Multi beam
    The overall progress is lagging behind with many open issues, especially proposals on MPUE enhancement are still diverging after several meetings.
  UL full power Tx
    Overall progress is lagging behind, major part of the work is complete, few remaining details such as power scaling, UE capability signaling are to be agreed.
  Low PAPR RS
    RAN1 work is complete.

## Slide 3: Rel-16 NR_eMIMO down scoping
Proposal for down scoping
  Multi TRP
    Motivation: focus discussion and complete the design for URLLC for PDSCH, multi DCI based eMBB, there are still lots of remaining work to be completed
    Potential items for down scoping
      Single and multi DCI based mTRP for FR2 including URLLC and eMBB
      UL control - CSI reporting enhancement
      RS signal(s) enhancement
  Multi beam
    Potential item for down scoping: UE multi-panel
      Companies still have diverging views on remaining alternatives
      A single framework to support MPUE2 and MPUE3 would be preferable from future extension perspective. Current discussion is focused on solution for MPUE3, however enhancement in future release to accommodate all types of MPUEs would be beneficial.

## Slide 4: Rel-16 NR_eMIMO WID objectives revisions
The work item aims to specify the enhancements identified for NR MIMO. The detailed objectives are as follows.
Extend specification support in the following areas [RAN1]
  Enhancements on MU-MIMO support:
    Specify overhead reduction, based on Type II CSI feedback, taking into account the tradeoff between performance and overhead
    Perform study and, if needed, specify extension of Type II CSI feedback to rank >2
  Enhancements on multi-TRP/panel transmission including improved reliability and robustness with both ideal and non-ideal backhaul, primarily targeting FR1 operation:
    Specify downlink control signalling enhancement(s) for efficient support of non-coherent joint transmission
    Perform study and, if needed, specify enhancements on uplink control signalling and/or reference signal(s) for non-coherent joint transmission
    Multi-TRP techniques for URLLC requirements are included in this WI
  Enhancements on multi-beam operation, primarily targeting FR2 operation:
    Perform study and, if needed, specify enhancement(s) on UL and/or DL transmit beam selection specified in Rel-15 to reduce latency and overhead
    Specify UL transmit beam selection for multi-panel operation that facilitates panel-specific beam selection
    Specify a beam failure recovery for SCell based on the beam failure recovery specified in Rel-15
    Specify measurement and reporting of either L1-RSRQ or L1-SINR
  Perform study and make conclusion in the first RAN1 meeting after start of the WI, and if needed, specify CSI-RS and DMRS (both downlink and uplink) enhancement for PAPR reduction for one or multiple layers (no change on RE mapping specified in Rel-15)
  Specify enhancement to allow full power transmission in case of uplink transmission with multiple power amplifiers (assume no change on UE power class)
Specify higher layer support of enhancements listed above [RAN2]
Specify core requirements associated with the items specified by RAN1 [RAN4]

## Slide 5
Thanks