## Slide 1: RP-191583 Title: On SFN-sync Agenda Item: 9.2.1 Source: Samsung, Huawei, ZTE

## Slide 2: What is meant by Synchronous operation
At RAN#81, it was agreed that only synchronous NR-NR DC is supported in the Rel-15.
In LTE, synchronous dual connectivity does not require SFN-sync
In EN-DC, synchronous dual connectivity does not require SFN-sync
In NE-DC, synchronous dual connectivity does not require SFN-sync
Observation 1: Synchronous operation for NR-NR DC is understood same as for any other DC option (i.e. only subframe/slot sync).

## Slide 3: Impacts of mandating SFN-sync between nodes
SFN-sync is new requirement for NW. It is not clear how it would impact NW implementation.
For example, for NW to locate SSB as it wish, NW shall be able to decide SFN by itself. If SFN-sync between nodes is mandated, it would be no more possible.
Above may not be the only impact. There should be thorough study in the relevant WGs to figure out the possible impacts
Observation 2: Mandating SFN-sync between nodes would impact NW implementation in negative way. WG-level study is required to identify the impacts.

## Slide 4: The motivation of SFN-sync
RP-190992 argues that blind PSCell addition operation in RAN1 is impacted if SFN is not synchronized as below
We could not identify where in the NR specifications the above operation is specified. Also, “SFN-sync” behavior is achievable by configuring 1 ms SMTC and proper ssbToMeasure if the NW is slot-sync.
Observation 3: There is no need to mandate SFN-sync. Regardless of SFN-sync, a desirable UE behavior is achievable by NW configuration

## Slide 5: Conclusion
Synchronous DC has never been SFN-sync in any of LTE DC, EN-DC, and NE-DC.
When agreeing to limiting NR-DC only to synchronous operation, it should be understood that it is the same synchronous operation as any other synchronous operation – i.e. slot/subframe boundary sync.
Mandating SFN-sync is new requirement and may have negative impact to network implementation.
The alleged motivation is not clear. There is no apparent reason for an impact to UE hardware depending on whether or not there is SFN-sync
Proposal: Do not introduce a new requirement for SFN-sync for synchronous NR-NR DC