## Slide 1: Motivation for R18 enhancement of NR SL Relay
OPPO

## Slide 2: Part-1: UE-based Relay in LTE

## Slide 3: Background: R13 eD2D L3 Relay
SID/WID: SP-140386 (SA1), SP-140385 (SA2), RP-142311 (RAN)
Time: 2015~2016
Objective: Support the extension of network coverage using L3-based UE-to-Network Relays, including service continuity (if needed), based on Release 12 D2D communication, considering applicability to voice, video. [RAN2, RAN1, RAN3].

## Slide 4: Background: R15 FeD2D L2 Relay
SID/WID : SP-160511 (SA1), SP-160961 (SA2), RP-170295 (RAN)
Time: 2016~2017
Objective: Study the possibility of a common solution supporting the following use cases:[RAN2]
  i. UE to network relaying over non-3GPP access (Bluetooth/WiFi).
  ii. UE to network relaying over LTE sidelink.
  iii. Unidirectional and bidirectional UE to network relay.
3GPP based UE-to-UE link

## Slide 5: Background
In LTE, although the UE-based relay has been specified (only in R13), it is quite limited in the sense that
  Single UE-to-UE protocol (i.e., LTE sidelink)
  Without scalability (single hop, single path)
  Supporting limited type of traffic (Public Safety oriented)

## Slide 6: Part-2.1: UE-based Relay in R17 NR

## Slide 7: R17 SL-Relay: L2/L3 Relay
SID/WID : SP-190303 (SA1), SP-190443 (SA2), RP-201474 (RAN)
Time: 2019~2021 (SI to be converted to WI @ RP#91-e)
Objective: Study mechanism(s) with minimum specification impact to support the SA requirements for sidelink-based UE-to-network and UE-to-UE relay, focusing on the following aspects (if applicable) for layer-3 relay and layer-2 relay [RAN2]..
L2 UE-to-NW Relay
L3 UE-to-NW Relay (non-N3IWF scheme)

## Slide 8: R17 SL-Relay: L2/L3 Relay
State of the Art
  SI of RAN2/SA2 has been finished
  SI-to-WI conversion to happen @ 2021-Q1
  Quite strong support for both L2/L3 UE-to-NW relay
  Limited to single-hop, single-path, 3GPP UE-to-UE interface, unicast in R17

## Slide 9: Part-2.2: UE-based Relay in R18 NR

## Slide 10: R18 SL-Relay
Single-hop Relay => Multi-hop Relay
Single-path (for relay/remote) => Multi-path (for relay/remote)
Unicast-only relaying => MBS-capable relaying
3GPP UE-to-UE interface => non-3GPP UE-to-UE interface
[Other R17 left-overs..]

## Slide 11: R18 SL Relay: Multi-Hop
Scenario | Max. data rate (DL) | Max. data rate (UL) | End-to-end latency (note 7) | Area traffic capacity (DL) | Area traffic capacity (UL) | Area user density | Area | Range of a single hop (note 8) | Estimated number of hops
InHome Scenario (note 1) | 1 Gbit/s | 500 Mbit/s | 10 ms | 5 Gbit/s/ home | 2 Gbit/s /home | 50 devices /house | 10 m x 10m – 3 floors | 10 m indoor | 2 to 3
Factory Sensors (note 2) | 100 kbit/s | 5 Mbit/s | 50 ms to 1 s | 1 Gbit/s /factory | 50 Gbit/s /factory | 10000 devices /factory | 100 m x 100 m | 30 m indoor / metallic | 2 to 3
Smart Metering (note 3) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /hectare | 200 x 100 bytes / 15 mins /hectare | 200 devices /hectare | 100 m x 100 m | > 100 m indoor / deep indoor | 2 to 5
Containers (note 4) | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 15000 x 100 bytes / 15 mins /ship | 15000 x 100 bytes / 15 mins /ship | 15000 containers /ship | 400 m x 60 m x 40 m | > 100 m indoor / outdoor / metallic | 3 to 9
Freight Wagons | 100 bytes / 15 mins | 100 bytes / 15 mins | 10 s | 200 x 100 bytes / 15 mins /train | 200 x 100 bytes / 15 mins /train | 120 wagons /train | 1 km | > 100 m outdoor / tunnel | 10 to 15
Public Safety (note 5) | 12 Mbit/s | 12 Mbit/s | 30 ms | 20 Mbit/s /building | 40 Mbit/s /building | 30 devices /building | 100 m x 100 m – 3 floors | > 50 m indoor (floor or stairwell) | 2 to 4
Wearables (note 6) | 10 Mbit/s | 10 Mbit/s | 10 ms | 20 Mbit/s per 100 m2 | 20 Mbit/s per 100 m2 | 10 wearables per 100 m2 | 10 m x 10 m | 10 m indoor / outdoor | 1 to 2
In 22.261, KPI for multi-hop UE-to-Network Relay has been provided

## Slide 12: R18 SL Relay: Multi-Path
Multi-path relaying can apply to UP and/or CP
The benefit can be scheme/scenario-dependent, and of major interest in general during R17 SI phase
  Robustness
  throughput
 | Path-1 | Path-2
Scenario-1 | Direct UE-gNB link | Indirect UE-Relay_UE-gNB link
Scenario-2 | Indirect UE-Relay_UE1-gNB link | Indirect UE-Relay_UE2-gNB link
Scenario-3.. | More advanced scenario if considering multi-hop.. | 

## Slide 13: R18 SL Relay: MBS-oriented
MBS-oriented Relaying helps at least Public Safety and V2X use case
Although in LTE UE-based Relay from Day-1, but not in R17 NR UE-based Relay due to the parallel MBS work in R17
It should be included in R18 as Phase-II for NR UE-based Relay
NOTE 2: Support of non-unicast mode communication (i.e. one-to-many communication/broadcast or multicast) between network and UE-to-Network Relay UE and between UE-to-Network Relay and Remote UE(s) depends on the result of FS_5MBS work.

## Slide 14: R18 SL Relay: Non-3GPP based
In LTE, the non-3GPP based PC5 has been studied / specified
  R13: EPC assisted WLAN direct discovery / communication
  R15: L2 UE-to-Network Relay over non-3GPP RAT
To continue the work in NR, it helps to bring the diverse UE-to-UE interface in the field (Wifi, BT..) into 3GPP network/system framework
Non-3GPP based UE-to-UE link (from R15 FeD2D)

## Slide 15: R18 SL Relay: [Other R17 left-overs]
R17 as a start point focusing on the baseline function, but limited in different dimensions*
* Pending on R17 SI-to-WI conversion discussion result
R17 | R18
gNB only, i.e., NR-Uu only | Cross-RAT control for eNB, i.e., LTE-Uu
NR SA, i.e., no support on DC | DC-compatible, i.e., (NG)EN/NE/NR-DC
Service continuity between direct and indirect | Service continuity between indirect1 and indirect2
No support for group-mobility | Support for group-mobility
… | …

## Slide 16: Summary
R18 Enhancement aims at a UE-based relay architecture which is
  Compatible with various UE-to-UE protocol (3GPP sidelink, IEEE Wifi/BT, and etc...)
  With enough scalability (single/multi-hop, single/multi-path)
  Support various traffic types (eMBB/URLLC/MTC, unicast/groupcast)