## Slide 1
3GPPTSG RAN Meeting #91e RP-210312
Electronic Meeting, March 16 - 26, 2021
Agenda Item: 9.6.7
Document for: Discussion & Decision
WID scope for Rel-17 RAN slicing

## Slide 2
A Rel-17 Study Item of “enhancement of RAN Slicing for NR”has been carried out by RAN2 and RAN3, the study item covered:
  Slice based cell (re)selection
  Slice based RACH configuration
  Mechanisms to Support Service Continuity
RAN2 conclusion:
  From RAN2 viewpoint, the RAN slicing SI can be concluded
  RAN2 has concluded that both slice based cell reselection and RACH configuration are recommended for normative work.
RAN3 status
  Common understanding at this time, that extending the RAN3 part of this SI would not impact the start of potential normative work in RAN2
  RAN3 proposes to extend the SI with one quarter in RAN3 and do down-selection during the extended SI. .5 TUs needed; whether to overload RAN3 or to take this .5 TU from another topic is up to RAN discussion (RAN3 Chairman input)
Proposal: RAN slicing normative work should begin in RAN2 and the WID scope to be updated when RAN3 finish it study item part.
Motivation

## Slide 3
    The objective of RAN2 work item should consider to specify mechanism(s) for RAN slicing to include:
    Support for slice based cell (re)selection, specify mechanisms and signalling including
      Broadcast supported slice info of the current cell and neighbour cells and cell reselection priority per slice for cell reselection assistance.
      Include slice info (with similar information as slice info in SI message) in RRCRelease message slice for cell reselection assistance
      Broadcast supported slice of serving cell in SI message for cell selection assistance
    Support slice based RACH configuration, specify mechanisms and signalling including
      Configuration of separated PRACH configuration (e.g., transmission occasions of time-frequency domain and preambles) for slice or slice group
      Configuration of RACH parameters prioritization (e.g., scalingFactorBI and powerRampingStepHighPriority) for slice or slice group
  Scope of the new RAN2 WID