## Slide 1
3GPP TSG RAN Meeting #91e RP-210324
Electronic Meeting, Mar. 22-26, 2021
Source: vivo
Document for: Discussion & Decision
Agenda Item: 9.13
Mobility enhancement in Rel-18

## Slide 2
Background
Deployment Scenarios
  In NR, FR2 which could enable high data rate and large capacity with wider bandwidth, will be an key deployment scenario, especially for 5G advance.
  5G deployment is expected to be much denser in the future (i.e. cell/TRP to UE ratio is higher)
    For coverage purpose in high frequency, e.g. FR2
    For capacity purpose
Intra-cell mobility  Inter-cell mobility
Inter-cell mobility
A
B
C
  Deployment scenarios:
    One layer: single layer with dense deployment
    Two frequency layers:
      FR1: One for coverage and mobility, sparse deploy
      FR2: Another with MTRP for high data rate, dense deploy
  Mobility performance and/or UE power consumption could be challenging for FR2 deployment or UDN (Ultra Dense Network)
    UEs perform more frequent measurement
    UEs perform more cell (re-) selection/Handover between cells

## Slide 3
Issue identification
Power consumption and Mobility
A
B
Degraded UE mobility performance
In UDN/FR2 deployment, compared to FR1 deployment
  UEs perform more frequent cell (re-)selection and handover
  Higher paging missing rate or higher handover failure rate will be led due to the hysteresis of L3 filter for RRM
For example, in above scenario, UE already moved to cell B from cell A, but due to the L3 filtering of current mobility procedure
  In idle/inactive mode, UE still receive paging from cell A  cell reselection delay, paging miss
  In connected mode, too late handover may happen  Handover failure
The above issues are similar to what is currently observed in high speed train deployment
Observation: Degraded mobility performance and high UE power consumption could be challenge for FR2 deployment or UDN.
High UE power consumption
In UDN/FR2 deployment, compared to FR1 deployment
  UEs perform more frequent cell search/ measurement for cell (re)-selection in idle/inactive mode
  UEs perform more frequent measurement and report for handover/TRP switch in connected mode
For example, in above deployment, while the UE is moving:
  There is no need to perform neighboring cell measurement in FR1 deployment;
  While UE should perform cell search/measurement in UDN/FR2 deployment

## Slide 4
Potential Solutions
SFN and/or UL mobility
In order to resolve the above issues, we could consider the following potential solutions in Rel-18 study:
SFN based cell camping for UE in idle/inactive mode
  Network could provide SFN specific RS. Then, idle/inactive UE measurement will be performed on SFN specific signals.
    UE power saving could be obtained due to less cell search and measurement.
    Some additional network signaling overhead would be introduced.
  On top of SFN based camping, SFN-based paging monitoring (and potentially SFN-based SI) may be considered.
    The paging miss issue could be mitigated.
UL signal based mobility
  UEs sends UL signals periodically. Network performs measurement and determine the cell changes based on UL measurement.
    There is no need for network to transmit DL RS in UDN.
    There is no need for the UE to perform DL measurement. No power consumption increasing may be achieved.
  UL signal based mobility could have benefit on
    Mitigating the handover failure rate in connected mode
    Reduce the paging missing rate in idle/inactive mode
  In addition, UL signals from UE could help network to identify the UE location. In this way, network could page UEs only in a small area (e.g. in cell range), which will reduce network paging load and network energy consumption
It is assumed that FR2 with UDN scenario will be deployed in 5G advance around in 2025. Thus, potential issues identified for UDN/FR2 deployment should be addressed in Rel-18.
Proposal: Potential solutions for degraded mobility performance and high UE power consumption should be studied for FR2 deployment or UDN.