## Slide 1: Proposed RAN2 Work Scope for RAN SLICING WI

## Slide 2: Current Status
RAN2 discussed the following enhancements during study item phase
  Slice-Aware Cell Reselection
  Slice-Aware Cell Selection
  Slice-Aware Access Control
  Slice-Aware RACH
RAN3 study is extended by one quarter to conclude the study
  Slice Re-mapping

## Slide 3: Time Budget for RAN slicing WI
Required RAN2 TU (from RAN2 status report)
  Only 0.5 TU per meeting is allocated.
  RAN2 work scope should be narrow enough to be completed within the 0.5 TU. Down-selection of normative works is essential.

## Slide 4: Slice-Aware Cell Reselection
RAN2 discussion
  gNB can broadcast slice information.
  gNB can provide slice information in RRC release message.
Considerations
  Slice-Aware Cell Reselection is essential to enable fast access of intended slices. Hence, this work should be the primary objective.
Proposal
  Specify RRC signaling of slice information via broadcast and dedicated signaling, and update the cell reselection rule using the slice information.

## Slide 5: Slice-Aware Cell Selection
RAN2 discussion
  No explicit conclusion was made in RAN2 on the support for slice-aware cell selection during WI phase.
  SIB1 size limitation is a critical issue for slice-aware cell selection.
Considerations
  Slice-aware cell reselection is sufficient for fast access to the intended slice. Slice-aware cell selection is not essential.
  Furthermore, slice-aware cell selection may delay cell search process time and hence worse cell selection performance.
Proposal
  Enhancements for slice-aware cell selection are not considered.

## Slide 6: Slice-Aware Access Control
RAN2 discussion
  RAN2 did not study any enhancements in details for slice-aware access control.
Considerations
  There is no clear justification that existing access control mechanism is insufficient.
Proposal
  Enhancements for slice-aware access control are not considered.

## Slide 7: Slice-Aware RACH
RAN2 discussion
  Separate RACH configuration can be configured per slice/slice group.
  Existing RACH prioritization parameters can be configured per slice/slice group.
Considerations
  Separation of RACH resources is not always beneficial because RACH resources are limited.
  RACH prioritization always requires lots of meeting time to conclude.
Proposal
  Enhancements for slice-aware of RACH are not considered.

## Slide 8: Summary of Proposed RAN2 Scope
Specify RRC signaling of slice information via broadcast and dedicated signaling, and update the cell reselection rule using the slice information.
  Enhancements for slice-aware cell selection are not considered.
  Enhancements for slice-aware access control are not considered.
  Enhancements for slice-aware of RACH are not considered.