## Slide 1: Handling of OTA Projects
Qualcomm Incorporated
3GPP TSG RAN Meeting #91e
Electronic Meeting, Mar. 16 - 26, 2021
RP-210506

## Slide 2: Background
Handling of 60GHz OTA testing was discussed in RAN#90-e under thread 43- 60GHz OTA
A WF with multiple options for handling this discussion was capture in the conclusion and is reproduced below:
  Proposal #1: Agree to study and define NR 52.6-71GHz UE OTA test methods in Rel-17
    Further discus how to handle NR 52.6-71GHz UE OTA test methods objectives in RAN #91e:
      Option 1: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR FR2 Test Methods Enhancements SI (FS_FR2_enhTestMethods)
      Option 2: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of a new “umbrella” SI on OTA topics (if such new item is approved)
      Option 3: Include NR 52.6-71GHz UE OTA test methods objectives in the scope of Rel-17 NR 52.6-71GHz WI
      Option 4: RAN4 define the core requirements for 52.6-71GHz and leave the test related issues to RAN5 WI, co-ordination between RAN4 and RAN5 can be triggered by LS if needed
      Other options are not precluded
    Further discuss the timelines of the work
      Option A: Wait until the NR 52.6-71 GHz RF Core requirements framework is stable
      Option B: Start work in parallel with NR 52.6-71 GHz RF Core requirements definition
      Other options are not precluded
    Objectives
      At least identify the applicability of the existing FR2 OTA test methods in to 52.6-71GHz frequency range
  Further discuss and refine detailed objectives of the studies before RAN #91e.

## Slide 3: OTA Testing Issues (1)
OTA testing is the only available testing method for FR2
  RAN4 has to develop testing methods in order for products to be tested for compliance
  Delivery of testing solutions to the industry is critical to ensure success of 3GPP technologies
Different features introduce different testing requirements
  It is important to have a comprehensive view of needs that have to be addressed to develop methods that are versatile
  Unified testing solutions are important to reduce cost and test times
It is expected that new features will be introduced in future release, very likely in each release
  Forward compatibility should be maintained to the extent possible
    It is not feasible to change OTA test equipment often

## Slide 4: OTA Testing Issues (2)
OTA is becoming increasingly important for FR1 also
  Only with OTA requirements can real performance be guaranteed
  FR1 OTA test methodology and requirements are needed to test FR1+FR2 operation(see below)
FR1+FR2 tests are also needed
  For device supporting simultaneous FR1+FR2 operation(EN-DC with FR2, NR CA of FR1+FR2,etc) it is not possible to test performance of both FR1+FR2
    Prerequisite for such tests is the definition of FR1 OTA requirements
  A comprehensive solution would be needed to ensure conformance during simultaneous FR1+FR2 operation

## Slide 5: Handling of OTA Projects
In order to address the issues in the previous slides, an umbrella study item addressing all the OTA testing issues is the best approach (Option 2)
  Best way to ensure that a comprehensive solution to address testing needs for all features from different WIs will be defined
  Work will be handled by the OTA experts under a single agenda item, not spread around different SIs/WIs

## Slide 6: Proposal
Introduce a Rel.17 OTA Testing SI
The SI should address at least the following issues:
  60GHz OTA testing (covered by the 52-71GHz WI)
  Multi panel UE Rx/Tx (covered by the FeMIMO WI)
  FR2 HST testing
  Leftovers from the current FR2 test enhancements SI, if any
Other topics should be further discussed
  RRM testing enhancements (tests not covered in Rel.15 and 16)
  FR1+FR2 testing (actual tests will depend on FR1 OTA requirements, however, test method study can start)