## Slide 1: Motivation of study for UE Aggregation
CMCC
3GPP TSG RAN Meeting #91e RP-210512
Electronic Meeting, March 16 - 26, 2021
Agenda item: 9.13

## Slide 2: Motivation
AR/VR
Video for Remote Monitoring
Drone with live video
The motivation of this SI is to investigate how to address the issue of the shortage of UL UE transmission power in 5G via UE aggregation mechanism:
  In compare to LTE, various type services required the wide UL bandwidth requirement is increasing and becomes pervasive in 5G network
    e.g. AR/VR devices, live video from UAV, etc.
  In this case, the bottleneck of supporting the applications with wide UL bandwidth on 5G terminals is the limited UL UE transmission power, e.g. 23dBm or 26dBm.
  Although some enhancement to eliminate the bottleneck has been adopted, e.g. SUL, it seems not sufficient to satisfy the demand.
Therefore, the mechanism of UE aggregation which can be one way to ensure a high UL bandwidth target value is desired to be investigated
  This is in particular useful in the case of the terminal with less size limitation
        e.g. terminal equipped in the UAV, vehicle and assessment line for motion controller in the factory

## Slide 3: Motivations
Issue
  How to avoid the data disorder and data duplication during the data splitting between the aggregated UEs
Intention of the SI is to study the potential UE aggregation mechanism
  Which kind of L2 architecture can be utilized to aggregate more than one terminal to improve the UL throughput
  How to support the data lossless or minimized data loss during the session/packet switching amongst the aggregated terminals
Figure : L2 architecture of UE aggregation for UL TX power boosting

## Slide 4: SI OBJECTIVES
Identify and study potential UE aggregation mechanism, including [RAN2, RAN3]
  RRC management procedure to enable UE aggregation [RAN2]
  L2 architecture, functionalities and interfaces to allow aggregated UEs to receive control signalling/data in coordination mode, e.g. without data disorder or data duplication during the data splitting between the aggregated UEs [RAN2]
  Mobility of aggregated UEs with Service continuity [RAN3]

## Slide 5
Thank you!