## Slide 1: L3 Relay Performance and Impact
MediaTek Inc., Huawei, HiSilicon, Interdigital, Futurewei, Apple, Convida Wireless, Philips

## Slide 2: Constraints on relay operation
Relaying needs to work for both commercial and public safety users
  In general, commercial users will have higher expectations of the service
    Service continuity, QoS, security, good performance, and reliability
    These are also concerns for PS users, e.g. the relay is not always a trusted device
  The WI should target commercial requirements
The selected solution must meet commercial service requirements to be useful
  Risk of a paper standard otherwise
In the SI in RAN2 it is concluded that
  The standards impact of L2 relay is principally in RAN and the standards impact of L3 relay is principally in SA.

## Slide 3: L3 U2N relay performance
The L3 U2N design has two flavours in TR 23.752
  Solution #6 (“IP router”) – similar to LTE solution
  Solution #23 (“N3IWF”) – uses N3IWF to provide security and service continuity
  SA2 endorsed the IP router solution when the relay is trusted, and N3IWF when the relay is not trusted
The IP router solution cannot meet commercial service requirements
  IP address changes at PC5/Uu path switch – service continuity is impossible unless the application happens to be robust to the address change
  Security is hop-by-hop – the relay UE has access to the remote UE’s traffic in the clear
The N3IWF solution addresses these deficiencies
  Consistent IP address allows service continuity (but without lossless handover)
  End-to-end security via IPsec
It is unclear whether SA has concluded to select N3IWF-based solution

## Slide 4: N3IWF performance
N3IWF architecture adds multiple extra layers over the air
  IPsec, inner IP, GRE
  The inner IP and GRE headers cannot be compressed by RoHC (they’re encrypted)
  Especially for small packets, this can cause unreasonable overhead (see R2-2009124)
  This issue was flagged to SA2 in R2-2010883 but not further discussed
    Note: SA2 indicated in TR 23.752 that RAN WGs should look at the issue of overhead
Recommendation: the N3IWF U2N solution causes much more overhead/complexity, RAN needs to indicate to SA2 that overhead/complexity needs further analysis, RAN cannot decide whether L3 relay should have normative work at this stage.

## Slide 5: L3 U2U relay performance
SA2 developed only one L3 U2U architecture (solutions #10 and #32)
  The solutions differ in how the link-local IP addresses are assigned
  Service continuity is available when switching between relays, but not when switching from relayed to direct PC5 communication
  For non-IP traffic it is said that it can be handled either via IP encapsulation or non-IP encapsulation.
    In case of IP encapsulation this will lead to protocol overhead
    In case of non-IP encapsulation it is not clear how the traffic will be secured.
  In general end-to-end security is not worked out (yet) for L3 U2U relay
  QoS management is available (solution #31)
Recommendation: More coordination with SA to clarify whether and how service continuity, non-IP traffic and security will be addressed and RAN cannot decide normative work at this stage

## Slide 6: RAN impact of L3 relay solutions
RAN2 identified no impact of the SA2 L3 U2U solutions
  RAN could ignore this part of the normative work and assume that if any issues arise, they will be handled by LS
  However, we should be clear to SA that from RAN perspective the service continuity, non-IP traffic and security is important
SA2’s L3 U2N solutions do require some RAN work (a mix of architecture-agnostic and architecture-specific aspects)
  The similar LTE design had the following impacts in RAN2:
    Discovery and relay re/selection
    AS conditions for relay/remote operation
    Contents of RRC signalling (SUI, sidelink-related SIBs)
    Stage 2 description
  Additional impacts that could be foreseen in NR:
    Maintenance of the PC5-RRC connection between relay and remote
    Potential PC5-RRC impact for QoS enforcement (left for WI in RAN2; specific to the L3 architecture)
    New SL-SRB (and potentially separate resource pool) for discovery
    Interaction with a gNB not providing SL relay configuration
    Transport of remote UE’s NAS signalling (specific to the N3IWF architecture)
    Performance aspects of N3IWF based relaying
Recommendation: RAN should wait for SA before making decision whether to support U2N and/or U2U L3 relay in RAN WI

## Slide 7: Summary and recommendations
ONLY N3IWF solution can support commercial cases
  Only N3IWF supports end-to-end QoS and end-to-end security
  There is additional overhead cost and deployment cost to support N3IWF
The overhead and complexity of N3IWF U2N solution needs further analysis
RAN should wait for SA before making decision whether to support U2N and/or U2U L3 relay in RAN WI because
  SA needs to be clear on how the service continuity, non-IP traffic and security will be addressed for L3 U2U relay
  L3 U2N needs clear guidance from SA which solution （e.g. N3IWF or not） is selected
  L3 U2N does require RAN work, with potential impacts in RAN2:
    Discovery and relay re/selection
    AS conditions for relay/remote operation
    Contents of RRC signalling (SUI, sidelink-related SIBs)
    Maintenance of the PC5-RRC connection between relay and remote
    New SL-SRB (and potentially separate resource pool) for discovery
    Interaction with a gNB not providing SL relay configuration
    Stage 2 description